XES:  eXtended Environment System
                =================================



            Official Documentation for XES Programmers
                          October 20,1991

                                by

                      Charles H. Medley, Jr.
                         ENiGMA Software
                     659 Kennedy Street, N.E.
                     Washington, D.C.  20011
                          (202) 636-9078



                         Simple Overview
                         +-+-+-+-+-+-+-+

     The XES consists of two parts:

          o    The TRAP #5 Dispatcher.

          o    The User Mode Handler.


     Every XES function is accessed by passing parameter(s) on the 
stack,  and then doing a TRAP #5.   To allow for full independence 
between copies of Wind-X,  and their utilities, the TRAP #5 simply 
"fixes"  up the parameters and passes them to a subroutine I  call 
the User Mode Handler.

     The  purpose  of the User Mode Handler is to  replace  large, 
memory hogging subroutines that would be required for almost every 
WNX application with a simple call.

     This  allows the XES to serve as a way to do complicated  AES 
functions,  and  replace large subroutines that would normally  be 
needed  within an application with one call.   A good  example  of 
this  is  XES_REDRAW (43) which can handle window redraws  for  an 
XES-based application,  with just a few lines of code.   I will go 
into detail on how each call works later on in this document.

     The method used by the XES is this:

          o    Wind-XES does a JSR into the WNX application to
               begin to run it.

          o    When  the WNX does a call to the XES (via TRAP  #5) 
               it's execution is stopped, and the system is put in 
               supervisor  mode.   The data and address  registers 
               are saved (A1-A6 and D3-D7 are saved).

          o    The  Trap  Handler adjusts the value on  the  stack 
               where  the RTE is to occur (from the TRAP  #5)  and 
               saves  the  RTE address for use by  the  User  Mode 
               Handler,  and  then does an RTE back to the  parent 
               copy of Wind-X's User Mode Handler after setting.

          o    The   User  Mode  Handler  performs  the   function 
               requested and JSRs back into the WNX's code at  the 
               location that the TRAP #5 would have RTE'd back to.
               This  means  that  you should NOT try  to  fix  the 
               stack  up,  like  you  do after a  normal  call  to 
               GEMDOS,  because the User Mode Handler has  already 
               dealt with that.   The original A1-A6/D3-D7  values 
               are restored (as of 9/09/90 version  incarnation of
               the XES).

          o    This  occurs  over and over until  either  the  WNX 
               process   hits   an  RTS  that   doesn't   have   a 
               corresponding BSR/JSR within it's code, or until it 
               reaches a XES_SUBMIT call.  

     One  thing  to note is that all data  and  address  registers 
should  be assumed to be unknown values when a WNX is first  JSRed 
to.   This may change by the time Wind-XES makes it to market, but 
for the most part, this isn't needed.  Also, note that the  SR  is
not properly restored after the TRAP #5 call, so don't count on 
the CCR remaining unchanged after a TRAP #5 as you can with other 
TRAPs.  




                     How To Write For the XES
                     +-+-+-+-+-+-+-+-+-+-+-+-

     A WNX application has to do two things first:

          1)   It  must  call  XES_INIT  with  the  address  of  a 
               parameter block of the form:

     Name                Size           Purpose
     ----                ----           -------
     WNX_id              (word)         one word I.D. number, 
                                        assigned by the XES.
     WNX_idname          (16 bytes)     unique 16 byte identifier
                                        set by WNX.
     WNX_apid            (word)         application I.D. of parent 
                                        copy of Wind-X
     WNX_grafhandle      (word)         graphics handle of parent
     WNX_global          (long)         ptr to parent's GLOBAL
                                        array
     WNX_vdiparams       (long)         ptr to parent's VDI
                                        array
     WNX_aesparams       (long)         ptr to parent's AES array
     WNX_messagebuf      (long)         ptr to parent's message
                                        buffer
     WNX_in              (8 words)      WNX_in array
     WNX_out             (8 words)      WNX_out array
     WNX_flags           (word)         event flags (a la the AES
                                        call evnt_multi)
     WNX_link            (long)         address for resuming
                                        execution (used by XES)
     WNX_tcount          (word)         timer count in 20ms 
                                        between events.
     WNX_troutine        (long)         address of TIMER routine
     WNX_mroutine        (long)         address of MESSAGE routine
     WNX_broutine        (long)         address of BUTTON routine
     WNX_kroutine        (long)         address of KEYBOARD
                                        routine
     WNX_rroutine        (long)         address of REDRAW routine
     WNX_termroutine     (long)         address if WNX terminates 
                                        (this    runs   after    a 
                                        WNX_flush call!)

               The values for  WNX_id,  WNX_apid,  WNX_grafhandle, 
               WNX_global,      WNX_vdiparams,      WNX_aesparams, 
               WNX_messagebuf,  and  WNX_link are set by  the  XES 
               immediately after this call.

          2)   Now,  the WNX must do a XES_RSRCINIT with a pointer 
               to a binary resource that has yet to be fixed up to 
               the proper screen coordinates.  Because the GEM AES 
               is not friendly to programmers who design resources 
               in  color,  various options are allowed with a  one 
               word  flag  which permits you to determine  if  the 
               resource  is  scaled  in any way  relative  to  the 
               screen font size (which is how GEM does it), and if 
               so,  how.   This  first call to  XES_RSRCINIT  will 
               initialize  the resource that will be displayed  in 
               the main Wind-XES window.

               Note:  You may also use a resource  that  has  been 
               previously fixed, but the  provision  for  this  is
               not fully implemented as of 8/23/91.   Also,  Laser 
               C's RCP.PRG can generate a  .C  file  that  is,  in 
               essence, a .RSC file that you can "imbed" in your C 
               applications.  It will need a  "fixup",  so  simply 
               pass a pointer to the array it defines,  and  Wind-
               XES will work everything out...

          3)   At this point,  the WNX application can do anything 
               it wishes (i.e.  initialize system variables,  find 
               out information about the screen,  etc...) and even 
               call  the XES until it does a  XES_SUBMIT.   It  is 
               good  practice to do the XES_SUBMIT and NOT an  RTS 
               on this part of the code.   The WNX application  is 
               required  to  supply pointers to  subroutines  that 
               should  be executed by Wind-XES  when  events  that 
               it  is looking for occur BEFORE the  XES_SUBMIT  is 
               done.   By  making  the processing the  GEM  events 
               modular  this helps improve  execution  speed,  and 
               makes life easier on WNX programmers,  particularly 
               those who are writing piecemeal.

     For  more  information on  the  XES_INIT,  XES_RSRCINIT,  and 
XES_SUBMIT, consult the section on XES functions.

     As  a  note  to more sophisticated  (and  usually  dangerous) 
programmers,  there  are  ways to determine if an  application  is 
running  as  a  WNX,  as an ACC or as  a  GEM  program.   When  an 
application   is  a  desk  accessory,   the  value  P_PARENT   (at 
basepage+36 in your application) will be 0.  For WNX applications, 
this points to the basepage of the parent copy of Wind-X, which is 
what is running the WNX as a child process.   However,  to  ensure 
that  you  can tell it is not running as a GEM  program,  you  can 
simply  look  at  P_RESERVED (basepage+40) where you  will  see  a 
longword containg the ASCII equivalent of the string "XES".

(NOTE:  Atari has officially changed  this.   The  current  method 
would be to check to see if your P_RESERVED (basepage+40)  is  the
longword $00584553 ("XES"), and if it is, you are a .WNX.  If not, 
then check the current value of A0, and if A0 is null, you  are  a 
.PRG, otherwise, you are an .ACC.  This method won't  work  inside 
the Laser C shell, though.)


                Handling Events the ENiGMA Way...
                +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

     If  you look at the structure of the parameter block used  in 
XES_INIT,  you see that you have to supply pointers to routines to 
be  executed on events.   As stated earlier,  you must assume  all 
data and address registers are unknown when these routines start!
(NOTE:  This may change by release day!)

     The way this works is that Wind-XES catches events, and first 
it handles any of its  own  (i.e.,  window  redraws  of  the  main 
Wind-XES window, etc...), and then begins to dispatch to  each  of
its children, which can then take action on the events.

     To  aid  the  WNX programmer,  Wind-XES passes some  valuable 
information,  depending  on  the event type,  to the  WNX  in  the 
WNX_out array...



     "Link" Events
     *-*-*-*-*-*-*

          To  get access to these,  set bit #6 of  the  WNX_flags.  
     This  feature  should  be able to work,  but has  yet  to  be 
     tested.   If you are writing a WNX,  try to avoid using  this 
     call until we have verified it is 100% working!

          "Link"  allows you to recieve information as if you  had 
     done an EVNT_MULTI.   You recieve information in your WNX_out 
     array giving your information about the type of event(s) that 
     occurred.

     WNX_out+0.W    =    bits 0-5 tell which events occurred.
     WNX_out+2.W    =    mouse x coordinate at time of event.
     WNX_out+4.W    =    mouse y coordinate "  "    "  "    .
     WNX_out+6.W    =    the button state.
     WNX_out+8.W    =    states  of  the  alternate,   shift,  and 
                         control keys.
     WNX_out+10.W   =    number of times left button was clicked.
     WNX_out+12.W   =    key scan code for keyboard event.           
     WNX_out+14.W   =    the handle of the active GEM window  (the 
                         one on top!).   The handle is negated  if 
                         the window is NOT the Wind-XES window,and 
                         and is  positive if it  is  the  Wind-XES
                         window.


          "Link" mode also tells Wind-XES to turn  operation  over
     to the WNX application at the address contained in  WNX_link.  
     This  is  so  that a programmer can  dynamically  change  the 
     "return" address without mucking with the stack.

          A "Link" mode call should not terminate with an RTS, but 
     instead, with a XES_SUBMIT, which places the address that the 
     TRAP #5 would have RTE'd back to in WNX_link.

          Be cautious with "link" mode!



     Keyboard Events
     *-*-*-*-*-*-*-*

          Bit  0 of the WNX_flags must be set to be able to  check 
     for keyboard events.  The WNX application will get control of 
     the CPU,  and the routine pointed to by WNX_kroutine will  be 
     JSRed to.

     Parameters passed to the WNX are:

     WNX_out+0.W    =    scan code of key that was pressed.
     WNX_out+14.W   =    the handle of the active GEM window  (the 
                         one on top!).   The handle is negated  if 
                         the window is NOT  the  Wind-XES  window,
                         and is positive if  it  is  the  Wind-XES
                         window.

          The keyboard routine should terminate with either an RTS 
     or a XES_SUBMIT.



     Mouse Button Events
     *-*-*-*-*-*-*-*-*-*

          Bit  1 of WNX_flags must be set to handle  mouse  button 
     events.  The routine pointed to by WNX_broutine is JSRed to.

          Due to an idiosyncracy of Wind-X,  you can only wait for 
     a  "left mouse button pressed" event.   This limits you to  a 
     "one button" mouse for this kind of input.   Future revisions 
     may change this but no such plan has been implemented.

     WNX_out+0.W    =    mouse button state.
     WNX_out+2.W    =    x coordinate of mouse.
     WNX_out+4.W    =    y coordinate of mouse.
     WNX_out+6.W    =    number of times mouse entered the state.
     WNX_out+8.W    =    the states of the alternate,  control and 
                         shift keys during the event.
     WNX_out+10.W   =    index  of  the object  clicked  on  (this 
                         applies only to the resource displayed in 
                         the   main   Wind-XES window,    and   no 
                         "simulated"   FORM_DO   call   has   been 
                         performed.   Call  XES_FORMDO  with  this 
                         value in WNX_in+6.W to perform a FORM_DO- 
                         like action.
     WNX_out+14.W   =    the handle of the active GEM window  (the 
                         one on top!).   The handle is negated  if 
                         the window is NOT  the  Wind-XES  window,
                         and is positive if  it  is  the  Wind-XES
                         window.

          You can use mouse button events to handle events for not 
     just the main Wind-XES window, but a  window  opened  by  the
     WNX.  Simply do  an XES_XFORMDO for the window  you  need  to
     know about!



     Message Events
     *-*-*-*-*-*-*-

          Bit  4 must be set in WNX_flags for the WNX  to  process 
     GEM  messages.   The  routine pointed to by  WNX_broutine  is 
     JSRed to.

          This  is  very important:   A WNX must never  alter  the 
     contents  of the message buffer (the address of which  is  in 
     WNX_messagebuf) because other WNXes may have a need to  check 
     for events!

          With this, you can check for GEM events, and even send a 
     message  to  another resident  application,  including  other 
     WNXes (provided they, too, are looking for messages).

     WNX_out+0.W    =    RESERVED (usually 1)
     WNX_out+2.W    =    type of message.
     WNX_out+14.W   =    the handle of the active GEM window  (the 
                         one on top!).   The handle is negated  if 
                         the window is NOT  the  Wind-XES  window,
                         and is positive if it is the Wind-XES
                         window.



     Timer Events
     *-*-*-*-*-*-

          Bit 5 must be set for a timer event to be processed by a 
     WNX.  The routine pointed to by WNX_troutine is JSRed to.

          A  WNX  can  wait for a timer event  for  no  less  than 
     20ms,  which  is the finest timer event possible on  the  ST.  
     There are no guarantees by either GEM,  the AES,  or the  XES 
     that exactly 20ms has elapsed between calls.   In  fact,  one 
     should  check the system clock (via the BIOS) or  install  an 
     interrupt (which should NEVER call the XES!) to handle  time-
     critical code...

     (IMPORTANT NOTE:  Never give less than a 1/5  second (i.e., a
     WNX_tcount of 10) delay between timer events  when your timer
     routine is calling GEMDOS, BIOS or XBIOS.   Right  now,  some 
     testing has indicated a problems occurring when programs  are
     run while such tight time constraints are being placed on the
     system.  Case in point is the sample code  provided  for  the
     BIN2C.WNX file converter, which does disk writes on the timer
     routine.  On my 16mhz 68000 machine, when WNX_tcount  is  set     
     to  10,  it  works  reliably  with  programs  being  run  and 
     terminate in rapid succession (using DC Desktop or the normal
     ST Desktop on TOS 1.2.).  With a WNX_tcount of 1, the program
     will crash under the same conditions.  This is why  BIN2C.WNX
     is not very fast... <grin>)

          When  a WNX is given control after a  timer  event,  the 
     following parameters are passed:

     WNX_out+0.W    =    reserved  (usually 1)
     WNX_out+2.L    =    number  of timer events processed by  the 
                         parent  copy  of  Wind-XES since it   was 
                         launched.   (naturally,   limited  to  32
                         bits!)
     WNX_out+14.W   =    the handle of the active GEM window  (the 
                         one on top!).   The handle is negated  if 
                         the window is NOT  the  Wind-XES  window, 
                         and is positive if  it  is  the  Wind-XES
                         window.



     The Purposes of WNX_rroutine and WNX_termroutine
     *-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-

          WNX_rroutine is automatically JSRed to if it is nonzero. 
     No bits in WNX_flags need be set.   WNX_rroutine is  executed 
     every time the main Wind-XES window is redrawn, and it should 
     not  do  an XES_DRAW of an object in that window  during  the 
     execution  of  WNX_rroutine.   No parameters  are  placed  in 
     WNX_out.

          A good use for WNX_rroutine is checking things that  may 
     change.  The ENiGMA Control Panel checks both the system time 
     and  date and pops in to supervisor mode to check the  system 
     palette in order to accurately represent any changes to these 
     values.

          WNX_termroutine is run when a WNX is about to  terminate 
     and  get  flushed from memory.   As stated  earlier  in  this 
     documentation,  it should be used for housekeeping  purposes, 
     like restoring stolen vectors,  etc...   However,  if D0.L is 
     equal  to  the ASCII value of the 24 bits that  make  up  the 
     string "XES",  the WNX is kept in memory, but  Wind-XES  will
     act oblivious to it.   As of 9/09/90,  this  feature  is  not
     fully implemented, but will be at the time of release.      


     
          
                XES Functions (08/23/91 Revision)
                +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

     All XES functions, excluding XES_INIT are performed like  so:

               move.w    <function_id>,-(a7)
               move.w    #-1,-(a7)
               trap      #5

     ...where the <function_id> is the number corresponding to the 
XES function you want.  XES_INIT works like so:

xes_init       move.l    <pointer to parameter blk>,-(a7)
               move.w    #0,-(a7) 
               trap      #5

     The following are descriptions of the various XES  functions.  
The descriptions are in a format, like this:

<name of function>  (<function number (decimal)>) 
<WNX_in parameters>
<WNX_out parameters>
<description of the function>



XES_submit          (-1)
in:  none.
out: none.

     This  allows  a WNX to stop execution of itself and  to  turn 
over  control to the XES so that other processes can get a  chance 
to  run.   In most cases,  an RTS without a corresponding  JSR/BSR 
would  suffice,  but  you  should use XES_submit  after  your  WNX 
initialization code.



XES_init            (0)
in:  none.
out: none.

     This initializes the XES parameter block of your  application 
and  makes sure it is recognized by the system.   You  should  NOT 
have any code preceding this,  as your program may be flushed  due 
to any number of reasons (i.e.  insufficient RAM,  conflicts  with 
other application's interfaces, etc...).
 


XES_rsrcinit        (1)
in:  WNX_in+0.W     =    non-zero causes .RSC to be fixed up.
     WNX_in+2.W     =    type of fixup.
                              0    =  no scaling.
                              1    =  scale pixel coords only.
                              2    =  scale both pixel and
                                      character coords.
     WNX_in+4.L     =    if WNX_in+0 = 0, a pointer to the binary 
                         resource to be fixed up, or else it is a 
                         pointer to a structure like this:

                         pointer to a .RSC header
                         pointer to the first tree in the .RSC

                         Where the .RSC  header  is  of  the  same 
                         format as the header of a binary resource 
                         file (.RSC).

out: WNX_out+0.W    =    number of trees in resource,  or 0 if the 
                         call failed.
     WNX_out+2.L    =    address of first tree in resource.
     WNX_out+6.L    =    address of the tree list in resource.

     The  first  time  this  call  is  made,  it  should  be  done 
immediately after a XES_init.  This first call tells Wind-XES what 
the resource that it will  be  displaying  in  the  main  Wind-XES
window for this WNX will be.   When Wind-XES is loading a  utility
in, it checks to see if it will fit  from  the  width  and  height 
coordinates  of  the  largest  resource  tree  contained  in  that
resource, and if there is not enough space in the Wind-XES window,
the application  is  flushed  immediately.   Subsequent  calls  to
XES_rsrcinit  can  be  used  to  initialize  resources  for  other
purposes,  such as windows  (see Paint-X).



XES_sibling         (2)
in:  WNX_in+0.L     =    pointer to 16 byte i.d. name field.
out: WNX_out+0.W    =    number of WNXes in system with that  i.d. 
                         name.
     WNX_out+2.L    =    a  pointer  to  "tempbuf",  which  is  a 
                         buffer containing a list of the matching 
                         .WNXes  in the system.  The format of an
                         entry in this structure is:

                         application i.d. of parent.W
                         WNX i.d. of matching child.W

                         If both are null, you are at the  end  of 
                         the "match" list.

     This function's sole purpose is to provide a way for a WNX to 
find  out if multiple copies of itself have been  installed.   For 
some  programs,  mainly vector stealers,  having  multiple  copies 
installed  can create headaches.   All this function does is  find 
out   how   many   copies   are   installed.    A   new   function 
(WNX_inqsibling) will probably be added which returns  information 
about each of the WNX processes that matches.



XES_mesagwrite      (4)
in:  WNX_in+0.L     =   pointer to recipient list/ap_id of ACC to send to.
     WNX_in+4.W     =   length of message (up to 256 bytes)
     WNX_in+6.L     =   pointer to message

out: none.

The eXtended Environment System can allow a WNX to write messages
selectively to another WNX process.  The recipient list 
is a structure of the form:

     (parent's ap_id).W | (32  bit  bit  field,  representing  the
     32 potential children of that parent).L

A set bit means to write to that child. 



XES_malloc          (38)
in:  WNX_in+0.L     =    amount of memory to allocate
out: WNX_out+0.L    =    0  if failed,  or location  of  allocated 
                         RAM.

     This function is used in order to fix a bug in some revisions 
of TOS that frees up memory allocated by a desk  accessory.   This 
happens mainly when a DA (or WNX, for that matter) is trying to do 
a M_ALLOC while a GEM program is running at the same  time.   When 
GEMDOS does the M_ALLOC,  it incorrectly gives the "ownership"  of 
that block of RAM to the GEM program.   This function is the  only 
known  "illegal" call in Wind-X,  but it is necessary in order  to 
prevent this GEMDOS bug from affecting program performance.

     To free up this RAM, simply use M_FREE (the GEMDOS call).



XES_flush           (39)
in:  none.
out: none.

     Tells the XES to terminate the execution of this application, 
and to free up the memory used by it.  The WNX will still have the 
WNX_termroutine  executed before being flushed,  so it can do  any 
cleanup it finds necessary (i.e.,  restore altered system vectors, 
close windows, etc...)



XES_genv            (40)
in:  none.
out: WNX_out+0.L    =    address of the Line-A structure.
     WNX_out+4.L    =    ptr to virtual workstation attributes  (a 
                         45 word structure).
     WNX_out+8.W    =    screen width (in pixels).
     WNX_out+10.W   =    screen height (in pixels).
     WNX_out+12.W   =    X  scale of screen font to an 8x8  screen 
                         font  (i.e.,  a 16x8 system  screen  font  
                         would make this value 2.
     WNX_out+14.W   =    Y  scale of screen font to an 8x8  screen 
                         font.

     This  call  simply  lets  the WNX  know  about  the  system's 
graphics capabilities.   You should note that the GEM work area is 
not  the same as the screen size.   To avoid doing a  WIND_GET  to 
find the work area on the desktop,  use XES_pwindow instead, since 
during  the accessory loading process,  calling the AES  would  be 
unpredictable  from  a  WNX  (and calling the  AES  during  a  WNX 
initialization should be avoided!).

     The  scales of the screen fonts is handy for when you have  a 
slider defined for a resource,  and the resource changes size  due 
to the changes from an 8x8 screen font (color STs) to 8x16  screen 
font  (monochrome).   This usually is a problem  for  applications 
that have vertical sliders, and the problem occurs naturally under 
GEM,  and is not limited to Wind-X.   (In fact, this is a neat fix 
for it!)



XES_pwindow         (41)
in:  none.
out: WNX_out+0.W    =    X   coordinate  of  the   Wind-XES window 
                         containing this application.
     WNX_out+2.W    =    Y coordinate of the Wind-XES window.
     WNX_out+4.W    =    W (width) of the Wind-XES window.
     WNX_out+6.W    =    H (height) of the Wind-XES window.
     WNX_out+8.W    =    X coord of desktop work area.
     WNX_out+10.W   =    Y coord of "     "   "    " .
     WNX_out+12.W   =    W of the   "     "   "    " .
     WNX_out+14.W   =    H of the   "     "   "    " .

     The  purpose  of  this  function  was  mainly  to  discourage 
programmers  from using the GEM AES WIND_GET call to find out  how 
large   the   desktop   work  area  was   during   their   program 
initialization,  which  may  occur  during  the  loading  of  desk 
accessories.   AES calls by a WNX, from within Wind-XES running  a
DA during the loading of DAs can cause unexpected problems.

     Basically,  WNX_out+8  to WNX_out+14 work like that  WIND_GET 
call to find out the coordinates of the desktop work area.

     WNX_out+0  to  WNX_out+6 allow the application  to  find  the 
coordinates of the main  window  used  by  the  copy  of  Wind-XES
running it.


 
XES_draw            (42)
in:  WNX_in+0.W     =    index of the starting object's depth  for 
                         the XES_draw.
     WNX_in+2.W     =    index of the ending object's depth.
out: none.

     This  call  is used to allow a WNX to  redraw  its  interface 
inside  of  the  Wind-XES window.   A good example of  this is the 
TIME.WNX  program,  which  updates  even when  other  windows  are 
overlapping it.  XES_draw is intelligent enough to output properly 
even with other windows  overlapping  the  main  Wind-XES  window,
which contains  the  resource you're  redrawing,  and  this allows
for "background" output.



XES_redraw          (43)
in:  WNX_in+0.W     =    handle of the window to redraw.
     WNX_in+2.W     =    alignment flag.
                              0 =  use ob_x and ob_y of resource.
                             -1 = align to window's work area.  
     WNX_in+4.L     =    address  of  the  resource  tree  to  use 
                         during the redraw.
out: none.

     This  is  a potent function which allows for quick  and  easy 
redraws of windows that contain resource trees.   All you need  to 
provide for the call is the handle of the window to redraw, a flag 
fr alignment,  and the address of the tree to use for the  redraw.  
There ARE limitations:

     o    Wind-XES currently  only draws 10 levels  deep  into  the 
          resource tree.

     o    Wind-XES does not check for proper  pointers  and  values 
          in this routine, so BE CAREFUL!

     These limitations may be removed by release day.

     The beauty of this call is that with six lines of  code,  you 
can redraw a window.   For example,  in Paint-X, two resources are 
initialized,  and  the second resource has a pointer to its  first 
resource  tree called "rsrcptr2".   This is the resource with  the 
icons showing the drawing tools, among other things.

xes_redraw_example
               move.w    w_handle,WNX_in
               move.w    #-1,WNX_in+2
               move.l    rsrcptr2,WNX_in+4

               move.w    #43,-(a7)
               move.w    #-1,-(a7)
               trap      #5

     However,  you  should always have  your  WNX_mroutine,  which 
catches  GEM  message  events ready to  catch  the  window  redraw 
requests  from  GEM for your WNX's window if you wish to  do  this 
properly,  as  Wind-XES  doesn't  notify  you  officially  of  the
redraw (GEM does this very well,  you know!).    It  is  a  simple
matter  to check  for the redraw message and to make sure the
window  handle matches yours before calling XES_redraw.



XES_chrsrc          (50)
in:  WNX_in+0.W     =    index of the new tree to use.
out: WNX_out+0.W    =    the new tree's index (-1 if failed)

     This  call  allows you to use a resource that  has  different 
resoruce  tree  "forks" within the Wind-XES main window.   A  good 
example  is the ENiGMA Control Panel (ECP.WNX) which  has  several 
levels the user can interact with, thanks to this call.



XES_stredit         (64)
in:  WNX_in+0.W     =    handle of the window this resource is in.
     WNX_in+2.L     =    address   of  resource  tree   containing 
                         editable object.
     WNX_in+6.W     =    index  of  the editable object  (must  be 
                         F_text or F_boxtext!).
     WNX_in+8.W     =    key   press  to  check  (uses   scan-code 
                         method, like C_RAWIO and EVNT_KEYBD).
     WNX_in+10.W    =    requested   cursor  position  inside   of 
                         editable  field.  (-1  makes  the  cursor 
                         position the first empty character inside 
                         of the displayed string). 
out: WNX_out+0.W    =    ASCII  character's  value.   -1  if  call 
                         failed.
     WNX_out+2.W    =    new cursor position (-1 if call failed).

     This  function lets the programmer use editable text  objects 
within the framework of Wind-XES without halting  other processes.  
Care  should  be  taken because the user  can  edit  multiple  WNX 
processes  simulaneously  (i.e.,  the same keypress goes  to  four 
different  applications!).   However,  the  advantage is  that  it 
allows  all  of  the WNX tasks to  continue  running  without  the 
interruption a GEM AES FORM_DO will cause.

     The limitation on this call is that the window containing the 
editable  object MUST be on top.   This prevents  keypresses  from 
going  to processes that are underneath the "active"  window,  and 
makes handling the XES_stredit call much