EEDRAW

                               User Guide




















EEdraw Manual For Version 2.4, 
Gershon Elber & Peter Cooper 

           EEDRAW - Electrical Engineering Drawings (ver 2.4)





     BECAUSE EEDRAW/EED-PS/EEDEPSON ARE LICENSED FREE OF CHARGE, I
     PROVIDE ABSOLUTELY NO WARRANTY, TO THE EXTENT PERMITTED BY
     APPLICABLE STATE LAW. EXCEPT WHEN OTHERWISE STATED IN WRITING, I
     GERSHON ELBER PROVIDE EEDRAW/EED-PS/EEDEPSON PROGRAMS "AS IS"
     WITHOUT WARRANTY OF ANY KIND, EITHER EXPRESSED OR IMPLIED,
     INCLUDING, BUT NOT LIMITED TO, THE IMPLIED WARRANTIES OF
     MERCHANTABILITY AND FITNESS FOR A PARTICULAR PURPOSE. THE ENTIRE
     RISK AS TO THE QUALITY AND PERFORMANCE OF THE PROGRAM IS WITH YOU.
     SHOULD THE EEDRAW/EED-PS/EEDEPSON PROGRAMS PROVE DEFECTIVE, YOU
     ASSUME THE COST OF ALL NECESSARY SERVICING, REPAIR OR CORRECTION.
     IN NO EVENT UNLESS REQUIRED BY APPLICABLE LAW WILL GERSHON ELBER,
     BE LIABLE TO YOU FOR DAMAGES, INCLUDING ANY LOST PROFITS, LOST
     MONIES,OR OTHER SPECIAL, INCIDENTAL OR CONSEQUENTIAL DAMAGES
     ARISING OUT OF THE USE OR INABILITY TO USE (INCLUDING BUT NOT LIMITED
     TO LOSS OF DATA OR A FAILURE OF THE PROGRAM TO OPERATE WITH
     PROGRAMS NOT DISTRIBUTED BY GERSHON ELBER) THE PROGRAM, EVEN IF
     YOU HAVE BEEN ADVISED OF THE POSSIBILITY OF SUCH DAMAGES, OR FOR
     ANY CLAIM BY ANY OTHER PARTY.


1. INTRODUCTION


EEDraw is a simple parametric drawing program, specifically designed for EE
(Electrical Engineering) type of drawing. The program fully allows new parametric
types, through library mechanisms, and in fact all the EE types are defined this way.
This library mechanism is extremely useful in defining new types and can be used for
other applications other than EE.

The following graphic devices are supported for display: Hercules, CGA, ATT, EGA,
VGA and SVGA (through user provided BGI driver). The following printing devices are
supported (via the printing drivers): EPSON compatible printers (8 pins), PostScript
printers. 

Usage: EEDraw [-z] *[FileName[.EED]]

Options: [-z] Print version number and usage.

Quick start:
The program comes with quite common setup. If you have a mouse and a
VGA/EGA/Hercules/CGA then you can simply start eedraw. Typing 'eedraw
82720-1.eed 82720-2.eed' will restart eedraw and prompt you for two windows for the
above two files. Click on left button (return on keyboard) to pick window corners.
Click on right button (space bar on keyboard) if you want to default size (maximum
size). Alt-Q, by default, will take you out.

From version 2.4 onwards a layer structure has been implemented, this will enable the
user to display only the information on the screen they want, also in adding new
layers of there own further detail and notes can be added to a drawing. Hard copy of
drawings show only the layers that were turned on when the drawing was last saved,
all other information is hidden from the printed output.




2. INSTALLATION

 For correct execution of the main program (EEDraw), the following files must exist
in one of the path directories: 

     1. EEDraw.exe
     2. EEDraw.cfg
     3. EEDraw.bnd
     4. EEDraw.hlp
     5. *.lib

For correct execution of the printer drivers (EED-PS, EED-Epsn), the following files
must exists in one of the path directories (see also Appendix B):

     1. EED-PS.exe                  1. EED-Epsn.exe
     2. EED-PS.cfg                  2. EED-Epsn.cfg
     3. *.lib                       3. *.lib

The library files (*.lib) are the same for the printer drivers and eedraw itself and
should exist probably only once. See SETUP below shows how to change the setup of
this programs. The default values should be enough to start and learn this program. 
 
3. SETUP


EEDraw set up is done through two files: EEDraw.cfg and EEDraw.bnd.

EEDraw.cfg


This files contain global parameters that should be selected and set only once, in final
installation stage. Empty lines or anything after a semicolon (';') is ignored. This file
is read once when eedraw is being started. Parameters that can be set are:

1. AutoPan -        Boolean flag. If TRUE, any operation involves in the drawing 
                    space (such as move, copy or draw) will auto-pan if cursor
                    exists screen.  If FALSE, Panning option must be used
                    manually to perform this operation.  This Boolean flag can be
                    set from the Status main menu.
       For example:
       AutoPan TRUE
2. WindowName -        Boolean flag. If TRUE each EEDraw data file name is printed 
                       in the head of the window. If FALSE no name is printed and
                       this makes some  more space for the drawing itself.  This
                       Boolean flag can be set from the Window main menu.
       For example:
       WindowName TRUE
3. ATKeyboard -        Boolean flag. If TRUE, it is assumed AT style keyboard bios 
                       calls (also known as Enhanced keyboard - if you have F11/F12
                       on your  keyboard, good chance you can set this to TRUE).
                       This will enable using  more complex scan codes, not
                       supported by regular keyboard (such as  F11/F12). Note
                       however it may HANG your system if it is not so.
      For example:
      ATKeyboard FALSE
4. MouseSensitivity -  Integer flag. Default is set to 10 which is a good  start. Making
                       this number bigger makes the mouse less sensitive.
      For example
      MouseSensitivity 10
5. HVLines -           Boolean flag. If TRUE, lines are coerced to be vertical or 
                       horizontal only. This Boolean flag can be set from the Status
                       main menu.
      For example
      HVLines TRUE
6. SnapDistance -      Integer value. Sets the distance in drawing space of   points 
                       to be snapped. You probably do not want to change this,
                       especially not in  the middle of a drawing. This Integer value
                       can be set from Status main  menu.
      For example:
      SnapDistance 16
7. Allow256Colors -    Boolean flag. 256 colours BGI drivers will have a richer  set of
                       colours. If FALSE such a driver will be forced to use only 16
                       colours  effectively having same colours are EGA or VGA
                       default colours   (EGAVGA.BGI).
      For example:
      Allow256Colors FALSE
8. AllowAsyncEvents -  Boolean flag. The user interface supports async event 
                       handling. This means that one can pop up something while
                       something else  is being popped up already for example. This
                       has the advantage of the  ability to arbitrary "jump" between
                       commands. However this may be VERY  confusing as well.
                       Leave it FALSE at least at the beginning!
      For example:
      AllowAsyncEvents FALSE

9. SaveBackMethod -    Integer. Underlaying windows are being saved for short  life
                       time pop up items such as queries. This integer selects where
                       to  save this data.
      Options are:
      1 - Conventional memory.     This obviously reduces the amount of memory  for
                                   the EE drawings themselves.
      2 - Expanded memory.
      3 - XMS Extended memory      (currently not supported).
      4 - Disk file.               For reasonable response this better be a ram disk.
                                   See also SaveBackPath below.  The device, this
                                   data is saved into, should be able to hold ~100k
                                   for  16 colours BGI drivers and twice that for 256
                                   colours BGI drivers.
      For example:
      SaveBackMethod 1
10. SaveBackPath -     String. This string specifies where back windows should  be
                       saved. This full path should have a postfix '\' in it.
      For example:
      SaveBackPath "f:\temp\"
11. Mouse -            Boolean flag. Inform the system if a Mouse exists or not.  If
                       this is commented out, auto detection will be used.
      For example:
      Mouse TRUE
12. Joystick -         Boolean flag. Inform the system if a joystick exists or not. 
                       Must be TRUE for a joystick to be used. Personally the
                       joystick was not  found accurate enough for this type of
                       drawing.
      For Example:
      Joystick FALSE
13. BGIDriverPath -    specifies where to look for the *.BGI drivers. Note the  drivers
                       are supplied with this program (type 'dir *.bgi') and you should 
                       update this path to the exact place you had moved them.
      For example:
      BGIDriverPath "C:/TC/BGI/ATI"
14. GraphDriver -      Set what type of display device to use. The relative driver 
                       *.BGI are looked in the directory specified in BGIDriverPath
                       above.  The following values are valid (same as TC 2.0/TC++
                       1.0 graphics.h file  if that helps):

      0      -     Auto detect (default, so you can delete this one...)
      1      -     CGA (Hires two colours mode)
      3      -     EGA
      4      -     EGA64
      5      -     EGAMONO
      7      -     Hercules
      8      -     ATT (Not tested)
      9      -     VGA
      999    -     SVGA (super VGA - see SVGANameMode below)
      For example:
      GraphDriver 999

15. SVGANameMode -     select a BGI driver to use. This driver is searched for   only  if
                       GraphDriver above is set to 999. Thus driver is assumed to be
                       800 by  600 in resolution but any driver with 4:3 aspect ratio
                       will probably be  o.k.. This driver is searched in the directory
                       specified by BGIDriverPath  above. For example if the driver
                       you want to use is ATI.BGI and in mode 2:
      SVGANameMode "ATI.2"
16. Libraries -        String value. A list of libraries (neither file type, nor  full  path
                       is required - only the name) to automatically load on restart, 
                       separated with commas (','). Libraries can also be loaded using
                       the libs  main menu, and/or will be automatically loaded when
                       a data file needs  them.
      For example:
      Libraries "TTL4LS,EPROM,GENERAL,LINEAR"
17. LibrariesPath -    String Value. Full path where libraries from  LoadLibByName
                       should be searched for. Note libraries loaded automatically 
                       will be searched in all path dirs and specified by PATH env.
                       variable.
18. FrameWidth -       Integer value. Sets the border width for all windows.
19. Colours control.   Below are all colours values to select. Each can be one of the
                       following 8 colours:
       0 - WHITE
       1 - BLACK
       2 - RED
       3 - GREEN
       4 - BLUE
       5 - YELLOW
       6 - CYAN
       7 - MAGENTA
                       The colours are self explanatory and grouped into the
                       following groups:  Root controls colours of the back ground
                       root window. Actv sets the active  drawing window colours.
                       Psv sets the passive window(s) colours. PopUp  controls all pop
                       ups like queries colours. Highlight sets the highlight  objects
                       colour. Below are the colour groups themselves.

       ;Root window - the background.
       RootFrameolor         7
       RootForeColor         3
       RootBackColor         5
       RootXorColor          6

       ;Pop up menus/queries.
       PopUpFrameColor       2
       PopUpForeColor        5
       PopUpBackColor        5
       PopUpXorColor         6


       ;The currently active file/window if any.
       ActvFrameColor        2
       ActvForeColor         5
       ActvBackColor         4

       ;All other passive files/windows if any.
       PsvFrameColor         3
       PsvForeColor          5
       PsvBackColor          4

       ;High light colour - selected items.
       HighLightColor        2


Following is the primary system layer colours,the program has upto 45 layers
available to the user with several of them preset, The numeric representation for
these layers is given at the end of this manual.
 
       LayerWire             0
       LayerBus              5
       LayerGate             3
       LayerIEEE             2
       LayerPinFun           4
       LayerPinNum           4
       LayerPinNam           4
       LayerRefDes           2
       LayerAttr             6
       LayerDevice           7
       LayerNotes            6
       LayerNetNam           3
       LayerPin              3
 
If this configuration file is not found in any of the path directories, a message is
printed to the screen, and internal defaults will be used instead. This is NOT
recommended - fix that as soon as you can, as the internal defaults are not guaranteed
to be anything specific.

EEDraw.bnd


This file allows you to bind any of the program internal functions (as can be selected
from any of the menus) to a specific key. Note some keys are hard-bound and can not
be used to rebind function (such as arrow keys - see Functionality below). The format
of the file is following. Empty lines, or lines begin with a semicolon (';') are ignored.
Every line consists of three items: "FunctionName KeyName ScanCode" separated by
white spaces. FunctionName are the fixed names this program supports (see blow).
KeyName is the name of the key ("AltK" for example) this FunctionName will be bound
to. Up to 4 characters are allowed for KeyName, and this name will appear in the main
menu which contains this function. ScanCode is the scan code of the bounded key.
If the key is regular ascii code, this ascii code is the scan code. If it is extended code
(such as F? keys are), add 256 to this value. All numbers should be in decimal.
Currently available FunctionName(s) and their associated main menu (see
Functionality section below for their description):



      File menu:
             LoadEEDFile
             NewEEDFile
             SaveAllEED
             SaveEEDFile
             SaveEEDAsOld
             SaveEEDAsNew
             SaveNetList
             CloseEEDFile
             ClearAll
             Directory
             ChangeDir
             ShellToDos
             ExitEEdraw

      Window menu:
            PopWindow
            PushWindow
            MoveWindow
            ResizeWindow
            FullSize
            ShowName
            MakeActive
            NameActive
            PanWindowLeft
            PanWindowRight
            PanWindowUp
            PanWindowDown

      Display menu:
            ZoomOut
            ZoomIn
            ZoomReset
            RedrawAll

      Libs menu:
            LoadLibrary
            LoadLibByName
            FreeLibrary
            ViewLibrary
            DirLibrary
            ChDirLibrary

      Draw menu:
            DrawLine
            DrawBus
            DrawConnect
            DrawText
            DrawLibItem
            ChangeLayer
            TglOneColor
            SetOneColor

      Modify menu:
            ModifyMove
            ModifyCopy
            EditLibItem
            ModifyDelete
            ModifyUnDel
            ModifyCut
            ModifyPaste
            ModifyDrop

      Status menu:
            Help
            GetMemoryFree
            GetZoomFactor
            SetDrawText
            SetTextSize
            SetHVLines
            SetSnapFactor
            SetLineWidth

      Other (not in any menu):
            SameAgain

4. Functionality


This section describes the currently available function set, and main modes. Although
most of the keys may be bound to any function as described in the Setup section
(EEDraw.bnd description), some of them are hard-bound and should not be used. Note
that in order for enhanced Keyboard scan codes to be used, such as F11 and F12,
'ATKeyboard' must be set to TRUE in eedraw.cfg file. See 'Mouse' and 'Joystick' in
eedraw.cfg for mouse and joystick setup. Below are the "hard-bound" keys: 

A.    All the numeric keypad (arrow keys, home, PhUp, End, PgDn). These keys  are
      used to move to cursor (even if mouse exists).
B.    All the numeric keys but 0 (used by shift-arrows).
C.    Enter (or Return) key. this is the SELECT key.
D.    Space bar. This is the ABORT key.
E.    Tab. This is equivalent to MIDDLE button key.

The arrow keys are used to move the cursor (co-exist with mouse), and if shifted,
move cursor faster. In addition to the cursor movement, three important keys are
defined as well:


A.    SELECT key, hard-bound to the Enter (or Return), left button on mouse,  if such
      exists, and button 1 on the joystick, if exists.
B.    ABORT key, hard-bound to the Space bar, right button on mouse if such  exists,
      and button 2 on the joystick, if exists.
C.    MIDDLE key, hard-bound to the Tab, middle button on mouse if such  exists (or
      pressing both mouse buttons), and both buttons on the joystick. All the eedraw
      functions described below uses these hard-bound keys.

This version supports multi file editing via multi window system (running on regular
DOS). Each time a file is being open, a new window is created for it. If window header
is to be shown (see ShowName function below) the file name the window is associated
with is displayed, in addition to its current drawing layer, and the status information.
The status is shown on the right hand side of the title bar, displaying the current
windows drawing modes and attributes. Below is a representation of the status
elements:


     File Mode     Line Drawing       Snap         Line Width     Single Colour

      File Mode:
            O)riginal  -           this file is exactly the same as first loaded in.
            M)odified  -           the current file state should be saved. Data has
                                   been modified.

      Line Drawing:
            O)rthoganal      -           Lines only either vertical or horizontal
            A)ngular   -           Lines can be drawn in any direction

      Snap:
                                   This gives a numeric display of the current snap
                                   radius 

      Line Width: 
                                   This shows the current line drawing width in use


      Single Colour:
            S)ingle    -           All the layers which are turned on are displayed in
                                   a single colour.
            N)ormal    -           All the layers which are turned on are displayed in
                                   the native colour.

There is no limit on the number of windows/files that may be open at once, aside
from DOS and memory limits. The libraries are being shared between all files, so
reduce memory usage. This means that even if two (or more) files needs LINEAR.LIB
it will be loaded once into memory. However, there is no way for the program to
detect which file uses which library when they are being saved and it is assumed ALL
libraries currently loaded are being used by all files.

Few type of interactors are defined to query the user:

      A.    Yes/No question - prompt the question, with Yes and No buttons. The
            SELECT key will select the answer. ABORT key is ignored. One may use
            the Y/N keys as well to signal Yes/No answer.
      B.    Continue question - prompt a message, and wait for SELECT on the
            continue button. ABORT key is ignored. One may use the C key to
            continue as well.
      C.    String question - prompt a message, and waits for string input. This
            facilitates a full line editor as follows (independent of key bindings): *
            Right and Left arrows will move right and left. Insert toggles
            Insert/Overwrite modes (toggles cursor shape). Delete deletes current
            character. * Backspace deletes character to the back. Home and End will
            move to beginning/end of string respectively. Esc clears the current
            string. Return will terminate editing.
      D.    List question - prompt with a list of items (files names for example). An
            item will be picked by the SELECT key if applicative (when viewing a
            directory nothing needs to be picked). ABORT key will usually abort the
            operation, but may have some special operation as well or may be ignored.
      E.    Menu(s) question. Two types of menus are used - top down from the
            mainmenu, and pop up on special occasions. Menus behave very much
            like List questions. SELECT key selects menu item while ABORT key
            usually abort the menu with no selection at all.


A. File menu:
 LoadEEDFile      -    Prompts for a file name (List question), and reads it from the
                       current directory, if SELECT key, abort if ABORT key. Note
                       file type must be '.eed'. A new window is created for it while
                       the user is prompted to set the window size (see
                       ResizeWindow).
 NewEEDFile       -    Creates a new drawing window not assosicated with any file.
                       This is the way to create new drawings. The user is prompted
                       to set the window size (see ResizeWindow).
 SaveAllEED       -    Saves all unsaved drawings. This is probably useful before
                       quitting eedraw.
 SaveEEDFile      -    Saves currently edited file. This routine can be used only after
                       a new file was saved at list once, or it was loaded. In both
                       cases, it will be saved on the same name, after renaming old
                       one to have '.bak' extension. Ask for verification (Yes/No
                       question).
 
 SaveEEDAsOld     -    Same as SaveEEDFile, but prompts with list of all '.eed' files
                       in current directory, and saved by the name selected  if
                       SELECT key, or abort if ABORT key.
 SaveEEDAsNew     -    Same as SaveEEDFile, but prompts for a new file using String
                       question.

 SaveNetList      -    Saves a net list for the active window. Default name is same
                       as '.eed' but with '.net' type. Net list is generated by scanning
                       the line and bus object in the drawing. A drawing should be
                       designed ahead of time so the net list will be correct in two
                       respects:
      1.    The net list can not identify individual pins in a BUS and  will list them
            all as one (BUS) connection. Therefore  bus lines should be made
            individually if this program is  to make a full net list for it.
      2.    Since only lines and buses are scanned, library items  connected directly
            connection will not be detected. An  easy solution is to put a dummy line
            connection there so  that connection will be scanned correctly. When the
            net list is generated the scanned lines/buses are highlighted so the
            remaining non scanned ones can be easily viewed.

 CloseEEDFile     -    Closes a drawing window associated with a file. Note that non
                       of the above saving functions close the window, and this
                       function is the only way to close a window. Ask for
                       verification if data modified (Yes/No question).
 ClearAll         -    Clears all eedrawing data in a picked window. The user is
                       requested to "click" on the window to clear. Ask for
                       verification (Yes/No question).


 Directory        -    Display content of current directory as in List question. both
                       SELECT key and ABORT key can be used to exit this mode.
                       Unlike LoadEEDFile, all files are displayed.
 ChangeDir        -    Prompts with String question for a new directory. Old
                       directory is provided to begin with.
 ShellToDos       -    "Fork"s (I wish this was true...) to the DOS O.S. . Type 'exit' at
                       the DOS prompt to return to EEDraw.
 ExitEEdraw       -    Exits the Program. Ask for verification (Yes/No question) and
                       issue a warning if not all files were saved.

B. Window menu:
 PopWindow        -    Pops up a window the user picks. The window is being picked
                       by "clicking" on it. ABORT key aborts this operation.
 PushWindow       -    Pushes down a window the user picks. The window is being
                       picked by "clicking" on it. ABORT key aborts this operation.
 MoveWindow       -    Moves a window the user picks. The window is being picked by
                       "clicking" on it. ABORT key aborts this operation. The picked
                       window frame is popped up so current position is all visible.
                       The cursor prompt changes to a box in the window size that
                       the user needs to place as the new position.
 ResizeWindow     -    Same as MoveWindow but for resizing the window.
 FullSize         -    Blows up a window the user picks. The window is being picked
                       by "clicking" on it. ABORT key aborts this operation. This
                       make the window as big as possible in the current display
                       device. Calling this function again on the window will recover
                       its original size. This function may be activated on drawing
                       windows only. 

 ShowName         -    A toggle to show/hide window name. The window name is
                       simply the filename the window is associated with. Also
                       displayed is the current status of the drawing window, for the
                       status codes, see earlier in this manual.
 MakeActive       -    All drawing operations are performed on the active window. If
                       only one drawing window exists it is the active one. If more,
                       exactly one of them is the active one. This function selects
                       the active window by a user pick. The window is being picked
                       by "clicking" on it. ABORT key aborts this operation.
 NameActive       -    All drawing operations are performed on the active window. If
                       only one drawing window exists it is the active one. If more,
                       exactly one of them is the active one. This function selects
                       the active window by name. A list query of all drawing window
                       (file) names is being popped up and the selected becomes the
                       active one.
 PanWindowLeft         -     Pan the ACTIVE window a half window to the left.
 PanWindowRight        -     Pan the ACTIVE window a half window to the right.
 PanWindowUp           -     Pan the ACTIVE window a half window up.
 PanWindowDown         -     Pan the ACTIVE window a half window down.

C. Display menu:
 ZoomOut          -    Zoom out (center of screen remains at center) by factor of 2.
                       Note that if you zoom out from regular zoom factor, text will
                       disappear as it can not be shrinked. You can enable text from
                       the Status menu manually.
 ZoomIn           -    Zoom in (center of screen remains at center) by factor of 2. 
                       ZoomReset - Reset Zoom value to the regular zoom factor.
 RedrawAll        -    Redraw all screen.





D. Libs menu:

 LoadLibrary      -    Prompts for a file name (List question), and reads it from the
                       library directory, if SELECT key, abort if ABORT key. Note file
                       type must be '.lib'.
 LoadLibByName    -    Loads one or several libraries (separated by commas) by
                       providing their names. To load EPROM.LIB and LINEAR.LIB
                       "eprom,linear" should be typed. Libraries are been search in all
                       directories as specified by the PATH environment variable.
 FreeLibrary      -    Prompts with all loaded libraries with List question, and frees
                       the selected one if SELECT key, abort if ABORT.
 ViewLibrary      -    Prompts with all loaded libraries with List question, If a library
                       has been selected via SELECT key, prompt with all parts
                       defined in this library again with a List question. Selection of
                       a part with SELECT key will display it. ABORT will go back to
                       library List question, which can be aborted again via the
                       ABORT key.
 DirLibrary       -    Displays content of library directory library files (those with
                       '.lib' extension) as in List question. Both SELECT key and
                       ABORT key can be used to exit this mode.

 ChDirLibrary     -    Prompts with String question for a new directory for library
                       search. Old directory is provided to begin with. This directory
                       is used for Load/DirLibrary routines above only.
                       LoadLibByName and auto library loading upon eedraw file
                       loading will search all directories as specified by the PATH
                       environment variable.



E. Draw menu:
 DrawLine         -    Enters drawing mode. If HVLines is set (see SETUP,
                       EEDraw.cfg section), only horizontal/vertical lines are
                       allowed. In this mode, pressing SELECT key will insert a new
                       point in the created polyline and pressing ABORT will delete
                       the last entered point. If however, there are no points at all in
                       the current polyline, ABORT key will abort this mode. Also,
                       pressing SELECT twice (at the SAME place as the last point
                       entered) will complete the drawn polyline. MIDDLE key will
                       also complete the line drawing.
 DrawWire         -    Same functionality as above, but forces the drawing layer to
                       the 'Wire' layer, wether it is enabled or not. Once the line is
                       entered, the current layer is returned.
 DrawBus          -    Same as DrawLine, but draw thicker lines.
 DrawConnect      -    Draw a connection junction, if SELECT key is pressed, or
                       abort if ABORT key is pressed.
 DrawText         -    Prompts for a string with String question, and then position
                       the text horizontally or vertically. If the positioning is
                       terminated with ABORT it is ignored, SELECT will update.


 DrawLibItem      -    Prompts for a part name with String question. If this is not
                       the first invocation to this mode, last part will be used as
                       default string (remember you can always use Esc to clear to a
                       fresh line). If part is found (name is exactly the same as shown
                       in the ViewLibrary function above), a pop up menu will allow
                       to rotate it 90 degree CW or CCW or mirror it. Successive
                       SELECT will transform the library item to the desired
                       orientation, while ABORT will abort this DrawLibItem mode.
                       SELECT PlaceIt (top menu entry) will allow to position the
                       part in the exact place. The user is also being prompted for
                       Chip (i.e. 74LS00) and Part (i.e. IC7) names if they are
                       required/allowed (see Appendix on library file definition) for
                       this part. These are positioned similar to the way DrawText
                       position its text, except that Chip name is already known and
                       can not be modified.
 ChangeLayer      -    Prompts the user to either change the mode, name or colour
                       of an already defined layer, else add a new layer to the data
                       base. The first menu presented to the user is a list of all the
                       currently defined layers, also two extra entries 'Quit' and
                       'NewLayer', this selection list works like all other long lists in
                       EEDraw, if there are more entries than screen space the list
                       can be scrolled up, by using the scroll bar on the right hand
                       side of the list. If a currently defined layer is selected the user
                       is presented with a sub menu to change the layer settings,
                       These changes are: Display mode, Display Colour, Layer Name,
                       and SetUsable, the last option is a quick method of setting a
                       selected layer both usable for drawing, and active.
                       If 'NewLayer' is selected the user is lead through a series of
                       system prompts to setup a new layer, this process is straight
                       forward, at any point in either layer create, or modify the
                       ABORT function will take the user back one menu level.
 TglOneColor      -    This function will take all the displayable layers to one colour,
                       which is defined with the next function. All primary layer
                       control is retained, where only layers which are turned on or
                       usable are displayed.
 SetOneColor      -    Prompts the user to select the 'OneColor' display colour, care
                       should be taken not to set this colour to any which is
                       unusable!




F. Modify menu:

This menu is heavily based on Picking objects. a single object is  being picked if the
cursor is on an object. The cursor is considered on an object if one of the following: 

      A.    Line and Bus items: the cursor is on one of the Line/Bus end points (any
            point that was set by SELECT when it was created, including internal
            points).
      B.    Connect item: the cursor is on the Connect center.
      C.    Text item: the cursor is inside the smallest axes parallel bounding box
            holding this text.
      D.    Library item: the cursor is on any polyline end point (including internal
            points).

The picked object will blink. SELECT key will select it, ABORT key  will cause the next
object, if such exists at this position, to blink  until one is selected via the SELECT
key, or no more objects can be  picked.

If no object at all is found at the cursor point, the point is used  as first corner of a
box to pick a set of objects - a second SELECT  key will pick the second corner of the
box, ABORT key will abort this  mode. All objects intersect with the defined box, will
be considered  picked, with no more verification.

 ModifyMove       -    Picks object(s), and moves it (them) to a new position. Once
                       the object(s) is (are) picked, SELECT key will set its(their) new
                       position, ABORT will leave it unchanged.
 ModifyCopy       -    Picks object(s), and copies it (them) to a new position. Once
                       the object(s) is (are) picked, SELECT key will place it(them) in
                       new position, ABORT will abort the copy operation.
 EditLibItem      -    if the picked object(s) is a single library item, allows editing
                       any of the following (via a pop up menu):
      A.    Editing the part name. This is the only way to add a part  name to a
            library item if the library item has none by  default.
      B.    Toggle to Draw/Undraw chip name (if this chip is allowed  to have one).
      C.    Reposition Chip name (if this chip have one).
      D.    Reposition Part name (if this chip is allowed to have one).
      E.    Reorient the lib part.
      Picking one of the above via SELECT will allow text positioning or text editing
      (via String question). ABORT or selecting Done (first menu entry) will abort this
      EditLibItem mode.
 ModifyDelete     -    Deletes the picked object(s). The deleted object(s) is (are)
                       saved in a special 10 places deep stack, and deleted items can
                       be undeleted using the ModifyUnDel function. Each of the 10
                       placed stack can hold any result of a pick no matter how many
                       objects are inside. This Delete/Undelete mechanism can be
                       used to cut and paste even between different files/windows -
                       this stack is never being cleared.
 ModifyUnDel      -    Undelete the last delete operation (see ModifyDelete), from the
                       delete stack (LIFO).

 ModifyCut        -    Same as ModifyDelete, but original is NOT deleted. The object
                       is being pushed onto the undelete stack and can then be
                       ModifyUnDel, ModifyPaste etc.
 ModifyPaste      -    Same as ModifyUnDel, but the undelete stack is NOT modified.
                       This function enables pasting and placing the same object few
                       times.
 ModifyDrop       -    Drops the top of stack from the undelete stack. May be used
                       to drop a cut/paste object sequence from stack.

G. Status menu:
 Help                  -     Pops up an help window and displays the content of
                             eedraw.hlp. If the help window is already popped up,
                             this function will close it (acts like a toggle.).
 GetMemoryFree         -     Prompts with a continue question, on the current free
                             memory. Getting close to zero is unsafe!
 GetZoomFactor         -     Allows you to see the current zoom factor
 SetDrawText           -     Sets drawing of text smaller than minimal size (8x8).
                             This will draw text at 8x8 size which is too big, but may
                             be sometimes useful.
 SetTextSize           -     Sets the scaling (up only) of the text size. By default this
                             is equal to 1, but scaling up by 7 is allowed. 
 SetAutoPan            -     If TRUE, auto panning will occur when placing objects
                             that have been moved off the active WINDOW. The
                             object will be place so it is centered in the window.
 SetHVLines            -     Allows drawing of diagonal lines as well if set to FALSE.
                             Uses Yes/No question.
 SetSnapFactor         -     Sets the invisible grid the cursor position is snapped to.
                             You probably do not want to change this, especially not
                             in the middle of file editing. Uses String question, and
                             display current Snap factor to begin with.
 SetLineWidth          -     Sets the current line width, at the moment there is only
                             widths '1' and '3' available, this should change in the
                             next release.

H. Other (not in any menu):
 SameAgain        -    Executes the last function again. This is hard bounded to
                       MIDDLE key, although in may be bounded to another key as
                       well.

5. Spacial Notes


Designing using A4 page size does not require much memory even when few libraries
are loaded. My system with 640k (-70k of the O.S) has almost 300k free to use (Use
the GetMemoryFree function to query free memory), when all the provided libraries
are loaded. I guess you will need to work hard to get down to less than 100k. If you
succeed and/or you system has less than 640k memory, make yourself a rule: never
to go below 64k of free memory. The program need about 32k of temporary memory
for the different operations, and getting close to that is dangerous! When you
approach 32k of free memory, you will be issued a warning (Continue question):  Free
memory too small - dangerous to continue.  Every 30 second (if you do any operation
in that time). Continuing at this point may result with loss of all your work - the
program will exit when no more memory will be available! This is especially true if
'SaveBackMethod' in eedraw.cfg is set to conventional memory.  Yes, I know this is
ugly, but you eat what you cook, right? I used this program quite a bit, and never
succeeded to go below 200k, so why bather.

6. Acknowledgement


I would like to thank skh@eng.sun.com (Steve Howell) for his great comments during
the last stages of bringing version 2.0 up.


Appendix A. Glossary


SELECT Key        -    The key used for the select operation. Currently hard-bound
                       to  Enter (or Return), the Left mouse button if mouse exists,
                       and to  Button 1 in a joystick.

ABORT Key         -    The key used for the abort operation. Currently hard-bound to 
                       Space bar, the Right mouse button if mouse exists and to
                       Button 2  in a joystick.

MIDDLE key        -    Another general purpose key. Currently hard-bound to  Tab
                       key, the Middle mouse button if mouse exists and has middle 
                       button (or both right and left buttons pressed simultaneously) 
                       and to both Buttons of the joystick.

Screen Space      -    the space of the display device. Depends on the graphic 
                       device coordinates on the selected mode.

Drawing Space     -    the space in which the drawing objects exist. This space  is
                       bounded by a wide box (zoom out twice to see this box on an 
                       empty drawing) so it will fit into an A4 (8.5" by 11") page in
                       both  the EPSON and the PostScript printer drivers (see
                       Appendix B).


Appendix B. Printer drivers and general support tools


The following printer drivers are available (see also installation section):

1. EPSON printer.

 Usage: EEDEpson [-g] [-r] [-1] [-2] [-3] [-d] [-z] FileName[.EED]

 Options:   [-g] Output goes to standard output as 1 bit per pixel (B&W) GIF file.
            [-r] Output goes to standard output as raw data.
            [-1], [-2], [-3] Output goes to LPT1:, LPT2:, LPT3: respectively.
            [-d] If output goes to Epson printer - print in double the density.
            [-z] Print version number and usage.

      * if neither [-g], not [-r] are specified, output is in Epson compatible format
      (default).
      * If non of [-1], [-2], [-3] are specified, output goes to standard output.
      * [-1], [-2], [-3], [-d] are ignored if [-g] or [-r] are specified.




2. PostScript Printer.

 Usage: EED-PS [-f FontName] [-z] FileName[.EED]

 Options:   [-z] Print version number and usage.
            [-f FontName] Specify the font name to use instead of the default name
            (Times-Roman).

 PostScript output goes to stdout. If a PostScript Printer is connected to com2: serial
port then 'eed-ps drawing.eed > com2:' will print drawing.eed on that printer.

3. Converter.

 Usage: CONV [-l] FileName.EXT

 Options:   [-l] Convert the old style library files into version 2.4 files, 

 This program is used to convert old style data files into the version  2.4 format,
adding layer information where needed. The layers are  selected on a best guess basis,
hence the user may need to edit the   data files to change the default information. 
Unlike other EEDraw programs the entire filename plus extension needs  to be passed
into the convertor program, as it can take in both '.EED'  files and '.LIB' files. The
convertor is called automatically from the  LoadEEDFile menu item when an old style
file is called.

Appendix C. Library file format


This appendix describes the format of the library file. It contains all the information
required to create your own libraries. The libraries are designed to be parametric only.
I.e. no bitmaps are supported. You can look at the given libraries while reading this
appendix for better understanding.

Empty lines and lines that starts with '#' are ignored. In order to identify a library as
such the first line must start with 'EEDRAW-LIB'. Following in the same line is version
number as 'Version X.X'. Currently 'X.X' equal '1.0' and is ignored. However it may
be used in future versions, to ensure backward compatibility. Following are the parts
themselves. Each part definition begins as follows:


DEF Name Prefix #Pins TextInside DrawNum #Units #PinsPerUnit

Were
      1.    Name is the Part name, i.e. "74LS00". If Name is prefixed with "~" (for
            example "~74LS00") then the name is not drawn, nor it will be accessible
            to editing by the user.
      2.    Prefix is the prefix to be used in chip name (IC, R, C etc.). If prefix is "~",
            then no prefix is drawn.
      3.    #Pins is the same as number of entries in PINS (see below), i.e 14 for
            74LS00.
      4.    TextInside is 0 if pin text is to be put outside as well (as the pin numbers
            are), otherwise inside. You may put any positive integer there to scale the
            distance inside. 10 is a good start.
      5.    DrawNum is 1 if pin numbers are to be drawn, 0 otherwise.
      6.    #Units holds number of multiple entries. For example 74LS00 has 4 units
            (Nand gates). For no multiple units put 0 here.
      7.    #PinsPerUnit holds number of entries for one unit if more than one unit
            per part. If #Units is 0, it is ignored.

The part definition follows by the following blocks, in any order:




1. DRAW/ENDDRAW        -     defines how to draw the part. This block is optional, and 
                             a simple box with half the pins on each side is drawn if
                             this block is  not defined. The following commands are
                             supported:

      A Ly x y r t1 t2 (Define ARC at x, y, radius r, angles t1 to t2)
      P Ly n x y x y x y... [F] (Define a POLYLINE of (any) length n)
      C Ly x y r (Define a CIRCLE at x, y, radius r)
      S Ly x1 y1 x2 y2 (Define a square (Not filled))
      T Ly x y h str (Define a text string at x, y (see below))
      L Ly x1 y1 x2 y2 [I] (Define terminal line to part - see PINS)

      Notes:
      A.    a text string (T) with be drawn horizontally if h is 1, vertically if 0. Also '~'
            characters will be replaced by spaces, or this provides a mechanism to
            have spaces in the string.
      B.    If the polyline (P) is postfixed by a F, the polyline should define a closed
            shape that will be filled. The first point of the polyline must be identical
            to last one in this case.
      C.    If the line (L) is postfixed by an I, this line is assumed to define negative
            logic, and a small circle will be drawn to express that.
      D.    The number of L definitions should be exactly the same as #Pins in the
            DEFS line if #Units = 0, and equal #PinsPerUnit if #Units != 0. The order
            will match to the order in the PINS/ENDPINS block if #Units = 0 and to
            the order in the MULTI/ENDMULTI if #Units != 0.
      E.    Arcs (A) should not exceed 180 degrees, are CCW, and 0 degrees is at 3
            o'clock.
      F.    The 'Ly' (Second field on each line) is the layer designation field, Later in
            the appendix is the description of what each layer does.


2. PINS/ENDPINS        -     defines the names (strings) associated with each pin.
                             This  block must always exists, and it is the minimum
                             required to define a part.  The block holds #Pins lines
                             each hold the string defines that pin. This  order must
                             be the same as define in the DRAW/ENDDRAW as L
                             commands  (if DRAW/ENDDRAW block is defined), from
                             pin 1 to #Pins. Empty lines  are allowed and defined
                             with only '~' in them. Not sign for X (vertical bar  above
                             it) is defined by ~X.

3. MULTI/ENDMULTI      -     This block must exists if #Unit != 0. Each line in this 
                             provides a mapping from L terminal definitions in the
                             DRAW/ENDDRAW block  to the pin numbers in a multi
                             unit part. This is required as same L  terminal will have
                             different pin number in different Units.  Each line in
                             this block holds the pin numbers of a unit.  Number of
                             lines should be equal to number units in part.

Part definition terminates with the ENDDEF line.

General Notes:

      1.    All parts are scaled up to easy the access of a single pin (by 16, but you 
            should not wonder about it too much - its internal mapping to drawing
            space).
      2.    Library file can hold any number of parts (at least one though...).
      3.    Library file must have '.lib' extension, to be usable by the EED* programs.



Appendix D Layers.


Following is a description of what each of the primary system layers is  used for, In
the current version of the library files layers like the IEEE layer are never used, it is
a good idea for the user to stick to the basic layer conversion when creating new
symbols for the libraries as some of the layers are called automatically by layer
number in the program, hence there is no way for the user to change there position
in the table. A good example of this is the 'Wire' layer, Layer '0', called by layer
number in the 'DrawWire' menu entry. All of the layer table is saved in the '.EED' data
file, so any new layers added, or the status of existing layers, is saved when the data
file is saved.


 Wire       -     Basic wire interconnections
 Bus        -     Buses (Groups of wires)
 Gate       -     Basic outline of a device
 IEEE       -     IEEE device outlines, (Not yet in libraries)
 PinFun     -     Function attached to a particular device pin
 PinNum     -     Pin Number on a device
 PinNam     -     Name attached to a pin on a device
 RefDes     -     Reference designator for a component
 Attr       -     Attribute to be attached to a component
 Device     -     Device type/name
 Notes      -     User notes etc
 NetNam     -     Wiring net name layer, needs changes to 'SaveNetList'
 Pin        -     Device Pins/Connection Points

The layers are numbered from zero (Wire) to Twelve (Pin), when described in the
database files and library files. 












































































Gershon Elber + Peter Cooper
Email: gershon@cs.utah.edu pcc@uk.ac.york.minster