Program:
                 OV.EXE - HP LaserJet II Overlay Utility
                        ALPHA TEST 1.03
                 Copyright 1988 by Keith P. Graham

     Contact:
                 Keith Graham at Other Woman BBS (707) 938-3508.

     Description:
                 OV.EXE creates Macro Files which can be sent
                 to a Hewlett Packard LaserJet II to form a
                 forms overlay. It uses graphics files from
                 several available sources to create the
                 macro file. The macro created by OV.EXE
                 will be set to automatically print whenever
                 a form feed is sent to the printer.

     Uses:
                 OV.EXE is useful for creating Letterheads
                 or endbars for letters. It can be used to
                 place graphics or signitures on form letters.
                 It can be used to created forms. Anything that
                 can be scanned or created on a paint program
                 can be placed automatically on a printed page.

     Operation:
                 First a suitable graphic must be created using
                 a paint file or a scanner program. Files must be
                 one of the following types:
                      1. PDA - Palantir scanned images type 1 or 2.
                      2. TIF - Aldus Microsoft Tag Image Format File.
                      3. PCX - (or PCC), ZSOFT PC Paintbrush files.
                      4. GEM - Gem Paint images.

                 Use black and white files only. The LaserJet cannot
                 print in colors. Do not use grey level images as
                 the LaserJet can't handle them either.
                 The files must have an extension of one of the above.
                 Use Optiks to convert a file from other formats.

                 OV.EXE does not create the graphics files, these
                 must be created by another program.

                 Start OV.EXE by typeing OV and pressing return.

                 A screen with fill in blanks will appear. If you
                 have a composite screen and have trouble reading the
                 screen use the MODE BW80 command before starting
                 OV.EXE.

                 There are 7 fields to fill in. You enter data into
                 the fields by typing. You move from field to field
                 by using the cursor keys. If you chicken out you
                 just press Esc.

                 Pressing F1 will give you information about the
                 field that the cursor is on.

                 Pressing F10 checks the data on the screen and
                 if it is correct it will create the overlay file.
                 If there is something wrong on the screen, the
                 field will be flagged and you will get the help
                 screen for that field.

                 FIELDS:

                 1. Image file. This is the name of a file with
                    the extension of PDA, PCX, IMG or TIF.
                    It must be a valid image file or OV will
                    give up. If the file is not on the current
                    disk and/or directory you can include a
                    path with the file name.

                 2. Macro file. The macro file is created by OV.EXE
                    and has all of the HP escape sequences to create
                    the macro on the printer. You must give a valid
                    file name. OV does not check to see if the file
                    already exists. If you put an existing file name
                    here, OV will replace it.

                 3. Printer density is the DOTS PER INCH that the
                    graphic will print at. It is either 75, 150
                    or 300. You have to know about how big your
                    graphic is to make it print at the right size on
                    the paper. If you graphic is 640 pixels wide
                    (640 is one screen), it will print out at
                    2-1/8 inches wide at 300 DPI and about 8-1/2
                    at 75 DPI. OV does what it is told, it is up to
                    you to decide how you want to print it.

                 4. Macro number. The LaserJet II allows up to 32
                    macros numbered 01 to 32. You can have more than
                    one macro around at a time so you may want to
                    give them separate numbers. Only one automatic
                    overlay is active at a time.

                 5. Inverse. This field controls whether or not
                    black dots form the screen will appear as
                    black dots on the paper. Some graphics programs
                    produce graphics which are acceptable as white
                    pixels on the screen on a black background, but
                    they look like negatives on the paper.
                    Entering a N here will make the paper print
                    just like the screen image. Placing a Y here
                    will make the screen a negative. Some graphics
                    are not immediately obvious as to which to use,
                    but you must use one or the other

                 6. X position. This is in character columns. It is
                    the count of inches from the left. If you
                    wanted the macro to start printing at the left
                    hand margin you would put 00000 in this field.
                    If you wanted the macro to start in the middle
                    of the paper, you would put 4.000 here.
                    (this field is not checked. Make sure its less
                    than 8.5 inches)

                 7. Y position is the vertical count of inches
                    measured from the top of the page used for
                    positioning the graphic. If you want the graphic
                    to print at the top of the page, put 000 here.
                    if you want it to start in the middle put 5.500.
                    (this field is not checked. Make sure its less
                    than 11 inches)


     Using the Macro File:

                  After you create a macro file you have to get it
                  to your printer. The easiest and fastest way is
                  to use the DOS COPY command.

                  If you had named the macro file LETTERH.HP:
                  (this is an example you can name it anything
                  that you like.)

                  Enter from the DOS prompt:

                        COPY LETTERH.HP LPT1: /B

                   COPY is the DOS COPY command.
                   LETTERH.HP is the name of the macro file that
                   you created.
                   LPT1: is the printer to copy to. If you have
                   a printer on LPT2: then use that instead.
                   /B means do the copy in binary mode. The /B
                   is required.

                   The PRINT command will not work correctly with
                   binary files. Do not use PRINT.

                   Once a file is created you can use it as often as
                   you like. The LaserJet will remeber the overlay
                   until it is turned off or reset. Use HPRESET.COM
                   included here to reset the LaserJet.

      Notes:

                   The Macro files are big. Even little ones can
                   be 256K. Make sure that there is enough free
                   room on the disk.

                   Your LaserJet must have enough memory (most likely
                   at least 1.5M) to run the graphics. You must have
                   a LaserJet II, LaserJet+ or a LaserJet 500+.
                   Some LaserJet compatibles can't handle m cros.

                   Sending a new macro to the printer with a different
                   number supercedes the current macro, but does
                   not clear it from memory. In a future release I
                   will add a few HP setup utilities.