OzGIS                                           
                                                                                
                                V8.0                                            
                                                                                
                            (January 1992)                                      
                                                                                
                                                                                
                                                                                
                                                                                
                                                                                
                                                                                
                                                                                
                                                                                
                                                                                
                                                                                
                                                                                
                                                                                
                                                                                
                                                                                
                                                                                
                                                                                
                                                                                
                                                                                
                         Geismar Holdings Pty Ltd.                              
                                                                                
                         QMDD Box 6108                                          
                         Queanbeyan 2620,                                       
                         Australia.                                             
                                                                                


                                                                       2
                         PREFACE                                                
                                                                                
OzGIS is a software system for displaying geographically referenced data as     
coloured choropleth maps on graphics display devices. The maps portray the data 
values associated with geographic zones by uniform colours, site data by        
different sized symbols, and line data by different line types.                 
                                                                                
OzGIS is designed to provide the following interactive graphics facilities:     
                                                                                
      -  to facilitate the interpretation of spatial distributions of data      
      -  to prepare colour maps to be output on hard copy devices for           
         publication and presentation,                                          
      -  to facilitate the interpretation of spatial distributions of data      
      -  to assist the analysis and modelling of spatial relationships in       
         data.                                                                  
                                                                                
The system can therefore be used to analyze socio-economic and demographic      
data produced by censuses and surveys and to support management decisions       
associated with for example marketing, sales, site and personnel location,      
and advertising.                                                                
                                                                                
                                                                                
The software was originally developed as part of a research project at the      
Division of computing Research of the Commonwealth Scientific and Research      
Organisation (CSIRO) in Canberra for a mapping product called COLOURMAP.        
                                                                                
Software development started in 1979 with the purchase of hardware that had     
been developed for the DIDS mapping system in the White House in Washington DC. 
This hardware consisted of a PDP11 mini-computer and a DeAnza display system.   
The display featured a 12bit frame buffer, 4096 value primary look-up table and 
cascaded 256 value colour table. This enabled maps of up to 4000 zones (e.g.    
USA Zip codes) to be displayed and manipulated very rapidly, and is the best    
hardware so far produced.                                                       
                                                                                
The environment changed over several years, with moves to larger PDP11 systems  
and to VAX and CDC machines. Several display systems were used, Tektronix,      
Jupiter and RAMTEK, and maps were generated on plotters and film recorders. The 
system was also available on CSIRONET, an Australia-wide computer network with  
Control Data and FACOM host computers. The 1981 ABS Census data could be        
accessed via the SIR/CENSYS system on the Cyber 845. A system was developed to  
handle the Census district boundaries digitised by the Division of National     
Mapping, to enable windowing, line simplification and aggregation for production
of geographic map data files. The SAS system was available on the FACOM 180 for 
statistical analysis and display of map data.                                   
                                                                                
 The Division of computing research was split into the CSIRONET computing bureau
and the new Division of Information Technology in 1985. Later, CSIRONET was     
given to private industry. The mapping project was abandoned.                   
                                                                                
The software was resurrected in late 1990 and ported to the IBM PC to produce   
the current system.                                                             
                                                                                
The first year of development was supported by Techway, and APASCO supported    
the development of techniques for retail applications. APASCO used the system   
and hardware for several years as part of their consulting activities to churn  
out thousands of maps.                                                          
                                                                                


                                                                       3
 The purpose of the Guide is to introduce the facilities of OzGIS. The Guide is 
intended to complement the messages and assistance given during the operation of
OzGIS.                                                                          
                                                                                
 The user should understand the techniques of statistical data analysis and     
computer mapping, and also have an elementary understanding of colour           
representations.                                                                
                                                                                
This manual describes the  IBM PC version. Some of the facilities that were     
available on the PDP11 and VAX systems have not yet been ported.                
                                                                                
                                                                                
                                                                                
                                                                                
Geismar Holdings is a Canberra based software company offering consulting and   
contract programming services in the areas of:                                  
                                                                                
. C and FORTRAN programming                                                     
. Spatial applications                                                          
. Scientific applications                                                       
. Graphics                                                                      
. UNIX workstation, minicomputer and PC environments                            
                                                                                


                                                                       4
                    1. OzGIS INTRODUCTION                                
                       ==================
 

  1. 1 Introduction                                      
       ------------
 
                                                                                
Easy to use systems are necessarily trivial systems, and the enormous number of 
options within OzGIS means that it takes some time to understand everything.    
                                                                                
However, maps can be produced quite simply by using only a small number of      
options and by using the system defaults.                                       
                                                                                
Start by using the OzCensus; its a simpler version of OzGIS suitable for        
Census-type mapping.                                                            
                                                                                
This manual tries to lead readers through the main options first and for the    
most common applications first. Working through the manual and generating the   
maps as explained will soon provide the knowledge to enable the rest of the     
system to be used.                                                              
                                                                                
The system consists of several modules:                                         
                                                                                
OzEnter  - for entry of data files into the system.                             
OzData   - preparation of data for mapping                                      
OzZone   - formation of zones / polygons structure from line segments           
OzGIS    - interactive display and analysis                                     
OzCensus - Display and analysis of Census type data (subset of OzGIS)           
OzGISco  - maths coprocessor version of OzGIS                                   
OzMap    - output of saved displays on plotters and printers and to files       
OzTerr   - definition of territories from zones                                 
OzProj   - map projections                                                      
                                                                                
Future releases may include:                                                    
                                                                                
OzCatch - allocation of zones to site catchments                                

  1. 2 Concepts                                          
       --------
 
 OzGIS can be considered as one system of a facility for analysis and display   
of Census type data. The various components are:                                
                                                                                
 - Database systems for manipulation and retrieval of attribute data            
 - Systems for generation of map boundary data                                  
 - Statistical analysis systems with graphic display and reporting facilities   
 - Mapping systems with analysis and hardcopy facilities.                       
                                                                                
 Visual inspection of choropleth maps is the intuitive way to interpret the     
spatial features of data. An analyst needs to be able to rapidly display and    
manipulate maps to aid his understanding. OzGIS was designed to enable maps to  
be changed within seconds so the analyst does not lose his train of thought.    
                                                                                
 OzGIS enables the analyst not just to display a map, but to generate the map   
that best shows the features of the attribute data. A hardcopy map can be       
generated as the final operation as a record or for dissemination.              


                                                                       5
                                                                                
The original design of OzGIS employed image processing technology to obtain     
speed of display. The essential hardware components were a dedicated super mini 
computer and an advanced raster display system. These display systems enable    
maps to be displayed (in image form) in full colour, where the colours are      
selected from a large palette. The main feature is that the colours are assigned
by hardware tables, and can be rapidly changed by rewriting the tables. Hence,  
once a map has been displayed, attribute data can be rapidly processed and      
displayed, as the major difference between successive maps is that the map zones
change colour. The hardware components can be packaged together to form a       
compact unit; a mapping workstation.                                            
                                                                                
 It is expected that an analyst would have access to a workstation close to his 
office. The workstation would usually be connected via a computer network to    
provide access to large host machines. The host machines would contain the      
database systems from which map data could be extracted, and other systems for  
analysis and hard-copy generation.                                              
                                                                                
 OzGIS aims to accept basic data files and to provide most of the facilities    
required for the analysis and display of attribute data as choropleth maps. The 
analyst has to be able to rapidly use the facilities, so OzGIS provides an      
interactive user interface. The user interacts via menus and is aided by on-line
assistance.                                                                     

  1. 3 Environment                                       
       -----------
 
 OzGIS requires advanced raster display systems for rapid display of maps.      
Unfortunately PC display systems are extremely limited in capability. In        
particular only a maximum of 256 colours are available (on 512K super VGA       
boards). OzGIS is able to generate maps on most graphic devices by using polygon
fill to colour map zones. This faciity also allows for hardcopy generation of   
maps previewed on raster displays.  PC display systems do not have hardware     
polygon fill, so map display is slow.                                           
                                                                                
 OzGIS is based on the GKS graphics standard. The standard provides device      
independence, and the basic graphic capabilities of lines, text and fill. OzGIS 
does contain its own set of GKS-type routines which can be used to interface to 
display devices with hardware fill capabilities or to other device independent  
packages. The INTERACTOR graphics package is used for the interactive version,  
and the SCIPLOT package for hardcopy map production.                            
                                                                                
 OzGIS is a large FORTRAN program. It will run on computer systems with a       
FORTRAN 77 compiler and about a mega-byte of memory. The system is well         
structured, so by using overlays and reducing capabilities (array sizes) the    
software can be implemented in smaller memory machines. Hence OzGIS is          
reasonably portable.  The PC version is heavily overlayed to fit it into the    
artificial 640K limit imposed by the DOS operating system.                      
                                                                                
Generally the speed of the system is dependent on hardware:                     
                                                                                
Processor 286 -> 386 -> 486                                                     
Disk speed                                                                      
Floating point processor                                                        
Extra memory for RAM disk                                                       
                                                                                
INTERACTOR is a graphics package produced by:                                   
                                                                                


                                                                       6
Interactive Software Services,                                                  
25 St Michael's Close,                                                          
Penkridge,                                                                      
Stafford. ST19 5AD.                                                             
U.K.                                                                            
                                                                                
We have found INTERACTOR very good, and the support is excellent.               
                                                                                
SCIPLOT is a plotting package produced by:                                      
                                                                                
MicroGlyph Systems,                                                             
PO Box 474,                                                                     
Lexington, MA 02173,                                                            
U S A                                                                           


                                                                       7
                    2. SUMMARY                                           
                       =======
 
                                                                                
OzGIS was designed to:                                                          
                                                                                
. facilitate the interpretation of the spatial distributions of data            
. prepare maps to be output on printers and plotters                            
. assist the analysis and modelling of spatial relationships in data            
                                                                                
The system can therefore be used to analyse socio-economic data produced        
by censuses and surveys and to support management decisions associated with     
for example Government planning, marketing, sales, site and personnel           
location, advertising and natural resources.                                    
                                                                                
Products:                                                                       
                                                                                
. Zone maps displaying polygons that are filled (with colours, patterns or      
  hatching) to show the distribution of attribute data                          
. Line maps displaying lines in different line patterns to show the attribute   
  data distribution                                                             
. Site maps displaying symbols at locations where the symbol sizes show the     
  attribute data distribution                                                   
. Bivariate maps showing filled zones for two attribute files                   
. Zone and line maps showing lines overlayed on zones for two attribute files   
  Zone and site maps showing site symbols overlayed on zones for two attribute  
  files                                                                         
. Geographic maps displaying polygons, line segments, symbols or site names     
  according to feature types but without reference to attribute files           
. Histograms showing the number of items (zones, lines or sites) assigned       
  to each class, or the number of items within value intervals (distribution)   
  or the attribute values sorted in ascending order                             
. Scatter diagram for two attributes                                            
. Map statistics                                                                
. Map reports                                                                   
                                                                                
Files:                                                                          
                                                                                
. Data files are raw Ascii data files in a variety of external formats. Standard
  GIS formats and formats from Census Bureaus and Mapping Agencies are          
  supported                                                                     
. Geographic files describe geographic data in terms of the graphic elements    
  zones, polygons,line networks, line segments, and points                      
. Attribute files contain the values of attributes (variates, statistics,       
  variables) referenced to zones, line or site names.                           
. Names files contain a list of zones, lines or sites that defines a region     
  of interest                                                                   
. Combine files define new items in terms of zones for aggregation              
. Marker files define simple shapes as polygons for display as symbols          
. Saved display files contain the information to regenerate a complete map      
. Device files define the graphics devices and their capabilities; colours,     
  fonts, line types, hatching, markers etc                                      
                                                                                
User Interface:                                                                 
                                                                                
. Menu / windows interface                                                      
. Help facility                                                                 


                                                                       8
. Trace information                                                             
. File interrogation, audits, deletion                                          
. Tutorials                                                                     
                                                                                
Data processing                                                                 
                                                                                
. Subsetting of geographic files                                                
. Line segment simplification                                                   
. Joining short line segments for polygons                                      
. Amalgamation of geographic and attribute data                                 
. New attributes by arithmetic and logical expression                           
. Building zones structure from line segments                                   
. Generation of names files                                                     
. Generation of template attribute data files                                   
. Map projections                                                               
                                                                                
Quantisation                                                                    
                                                                                
. Classification methods: equal value, quantiles, specified intervals,          
  specified number, refined, sequential colour, mean and standard deviations,   
  nested means, natural breaks, percentiles, fixed                              
. Quantisation over value ranges                                                
. Quantisation for lists of items                                               
. Independent quantisation for one or two files                                 
                                                                                
Map regions                                                                     
                                                                                
. Display of several geographic files at the same time, joined together or      
  as multiple regions                                                           
. Windowing and viewporting for layout                                          
. Coordinate grids                                                              
. Overlays of line segments, names and symbols                                  
                                                                                
Attribute selection                                                             
                                                                                
. Sequentially off attribute file                                               
. By position in file                                                           
. By description                                                                
                                                                                
Map enhancement                                                                 
                                                                                
. Specification of legend contents                                              
. Addition of text                                                              
. Addition of histograms showing distributions, sorted values or quantisation   
  results                                                                       
. Addition of scatter diagrams to bivariate maps                                
. Overlay of mean and standard deviation, median and regression curves on       
  diagrams                                                                      
                                                                                
Hardcopy Map Production                                                         
                                                                                
. HP compatible plotters                                                        
. Many dot matrix printers                                                      
. Postscript laser printers                                                     
. HPGL, CGM and word processor files                                            
                                                                                
Applications                                                                    
                                                                                


                                                                       9
. Territory assignment                                                          
. Site catchments                                                               
                                                                                
Environment                                                                     
                                                                                
. Requires minimum of IBM PC compatible with hard disk, 640K RAM and EGA.       
. Preferred hardware is AT compatible with 512K super VGA card giving 256       
  colours at at least 640 x 480 resolution. 1Mbyte boards with Trident or       
  Tseng Labs 4000 chipsets are recommended.                                     
. MS DOS operating system                                                       


                                                                      10
                    3. SYSTEM CONFIGURION                                
                       ==================
 

  3. 1 Introduction                                      
       ------------
 
Various parameter files have to be set up correctly before the system can be    
used as OzGIS supports a range of video boards. This should be quite straight   
forward for standard EGA and VGA boards, but as there are no standards for      
super VGA boards the procedure gets involved.                                   
                                                                                
The configuration is worth spending the time on as it is very important to      
display maps as fast as possible and to use the highest display resolution      
possible. If you plan to do a lot of mapping it is worth purchasing the         
hardware (its optional).                                                        
                                                                                
Resolution is provided by using Super VGA boards.                               
                                                                                
Speed is provided by:                                                           
                                                                                
    . Super VGA boards with 256 colours (512K or 1 Mbyte RAM on the board)      
    . Using an extra 1MByte of RAM as a RAM disk.                               
    . Math coprocessor                                                          
    . fast processors (386 / 486)                                               
                                                                                
The other hardware worth having is a mouse. While the arrows on the keyboard    
can be used, they are slow.                                                     
                                                                                
                                                                                
FOLLOW THE INSTRUCTIONS CAREFULLY!                                              
                                                                                

  3. 2  DOS system files                                 
       -----------------
 
The start-up command file AUTOEXEC.BAT will have to be modified so the programs 
can be accessed by changing the path statement to reference /ozgis. e.g.        
                                                                                
PATH C:\DOS;C:\PROGS;C:\OZGIS                                                   
                                                                                
                                                                                
The system file CONFIG.SYS has to have:                                         
                                                                                
FILES=20                                                                        
BUFFERS=20                                                                      
                                                                                
These changes to the DOS system files will not take effect until the system is  
re-booted.                                                                      

  3. 3  Standard EGA and VGA boards                      
       ----------------------------
 
If you have a super VGA board skip this section.                                
                                                                                
You need to be aware of the resolution of your video card. This is one of:      
                                                                                


                                                                      11
350 lines of 640 pixels for EGA                                                 
480 lines of 640 pixels for VGA                                                 
                                                                                
Both boards have 16 colours.                                                    
                                                                                
You now need to check two configuration files:                                  
                                                                                
All the following take place in the \ozgis directory.                           
                                                                                
                                                                                
The file \OZGIS\OZGIS.INI is the initialisation file for the system.            
This file has to be modified using your word-processor.                         
                                                                                
The file should be well commented, and modifications should be fairly obvious.  
Ensure that you dont alter the columns used i.e. the file is not free format!   
                                                                                
The first three lines should be either:                                         
                                                                                
for the EGA board                                                               
                                                                                
       640         Number of pixels across EGA screen                           
       350         Number of lines on screen                                    
        16         Number of colours                                            
                                                                                
                                                                                
or for the VGA board                                                            
                                                                                
       640         Number of pixels across VGA screen       (640 - 1024)        
       480         Number of lines on screen                (350 - 768)         
        16         Number of colours                        (16 or 256)         
                                                                                
                                                                                
                                                                                
The file \OZGIS\INTERACT.INI is the initialisation file for the interactor      
graphics package. This file has to be modified using your word-processor.       
                                                                                
The file should be well commented, and modifications should be fairly obvious.  
                                                                                
If a standard VGA card is being used, nothing may have to be changed.           
                                                                                
If an EGA card is being used the display type may have to be set via            
the DISPLAY= parameter.                                                         
                                                                                
                                                                                

  3. 4  Super VGA boards                                 
       -----------------
 
The recommended display is a super VGA board with the ability to display 256    
colours at a resolution of at least 640 X 480, as this enables maps of up to    
240 zones to be manipulated rapidly by changing the colours via the colour      
look-up table. Other displays require the map polygons to be redrawn every time 
the colours change (e.g. by displaying another attribute).                      
                                                                                
Hence you should use the highest resolution available with your board and       
monitor that gives 256 colours. (this may not be true if you are mapping e.g.   
environmental data without attribute data or have maps of more than 240 zones   
when resolution may be more important).                                         


                                                                      12
                                                                                
First determine the resolution and number of colours you want to use. This will 
depend on the amount of memory on your board and the chipset. If in doubt read  
your video board manual or ask your computer shoppe.                            
                                                                                
In order of preference the resolutions are:                                     
                                                                                
Pixels Lines Colours                                                            
                                                                                
1024   768   256         (1MByte boards)                                        
 800   600   256         (512K boards)                                          
 640   480   256         (512K boards with standard monitor)                    
 800   600    16         (256K board)                                           
                                                                                
If your board has only 256K of memory you should consider adding more memory,   
but in the meantime use the highest resolution possible for 16 colours          
                                                                                
The boards supported by the graphics package are:                               
                                                                                
    Chipset     Chipset   640x350   640x400   640x480   800x600  1024x768       
                Number                                                          
    Tseng 3000    0          y                   y         y                    
    Tseng 4000    1          y         y         y         y         y          
    Paradise      2                    y         y                              
    Video 7       3                    y         y         y                    
    Everex        4          y         y         y         y                    
    ATI           5                    y         y         y                    
    Trident       6                    y         y         y         y          
    Chips & Tech  7                    y         y         y                    
    Ahead B       8                    y         y         y                    
    Oak           9                              y         y                    
                                                                                
The precise combination of modes available on any given board varies            
according to the manufacturer and the amount of video RAM available.            
The 640x480 and 800x600 modes require 512k and the 1024x768 mode requires       
1 megabyte.                                                                     
                                                                                
                                                                                
You now need to modify two configuration files:                                 
                                                                                
All the following take place in the \ozgis directory.                           
                                                                                
                                                                                
The file \OZGIS\OZGIS.INI is the initialisation file for the system.            
This file has to be modified using your word-processor.                         
                                                                                
The file should be well commented, and modifications should be fairly obvious.  
                                                                                
The first three lines have to be the resolution and number of colours e.g.      
                                                                                
       800         Number of pixels across VGA screen       (640 - 1024)        
       600         Number of lines on screen                (350 - 768)         
       256         Number of colours                        (16 or 256)         
                                                                                
Ensure that you dont alter the columns used i.e. the file is not free format!   
                                                                                
                                                                                
The file \OZGIS\INTERACT.INI is the initialisation file for the interactor graph


                                                                      13
package. This file has to be modified using your word-processor.                
                                                                                
The file should be well commented, and modifications should be fairly obvious.  
                                                                                
                                                                                
The display type may have to be set via the DISPLAY= parameter.                 
                                                                                
Super VGA boards require registers to be initialised. Look through the list and 
find yours. If its not there you may have to use the system as a standard VGA   
as described in the previous section, but first look in your video board manual 
to see if there is information about the registers to be used to set modes. If  
there is you may be able to set up an appropriate mode command as described     
in the following paragraphs (try it to see if it works).                        
                                                                                
The following section gets quite complicated, but all you have to do is to      
enable a command that corresponds to your video card.                           
                                                                                
                                                                                
e.g. if you have a TSENG Labs ET4000 card you will find the following entry:    
                                                                                
REM mode13  = 56 0 0 0 1 1024 768 (1024x768 256-colour graphics)  C             
                                                                                
All you have to do is remove the "REM " from the front (dont forget the blank   
i.e. left align it).                                                            
                                                                                
You would normally also remove the comment too, so you end up with:             
                                                                                
mode13  = 56 0 0 0 1 1024 768  C                                                
                                                                                
(the "C" on the end is require with a mouse to tell the system to generate a    
cursor as mouse drivers normally do no do that with super VGAs).                
                                                                                
                                                                                
                                                                                
Try and find the corresponding entry for your board. If you are still confused  
try reading the following:                                                      
                                                                                
                                                                                
INTERACTER supports 5 non-standard screen modes numbered 9 to 13 which          
can be activated by inserting suitable 'MODEnn' keywords in the INTERACTER      
initialisation file. The INTERACT.INI file contains some examples which         
contain suitable initialisation file MODEnn entries for various combinations    
of video board and display monitor.                                             
                                                                                
                                                                                
The supported non-standard screen modes are as follows                          
                                                                                
   INTERACTER      Mode Type                                                    
   Mode Number                                                                  
   -----------     ---------                                                    
       9            640x400 'Olivetti' monochrome graphics                      
      10            132x25   16 colour text                                     
      11            800x600  16 colour 'Super VGA' graphics                     
      12            256 colour 'Super VGA' graphics                             
      13            256 colour 'Super VGA' graphics                             
                                                                                
Notes :                                                                         
(1) The dimensions of mode numbers 12 and 13 are definable as part of           


                                                                      14
    the MODEnn keyword. By default they are 640x480 and 800x600 modes.          
(2) 800x600 and 1024x768 modes will require a multisync or Super-VGA type       
    monitor. On certain boards, 132 column mode also requires such a monitor.   
    Be sure to use a suitable monitor/adapter combination.                      
(3) The precise mode numbers used by particular video board manufacturers       
    can vary. Users should check the documentation supplied with their          
    video board before including the supplied example MODEnn entries            
    in their INTERACTER initialisation file.                                    
                                                                                
Initialisation entries can be found for following:                              
                                                                                
  Ahead B chipset                                                               
  ATI VGA Wonder chipset                                                        
  Chips & Technology chipset                                                    
  Everex chipset                                                                
  Oak Technology chipset                                                        
  Olivetti M24/M28/M300, AT&T 6300, Compaq Portable                             
  Paradise chipset (inc. Compaq, Dell, HP D1180A, AST VGA's))                   
  Toshiba 3100 + Gas plasma screen                                              
  Trident chipset                                                               
  TsengLabs ET3000 chipset                                                      
  TsengLabs ET4000 chipset                                                      
  VAXmate II                                                                    
  Video 7 chipset                                                               
                                                                                
  By default, mode numbers 12 & 13 are 640x480 and 800x600 256 colour Super     
  VGA modes using the TsengLabs ET3000 chipset.                                 
  However the precise dimensions of these modes can now be specified using the  
  MODE12 and MODE13 initialisation keywords which now take up to 7 parameters : 
                                                                                
      MODE12 = ax bx cx dx chipset width height                                 
      MODE13 = ax bx cx dx chipset width height                                 
                                                                                
      ax bx cx dx = Interrupt 10h mode selection register values, as before     
                                                                                
      chipset     = VGA chipset number :                                        
                    0 = Tseng Labs ET3000 (default)  5 = ATI                    
                    1 = Tseng Labs ET4000            6 = Trident                
                    2 = Paradise                     7 = Chips & Technology     
                    3 = Video 7                      8 = Ahead B                
                    4 = Everex                       9 = Oak Technology         
                                                                                
      width       = screen mode width in pixels                                 
                    (default = 640 in mode 12 or 800 in mode 13)                
                                                                                
      height      = screen mode height in pixels                                
                    (default = 480 in mode 12 or 600 in mode 13)                
                                                                                
  Any trailing values which are omitted take the default values indicated.      
  Available modes on the supported chipsets include :                           
                                                                                
    Chipset     Chipset   640x350   640x400   640x480   800x600  1024x768       
                Number                                                          
    Tseng 3000    0          y                   y         y                    
    Tseng 4000    1          y         y         y         y         y          
    Paradise      2                    y         y                              
    Video 7       3                    y         y         y                    
    Everex        4          y         y         y         y                    


                                                                      15
    ATI           5                    y         y         y                    
    Trident       6                    y         y         y         y          
    Chips & Tech  7                    y         y         y                    
    Ahead B       8                    y         y         y                    
    Oak           9                              y         y                    
                                                                                
  The precise combination of modes available on any given board varies          
  according to the manufacturer and the amount of video RAM available.          
  The 640x480 and 800x600 modes require 512k and the 1024x768 mode requires     
  1 megabyte. Here are some examples of suitable initialisation file keywords   
                                                                                
  VGA board based on the Tseng Labs ET3000 chipset :                            
    MODE12 = 46                                                                 
    MODE13 = 48                                                                 
                                                                                
  VGA board based on the Paradise chipset :                                     
    MODE12 = 94 0 0 0 2 640 400                                                 
    MODE13 = 95 0 0 0 2 640 480                                                 
                                                                                
  VGA board based on the Video 7 chipset :                                      
    MODE12 = 28421 103 0 0 3                                                    
    MODE13 = 28421 105 0 0 3                                                    
                                                                                
  VGA board based on the Everex chipset :                                       
    MODE12 = 112 19 0 0 4 640 350                                               
    MODE13 = 112 20 0 0 4 640 400                                               
                                                                                
  The number of text columns and rows available in modes 12 and 13 varies       
  according to the pixel dimensions :                                           
                                                                                
    Columns = mode_width/8                                                      
    Rows    = mode_height/14 (if mode_height < 480)                             
           or mode_height/16 (if mode_height >=480)                             
                                                                                
  This gives the following text dimensions :                                    
                                                                                
     640x350 mode :  80 columns x 25 rows                                       
     640x400 mode :  80 columns x 28 rows                                       
     640x480 mode :  80 columns x 30 rows                                       
     800x600 mode : 100 columns x 37 rows                                       
    1024x768 mode : 128 columns x 48 rows                                       
                                                                                
- Since most Microsoft compatible mouse drivers do not support a mouse          
  cursor in non-standard PC graphics modes, an option has been added to         
  the MODEnn initialisation file keyword which tells INTERACTER to display      
  it's own cross-hair cursor in such modes. Simply place a single letter        
  'C' (upper or lower case) at the very end of the record containing the        
  MODEnn keyword to cause INTERACTER to provide a mouse cursor in that mode.    
                                                                                
      MODE9  = 64 C                                                             
      MODE11 = 88 C                                                             
      MODE12 = 94 0 0 0 2 640 400 c                                             
      MODE13 = 95 0 0 0 2 640 480 c                                             
                                                                                
                                                                                
EXAMPLE................                                                         
                                                                                
                                                                                


                                                                      16
Here is the configuration file for a 1Mbyte Trident board (1024 x 768 x 256)    
using a mouse and saving screens on disk.                                       
                                                                                
                                                                                
DISPLAY    = 10                                                                 
CHARSET    = c:\ozgis\standard.chr                                              
COLUMNS    = 80                                                                 
TEMPMENU   = \ozgis\menu.tmp                                                    
TEMPWINDOW = \ozgis\window.tmp                                                  
mode13  = 98 0 0 0 6 1024 768 C                                                 
                                                                                
                                                                                
The system is now configured for OzGIS with super VGA board.                    
If you are going to produce maps on printers and plotters you will have         
to configure for OzMAP as described in the following section.                   

  3. 5 Maths Coprocessor                                 
       -----------------
 
If you have a maths coprocessor you can use a different version of the main     
OZGIS program.                                                                  
                                                                                
You need to modify the batch files \ozgis\ozgis.bat and \ozgis\ozcensus.bat to  
use the program ozgisco instead of ozgisprg.                                    

  3. 6 Extra RAM                                         
       ---------
 
If you have more than 1 Mbyte of RAM you can speed up display of menus and      
other windows enormously by using a RAM disk.                                   
                                                                                
You put a command in your config.sys file like:                                 
                                                                                
DEVICE=C:\DOS\RAMDRIVE.SYS 1024 /E                                              
                                                                                
This then gives you a pseudo disk drive in RAM, so its very fast. The drive     
identifier is one more than you are using e.g. if you have one disk drive       
called C: then the RAM disk drive will be D:                                    
                                                                                
After you have put in the command, reboot you PC and type "DIR D:" to check     
that you got it right (see your DOS manual).                                    
                                                                                
Now modify the \ozgis\interact.ini file to define the two save files to be on   
the RAM drive. The entries should look something like:                          
                                                                                
TEMPMENU   = D:\menu.tmp                                                        
TEMPWINDOW = D:\window.tmp                                                      
                                                                                

  3. 7 Hardcopy configuration                            
       ----------------------
 
You may wish to leave this section until you want to output maps to printers or 
plotters.                                                                       
                                                                                
The configuration file \ozgis\sciplot.ini has to be set up if OzMap is going to 
be used to produce hardcopy maps. The file looks like:                          
                                                                                


                                                                      17
VGA                                  VGA or EGA                                 
40.0      0                          HP Plotter metafile                        
18.0      1                          Dot-matrix printer metafile                
18.0      1                          Postscript Ascii metafile                  
18.0      1                          Encapsulated Postscript file               
18.0      0                          HPGL file                                  
18.0      1                          CGM file                                   
18.0      0                          WordPerfect graphics file                  
18.0      1 COM1                     On-line Apple Laser Writer                 
40.0      0 LPT1                     On-line HP plotter                         
00C3                                 device mode & serial modes HEXIDECIMAL     
                                                                                
The first column is the width of the drawing surface in cm. Values will need to 
be set for your plotter or printer.                                             
                                                                                
The second column is the drawing line width for Postscript, Encapsulated        
Postscript, Apple LaserWriter, Computer Graphics Metafile, dot matrix, and HP   
LaserJet printers.                                                              
0  = Ignore parameter                                                           
1  = 1 device space units (1-10 Valid)                                          
                                                                                
The third column is the port used for printers and plotters:                    
'COM' - Primary Serial Port                                                     
'COM2'- Secondary Serial Port                                                   
'LPT1'- Primary Parallel Port                                                   
'LPT2'- Secondary Parallel Port                                                 
                                                                                
The value at the bottom is a hexidecimal set of flags for setting the port for  
on-line printers or plotters.                                                   
                                                                                
The packed coded device mode word with the device mode byte in the most         
significant part of the integer, and the serial modest byte in the least        
significant part of the integer.                                                
                                                                                
Format of the integer = [device mode | serial modeset].                         
                                                                                
Device mode byte description:  [bits]                                           
76543210                                                                        
_______0  = XON/XOFF flow control                                               
_______1  = Hardware flow control on DSR line                                   
______0_  = Bell with FRAME or PLTEND                                           
______1_  = No bell with FRAME or PLTEND                                        
_____0__  = Cr with FRAME or PLTEND                                             
_____1__  = No cr with FRAME or PLTEND                                          
____0___  = Check for break in PLOT                                             
____1___  = No check for break in PLOT                                          
___0____  = HP pen plotter handshake init                                       
___1____  = No HP pen plotter handshake init                                    
                                                                                
Serial modeset byte description:  [bits]                                        
7      6   5  4    3        2        1    0                                     
--Baud Rate-- -Parity-  -Stop Bits- -Char Length-                               
000 -   110  00 - None  0  - 1   10  - 7 Bits                                   
001 -   300  01 - Odd   1  - 2   11  - 8 Bits                                   
010 -   600  11 - Even                                                          
011 -  1200                                                                     
100 -  2400                                                                     
101 -  4800                                                                     


                                                                      18
110 -  9600                                                                     
111 - 19200                                                                     
                                                                                
For example, 9600 baud, no parity, 1 stop bit, 8 bits is                        
                                                                                
110 00 0 11 = C3 hex = 195 decimal                                              
                                                                                

  3. 8 Plotter setup                                     
       -------------
 
                                                                                
Plotter pens should agree with those defined in device files. The standard      
order is:                                                                       
BLACK        PEN 1                                                              
BLUE         PEN 2                                                              
GREEN        PEN 3                                                              
RED          PEN 4                                                              
YELLOW       PEN 5  The last four dont matter that much!                        
MAGENTA      PEN 6                                                              
CYAN         PEN 7                                                              
GREY         PEN 8                                                              
                                                                                
If this order conflicts with other packages in use the device files can be      
modified. The order of the first four pens is particularly important for colour 
simulation, although as long as all pens have different colours the final maps  
will probably be acceptable.                                                    
                                                                                
                                                                                
Plotters will usually use software handshaking.                                 
                                                                                
HP pen plotters require a serial interface between the  Personal Computer and   
the HP pen plotter. On the PC side, a cable with a D9 or D25 connector should be
connected to a  serial port or asynchronous adapter port. On the HP pen plotter,
a cable with a D25 connector should be connected to the computer/modem port. A  
detailed specification of the way the  cable should be wired follows:           
                                                                                
Serial cable wiring for HP pen plotters: 7440A, 7470A, 7475A, 7550A             
                                                                                
 ----------------------------             -----------------------               
| Personal Computer          |           | HP Pen Plotter        |              
| [Serial I/O Port or        |           | [Computer/modem port] |              
| Asynchronous Adapter Port] |           |                       |              
 ----------------------------              ----------------------               
                                                                                
      Transmit Data     *-------------------*   Receive Data                    
       [D9/Pin-3, or                             [D25/Pin-3]                    
        D25/Pin-2]                                                              
                                                                                
      Receive Data      *-------------------*   Transmit Data                   
       [D9/Pin-2, or                             [D25/Pin-2]                    
        D25/Pin-3]                                                              
                                                                                
      Signal Ground     *-------------------*   Signal Ground                   
       [D9/Pin-5, or                             [D25/Pin-7]                    
        D25/Pin-7]                                                              
                                                                                
      Data Set Ready    *-----*-------------*   Data Terminal Ready             


                                                                      19
       [D9/Pin-6, or          |                  [D25/Pin-20]                   
        D25/Pin-6]            |                                                 
                              |                                                 
      Clear-To-Send     *-----*                                                 
       [D9/Pin-8, or                                                            
        D25/Pin-5]                                                              
                                                                                
      Data Terminal Rdy *--------------*-----*  Data Set Ready                  
       [D9/Pin-4, or                   |         [D25/Pin-6]                    
        D25/Pin-20]                    |                                        
                                       |                                        
                                       *-----*  Clear-To-Send                   
                                                 [D25/Pin-5]                    
                                                                                
Please note that the previous wiring diagram is necessary if full hardware      
handshake is desired. If the user intends to  use only software handshake       
(XON/XOFF), then only three wires  are required. For software handshake the only
connections  required are: signal ground, receive data, and transmit data.      
                                                                                
     There are certain restrictions when an HP pen plotter is used as the plot  
device. Not all HP pen plotters possess equal capability! SciPlot only supports 
the 7470A, the 7475A, and the 7550A HP Pen Plotter. There are enough control    
mechanisms in SciPlot to allow the use of others though.  Please note the       
following:                                                                      
                                                                                
 The "INIT=ON" command in the VECTOR.CFG file will send initialization commands 
in the I/O stream to the  plotter when VECTOR is executed. Older HP plotters    
will  produce errors on receipt of these handshake mode commands.  If this      
happens, set "INIT=OFF" in the VECTOR.CFG file, and the offending commands will 
be deleted from the stream.                                                     

  3. 9 Mouse                                             
       -----
 
If you have a mouse it must be installed in the standard way.                   
                                                                                
The driver must be call MOUSE.COM (for the system to detect it).                
                                                                                
Mouse drivers usually only work with standard VGA and EGA. If you are operating 
in super VGA modes you would have to set the mode command in                    
\ozgis\interact.ini with a "C" on the END (as already described) for the cursor 
to appear.                                                                      


                                                                      20
                    4. BASIC CHOROPLETH MAPPING EXAMPLE                  
                       ================================
 

  4. 1 OzCensus                                          
       --------
 
The main display and analysis program is OzGIS.                                 
                                                                                
A much simpler version of OzGIS is provided called OzCensus.                    
                                                                                
This version is suitable for simple mapping of Census type data and is          
recommended for use while learning to use the system.                           
                                                                                
OzCensus has two or three menus and about twenty menu options while the full    
OzGIS version has about fifty menus and a few hundred menu options.             
                                                                                
When you want to do more advanced mapping use OzGIS!                            

  4. 2 Example map                                       
       -----------
 
The most common application is the display of data such as Census data as       
coloured polygons. Here the processes necessary to display such data are        
described.                                                                      
                                                                                
You should print out the template for the function keys \ozgis\fnkeys.doc       
                                                                                
You will probably have a file of attribute data (such as population Census      
data) and a file of digitised boundary data for mapping:                        
We will look at data for Far East Asia. There are two data files:               
                                                                                
FEA-G.DAT are the digitised boundary data, and                                  
FEA-A.DAT are the attribute data                                                
                                                                                
First of all we have to enter the data so it is checked and written into        
internal files:                                                                 
                                                                                
type                                                                            
                                                                                
cd \ozdemo                                                                      
ozenter                                                                         
                                                                                
1. select the option to enter standard format geographic files                  
give the input data file as fea-g                                               
give the output geographic file as fea                                          
                                                                                
2. select the option to enter an attribute file                                 
give the input data file as fea-a                                               
give the output attribute file as fea                                           
                                                                                
3. type F10 to exit                                                             
                                                                                
Now the files can be displayed                                                  
                                                                                
type                                                                            
                                                                                


                                                                      21
ozcensus                                                                        
                                                                                
                                                                                
choose the option to "DISPLAY A NEW MAP".                                       
                                                                                
give the attribute file name as FEA (from above)                                
                                                                                
When asked for the geographic file name input "L". A list of the available files
will appear (type Enter or Esc to exit). Give the geographic file name as FEA   
                                                                                
The data are now processed, the map is displayed, and the next menu appears.    
                                                                                
You now have a default map with legend and distribution diagram. The legend     
has the numbers of zones in each class on the left and the class value ranges   
to the right of the coloured boxes.                                             
                                                                                
Now investigate some of the options:                                            
                                                                                
Choose the option to display the next sequential attribute                      
                                                                                
If you only have 16 colours the system does not display the map until you       
request regeneration. This enables several options to be changed before the     
slow polygon drawing takes place.                                               
                                                                                
If the map does not change type F3 to regenerate the map.                       
                                                                                
                                                                                
Select the option to select by number. Type 0 to get a list.                    
Type Esc to return to the question. Type in a number to select an attribute.    
(type F3 to regenerate if necessary)                                            
                                                                                
                                                                                
Now investigate some of the function keys:                                      
                                                                                
You can print the file FNKEYS.DOC for a template.                               
                                                                                
Type F1 to get a help message. Esc is usually used to return.                   
                                                                                
F2 hides the menu; type Esc to redisplay it.                                    
                                                                                
F3 regenerates the map when required (followed by Enter to display a menu).     
                                                                                
F4 enables files to be audited and maintained. Type F4 and select the option to 
interrogate files. Select geographic files and use the file name FEA (the one   
displayed). Type Esc three times to return to main menu (Esc is used to return  
to the previous menu).                                                          
                                                                                
F6 enables the user interaction to be controlled; try turning on partial trace  
(level 1) which causes a series of messages to appear at the bottom of the      
screen telling you what the system is doing, but not as many as level 2.        
                                                                                
F8 causes a jump back to the previous main menu. This enables skipping back     
several levels. You will find that at main menus this is the only way to exit.  
(Irrelevant with the tiny number of menus in OzCensus).                         
                                                                                
F10 is used to exit from the program. Dont use it yet!                          
                                                                                
Select the option to change the number of classes.                              


                                                                      22
                                                                                
change the number of classes to 10.                                             
(type F3 to regenerate if necessary)                                            
                                                                                
Select the option to change the quantisation method. Another menu will appear.  
These options are very important as they enable the map to show the data in a   
way relevant to the purpose of the analysis.                                    
                                                                                
Choose QUANTILES and set the number of classes to 10 (deciles).                 
                                                                                
Type Esc to go back to the previous menu.                                       
                                                                                
Choose the option to display statistics. Type return (or Esc) to remove the     
window.                                                                         
                                                                                
Choose the option to interrogate the map. This will enable the current values   
for the displayed zones to be listed. A cursor will appear on the screen which  
indicates the bottom left position. Place it using either the arrows (type      
Enter to select the position) or the mouse (left button to select). A box       
cursor then appears to select the other corner. All zones are listed where the  
minimum bounding rectangle (MBR) intersects the selected window.                
                                                                                
                                                                                
etc                                                                             
                                                                                
Continue investigating options                                                  
                                                                                
Type F10 to exit.                                                               


                                                                      23
                    5. INTERACTIVE USER INTERFACE TO OzGIS               
                       ===================================
 
      The user controls OzGIS by responding to menus, questions and             
commands presented on the alphanumeric terminal.                                
                                                                                
      This section describes these forms of user communication.                 

  5. 1 Menus                                             
       -----
 

  5. 1. 1 Menu format                                       
          -----------
 
      Menus are presented in the format below.  The MENU HEADER                 
contains the previous menu item selected, or in the case of a main menu         
the system title.                                                               
                                                                                
               [MENU HEADER]                                                    
                1:  [menu item 1]                                               
                2:  [menu item 2]                                               
                         :                                                      
                         :                                                      
                         :                                                      
                n:  [menu item n]                                               
                                                                                
Menu items are numbered sequentially from one.  A selection is made by typing in
the character next to the item. Alternatively the arrows can be used to move up 
or down and Enter typed to select.                                              
                                                                                

  5. 1. 2 Function keys                                     
          -------------
 
      User assistance is provided at every menu by typing function keys:        
                                                                                
      (print out fnkeys.doc for a template)                                     
                                                                                
                                                                                
      F1    presents "help" or informative messages about the menu items        
            and describes the effect of selection of the items                  
                                                                                
      F2    enables the menu to be removed so it does not obscure the display.  
            Esc will display it again.                                          
                                                                                
      F3    regenerates the map after parameters have changed. Enter must be    
            typed to display the next menu.                                     
                                                                                
      F4    permits interrogation and maintenance of OzGIS files.               
            A menu is presented with the following options:                     
                                                                                
               -  delete a file                                                 
               -  interrogate the header of a file                              
               -  generate a list of files.                                     
                                                                                
      F6    permits the extent of user communication to be controlled.          


                                                                      24
            A menu with the following options is presented:                     
                                                                                
               -  turn user assistance messages on/off                          
               -  turn trace messages from tasks on/off                         
               -  turn the bell to signal cursor operation on/off               
               -  turn on debug (useful for reporting errors)                   
                                                                                
            The default of the option for user assistance messages is "on"      
            (i.e., that the messages are displayed).                            
            The default of the option for trace messages depends on the module. 
            (it is useful for data entry and preparation)                       
            The debug option is for system testing, but may be useful to trace  
            faulty data problems. Output goes to the print file OZGIS.OUT       
                                                                                
      F8    exits from the current menu to the last major menu, which           
            depends on the stage of processing.                                 
                                                                                
      F10   quit the OzGIS session.                                             
                                                                                
Pressing the "Esc" key before entering any other character has one of           
two effects:                                                                    
                                                                                
      -  return to the previous menu                                            
or    -  repeat of the current menu ("F8" should be typed to return to the      
previous main menu)                                                             
The option taken depends upon the stage of processing.                          

  5. 1. 3 Stacking selections                               
          -------------------
 
Menus take quite a time to display as the underlying graphics has to be stored  
first. A series of selections can be made when the sequence of menu options is  
known, and the menus will not appear.                                           

  5. 2 Questions                                         
       ---------
 
      Questions are asked by OzGIS when data are required for an                
operation.  The user must supply the data by entering appropriate responses     
on the keyboard.                                                                
                                                                                
      The format of questions consists of the question, a possible range of     
values in brackets (if appropriate), a default value in parentheses (if         
appropriate) and terminated by a question mark.  The range of values and        
default values indicate the form of the expected answer.  An example is:        
                                                                                
      -  request to replace an existing file:                                   
         DO YOU WANT TO REPLACE THE FILE [Y,N]?                                 
                                                                                
                                                                                
         The user must respond by typing either "Y" (for "YES") or "N"          
         (for "NO").                                                            
                                                                                
      The following single character responses provide assistance when          
answering questions:                                                            
                                                                                
      "H":  presents a "help" or informative message about the required         
            response.                                                           


                                                                      25
                                                                                
      "E":  returns to the previous menu without further action.                
                                                                                
                                                                                
      Errors in responses are trapped and result in help messages being         
printed.  The user is asked the question again.                                 

  5. 3 Commands                                          
       --------
 
      Commands are issued by OzGIS when an operation has to be                  
performed by the user.  When the operation is completed, control returns to     
the appropriate menu.                                                           
                                                                                
      The format for commands consists of a directive, a possible range of      
values in brackets (if appropriate), a default value in the input field (if     
appropriate), terminated by a colon.  Examples are:                             
                                                                                
      -  to provide the number of classes:                                      
         TYPE NUMBER OF CLASSES [1-6] (4):                                      
                                                                                
         The number of classes must be in the range 1 to 6, and if              
         the user simply presses the "Enter" key a default value of 4 will      
         be selected.                                                           
                                                                                
      -  request for the name of a file:                                        
         TYPE FILENAME (TEST):                                                  
                                                                                
         The filename must be entered as a character string, or the             
         "Enter" key pressed to accept the default filename "TEST".             
                                                                                
      The following single character responses provide assistance when          
responding to commands:                                                         
                                                                                
      "L":  provides a list of data items that can be selected.                 
                                                                                
            e.g. for FILENAME, a list of available files will be printed.       
            e.g. for ATTRIBUTE DESCRIPTION, the names of attributes on the file 
            will be listed.                                                     
                                                                                
      "H":  presents a help or informative message about the desired            
            operation.                                                          
                                                                                
                                                                                
      "E":  returns to the previous menu without further action.                
                                                                                
Errors in responses are trapped and cause a help message to be printed and      
the command to be repeated.                                                     

  5. 4 Graphic interaction                               
       -------------------
 
      Graphic interaction in OzGIS involves the use of the mouse and/or         
arrow keys to control the cursors on the monitor.                               
Use the left mouse button or type Enter to select the position.                 
                                                                                
      The user is directed to operate the mouse etc by the appearance of the    
cursor on the monitor and by an appropriate command on the screen.  The         


                                                                      26
extent of the command depends on the current level of user communication        
(see F6  option)                                                                
                                                                                
There are two types of cursors:                                                 
                                                                                
1. a pointer to select a position of object                                     
2. a box to select a region. The bottom left corner is selected and then the    
   other.                                                                       

  5. 5 Pop-up                                            
       ------
 
The menus and windows operate in "pop-up" mode. This requires that the screen   
under the menu etc has to be saved to file before the menu appears so it can be 
restored. This is slow. Display speed can be increased by specifying the save   
files to be on RAM disk (if you have extended memory) by modifying the file     
name in the \ozgis\interact.ini file.                                           

  5. 6  Print file                                       
       -----------
 
Every program generates printout on a file OZGIS.OUT.                           
                                                                                
This includes:                                                                  
                                                                                
Reports                                                                         
Error messages                                                                  
Debug output                                                                    


                                                                      27
                    6. OzGIS FILES                                       
                       ===========
 
      This Chapter describes the various files which are processed by           
OzGIS.  Some of the files can be entered into OzGIS as data, and                
the external formats for these files are given later.  All of the               
files have internal formats, which are generated as part of the user            
interaction.                                                                    
                                                                                
Data files usually come from Census bureaux, map data suppliers or your         
corporate database.                                                             
                                                                                
The file types will become obvious with use of the system.                      
                                                                                
      External data files must be entered into OzGIS explicitly.  This          
operation permits OzGIS to generate internal representations of the             
data for efficient processing and to check the data.                            
                                                                                
      The following kinds of files must be entered into OzGIS:                  
                                                                                
      -  marker files                                                           
      -  device files                                                           
      -  presentation files                                                     
                                                                                
      Certain files must be prepared explicitly within OzGIS under user         
direction.  These files are:                                                    
                                                                                
      -  saved display files                                                    
      -  catchment files (OzCatch)                                              
      -  time lapse files  (no longer available)                                
      -  palette files (no longer available)                                    
      -  hardcopy files  (no longer available)                                  
                                                                                
      Some files can be prepared externally or internally.  These are:          
                                                                                
      -  geographic files                                                       
      -  name files                                                             
      -  combine files                                                          
      -  colour names file  (no longer available)                               
                                                                                
      OzGIS distinguishes the various types of files, so that users can         
interrogate the current set of files of a specified type.                       
                                                                                
(a)  Geographic Map files describe geographic (map) data in terms of            
     graphic elements - zones, polygons, line networks, line segments and       
     points.  The data can be drawn in geographic regions, or overlayed on      
     displayed maps.                                                            
                                                                                
     The files are generated by digitising base maps.  This is a                
     time-consuming soul-destroying task.  Fortunately digitised map data       
     are available for many commonly used maps e.g. states, postcodes,          
     Census districts.  Where special zones are required, they can often be     
     defined in terms of Census districts and the map boundaries obtained       
     by amalgamating the digitised Census boundary data (dropping internal      
     lines).  This has the additional advantage that Census data can also       
     be extracted for the amalgamated zones and used for comparisons with       
     the user's own attribute data.                                             


                                                                      28
                                                                                
(b)  Attribute files contain the values of attributes (variates,                
     statistics, variables) referenced to zone, line or site names.  Each       
     file may contain a number of attributes for a fixed set of names.          
                                                                                
     Attribute files are processed to assign a class number to zones            
     (colour) or lines (line type) or sites (symbol sizes) in a displayed       
     map.                                                                       
                                                                                
     Attribute data files are usually generated via a standard database or      
     modelling system or by a user's own programs.                              
                                                                                
(c)  Names files contain a list of zones, lines or sites that defines a         
     geographic region of interest.  The files may be used to subset            
     geographic data.  It may also be used to restrict the set of               
     attributes to be quantised for a map, or alternatively the set of          
     zones lines or sites to be displayed on a map.                             
                                                                                
(d)  Combine files - define new items in terms of zones.  A file may define     
     new zones in terms of amalgamated base map zones or the influence of       
     surrounding zones on a site.                                               
                                                                                
     The file contains a list of names of the new zones or sites defined.       
                                                                                
     For each new item there is a list of the base map zones it is defined      
     by and a list of weights.                                                  
     New zones are defined by complete base map zones so the weights have       
     value 1.0 e.g. Sales Territories. Site Catchments are used to retrieve     
     data from underlying map zones so the weights give the proportions of      
     the zones (range 0-1).                                                     
                                                                                
(e)  Marker files - define simple shapes as single polygons for display as      
     markers.                                                                   
                                                                                
     The data are simply the (X,Y) points that are used to draw the             
     polygons.  The points are in the range -0.5 to +0.5 so the polygon can     
     be easily scaled and displayed centred at a location.                      
                                                                                
(f)  Saved Display files contain the data to regenerate a complete display.     
     These files should be stored by the user upon completion of a display      
     for later recall.  Subsequent manipulation of the display is possible      
     after recall.                                                              
     There are two modes. The screen is usually saved so the map can be rapidly 
     displayed, but this is not relevant for later regeneration on plotters     
     etc.                                                                       
                                                                                
     Saved display files are the common level of storage and retrieval of       
     maps.  A user may build up a set of commonly displayed maps with all       
     the desired features that can be displayed and modified rapidly.           
     Saved display files are also used for presentations.                       
                                                                                
(g)  Presentation files contain references to a number of Saved Display         
     files.  The files are used to present a set of displays quickly,           
     usually for demonstration purposes.                                        
                                                                                
(h)  Time Lapse files contain a set of attributes for display as a time         
     lapse sequence.  All attributes are quantized in the same way by           
     OzGIS and must exist on the same file. e.g. data that has been             


                                                                      29
     collected regularly, say weekly, can be displayed as a 'movie' to see      
     if there are any time-based spatial features.                              
     The format of the files is internal to OzGIS.  These facilities            
     are only available for 256 colour display systems.                         
      (no longer available)                                                     
                                                                                
(i)  Device files - define the graphic devices and their capabilities.          
     Each device is a GKS workstation.  Several files may exist for each        
     device giving different values for the graphic primitive attributes        
     (line type, text, colours, patterns etc.).  In particular, each file       
     contains sets of fill colours or patterns for single and bivariate         
     maps.                                                                      
                                                                                
                                                                                
(j)  Palette files contain a set of colours which can be selected for           
     display.  The set of colours is displayed as a palette during the          
     colour selection process.  Colour palette files can be modified and        
     generated by user interaction, but their format is internal to             
     OzGIS.                                                                     
     (no longer available)                                                      
                                                                                
(k)  Colour Names files contain a set of colour names and associated blue,      
     green and red (B,G,R) values for the display system.  The files enable     
     users to specify colours by typing a name (e.g. LIGHT RED) on the          
     keyboard.  Colour names files can be entered as external data files or     
     can be prepared by entering names and indicating the corresponding         
     colours.                                                                   
     (no longer available)                                                      
                                                                                
(l)  Hardcopy files - contain information to enable maps to be reproduced       
     off-line on other devices (with the vector program)                        
     (no longer available)                                                      
                                                                                
(m)  Catchment files - contain definitions of sites, boundaries of              
     catchments around sites, and catchment weights.  Catchment files are       
     interactively generated with reference to a base map.                      
     (not implemented yet)                                                      


                                                                      30
                    7. DEVICE FILES                                      
                       ============
 
Device files control the appearance of maps:                                    
                                                                                
     . polygon colours and type of fill                                         
     . text colours, sizes and fonts                                            
     . line colours and styles                                                  
     . sequences of class colours or hatch patterns                             
     . menu and message colours                                                 
                                                                                
Experience showed that it is better to have fixed sets of definitions rather    
than allow the user to specify the display parameters.                          
                                                                                
Remember that the basic display definition (number of pixels, lines and colours)
was specified when configuring the system.                                      
                                                                                
The best way to understand device files is to look at the contents:             
                                                                                
First of all type:                                                              
                                                                                
cd \ozgis                                                                       
ozgis                                                                           
                                                                                
Select the option to CHANGE DEVICE FILE                                         
                                                                                
Give the file as *C16SV1                                                        
                                                                                
Select the option to DISPLAY DEVICE CHARACTERISTICS                             
                                                                                
You will now get a display that shows the text types (sizes and colours),       
line (types and colours) and the various polygon fills as rectangles.           
                                                                                
Of particular interest are the class colours. The bottom set is a sequence of   
121 colours which is designed to give the appearance of increasing attribute    
values. In this device file for a 16 colour board the colours are in blocks,    
but for 256 colour boards all the colours will be different (and can be used    
for "continuous colour" maps). The set of colours above are a 7 x 7 set for     
bivariate maps. They actually map onto the same set as for single variate maps, 
so if bivariate maps are to be produced different device files should be used.  
                                                                                
Now choose a bivarite device file *C16BV1 and display that. The bivariate       
sequence will show a progression of colour in each dimension.                   
                                                                                
There is a set of files for 16 colour displays, *C16SV1 to *C16SV9 for single   
variate maps, and *C16BV1 to *C16BV3 for bivariate maps.                        
                                                                                
                                                                                
There is also a set of files *C256SV1 to *C256SV9 and *C256BV1 to *C256BV3 for  
256 colour boards. If you have a suitable board display one of these. The       
colour sequence will now be complete.                                           
                                                                                
                                                                                
Other device files are also available, primarily for display on printers and    
plotters, but these can also be used on the display; try them!                  
                                                                                
*HATCHSV1 is for display of hatched single variate maps and *HATCHBV1 for       


                                                                      31
bivariate maps.                                                                 
                                                                                
You should now display a few of the single variate decvice files (*C16sv? or    
*C256SV?) and decide on one that you will use as the default file.              
                                                                                
When you have decided on the default file type F10 to exit from OzGIS and:      
                                                                                
cd \ozgis                                                                       
copy C256SV6.DEV DEFAULT.DEV  (using the file you have chosen)                  


                                                                      32
                    8. OzGIS MAP TYPES                                   
                       ===============
 
Several types of maps and diagrams can be displayed.                            
                                                                                

  8. 1 Attribute maps                                    
       --------------
 
     There are one or two streams of attribute processing for the types of      
maps available for zone, line and site attribute data:                          
                                                                                
     -  zones map                                                               
     -  lines map                                                               
     -  sites map                                                               
     -  two zone streams i.e. bivariate maps                                    
     -  zones and lines                                                         
     -  zones and sites                                                         
                                                                                
     The type of map is selected before display and cannot be changed.          
                                                                                
Basic choropleth maps have already been demonstrated. Here are some more        
examples... Remember you can type "L" to get a list of files when asked for a   
file name.                                                                      

  8. 1. 1 Bivariate zones map Example                       
          ---------------------------
 
Select the bivariate zones option.                                              
                                                                                
Use attribute files LOWE1 and LOWE2 and geographic file LOWE.                   
                                                                                
Remember that you may have to type F3 to display the map.                       
                                                                                
 Note the form of the legend; the primary attribute (first file, top            
description) is the vertical part of the legend.                                
                                                                                
Type F8 to return to the main menu.                                             

  8. 1. 2 Zones & sites Example                             
          ---------------------
 
Now select zones & sites option.                                                
                                                                                
Use the LOWE1 and LOWE2 attribute files again, and the LOWE zones geographic    
file.                                                                           
                                                                                
Give the sites geographic file as LOWE-S1.                                      
                                                                                
Next choose the option to change quantised data and then the option to display  
more quantised sites. Give the next sites geographic files as LOWE-S2. Use      
symbol number 2 (number one is already used).                                   
                                                                                
You will have a coloured zones map with different sized symbols. This type of   
map is for applications such as deciding where to put shopping centres, where   
different symbols can be used for e.g. existing centres, centres owned by       
different retail chains and proposed new centres.                               


                                                                      33

  8. 1. 3 Geographic (GIS) maps Example                     
          -----------------------------
 
Maps can be displayed that show geographic data without attribute data i.e.     
polygons, lines, names at points and symbols at points.                         
                                                                                
Where the data are preclassified feature codes can be used to subset the files  
for display.                                                                    
                                                                                
For example, display some of the Hawaii DLG files. These files came from the    
USGS, and after some cleaning up, were entered as DLG-3 data and the polygons   
formed using OzZone.                                                            
                                                                                
Select the option to display geographic maps.                                   
                                                                                
Select the option to display polygons and use file HAWDLGWB, which is the       
outlines of the islands. Use any polygon number, give some text for the legend  
(e.g. "Islands") and use the no boundaries default.                             
                                                                                
Type F3 to regenerate if necessary.                                             
                                                                                
Select the option to display polygons for feature codes.                        
Use file HAWDLGAB  which is administrative boundaries. The file has feature     
codes in the range 900103 to 900108. Give the range as 900103 to 900103 and use 
polygon number say 4.  Repeat for another feature code range and polygon        
number.                                                                         
                                                                                
The administrative boundaries go outside the island coastlines so you may want  
to redraw the island outlines by overlaying line segments for file HAWDLGWB.    
                                                                                
Select the option to overlay line segments for feature codes.                   
Use file HAWDLGRD which is roads.  The file has feature codes in the range      
2905001 to 2905041.  Select a subset e.g. 2905000 to 2905020.                   
Give the legend text as "roads".                                                
                                                                                
Select the option to overlay line segments.                                     
Use file HAWDLGST which is streams. Give the legend text as streams.            
                                                                                
Select the option to display names at sites. Give the file HAWDLGWB.  The       
polygon names will be displayed (the area numbers from the DLG file). Usually a 
points file would be used that has the actual names.                            
                                                                                
If necessary, type F3 to regenerate the map.                                    
                                                                                
Select the option to add text, type in a title e.g. "HAWAII", and position it at
the top of the map.                                                             
                                                                                
Note that if you regenerate the map the polygons are drawn first, and then line 
segments, symbols and finally names.  Within each type they are displayed in    
the order specified.  If a mistake is made overlays can be removed.             
                                                                                
                                                                                
If polygons overlap, "polygon overlay" operations can be simulated by           
displaying using hatching. e.g. select the hatch device file *HATCHSV1 from     
the main menu and then display polygons from the two files HAWDLGWB (the        
islands) and HAWDLGAB (administrative boundaries).                              


                                                                      34
                                                                                
Type F8 to return to the top level menu                                         
                                                                                
Be aware that you can type several menu selections without waiting for the      
menus to appear.                                                                

  8. 1. 4 Diagrams Example                                  
          ----------------
 
Distributions, sorted values and quantisation results can be displayed as full  
screen diagrams for one or two attribute files. Scatter diagrams can be         
displayed for two files.                                                        
                                                                                
Choose the display attribute file option and then the distribution for two      
attribute files. Use LOWE1 and LOWE2 files. Next choose "change display         
features", followed by "add statistics" and "display mean & std. deviation".    
                                                                                
You can change attributes and quantisation in the usual ways (and type F3 to    
show the results).                                                              

  8. 2 Device files                                      
       ------------
 
Device files are a critical part of the system as they define how maps are to   
appear. Experience showed that it is better to have standard sets of colours,   
line types, fonts, text sizes etc than to try and interactively select them.    
                                                                                
Select the option to display device characteristics. This option is used when   
defining your own device files. A major feature is the colour sequences. The    
full colour sequences, available in the CSVGAS.. files have 121 colours         
available, while other files have a subset of 10 colours. The full sequence is  
designed to give a progression of colours to show the range of attribute        
values. The full set is used for continuous colour maps. 121 are used as it can 
be exactly sampled for most numbers of classes (120 is divided by 2,3,4,5,6,8   
and 10). similarly there is a bivariate sequence for bivariate maps. This is 49 
colours (7x7), (as 6 is divided by 2 and 3). You should not change hardware     
text sizes as they are fixed by the VGA/ EGA capabilities, but any size can be  
used for software fonts. Any colours can be changed. You can also set up your   
own markers.                                                                    
                                                                                
To design your own device files you usually modify a standard one.              
                                                                                
Note that bivariate device files should be used for bivariate maps.             
                                                                                
Now choose the option to change the device file and display several others. You 
can choose the one you like best and go back to the entry phase and make it the 
default device file (or copy the .DEV file).                                    
                                                                                
Device files are usually held as system files (in \ozgis) so the file names     
must be given with a '*' at the front.                                          

  8. 3 Presentations                                     
       -------------
 
This option enables a set of saved display files to be defined for              
demonstrations.                                                                 
                                                                                
An Ascii file is set up that gives the names of the saved display files and     


                                                                      35
menu lines that are associated with them.                                       

  8. 4 Time Lapse Display (not available)                
       ----------------------------------
 
Special options are available for the display of time lapse files.  The         
following parameters can be altered:                                            
                                                                                
      -  The time interval between successive attributes (given in units of     
         approximately seconds)                                                 
                                                                                
      -  The time interval between the end and beginning attributes of a        
         sequence (given in units of seconds); i.e. the pause between a         
         repeated sequence.                                                     
                                                                                
      -  The beginning and end attribute of the sequence being displayed.       
                                                                                
The zone legend format is not updated during a time lapse sequence, and by      
default the class description of the legend is set to the "HIGH" and "LOW"      
format.  Histograms and scatter plots cannot be displayed during a time lapse   
presentation.                                                                   
tribute values.                                                                 


                                                                      36
                    9. ATTRIBUTE SELECTION                               
                       ===================
 
     Various attribute files can be nominated to generate a map display.        
It is the user's responsibility to ensure that the names referenced by the      
attributes match the names of the displayed zone lines and sites in the         
map.  Obviously colours can be assigned only to the zone with names common      
to the attribute and zone files etc.                                            
                                                                                
Only some of the names have to agree; it is quite common to process attribute   
data for a larger area than is displayed.                                       
                                                                                
     Attribute may be selected for quantisation and display from attribute      
files in various ways:                                                          
                                                                                
To try these options, display a zones map using attribute file LOWE1 and        
geographic file LOWE as before and then select the option to change attributes. 

  9. 1 Sequentially                                      
       ------------
 
This option will simply select the next attribute off the file. As usual F3 may 
have to be used to display the map.                                             

  9. 2 By number (position in file)                      
       ----------------------------
 
A prticular attribute may be selected by the position within the file. Type     
zero to generate a list of the attributes on the current file.                  

  9. 3 By attribute description                          
       ------------------------
 
The attribute can also be selected by typing part of the description e.g.       
"FORC" to retrieve "ARMED FORCES". Typing L lists the attributes.               

  9. 4 By arithmetic operation                           
       -----------------------
 
This option is not available due to the limited PC memory. See the data         
preparation option.                                                             


                                                                      37
                   10. QUANTISATION                                      
                       ============
 
     Attributes are usually presented to OzGIS as values which have to          
be quantized into a number of classes for display.                              
                                                                                
     A maximum of 10 classes can appear in single variate zone displays and     
9 classes (a maximum of 3 per variate) in a bivariate display.  A maximum       
of 4 classes is available for lines and 4 classes for sites.                    
                                                                                
     The quantisation process is the most important aid for the analyst in      
understanding the features of the attribute data.  The quantisation method      
and parameters should be chosen logically according to the purpose of           
analysing the data.                                                             
                                                                                
     The aim is to display the map that best shows the spatial features and     
distribution of the data.                                                       
                                                                                
Note that the best maps usually have a small number of classes; manipulate the  
map to show the data according to requirements. This contrasts with the         
production of atlases, where large numbers of colours are used as the purpose   
to which the map will be put is not known.                                      
                                                                                
To try these options, display a zones map using attribute file LOWE1 and        
geographic file LOWE as before, and select the option to change the             
quantisation. Try changing the number of classes first and then work through    
the various methods.                                                            
                                                                                
There are other options to change the list of zones to which quantisation is    
applied and to change the range of values over which the method operates.       

 10. 0. 1 Quantisation Methods                              
          --------------------
 
     The following methods for quantization are available for determining       
the class intervals:                                                            
                                                                                
   (a)  Equivalence Classes:  numbers are assigned to the attribute values      
        (possibly with integer round-off).  The attribute values should lie     
        in the range of the maximum number of classes permitted but they        
        will be scaled for the selected number of classes.                      
                                                                                
        This method enables the quantisation to be carried out on another       
        system and the resulting class numbers entered instead of attribute     
        values.  A common use is for mapping discrete data e.g. political       
        parties on election maps.                                               
                                                                                
   (b)  Quantiles:  intervals are computed by assigning the same number of      
        zones to each class.                                                    
                                                                                
        This method has often been used to generate choropleth maps, e.g.       
        deciles.  The effect of equal numbers of zones is maps that have        
        approximate equal areas of each class colour.  Such maps are            
        pretty.  Unfortunately quantiles tend to obscure the distribution       
        of the attribute data.                                                  
                                                                                
   (c)  Equal Value Intervals:  intervals are computed from equal               


                                                                      38
        increments over the range of attribute values.                          
                                                                                
        The default quantisation method selected when a map is first            
        generated is equal value intervals.  The advantage of this method       
                                                                                
        is that the number of zones assigned to each class indicate the         
        distribution of the data.  It is recommended for general purpose        
        maps and for initial investigations of attribute data.                  
                                                                                
   (d)  Refined Equal Value Intervals:  intervals are computed from equal       
        increments over the attribute value range, modified by a                
        "round-off" procedure (e.g. an increment of 10.12 would become          
        10.00).                                                                 
                                                                                
        Maps for publications usually have 'nice' values in the legend.         
                                                                                
   (e)  121 Equal Value Intervals:  121 intervals are computed from equal       
        increments over the range of attribute values.  Only 8 classes are      
        displayed in the legend, but the colours are assigned over the 121      
        quantized values to give a "continuous colour" appearance.              
        This option is only available with standard zone maps.                  
                                                                                
   (f)  Interactive Selection of Class Intervals:  intervals are selected       
        by the user by placing crosshairs on a displayed histogram.             
        (256 colours interactive mode only!)                                    
                                                                                
   (g)  Mean and Standard Deviation:  intervals are determined by dividing      
        the range of attribute values at the mean value and at specified        
        offsets from the mean that are multiples of the standard deviation      
        of the data.  The number of classes must be even.                       
                                                                                
        This method has particular application for attribute data from          
        random populations where the data are expected to have a normal         
        distribution and hence statistical theorems govern percentages of       
        population within the classes.                                          
                                                                                
   (h)  Nested Means:  intervals are determined by iterative division of        
        the range of attribute values at the mean value of the subdivision.     
        The number of classes must be 2, 4 or 8.                                
                                                                                
   (i)  Natural Breaks:  intervals are determined by iterative division at      
        the largest difference between attribute values.  The number of         
        attribute values between differences is user-specified.  Hence          
        class intervals occur at "jumps" in the data.                           
                                                                                
   (j)  Specification of Class Intervals:  interval values (for a specified     
        number of classes) are typed in by the user.                            
                                                                                
        Hence data within certain value ranges can be isolated.   Suitable      
        class intervals for hard-copy maps can be selected.                     
                                                                                
   (k)  Specification of Numbers Per Class:  intervals are determined by        
        user-specification of the number of zones or sites in each class.       
        The numbers need only be given for some of the classes; the             
        remaining zones or sites will be distributed over the remaining         
        classes during each quantization.                                       
                                                                                
        An analyst can isolate data at the extremes of the attribute            


                                                                      39
        distribution by using this method.                                      
                                                                                
   (l)  Class Number Percentiles:  intervals are determined from                
        user-specified values giving the percentages of the number of zones     
        within each class.                                                      
                                                                                
   (m)  Class Range Percentiles:  intervals are determined from                 
        user-specified values giving the percentage of the total range of       
        attribute values in each class.                                         
                                                                                
   (n)  Current Class Intervals:  the intervals (and number of classes) are     
        used to quantize subsequent attributes.                                 
                                                                                
        Hence a series of maps can be produced with the same legend which       
        enables attributes to be compared.                                      
                                                                                
   (o)  Current Numbers:  the number of zones or sites per class (and           
        number of classes) are used to determine the intervals for              
        subsequent attributes.                                                  

 10. 0. 2 Quantisation Ranges                               
          -------------------
 
      The range of values over which the quantization is applied can be         
restricted in all methods.  The following options are available for             
limiting the range:                                                             
                                                                                
      -  the extremes of all values (default)                                   
      -  user-specified limits (the user enters the low and high values)        
      -  refined values (i.e., automatically rounded to "nice" values)          
      -  limits fixed at current values for subsequent quantisations            
                                                                                
Zones with values outside these limits are assigned the "excluded zone"         
value and colour, lines and sites are not displayed.                            
                                                                                
For example a standard legend for percentage data with value ranges             
0,25,50,75 and 100 could be generated by choosing extremes to be 0 and 100      
and fixing them, and by using 4 equal value classes.                            

 10. 0. 3 Quantisation Lists                                
          ------------------
 
      Each of the attribute processing streams has an associated list           
that holds the names of the items being quantised i.e. zones or lines or        
sites.  There is one list for a single stream, one zones list for bivariate     
maps, and for two streams there is a list of zones and a list of lines or       
sites.                                                                          
                                                                                
      Each list selects the items that are to be quantised from the             
corresponding attribute file.  When a map is generated the lists are set to     
all the names if the attribute files (common names in the case of bivariate     
maps).                                                                          
                                                                                
      Zone lists can be reset to:                                               
                                                                                
      -  all zones in current attribute file (single variate)                   
      -  all zones common to two attribute files (bivariate)                    
      -  the displayed zones                                                    


                                                                      40
      -  zones in a names file                                                  
                                                                                
      Zone lists can also be modified by adding or deleting zone names by       
typing in a name or selecting the zone with the cursor (256 colour mode)        
                                                                                
      Site lists and line lists can be modified by giving the names.            
                                                                                
      Hence the quantisation can take place for a set of items that is          
independent of the displayed, zone lines and sites (although it is              
illogical for none to be the same).  It is common for the quantisation to       
be carried out over a larger geographic area than that being displayed.         
Sometimes zones are removed because the attribute data are doubtful e.g.        
Census districts with a low population.                                         
                                                                                
      Changing attribute files does not change the items whose values are       
quantized.                                                                      


                                                                      41
                   11.  DISPLAY CONTROL & MAP DESIGN                     
                       =============================
 

 11. 0. 1  Map Quantisation Legends                         
          -------------------------
 
                                                                                
      A legend is always displayed on the monitor when an attribute is          
quantised for map display.  Similar legends are displayed for zones, lines      
and sites.                                                                      
                                                                                
The elements of a legend are:                                                   
                                                                                
      -  TITLE, a title for the legend (maximum of 3 lines and 16               
         characters per line).                                                  
                                                                                
      -  UNITS, description of the units of a legend (maximum of 10             
         characters).                                                           
                                                                                
      -  HEADER, a header for the class annotation (maximum of 8                
         characters).  The default is "RANGE".                                  
                                                                                
                                                                                
      -  CLASS ANNOTATION, either                                               
                                                                                
            -  the class intervals as numbers aligned between boxes             
               (maximum of 8 characters), or                                    
                                                                                
            -  class description aligned with the centre of boxes (maximum      
               of 2 lines, 8 characters per line), or                           
                                                                                
            -  "HIGH" and "LOW" at the top and bottom of the boxes              
               respectively.                                                    
                                                                                
      -  EXCLUDED ZONES, annotation for the "excluded zones" class              
                                                                                
      -  MISSING DATA ZONES, annotation for the "missing data" class            
                                                                                
      -  NUMBERS, the numbers of items in each class.                           
                                                                                
      Zone legends have fixed size boxes that give the colours used for the     
classes.                                                                        
                                                                                
      Site legends have variable sized symbols in a special colour that give    
the markers and their sizes used for the classes.                               
                                                                                
      Line legends replace the boxes by sample lines in a special colour        
that give the line types used for the classes.                                  
                                                                                
      All text in a legend is written with small fixed size characters.         
                                                                                
      Display of the legend elements can be controlled by the user.  The        
boxes corresponding to attribute classes are always displayed but the           
elements (including "excluded zones" and "missing data " boxes) can be          
removed.                                                                        
                                                                                


                                                                      42
      Some of the legend text can be replaced by characters entered by the      
user on the keyboard, viz.,                                                     
                                                                                
         -  title                                                               
         -  units                                                               
         -  header                                                              
and      -  class description                                                   
                                                                                
      The default map layout sets the map image viewport as the left three      
quarters (approximately) of the monitor, and the legend viewpoints on the       
right side of the screen.  The zone legend is on the bottom, line or site       
legend above.                                                                   
                                                                                
      New legend viewpoints can be selected with the box cursor.  A single      
variate legend may need more than one column to fit.                            

 11. 0. 2 Overlays (GIS) legends                            
          ----------------------
 
When line overlays, markers, text at points or polygon underlays are displayed  
a legend appears that describes the overlays. The text must be specified by the 
user.                                                                           

 11. 0. 3 Other Legends                                     
          -------------
 
      When several line files are being displayed using different lines, or     
several site files are displayed using different markers, a legend can be       
added.                                                                          
                                                                                
      The line and marker legends have similar format:                          
                                                                                
      -  a header line of text                                                  
      -  legend entries                                                         
      -  marker or box in quantisation legend colour                            
      -  description                                                            

 11. 0. 4 Text                                              
          ----
 
      Lines of text can be typed in and displayed on the screen in one of       
the four available text types.  The text is positioned with the cursor.  Up     
to 20 lines of text can be displayed.                                           
                                                                                
      Lines of text can be deleted and moved around the screen.                 
                                                                                
      Text is usually added to a map to supply extra information e.g. the       
name of the geographic region and type of zones, organisation names,            
disclaimers.                                                                    

 11. 0. 5 Attribute Diagrams                                
          ------------------
 
      (a)  Histograms can be displayed in the map area.  The                    
           histograms show one of the following:                                
                                                                                
            -  the number of items (zones or sites) within equal intervals      
               of a single attribute                                            


                                                                      43
            -  the number of items within class intervals of a single           
               attribute                                                        
            -  the attribute values corresponding to zones sorted in            
               ascending order of attribute value.                              
                                                                                
               The bars of a histogram are coloured according to the class      
               colours in the legend.  For two variate displays, two            
               histograms can be displayed one underneath the other.  The       
               histograms provide an overview of the statistical                
               distribution of the attribute values.                            
                                                                                
      (b)      Scatter plots can be displayed in the map area for               
               bivariate zone displays.  The plots show the distribution of     
               zones within the ranges of each attribute.  The elements of      
               the plot are coloured according to the class colours in the      
               legend.  The scatter plots provide an overview of the            
               statistical distribution of the attribute values.                
                                                                                
      (c)   Statistics can be added to the diagrams:                            
                                                                                
      -  mean and standard deviation lines                                      
      -  median                                                                 
                                                                                
      A regression polynomial of order 1,2 or 3 can be added to a scatter       
diagram.                                                                        
                                                                                
      The diagram viewport is selected with the cursor.                         
                                                                                
      Addition of a distribution histogram or scatter diagram (bivariate)       
add considerably to the information content of a map.  It is recommended        
that they be displayed.                                                         

 11. 0. 6 Displayed Colours (removed)                       
          ---------------------------
 
      All colours within a map display can be changed by the user when a        
256 colour VGA display system is being used.  Individual colours can be         
selected in three ways:                                                         
                                                                                
      (a)  by reference to a colour palette.  The colour is selected with       
           the crosshairs (256 colour mode).                                    
                                                                                
      (b)  by a blue, green and red (B,G,R) triple.  Values for each of the     
                                                                                
           elements in the triple range from 0 to 1.0;  a red colour would      
           therefore be 0.0,0.0,1.0.                                            
                                                                                
      (c)  by a name from a colour names file.  The name is a character         
           string typed on the keyboard.                                        
                                                                                
Any of these ways can be selected by the user.                                  
                                                                                
      The set of colours is assigned to map classes and associated map          
elements by reference to the current device file.                               
                                                                                
This enables colours for all of  the classes to be assigned quickly, although   
individual colours in the set can be modified subsequently.                     
                                                                                


                                                                      44
      Displayed elements must be identified in order to change their            
colour.                                                                         
                                                                                
      Certain elements are explictly referenced in the menus associated         
with colour change, and can be identified by selecting the appropriate menu     
option.  These elements are:                                                    
                                                                                
     -  text                                                                    
     -  markers                                                                 
     -  lines                                                                   
     -  zone boundary                                                           
     -  map background                                                          
     -  excluded zones                                                          
     -  zones with missing data                                                 
     -  zone attribute classes                                                  
     -  background of attribute diagrams                                        
     -  site legend markers                                                     
     -  line legend                                                             
                                                                                
Specific attribute classes, text, markers and lines are identified by           
number.                                                                         


                                                                      45
                   12. MAP REGIONS                                       
                       ===========
 

 12. 0. 1 Regions                                           
          -------
 
      Maps usually consist of a data from a geographic file displayed on a      
default part of the monitor.                                                    
                                                                                
      Map regions enable complex map layouts to be generated.  Maps often       
have only one region, typically zones from one geographic file displayed on     
the default viewpoint on the monitor.  Multiple regions, each with defined      
window and viewport provide many possibilities e.g. subsets of a main map       
can be added as new regions at high magnification e.g. extreme parts of a       
map can be chopped off and added on as new regions in a corner e.g. several     
files for different parts of a country could be displayed as separate map       
regions.                                                                        
                                                                                
      Geographic files can be displayed in user-defined parts of the            
monitor.                                                                        
                                                                                
      A map region is established when a geographic file is displayed.  The     
region is defined by the geographic window (or subset) and its displayed        
area (or viewport) on the monitor.  A maximum of 10 map regions can be          
defined in a map.                                                               
                                                                                
      A geographic window is the total area of the geographic file.  Files      
are subset as a data preparation process.                                       
                                                                                
      A viewport is selected by positioning the cursor on the monitor with      
the mouse or arrows (i.e. it is a rectangular part of the screen).              
                                                                                
      It is possible to overlay data from geographic files onto a map           
region.  More than one set of zones from a geographic file can be displayed     
in a region but the zones being displayed will overwrite any underlying         
zones.                                                                          
                                                                                
      Geographic files are automatically windowed, scaled and clipped for       
display on map regions.                                                         
                                                                                
      When multiple files are displayed on a region, the precedure order is     
quantised zones, lines, sites, line overlays, markers and finally text at       
points.                                                                         
                                                                                
      Multiple regions can be defined anywhere on the map display area of       
the monitor.  However, if regions overlap the display procedure is              
established by the order of display.  Therefore the user should consider        
the order of display carefully in multiple region presentations.                
                                                                                
      Geographic files can be displayed  in any order, and                      
regions can be defined and changed as desired.  Many  of these operations       
destroy the data in the display system memory (the map display is               
corrupted) so F3 must be typed to completely regenerate the map display.        


                                                                      46

 12. 0. 2 Map List                                          
          --------
 
      A list of displayed items (zones, lines and sites) is maintained by       
the system.                                                                     
                                                                                
      The list is sorted into alphabetical order, and the items are             
displayed using pixels corresponding to the position in the table (fast         
interactive system).  This enables items to be selected with the cursor and     
identified.                                                                     
                                                                                
      A list of flags corresponding to the map list is also held.  The          
                                                                                
flags enable some of the displayed items to be dropped interactively.           
                                                                                
      The flags are usually set to items in the attribute files:                
                                                                                
      The options are:                                                          
                                                                                
      -  names in attribute file (single variate)                               
      -  common to two attribute files (bivariate)                              
      -  names in two attribute files (zones and lines or sites)                
      -  names for ranges of classes                                            
      -  names in quantisation lists                                            
                                                                                
      Items can be added or deleted by selecting them with the cursor or        
typing the name.                                                                
                                                                                
      The PC version of OzGIS can display up to 500 items.  When                
the number of display items (plus standard features) is less than the           
length of the hardware LUT (number of simultaneous colours) the system can      
display the results of quantising zone attribute data extremely rapidly by      
changing the colours.  When the number of items is too large the system has     
to revert to displaying each zone by polygon fill.                              

 12. 0. 3 Quantised Zones                                   
          ---------------
 
      Up to 10 sets of zones files can be displayed on defined regions.         
Adjacent files will automatically join.  GKS clips the polygons to the          
edges of the region viewports.  Where regions overlap, the zones of the         
last one to be displayed will overwrite the displayed data underneath.          
                                                                                
      Zones that are not in the map list are not displayed.                     
                                                                                
      When the system operates in fast interactive mode the zones are           
displayed once and the colours changed for the quantisation results.  In        
polygon fill mode the zones are displayed every time attribute data are         
quantised using fill (colour, pattern or hatch) for the appropriate             
classes.                                                                        
                                                                                
      Note that OzGIS expects overwriting to occur.  Hence display of           
polygons on top of others is not successful using hatching on plotters,         
so OzGIS handles polygons in a special way for this case.                       


                                                                      47

 12. 0. 4 Quantised lines                                   
          ---------------
 
      Up to 10 sets of lines can be displayed on regions.  GKS clips lines      
to region viewports.                                                            
                                                                                
      Lines that are not in the map list are not displayed.                     
                                                                                
      Each file is assigned to a different line, and is displayed in that       
line colour.  Four different lines are available.  The results of the           
quantisation are displayed by using different line types.                       
                                                                                
      The attribute data can be quantised into up to four classes, so four      
line types are used.  The line files are assigned to the four available         
lines according to overall classification when they are defined (e.g.           
roads, railway tracks and rivers).                                              

 12. 0. 5 Quantised sites                                   
          ---------------
 
      Up to 10 files can be displayed on regions.                               
                                                                                
      Sites that are not in the map list or are outside the region window       
are not displayed.                                                              
                                                                                
      Each file is assigned to a different marker and is displayed in that      
marker's colour and background colour.  Four different markers are              
available.  The results of the quantisation are displayed as different          
sized markers.  When operating in fast interactive mode, the markers are        
displayed in bit planes so they can be rapidly cleared.                         
                                                                                
      The attribute data can be quantised into up to four classes so four       
different marker sizes are used.  The files are assigned to the four            
available markers according to overall classification (e.g. owners of banks     
at the sites).                                                                  

 12. 0. 6 Line Overlays                                     
          -------------
 
      The segments from up to 10 geographic files can be displayed as           
overlays on map regions.  Each file is assigned to a region and one of four     
available lines and is displayed as a solid line in that line's colour.         
GKS clips the lines to the region's viewport.                                   

 12. 0. 7 Polygon underlays                                 
          -----------------
 
      The polygons from up to 10 geographic files can be displayed as           
underlays on map regions.  Each file is assigned to a region and one of eight   
available polygon colours.                                                      

 12. 0. 8 Marker Overlays                                   
          ---------------
 
      The points from up to 10 geographic files can be used to display          
markers at points in regions.  Each file is assigned to a region and to one     


                                                                      48
of four available markers.  Markers are not displayed for points outside        
the region's window.                                                            

 12. 0. 9 Name Overlays                                     
          -------------
 
      The  points from up to 10 geographic files can be used to display         
names at points in regions.  Each site file is assigned to a region and to      
one of four available types of text.  Names are not displayed for points        
outside the region's window.                                                    

 12. 0.10 Map Modification                                  
          ----------------
 
      The window and viewport of a map region can be modified by selecting      
a new one with the cursors.                                                     
                                                                                
      Files displayed for quantisation can be deleted from regions, unless      
the only one of that type.                                                      


                                                                      49
                   13.  MAP ANALYSIS                                     
                       =============
 

 13. 0. 1 Map Reports                                       
          -----------
 
                                                                                
      An option is available to write a full map report (giving details of      
the displayed items, their attribute values and class numbers) on the line      
printer file OZGIS.OUT                                                          
                                                                                

 13. 0. 2 Attribute Data Statistics                         
          -------------------------
 
                                                                                
      The statistics of displayed attributes can be computed and printed        
under user control.                                                             
                                                                                
      The following stastics are computed for a simple attribute:               
                                                                                
      -  minimum value                                                          
      -  maximum value                                                          
      -  mean value                                                             
      -  median value                                                           
      -  standard deviation                                                     
      -  skewness                                                               
      -  kurtosis                                                               
                                                                                
      For pairs of attributes (bi-variate displays) the above statistics        
are computed for each attribute, as well as                                     
                                                                                
      -  correlation coefficient                                                
and   -  regression polynomial coefficients (to order 3).                       
                                                                                
      These values can be printed on the user's terminal or the line            
printer file OZGIS.OUT                                                          
                                                                                

 13. 0. 3 Map Interrogation                                 
          -----------------
 
                                                                                
      When a map has been displayed, it is possible to interrogate the map      
data interactively.                                                             
                                                                                
      The details generated by interrogation are the names of the zones,        
lines or sites, the values of the displayed attributes (one value for           
single variate displays, and two for bivariate) and their assigned class        
number.  The options for interrogation are:                                     
                                                                                
                                                                                
   (a)  class number range                                                      
                                                                                
        -  items (zones, lines or sites)                                        
 within a specified range of class numbers.                                     


                                                                      50
                                                                                
   (b)  single item identification                                              
                                                                                
        -  zone line or site selected by entering its name at the keyboard.     
                                                                                
   (c)  set identification                                                      
                                                                                
        -  items selected by a names file, items in map, or items in            
           quantisation lists.                                                  
                                                                                
   (d)  Lists                                                                   
                                                                                
        -  The names of all the displayed items are held in one list.           
           Each attribute stream has an associated list of items that are       
           being quantised.                                                     
                                                                                
   (e)  Interactive selection                                                   
                                                                                
        -  The "box cursor" can be used to describe a rectangular region to     
           select items.  The selection of zones and lines is either by         
           all minimum bounding rectangles (MBR) of the items that fall         
           completely within the cursor window or MBRs that intersect           
           the window.  Sites (and zone centroids) are selected by points       
           that lie inside the window.                                          
                                                                                


                                                                      51
                   14. OzEnter DATA ENTRY                                
                       ==================
 

 14. 1 Introduction                                      
       ------------
 
                                                                                
Most data are entered into OzGIS as external data files. Examples are Census    
data and Census digitised boundaries. These files come from Census Bureaux,     
Mapping agencies, data supply companies or your own data-base systems.          
Some data can be prepared or modified with word processors or spreadsheets.     
                                                                                
This chapter describes the formats of external data files required by           
OzGIS and shows how to enter the example file provided with the system.         
                                                                                
The files are entered into the system via the OzEnter program which checks the  
data and writes them to internal files.                                         
                                                                                
All data files must have names that finish with the extension DAT.              
e.g. LONDON.DAT, SALES.DAT                                                      
                                                                                
Often data files will need further processing by the OzData program before used 
for mapping e.g. attribute data may need manipulating by arithmetic expressions 
geographic line segments may need thinning and forming into polygons.           
                                                                                
Future versions of the OzGIS system may have incompatible internal file formats 
so always keep important data files.                                            
                                                                                
The system comes with many of the system files already entered e.g. device      
files. The data files are also provided.                                        

 14. 2 Demonstration Files                               
       -------------------
 
The OzGIS system is supplied with a complete set of sample external             
data files so that the user can become familiar with the system.  These         
files can be inspected to clarify the file formats.                             
                                                                                
The files are usually in the directory \OZDEMO                                  

 14. 3 Example geographic and attribute data             
       -------------------------------------
 
Generally there will be two data files for each map; a file that describes the  
map boundaries and another for attribute data. The example files are:           
                                                                                
1. Far East Asia                                                                
                                                                                
Attribute file - FEA-A                                                          
Geographic file- FEA-G                                                          
                                                                                
These files have already been input in the demonstration chapter.               
                                                                                
2. Lowe electorate (Sydney)                                                     
                                                                                
Attribute files- LOWE-A1 and LOWE-A2                                            


                                                                      52
Geographic files- LOWE-G (zones), LOWE-S1, LOWE-S2 (sites)                      
                                                                                
3. Australia                                                                    
                                                                                
Attribute file - OZ-A                                                           
Geographic file- OZ-G                                                           
                                                                                
These files are already entered (supplied with the system).                     

 14. 4 Example device files                              
       --------------------
 
The characteristics of devices and the appearance of maps are given by display  
files. Data files are provided for all the device files supplied with the       
system. There are two sets for 16 and 256 colour video boards, and also sets    
for hatching and colour simulation on plotters etc.                             
                                                                                
Files are already entered on the system and have already been used.             

 14. 5 Marker data files                                 
       -----------------
 
These have already been entered, and are supplied with the system. They are     
circle, diamond, hbar, nabla, plus, square, triangle, vbar. (You can of cource  
have your own markers).                                                         
                                                                                

 14. 6 Colour names data (no longer used)                
       ----------------------------------
 
A colour names file X11-BGR.DAT is supplied and has probably already been       
entered as the default.                                                         
                                                                                
The colour names file can be entered as:                                        
                                                                                
Type ozenter to run the data entry program                                      
select the option to enter a colour names file                                  
give the name of the data file as X11-BGR                                       
give the output file name as DEFAULT                                            
type F10 to exit                                                                


                                                                      53
                   15. OzData DATA PREPARATION                           
                       =======================
 
The raw data are input to the system using the OzEnter program. However, the    
data often need further processing. Also, some data needed within the system    
cannot be specified as data files and need to be prepared.                      
                                                                                
These facilities are provided by the OzData program.                            

 15. 1 Attribute Files                                   
       ---------------
 
   A new attribute file can be generated from an attribute file and a           
   combine file.  The combine file defines new zones (or site catchments)       
   in terms of the names referenced by the attribute file.                      
                                                                                
   Attributes can also be derived from existing attributes by applying          
   arithmetic operations to the attribute values.                               
                                                                                
   Attributes are identified by the character # followed by a number,           
   indicating the sequential position of the attribute on the input file        
   (e.g. #10 represents the tenth attribute).  An example of an expression      
   to form a composite attribute is:                                            
                                                                                
                 (#1+#2)/2 > 0 < 1000                                           
                                                                                
   This creates a new attribute whose values are half the sum of the values     
   from the first and second attributes on the input file.  Any valid           
   arithmetic expression is acceptable.  The output values are limited to       
   the given range.                                                             
                                                                                
   Functions available are:-                                                    
                                                                                
      LOG10  :  common logarithm                                                
      SQRT   :  square root                                                     
      ABS    :  absolute value                                                  
      EXP    :  exponential                                                     
      SIN    :  sine                                                            
      COS    :  cosine                                                          
                                                                                
   Functions removed from the PC version are:                                   
                                                                                
      LOG    :  natural logarithm                                               
      AINT   :  truncation                                                      
      TAN    :  tangent                                                         
      ATAN   :  arc tangent                                                     
      SINH   :  hyperbolic sine                                                 
      COSH   :  hyperbolic cosine                                               
                                                                                
   Pi is referred to as PI.                                                     
                                                                                
   Operators are:                                                               
                                                                                
   +  addition                                                                  
   -  subtraction                                                               
   *  multiplication                                                            
   /  division                                                                  


                                                                      54
   >  greater than or equal to                                                  
   <  less than or equal to                                                     
                                                                                
   Expressions are evaluated left to right and have a limit of 70               
   characters.  Parentheses should be used to ensure there are no               
   ambiguities.                                                                 
                                                                                
   The user must give a 30 character attribute description and 10 character     
   units description for each new attribute that is generated.                  
                                                                                

 15. 2 Geographic Files                                  
       ----------------
 
Geographic files can be subset (windowed) on the basis of a                     
list of required display items (zones, sites, lines).                           
      - items in a names file                                                   
      - items in an attribute file                                              
      - items within a window selected with the cursor from a displayed file    
                                                                                
The line segments can be simplified to reduce the number of points that         
have to be processed.  This is used to speed up display where the               
resolution of the digitised data are higher that that needed for display        
terminals.                                                                      
                                                                                
Line segments that form polygons can be joined together into long segments.     
Where many short segments are used this process, in conjunction with            
simplification, can sustantially reduce the disk storage required and speed     
processing.                                                                     
                                                                                
The zones in a geographic file can be amalgamated according to a combine        
file to generate a new geographic file.  The new file contains the new          
zones.  The same combine file can be used to generate attribute data for        
the same new zones.                                                             

 15. 3 Palette Files (Removed from system)               
       -----------------------------------
 
Palettes are generated by selecting colours for the elements of a               
palette shown on the screen.  The colours can be selected in the                
following ways:                                                                 
                                                                                
      -  by entering blue, green and red values.                                
                                                                                
      -  by reference to another palette                                        
                                                                                
      -  by reference to a colour names file                                    
                                                                                
      -  by reference to a colour cross-section displayed in the map area       
         of the screen.                                                         
                                                                                
After colour selection, the palette can be saved as a file.                     
                                                                                
   An existing palette file can be modified to produce a new file, by           
   displaying it and adding or deleting elements.                               


                                                                      55

 15. 4 Colour Names Files  (Removed from system)         
       -----------------------------------------
 
   Colour names files are generated by typing in a name and then selecting      
   the corresponding colour in the ways described above for selecting           
   colours for palettes.  An existing colour names file can be modified.        

 15. 5  Names Files                                      
       ------------
 
Names files give lists of items (zones, sites,lines) that are to be processed.  
These lists can be generated from other types of files. These options are       
particularly useful when the names files are to be modified.                    

 15. 6  Output to Data Files                             
       ---------------------
 
Options are provided to output internal files as data files so they can be      
modified with word-processors for further processing.                           
                                                                                
Names files can be editted to change the lists of items used for processing.    
                                                                                
Attribute files can be output in simple database format.                        
                                                                                
Combine files can be modified as part of the definition of territories and      
sites.                                                                          
                                                                                
Attribute templates can be generated for preparation of attribute files with    
a word-processor.                                                               


                                                                      56
                   16. OzZone BUILDING ZONES FROM SEGMENTS               
                       ===================================
 

 16. 1 Use                                               
       ---
 
Zone boundary data can be supplied either as the complete set of points for the 
outsides of each polygon or as the line segments that make up the boundaries.   
Most segments will be common to two polygons so only about half the number of   
points are required. The segment form also allows zones to amalgamated into     
larger zones (by dropping internal segments) and to be thinned (by dropping     
excess points).                                                                 
                                                                                
The segments form is preferred to polygon formats.                              
                                                                                
The program takes line segments and joins the ends together to form polygons.   
The names of the zones on each side of the segments are used to derive the zone 
names.                                                                          
                                                                                
Complex polygons are handled. Zones can be made up of many polygons, both       
disjoint polygons and polygons within polygons. The display order of the        
polygons are calculated so e.g islands within lakes within zones all appear.    
                                                                                
The OzZone program has been implemented as a separate program to provide        
maximum capacity on the PC.                                                     
                                                                                
It is usual to line simplify (thin) the segments before building as many        
digitised boundary files (e.g. census) are at a much higher resolution than     
require for the display. Joining of line segments and further thinning may      
follow.                                                                         
                                                                                
The algorithm assumes that the segments have been produced on a proper          
digitising system and are correct e.g. it is assumed that end-points meet and   
the segments do not cross. Problems such as repeated segments, missing segments 
etc may cause problems. Ensure you use the program with trace turned on. If     
necessary turn on debug and look at the OZGIS.OUT file.                         
                                                                                
Use the file interrogation option to find the statistics on the geographic file 
e.g. the number of zones.                                                       
                                                                                
OzData can be used to generate a prototype attribute file (simple format) from  
the zones in the geographics file and hence get some test data that can be      
entered via OzEnter to form an attribute file. Displaying both files with       
OzCensus will allow the file to be checked.                                     
                                                                                

 16. 2 Example                                           
       -------
 
The procedure can be demonstrated with any of the geographic data files:        
                                                                                
Use OzEnter to input the standard geographic file LOWE-G and give it name       
TEMP1.                                                                          
                                                                                
Start OzData, select geographic files and then line simplification. Input file  
TEMP1 and output the new one as TEMP2. Simplify according to the size of the    


                                                                      57
final map on the screen e.g. give a value of 100 to throw away a lot of the     
data points.                                                                    
                                                                                
Now use OzZone to input TEMP2 and output it as TEMP3.                           
                                                                                
Finally use OzGIS to display the result (using attribute file LOWE1).           


                                                                      58
                   17. MAP PROJECTIONS (under development)               
                       ===================================
 

 17. 1 Introduction                                      
       ------------
 
OzGIS is a program is that will process a geographic file to form a new         
geographic file converting either from (Longitude,Latitude) to a projection     
or in the reverse direction.                                                    
                                                                                
You will have to have a basic knowledge of the projection you want to use       
e.g. that AMG is UTM with the Australian Spheroid and a false origin            
(500000,10000000).                                                              
                                                                                
OzProj is based on public domain software from USGS.                            
                                                                                

 17. 2 Precision                                         
       ---------
 
Vertices are stored in single precision in OzGIS (there is not                  
enough memory on the PC to do anything else). This means an accuracy of         
seven digits, so some values may not be accurate e.g. UTM may be a few metres   
out.  If more precise values are required, you may have to define your own false

 17. 3 Latitude / longitude                              
       --------------------
 
Latitude / longitude data must be given with units degrees.                     
                                                                                
Latitudes are negative in the Southern hemisphere.                              
                                                                                
Usual value ranges are:                                                         
Longitude -180 to +180                                                          
Latitude  -90  to +90                                                           
                                                                                
Note that the X value in data files is the longitude.                           
                                                                                
examples: (-100.0,50.0) i.e. longitude -100, latitude 50                        
          (145.0, -42.0) a point in Tasmania                                    

 17. 4 Projections                                       
       -----------
 
Twenty projections are supported:                                               
                                                                                
Albers Conical Egual Area                                                       
Azimuthal equidistant                                                           
Equidistant Conic                                                               
Equirectangular                                                                 
General Vertical Near-side Perspective                                          
Gnomic                                                                          
Lambert Conformal Conic                                                         
Lambert Azimuthal Equal Area                                                    
Mercator                                                                        
Miller Cylindrical                                                              


                                                                      59
Oblique Mercator (Hotine)                                                       
Orthographic                                                                    
Polar Stereographic                                                             
Polyconic                                                                       
Stereographic                                                                   
Transverse Mercator                                                             
Sinusoidal                                                                      
State Plane (USA)                                                               
Universal Transverse Mercator                                                   
Van der Grinten                                                                 

 17. 5 Ellipsoids                                        
       ----------
 
Several spheroids are available. The default is Clarke 1866.                    
                                                                                
MERIT 1983                                                                      
GRS 1980(IUGG, 1980)                                                            
IAU 1976                                                                        
Airy 1830                                                                       
Australian Natl, S. Amer., IAU 64                                               
GRS 67(IUGG 1967)                                                               
Bessel 1841                                                                     
Clarke 1866                                                                     
Clarke 1880 mod.                                                                
Everest 1830                                                                    
Hough                                                                           
International 1909 (Hayford)                                                    
Krassovsky, 1942                                                                
Mercury 1960                                                                    
Modified Airy                                                                   
Modified Everest                                                                
Modified Merc 1968                                                              
New International 1967                                                          
Southeast Asia                                                                  
Walbeck                                                                         
WGS 66                                                                          
WGS 72                                                                          
Sphere of 6370997 m                                                             


                                                                      60
                   18. HARDCOPY MAP PRODUCTION                           
                       =======================
 

 18. 1 Overview                                          
       --------
 
Maps are designed with the interactive OzGIS program and saved as Saved display 
files. These files are then read into the OzMap program and output on the       
desired device or file. Attributes and quantisation can be changed in the usual 
way to produce a series of maps.                                                
                                                                                
Often maps will be previewed on the screen and then output to a plotter,        
printer or file.                                                                
                                                                                
Hardcopy map production is limited by the capabilities of the SCIPLOT package.  
                                                                                
SciPlot produces many graphic file types:                                       
                                                                                
The Postscript file is an ASCII file that may be edited or sent directly to any 
Postscript printer.                                                             
                                                                                
The Encapsulated Postscript file (EPS) and the Computer Graphics Metafile (CGM),
an ANSI standard format file, are files that should not be edited for they      
contain binary information.  EPS and CGM files can be imported directly into    
wordprocessors or other graphical products.                                     
                                                                                
The HP pen plotter file (HPGL) is an ASCII file that can be edited or imported  
into wordprocessors or other graphical products.                                
                                                                                
The WordPerfect file (WPG) is a binary file in WordPerfect's internal graphics  
format.  WPG files are directly importable into the WordPerfect wordprocessor.  
                                                                                
The SciPlot Graphics file is a file in SciPlot's own internal format and is     
used solely as input to the VECTOR program.  This file is a binary file in very 
compact format.  It contains the stream of vectors which represent the figures, 
characters, etc. generated during the execution of the application program.     
VECTOR processes this graphic file and arranges raw vectors in a direction of   
paper motion order before display on dot matrix printers and laserjet printers. 
                                                                                
For Apple LaserWriters, HP pen plotters, and other graphics devices that        
support avector drawing commands directly, ordering is not required and VECTOR  
immediately displays the vectors.                                               
                                                                                
VECTOR's function is to provide a utility to register SciPlot's output on       
plotting devices (dot matrix and laserjet printers) which cannot be supported   
directly without requiring significant system resources.  VECTOR also provides  
interactive preview of graphics files on the screen or bath processing at some  
other time.                                                                     
                                                                                

 18. 2 Device files                                      
       ------------
 
Several device files are provided to control the appearence of maps on output   
devices. These device files can also be used with OzGIS (they will need minor   
modification for use with EGAs).                                                


                                                                      61
                                                                                
You have to use device files that use hatching for polygon fill. The            
configuration section explains the files available. Generally you need to use   
hatching device files that have the same resolution as that used in OzGIS or    
aspects and character sizes may not be suitable.                                
                                                                                
HATCHSV1   - provides polygon display using hatching.                           
HATCHBV1   - hatching for bivariate maps.                                       
CSIMSV* and CSIMBV* - a series of device files that use the red, green and blue 
plotter pens (or screen colours) to simulate the colour sequences; look at then 
on the screen first to decide which ones to try.                                
                                                                                
The hatching device files can of course be modified to define other hatching    
patterns.                                                                       
                                                                                

 18. 3 VECTOR Program                                    
       --------------
 
                                                                                
This program enables metafiles produced in the OzMap program to be output to a  
variety of devices and files with such options as rotation and scaling.         
                                                                                
                                                                                
VECTOR has two modes of operation, an interactive mode and a batch mode.        
The batch mode processes command strings from a disk file.  The user can        
include the command filename with the VECTOR command (eg. VECTOR                
command.fil).  Alternatively, the user can wait until VECTOR issues a           
prompt for the type of interaction desired.  The format of the command          
file and a description of the VECTOR.CFG file follows:                          
                                                                                
VECTOR[d:][path][filename[.ext]] [/U]                                           
                                                                                
[d:][path][filename[.ext]] [/U] - Process file which contains                   
filenames of graphics files to be processed in batch mode.  These               
files will be processed one at a time and plotted on the designated             
printer, plotter, or graphics crt device.  As a default, the                    
VECTOR.CFG file will be searched for a process filename.  When a                
filename is specified on the VECTOR command line, the process                   
filename given in VECTOR.CFG file is totally ignored and replaced by            
this new filename.                                                              
                                                                                
/U - This update option is used to override all parameters specified            
in the VECTOR.CFG file. The option initiates an interactive dialog              
with the user to obtain a new set of parameters for VECTOR. The user            
is given the opportunity at the end of the dialog to update the                 
current VECTOR.CFG file with these new parameters.                              
                                                                                
VECTOR.CFG Configuration File.                                                  
                                                                                
The VECTOR.CFG configuration file contains a list of commands that              
define VECTOR processing parameters. Each time VECTOR executes, it              
reads and interprets this file. If the VECTOR.CFG file cannot be                
located, VECTOR will interact with the user from the terminal to set            
up these parameters.                                                            
                                                                                
Format of Configuration File Commands:                                          
                                                                                


                                                                      62
Cmd    Option        Description                                                
                                                                                
FILE   =CONS         -Get graphics filenames from console.                      
       =[d:][path][filename[.ext]]- Use this file as a process file             
containing graphics filenames.                                                  
                                                                                
DEVICE =DOT          -Dot Matrix Printer                                        
       =PEN          -HP Pen Plotter                                            
       =JET          -HP LaserJet Printer                                       
       =WRITER       -Apple LaserWriter Printer                                 
       =CGA          -CGA Color Screen                                          
       =EGA          -EGA Color Screen                                          
       =VGA          -VGA Color Screen                                          
       =HGA          -Hercules Monochrome Screen                                
                                                                                
PORT   =COM1         -Printer/Plotter on Primary Serial Port                    
       =COM2         -Printer/Plotter on Secondary Serial Port                  
       =LPT1         -Printer/Plotter on Primary Parallel Port                  
       =LPT2         -Printer/Plotter on Secondary Parallel Port                
                                                                                
ANGL   =XXX.XX       -Rotation Angle (degrees)                                  
XSCL   =XXX.XX       -X-Axis Scale Factor                                       
YSCL   =XXX.XX       -Y-Axis Scale Factor                                       
XOFS   =XXX.XX       -X-Axis Offset (inches)                                    
YOFS   =XXX.XX       -Y-Axis Offset (inches)                                    
                                                                                
WAIT   =ON           -Wait between Plot Frames                                  
       =OFF          -Do not wait between Plot Frames                           
                                                                                
[When serial port is used for printer/plotter device, following                 
commands are valid]:                                                            
                                                                                
HAND   =SOFT         -Software Handshake (XON/XOFF)                             
       =HARD         -Hardware flow control on DSR line                         
                                                                                
MODE   =195          -Serial Port Mode Set Code, specified in                   
decimal format. 195 = (9600 baud, no parity,                                    
1 stop bit, 8 bit characters)                                                   
                                                                                
- Mode Set Code Description -    [bits]                                         
                                                                                
7     6    5  4     3       2          1       0                                
--Baud Rate-- -Parity-   -Stop Bits-  -Char Length-                             
000 -  110   00 - None 0  -    1      10  - 7 Bits                              
001 -  300   01 - Odd  1  -    2      11  - 8 Bits                              
010 -  600   11 - Even                                                          
011 - 1200                                                                      
100 - 2400                                                                      
101 - 4800                                                                      
110 - 9600                                                                      
111 -19200                                                                      
                                                                                
[When dot matrix printer is used, following commands are valid]:                
                                                                                
PINS   =9           -EPSON (MX-80,FX-80,FX-85,FX-850...)                        
       =24          -RPDON (LQ-800)                                             
                                                                                
HRES   =HIGH        -High Horizontal Resolution                                 


                                                                      63
       =LOW         -Low Horizontal                                             
                                                                                
VRES   =HIGH         -High Vertical Resolution                                  
       =LOW          -Low Vertical Resolution                                   
                                                                                
- Printer Resolution Table -                                                    
                                                                                
Printer  Resolution   Vertical  Horizontal                                      
9-Pin     LOW           72         120                                          
9-Pin     HIGH          216         240*                                        
24-Pin     LOW          180         180                                         
24-Pin    HIGH          180         360                                         
* 240 dot per inch resolution is not available on MX-80.                        
                                                                                
[When HP Pen plotter is used, following plotter initialization                  
command is valid]:                                                              
                                                                                
INIT   =ON           -Send handshake init sequence before plotting              
       =OFF          -No handshake init sequence required                       
                                                                                
When a process file is specified, VECTOR will process multiple graphics         
files in a batch mode. For the individual graphics file, VECTOR processes       
one plot frame at a time, for each file may contain more than one plot          
frame.  For dot matrix and HP LaserJet printers, VECTOR first sorts all         
the vector records in a minimum Y order for one plot frame.  This sorting       
is accomplished by creating an in-memory linked list directory of the           
disk records for the frame.  VECTOR accesses the graphics file randomly,        
bringing in only those records that contain vectors in the current              
process window. These print devices restrict the processing to a paper          
movement order. For HP Pen Plotters, Apple LaserWriters, and crt                
displays, VECTOR can process the vectors directly without any sorting for       
these devices support vector drawing commands.                                  
                                                                                
An inherent difficulty in this sort of processing approach is the limit         
imposed by the processor's memory size. There is an upper bound on the          
size of the graphics plot that can be handled because the linked list           
directory as well as a limited set of the vectors must be memory                
resident.  The exact size limit is difficult to predict because it is a         
function of the number of records in the file, the density of vectors per       
processing window, and the amount of lengthy vectors that must be               
remembered over many processing windows.  The VECTOR.OBJ file on the            
distribution diskette supports 64KB of directory sort space.  If this is        
not enough, a VECTOR.LRG file is included which supports 256KB of               
directory sort space.  Please note that the use of the VECTOR.LRG object        
file will significantly increase the size of the VECTOR.EXE file.               
                                                                                
Features                                                                        
                                                                                
The features incorporated in VECTOR are numerous.  Multiple plot frame          
processing is automatic.  A graphics vector file may be accessed from any       
disk.  Normal FORTRAN I/O is used to read the 128 byte binary records by        
the direct access method.  The VECTOR program will respond to a                 
control-C/Break at any time during execution.  This will terminate the          
current processing task, reset the printer to the top of form, and              
request another task.  Statistics for each plot frame, as well as total         
run statistics are displayed during the execution of VECTOR. For the dot        
matrix type graphics printer, four basic resolutions are provided by            
VECTOR depending on the type of printer attached.  A low resolution mode        


                                                                      64
is supported to quickly review the plot with very limited definition.           
This mode is useful for quick turn-around. The high resolution mode takes       
much more time because of hardware constraints, but gives very                  
satisfactory results.  VECTOR also has an on-screen preview capability          
which allows quick identification of graphics files.                            
                                                                                
Error Conditions:                                                               
                                                                                
During the execution of VECTOR, several error messages might be displayed       
on the terminal.  The only message that is not serious has to do with a         
premature termination of the programs that produced the graphics output         
file. The message reads "Premature End-of-File at Record XXXX". It just         
means that the graphics file was not terminated properly, but all the           
graphics data is valid.                                                         
                                                                                
The second class of messages is serious and should not be ignored. The          
messages are listed along with reasons.                                         
                                                                                
"Error reading graphics file" - means that FORTRAN I/O was unable to read       
the graphics file. The file should be recreated on another disk to              
correct the error condition.                                                    
                                                                                
"File not in graphics format" - means that the speacified file is not in        
SciPlot graphics format. Check to see if the filename is correct or was         
produced by a current version of SciPlot.                                       
                                                                                
"Graphics file too large for memory" - means that the graphics file             
specified cannot be processed by VEACTOR due to inadequate memory sort          
space.                                                                          
                                                                                
"Too many vectors for memory" - means that number of vectors per                
processing window is too dense. Try using the VECTOR.LRG object deck to         
generate the VECTOR.EXE command file.                                           
                                                                                
                                                                                
The VECTOR program supports IBM Graphics, IBM ProPrinters, EPSON MX-80,         
FX-80 with GRAFTRAXPLUS, FX-85, FX-850, LQ-800 dot matrix printers              
connected on an 8-bit parallel I/O interface.  All 8 bits are necessary         
to register the full resolution of the graphics printers.  The resolution       
obtained is a plot frame of (960,1920,2880) pixels over 8 inches in the         
horizontal direction by (1800,2160) pixels over 10 inches in the vertical       
direction. The feature of positioning (1/216th, 1/180th) of an inch is          
used, giving a basic resolution of (120,240,360) by (180,216) pixels per        
inch over a unit square of one inch on a side.  The IBM                         
Graphics/ProPrinter, and the EPSON FX-80,85,850 printers have twice the         
resolution as that of the EPSON MX-80.  The hardware requires double            
passes to absolutely register two dots in adjacent columns for this high        
resolution mode.  This is the reason for the lengthy processing time in         
this mode.                                                                      
                                                                                
There is no paper positioning done by VECTOR. Therefore, the user must          
position the paper before executing the VECTOR program.  This is done           
purposefully to allow plots to be manually positioned.  It is possible to       
imbed plots in full text with a careful alignment of the paper.                 
                                                                                
The HP Pen Plotter, the HP LaserJet, and the Apple LaserWriter are all          
supported by VEACTOR to register the graphics files produced by SciPlot.        
                                                                                


                                                                      65

 18. 4 Example                                           
       -------
 
You start by displaying a map with OzGIS and adding any text etc. When it is    
ready you save the map. There are two options for saved displays; either can be 
used but when saved for hardcopy output the screen is not saved so takes less   
disk space.                                                                     
                                                                                
The OzMap program is then started.                                              
                                                                                
The name of the saved map file is given and a HARDCOPY! device file chosen.     
Use the default one.                                                            
                                                                                
Type F3 to display the map on the screen.                                       
                                                                                
Now select a device - choose the printer metafile.                              
                                                                                
Type F3 to output the map to the file; give the file name e.g. phred.           
                                                                                
Type F10 to exit OzMap.                                                         
                                                                                
Type VECTOR to execute the program.                                             
                                                                                
Accept all default values (dot matrix printers) and give the Graphics file as   
phred.hrd (note the file extension).                                            
                                                                                
The map will be printed.                                                        


                                                                      66
                   19. OzTerr                                            
                       ======
 
Usually territories are to be developed from base zones according to some       
criterion;  e.g. Sales territories should all have similar sales potential;     
e.g. School districts should have similar numbers of children.                  
                                                                                
The operations are as follows.                                                  
                                                                                
     A base map is displayed:  Usually this will be a standard geographic       
     file (e.g. Melbourne postcodes).  Basic OzGIS facilities are used          
     to subset files if non-standard regions are required.                      
                                                                                
     Specification of territories:  Each territory has a unique 10              
     character name.  Zones are assigned off the screen with the cursor.        
     Zones can be moved between territories and deleted.  Territories can       
     be defined or deleted at any time.                                         
                                                                                
     Specification of a base-map attribute file:  Territory attributes are      
     continually calculated by adding the values for the base zones in each     
     territory.  The derived values are quantised (usually sequential           
     colour 121 class method), the territories coloured, and a legend and       
     histogram of sorted values displayed.                                      
                                                                                
     Zones can be shuffled according to the displayed territories attribute     
     values to meet the assignment criteria  while watching the legend          
     and histogram.                                                             
                                                                                
     When territory assignment is complete, the definition is output as a       
     combine file.                                                              
                                                                                
OzData provides a facility for amalgamating attribute data                      
for a combine file.                                                             
                                                                                
     The combine file can be used to amalgamate the base map geographic         
     file zones to produce a new geographic file, where the new zones are       
     the territories.                                                           
                                                                                
     The new geographic file and attribute data can be mapped                   
     by OzGIS in the standard way.                                              
                                                                                
     Territory assignment can be iterated by displaying the base map as         
     before, but using the combine file to set the initial territory            
     definition.  Similarly, if a basic territory assignment is know, it        
     can be  input as a combine data file and used to start the process.        


                                                                      67
                   20. OzCatch (NOT AVAILABLE YET)                       
                       ===========================
 

 20. 1 Introduction                                      
       ------------
 
Modules have been developed for site selection                                  
on a VAX using RAMTEK display systems.                                          
                                                                                
This software has to be completely rewritten for the limited PC displays.       

 20. 2  SITE CATCHMENTS                                  
       ----------------
 
The system aims to provide facilities for analysis of sites for the             
 definition of site locations and catchments, the                               
retrieval of data, development of models and display of results.                
                                                                                
The base of the process is the catchment file.                                  
A catchment file holds the definition of several sites.  The sites have         
some common grouping (e.g. all part of the same retail chain) and all fit       
on the same base map.                                                           
                                                                                
A typical analysis would involve several catchment files, e.g. several sets     
of sites each for a different organisations( e.g. several sets, each            
defined on different base maps to increase resolution. )                        
                                                                                
    Site definition is carried out for a current set of sites.  These           
     sites can be modified and new sites defined.  A base map is always         
     displayed and all the current sites must fit on the displayed map.         
                                                                                
    Also defined for assistance                                                 
 are any other catchment files relevant to the analysis.                        
     Site symbols, names and catchments are displayed if they fit on the        
     map.  These sites can not be modified.                                     
                                                                                
A catchment file contains the following information for each site.              
                                                                                
-    site name (10 characters)                                                  
-    site location                                                              
-    site symbol display location                                               
-    site name display location                                                 
-    catchment contours (up to 5)                                               
-    base zones and weights within catchment                                    
-    type of zones.                                                             
                                                                                
A site analysis could be carried out as follows.                                
                                                                                
Phase 1 - Definition                                                            
                                                                                
Each catchment file has to be defined.                                          
                                                                                
-    A base-map geographic file of suitable size is displayed.                  
                                                                                
-    An old catchment file may be read in for modification.                     
                                                                                


                                                                      68
-    Sites are defined by giving a name and location (cursor or typing lat      
     long).  Initial catchment contours are given as circles.                   
                                                                                
-    The results are stored as a catchment file.                                
                                                                                
The zones list in the catchment file can now be output as anames file.          
                                                                                
The names file is passed to OzData, attribute data are retrieved for the site   
catchments, and some basic statistics calculated.  On the basis of              
correlation coefficient and error levels for particular sites, the              
modifications for site catchments are decided.                                  
                                                                                
e.g.   there may be 2 or 3 base maps for Melbourne and                          
others for the country areas, each with different sites on them.                
                                                                                
Phase II - Modification of Catchments                                           
                                                                                
The site catchments (or positions) now have to be modified to obtain better     
agreement with known results.                                                   
                                                                                
-    The base map is displayed again.  Other site catchment files and           
     geographic overlays (e.g. roads) may also be displayed.  Note that the     
     base map could be changed.                                                 
                                                                                
-    the sites are modified.  More contours may be added.  Contours may be      
     replaced with circles of different radii or a replacement digitised.       
                                                                                
-    Zones lists are re-calculated.                                             
                                                                                
-    The new sites are processed by OzData again, and the process repeated      
     if necessary.                                                              
                                                                                
For example,  the base maps could change, say to go from                        
postcodes to collection districts.  Contours would change to get a better       
fit to the client's data.                                                       
                                                                                
Phase III - Zones                                                               
                                                                                
A base map is displayed and the contours overlayed.                             
The pixels within each contour polygon are counted and from the                 
total zone pixel counts and contour weights                                     
a list of zones and weights for each site is generated                          
and stored in the catchment file.                                               
                                                                                
The user has to make sure that the base map extends past the                    
catchment.                                                                      
Note that any type of zones can be used as the contours are                     
stored as lat-long points.                                                      
                                                                                
Phase IV - Display Preparation                                                  
                                                                                
A base map is displayed that is to be used for the final maps, and current      
catchment file displayed.  All the catchment files are displayed -              
contours, symbols and site names.                                               
                                                                                
Symbols and names in the current catchment file are repositioned with the       
cursor if they conflict with those from other files.                            
Lines are displayed between the symbol and true positions.                      


                                                                      69
                                                                                
A new catchment file is generated.                                              
                                                                                
An combine file is generated for retrieval of attribute data for all site       
names.                                                                          
                                                                                
A base map is displayed and the catchment files displayed that are to have      
the same symbol on the maps.                                                    
                                                                                
A geographic file is generated for site symbol display.                         
                                                                                
A geographic file to display the lines between the offset                       
symbol locations and site locations is generated.                               
This file also contains points for site name display.                           
                                                                                
For example,  a base map for the part of Victoria required                      
would be subset from a Victorian postcode map.  All the catchment files are     
displayed and names and symbols moved for the locations where there are two     
close sites.                                                                    
                                                                                
Phase V - Map Production                                                        
                                                                                
A names file is generated from the combine file for                             
all sites that are to be displayed.                                             
                                                                                
-    Data are retrieved from OzData for the names file.                         
                                                                                
-    A map is displayed for either just sites, or sites on quantised map        
     zones.                                                                     
                                                                                
     If there are several sets of sites each file                               
 is added and possibly assigned                                                 
     to a different symbol.                                                     
Note that symbol 1 is the top bit plane, symbol 2 the                           
next down etc.                                                                  
                                                                                
Standard geographic overlays can be added from the geographic                   
files that were generated; sites names, symbols, lines                          
between symbol and true locations.                                              
                                                                                
-    Other geographic overlays, diagrams etc are added.                         
                                                                                
For example,  a map could be displayed by using the Victorian                   
postcode map as a base with postcode attributes, and displaying symbols at      
sites using attributes calculated by OzData.  If potential sites are being      
evaluated, they would be in different geographic files and different            
symbols would be used.                                                          
                                                                                


                                                                      70
                     A. DATA SOURCES                                      
                       ============
 

  A. 1 Australia                                         
      ---------
 

  A. 1. 1 AUSLIG data                                       
          -----------
 
The Australian Land Information Group in Canberra can supply                    
the boundaries of the Collection Districts for the 1986 Census.                 
                                                                                
Data are available for each state for:-                                         
      - collection districts                                                    
      - postcodes                                                               
      - Local Government Areas                                                  
      - Statistical divisions                                                   
      - etc                                                                     
                                                                                
Ozenter can process the AUSLIG segments data to produce the OzGIS segments,     
which can then be formed into polygons with OzZone (to reflect                  
the structure of the data e.g. which polygons are inside others).               
                                                                                
The data are extremely detailed, so large files are involved. Hence subsetting, 
segment joining and line simplification are usually used.                       
                                                                                
All data are projection code 1 = latitude-longitude, units degrees.             
                                                                                
Make sure you get census boundaries in SEGMENTS format on floppy disk.          
                                                                                
Other map data are available, but need reformatting for use with OzGIS e.g.     
names file.                                                                     
                                                                                
Unfortunately, government policy of cost recovery means that AUSLIG data are    
expensive.                                                                      
                                                                                
Several publications are available.                                             
                                                                                
Contact:                                                                        
                                                                                
AUSLIG SALES (Digital Data), PO Box 2, Belconnen ACT 2616.                      
Phone (06) 252 6389  Fax (06) 251 5446                                          

  A. 1. 2 Australian Bureau of Statistics                   
          -------------------------------
 
The ABS collects and disseminates enormous volumes of statistics, some of which 
is available on floppy disk and CD ROM for mapping.                             
                                                                                
The major data source is the Census of Population and Housing - by far the most 
extensive source of demographic data available in Australia.                    
                                                                                
The ABS will supply data on floppy disk. Data output from the GeoStats product  
in LAMM format is supported.                                                    
                                                                                


                                                                      71
The ABS will supply boundary data for the 1991 Census.                          
                                                                                
Many publications describing the data are available.                            
                                                                                
Contact:                                                                        
                                                                                
Information Services,                                                           
Australian Bureau of Statistics,                                                
PO Box 10, Belconnen, ACT 2616.                                                 
Phone (06) 252 5402, 252 6627, or 252 6007.                                     
                                                                                
or any ABS state office.                                                        

  A. 2 New Zealand                                       
      -----------
 
The Department of Statistics have a product SAM (Socio-economic Area Mapping)   
and will supply data suitable for mapping.                                      
                                                                                
Contact their Information Consultancy Group first.                              
                                                                                
Offices are in Auckland, Wellington, Christcurch and Dunedin.                   
                                                                                
The boundary data are digitised and maintained on a GeoVision system so it is   
suggested that they be obtained in Gina format.  The data are prepared by the   
Department of Survey and Land Information - you could contact them directly.    
                                                                                
Population Census data and other attribute data are available in comma          
delimited formats.                                                              

  A. 3 United Kingdom                                    
      --------------
 
The various agencies are in the process of generating digitised boundary data,  
and there are some private efforts.                                             
                                                                                
Contact:                                                                        
The Office of Population Censuses and Surveys (OPCS),                           
St Catherines House,                                                            
10 Kingsway London                                                              
Phone 071 242 0262                                                              
                                                                                
or:                                                                             
                                                                                
Customer Services,                                                              
General Register Office,                                                        
Ladywell House,                                                                 
Edinburgh.                                                                      
Phone 031 334 0380                                                              

  A. 4 Canada                                            
      ------
 
Statistics Canada has not answered our letters or FAX.                          


                                                                      72

  A. 5 USA                                               
      ---
 
The Advanced Technology Group (ATG) market PC systems to extract Census and     
Tiger boundary data from CDrom.                                                 
                                                                                
Contact: ATG Inc.,                                                              
205 Regency Executive Park,                                                     
Suite 306,                                                                      
Charlotte,                                                                      
NC 28217.    Phone (704) 521 8113                                               
                                                                                
                                                                                
The US Census Bureau produce a large amount of boundary and attribute data.     
They have a product called TIGER/boundaries for PC mapping.                     
                                                                                
We obtained some information early in 1991, but a subsequent letter and a FAX   
offering to buy test data have not been answered.                               

  A. 6 Others                                            
      ------
 
Attemps to obtain other data from other suppliers has so far failed. The best   
we get is a heap of glossies. Questions we ask in our letters are ignored.      
Requests for test data are either greeted with paranoia or are ignored.         
                                                                                
Hence we request users with data to send us samples, with documentation so we   
can support the data in the system.                                             


                                                                      73
                     B. MAP DATA FORMATS                                  
                       ================
 

  B. 1 Introduction                                      
      ------------
 
The OzGIS system was designed to accept data from external sources.             
                                                                                
These data may be supplied in standard GIS formats that are supported by the    
system or may have to be reformatted into one of the system formats before use. 

  B. 2 Data Format                                       
      -----------
 
The data files have been designed with a simple format which can be easily      
generated on computer systems.                                                  
                                                                                
Most data are held as character files so that they can be generated by          
programs with, for example, database system export procedures, formatted        
FORTRAN write statements, or by a text editor.  The record lengths are up to    
80 bytes long.                                                                  
                                                                                
Each file starts with a comment record of up to 80 characters, which should     
be used to hold a meaningful description of the file.  The OzGIS system         
will display this comment when data files are interrogated, so it is in the     
users' interest to make the comments meaningful.  This record must contain      
at least one non-blank character.                                               
                                                                                
Data values are entered in record fields that are multiples of 10 bytes.        
The following computer restrictions apply:                                      
                                                                                
     -  Character data (e.g. zone names) are usually left justified and         
        blank filled.  Sorted character strings must conform to the ASCII       
        collating sequence.                                                     
                                                                                
     -  All real values (i.e. with decimal points) can be placed anywhere       
        in the 10 byte fields, but the decimal points must be included.         
                                                                                
     -  All integer values must be right justified in the 10 byte fields.       
        Their values must be within the range the computer is capable of        
        handling.                                                               
                                                                                
The maximum numbers of some data items that can be handled                      
are system parameters. Refer to theaAppendix.                                   

  B. 2. 1 Description of File Formats                       
          ---------------------------
 
The formats for describing the data files in the following sections are         
similar.                                                                        
                                                                                
The number of bytes in the field is given at the start of the line.  If         
there are several values in a format, this condition is indicated               
differently (e.g. 8 x 10 implies eight fields of 10 bytes).                     
                                                                                
The information on the next line is the type of data in a field:                


                                                                      74
                                                                                
     byte     = character                                                       
     real     = number containing a decimal point                               
     integer  = number without a decimal point                                  
                                                                                

  B. 3 Format of attribute files                         
      -------------------------
 

  B. 3. 1 General                                           
          -------
 
Attribute data are often obtained from Census Bureaux. These data are seldom    
what is required, so will need processing by OzData before use.                 
                                                                                
Data often need normalising to allow for the differences in zone sizes. This is 
done by arithmetic operations where new attributes are derived by dividing by   
total population, area etc.                                                     
                                                                                
Also, data often need amalgamation e.g. census age groups to get the required   
group.                                                                          

  B. 3. 2 Standard format                                   
          ---------------
 
Attribute files contain the attribute value of each zone or line or site        
for a number of attributes.  The names must correspond to those defined in      
a geographic file.                                                              
                                                                                
The attribute description is used by OzGIS as a heading in a map                
displaying the attribute.  The units description is used by OzGIS as a          
heading to the class values in the map legend.                                  
                                                                                
For efficient use of the system and to facilitate disc file management,         
files should contain as many attributes as possible (to avoid having            
separate files for each attribute).                                             
                                                                                
Attribute files will usually be prepared by special programs which extract      
data from a data-base and convert attribute values into the OzGIS               
format.                                                                         
                                                                                
     Comment Record:                                                            
     80       byte      comment describing the data                             
                                                                                
     Header Record:                                                             
     10       integer   number of attributes                                    
     10       integer   number of names                                         
     10       real      value used to indicate missing data                     
                                                                                
     Name Records:                                                              
     8 x 10   byte      names, sorted into ascending order                      
                                                                                
Sets of records follow to define the attributes:-                               
                                                                                
     Definition Record:                                                         
     30       byte      attribute description                                   
     10       byte      units description                                       


                                                                      75
                                                                                
     Values Records:                                                            
     8 x 10   real      attribute values for zones, lines or sites in name      
                        order                                                   
                                                                                

  B. 3. 3 Sample attribute file DEMOATTR.DAT                
          ----------------------------------
 
DEMOATTR.DAT   - ATTRIBUTES FOR SIMPLE 3 ZONE TEST MAP                          
         5         6     -9.9                                                   
ABCDEFGHIJZONE 1    ZONE 2    ZONE 3    ZONE 4    ZONE Z                        
FIRST STATISTIC               FIRST UNITS                                       
       1.0       2.0       3.0       4.0       5.0       6.0                    
SECOND STAT                   SECOND UNITS                                      
     100.0     200.0      -9.9     400.0     500.0     600.0                    
THIRD STAT                    3RD UNITS                                         
       0.1       0.9       0.3       0.7       0.1       0.8                    
FOURTH STATS                  4TH UNIT                                          
       1.0       2.0       3.0       3.0       2.5       1.5                    
FIFTH STAT                    5TH UNIT                                          
       9.0       6.0       3.0       2.0       6.0       8.0                    

  B. 3. 4 Simple Attribute format (database format)         
          -----------------------------------------
 
                                                                                
Many data retrieval systems (e.g. ORACLE,SAS) produce attribute data in a form  
where for each attribute the names and their values are given.                  
                                                                                
This table format is supported in OzGIS although there are some restrictions    
on its use.  The list of names is obtained from the first attribute; hence      
no new names can occur in following attributes (although names may be           
missing).  A set of data records for an attribute is assumed to finish (and     
the next set start) when the attribute description changes.                     
                                                                                
     Comment record:                                                            
     80      byte       Comment describing the data                             
                                                                                
     Data records:                                                              
     10      byte       name                                                    
     10      real       value                                                   
     30      byte       attribute description                                   
     10      byte       attribute units                                         
                                                                                

  B. 3. 5 Sample simple attribute file DEMOSASA.DAT         
          -----------------------------------------
 
SIMPLE FORMAT ATTRIBUTE FILE - DEMOSASA.DAT                                     
TOP            1.0   DESCRIPTION A                 UNITS A                      
SQUARE         2.0   DESCRIPTION A                 UNITS A                      
DIAMOND        3.0   DESCRIPTION A                 UNITS A                      
TRIANGLE       4.0   DESCRIPTION A                 UNITS A                      
TOP            1.0   DESCRIPTION B                 UNITS B                      
DIAMOND        3.0   DESCRIPTION B                 UNITS B                      
SQUARE         2.0   DESCRIPTION B                 UNITS B                      
TRIANGLE       4.0   DESCRIPTION B                 UNITS B                      


                                                                      76
TOP            1.0   DESCRIPTION C                 UNITS C                      
SQUARE         2.0   DESCRIPTION C                 UNITS C                      
DIAMOND        3.0   DESCRIPTION C                 UNITS C                      
TRIANGLE       4.0   DESCRIPTION C                 UNITS C                      
TOP            1.0   DESCRIPTION D                 UNITS D                      
TRIANGLE       4.0   DESCRIPTION D                 UNITS D                      
DIAMOND        3.0   DESCRIPTION D                 UNITS D                      
DIAMOND        3.0   DESCRIPTION E                 UNITS E                      
TRIANGLE       4.0   DESCRIPTION E                 UNITS E                      
                                                                                

  B. 3. 6 Spreadsheet data formats                          
          ------------------------
 
                                                                                
Data from spreadsheets can be input in Lotus 1-2-3 format.                      
                                                                                
The spreadsheet must be set up in a fixed format:                               
                                                                                
The data values are in a matrix with the values for the zones (or sites or      
lines) in columns and the different attributes across in the rows.              
Values can be missing and can be integer or floating point.                     
                                                                                
The first column must contain labels which are the 10 character zone (site etc) 
names, beginning at row 3. These must be SORTED in ascending order.             
                                                                                
The top row contains labels that are the (up to) 30 character attribute         
descriptions starting at column 2.                                              
                                                                                
The second row is the 10 character attribute descriptions.                      
                                                                                
e.g. the file DEMO123.dat can be read into the spreadsheet. It should look      
like:                                                                           
                                                                                
            POPULATION GROWTH   SALES                                           
            NUMBER              $                                               
ABBOTSFORD                 7418      237                                        
BURWOOD E                  9925      955                                        
CONCORD                    8984      202                                        
CROYDON N                  9369      298                                        
CROYDON W                   735                                                 
FIVE DOCK                  9903      716                                        
HABERFIELD                           727                                        
HOMEBUSH                   6631      704                                        
HUDSONPARK                 4668       71                                        
MORTLAKE                   1725      198                                        
STRATHFIELD                6285      663                                        
YARALLA                    9875      516                                        

  B. 3. 7 LAMM format                                       
          -----------
 
The LAMM package was developed at the CSIRO Division of Building Research. The  
format is supported as it is the only suitable format for mapping available in  
the Australian Bureau of Statistics GEOSTATS system.                            
                                                                                
An example file is DEMOLAMM:                                                    
                                                                                


                                                                      77
12,8                                                                            
MALES 35 - 44 (81)                                                              
MALES 35 - 44 (86)                                                              
MALES - UNEMPLOYED (76)                                                         
MALES - UNEMPLOYED (81)                                                         
MALES - UNEMPLOYED (86)                                                         
INCOME MALES $18001-$26000 (76)                                                 
INCOME MALES $18001-$26000 (81)                                                 
INCOME MALES $18001-$26000 (86)                                                 
'ABBOTSFORD'   69 0 14 27 48 0 51 55                                            
'BURWOOD E'    223 0 48 134 89 0 218 397                                        
'CONCORD'      102 0 5 12 29 0 109 197                                          
'CROYDON N'    161 0 27 50 53 0 156 284                                         
'CROYDON W'    180 0 24 36 76 0 307 241                                         
'FIVE DOCK'    50 0 20 2 0 0 19 11                                              
'HABERFIELD'   126 0 28 20 20 0 208 185                                         
'HOMEBUSH'     114 0 26 51 37 0 165 212                                         
'HUDSONPARK'   243 0 65 99 65 0 231 385                                         
'MORTLAKE'     0 0 0 0 2 0 0 113                                                
'STRATHFIELD'  100 0 4 7 10 0 74 70                                             
'YARALLA'      7 0 16 2 0 0 4 3                                                 
                                                                                

  B. 3. 8 Comma delimited format                            
          ----------------------
 
The comma delimited format consists of a set of records:                        
                                                                                
Each record has a series of values separated by commas.                         
                                                                                
The first value is the item (zone,line or site) name and there follows one      
number for each attribute.                                                      
                                                                                
                                                                                
The comma delimitted form is seriously deficient in that it contains no         
attribute descriptions.                                                         
                                                                                
Processing this format would require asking the user to type in the description 
for each attribute which is time consuming and there is always the danger that  
an attribute could be incorrectly labelled.                                     
                                                                                
Either:                                                                         
                                                                                
read the data into a spreadsheet                                                
                                                                                
Or:                                                                             
                                                                                
convert into LAMM format with a word processor.                                 
                                                                                
The file DEMOCOMD.DAT looks like:                                               
                                                                                
2727400,115,114,105,6                                                           
2727800,77,75,63,29                                                             
PHRED,85,81,66,36                                                               
NEW YORK,5,6,3,3                                                                
2728200,27,27,21,12                                                             
2728300,74,72,63,34                                                             
.                                                                               


                                                                      78
.                                                                               
.                                                                               
.                                                                               
2739100,13,12,12,5                                                              
2739200,2,0,3,1                                                                 
                                                                                

  B. 3. 9 Other attribute data formats                      
          ----------------------------
 
Other formats will be supported as required.                                    
                                                                                
We will support any formats for major data suppliers, but you must send sample  
data and documentation.                                                         
                                                                                
We will also attempt to support file formats from other packages.               

  B. 4 Standard format of geographic files               
      -----------------------------------
 

  B. 4. 1 General Information                               
          -------------------
 
The standard data format reflects the internal topological file structure.      
                                                                                
In practice, a complete data file is seldom available. It is more common to     
bring in just points (as a map and points partition) or lines (as a map and     
segments partition). Zones are usually formed from the segements with the       
OzZone program.                                                                 
                                                                                
Coordinates are usually given either in degrees (for lat,long) or in metres /   
feet for UTM.                                                                   

  B. 4. 2 Structure of data                                 
          -----------------
 
Geographic files contain several partitions.  The first must be the map         
partition, and can be followed by at most one of each of zones, polygons,       
lines, segments and points partitions.                                          
                                                                                
Each partition is preceded by a type record, which is one of MAP, ZONES,        
POLYGONS, LINES or POINTS; for example, a zones file must  have the             
following structure:                                                            
                                                                                
     Comment record                                                             
     MAP                                                                        
     map records                                                                
     POLYGONS                                                                   
     polygon records                                                            
     ZONES                                                                      
     zone records                                                               
     SEGMENTS                                                                   
     segment records                                                            
                                                                                
Different partitions are present (the MAP partition is always first)            
 according to the type of data:-                                                
                                                                                


                                                                      79
Files which describe zones have a ZONES partition to define                     
the zones, a POLYGONS partion to give the polygons that                         
bound each zone (including lakes and islands), and a SEGMENTS partition         
to define the coordinate points that draw the segments along the                
polygon boundaries.                                                             
                                                                                
Sites files have a POINTS partition to give the site names                      
and locations.                                                                  
                                                                                
Lines files have a LINES partition to define the line names                     
and a SEGMENTS partion to define the coordinate points in the                   
segments that make up the lines.                                                
                                                                                
Line overlays are defined by SEGMENTS partitions.                               
                                                                                
Marker and name overlays are defined by POINTS partitions.                      
                                                                                
Coordinate data should be entered in standard units.  Coordinate pairs are      
always in the order (X,Y) (e.g. (Longitude, Latitude)).  Note that latitude     
must be entered as a negative number in the Southern Hemisphere.                
                                                                                
Data entered in latitude-longitude projection with units of degrees can be      
converted to other projections.                                                 
Feature codes may be included to give a classification of geographic items.     
e.g. segments may be classified as different types of roads.                    
                                                                                
All geographic regions (windows) are given in actual coordinate values in       
the order:  X-minimum, X-maximum, Y-minimum, Y-maximum.                         

  B. 4. 3 Internal Data                                     
          -------------
 
The geographic data are held internally as a word-addressable                   
random access disk file.                                                        
The file structure reflects the data structure with the necessary               
indexing etc for processing.                                                    
Additional data are also generated for efficient processing:-                   
                                                                                
Polygons are held in display order so the map zones can be                      
rapidly displayed.                                                              
                                                                                
 A POINTS partition is generated internally by OzGIS                            
for the centroids of the zone polygons.                                         
This enables markers or zone names to be overlayed over                         
a zones map, and for the points to be displayed as sites                        
where the site names are the zone names.                                        
                                                                                
Lists of names are also generated for zones, lines or sites                     
for rapid retrieval.                                                            

  B. 4. 4 Comment Record                                    
          --------------
 
                                                                                
     80      byte       comment describing the data                             
                                                                                


                                                                      80

  B. 4. 5 Map Partition                                     
          -------------
 
                                                                                
This partition contains general information about the file (map) and must       
be the first partition.                                                         
                                                                                
     Type Record:                                                               
     3        byte      partition header = MAP                                  
                                                                                
     Window Record:                                                             
     4 x 10  real       the region covered by the file                          
                                                                                
     Projection Record:                                                         
     10 integer         Map projection code                                     
                        0=none, 1=lat-long degrees                              
     10       integer   type of zones (optional)                                
                                                                                

  B. 4. 6 Zones Partition                                   
          ---------------
 
                                                                                
This partition defines the zones in the geographic region.                      
                                                                                
Each zone is defined by one or more polygons.  A zone may consist of a          
polygon, several separated polygons, polygons with interior polygons of         
other zones, etc.                                                               
                                                                                
If a zones partition is present, a polygons partition with the referenced       
must be given.                                                                  
                                                                                
The partition may be used as a polygon underlay and feature codes may be used   
to give a classification e.g. the polygons may be different soil types.         
                                                                                
     Type Record:                                                               
     5        byte      partition header = ZONES                                
                                                                                
     Definition Record:                                                         
     10       integer   number of zones                                         
     10       integer   number of feature codes                                 
                                                                                
     Feature code Records (if required):                                        
     8 x 10  integer    feature codes                                           
                                                                                
     Zone Records:                                                              
     10       byte      zone name, usually left justified, blank filled         
     10       integer   number of polygons in the zone                          
                                                                                
     Polygon Records:                                                           
     8 x 10  integer    identifying numbers of the polygons                     


                                                                      81

  B. 4. 7 Line Partition                                    
          --------------
 
                                                                                
The partition defines networks of lines (e.g. roads, rivers).  Each network     
has a name and is specified in terms of line segments.The name can be used      
to apply quantised attribute data.                                              
                                                                                
Type record:                                                                    
     5       byte       partition Leader = LINES                                
                                                                                
Header record:                                                                  
     10      integer    number of lines                                         
                                                                                
                                                                                
Line record:                                                                    
     10      byte       line name, usually left justified, blank                
                        filled                                                  
     10      integer    number of segments forming the line                     
                                                                                
                                                                                
Region Record:                                                                  
     4x10    real       line limits (window)                                    
                        X minimum, X-maximum, Y-minimum, Y-maximum)             
                                                                                
Segments Records:                                                               
     8x10    integer    the identifying numbers of the line segments.           

  B. 4. 8 Polygons Partition                                
          ------------------
 
                                                                                
A polygon defines an enclosed geographic area.  Each polygon is specified       
in terms of the line segments which constitute its boundary.  If a zones        
partition is given, every polygon referenced by the zones must be defined.      
                                                                                
The centroid or internal point of a polygon is be used by OzGIS to              
locate text (zone names) or graphic symbols;                                    
a points partition is generated.                                                
                                                                                
Type Record:                                                                    
     8        byte      partition header = POLYGONS                             
                                                                                
     Header Record:                                                             
     10       integer   number of polygons                                      
                                                                                
A set of records follow for each polygon:-                                      
                                                                                
     Definition Record:                                                         
     10       integer   polygon identification number                           
     10       byte      name of zone enclosed by polygon                        
     10       integer   number of lines forming the polygon boundary            
     10       integer   level of polygon for display using                      
                        polygon fill 0=standard, 1=lakes, 2=islands in          
                        lakes etc. (range 0-5)                                  
                                                                                


                                                                      82
     Region Record:                                                             
     4 x 10   real      polygon limits (window)                                 
                        (X-minimum, X-maximum, Y-minimum, Y-maximum)            
                                                                                
     2 x 10   real      centroid or labelling point (X,Y) in the polygon        
                        (set to centre of window if not given)                  
     10       real      area of polygon                                         
                        (calculated if not given)                               
                                                                                
     Segments Records:                                                          
     8 x 10   integer   the identifying numbers of the segments + ve if         
                        segment is clockwise, -ve if anticlockwise.             

  B. 4. 9 Segments Partition                                
          ------------------
 
Line segments are defined by a set of points connected by straight lines.       
                                                                                
Segments may define the boundaries of zones, define line                        
networks, or line overlays.                                                     
                                                                                
When a segment is a boundary segment of a polygon, it can be the boundary       
of at most two polygons.                                                        
  In other words, the polygons must be a unique tessellation of the geographic r
                                                                                
When the segments define polygon boundaries, the partition should contain       
only the segments of the polygons, and the records must contain the names       
of the zones on each side.  Left and right zones are defined by the             
direction implied by the sequence of points in the line.  The zone names        
must correspond to those defined in the zones partition.  The special zone      
name OUTSIDE (left aligned)                                                     
should be used when the line is at the edge of the map, or on                   
the boundary of void areas.                                                     
                                                                                
Line segments (of polygons)                                                     
 must be closed (i.e., the last point in a segment must be the                  
first point of another segment), and segments must not cross or have loops.     
Further, segment must not be repeated.                                          
                                                                                
Segments that are to be used as geographic overlays may have feature codes to   
give a classification e.g. different types of rivers.                           
                                                                                
     Type Record:                                                               
     8        byte      partition header = SEGMENTS                             
                                                                                
     Header Record:                                                             
     10       integer   number of segments                                      
                                                                                
A set of records follows for each segment.                                      
                                                                                
     Definition Record:                                                         
     10       integer   identifying number                                      
     10       byte      name of left zone (if line is part of a zone            
                        boundary)                                               
     10       byte      name of right zone (if line is part of a zone           
                        boundary)                                               
     10       integer   number of points in segment                             
     10       integer   number of feature codes                                 


                                                                      83
                                                                                
     Feature code Records (if required):                                        
     8 x 10  integer    feature codes                                           
                                                                                
     Point Records:                                                             
     8 x 10   real      (X,Y) coordinate pairs (4 per record)                   

  B. 4.10 Points Partitions                                 
          -----------------
 
                                                                                
The partition contains a set of points or sites at which symbols can be         
overlayed on the map.  The site name can be used to apply quantised             
attribute data or used to annotate the points.                                  
                                                                                
Feature codes can define a classification for display as sites.                 
                                                                                
Type Record:                                                                    
     6        byte      partition header = POINTS                               
                                                                                
     Header Record:                                                             
     10       integer   number of points                                        
                                                                                
     Point Records:                                                             
     10       real      X-coordinate value                                      
     10       real      Y-coordinate value                                      
     40       byte      site name or annotation                                 
     10       integer   number of feature codes                                 
                                                                                
     Feature code Records (if required):                                        
     8 x 10  integer    feature codes                                           
                                                                                
Note that only the first 10 characters are used for the site name.              

  B. 4.11 Sample boundaries geographic file DEMOZSEG.DAT    
          ----------------------------------------------
 
Geographic data for zones (e.g. Census districts) are usually brought in as the 
line segments that form the boundaries of the zones.                            
                                                                                
The boundary segments contain the (X,Y) vertices that make up the line and the  
names of the zones on each side of the line.                                    
                                                                                
These data are usually entered using OzEnter, then excessive vertices discarded 
(thinned) using OzData, and then the full zone / polygon/ line segment /        
centroids structure built using OzZone to prepare for display.                  
                                                                                
For example, to extract ZIP code boundaries from USA TIGER files, the left and  
right ZIP codes are extracted from the records and formed into left aligned     
zone names, and the latitude / longitude vertices are also extracted. If the    
left and right zone names are the same the segments are internal to the zone    
and can be ignored.                                                             
                                                                                
The following illustrates the standard format used to enter such data. Note     
that the MAP partition is required but that the extent need not be given.       
                                                                                
EXAMPLE ZONE BOUNDARY SEGMENTS THAT CAN BE BUILT INTO ZONES - DEMOZSEG.DAT      
MAP                                                                             


                                                                      84
  0.0       0.0       0.0       0.0                                             
         0                                                                      
SEGMENTS                                                                        
        10                                                                      
       107ZONE 1    OUTSIDE            2                                        
102.00    503.00    114.00    503.00                                            
       125ZONE 2    ZONE 1             2                                        
102.00    503.00    110.00    513.00                                            
       143ZONE 1    ZONE 3             2                                        
114.00    503.00    110.00    513.00                                            
       161ZONE 3    OUTSIDE            6                                        
114.00    503.00    115.00    505.00    116.00    507.00    117.00    509.00    
118.00    511.00    119.00    513.00                                            
       187ZONE 2    ZONE 3             2                                        
110.00    513.00    119.00    513.00                                            
       205ZONE 2    OUTSIDE            4                                        
119.00    513.00    114.00    518.00    109.00    517.00    104.00    516.00    
       227ZONE 2    OUTSIDE            2                                        
104.00    516.00    110.00    513.00                                            
       245SURPLUS   SURPLUS            2                                        
119.00    513.00    122.00    506.00                                            
       263OUTSIDE   ZONE 2             2                                        
103.00    509.00    110.00    513.00                                            
       281OUTSIDE   ZONE 2             2                                        
102.00    503.00    103.00    509.00                                            

  B. 4.12 Sample geographic file DEMOZONES.DAT              
          ------------------------------------
 
The full topological geographic structure can be entered (although in practise  
this is seldom available).                                                      
                                                                                
COMMENT LINE FOR TEST DATA     - DEMOZONE.DAT                                   
MAP                                                                             
102.00    122.00    502.00    518.00                                            
         0                                                                      
ZONES                                                                           
         3                                                                      
ZONE 1             1                                                            
       352                                                                      
ZONE 2             2                                                            
       377       402                                                            
ZONE 3             1                                                            
       327                                                                      
POLYGONS                                                                        
         4                                                                      
       327ZONE 3             3         0                                        
110.00    119.00    503.00    513.00    114.00    510.00                        
       187      -161       143                                                  
       352ZONE 1             3         0                                        
102.00    114.00    503.00    513.00    108.00    506.00                        
      -125       107       143                                                  
       377ZONE 2             3         0                                        
102.00    110.00    503.00    513.00    104.00    508.00                        
      -263      -281       125                                                  
       402ZONE 2             3         0                                        
104.00    119.00    513.00    518.00    110.00    515.00                        
       205       227       187                                                  


                                                                      85
SEGMENTS                                                                        
        10                                                                      
       107ZONE 1    OUTSIDE            2                                        
102.00    503.00    114.00    503.00                                            
       125ZONE 2    ZONE 1             2                                        
102.00    503.00    110.00    513.00                                            
       143ZONE 1    ZONE 3             2                                        
114.00    503.00    110.00    513.00                                            
       161ZONE 3    OUTSIDE            6                                        
114.00    503.00    115.00    505.00    116.00    507.00    117.00    509.00    
118.00    511.00    119.00    513.00                                            
       187ZONE 2    ZONE 3             2                                        
110.00    513.00    119.00    513.00                                            
       205ZONE 2    OUTSIDE            4                                        
119.00    513.00    114.00    518.00    109.00    517.00    104.00    516.00    
       227ZONE 2    OUTSIDE            2                                        
104.00    516.00    110.00    513.00                                            
       245SURPLUS   SURPLUS            2                                        
119.00    513.00    122.00    506.00                                            
       263OUTSIDE   ZONE 2             2                                        
103.00    509.00    110.00    513.00                                            
       281OUTSIDE   ZONE 2             2                                        
102.00    503.00    103.00    509.00                                            
                                                                                

  B. 4.13 Sample lines geographic file DEMOLINES.DAT        
          ------------------------------------------
 
A lines structure is used for line data that is to be displayed for attribute   
data:                                                                           
                                                                                
COMMENT LINE FOR TEST DATA       DEMOLINES.DAT                                  
MAP                                                                             
103.50    121.50    503.50    517.50                                            
         0                                                                      
LINES                                                                           
         4                                                                      
ROAD 3             3                                                            
110.50    119.50    503.50    513.50                                            
       187       161       143                                                  
ROAD 1             3                                                            
103.50    114.50    503.50    513.50                                            
       125       107       143                                                  
ROAD 2             3                                                            
103.50    110.50    503.50    513.50                                            
       263       281       125                                                  
ROAD 4             3                                                            
104.50    119.50    513.50    517.50                                            
       205       227       187                                                  
SEGMENTS                                                                        
        10                                                                      
       107ROAD 1    OUTSIDE            2                                        
103.50    503.50    114.50    503.50                                            
       125ROAD 2    ROAD 1             2                                        
103.50    503.50    110.50    513.50                                            
       143ROAD 1    ROAD 3             2                                        
114.50    503.50    110.50    513.50                                            
       161ROAD 3    OUTSIDE            6                                        


                                                                      86
114.50    503.50    115.50    505.50    116.50    507.50    117.50    509.50    
118.50    511.50    119.50    513.50                                            
       187ROAD 2    ROAD 3             2                                        
110.50    513.50    119.50    513.50                                            
       205ROAD 2    OUTSIDE            4                                        
119.50    513.50    114.50    517.50    109.50    517.50    104.50    516.50    
       227ROAD 2    OUTSIDE            2                                        
104.50    516.50    110.50    513.50                                            
       245SURPLUS   SURPLUS            2                                        
119.50    513.50    121.50    506.50                                            
       263OUTSIDE   ROAD 2             2                                        
103.50    509.50    110.50    513.50                                            
       281OUTSIDE   ROAD 2             2                                        
103.50    503.50    103.50    509.50                                            

  B. 4.14 Sample points geographic file DEMOPOINT.DAT       
          -------------------------------------------
 
Points files just give the (X,Y) locations and a site name / label.             
                                                                                
These files can be used with an attribute file for mapping site data or can be  
used to place sysmols or labels at locations (overlays).                        
                                                                                
COMMENT LINE FOR TEST DATA     - DEMOPOINT.DAT                                  
MAP                                                                             
102.00    122.00    502.00    518.00                                            
         0                                                                      
POINTS                                                                          
         3                                                                      
114.0     503.0     PNT1                                                        
104.0     516.0     PNT2                                                        
114.0     518.0     PNT3                                                        
                                                                                

  B. 5 Format of polygon geographic files                
      ----------------------------------
 

  B. 5. 1 Standard (not implemented)                        
          --------------------------
 
                                                                                
Geographic data are often available in polygon format, and this data            
definition enables it to be used used with OzGIS.                               
                                                                                
The common line segments on the boundaries of adjacement polygons are           
effectively defined twice in polygon data; OzGIS assumes that they are          
exactly the same.  The polygon boundary must not cross itself.                  
                                                                                
Each polygon has a name, which is the name of the zone to which it belongs.     
                                                                                
Polygons may occur inside other polygons.  Where the polygon is not part of     
a zone (e.g. a lake) it may be given the name OUTSIDE.  The level field         
defines lakes, islands within lakes etc.  When maps are generated on            
devices using polygon fill the level gives the order of display so the          
polygons will overwrite correctly.                                              
                                                                                
                                                                                


                                                                      87
Comment record:                                                                 
                                                                                
     80      byte       comment describing the data                             
                                                                                
Definition Record:                                                              
     10      integer    map projection code                                     
     10      integer    zone type (optional)                                    
                                                                                
Each polygon is defined by a set of records:                                    
                                                                                
Polygon header:                                                                 
     10      byte       zone name, usually left justified, blank filled         
                        or OUTSIDE if an internal polygon.                      
     10      integer    number of points in the line                            
     10      real       level of polygon for hardcopy generation using          
                        polygon fill 0=standard, 1=lakes, etc.                  
                                                                                
Centroid record:                                                                
     2x10    real       centroid or labelling point (X,Y) in polygon            
                                                                                
Point records:                                                                  
     8x10    real       (X,Y) coordinate pairs (4 per record) The last          
                        point must be the same as the first.                    
                                                                                

  B. 5. 2 Simple Format (SAS) Zone Files                    
          ------------------------------
 
                                                                                
Simple format files are in common use by the SAS system and other packages      
providing SAS interfaces.  Polygon for lakes etc. should follow standard        
polygons to provide the correct display order for overwriting.                  
                                                                                
   Header   Record                                                              
                                                                                
     80      byte       Comment                                                 
                                                                                
Each data record has the form                                                   
     10      byte       zone name                                               
     10      real       X coordinate                                            
     10      real       Y coordinate                                            
     10      integer    Polygon number within zone                              

  B. 5. 3 Sample simple zones data file DEMOSASG.DAT        
          ------------------------------------------
 
SAS FORMAT GEOGRAPHIC DATA - DEMOSAS.DAT                                        
SQUARE        3.0       5.0                                                     
SQUARE        7.0       5.0                                                     
SQUARE        7.0       10.0                                                    
SQUARE        3.0       10.0                                                    
DIAMOND       8.0       8.0                                                     
DIAMOND       10.0      5.0                                                     
DIAMOND       12.0      8.0                                                     
DIAMOND       10.0      11.0                                                    
TRIANGLE      13.0      5.0                                                     
TRIANGLE      16.0      10.0                                                    
TRIANGLE      19.0      5.0                                                     


                                                                      88
TRIANGLE      13.0      2.0            2                                        
TRIANGLE      15.0      2.0            2                                        
TRIANGLE      14.0      4.0            2                                        
SQUARE        4.0       0.0            2                                        
SQUARE        8.0       0.0            2                                        
SQUARE        8.0       4.0            2                                        
SQUARE        4.0       4.0            2                                        
SQUARE        0.0       0.0            2                                        
SQUARE        5.0       1.0            2                                        
SQUARE        5.0       3.0            2                                        
SQUARE        7.0       3.0            2                                        
SQUARE        7.0       1.0            2                                        
OUTSIDE       15.0      6.0            2                                        
OUTSIDE       15.0      7.0            2                                        
OUTSIDE       17.0      7.0            2                                        
OUTSIDE       17.0      6.0            2                                        
TOP           4.0       8.0                                                     
TOP           19.0      8.0                                                     
TOP           19.0      9.0                                                     
TOP           4.0       9.0                                                     

  B. 6 GIS / standard geographic file formats            
      --------------------------------------
 

  B. 6. 1 DIME format                                       
          -----------
 
This format is supported, but has not had much use. The data are primarily 2    
point segments, so is inefficient on storage.                                   
                                                                                
Note that only 499 2 point segments can be handled.                             
                                                                                
The data are usually passed through OzZone to build polygons and then through   
OzData to join up the segments into ones of decent length.                      
                                                                                
The data are long Ascii records, and look something like:                       
                                                                                
XX91609160012583                       1                                        
  MANUEL              ST                       8    8      201   299   200      
   29891600000011 14502 1450219711197119160       38  440195019510003016     234
  10003016     213   1818                        396750 757476396740            
7574760610215040685606098370406849                                              
  MANUEL              ST                       8    8      301   359   300      
  35891600000029 14502 1450219711197119160       44  480195019510003016     233 
  10003016     212   1818                        396740 757476396730            
7574760609837040684906095020406848                                              
  MANUEL              ST                       8    8      361   399   360      
  39891600000037 14502 1450219711197119160       48  540195019510003016     233 
  10003016     233   1818                        396730 757476396718            
7574760609502040684806090470406846                                              
  SCHOOL              ST                       9    9      900   998   901      
   99991600000045 162   162  19720197209160       37  220200020010003031     107
  10003031     108   1818                        396611 755737396619            
7557430605026045580006053140455632                                              
  SCHOOL              ST                       9    9     1000  1098  1001      
  109991600000052 162   162  19720197209160       22  140200020010003031     115
  10003031     115   1818                        396619 755743396624            


                                                                      89
7557460605314045563206054910455542                                              

  B. 6. 2 DLG optional 3 format                             
          ---------------------
 
The DLG-3 format is the major interchange format in use, and data can be obtaine
from many mapping agencies e.g. from USGS.                                      
                                                                                
The data differs in concept from the usual data displayed by OzGIS in that it   
is preclassified by the assignment of numeric "feature codes".                  
                                                                                
All identifiers are numbers. These are converted to names by adding prefixes.   
Point names are POINT + 5 digit number, zone names are AREA + 6 digit zero      
filled number e.g.                                                              
                                                                                
AREA000001                                                                      
AREA000630                                                                      
POINT00004                                                                      
POINT00234                                                                      
                                                                                
The data entry process processed the lines only. Any line with one vertice or   
two vertices and the same node numbers is taken as a point.                     
                                                                                
Other lines are output with the left and right names set to the area names.     
Left and right area numbers of zero or one are taken to be outside the map.     
                                                                                
Feature codes are stored as numbers (combined input pairs) for lines, points    
and zones e.g. '291  22' becomes 2910022.                                       
                                                                                
The first area is ignored as it should be the boundary of the map.              
                                                                                
Polygons are generated by passing the geographic file through the OzZone        
program.  This carries the area feature codes through to the polygons, retains  
the line segments, and forms a points segment that contains the centroids of    
the polygons.                                                                   
                                                                                
Note that file must have 80 character fixed length records.                     
                                                                                
Some test files are supplied for Hawaii.  These were read off the USGS GeoDATA  
CD ROM on a SUN system, and 'newline' characters inserted to form 80 character  
records.  The files had to be editted as an arbitrary polygon was given as      
outside the map as the left and right areas on the line (this could also be     
handled during display by specifying feature codes).                            
                                                                                
The test files are:                                                             
                                                                                
HAWDLGWB - water boundaries i.e. the islands                                    
HAWDLGWB - administrative boundaries                                            
HAWDLGRD - roads                                                                
HAWDLGST - streams                                                              
                                                                                
The data format is described in the US Geological Survey Circular 895-c         
"USGS Digital Cartographic Data Standards, Digital Line Graphs"                 
                                                                                
The files look like:                                                            
                                                                                
USGS-NMD  DLG DATA - CHARACTER FORMAT - 09-29-82 VERSION s21_wb.dlg             
HAWAIIAN ISLANDS POLY 10 DROPPED        1967, 1980  2000000.                    


                                                                      90
                                                                                
     3     3  9999     2 0.50800000000D+02     4     0     4     1              
   0.637820640000000D+07   0.676865799729109D-02   0.800000000000000D+07        
   0.180000000000000D+08  -0.157000000000000D+09   0.300000000000000D+07        
   0.0                     0.0                     0.0                          
   0.0                     0.0                     0.0                          
   0.0                     0.0                     0.0                          
 0.10000000000D+01 0.0               0.0               0.0                      
SW       19.000000 -160.000000        -316386.41  1771715.66                    
NW       22.000000 -160.000000        -312489.03  2102112.53                    
NE       22.000000 -155.000000         208312.61  2101093.98                    
SE       19.000000 -155.000000         210917.63  1770684.40                    
WATER BODIES           0    74    74 010    12    12 010    70    70   1        
N    1  -316386.41  1771715.66           0           0     0                    
N    2  -312489.03  2102112.53           0           0     0                    
N    3   208312.61  2101093.98           0           0     0                    
N    4   210917.63  1770684.40           0           0     0                    
.                                                                               
.                                                                               
.                                                                               
.                                                                               
N   74  -320966.08  2105481.92           2           0     0                    
   -69    70                                                                    
A    1   -68438.87  1949336.24           3     0     1     0     0              
     8     9     7                                                              
     0     0                                                                    
A    2  -327997.34  2094827.63           3     0     1     0     0              
   -10    -2    -1                                                              
    40   150                                                                    
.                                                                               
.                                                                               
.                                                                               
.                                                                               
A   13   -91708.84  2025480.45           3     0     1     0     0              
   -66   -65   -67                                                              
    40   150                                                                    
L    1     7     6     2     0                24     1     0                    
  -332906.23  2078428.77  -332805.62  2077920.57  -331991.53  2078579.38        
  -332446.45  2079748.67  -331479.96  2080407.19  -331224.96  2080914.69        
  -331578.38  2082032.98  -331221.19  2082845.09  -330100.11  2084620.90        
  -329235.22  2085279.61  -328573.03  2086192.72  -328571.24  2087107.12        
  -327247.56  2088577.74  -325977.26  2088727.66  -325164.16  2088878.47        
  -324909.37  2089284.37  -324503.57  2088978.78  -323182.17  2089280.99        
  -322319.07  2089025.30  -321707.68  2089938.51  -321250.68  2089836.02        
  -320995.88  2090241.92  -319775.79  2090696.74  -318961.20  2091609.55        
   290  4000                                                                    
.                                                                               
.                                                                               
.                                                                               
.                                                                               
L   70    74    66    11     0                 2     1     0                    
  -320966.08  2105481.92  -321422.78  2105736.82                                
   290  4002                                                                    


                                                                      91

  B. 6. 3 Gina format                                       
          -----------
 
The standard interchange format for GeoVision GIS is Gina.                      
                                                                                
OzEnter processes some of the file. Feature codes must be numeric. Zone names   
generated are of the form ZONE12345 and site names are of the form POINT12345.  
                                                                                
Only boundary lines and points are output - OzZone has to be used to generate   
the zones / polygons.                                                           
                                                                                
The sample file DEMOGINA.DAT is as follows:                                     
                                                                                
udb-start b v 8192                                                              
                                                                                
udb-header 0.5 fred-db "Fred's test database"                                   
descr      29oct85 14:32:10 example GINA files                                  
coord-sys  rect  feet                                                           
extent -12000, -8000,  12000, 8000                                              
layer 1 base        "base information layer"                                    
layer 2 roads       "roads and streets layer"                                   
layer 3 hydro       "hydrographic layer (rivers, streams etc)"                  
layer 4 telephone   "telephone plant layer"                                     
layer 5 lots        "property lots layer"                                       
                                                                                
network 1 emergency l 2 "emergency routes"                                      
network 2 property  p 5 "property polygon network"                              
                                                                                
udb-primary                                                                     
table road free                                                                 
field name        char 40   i n   "road name"                                   
field r_type      char 12   i n   "type of road, arterial, highway etc"         
field lanes       num  2,0        "maximum number of lanes"                     
field surface     char 10   n     "type of surface"                             
fc   1000, 1099                                                                 
table house free                                                                
field h_type      char 10   n     "house type: bungalow;""test quotes""  etc"   
field lot_no      num 10    i     "lot number"                                  
fc   1130,  1139                                                                
table lots free                                                                 
field lot_no      num  10   i u n "lot number"                                  
field address_no  num  6,0  i n                                                 
field street      char 40   n     "street name"                                 
fc   1100                                                                       
                                                                                
                                                                                
udb-feature                                                                     
feat 1  1002 2 0 l xy 0 0 0 1 0                                                 
coor 1805 1120 1805 1143                                                        
coor 2018 1143 2018 1204 2508 1204                                              
text "Elm Street"                                                               
attr Elm suburban 2 "asphalt"                                                   
feat 2  1004 2 0 l xy 0 0 0 1 0                                                 
coor 2508 1204 2508 820                                                         
text "Oak Street"                                                               
attr Oak arterial 4 "concrete"                                                  


                                                                      92
feat 3  1400 5 2 l xy                                                           
coor 2508 903 2508 933                                                          
feat 4  1400 5 2 l xy                                                           
coor 2508 933 2568 933                                                          
feat 5  1400 5 2 l xy                                                           
coor 2568 933 2568 903                                                          
feat 6  1400 5 2 l xy                                                           
coor 2508 903 2568 903                                                          
feat 7  1400 5 2 l xy                                                           
coor 2508 873 2508 903                                                          
feat 8  1400 5 2 l xy                                                           
coor 2568 903 2568 873                                                          
feat 9  1400 5 2 l xy                                                           
coor 2508 873 2568 873                                                          
feat 20  1100 5 2 p xy                                                          
coor 2520 920                                                                   
attr  10875,  104 Oak                                                           
feat 21  1133 5 0 l xy                                                          
coor 2530  920                                                                  
attr 2-story  10875                                                             
feat 22  1100 5 2 p xy                                                          
coor 2520  890                                                                  
attr 10874,  106 Oak                                                            
feat 23  1133 5 0 l xy                                                          
coor  2530 890                                                                  
attr bungalow 10874                                                             
                                                                                
udb-polygon                                                                     
poly 3 20 r e                                                                   
poly 4 20 r e                                                                   
poly 6 20 l e                                                                   
poly 5 20 r e                                                                   
poly 6 22 r e                                                                   
poly 8 22 r e                                                                   
poly 9 22 l e                                                                   
poly 7 22 r e                                                                   
                                                                                
udb-indirect                                                                    
table road_types free                                                           
field r_type    char 12 i u n  "road type"                                      
field maint     char 2         "maintenance class"                              
field resp_code char 3  n      "responsibility code"                            
attr highway    m3  A-4                                                         
attr aterial    m6  B-3                                                         
attr secondary  n2  B-1                                                         
attr suburban   s4  B-8                                                         
                                                                                
                                                                                
udb-indirect                                                                    
table house_types  free                                                         
field h_type    char 10  i u n "house  types"                                   
field tax_code  char 4   n     "taxation code"                                  
attr bungalow  10-5                                                             
attr 2-story   12-2                                                             
attr split     11-5                                                             
                                                                                
udb-end                                                                         


                                                                      93

  B. 6. 4 ANSII standard                                    
          --------------
 
The new standard format for interchange will be supported when test data become 
available.                                                                      

  B. 6. 5 SIF format (not available)                        
          --------------------------
 
SIF format will be supported if there is a demand.                              
Data files appear to be 80 character ascii files.                               
                                                                                
The files contain a series of commands that define how the coordinates are to be
displayed.                                                                      
                                                                                
Most of the commands are ignored.                                               
                                                                                
The commands of value seem to be:                                               
                                                                                
DID/ is the first record in the file, and gives some basic information. The     
parameter MO=2 or MO=3 gives the number of dimensions (compulsory?). Any Z value
is ignored.                                                                     
                                                                                
OVR/   defines the active level. This is stored in the relations as a number    
column 'ovr' as it seems to  be  effectively a layer.                           
                                                                                
ASC/ggnum defines the graphic group number, and is used to  form the entid of   
form SIFggnum.                                                                  
                                                                                
If ggnum is 0 the item is ignored (not appended).                               
                                                                                
If ggnum is <0 a number is assigned to it (sequentially starting at 10001).     
                                                                                
LST/xx, defines a line. There are 2-101 vertices in a record. If a record has   
101 values and the next record starts with the same point as the end point it is
taken to be a continuation. (actually found some records with more than 101)    
                                                                                
LST/ and LST/OP are line strings.                                               
                                                                                
LST/HO and LST/SO are polygons (solid & holes)                                  
                                                                                
Vertices are (x,y) or (x,y,z) according to the DID/ header.                     
                                                                                
New records that are not continuations are taken to be new components.          
                                                                                
                                                                                

  B. 6. 6 DXF format (not available)                        
          --------------------------
 
DXF format will be supported if there is a demand.                              
                                                                                


                                                                      94

  B. 7 Format of names files                             
      ---------------------
 
                                                                                
Names files give lists of zones, lines or sites which are to be used to         
restrict certain kinds of processing in OzGIS.                                  
                                                                                
The file would usually be prepared with a text editor, possibly operating       
on a file output from OzGIS.                                                    
                                                                                
     Comment Record:                                                            
     80       byte      comment describing the data                             
                                                                                
     Name Records (one per zone or line or site)                                
     10       byte      name                                                    
                                                                                

  B. 7. 1 Sample names file DEMOATTR.DAT                    
          ------------------------------
 
DEMONAMES.DAT - NAMES FILE                                                      
ZONE 1                                                                          
ZONE 2                                                                          
ZONE 4                                                                          
                                                                                

  B. 8 Format of colour names files (Removed from system)
      --------------------------------------------------
 
                                                                                
Colour names files are usually generated within OzGIS, but they may be          
entered as data files. The file X11-BGR is supplied.                            
                                                                                
Comment record:                                                                 
     80      byte       comment describing the file                             
                                                                                
Colour records:                                                                 
     40      byte       colour name (in ascending order)                        
     10      real       blue value, range 0.0 to 1.0                            
     10      real       green value, range 0.0. to 1.0                          
     10      real       red value, range 0.0 to 1.0                             
                                                                                
The demonstration file DEMOCOLNM.DAT looks like:                                
                                                                                
DEMO COLOUR NAMES FILE                                                          
aquamarine                                   .8314    1.0000     .4980          
blue                                        1.0000     .0000     .0000          
brown                                        .1647     .1647     .6471          
darkseagreen                                 .5608     .7373     .5608          
hotpink                                      .7059     .4118    1.0000          
lemonchiffon                                 .8039     .9804    1.0000          
lightskyblue                                 .9804     .8078     .5294          
mintcream                                    .9804    1.0000     .9608          
pink                                         .7961     .7529    1.0000          
purple                                       .9412     .1255     .6275          
royalblue                                    .8824     .4118     .2549          


                                                                      95
salmon                                       .4471     .5020     .9804          
steelblue                                    .7059     .5098     .2745          
turquoise                                    .8157     .8784     .2510          
yellowgreen                                  .1961     .8039     .6039          
                                                                                

  B. 9 Format of combine files                           
      -----------------------
 
                                                                                
Combine files define new map zones in terms of zones in a base map, or site     
catchments in terms of percentages of base zones.                               
                                                                                
Comment record:                                                                 
     80      byte       comment describing the file                             
                                                                                
Header record:                                                                  
     10      integer    number of items defined                                 
                                                                                
                                                                                
Sets of records follow for the items:                                           
                                                                                
Item definition record:                                                         
     10      byte       name (ascending order)                                  
     10      integer    number of zones                                         
                                                                                
Zone records:                                                                   
     10      byte       zone name (ascending order)                             
     10      real       proportion of zone in area (0 to 1.0)                   
                                                                                
                                                                                

  B. 9. 1 Sample combine file DEMOCOMB.DAT                  
          --------------------------------
 
This file defines three territories AREA1, AREA2, AREA3 in terms of base zones  
A, B, ......                                                                    
                                                                                
3 AREAS                                                                         
         3TEST AREAS                                                            
AREA1              1                                                            
H             1.0                                                               
AREA2              3                                                            
N             1.0                                                               
O             1.0                                                               
R             1.0                                                               
AREA3              5                                                            
A             1.0                                                               
B             1.0                                                               
C             1.0                                                               
D             1.0                                                               
E             1.0                                                               

  B.10 Format of presentation files                      
      ----------------------------
 
                                                                                
Presentation files give a set of saved map files that are to be referenced      


                                                                      96
by menu items so the maps can be easily displayed when giving demonstrations.   
                                                                                
     First record:                                                              
                                                                                
     60      byte       menu header                                             
                                                                                
A pair of records is given for each saved display file                          
     60      byte       menu item text                                          
     50      byte       saved map file in full form                             
                                                                                

  B.10. 1 Sample presentation file                          
          ------------------------
 
AURISA Exhibition                                                               
Far East Asia zone map                                                          
DEMOFEA.SAV                                                                     
Lowe Electorate bivariate zone map                                              
BIVLOWE.SAV                                                                     
Diagram map                                                                     
DIAG1.SAV                                                                       
Zones & Sites map                                                               
ZONESITE.SAV                                                                    
Australia Statistical Division zones map                                        
DEMOOZ.SAV                                                                      
Canberra LGAs zone map with overlays                                            
ACT.SAV                                                                         

  B.11 Format of marker files                            
      ----------------------
 
                                                                                
Markers are displayed in OzGIS as single polygons using polygon fill.           
                                                                                
OzGIS has standard files available (star, triangle etc.) but a user can         
define additional ones.                                                         
                                                                                
A marker is a single closed polygon.  OzGIS requires that the points that       
define the polygon lie within a circle of unit diameter.                        
                                                                                
The data points are usually prepared by drawing the marker on graph paper,      
centred on the origin, and lying within a circle of radius 0.5.                 
                                                                                
     Comment record:                                                            
                                                                                
     80      byte       marker name, comments                                   
                                                                                
     Header record:                                                             
                                                                                
     10      integer    number of points (3-100)                                
                                                                                
     Boundary record:                                                           
                                                                                
     8x10    real       Polygon points (X,Y) 4 per record                       
                        Values are in the range (-0.5 to +0.5)  The last        
                        point must be the same as the first                     
                                                                                


                                                                      97

  B.11. 1 Sample marker file SQUARE.DAT                     
          -----------------------------
 
SQUARE.DAT - MARKER                                                             
         5                                                                      
-0.35     -0.35     -0.35     0.35      0.35      0.35      0.35      -0.35     
-0.35     -0.35                                                                 

  B.12 Format of device files                            
      ----------------------
 
                                                                                
Device files describe the characteristics of graphics display devices and set   
colours etc.                                                                    
                                                                                
Standard files are usually held on the system for all devices available. Users  
would not usually define their own.                                             
                                                                                
 OzGIS was designed to operate as a highly interactive colour mapping system    
where speed of display was obtained by the use of an  advanced raster display   
system.                                                                         
                                                                                
 The software can operate on most graphics devices, but there could be loss of  
speed and capabilities depending on the characteristics of the devices being    
used.                                                                           
                                                                                
 OzGIS is based on graphics packages with the functionality of the GKS graphic  
standard. These graphic packages provide graphic primitives such as lines,      
text, and filled polygons. An important feature of GKS is that it is device     
independent so the package allows OzGIS to produce maps on a large range of     
devices.                                                                        
                                                                                
 Every device available for use with OzGIS has at least one file associated with
it.                                                                             
                                                                                
All devices within OzGIS have the same characteristics so e.g. a map previewed  
on a display device can be output directly to a hard-copy device. The files     
ensure that a device with limited capabilities can  simulate the required       
capabilities in the best way.                                                   
                                                                                
 The device files also set GKS primitive attributes such as colours and zone    
fill types. A colour display system has several files available that provide    
standard sets of colours for maps. Files with similar colours are usually       
available for different devices for hard-copy generation.                       
                                                                                
The easiest way to generate device data files is to edit standard ones.         
                                                                                
The device files require colours to be specified in blue,green,red. One way to  
decide on these values is to look at the definitions in the colour names data   
file \ozgis\x11-bgr.dat.                                                        
                                                                                
Hardcopy device files are based on the SCIPLOT package which has a fixed set of 
colours. Of course plotter colours depend on the pens. SCIPLOT colours are:     
     Black                                                                      
     Blue                                                                       
     Green                                                                      


                                                                      98
     Cyan                                                                       
     Red                                                                        
     Magenta                                                                    
     Brown                                                                      
     Light Gray                                                                 
     Dark Gray                                                                  
     Light Blue                                                                 
     Light Green                                                                
     Light Cyan                                                                 
     Light Red                                                                  
     Light Magenta                                                              
     Yellow                                                                     
     White                                                                      
                                                                                
                                                                                
                                                                                
     Comment record:                                                            
                                                                                
     80      byte       Device description                                      
                                                                                
                                                                                
     Size record:                                                               
                                                                                
     10      real       Extent of device surface                                
     Note: defines units used for all sizes in data i.e. divide by this         
     10      real       width of device in device units (now set fromOZGIS.IN)  
     10      real       max address height of device    (now set fromOZGIS.IN)  
                                                                                
     Type record:                                                               
                                                                                
     10      integer    GKS workstation number                                  
     10      integer    Display type, 1 = raster display, pixel addressed       
                                      2 = continuous coordinates                
     10      integer    Fill type, 1 = solid colour                             
                                   2 = pattern                                  
                                   3 = hatch                                    
     10      integer    Locator device number, 0 = none, 1 = default            
                                               2 = crosshairs                   
                                                                                
     Advanced Raster Record  (now set fromOZGIS.IN)                             
                                                                                
     10      integer    number of bit planes (1-24)                             
     10      integer    length of LUT (1-4096)                                  
     10      integer    number of pixels across screen (256-4096)               
     10      integer    number of lines on screen (256-4096)                    
     10      integer    run-length encoding/decoding, 0 = not available         
                                                                                
     Colour definition record:                                                  
                                                                                
     10      integer    number of colours defined                               
                                                                                
     Colour table records:                                                      
                                                                                
     10      real       blue value (0.0 - 1.0) for colour table                 
     10      real       green                                                   
     10      real       red                                                     
                                                                                
     Hatch definition record:                                                   


                                                                      99
                                                                                
     10      integer    number of hatch patterns (0 - 256)                      
                                                                                
     Hatch records (if required):                                               
                                                                                
     10      integer    line number (1 - 8)                                     
                        (from overlay and quant. lines)                         
     10      real       line angles (0.0 - 180.0)                               
     10      real       line separation  (<0.1)                                 
     10      integer    line number (0 - 4) , 0 = not used                      
     10      real       second line angle (if reqd)                             
     10      real       second line separation (if reqd)                        
                                                                                
The rest of the data records set internal tables for GKS primitive              
attributes.  Most records reference the colour table; the index has range 1     
to length of table.                                                             
                                                                                
                                                                                
A style table is used with the colour table for polygon fill according to       
the fill type.                                                                  
                                                                                
-  SOLID - the colour is used, style not relevant                               
-  HATCH - the pen colour is obtained from the colour table, the hatch          
           pattern number from the style table                                  
-  PATTERN - the colour table is not used, the style table gives the device     
             dependent pattern number                                           
                                                                                
Area Fill records:                                                              
                                                                                
10   integer            colour index                                            
10   integer            fill or style index                                     
                                                                                
Several fill records are required, in following order:                          
                                                                                
-  background. NOTE also the menu / messages/ everything colour                 
-  zone missing data                                                            
-  excluded zones                                                               
-  diagram background                                                           
-  line or site quantisation legend and diagram                                 
-  8 polygon underlay records                                                   
                                                                                
Text records:                                                                   
                                                                                
10   integer            colour index                                            
10   integer            font number  (1-9)                                      
10   integer            text precision 0=STRING, 1=CHAR, 2=STROKE               
10   real               height of character space (pixels)                      
10   real               width of character space  (pixels)                      
                                                                                
Note:  on display devices hardware text of known size will be used.             
Fonts are available for use on the screen, but are more usually used for output 
on plotters.                                                                    
                                                                                
The following fonts are available:                                              
                                                                                
1 VGA/EGA hardware font or default hardcopy font                                
2 Simplex Roman, the most basic                                                 
3 Duplex Roman, more detailed than the simplex with about twice as many strokes 


                                                                     100
4 Complex Roman, similar but with more tapered segments                         
5 Triplex Roman, heavier version                                                
6 Simplex script, based on handwriting                                          
7 Complex script                                                                
8 Complex italic italic version of complex roman                                
9 Triplex italic                                                                
                                                                                
The text records are:                                                           
                                                                                
4 records to define the text available for name overlays at sites or typed      
in text.                                                                        
The text is usually defined in increasing size order.                           
                                                                                
Legend text record:  This is fixed size text used for generation of all the     
legends.  The size is very important as it governs the overall size of the      
legend e.g. the zone legend boxes are 3 times the text height in height, 2      
times the text width in width.                                                  
                                                                                
Attribute description text record:  This is normally large text.  The           
interactive system has to be able to clear it off for each attribute so it      
should be fixed size hardware text in that case.  When two variates are         
displayed the two descriptions are separated by                                 
 a 'VS' or 'AND' generated using the                                            
legend text.                                                                    
                                                                                
                                                                                
Line records:                                                                   
                                                                                
10   integer            colour index                                            
10   integer            GKS type (1-4)                                          
                        1 = solid, 2 = dashed, 3 = dotted, 4 = dash dot         
                                                                                
The actual records are as follows:                                              
                                                                                
4 records for lines to be used for line overlays.                               
                                                                                
4 records for lines to be used for quantised lines (line-type has no            
meaning here as types are assigned according to quantisation).                  
                                                                                
Note that these first 8 records also define the hatching                        
plotter 'pens' if applicable.                                                   
                                                                                
A record to define zone boundaries line.                                        
                                                                                
A record to define the line used to draw axes on diagrams (should be            
solid).                                                                         
                                                                                
A record to define the line used to draw statistical values on diagrams.        
                                                                                
Marker records:                                                                 
                                                                                
10     integer     colour index                                                 
10     integer     fill style index                                             
10     real        marker height (and width)                                    
40     byte        marker file name, left aligned, system format                
                                                                                
The records are as follows:                                                     
                                                                                


                                                                     101
4 records for markers to be used as overlays at sites.                          
                                                                                
4 records for markers used for sites with quantised attribute data (marker      
size has no meaning, is set for class).                                         
                                                                                
1 record for site marker background  (currently not used)                       
                                                                                
1 record for scatter diagram (GKS marker no 1)                                  
                                                                                
Colour Sequence records (170 records):                                          
                                                                                
10     integer  colour index                                                    
10     integer  style index                                                     
                                                                                
These records give sequences of colours (or patterns) or hatching for           
colouring zones after quantisation.                                             
                                                                                
There are two types of sequence:                                                
                                                                                
-  a 121 value array for single variate zones followed by                       
-  a 7x7 array for bivariate                                                    
                                                                                
                                                                                
The class fill is found by sampling out of the sequence for the number of       
classes, e.g. for bivariate                                                     
                                                                                
2 classes         1        7                                                    
3 classes         1   4    7                                                    
4 classes         1  3  5  7                                                    
                                                                                
Similarly, the single variate 121 value array allows exact sampling for         
number of classes 2-7; a best choice is made for 8,9 or 10 classes.  In the     
special case of pseudo-continuous colour maps the whole 121 values are          
used.                                                                           
                                                                                
Menu colour records                                                             
                                                                                
10 integer background text number (0-7)                                         
10 integer foreground text number (0-7)                                         
                                                                                
The menu colours are:                                                           
                                                                                
1 main menus                                                                    
2 lists                                                                         
3 help messages                                                                 
4 input of values                                                               
5 error messages                                                                
                                                                                
The 5 menu records use internal text numbers                                    
                                                                                
Note:  Files for advanced raster display systems with long LUT's should be      
set up as follows:                                                              
                                                                                
-  Display type = 1                                                             
-  Fill type = 1                                                                
-  LUT length 256 or greater                                                    
-  One LUT colour for each record in the data file i.e. all colour index        
   values unique                                                                


                                                                     102
                                                                                
The system by passes the colour index and style index when operating in         
fast interactive code and accesses the LUT directly.                            


                                                                     103
                     C. GLOSSARY OF TERMS                                 
                       =================
 
The purpose of this Appendix is to provide definitions for a number of          
terms used within this Guide.  Most of these terms are commonly used words      
or phrases which have taken on a more precise technical meaning in one of       
the areas spanned by the OzGIS system.  Technical terms have been               
borrowed from the jargon of statistics, data processing, computer software      
and hardware, cartography, and graphic arts.  Because of the diversity of       
these disciplines, it is unlikely that a potential OzGIS user will have         
developed a level of expertise in each.  This glossary should provide most      
of the information necessary for communicating the basic concepts of            
OzGIS.                                                                          
                                                                                
The glossary is available on-line, and is accessed by typing 'G' to a menu      
selection request.                                                              
                                                                                
Area - 1) A measurement of the size of a geographical region whose shape is     
   displayed on the OzGIS monitor.  2) An arbitrary portion of the face         
   of the monitor.                                                              
                                                                                
Attribute - A general term for the variable associated with a set of            
   geographic zones, lines or sites to be processed by OzGIS.                   
   Attributes may be variates, statistics or simply data collected for each     
   item.  Note that the modes of display for an attribute are usually           
   referred to as "single variate" or "bi-variate".  See also Variate and       
   Statistic.                                                                   
                                                                                
Background - The informationless area displayed on the monitor around a map     
   and its associated components.  Usually given a user selected, neutral       
   colour such as black or white.                                               
                                                                                
Bit - A unit of information representing the value (either 1 or 0) of a         
   single binary digit.                                                         
                                                                                
Bivariate - A display of the relative distribution of two different sets        
   of statistics on the same map.  It must be noted that no relationship        
   between the two statistics is implied by the display.  For example, if       
   the distribution of little old ladies is displayed simultaneously with       
   the distribution of cricket players, the result is not a display of the      
   distribution of little old ladies who play cricket.  See also Variate.       
                                                                                
Boundary - A set of lines displayed on the monitor to represent the edges       
   of polygons defined to the system.  Often the same as zone edges.            
                                                                                
Byte - A group of eight bits.  See also Bit.                                    
                                                                                
Catchment - The region of influence around a site e.g. suburbs around a         
   shopping centre where most of the customers live.                            
                                                                                
                                                                                
Character - A single symbolic pattern which may be displayed on either the      
   monitor or terminal.  It may be alphabetic, numeric, or punctuational,       
   as the normal symbols encountered on a typical typewriter keyboard, or a     
   special symbol generated for display as an entity, such as a square root     
   symbol.                                                                      
                                                                                


                                                                     104
Choropleth Map - A map portraying the values of an attribute averaged over      
   data collection units (or zones) and represented by a symbol covering        
   the entire unit.  A map displayed by OzGIS represents the zones by a         
   uniform colour.                                                              
                                                                                
Class - A convenient subdivision of the total range of values of a              
   particular statistical variate.  Classes are usually chosen to make          
   computations or analyses less labourious, or to make the results of such     
   analyses more obvious or meaningful.  For example, the range of a set of     
   values might be divided into ten equal classes in order to highlight         
   items in the top ten percent.  See also Variate, Class Boundary, Class       
   Interval and Class Number.                                                   
                                                                                
Class Boundary - The special values of variates which determine the upper       
   and lower limits of the range of a class.  See also Class.                   
                                                                                
Class Interval - The range of variate values between the upper and lower        
   limits of the class.  See also Class.                                        
                                                                                
Class Number - A cardinal number assigned to each class into which a            
   particular statistical range has been divided.  Conventionally, the          
   class whose members have the lowest magnitude is assigned number 1, with     
   class numbers increasing uniformly as the magnitude of class values          
   increases.  See also Class.                                                  
                                                                                
Colour - One of the combinations of blue, green, and red which may be           
   specified for display on the monitor.  The total number of colours           
   available depends on the display system.                                     
                                                                                
Colour Space - The range of colours which may be specified for display on       
   the colour monitor.  Since the colours are specified as values of blue,      
   green, and red, it is convenient to think of the colour space as a cube      
   located on a standard three dimensional coordinate system.  Black is         
   placed at the origin, with each of the x, y and z axes representing          
   blue, green, and red, respectively.  The range of possible values is 0.0     
   to 1.0 on each axis of the cube.                                             
                                                                                
Continuous Colour - A method of representating statistical values               
   associated with map zones by graduating zone colours to correspond with      
   changes in statistical value.  From a user defined, or default, sequence     
   of colours, OzGIS generates the intermediate colours to provide a            
   12 colour graduated path through the colour space.  The statistic to be      
   represented is quantized into 12 equal value classes, and the classes        
   are assigned colours from the generated colour sequence.  This allows        
   small changes in statistical value to be represented by subtle changes       
   in colour, while large changes in value may be visually observed as          
   significant colour differences.                                              
                                                                                
                                                                                
Controller - A general term applied to a piece of intermediate equipment in     
   the data path between the electrical signals of a processor and their        
   physical realization in a peripheral device.  Within OzGIS, the term         
   will most often be used for the Color Display Controller.                    
   It will be used to a lesser extent to describe interface controllers for     
   the various disc and tape drives.                                            
                                                                                
Coordinate - One of a pair of numbers which designates the location of a        
   geographic point with respect to another known point.  Geographic files      


                                                                     105
   for entry into the system under OzGIS must have their points                 
   specified in appropriately scaled and formatted coordinates.  The            
   coordinates specified by the user are converted by OzGIS for display         
   on the monitor.  On the monitor screen, the origin is in the lower left      
   hand corner of the viewing area.  The coordinates of a point on the          
   monitor screen are specified by their distance right and up from the         
   origin                                                                       
                                                                                
Crosshair Cursor - A pair of lines at right angles to each other which is       
   displayed on the monitor to designate the location of a certain point of     
   interest.  Under most circumstances, the location of the crosshair           
   cursor may be controlled by movements of the mouse.  See also Box            
   Cursor, and Joystick.                                                        
                                                                                
Data - Numerical values associated with certain physical phenomena, such as     
   128 cm long, 14 years old, or 43 kangaroos.  As a generality,                
   OzGIS was not designed to handle data, but rather the statistics             
   derived from data, such as average length, medium age, or number of          
   kangaroos per hectare.  See also Statistics.                                 
                                                                                
Decile - One of the nine data values which divide the range of a variate        
   into ten equal sized classes.  See also Quantile and Percentile.             
                                                                                
Default - A set of parameters automatically selected by OzGIS in the            
   absence of any stated preference by the user.  The actual default            
   parameters may be defined by the user in the users default file.  For        
   example, OzGIS may initially display a map by arbitrarily selecting          
   zone colours from a palette of possible shades which the user selected       
   previously.  After this default colouring, the user may wish to change       
   some particular zone colour to improve the appearance of the display.        
                                                                                
Disc - An electronic device for storing digital data on a rotating plate        
   coated with magnetic material.  See also Controller.                         
                                                                                
Display - As a verb, the act of presenting information on the monitor or        
   terminal for the purpose of visually communicating that information to       
   the user.  This includes all the procedures necessary to correctly           
   present the information in a format suitable for both the equipment and      
   the viewer.  Example:  "A map is displayed on the monitor, while a menu      
   is displayed on the terminal".                                               
                                                                                
                                                                                
   As a noun, the presentation which is visually perceived when a user          
   looks at the screen of the monitor or terminal;  the total information       
   content on the screen.  Examples:  "The terminal display indicates the       
   options possible now";  "This map display is too red".  See also Monitor     
   and Terminal.                                                                
                                                                                
Display Elements - The components or items of a display on the OzGIS            
   monitor;  for example, legend, title, image map, boundaries, image           
   symbols, histograms.                                                         
                                                                                
Distribution - The manner in which a number of samples of data are spread       
   across the range of possible values.  May be a subjective statement,         
   such as:  "These data appear to have an even distribution".  More often,     
   some quantifiable measure will be given such as:  "These data have a         
   normal distribution with a mean of 40 and standard deviation of 3".          
   Sometimes, distribution information will be presented in graphical form,     


                                                                     106
   such as a histogram or scatter diagram.                                      
                                                                                
Equal Value Quantization - A method of dividing the range of values of a        
   statistical variate into a number of classes where the magnitude of the      
   range of each class is the same.  See also Class.                            
                                                                                
Excluded Zone - A zone displayed on the map and coloured with a special         
   shade indicating that it has not been used for quantization or has been      
   omitted from the area of interest.                                           
                                                                                
File - A number of data items grouped together and considered as a unit for     
   convenience of storage and retrieval by a computer.  Within OzGIS,           
   such files are stored as distinct entities on disk.  Files are               
   identified by media designation, name, and type.  The OzGIS user             
   normally supplies only the file name, but the storage media may also be      
   specified.  The file type is supplied by the system.  The same name may      
   be used for files of different types, but within a particular type, no       
   two files may have the same name.                                            
                                                                                
Frequency - A statistical term referring to the number of members of a          
   population falling into a specified class.  See also Class.                  
                                                                                
Geographic Data - Digitized map data which are referenced to a geographic       
   (or spatial) coordinate system, usually a map projection.                    
                                                                                
Graphics - Data which can be displayed on the monitor in terms of lines         
   points and text, as opposed to colouring and filling regions of the          
   screen.  Used to refer to geographic and symbol data.                        
                                                                                
Histogram - A type of bar graph in which vertical rectangles are erected on     
   the horizontal axis with the height of each bar representing the             
   frequency, and the width representing the corresponding class interval,      
   for each of the classes of a particular variate.  OzGIS can display          
   such statistical information on the monitor.  See also Scatter Diagram,      
   and Class.                                                                   
                                                                                
                                                                                
Information - The subjective knowledge which may be associated with an          
   objective set of data.  The ages and locations of children are data;         
   the distribution of school age children is statistic;  where the schools     
   should be built is information.  See also Data and Statistics.               
                                                                                
Interval - The numerical distance between the upper and lower limits of a       
   class.                                                                       
                                                                                
Joystick - An electro-mechanical device which converts the positions of a       
   small lever into electrical voltages.  The voltages are further              
   converted into digital signals which are used by the PDP11 to                
   position various cursor patterns on the monitor screen.  See also Box        
   Cursor, and Crosshair Cursor.                                                
                                                                                
Legend - A display on the monitor which indicates the correspondence            
   between the statistical values and their associated colours or symbols       
   as defined for a particular map.  The legend usually occupies                
   approximately the rightmost one fifth of the viewing area of the monitor     
   and has two general forms, single variate and bivariate.  One type of        
   single variate legend consists of a column of coloured rectangles beside     
   which are numbers indicating the corresponding class boundaries for          


                                                                     107
   those colours.  The other is a rectangular column with colours gradually     
   changing from top to bottom, and an upper and lower number indicating        
   the range across which the "Continous Colour" varies.  The bivariate         
   legend consists of a 45 degree parallelogram divided left to right and       
   up and down into coloured smaller parallelograms.  A set of numbers          
   along the left side indicates the class boundaries of the primary            
   variate, while similar numbers across the upper side indicate the            
   secondary variate class boundaries.                                          
                                                                                
Line - This term has three special meanings within OzGIS in addition to         
   its normal English usage.  (1) Any set of contiguous segments comprising     
   the section of a zone boundary which has one zone on its right and a         
   second zone on its left as part of a map.  (2) Any contiguous set of         
   segments as part of a graphics display.  (3) A set of alpha-numeric          
   characters meant to be displayed as one row on either the monitor or the     
   terminal.                                                                    
                                                                                
Location - The position of a datum point, or pixel, on the monitor screen.      
   This is given by its x and y coordinates, with the origin in the lower       
   left hand corner.  The range of values depends on the display system.        
                                                                                
Lookup Table (LUT) - A table in the display system which can modify the         
   value in memory for display purposes.                                        
                                                                                
Map - Geographic data which can be displayed on the monitor by colouring        
   and filling regions of the screen or as lines or symbols.                    
                                                                                
Map Projection - Refers to the coordinate system used for processing the        
   display of a map.                                                            
                                                                                
                                                                                
Markers - Special characters or symbols which may be displayed on the           
   monitor to identify locations of points.  For example, aircraft              
   symbols to indicate the location of airports.  Different sized markers       
   are used to show the classification of site attribute data.                  
                                                                                
Mean - The arithmetic average of a set of data values.                          
                                                                                
Memory - A portion of the OzGIS hardware used for the storage of data           
   by the altering of the electrical state of the appropriate circuitry.        
                                                                                
Menu - An itemized list of alternative actions which might be selected          
   within OzGIS.  Menus are displayed on the terminal.  The terminal            
   keyboard is used to enter selections from the options listed on the          
   menu.  The sequence of menu items which is selected controls the "flow"      
   of the OzGIS program through its various tasks.                              
                                                                                
Monitor - The electronic equipment, resembling a colour television              
   receiver, on which maps and graphics are displayed.                          
                                                                                
Nested Means - A quantization method in which classes are generated by          
   dividing each variate range into two classes about the mean for that         
   range.  For example, the central class limit is set at the overall mean,     
   then the upper and lower classes are each divided at the means of the        
   two parts, giving four classes.  This process may be repeated, giving        
   eight classes.                                                               
                                                                                
Operating System - Computer software provided to facilitate usage of the        


                                                                     108
   various computer resources available within the OzGIS system.                
                                                                                
Overlay - As a noun, overlay refers to graphic data written on top of the       
   existing display.  This is displayed on the monitor as though placed         
   between the previous display and the viewer.  Overlays generally are         
   entered in the refresh memory in single bit planes.                          
   As a verb, overlay refers to the act of adding graphics data to a            
   display by putting it "on top of" the previous display.                      
                                                                                
Palette - An array of coloured rectangles which is displayed on the monitor     
   at certain stages of OzGIS.  The palette shows a range of colours            
   which are available for selection by the user.  Palettes are held as         
   files within OzGIS.  Several palette files are provided as part of           
   the software package.                                                        
                                                                                
Parameter - A general term referring to a physical characteristic which may     
   be measured or quantified in some way, even though the precise value of      
   that measurement may be unknown in specific instances.  For example, age     
   is a parameter of human beings.                                              
                                                                                
Percentile - One of the set of 99 values which divide the range of a            
   statistic into 100 equal sized classes.                                      
                                                                                
Peripherals - Items of auxillary equipment added to a computer to enhance       
   its performance.  These include such items as disc drives, tape drives,      
   and printers.                                                                
                                                                                
                                                                                
Pixel - The smallest, individually controllable, element (or cell)              
   displayed as dots of colour on the monitor's screen.  The monitor area       
   is made up of lines of pixels.  For each pixel, there is a corresponding     
   location in the refresh memory for storing the data value associated         
   with that pixel.  This location is the smallest datum area which can be      
   individually controlled by the software.  See also Image and Location.       
                                                                                
Point - A geographic feature which, for display purposes, may be described      
   by only indicating its location as an x and y coordinate.                    
                                                                                
Polygon - A geographic area described by the line segments forming its          
   boundary and the zone name which forms its surface.  One or more             
   polygons may be combined to form a zone.                                     
                                                                                
Presentation Maps - A set of maps prepared for rapid display on the             
   monitor.                                                                     
                                                                                
Primary Variate - The set of statistical values characterized by a common       
   name which is displayed on any given single variate map.  Two such sets      
   of values are displayed on a bivariate map.  The primary variate is          
   named at the top of the title, and its colour values are indicated in        
   the rows of the legend.  See also Variate.                                   
                                                                                
Processor - The hardware which executes the procedural and computational        
   tasks specified by OzGIS.  The standard OzGIS processor is a                 
   Digital Equipment Corporation minicomputer, the VAX.                         
                                                                                
 Projection - The representation of a physical shape on the screen of the       
   monitor according to a fixed mathematical coordinate system.  Normally,      
   a projection in OzGIS terms will refer to a method for presenting            


                                                                     109
   maps of geographic areas.  See also Map Projection.                          
                                                                                
Quantile - Any of the specific values which divide the range of a statistic     
   into equal sized classes.  Some values have other special terms, i.e.,       
   if the range is divided into four classes, the boundary values are           
   called quartiles.  See also Percentile.                                      
                                                                                
Quantify - To assign a number or quantity to an otherwise unnumbered            
   entity.  In particular, to assign a class number to a statistical value      
   or zone name.                                                                
                                                                                
Quantization - The process of assigning class numbers to zones according to     
   the value of the statistic for that zone.  Viewed the other way,             
   quantization is the process of putting zones into classes.                   
                                                                                
Quartile - One of the three data values which divide the range of a variate     
   into four equal sized classes.  See also Quantile and Percentile.            
                                                                                
Raster - a term applied to image data.  In particular data handled on a         
   line basis.                                                                  
                                                                                
                                                                                
Refresh Memory - The portion of the hardware (within the display                
   controller) which holds the digital data necessary to continuously           
   regenerate the colour monitor display.  The cathode ray tube (CRT) of        
   the monitor produces its display by electrically stimulating various         
   phosphorus based compounds deposited on its face.  The colours thus          
   produced fade rapidly with time and must be continually "refreshed".         
   The data necessary to perform this refresh correctly is stored in the        
   refresh memory.                                                              
                                                                                
Region - A designated portion of a map displayed on the monitor.  A region      
   consists of one or more zones or parts of zones defined in some way          
   (e.g. a circular region centered at a point on the map).  The concept of     
   a region is important when the displayed map consists of several             
   geographic areas.  In this context, a region consists of a window            
   (geographic area) and its displayed viewport on the screen (screen           
   area).  See also Area.                                                       
                                                                                
Save - To store on disc (or magnetic tape) all the pertinent data regarding     
   a map displayed on the monitor.  The maps which are "saved" can later be     
   fully regenerated with all details preserved.                                
                                                                                
Scatter Diagram - A two dimensional plot of points whose x and y                
   coordinates are the values of the individual variates associated with        
   those points.  Scatter diagrams are displayed on the monitor in              
   conjunction with bivariate maps.  In this instance, each map zone is         
   assigned a point on the diagram.  The y-coordinate of the point              
   corresponds to the value of the primary variate for that zone as             
   displayed on the map.  The x-coordinate of the point has a similar           
   relationship to the secondary variate.  In addition, the point will be       
   coloured the same as its associated map zone.  Scatter diagrams provide      
   a visual method of assessing the correlation between the two variates        
   displayed on the map.                                                        
                                                                                
Secondary Variate - The second set of statistical values which are              
   displayed (along with a primary variate) on the map.  The                    
   secondary variate is named at the bottom of the title.  See also Primary     


                                                                     110
   Variate.                                                                     
                                                                                
Segment - A set of connected straight lines defined to OzGIS by                 
   specifying the coordinates of their starting, intermediate, and end          
   points, along with the names of the two zones on either side of the          
   lines.  Consequently, segments must represent a portion, or all, of the      
   boundary between two zones.  See also Line and Boundary.                     
                                                                                
Site - A geographic location that has associated attribute data.  A site is     
   defined by a name and fixed location e.g. a site could be a city or a        
   retail store.                                                                
                                                                                
Standard Deviation - A statistical measure of the dispersion amongst a set      
   of measured values.  The standard deviation is mathematically equivalent     
   to the positive square root of the variance of the sample on which the       
   statistic is based.                                                          
                                                                                
                                                                                
Statistics - A general term referring to:  1) The branch of mathematics         
   involved with performing certain analytical calculations regarding           
   various relationships among sets of numerical data, and 2) The numerical     
   results of such calculations.  The height of an individual is data;  the     
   average height of a group is a statistic.                                    
                                                                                
Status - The present condition of the software and hardware system,             
   especially as to its progress toward the completion of the tasks at          
   hand.  The status messages are displayed as a response to                    
   typing interpretation of various abbreviated messages displayed on the       
   terminal.  The status messages are displayed as a response to typing an      
   "S" command.                                                                 
                                                                                
Terminal - An item of hardware comprising a keyboard for entering commands      
   to the processor, and some means for the processor to return                 
   alpha-numeric messages to the user.  The standard OzGIS terminal is          
   the Digital Equipment Corporation VT100.  This contains the necessary        
   keyboard, and a cathode ray tube for displaying processor generated          
   messages.  Some OzGIS installations may also have a printer terminal         
   for providing a permanent copy of the messages on paper.                     
                                                                                
Territory - a zone which has been formed by amalgamating bas zones e.g. sales   
   territories formed from postcodes.                                           
                                                                                
Text - Combinations of characters which may be specified by typing at the       
   terminal.  Lines of text may be displayed on either the terminal or the      
   monitor in various fonts.  See also Character, and Line.                     
                                                                                
Time Lapse Maps - A formatted set of maps concerning a geographic area and      
   certain statistics associated with it as they have been collected over       
   time.  Time lapse files are used to display the time related changes in      
   the statistical data by rapid and periodic changes in map colours            
   corresponding to the statistics.  For example, variations in population      
   density, as recorded by the 1971, 1976, and 1981 census data, could be       
   shown by changing the colours of the displayed map at one second             
   intervals corresponding to the 3 sets of data.                               
                                                                                
User - The person who is interactively controlling the OzGIS system at          
   the terminal.                                                                
                                                                                


                                                                     111
Value - The number associated with a particular statistical item, as            
   opposed to the colour associated with that item.  For example, the zone      
   might be coloured red to indicate four to ten beer drinkers per pub in       
   that zone.  The actual value of the statistic might be 9.4 beer drinkers     
   per pub.                                                                     
                                                                                
Variate - A measurable quantity which may take on any of the values within      
   a given range, and which has associated with it a specified probability      
   function describing the manner in which the permissible values are           
   likely to occur.  See also Bivariate, Primary Variate, and Secondary         
   Variate.                                                                     
                                                                                
Viewport - The rectangular area of the colour monitor face selected for         
   displaying a specified item.                                                 
                                                                                
Window - The rectangular portion of a geographic map which is selected for      
   display on the colour monitor.                                               
                                                                                
                                                                                
Zone - A geographic area which is to be considered as a spatial unit.  A        
   zone is defined in terms of one or more polygons which form it.              
   Statistically, a zone is defined in terms of a single value for each         
   variate in question.  This relationship of one variate value per defined     
   geographic zone allows zones to be completely and uniformly coloured in      
   a map display.  See also Polygon and Variate.                                
                                                                                
Zone Name - An alphanumeric designation attached to the various                 
   computerized data associated with a zone.  The zone name facilitates for     
   the processor the task of relating various data items to the proper          
   zones.                                                                       


                                                                     112
                     D. SYSTEM LIMITS                                     
                       =============
 
The OzGIS system has a standard set of limits to various maximum counts. These  
correspond to array sizes.                                                      
                                                                                
The limited memory on the PC makes these limits quite small.                    
                                                                                
                                                                                
The standard limits are:-                                                       
                                                                                
500   max no displayed zones+sites+lines                                        
500   max no values in attribute file (zones,sites,lines)                       
10    max no map regions                                                        
10    max no quantised zone geog files                                          
10    max no quantised site geog files                                          
10    max no quantised line geog files                                          
10    max no line overlays                                                      
10    max no polygon underlays                                                  
10    max no marker overlays                                                    
10    max no name overlays                                                      
20    max no test strings displayed                                             
50    max no polygons in a zone                                                 
499   max no segments in a polygon                                              
100   max no segments in a line                                                 
256   max no vertices in a segment                                              
500   max no points in a fast display polygon                                   
1000  max no zones per item in a combine file                                   
256   max length of display system LUT                                          
2000  max no vertices in foreign segments data file                             
5000  max no zones that can be built from line segments                         


                                                                     113
                     E. TROUBLE-SHOOTING                                  
                       ================
 
Many of the Oz programs use most of available memory in the 640K. If you have   
other programs loaded they man not run. This will often show up as errors when  
opening files.                                                                  
                                                                                
If you have trouble displaying maps then you probably have not configured the   
system properly. If you are using a super VGA get the system working in standard
VGA mode first. Generally check the \ozgis\interact.ini file for the DISPLAY    
parameter for the monitor type (usually 10). Super VGA modes need the correct   
startup register values to be set. Edit the interact.ini file and throw away    
irrelevant parts.                                                               
                                                                                
If you have trouble with the mouse in super VGA mode you may need the C         
parameter on the end of the mode command in the interact.ini file. Ensure that  
there are no comments following the C parameter. There have also been problems  
with incompatible mouse drivers; microsoft and Genius drivers are known to work.
The mouse driver must be called MOUSE.COM.                                      
                                                                                
If you have trouble with menus reload the \ozgis\ozgis.men file. This file      
defines all the menus and actions and is constantly rewritten. A hardware error 
could corrupt the file.                                                         
                                                                                
Check the osgis.out file after problems to see if there are any error messages. 
                                                                                
GIS data (digitised data) are often incorrect. This can cause problems with     
polygon display e.g. if zone boundaries cross themselves, and during zone       
building. Your data supplier probably wont be of much help. Try windowing into  
the part of the map with problems to isolate it and use the debug option to     
print values. You will have to patch the data files with a word processor.      
                                                                                
Rebooting the system while the OzGIS programs are running can cause "loss" of   
disk space. This can be recovered using CHKDSK.                                 


                                                                     114
                     F. OzGIS REFERENCES                                  
                       ================
 
                                                                                
O'CALLAGHAN, J.F., SIMONS, L. and PALMER, J.A.B. (1980).  A prototype           
system for interactive colour mapping.  Proc. URPIS-8 (k. Davies (ed.)),        
Surfers Paradise, pp. 9.1-9.5.                                                  
                                                                                
SIMONS, L., O'CALLAGHAN, J.F. and PAINE, T. (1982).  COLOURMAP - an             
interactive colour mapping workstation.  Proc. DECUS (Digital Equipment         
Computer Users Society), Melbourne, Vol. 10, pp.1501-1504.                      
                                                                                
O'CALLAGHAN J.F., and SIMONS, L.W.J. (1983) COLOURMAP: An Interactive           
Colour Mapping System. Proc. First Australasian Conference on Computer          
Graphics, Sydney.                                                               
                                                                                
O'CALLAGHAN J.F., and SIMONS, L.W.J. (1984).   Map Display Techniques for       
Interactive Colour Mapping.                                                     
                                                                                
Henzell, O'Callaghan. A Sequential Line Simplification Algorithm based on       
Equivalent Height. CSIRONET Technical Report, May 1980                          
                                                                                
Robertson, O'Callaghan. The Generation of Colour Sequences for Univariate and   
Bivariate Mapping. IEEE Computer Graphics and Applications, February 1986.      
                                                                                
Gerald Evenden. Cartographic Projection Procedures for the UNIX Environment - A 
User's Manual. USGS open-file report 90-284.                                    
                                                                                
General Mapping References                                                      
                                                                                
J Sibert, 'Continuous-colour Choropleth Maps', Geo-Processing, (1980)           
207-216.                                                                        
                                                                                
'The Harvard Library of Computer Graphics Mapping Collection', Harvard          
University.                                                                     
                                                                                
E Giamottic and P Puliafits, 'An Interactive Spatial Information System: A      
Tool for Regional Planning'; Proc IFIP 79.                                      
                                                                                
J Dalton et al, 'Interactive Colour Map Displays of Domestic Information',      
Proc SIGGRAPH 79, Computer Graphics, Vol 13 No 2 ACM/SiGGRAPH.                  
                                                                                
A Robinson et al, 'Elements of Cartography', Wiley 1978.                        
                                                                                
                                                                                
D Des Jardins, 'Multi-Level Statistical Maps in Graphic Communication',         
Proc NCGA, Anaheim 1982.                                                        


                                                                     115
                     G. OTHER SPATIAL SOFTWARE                            
                       ======================
 

  G. 1 Background                                        
      ----------
 
 Geismar Holdings has been involved with the development of several other       
systems with the Commonwealth Scientific and Industrial Research Organisation,  
Division of Information Technology. CSIRO is the major Australian government    
research organisation.                                                          
                                                                                
These systems are based on the latest hardware and software technolgy, and      
typically run on Unix workstation (e.g. SUN SPARC), are written in C or C++ and 
use commercial relational database systems (e.g. Oracle, INGRES).               
                                                                                
Several systems developed at CSIRO Division of Information Technology are now   
being maintained and marketed by Australian Companies. Geismar provides         
contract programming services to CSIRO and to a company selling the systems,    
CLOUGH Engineering (Systems Division).                                          
                                                                                
We do not market these systems, but can arrange for information to be sent.     
                                                                                

  G. 2 SIRO-DBMS Spatial Information in a Relational DBMS
      --------------------------------------------------
 
                                                                                
SIRO-DBMS is a spatial database tool-kit for databases in the fields of         
Geographic Information Systems, Land Information Systems and Facilities         
Information Systems.  It offers high performance for queries involving          
selection by location, full integration of spatial and other corporate          
information, support for distributed database and a simple data model for       
spatial databases built on the relational data model.                           
                                                                                
The system is of particular interest to Spatial Information System software     
developers.                                                                     
                                                                                
SIRO-DBMS is built as a shell around off-the-shelf relational database          
management systems (rdbms) and uses the rdbms solely for both graphic and       
attribute information.  No changes to the rdbms are required and the full rdbms 
facilities remain available for use on tables interpreted by SIRO-DBMS as       
describing spatial entities.  This provides for full integration of the spatial 
database with other corporate databases.                                        
                                                                                
The data model allows the geometric definitions of objects to be described as a 
point, a rectangle, a line, a chain, a ring, a polygon (simple or complex) etc  
in agreement with the ANSII standard on data interchange.  Linkages enable      
hierarchies of components (e.g. points into chains into polygons). Other        
attributes for entities can be described using the full set of data types       
provided by the host rdbms.  Several options are available for the internal     
representation of the geometry of objects, to allow database to be designed to  
best satisfy the particular requirements of the task in hand.                   
                                                                                
The core operations are append, retrieve, delete and update.                    
                                                                                
Spatial operations available are minimum-bounding-rectangle, intersection,      


                                                                     116
enclosure, crossing, connection, within-buffer and adjacency.                   
                                                                                
Good performance is provided by spatial indexing, a specialist form of indexing 
for retrieval of objects by their location, implemented using the standard      
rdbms indexing facilities.  Tests on a 1 Mip system show response times of 0.5  
seconds (elapsed) to retrieve an average of 7 points from a set of 230000       
points by windowing and response times of under 2 seconds (elapsed) to retrieve 
5 polygons from a set of 300000 polygons.                                       
                                                                                
Distribution of a SIRO-DBMS Spatial Database is achieved using the distributed  
database tools in the host rdbms.  Further support is provided by the SIRO-DBMS 
'class' facility, which allows a spatial data set to be distributed on regional 
computers with SIRO-DBMS accessing only relevant partitions of the data set.    
                                                                                
SIRO-DBMS has been implemented in the C programming language.  It has been      
ported to several UNIX workstations, including SUN, HP and PC systems. Versions 
are available that use ORACLE, INGRES and INFORMIX as the kernel rdbms, although
any other rdbms with SQL and with host language interfaces are potentially      
suitable.  SIRO-DBMS is being used within the Centre for Spatial Information    
Systems for development of Geographic Information Systems.                      
                                                                                

  G. 3 DISIMP Image Processing                           
      -----------------------
 
                                                                                
Processing and analysis of spatial data has become increasingly important in    
areas such as land resource management, mapping, mineral exploration,           
agriculture and oceanography. Previously, comprehensive, flexible and           
functional high performance image processing and analysis systems have not been 
available. This gap has been bridged by an extensive suite of image processing  
software, DISIMP, developed by The Centre for Spatial Information Systems of    
the CSIRO's Division of Information Technology.                                 
                                                                                
Featuring a sophisticated, icon-based user interface, DISIMP is an ideal tool   
for any application involving restoration, analysis, enhancement and display of 
digital images. DISIMP is now available on a growing range of computer systems, 
which can be networked together to provide a flexible and expandable            
distributed image processing workstation environment .                          
                                                                                
DISIMP has comprehensive facilities for processing digital images from many     
different sources. The full integration of graphics with support for geographic 
projections, provides GIS functionality. Imaging facilities include image       
restoration and enhancement, geometric and intensity transformations,           
statistical analysis and interactive colour image display.  Special facilities  
are provided in DISIMP for analyzing multi-spectral images from the Landsat,    
SPOT and NOAA satellites and for integrating these images with related data     
involving topographic, geophysical and cultural properties.  The main           
applications for DISIMP have therefore been in the analysis of remotely sensed  
data and in image-based geographic data processing.                             
                                                                                
The modular and flexible design of DISIMP allows system builders to extend its  
capabilities and to develop additional utilities as required for specific       
applications.  The design provides an excellent base for the development of     
production-oriented systems for specific applications, and allows DISIMP to be  
configured as part of turnkey systems for image processing.                     
                                                                                
DISIMP has recently been released for the workstation/Unix environment and is   


                                                                     117
available for SUN/SPARC and HP systems with various image displays.  The        
software supports multi-host configurations of distributed workstations linked  
into a host environment with tape and large scale storage facilities.  DISIMP   
also supports a wide range of peripherals, including digitizers, interactive    
image display systems and hardcopy devices.                                     
                                                                                
DISIMP is being installed in a growing number of user sites, including Federal  
and State government departments, universities, mineral exploration companies   
in Australia. It is also in use in research, government and commercial groups   
overseas.                                                                       
                                                                                
 Software Functions and Organisation                                            
 Version 4.1 of the software was released in 1988 and contains more than 125    
utilities.  Version 4.1 supports the Apollo DN3000 and DN4000 workstations with 
a Truevision VISTA display.  Version 5.0 runs on the SUN / SPARC under Xwindows 
in 8-bit mode on the standard screen or in 24-bit mode with a RasterOps card.   
The software is written in standard FORTRAN 77, but some low level routines for 
bit manipulation and file access are provided in assembler (or C on UNIX        
systems) to improve operational performance.                                    
                                                                                
A menu-driven interface to the utilities has been implemented to assist users   
unfamiliar with the capabilities of the packages and their utilities.  A modern 
icon-based interface to control the interactive image has been developed for    
bit-map graphics workstations.                                                  
                                                                                
                                                                                
Special Features of DISIMP                                                      
                                                                                
DISIMP is in demand as a general package for image processing applications      
and as a base for further development.                                          
                                                                                
Generalised image representation                                                
 . device independence:  handles images on various devices (disc,               
        magnetic, tape, display system, etc.) in a uniform way                  
 . detailed image information in a standard header and in ancillary             
        data records                                                            
 . multi-image and multi-channel files                                          
 . no limit to image dimensions or number of channels                           
 . binary, packed, integer, floating point and complex intensity                
        data formats                                                            
 . geocoding for geographically-referenced data                                 
 . special encoding for physically-based data                                   
                                                                                
Flexible image transfer                                                         
 . user-defined image windowing and viewporting                                 
 . variable expansion and sampling of images                                    
 . intensity scaling and clipping                                               
 . pixel aspect ratio correction                                                
 . null value handling                                                          
 . error checking and reporting                                                 
                                                                                
                                                                                
Advanced image processing                                                       
 . generalised image correction, registration and rectification                 
 . integration of graphic and tabular data                                      
 . generalised image/graphic handling                                           
 . support for a range of geographic map projections                            
 . fast three-dimensional transformations                                       


                                                                     118
       (relief shading, perspective, shadowing and stereo views)                
 . colour space transformations based on human perception theory                
 . colour display calibration and modelling for colour consistency              
 . realistic scene synthesis:  coloured surfaces and transparencies             
                                                                                
User-accessible subroutine libraries for                                        
 . image and file handling                                                      
 . programming interactive applications                                         
 . general image processing                                                     
                                                                                
Extensive user support                                                          
 . on-line help messages                                                        
 . menu-driven interface to utilities                                           
 . comprehensive documentation and training                                     
 . comprehensive support and maintenance                                        
                                                                                
Details of the packages are documented in various publications:                 
                                                                                
       DISIMP Users' Guide                                                      
       DISIMP Utilities Reference Manual                                        
       DISIMP Programmers' Guide                                                
       -Part 1 Image Processing Base                                            
       -Part 2 Common Display Interface                                         
       -Part 3 File Formats and File Access                                     
       DISIMP System Reference Manual                                           
       Software Application Notes (series)                                      
       Utility Users' Guide (series)                                            
       DISIMP Release Notes                                                     
                                                                                
 A two-day course has been developed for training users at DISIMP sites, and is 
offered as part of the installation procedure.  Users and collaborators are     
welcome to spend time working with the Project Team in Canberra.                
                                                                                
A User's Meeting is hosted regularly by the Project Team to discuss the         
priorities for support activities and to exchange experiences at user sites.    
                                                                                

  G. 4 ITA Interactive Location and Territory Planning   
      -----------------------------------------------
 
                                                                                
ITA is a decision-support system designed to facilitate the solution of         
location and territory planning problems.  Applications include location        
planning for warehouses, schools, fire stations, and retail stores; electoral   
reapportionment; and definition of administrative districts and sales           
territories.  Areas under consideration for further development include         
transportation network analysis and demand modelling for marketing              
applications.                                                                   
                                                                                
The emphasis on solving problems distinguishes ITA both from the                
general-purpose geographic information systems and from specialized predictive  
modelling packages.  ITA is designed to run on a graphics workstation, which    
provides the basis for an easy, intuitively direct style of dialogue between    
the system and its users.  No special knowledge of computing is needed for      
effective use of the system:  most operations are invoked simply by using a     
mouse to select items from menus.                                               
                                                                                
Both automated and manual plan-making techniques are provided.  The manual      


                                                                     119
techniques allow users of the system to make or modify plans directly, using a  
mouse to select and assign objects on the workstation's graphical display       
monitor.  The automated techniques are heuristic optimization procedures,       
capable of addressing requirements such as efficiency in terms of               
transportation costs, compactness in the shape of territories, restrictions on  
territory size, connectivity constraints, and scope restrictions.               
                                                                                
To enhance a planner's understanding of a problem or situation in its           
geographical context, the plan-making procedures are closely integrated with a  
number of powerful display techniques, based primarily on the use of maps.      
These include functions such as zooming and panning, chloropleth display of     
spatially referenced attribute data, geographical    attribute data,            
geographical inquiry, and attribute data summaries.  ITA also provides          
facilities for producing hard-copy output, in the form of printed reports and   
plotted maps.                                                                   
                                                                                
All the data used by the system is stored and managed in a relational database. 
The database for collaborative projects in Australia is set up in terms of the  
Census Collector Districts and other geographical entities defined by the       
Australian Bureau of Statistics (ABS).  The ABS has provided most of the        
spatially referenced data used in these projects, and the cartographic          
components of the database have been obtained from the Australian Survey and    
Land Information Group.  A database administrator's utility program called      
ITA-ADMIN simplifies management of the database and allows ITA users to         
introduce data from sources other than those mentioned above.                   
                                                                                
The primary version of ITA is currently based on the DECstation colour graphics 
workstations, with the Ultrix (Unix System V) operating system and X11          
graphics. The software is also available on SUN, HP Apollo and Intergraph       
workstations.                                                                   
                                                                                
                                                                                

  G. 5 CSIRO Division of Information Technology          
      ----------------------------------------
 
                                                                                
The Division of Information Technology was established in 1985 as the result of 
increasing demand for strategic research and development to assist the          
Australian information industries.                                              
                                                                                
The research activities of the Division concentrate on software-related aspects 
of information technology, covering software engineering, information systems   
and computer communications.  The Division has about 70 staff located in        
laboratories in Sydney (headquarters), Melbourne and Canberra.                  
                                                                                
The Division collaborates with other research groups in CSIRO, academic         
institutions and industry.  Consultants from these external groups assist the   
Division in research planning and management.  Joint appointments are also      
being made to focus the research efforts with other institutions, and visitor   
exchange programs are being developed with overseas organisations.              
                                                                                
As an example of its research associations, the Division is affiliated with the 
Centre for Information Sciences Research at the Australian National University, 
and the Canberra Laboratory of the Division is located on the ANU Campus.       
                                                                                
The Division has a number of commercial agreements with industrial partners in  
order to make its research results available to industry and to develop         


                                                                     120
products for local and international markets.  These agreements cover software  
licences, collaborative and contract research, product design and development   
and consultancy.                                                                
                                                                                
The activities of the Divisional research programs are outlined below.          
                                                                                
CENTRE FOR SPATIAL INFORMATION SYSTEMS                                          
                                                                                
The Centre conducts research leading to the design, implementation and          
application of computer based systems for processing geographic and spatially   
referenced data.  The main research topics of the Centre involve key software   
technologies:  expert systems, spatial data bases, image processing, computer   
graphics, spatial analysis, computer mapping and distributed computing.         
Software developed by this research is now being exploited by collaborative     
programs with industry.                                                         
                                                                                
The research is being focussed on the requirements of systems for applications  
including resource and environmental management, atmospheric and oceanographic  
research, mineral exploration, public utilities and sales planning and          
marketing.                                                                      
                                                                                
As an example, a prototype information system is being developed with the CSIRO 
Division of Wildlife and Ecology for monitoring seasonal weather conditions to  
assist the management of pastoral properties in the Australian rangelands.      
                                                                                
The Centre has established several joint research agreements with Australian    
companies for product design and development, with the aim of developing        
Australian products for the international market.  These agreemens are          
supporting research on image processing and graphic techniques in collaboration 
with several other research groups for applications in remote sensing, oil and  
mineral exploration and biological analysis.  An interactive terrain modelling  
package  is currently the subject of commercial negotiation.                    
                                                                                
The Centre is developing spatial inferencing techniques for use in "emergency"  
planning systems, such as required in military command and control and in civil 
emergencies.  The techniques involve "expert system" concepts to detect and     
analyze conflicts for proposed tactical plans, given the constraints of         
personnel, equipment, environmental conditions and threats.  This is a          
collaborative project with the ANU Department of Computer Science, and the      
Applied Research and Development Division of Computer Power.                    
                                                                                
SOFTWARE ENGINEERING                                                            
                                                                                
The program has a broad charter covering many aspects of software technology.   
There are four main projects.                                                   
                                                                                
A collaborative project with the Royal Melbourne Institute of Technology is     
investigating the use of multiple processors ('parallelism') to achieve         
extremely fast computer systems.  The research is concentrating on algorithms,  
programming methodologies and languages to exploit a particular model of        
parallel architecture called "dataflow".  The main applications of this work    
are currently in scientific computing and artificial intelligence.              
                                                                                
Another project is concerned with the development of associative memory         
techniques for high speed table searching and their implementation in hardware. 
 A prototype implementation has been produced in collaboration with the         
University of New South Wales and is now the subject of commercialization.      
Associative memory techniques are key components in information systems and     


                                                                     121
knowledge-based systems.                                                        
                                                                                
The program has considerable expertise in the software engineering of           
knowledge-based (expert) systems, and has used its experience to tackle several 
practical problems such as the re-engineering of the cotton pest management     
system SIRATAC (with CSIRO Division of Plant Industry) and the analysis of the  
results of thyroid assay blood tests (with Garvin Institute of Medical          
Research).  Expert systems are becoming increasingly important for automating   
industrial processes.                                                           
                                                                                
A new project on human-computer interfaces aims to develop techniques to        
provide more effective means of communication between user and computer         
systems.  These techniques will rely heavily on graphical representations and   
will be compatible with the computer technology anticipated in the 1990s.       
                                                                                
COMPUTER COMMUNICATIONS                                                         
                                                                                
Programs in computer communications undertake research on computer networking   
and the development of digital communications services on these networks.  The  
research aims to improve the current computer communications infrastructure in  
the Australian academic and research environment and to assist manufacturers to 
exploit the opportunities presented by the emerging international standards for 
interconnection of different computer systems.                                  
                                                                                
One program is concerned with the development of prototype systems for          
communication services based on the Open System Interconnection (OSI) Reference 
Model, which has been adopted by the International Standards Organization.      
Members of the program participate in the development of standards for          
communications services such as  file transfer, access and management (FTAM),   
electronic directory services and distributed computing, in order to reduce the 
product development time.  Products based on the emerging standards have        
enormous sales potential in the international markets.                          
                                                                                
The program has established an extensive computer environment, with gateways to 
Australian and international networks, for testing products and prototype       
implementations of OSI standards.                                               
                                                                                
Another program is concerned with the specification, validation and             
implementation of protocols which underlie computer communication services.     
This area called "protocol engineering" employs formal software engineering     
techniques and aims to produce more efficient and more reliable implementations 
of complex communications systems.                                              
                                                                                
for further information contact:                                                
                                                                                
The Information Officer,                                                        
CSIRO Div. Information Technology,                                              
GPO Box 664,                                                                    
Canberra 2601,                                                                  
Australia.                                                                      
Fax 06 275 0911                                                                 


                    CONTENTS

  1. OzGIS INTRODUCTION                                              4          
  1. 1 Introduction                                                  4          
  1. 2 Concepts                                                      4          
  1. 3 Environment                                                   5          
  2. SUMMARY                                                         7          
  3. SYSTEM CONFIGURION                                             10          
  3. 1 Introduction                                                 10          
  3. 2  DOS system files                                            10          
  3. 3  Standard EGA and VGA boards                                 10          
  3. 4  Super VGA boards                                            11          
  3. 5 Maths Coprocessor                                            16          
  3. 6 Extra RAM                                                    16          
  3. 7 Hardcopy configuration                                       16          
  3. 8 Plotter setup                                                18          
  3. 9 Mouse                                                        19          
  4. BASIC CHOROPLETH MAPPING EXAMPLE                               20          
  4. 1 OzCensus                                                     20          
  4. 2 Example map                                                  20          
  5. INTERACTIVE USER INTERFACE TO OzGIS                            23          
  5. 1 Menus                                                        23          
  5. 1. 1 Menu format                                               23          
  5. 1. 2 Function keys                                             23          
  5. 1. 3 Stacking selections                                       24          
  5. 2 Questions                                                    24          
  5. 3 Commands                                                     25          
  5. 4 Graphic interaction                                          25          
  5. 5 Pop-up                                                       26          
  5. 6  Print file                                                  26          
  6. OzGIS FILES                                                    27          
  7. DEVICE FILES                                                   30          
  8. OzGIS MAP TYPES                                                32          
  8. 1 Attribute maps                                               32          
  8. 1. 1 Bivariate zones map Example                               32          
  8. 1. 2 Zones & sites Example                                     32          
  8. 1. 3 Geographic (GIS) maps Example                             33          
  8. 1. 4 Diagrams Example                                          34          
  8. 2 Device files                                                 34          
  8. 3 Presentations                                                34          
  8. 4 Time Lapse Display (not available)                           35          
  9. ATTRIBUTE SELECTION                                            36          
  9. 1 Sequentially                                                 36          
  9. 2 By number (position in file)                                 36          
  9. 3 By attribute description                                     36          
  9. 4 By arithmetic operation                                      36          
 10. QUANTISATION                                                   37          
 10. 0. 1 Quantisation Methods                                      37          
 10. 0. 2 Quantisation Ranges                                       39          
 10. 0. 3 Quantisation Lists                                        39          
 11.  DISPLAY CONTROL & MAP DESIGN                                  41          
 11. 0. 1  Map Quantisation Legends                                 41          
 11. 0. 2 Overlays (GIS) legends                                    42          
 11. 0. 3 Other Legends                                             42          
 11. 0. 4 Text                                                      42          
 11. 0. 5 Attribute Diagrams                                        42          
 11. 0. 6 Displayed Colours (removed)                               43          
 12. MAP REGIONS                                                    45          


 12. 0. 1 Regions                                                   45          
 12. 0. 2 Map List                                                  46          
 12. 0. 3 Quantised Zones                                           46          
 12. 0. 4 Quantised lines                                           47          
 12. 0. 5 Quantised sites                                           47          
 12. 0. 6 Line Overlays                                             47          
 12. 0. 7 Polygon underlays                                         47          
 12. 0. 8 Marker Overlays                                           47          
 12. 0. 9 Name Overlays                                             48          
 12. 0.10 Map Modification                                          48          
 13.  MAP ANALYSIS                                                  49          
 13. 0. 1 Map Reports                                               49          
 13. 0. 2 Attribute Data Statistics                                 49          
 13. 0. 3 Map Interrogation                                         49          
 14. OzEnter DATA ENTRY                                             51          
 14. 1 Introduction                                                 51          
 14. 2 Demonstration Files                                          51          
 14. 3 Example geographic and attribute data                        51          
 14. 4 Example device files                                         52          
 14. 5 Marker data files                                            52          
 14. 6 Colour names data (no longer used)                           52          
 15. OzData DATA PREPARATION                                        53          
 15. 1 Attribute Files                                              53          
 15. 2 Geographic Files                                             54          
 15. 3 Palette Files (Removed from system)                          54          
 15. 4 Colour Names Files  (Removed from system)                    55          
 15. 5  Names Files                                                 55          
 15. 6  Output to Data Files                                        55          
 16. OzZone BUILDING ZONES FROM SEGMENTS                            56          
 16. 1 Use                                                          56          
 16. 2 Example                                                      56          
 17. MAP PROJECTIONS (under development)                            58          
 17. 1 Introduction                                                 58          
 17. 2 Precision                                                    58          
 17. 3 Latitude / longitude                                         58          
 17. 4 Projections                                                  58          
 17. 5 Ellipsoids                                                   59          
 18. HARDCOPY MAP PRODUCTION                                        60          
 18. 1 Overview                                                     60          
 18. 2 Device files                                                 60          
 18. 3 VECTOR Program                                               61          
 18. 4 Example                                                      65          
 19. OzTerr                                                         66          
 20. OzCatch (NOT AVAILABLE YET)                                    67          
 20. 1 Introduction                                                 67          
 20. 2  SITE CATCHMENTS                                             67          
  A. DATA SOURCES                                                   70          
  A. 1 Australia                                                    70          
  A. 1. 1 AUSLIG data                                               70          
  A. 1. 2 Australian Bureau of Statistics                           70          
  A. 2 New Zealand                                                  71          
  A. 3 United Kingdom                                               71          
  A. 4 Canada                                                       71          
  A. 5 USA                                                          72          
  A. 6 Others                                                       72          
  B. MAP DATA FORMATS                                               73          
  B. 1 Introduction                                                 73          
  B. 2 Data Format                                                  73          


  B. 2. 1 Description of File Formats                               73          
  B. 3 Format of attribute files                                    74          
  B. 3. 1 General                                                   74          
  B. 3. 2 Standard format                                           74          
  B. 3. 3 Sample attribute file DEMOATTR.DAT                        75          
  B. 3. 4 Simple Attribute format (database format)                 75          
  B. 3. 5 Sample simple attribute file DEMOSASA.DAT                 75          
  B. 3. 6 Spreadsheet data formats                                  76          
  B. 3. 7 LAMM format                                               76          
  B. 3. 8 Comma delimited format                                    77          
  B. 3. 9 Other attribute data formats                              78          
  B. 4 Standard format of geographic files                          78          
  B. 4. 1 General Information                                       78          
  B. 4. 2 Structure of data                                         78          
  B. 4. 3 Internal Data                                             79          
  B. 4. 4 Comment Record                                            79          
  B. 4. 5 Map Partition                                             80          
  B. 4. 6 Zones Partition                                           80          
  B. 4. 7 Line Partition                                            81          
  B. 4. 8 Polygons Partition                                        81          
  B. 4. 9 Segments Partition                                        82          
  B. 4.10 Points Partitions                                         83          
  B. 4.11 Sample boundaries geographic file DEMOZSEG.DAT            83          
  B. 4.12 Sample geographic file DEMOZONES.DAT                      84          
  B. 4.13 Sample lines geographic file DEMOLINES.DAT                85          
  B. 4.14 Sample points geographic file DEMOPOINT.DAT               86          
  B. 5 Format of polygon geographic files                           86          
  B. 5. 1 Standard (not implemented)                                86          
  B. 5. 2 Simple Format (SAS) Zone Files                            87          
  B. 5. 3 Sample simple zones data file DEMOSASG.DAT                87          
  B. 6 GIS / standard geographic file formats                       88          
  B. 6. 1 DIME format                                               88          
  B. 6. 2 DLG optional 3 format                                     89          
  B. 6. 3 Gina format                                               91          
  B. 6. 4 ANSII standard                                            93          
  B. 6. 5 SIF format (not available)                                93          
  B. 6. 6 DXF format (not available)                                93          
  B. 7 Format of names files                                        94          
  B. 7. 1 Sample names file DEMOATTR.DAT                            94          
  B. 8 Format of colour names files (Removed from system)           94          
  B. 9 Format of combine files                                      95          
  B. 9. 1 Sample combine file DEMOCOMB.DAT                          95          
  B.10 Format of presentation files                                 95          
  B.10. 1 Sample presentation file                                  96          
  B.11 Format of marker files                                       96          
  B.11. 1 Sample marker file SQUARE.DAT                             97          
  B.12 Format of device files                                       97          
  C. GLOSSARY OF TERMS                                             103          
  D. SYSTEM LIMITS                                                 112          
  E. TROUBLE-SHOOTING                                              113          
  F. OzGIS REFERENCES                                              114          
  G. OTHER SPATIAL SOFTWARE                                        115          
  G. 1 Background                                                  115          
  G. 2 SIRO-DBMS Spatial Information in a Relational DBMS          115          
  G. 3 DISIMP Image Processing                                     116          
  G. 4 ITA Interactive Location and Territory Planning             118          
  G. 5 CSIRO Division of Information Technology                    119