=================
                               C o m p u S h o w
                               =================


                            Standard Version 8.44a

                                    for the
                 IBM PC, XT, AT, PCjr, PS/2 (and compatibles)
                                     with

                     Hercules Monochrome Graphics Adapter
                                      or
                         Color Graphics Adapter (CGA)
                                      or
                        Enhanced Graphics Adapter (EGA)
                                      or
                       Multi-Color Graphics Array (MCGA)
                                      or
                          Video Graphics Array (VGA)

Complete CompuShow documentation consists of the following files:

WHATSNEW.DOC  A summary of the changes in this version. "Last minute"  changes
              (since CSHOW.DOC).
SETUP.DOC     Installing CompuShow on a floppy or hard disk. Selecting a video
              driver. Deleting unnecessary files.
DRIVERS.DOC   A complete list of CompuShow video and printer drivers.
CSHOW.DOC     This complete, detailed CompuShow User's Guide.
Q&A.DOC       Frequently asked questions, complete with answers!
CATALOG.DOC   The CaSSS software catalog.
ORDRFORM.DOC  Software order form.

 +--------------------------------------------------------------------------+
 | See  SETUP.DOC for instructions on installing CompuShow and  configuring |
 | it to work with your computer.                                           |
 +--------------------------------------------------------------------------+

Using CompuShow: A Quick Start Overview 
======================================= 

 CompuShow is a program  for viewing graphics on  an IBM compatible  computer.
 This section is designed  to give you  a brief overview  and get you  started
 quickly. Detailed instructions follow.

  1) Start the program from your DOS  prompt by typing 'CSHOW' and a  carriage
     return. The screen shows a sorted list  of the disk files on the  current
     disk drive and sub-directory. If you loaded CompuShow from a floppy disk,
     you can remove the disk  once the program is  running, in order to  mount
     other floppy disks.

  2) The cursor  is positioned  in an  "input  area" near  the bottom  of  the
     screen. Use the "up arrow" cursor key (or your mouse) to move up into the
     file directory.

  3) Move the highlight bar around the list of files using the mouse or cursor
     arrow keys, PgDn, PgUp,  Home, End, etc. (Click  the mouse above the  top

                                                            [CSHOW.DOC] Page 1

     line of file  names to page  up or at  the bottom of  the screen to  page
     down.)

  4) With the highlight bar positioned at  a graphic file, press the  spacebar
     (or click the left mouse button) to  view the picture. If you don't  know
     which files are graphics, just try each one in turn. CompuShow will  tell
     you if a file isn't a graphic.

  5) If the image is larger than the screen, you can "pan around" the image by
     moving the mouse or pressing the cursor arrow keys.

  6) Press ESCape (or click  a mouse button) to  return to the file  directory
     and you're back at step 3 ready to select another file, or...

  7) Press ESCape (or click the mouse in the input area) to return the  cursor
     to the input area (you're back at step 2).

  8) Press ESCape in the input area to exit CompuShow and return to DOS.

 Of course, you may have graphics files on a different disk drive and/or in  a
 different sub-directory (and it's quite  possible that there are no  graphics
 files listed on  the current  directory screen).  There are  several ways  to
 select a different disk drive and sub-directory:

  a) With the highlight bar at a sub-directory (marked <DIR>), press  carriage
     return (or click the mouse) to move into the sub-directory.

  b) Press [F2] to pop up  the "log box" to switch  to drive C: (or drive  D:,
     E:, F:, etc.)

  c) Use Alt-A and Alt-B (hold down the 'Alt' key and type 'a' or 'b') to "log
     in" a new disk in floppy drive A: or B:

 With these basic  instructions you  can switch  to different  disks and  move
 around the  sub-directories  to  select and  display  graphics  images.  Also
 remember that [F1] displays a help screen.

 In addition to this standard "pick a file and display" method, CompuShow also
 allows you to:

  - tag a group of files for display one after another
  - display one or more graphics "from the command line"
  - display a graphic and return to DOS with the image on screen

 These are described in "Other Display Methods" in this document.

Start-Up Options 
================ 

 CompuShow requires  at  least 275k  of  available memory  (depending  on  the
 start-up options specified.) If the program displays an "Insufficient memory"
 message, you need to make more memory available. (Remove some memory-resident
 programs, for example.)

 "Command-line switches" let you control  graphics video features and the  way
 that the program allocates memory for various purposes.


                                                            [CSHOW.DOC] Page 2

Optional Features
-----------------

 A "#" switch is used to specify optional features. (We use UPPERCASE  letters
 in these examples for emphasis; you can use either UPPER- or lower-case.)

  >cshow #B    use <B>lack and gray screen colors. If you have a laptop or any
               computer with an LCD screen, this option will provide  readable
               colors.

  >cshow #D300 this option lets you control the amount of memory reserved  for
               the file  <D>irectory.  The "default"  is  120 files.  You  may
               specify any number from 0 to 9999.

  >cshow #E    if your  <E>GA  display  is "scrambled",  use  this  switch  to
               disable horizontal panning.

  >cshow #I0   controls d<I>thering.  The number following  the letter "I"  is
               the type of dithering where 0=none, 1=Rough, 2=Floyd Steinberg,
               and 3=Burke (which is the  default). Of course, you may  change
               the type  of dithering  by pressing  [F6] while  the  program's
               running.

  >cshow #J    enables  PC-<J>unior/Tandy-1000   video  modes.   The   program
               reserves 32k of memory required for these special video modes.

  >cshow #K    <K>eyboard only. Ignore the mouse.

  >cshow #L    use this  switch if  the CompuShow  screen goes  blank on  your
               <L>eading Edge "IBM compatible" computer.

  >cshow #MS   to control the amount of  <M>emory that the program sets  aside
               for the file read buffer: #mS (Small=2k), #mM (Medium=32k), #mL
               (Large=62k). A small buffer is the default. A 45k file requires
               23 reads with a  2k buffer, 2  reads with a  32k buffer, and  1
               read with a 62k buffer.

  >cshow #N    <N>ormal memory. Don't use EMS/XMS memory.

  >cshow #O    <O>riginal size. Don't  automatically rescale  to fit/fill  the
               screen.

  >cshow #Q    Turns off the sounds that the program makes (<Q>uiet).

"Super-Ega"
-----------

 A "/" switch is  used to  indicate the  presence of  a 480  line  "Super-EGA"
 adapter. The program knows about several:

  >cshow /A    Ahead Systems
  >cshow /G    Genoa
  >cshow /P    Paradise AutoSwitch EGA-480
  >cshow /T    Tseng
  >cshow /V    'VGA' (eg. the Zenith 'VGA')
  >cshow /71   use mode 71 (decimal)


                                                            [CSHOW.DOC] Page 3

 These  commands  specify  graphics  modes  38,   115,  80,  37,  18  and   71
 respectively, to put each card in "480 line EGA" mode.

Video Hardware Identification 
-----------------------------

 CompuShow should recognize the type of video adapter present in your computer
 (Hercules, CGA, EGA, MCGA, or VGA). A "+" command-line switch can be used  to
 override the automatic detect routine:

  >cshow +H    force Hercules mode
  >cshow +C    force CGA mode
  >cshow +E    force EGA mode
  >cshow +B    force EGA (monochrome monitor) mode
  >cshow +M    force MCGA mode
  >cshow +V    force VGA mode and disable non-standard "[],./" modes

 Keep in mind that IT SHOULDN'T BE NECESSARY to use one of these switches.  If
 CompuShow doesn't recognize  your video adapter,  there's probably  something
 wrong with the hardware!

Super-VGA and other Hardware support
------------------------------------

 The "+S" switch is a  special case, used to specify  the name of a  hardware-
 <S>pecific video driver (as described in SETUP.DOC and DRIVERS.DOC).

  >cshow +sT4  loads the videoT4 (Tseng Labs ET4000) driver.

Dual Monitor Operation 
====================== 

 On a system with  both a monochrome  (MDA or Hercules)  and color (CGA,  EGA,
 VGA, etc.) adapter installed, start the program on the monochrome adapter  to
 operate in  dual  monitor mode.  The  directory  screen will  appear  on  the
 monochrome monitor, and graphics images on the color graphics monitor.

 When you finish  displaying a  graphic, press  carriage return  to leave  the
 graphic image on screen, or <ESCape> to clear the graphics screen.

[F1] for Help
=============

 Press the [F1]  function key (or  left-click with  the mouse on  [F1] at  the
 bottom of the screen) to  pop up a quick-reference  Help Screen with a  brief
 description of the options available.

[Shift-F1] for Information
==========================

 Hold a shift key  and press the  [F1] function key  (or right-click with  the
 mouse on [F1] at the  bottom of the screen) to  pop up a Program  Information
 box, which identifies the  amount of memory used  by the program for  various
 purposes. Several  of  the  start-up  options control  the  way  the  program
 allocates memory, which is important for several reasons.



                                                            [CSHOW.DOC] Page 4

  - The size  of  the "virtual  screen"  determines the  extents  for  panning
    images, and  can  affect the  operation  of transparency  and  restore-to-
    previous functions.

    The (default)  small read  buffer provides  the most  memory for  a  large
    virtual screen. If you specify a larger read buffer (eg. with the '#MM' or
    '#ML' command line switch), you take memory away from the virtual screen.

  - If you have a lot of files in the directory, and the program needs  memory
    to pop up a box, it will have to "abandon" the sorted file list. When  you
    return to the directory screen, the  program will retrieve, sort, and  re-
    display the directory, and  you will be  placed at the  first file on  the
    first screen.

    The '#D' option  lets you reserve  memory for  a directory of  up to  9999
    files, so that the  program won't have  to "abandon" it  to pop up  boxes.
    Keep in  mind that  reserving memory  for a  large directory  leaves  less
    memory for the virtual screen.

 If CompuShow uses EMS  or XMS memory for  the virtual screen,  the #M and  #D
 switches have no effect on the size of the virtual screen.

Changing the directory display
==============================

 - Press [F2] to pop up the "log box".

    - Move the mouse to a disk drive letter and click, or

      Type in  a drive  designation (like  D:) and  press carriage  return  to
      switch to that drive.

        Shortcut: at the input area or in the file directory, press [Alt-A] to
        switch to drive A: or [Alt-B] for drive B:

    - Switch directly to  a different  (drive and)  sub-directory by  entering
      "\PICS" or  "E:\GRAPHICS". This  can be  any form  acceptable in  a  DOS
      "ChDir" command, such as '\' or '..' or '..\..\OTHER'.

        Shortcut: in the file directory

          Press carriage return (or mouse click)  with the highlight bar on  a
          sub-directory to move into it.

        At the input area OR in the file directory:

          Press [Shift-F2] to change to your original drive and sub-directory;
          where you were when you started CompuShow.

          Press [Ctrl-F2] to change to the drive and sub-directory  containing
          the CompuShow program.

 - Press [F3] to  switch between  a compressed directory  display, showing  as
   many files as possible,  and a two-column  directory display including  the
   file name, size, date, and time.



                                                            [CSHOW.DOC] Page 5

 - Press [F4] to pop up the "file mask  box" and enter a mask such as  "*.GIF"
   to display only files with a 'GIF' file name extension.

 - Press [F5] to pop up a directory sort box:

    - Press 'O' to  display Only  files. Press  'C' for  a Complete  directory
      display including  hidden files,  the volume  label (marked  <VOL>)  and
      sub-directories (marked <DIR>). Keep in mind that the '.'  sub-directory
      is "this one" and the '..' sub-directory is "the one above this one".

    - Press 'U', 'N', 'E', 'S', or 'D' for Unsorted (DOS sequence) or to  sort
      the directory on Name, Extension, Size, or Date.

    - Press 'F'  or  'B'  for Forward  (ascending)  or  Backward  (descending)
      sequence.

    - Press carriage return when you're done.

Changing Program Options 
========================

 Press (or click on) [F6] to pop up the "Option Box":

  - Press 'S' to turn on <S>ounds or 'Q' for <Q>uiet operation.

  - Press 'A' to <A>uto-scale or 'O' for <O>riginal size. With auto-scale  on,
    the program will automatically scale graphics to fit or fill the screen.

  - Press 'N' for  <N>o dithering  or 'R', 'F',  or 'B'  for <R>ough,  <F>loyd
    Steinberg or <B>urke dithering. Dithering  is used for display modes  with
    fewer than 256 colors:

     - All two color (monochrome) modes (A..O).

     - CGA four color modes (palettes 1 and 3).

     - All sixteen color modes (EGA/VGA and video driver modes).

Selecting a file to display
===========================

Method 1: Enter the name of the file
------------------------------------

 Type the name of any file and press carriage return to select it. If the file
 isn't on the  current directory  screen, you need  to include  the drive  and
 subdirectory,  as  in  "c:\pics\special\hidden\other.gif".  When  you   press
 carriage return, the file will be retrieved,  or a "buzzer" will sound if  it
 wasn't found.

Method 2: Selecting from the directory list
-------------------------------------------

 Press the 'up  arrow' cursor  key (or move  the mouse  up) to  move into  the
 directory display. Move the highlight bar around the file directory with  the
 mouse or cursor keys:


                                                            [CSHOW.DOC] Page 6

  - Down arrow (up arrow) moves you to  the next (previous) file. At the  last
    (first) file on the screen, you move to the next (previous) screen.
  - PgDn (PgUp) moves you  to the next (previous)  screen, or click the  mouse
    above the top file name to page up or below the bottom file name  (outside
    the input area) to page down.
  - Ctrl-PgDn (Ctrl-PgUp) moves you to the bottom (top) of the column.
  - Ctrl-End (Ctrl-Home) moves you to the last (first) file on the screen.
  - End (Home) moves you immediately to the last (first) file.
  - A letter key (A..Z) moves you to the next file starting with that  letter.
    (Type "A" repeatedly to move to each file starting with "A".)

      As you  move around  the  file directory,  three special  functions  are
      available to help you to manipulate your graphics files:
        - Press Alt-C to <C>opy the current file.
        - Press Alt-R to <R>ename the current file.
        - Press Alt-D to <D>elete the current file.

 With the highlight bar at  a graphic file, press  the SpaceBar (or click  the
 left mouse button) to  display it immediately, or  press carriage return  (or
 click the right mouse button) to pop up the Graphics Information Box.

 Press ESCape (or move the mouse cursor to the input area and click) to return
 the cursor to the input area

The Graphics Information Box
============================

 If you type  the name of  a graphic file  in the input  area or position  the
 highlight bar on a graphic file and press carriage return or click the  right
 mouse button, the Graphics Information Box pops  up. The top line of the  box
 identifies the type of graphic, and any other information available, such  as
 "version", width,  height, and  number of  colors. CompuShow  displays  these
 graphics formats:

  monochrome graphics:
    CompuServe RLE
    MacPaint

  color graphics:
    CompuServe GIF
    PC Paintbrush (PCX)
    PC Paint/Pictor
    Dr. Halo
    Rix ColoRIX and Ega Paint
    Targa uncompressed and run-length encoded, mapped and true-color
    Deluxe Paint II and Deluxe Paint II enhanced
    Microsoft Windows Paint (BMP)
    TIFF
    GEM/Ventura IMG

 In the main body of the Graphics Information Box are listed up to 40  display
 modes, for example "EGA 5=320x200x16":

   - The "5" will appear in a bright text color if it's "recommended" or in  a
     dim color if the graphic is larger than the screen, or has more colors.



                                                            [CSHOW.DOC] Page 7

   - The "=" indicates that this is a  "true" graphic mode. A ":" indicates  a
     simulated mode where the program sets the screen to a certain  resolution
     and then  simulates a  different  size by  either repeating  or  skipping
     columns and rows. These simulated display modes generally provide a  good
     looking display of  most graphics,  except for areas  that contain  text,
     which may be illegible due to the detail lost in skipping pixels. If  you
     have a choice between a simulated mode and a true mode, you'll always see
     better image quality with the true mode.

   - "320x200x16" means that  the screen is  320 "pixels" (dots)  wide by  200
     pixels (rows) high in 16 colors.

   - Based on the type of video  adapter(s) installed, you may have  Hercules,
     CGA, PCjr/Tandy, EGA, MCGA, and VGA modes available:

        Mode (width x height x colors)   Herc Cga Ega Ega-480 MCGA VGA
        --------------------------------+----+---+---+-------+----+---+
        720x348     monochrome          | Y  |   |   |       |    |   |
        640x200     monochrome          |    | Y | Y |       |    |   |
        640x350     monochrome          |    |   | M |       |    |   |
        640x480     monochrome          |    |   |   |       | Y  | Y |
        320x200x4   color (4 palettes)  |    | Y | Y |   Y   | Y  | Y |
        320x200x16  color "PCjr/Tandy"  |    | O | O |   O   | O  | O |
        640x200x4   color "PCjr/Tandy"  |    | O | O |   O   | O  | O |
        320x200x16  color EGA           |    |   | Y |   Y   |    | Y |
        640x200x16  color EGA           |    |   | Y |   Y   |    | Y |
        640x350x16  color EGA           |    |   | Y |   Y   |    | Y |
        640x480x16  color EGA           |    |   |   |   Y   |    | Y |
        320x200x256 color MCGA          |    |   |   |       | Y  | Y |
        320x400x256 color extended MCGA |    |   |   |       | P  | P |
        640x400x256 color (simulated)   |    |   |   |       | P  | P |
        640x480x256 color (simulated)   |    |   |   |       | P  | P |
        360x480x256 color extended MCGA |    |   |   |       | P  | P |
        720x480x256 color (simulated)   |    |   |   |       | P  | P |
        --------------------------------+----+---+---+-------+----+---+
        O=Optional, M=EGA+mono monitor, P=PS/2 and compatible VGAs

     The five "extended"  modes work  on a  PS/2 or  register compatible  VGA,
     although they aren't "IBM standard" modes:

      [ sets the adapter to 360x480x256 mode.
      ] simulates 720x480x256 by skipping every other pixel horizontally.

      , sets the adapter to 320x400x256 mode.
      . simulates 640x400x256 by skipping every other pixel horizontally.
      / simulates 640x480x256 by skipping every other pixel horizontally,  and
        skipping one row out of every six.

   - On an EGA or VGA, with a graphic that's 320x200 or smaller, a "Z" mode is
     also available:

      - If the graphic has 16 colors or less, this will display it double-wide
        and double-high using  the 640x350x16 or  640x480x16 mode, which  will
        have much truer colors than the 320x200x16 display.

      - If it has more that 16 colors, it will be displayed using a high-speed
        dithering routine, which simulates over 2000 colors.

                                                            [CSHOW.DOC] Page 8

   - If the  image is  a  size that  "doesn't fit"  your  screen, one  or  two
     additional (simulated) modes are available:

      - Press '-' to rescale the image to FILL the screen. This mode simulates
        a screen the same size as the image.

      - Press '=' to rescale the image to FIT the screen. This mode  preserves
        the original aspect ratio  by expanding or  compressing the image  the
        same amount vertically and horizontally.

   - With a video  driver loaded, you  may have up  to seven additional  modes
     available (S..Y) which  use the unique  graphics display capabilities  of
     your video adapter.

 You may display in any of the modes listed on the screen by pressing the  key
 corresponding to the mode you want. The "best available mode" is indicated by
 the character displayed at the cursor.  Press the spacebar or click the  left
 mouse button to display in this  mode. Press '0', carriage return, ESCape  or
 click the right button to return to the directory screen.

During Graphics Display
=======================

 Graphics images  are displayed  one row  at a  time. As  the image  is  being
 displayed, press  ESCape  or  Ctrl-C  or click  the  right  mouse  button  to
 interrupt and abort display of the rest of the image. The partial image  will
 remain on the screen; press carriage return or ESCape or click a mouse button
 to return to the information box or directory screen.

 - Images larger than the PHYSICAL SCREEN may be "panned", using the mouse  or
   the up, down, left and right cursor arrow  keys. Press a key (once) to  pan
   in that direction. Panning  will stop at  the end of the  image, or may  be
   interrupted by pressing any key. In addition:

     Home/End jump to the upper-left/lower-right corner, 
     Ctrl-Lft/Ctrl-Rgt jump "one screen width" Left/Right, 
     Ctrl-Home/Ctrl-End jump "one screen height" Up/Down.

   The  EGA/VGA  display  pans  both  vertically  and  horizontally,  and  can
   accommodate 16 color images up to 320x1638, 640x819, or 1024x512.

   Other display modes (including hardware-specific modes) pan both vertically
   and horizontally, with the maximum size dependent upon the amount of memory
   available. (The  [Shift-F1]  information  box indicates  the  size  of  the
   "virtual screen".)

 - Pressing the TAB key displays the file name and graphic size.

 - Alt-N negates any monochrome display (modes A..P).

 - The brightness of any (non-dithered) monochrome display may be adjusted:

   Adjust EGA/VGA  monochrome  mode P  by  pressing  PgUp to  make  the  image
   brighter, or  PgDn  to  make  it  darker.  This  brightness  adjustment  is
   instantaneous.



                                                            [CSHOW.DOC] Page 9

   Adjust a Hercules, CGA,  or MCGA monochrome mode  A..O by pressing PgUp  to
   make the image brighter, or PgDn to make it darker. You may also adjust the
   image to a particular  brightness by pressing the  letter key (A..O).  This
   "adjustment" is accomplished by re-displaying the image. The previous image
   is left on the screen, so you can  see the effect of the adjustment as  the
   new image replaces the former display.  (Displaying an image in mode H  and
   pressing PgUp results in the same image as mode G.)

 - Adjust a color image displayed in EGA modes 7, 9, or Z:

   The sixteen colors displayed are numbered 0 to 9 and A to F. Color zero  is
   always the background. To select a  color to adjust, type the color  number
   (0..9 or A..F). That color will flash, so that you can see where it is  and
   decide whether it should be adjusted.  There are two methods for  adjusting
   colors:

    - A selected color may  be adjusted by increasing  or decreasing the  Red,
      Green, or Blue component:

                RED:            decrease [F1]   [F2] increase 
                GREEN:          decrease [F3]   [F4] increase
                BLUE:           decrease [F5]   [F6] increase

      Each color has a Red, Green, and Blue component with a "weight" of 0..3,
      so pressing [F2] four  times will step through  all four levels of  Red.
      [ 4 (Red) x 4 (Green) x 4 (Blue) = the palette of sixty-four colors. ]

    - You may "step through" all sixty-four colors in color number sequence:

                COLOR NUMBER:   decrease [F7]   [F8] increase

   Press Alt-F10 (hold down the  Alt key and type  the [F10] function key)  to
   save the adjusted palette to disk. When you display the GIF file in mode 7,
   9, or Z, the program automatically  uses this saved palette (press [F9]  to
   see the original  color palette; [F10]  to switch back  to the saved  color
   palette.)

 - Adjust a color image displayed  in an MCGA, VGA,  or "Super-VGA" 16 or  256
   color mode (5, 6, 7, 8, 9, Z, S..Y):

    - PgUp/PgDn brightens/darkens the image.

    - The color may be adjusted:

                RED:            decrease [F1]   [F2] increase 
                GREEN:          decrease [F3]   [F4] increase
                BLUE:           decrease [F5]   [F6] increase

      As with an EGA, the adjusted palette  is saved to disk by pressing  Alt-
      F10, and [F9] and [F10] allow you to review the differences between  the
      original and the adjusted palette.

    - Press Alt-G to convert the color image to <G>rayscale.

       - Press Alt-N to <N>egate a grayscale image.

       - Press PgUp/PgDn to lighten/darken the grayscale image.

                                                           [CSHOW.DOC] Page 10

       - Press Alt-C to return to a <C>olor display.

    - Alt-R <R>otates the palette of a color, grayscale, or negated image.

CompuServe GIF Graphics
-----------------------

 With the release of GIF version 89a (July '90) several exciting new  features
 are supported:

  - Text may  be included  for display  with the  graphic. On  an EGA  or  VGA
    system, CompuShow uses a text font "built-in" to the adapter. On any other
    adapter, the program uses the character fonts in the file FONTS.DRV.

  - A "user input" request  causes CompuShow to  wait for you  to press a  key
    before continuing, to allow you time  to read text, etc. To indicate  that
    it's waiting for you, the program  "ticks". Press ESCape or a right  mouse
    button to interrupt further  processing; any other key  or the left  mouse
    button to proceed.

  - Delays between images may be used for  animation or to allow time for  you
    to read text. Delays are also  usually associated with any user input,  so
    that the program can  continue after you've pressed  a key (or button)  or
    the delay time has expired.

  - Transparency may  be  used  to  create  non-rectangular  images  (or  text
    characters) to appear "on top of" the underlying image.

  - Images may  appear which  are "disposed  of" by  restoring to  either  the
    background color or the previous (underlying) image.

  - Comments may be  included by  the person  creating the  GIF. After  you've
    viewed a GIF with  comments, you're asked whether  you want to read  them.
    Press "Y"  or click  the left  button  to read  the comments;  press  'N',
    ESCape, or carriage return or click the right button to skip comments.

 As a  rule of  thumb, transparency  and restore  to previous  functions in  a
 640x480x256 GIF will require either EMS memory or a 640k system, with no  RAM
 resident programs loaded (TSRs,  RAM disks, etc.), so  that at least 530k  of
 memory is available to CompuShow. If there isn't enough memory available, the
 transparent color will be displayed, and restore to previous will be  handled
 as a restore to background.

  +-------------------------------------------------------------------------+
  | See CATALOG.DOC for information about "CompuMake Tools"  for converting |
  | your  existing  graphics  images  to GIF,  including  support  for  all |
  | features of the GIF89a format.                                          |
  +-------------------------------------------------------------------------+










                                                           [CSHOW.DOC] Page 11

Other Display Methods 
===================== 

Tagging Files 
-------------

  - Press [F7] to tag the  file at the highlight  bar, or left-click with  the
    mouse in the space to the left  of the file name. A "tag-pointer"  appears
    and the highlight is moved down one file.
  - Press [F7] at a tagged file to un-tag it.
  - Press (or click on) [F9] to tag  all files (on all screens of the  current
    directory.)
  - Press (or click on) [F8] to show all tagged files.
     - As each image is displayed in turn, you may pan, adjust the appearance,
       etc., just as though you'd displayed it individually.
  - Press (or click on) [F10] to clear all tags (or [F8] to display again.)

Command-line file specification
-------------------------------

 To start CompuShow logged to a different drive and/or sub-directory:

    >cshow d:                         log to drive d:
    >cshow e:\pics                    log to drive e:, sub-directory \pics

 You can also specify a file mask:

    >cshow *.gif                      set the [F4] mask to *.GIF
    >cshow c:\graph\pix\*.pcx         log to  c:\graph\pix,  set the  mask  to
                                      *.pcx

 CompuShow can display one or more files as specified on the command line:

    >cshow c:\pics\favorite.gif+      display one graphic
    >cshow d:\pics\*.gif+             display multiple graphics

 As each image is displayed in turn you may adjust the appearance, pan, etc.

    >cshow e:\graph\sample.pcx+x      display and exit to DOS

 Add a '+X' to the end of the file name to display it and exit to DOS with the
 graphic still on screen.
















                                                           [CSHOW.DOC] Page 12

                       CompuShow Standard Version 8.44a

                               S H A R E W A R E
                               =================

  CompuShow is copyrighted software. However,  you are encouraged to copy  and
share  the  standard   version  with   others  according   to  the   following
requirements:

      The standard version of CompuShow  may be freely copied and  shared
      with others, so long as no charge is made for the software, and  it
      is unmodified and  copied in  its entirety,  including all  program
      documentation and  all support  files. It  may be  distributed  via
      modem, provided that all files are transmitted (archived) together.

  Notice that  ShareWare is  copyrighted software.  It's not  "Public  Domain"
software, nor  is it  "free" software.  If you  continue to  use this  program
beyond a reasonable "trial period", not to exceed 21 days, you must pay for it
by registering.

WHY SHAREWARE?
--------------

   A few  years ago,  we advertised  a (much  simpler) program  in a  national
 computer magazine. Our advertising cost was so high that, even with a  retail
 price of  $45, we  never reached  "break-even"! The  ShareWare concept  turns
 CompuShow into  its own  ad! Our  costs are  reduced, and  we can  price  the
 program accordingly.

   ShareWare let's you "try it before you buy it"! You can determine whether a
 program works properly and how easy it is to use, before you pay for it.

WHY REGISTER?
-------------

   Since CompuShow is a ShareWare product,  we don't receive a penny when  you
 download it  from a  commercial information  service, such  as CompuServe  or
 GEnie, from a BBS, or receive it on a disk of ShareWare programs.

   Since version 1.7 was released in July 1987, we've continued to improve and
 enhance the program, and have released new versions on a regular basis.  Most
 of the enhancements were suggested by  our registered users, and most of  our
 registered users  have upgraded  as  new versions  are announced.  They  like
 CompuShow and  the  improvements  that  their  registration  fees  have  made
 possible!

 If you use CompuShow, you must register:

   - Your registration fee makes it possible for us to continue to improve the
     program and  to  provide  similar high  quality  software  at  reasonable
     prices.

   - For your registration fee you receive the LATEST COMPLETE VERSION of  the
     ENHANCED PROGRAM.

   - As a registered user,  you'll be notified as  new versions are  released,
     and may upgrade for a nominal charge.

                                                           [CSHOW.DOC] Page 13

   - Registered users may purchase other CaSSS software at reduced prices.

   - IF YOU USE THE PROGRAM FOR COMMERCIAL PURPOSES, YOU MUST REGISTER.

Registering for the Enhanced Program
------------------------------------

 The enhanced program (CompuShow version  8.44b) includes all features of  the
 standard program, plus:

  - Printing of all graphics images on most dot matrix and laser printers.

     See DRIVERS.DOC for a complete list of supported printers.

  - The [F8] show of tagged files allows  you to specify an optional delay  in
    seconds between images for a continuous "slide show".

  - Similarly, you may  specify a delay  for a one-pass  or continuous  "slide
    show" of the files specified on the command-line.

  - For the most  flexibility and control,  the slide show  feature follows  a
    prepared script to provide automated display of graphics:
      - from any drive and sub-directory,
      - using the best (space bar) mode or a specified mode,
      - with control of (up, down, left, right) panning,
      - specifying an optional delay in seconds between images,
      - providing a "wait for a key press",
      - to run continuously or quit after one pass.

  - A System Configuration program, which  lets you change screen colors,  and
    specify "start-up" options, making the command-line switches  unnecessary.
    You can also automatically log to  a disk drive and/or sub-directory,  and
    set the type of directory display you want, including:

     the [F3] "wide" directory display,
     the [F4] directory mask (eg. "*.GIF"),
     the [F5] directory sort options.

 For your convenience, we've included an order form (ORDRFORM.DOC) with  space
 for all  the  required information.  (Complete  it by  hand  or with  a  word
 processor.)

                           Prices as of January, 1992
                           --------------------------

 Basic registration, 5.25" disk............................. $25
 To receive a 3.5" disk, please add......................... $ 1
 For overseas delivery, please add.......................... $ 2
 Arizona residents, please include 7% sales tax............. 

   - Credit Card: Indicate  Visa or  MasterCard, card  number, and  expiration
     date.

   - Check or Money Order:  must be in  U.S. funds, drawn on  a U.S. bank.  (A
     Canadian Postal Money Order in US Dollars is acceptable.)

   - Sorry, no CODs or Purchase Orders.

                                                           [CSHOW.DOC] Page 14

   - The $2 for  overseas shipping  IS NOT  REQUIRED for  the continental  US,
     Alaska, Hawaii, US possessions, APOs, FPOs, Canada or Mexico.

   Electronic Mail:  CompuServe Mail: [76555,167]
                     (MCI Mail can be routed to CompuServe) 
                     Internet (BITNET, ARPANET, CICNet, etc.): 
                         76555.167@compuserve.com
                     GE Mail: R.BERRY7

   Paper Mail:       Canyon State Systems and Software
                     Post Office Box 86
                     Sedona, AZ. 86336

   Voice:            (602) 282-5070

 Orders are shipped first class mail, and registration puts you on our mailing
 list for notification when future versions are available. If you're  ordering
 through a  corporation,  college,  or university  purchasing  department,  an
 individual's name would be advisable, so that upgrade notices don't get  lost
 in "receiving department".

Uploading to a Bulletin Board: 
-----------------------------

 As mentioned, we encourage you to copy and share CompuShow with others. We do
 ask, however, that you  be considerate when  you upload to a  BBS (or give  a
 copy to a  friend, computer  club, or  user group.)  A number  of users  have
 called asking for help because the CompuShow that they downloaded from a  BBS
 was missing documentation, and/or support files. Be kind to the other guy! If
 you're going  to upload  to a  BBS, be  sure you  include ALL  FILES in  your
 upload. Not only  is this A  REQUIREMENT for distribution  as ShareWare,  but
 it's also the only way to be fair to the people who download it!

 Keep in mind that any  upload that doesn't include  all files will result  in
 the display of  the "missing files"  message, indicating that  it MAY NOT  BE
 DISTRIBUTED!

BBS SysOps and ShareWare Distributors:
-------------------------------------

 We appreciate the distribution of CompuShow on electronic bulletin boards and
 ShareWare disks. If  you have a  version of CompuShow  which may be  outdated
 (the program date is displayed on the second line of the screen), or you just
 want to be sure you  have the latest version, contact  me. I'll send you  the
 most current  version (at  no  charge), and  put you  on  a mailing  list  to
 automatically receive free upgrades when available.

 If you see the  "missing files" message at  program start-up, you don't  have
 the full package and  don't have permission to  distribute it. If the  person
 who provided the disk or archive  can't supply the missing files, contact  me
 for the latest complete version.







                                                           [CSHOW.DOC] Page 15

Viruses and Trojan Horses:
-------------------------

 Due to the growing  concern over computer viruses,  Trojan horses, and  other
 malicious programs,  BBS  SysOps  and  ShareWare  distributors  have  started
 establishing "direct from author" libraries, or providing ONLY that  software
 which they receive  directly from the  author. We feel  this is an  excellent
 policy, and expect to see it become more common as time passes.

 For your information, we  post CompuShow to CompuServe,  GEnie, and the  "One
 Stop Bit BBS"  (602-282-9035) and  mail copies directly  to a  number of  BBS
 SysOps and ShareWare distributors. We NEVER post directly to BBS's.

 (Just to  put  in  one  last "plug"),  your  concern  about  possible  "virus
 infection" is another  reason to register  the ShareWare that  you intend  to
 continue using.

  Thank you for your support:   Bob Berry
                                Canyon State Systems and Software
                                Post Office Box 86
                                Sedona, Az. 86336
                                Voice:      (602) 282-5070
                                BBS:        (602) 282-9035
                                CompuServe: [76555,167]
                                Internet:   76555.167@compuserve.com
                                GEnie:      R.BERRY7

           Graphics Interchange Format(c) copyright CompuServe Inc.
             GIF(sm) is a Service Mark property of CompuServe Inc.

    Copyright (c) 1992, Canyon State Systems and Software (tm), Sedona, Az.



























                                                           [CSHOW.DOC] Page 16