*** SPECIAL FOR 0100 TO 0106 UNITS ***
 
 
DOC FILE FOR "RUN-MON0.OBJ"   (MODIFIED	FOR 010x UNITS)
 
This is	modified version of the	Blues Brothers "RUN" chip for
010x units.  U20 must be loaded	with seed keys and monthly
unit data by means of a	U20 loader chip	you already have.
 
The stock "RUN"	chip was designed to prevent the user from
discovering the	true unit id number or location	code.  The
"RUN-MON0" chip	(MON means monitor) is designed	to give	the
user full access to all	information in U20.  It	does not
mask the unit id or location code and includes a "RAM-VIEW"
function.  The user can	also directly observe the unit
monthly	authorization data (tier mask and month	key).
You can	also observe authorization data	for other units!
 
It should also work in IRDs.  It was only tested in a TRACKER VIII.
 
 
To view	unit authorization data	press the "HELP" key.
 
Example:
 
   0100	0000 0000 33 <---- UNIT	TIER MASK (HBO/CINEMAX)
EE 5610	F2C5 903E A6 <---- UNIT	MONTH KEY FOR MONTH 24
00 0000	C424	     <---- LAST	4 BYTES	ARE SERVICE ID & MONTH NUMBER
 
   0100	0000 0000 33 <----SAME AS ABOVE	BUT FOR	MONTH 25
16 DF4E	71DC 5F42 B1
00 0000	C425
 
F016 7750 4D65 3900  <----Current decrypted month key.
			  Same for all units with same service
			  id (C4) Changes every	2 months.
			  1st 7	bytes are the key.  Last byte
			  should always	be 00.	This example
			  really IS the	C424 month key!
			  Month	24 is Apr.- May	1988.
 
RAM-VIEW
 
To access the RAM-VIEW function	do SETUP-0 then	hit "7"	several
times until you	get a screen full of HEX numbers.  The ram address
of the first byte displayed is in the upper left hand corner.
The next 8 lines are the actual	data (8	bytes per line).  To change
the block of memory displayed hit the "->" or "<-" keys	to go
forward	or backward.  The addresses wrap around	at 67FF	and 6000.
To get back to normal SETUP-0 screen hit the "CANCEL" key.
 
Some addresses of interest are:
 
6740  The first	4 lines	are the	units scrambled	seed keys.
      The fifth	line is	the key	used to	de-scramble them
      prior to use.  It	is usually 11223344556677.  This
      is a Blues Brothers innovation to	keep the user
      from knowing the seed keys.
 
6600  This is a	special	function of "RUN-MON0".	 Authorization
      data for ALL OTHER units with the	last byte of their unit
      ID the same as this unit is moved	here when received.
      The user can observe their tier mask to see what services
      are popular with other VC-2 owners.
 
Format:	  6600		       <--this memory address
	  0187 2DFA A524 0000  <--UNIT ID PLUS SERVICE ID & MONTH #
	  0100 0000 8000 0000  <--1st 7	BYTES= TIER MASK
	  CDF4 029F FEC3 6789  <--MONTH	KEY #24	FOR UNIT 0187 2DFA
	  0080 00A5 2400 D095  <-- ?  The "D0" goes to 6223 in U20
	  C424 3853 1308 0000  <--- ** see note	1 below
	  0100 1234 FF00 0000  <--the ID of THIS unit in U7 (see note 2)
	  F016 7750 4D65 3900  <--current decrypted month key
	  6600 0700 0000 FF00  <--Misc.	junk for ramview (pointers)	       
 
 
note 1:	This line is the service ID and	unit key selectors for
	ALL units being	served by this programmer.  The	first
	byte will cycle	through	C4,A0,A5....  going through
	all service IDs	being served.  For example CNN (G1-7) will
	cycle through A5,A0,C4,E3.  "E3" is their commercial service
	ID for cable companies.	 Some services such as Telstar channels,
	have only a commercial service ID and don't serve C4 or	A5.
	That's why you don't get any audio from	them!
 
 
note 2:	If the 5th byte	in this	line is	FF then	the keys in U7
       are probably OK and the unit could be restored to normal
       service.
 
 
PROGRAM	TIER MASK:
 
6100, 4th line,	last byte plus 1st 6 bytes on line 5   is
the PROGRAM tier mask for the current or next program.	Usually
only one bit will be set.  In a	normal VC-2 this will be and'ed
with the UNIT tier mask	to see if you are allowed to view this
program. ie: any matching bits win.  For example G1-19,	Cinemax,
uses a mask of 0000 0000 0000 20.  Any units with bit 6	set in
their tier mask	can watch it.  Select-TV is 0000 0000 8000 00 (bit 24).
You can	tune in	different services, observe their program tier mask,
then develop a map of bits vs services.	 You can then observe
the data at 6600 to see	who subscribes to what.	 All zeros mean
that the unit is either	out of service or GI may
be doing electronic counter-measures.
 
 
Electronic counter-measures
 
IF GI SENDS YOUR UNIT A	TIER MASK OF ALL ZEROS WHEN YOU	HAVE A
VALID SUBSCRIPTION TO 1	OR MORE	SERVICES THEY ARE TESTING TO SEE
IF YOU HAVE A MODIFIED DECODER!!!!
 
0000 0000 0000 00  <--bad news tier mask
0100 0000 0000 00  <--also bad news (everybody gets that bit
				      plus one or more others)
 
If your	decoder	had not	been modified you would	see the
"NO SUBSCRIPTION" message when attempting to view the services
you paid for.  You would then call the service to complain.  They
would then send	out the	proper tier mask bits to restore service.
IF YOU DON'T CALL TO COMPLAIN WITHIN A SEVERAL WEEK TIME SPAN
GI WILL	ASSUME YOU CAN WATCH REGARDLESS	OF THE ZEROED TIER MASK
AND MUST HAVE A	MODIFIED UNIT.	They then program their	addressing
computer to send your unit incorrect month keys	which shut down
the audio in your unit.	 Their is NO WAY to fix	this.  That
unit ID	number is forever useless!  (Unless you	can
reprogram THEIR	computer )
 
Please remember	that GI	sends the NEXT month key many times
during the current month(s).  They only	send the current month
key if the user	calls for a change of service.	They will most
likely zero the	tier mask for the NEXT month if	they want to do	it.
If you call in to complain before it takes effect you will give
yourself away.	If you see a all zero tier mask	for your unit
be sure	it is for the current month.   The current month number
is on the setup	"0" screen directly above the "SA" or "FA" indicator.
 
** Note: For several hours on April 1st, the month number indicated
	 that they had changed to key "24"  but	were actually
	 still using key "23" .	 They could fool you!
 
 

Downloaded From P-80 International Information Systems 304-744-2253