Chapter 4                               Cracking Self Booters



     -------------------------------------------------------------
     Now we'll take a look at cracking self booters.  A few compa-
     nies  have found this to be the best copy  protection  scheme
     for them, one of which is DataEast, makers of Ikari Warriors,
     Victory Road,  Lock-On, Karnov, etc...  This posses a special
     problem  to the Amateur Cracker, since they seldom use  stan-
     dard DOS formats.  So let's jump right in!
     -------------------------------------------------------------


     This  is the area where a "Higher than Normal"  knowledge  of
     Assembly  Language and DOS Diskette structures,  so first  of
     all, the Basic's.


     The Disk's Physical Structure

     Data is recorded on a disk in a series of concentric circles,
     called Tracks.   Each track if further divided into segments,
     called  Sectors.   The  standard  double-density  drives  can
     record  40 tracks of data, while the new quad-density  drives
     can record 80 tracks.

     However, the location, size, and number of the sectors within
     a  track are under software control.   This is why  the  PC's
     diskettes are known as soft-sectored.  The characteristics of
     a  diskette's sectors (Their size, and the number per  track)
     are set when each track is formatted.  Disk Formatting can be
     done either by the operating system or by the ROM-BIOS format
     service.   A lot of self booters and almost all forms of copy
     protection  create unusual formats via the ROM-BIOS  diskette
     services.

     The  5 1/4-inch diskettes supported by the standard  PC  BIOS
     may  have  sectors that are 128,256,512,  or 1,024  bytes  in
     size.   DOS, from versions 1.00 through 4.01 has consistently
     used sectors of 512 bytes, and it is quite possible that this
     will continue.

     Here is a table displaying 6 of the most common disk formats:
     _____________________________________________________________

     Type      Sides        Sectors       Tracks       Size(bytes)
     _____________________________________________________________

      S-8        1             8            40            160K
      D-8        2             8            40            320K
      S-9        1             9            40            180K
      D-9        2             9            40            360K
     QD-9        2             9            80            720K
     QD-15       2            15            80          1,200K
     _____________________________________________________________



     S  - Single Density
     D  - Double Density
     QD - Quad Density

     Of all these basic formats,  only two are in widespread  use:
     S-8  and D-9.   The newer Quad Density formats are for the  3
     1/2" and 5 1/4" high density diskettes.


     The Disk's Logical Structure

     So,  as we have already mentioned,  the 5  1/4-inch  diskette
     formats have 40 tracks,  numbered from 0 (the outside  track)
     through 39 (the inside track,  closest to the center).   On a
     double  sided diskette,  the two sides are numbered 0  and  1
     (the  two  recording heads of a double-sided disk  drive  are
     also numbered 0 and 1).

     The BIOS locates the sectors on a disk by a three-dimensional
     coordinate  composed of a track number (also referred  to  as
     the  cylinder number),  a side number (also called  the  head
     number),  and a sector number.  DOS,  on the other hand,  lo-
     cates information by sector number,  and numbers the  sectors
     sequentially from the outside to inside.

     We   can  refer  to  particular  sectors  either   by   their
     three-dimensional  coordinates or by their sequential  order.
     All ROM-BIOS operations use the three-dimensional coordinates
     to locate a sector.  All DOS operations and tools such as DE-
     BUG use the DOS sequential notation.

     The BASIC formula that converts the three-dimensional coordi-
     nates  used by the ROM-BIOS to the sequential sector  numbers
     used by DOS is as follows:

          DOS.SECTOR.NUMBER = (BIOS.SECTOR - 1) + DIOS.SIDE
            * SECTORS.PER.SIDE + BIOS.TRACK * SECTORS.PER.SIDE
            * SIDES.PER.DISK

     And  here are the formulas for converting  sequential  sector
     numbers to three-dimensional coordinates:

          BIOS.SECTOR = 1 + DOS.SECTOR.NUMBER MOD SECTORS.PER.SIDE
            BIOS.SIDE = (DOS.SECTOR.NUMBER \ SECTORS.PER.SIDE)
            MOD SIDE.PER.DISK
            BIOS.TRACK = DOS.SECTOR.NUMBER \ (SECTORS.PER.SIDE
            * SIDES.PER.DISK)

          (Note:  For double-sided nine-sector diskettes, the PC's
          most  common disk format, the value of  SECTORS.PER.SIDE
          is  9 and the value of SIDES.PER.DISK is 2.   Also  note
          that  sides and tracks are numbered differently  in  the
          ROM-BIOS numbering system: The sides and tracks are num-
          bered from 0, but the sectors are numbered from 1.)

     Diskette Space Allocation

     The  formatting  process divides the sectors on a  disk  into
     four sections, for four different uses.  The sections, in the
     order they are stored, are the boot record,  the file alloca-
     tion  table (FAT),  the directory, and the data  space.   The
     size of each section varies between formats,  but the  struc-
     ture and the order of the sections don't vary.

          The Boot Record:

          This section is always a single sector located at sector
     1 of track 0, side 0.  The boot record contains,  among other
     things,  a short program to start the process of loading  the
     operating system on it.   All diskettes have the boot  record
     on them even if they don't have the operating system.  Asisde
     from  the start-up program,  the exact contents of  the  boot
     record vary from format to format.

          The File Allocation Table:

          The  FAT follows the boot record,  usually  starting  at
     sector 2 of track 0,  side 0.   The FAT contains the official
     record of the disk's format and maps out the location of  the
     sectors used by the disk files.   DOS uses the FAT to keep  a
     record of the data-space usage.  Each entry in the table con-
     tains  a specific code to indicate what space is being  used,
     what space is available,  and what space is unusable (Due  to
     defects on the disk).

          The File Directory:

          The file directory is the next item on the disk.   It is
     used  as a table of contents,  identifying each file  on  the
     disk  with a directory entry that contains several pieces  of
     information, including the file's name and size.  One part of
     the entry is a number that points to the first group of  sec-
     tors  used by the file (this number is also the  first  entry
     for this file in the FAT).

          The Data Space:

          Occupies  the bulk of the diskette (from  the  directory
     through the last sector),  is used to store data,  while  the
     other  three  sections are used to support  the  data  space.
     Sectors  in  the  data space are allocated  to  files  on  an
     as-needed basis,  in units known as clusters.   The  clusters
     are one sector long and on double-sided diskettes, they are a
     pair of adjacent sectors.



     (From  here  on I'll continue to describe the basics  of  DOS
     disk structures, and assembly language addressing technics.


     -------------------------------------------------------------
     Here  is a simple routine to just make a backup copy  of  the
     Flight Simulator Version 1.0 by Microsoft.  I know the latest
     version  is  3.x but this version will serve the  purpose  of
     demonstrating  how to access the data and program files of  a
     selfbooter.
     -------------------------------------------------------------


     By:            PTL
     Title:         Microsoft Flight Simulator 1.00 Unprotect


     This procedure will NOT convert the Flight Simulator disk  to
     files  that can be loaded on a hard drive.   But...  it  will
     read  off the data from the original and put it onto  another
     floppy.  And this should give you an idea of how to read data
     directly from a disk and write it back out to another disk.

     First of all take UNFORMATTED disk and place it in drive  B:.
     This will be the target disk.

     Now  place your DOS disk (which has Debug) into drive A:,  or
     just load Debug off you hard disk.

                    A>DEBUG

     Then  we  are going to enter (manually) a little  program  to
     load the FS files off the disk.

                    -E CS:0000 B9 01 00 BA 01 00 BB 00
                               01 0E 07 06 1F 88 E8 53
                               5F AA 83 C7 03 81 FF 1C
                               01 76 F6 B8 08 05 CD 13
                               73 01 90 FE C5 80 FD 0C
                               76 E1 90 CD 20

                    -E CS:0100 00 00 01 02 00 00 02 02 00 00 03 02
                               00 00 04 02 00 00 05 02 00 00 06 02
                               00 00 07 02 00 00 08 02

     Next we'll [R]eset the IP Register by typing.

                    -R IP

     And then typing four zeros after the address prefix.

                    xxxx:0000

     Next insert the original Flight Simulator disk into drive  A:
     and we'll run our little loader.

                    -G =CS:0000 CS:22 CS:2A

     Now enter a new address to load from.

                    -E CS:02 0E
                    -E CS:27 19

     And run the Loader again.

                    -G =CS:0000 CS:22 CS:2A

     New address

                    -E CS:02 27
                    -E CS:27 27

     Run Loader

                    -G =CS:0000 CS:22 CS:2A

     Here  we'll  do some [L]oading directly from  the  disk  our-
     selves.

                    -L DS:0000 0 0 40

     And the in turn, write it back out to the B: (1) drive

                    -W DS:0000 1 0 40

     Etc...

                    -L DS:0000 0 40 28
                    -W DS:0000 1 70 30
                    -L DS:0000 0 A0 30
                    -W DS:0000 1 A0 30
                    -L DS:0000 0 138 8
                    -W DS:0000 1 138 8

     When  we are all through,  [Q]uit from debug and  you  should
     have a backup copy of the Flight Simulator.

                    -Q

     And that's all there is to it.

     END.





            ///////////////////////////////////////////////////////
            //               The PIRATES' HOLLOW                 //
            //                  415-236-2371                     //
            //         over 12 Megs of Elite Text Files          //
            //                  ROR-ALUCARD                      //
            //             Sysop: Doctor Murdock                 //
            // C0-Sysops: That One, Sir Death, Sid Gnarly & Finn //
            //                                                   //
            //    "The Gates of Hell are open night and day;     //
            //     Smooth is the Descent, and Easy is the way.." //
            ///////////////////////////////////////////////////////



 

[0;33;40;1mWhich G-file (Q=Quit) ? [0;37;40m


     Another file downloaded from:                     NIRVANAnet(tm)

     & the Temple of the Screaming Electron              415-935-5845
     Just Say Yes                                        415-922-1613
     Rat Head                                            415-524-3649
     Cheez Whiz                                          408-363-9766
     Reality Check                                       415-474-2602

   Specializing in conversations, obscure information, high explosives,
       arcane knowledge, political extremism, diversive sexuality,
       insane speculation, and wild rumours. ALL-TEXT BBS SYSTEMS.

  Full access for first-time callers.  We don't want to know who you are,
   where you live, or what your phone number is. We are not Big Brother.

                         "Raw Data for Raw Nerves"