Converting a Tone Dialer into a Red Box
---------------------------------------
By Noah Clayton

A very simple modification to Radio Shack pocket tone dialer part
#43-141 ($24.95) can make it into a red box.  The modification
consists of changing the crystal frequency used to generate the
microprocessor's timing.  To make this modification you will need
a Phillips screwdriver, a flat bladed screwdriver, a soldering
iron, a pair of long nose pliers, a pair of wire cutters and a
6.5536 MHz (megahertz) crystal.

Orient the dialer with the keypad down and the speaker at the
top.  Remove the battery compartment cover (and any batteries) to
expose two screws.  Remove these two screws and the two on the
top of the dialer near the speaker.  There are four plastic clips
that are now holding the two halves of the dialer together.  Push
on the two bottom clips near the battery compartment and pull up
to separate the bottom part.  Now slide a flat screwdriver into
the seam on the left starting from the bottom and moving towards
the top.  (You may have to do this on the right side as well.)

When the two halves separate, slide the speaker half underneath
the other half while being careful not to break the wires
connecting the two.  Locate the cylindrical metallic can (it's
about half an inch long and an eighth of an inch in diameter) and
pull it away from the circuit board to break the glue that holds
it in place.  Unsolder this can, which is a 3.579545 MHz crystal,
from the circuit board.

The hard part of this modification is getting the new crystal to
fit properly.  Bend the three disk capacitors over so that there
will be room for the new crystal.  You may also need to remove a
screw.  Since the 6.5536 MHz crystal you have is probably much
bigger than the crystal you are replacing, you will need to bend
the leads on the new crystal so that they will match up with the
pads on the circuit board.  Place the new crystal on the circuit
board, making sure that it will fit once you replace the bottom
half.  Solder the new crystal in place.  As an added touch you
might peel the QC sticker off of the PC board and place it on top
of the crystal.  Now carefully snap the two halves back together
while checking to make sure that none of the wires are getting
pinched or are in the way of the screw holes. Put the case screws
back in and insert three AAA batteries into the battery
compartment.

Your dialer is now ready to test.  Switch the unit on.  The LED
on the dial pad should be lit.  Set the lower slide switch to
STORE mode.  Press the MEMORY button on the dial pad.  Press the
* key five times.  Press the MEMORY key again and then press the
P1 key.  A beep tone should be heard when any key is pressed and
a long beep should sound after the P1 key has been pressed to
indicate that the programming sequence was performed correctly.

Switch the unit into DIAL mode.  Press the P1 key, and five tone
pulses that sound remarkably like coin tones should come out of
the speaker.  I usually program P1 to be four quarters (insert
one or two PAUSE's between each set of five tones), P2 to be two
quarters, and P3 as one quarter.

Of course, you can no longer use the unit to generate touch
tones.

History and Theory
------------------

A friend of mine and I were sitting around his house one day
trying to come up with a way to build a reasonable red box.  I
had built one with analog sine wave generators in the past, but
it was difficult to adjust the frequency of the outputs and keep
them accurate over time and with changes in temperature.  The
electronic project box I had assembled it in was bulky, hard to
conceal, and definitely suspicious-looking.

My friend was playing with his calculator while I was wishing we
had the money and time to design a microprocessor-controlled
device with its own custom PC board.  After a while, he announced
that he had an idea.  He had been looking at a data sheet for a
DTMF (Dual Tone MultiFrequency aka touch tone) generator chip. He
calculated the ratio of the coin tone frequencies of 1700 Hz and
2200 Hz to be .7727.  He then went through all of the tone pairs
used for DTMF, calculating each of their ratios. He discovered
that the ratio of the tone pair used for * was very close to the
ratio for the coin tone frequencies.  This ratio, 941/1209 =
0.7783, differed from the coin tone ratio by less than one
percent.

What this meant was that since the tones generated by such a chip
are digitally synthesized from a divider chain off of a reference
crystal, if one changed the reference crystal to the "right"
frequency, the coin tones would be generated instead of the DTMF
*.  Most DTMF chips use a TV color-burst crystal with a frequency
of 3.579545 MHz.  To determine the crystal frequency that would
generate the coin tones, one would compute:

3,579,545 / 941  * 1700 = 6,466,766 MHz
3,579,545 / 1209 * 2200 = 6,513,647 MHz

(6,466,766 + 6,513,647) / 2 = 6,490,206 MHz
                       
Unfortunately, this is not a standard crystal value and getting
custom crystals made is a real pain for the hobbyist.  The
closest I could find was 6.5536 MHz.  I tried a crystal of this
value and it worked.

(The actual frequencies produced by a DTMF generator chip depend
on the particular manufacturer's design.  The color-burst
crystal's frequency is divided down to DTMF tones by an integer
divider chain.  Because the color-burst crystal's frequency is
not an integer multiple of the DTMF tones there will be a small
difference in the frequencies produced from the standard.)

When we first tried this, we were using one of Radio Shack's
earliest tone dialers.  It consisted of a DTMF generator chip
only, and as such could not produce a sequence of tones
automatically.  Tones were generated as long and as fast as one
could press the buttons.  We were able to simulate nickels using
this device but doing so was fairly slow and tedious.  Because
our manual timing was so far off of the mark, our attempts at
producing dime or quarter signals were a miserable failure.  A
live operator would be instantly connected to the line whenever
we tried it.

The Shack's next model had a microprocessor and a tone generator
in it, each with separate crystals controlling their respective
timing.  It was just a matter of changing the micro's crystal to
get the right on-off timing for a quarter's timing for a
quarter's tone sequence as well as the tone generator's crystal
to get the proper coin frequencies.

Later Radio Shack came out with the model used in this project. 
I promptly bought one because it was lower cost and more compact
than their older model.  I put some batteries in it and tried it
out.  It generated DTMF sequences with very long on and off
times, but other than that, seemed like a nice unit.  Upon
disassembling it though, I became unhappy.  There was only one
crystal.  It controlled the timing for a microprocessor that was
specifically designed to synthesize DTMF.  There was no way to
independently adjust the output frequency of the tones from their
on-off timing.  I was just about to say, "Oh well, yet another
tone dialer for my collection" when it hit me.  Why not try the
higher frequency crystal?  The timing might come out close enough
to simulate either a quarter or a dime.  I made the mod and
tested it out.  It worked!

Thank you Radio Shack, for giving us a convenient to use, easily
concealable and non-suspicious-looking red box.

Reference
---------

The crystal is available from Fry's Electronics in Freemont, CA
for $0.89 plus the charge for UPS Red or Blue. Their number is
415-770-3763. I would suggest buying five, some for future use
and some just in case you cut the leads too short when trying
this project.

Coin Frequencies
----------------

1700 Hz and 2200 Hz +/- 1.5%.

Timing
------

5 cents:  One tone burst for 66 ms (milliseconds) +/- 6 ms.

10 cents: Two tone bursts each 66 ms, with a 66 ms silent period  
          between tones.

25 cents: Five tone bursts each 33 ms +/- 3 ms with a 33 ms       
          silent period between tones.


[Originally published in 2600 magazine, Vol. 7 #3, Autumn 1990]