RADIO REMOTE CONTROL PROGRAM





                       By Lydia Rosa


   Copyright 1990 by Lydia Rosa










                RADIO REMOTE CONTROL PROGRAM
  WHAT'S NEW IN THIS RELEASE




   Version 0.3
      Added the TXADR command to allow addresses other than 8 for
      the ICOM radios.

      Fixed a bug in the SEARCH function.

   Version 0.2
      Initial Release















































WHAT'S NEW IN THIS RELEASE                               1


                RADIO REMOTE CONTROL PROGRAM
  DISCLAIMERS





     IBM is a tradmark of IBM corporation.

     ICOM is a tradmark of ICOM incorporated.

     KENWOOD is a tradmark of KENWOOD corporation.

     DBASE III is a trademark of Ashton-Tate.

   The author  takes no  responsibility for any damages that
  may occur due to the operation of this program.

   This  program  is being distributed  as  SHAREWARE.  This
  means that voluntary contributions are the only  source of
  remuneration  obtained  for this  work. A contribution  of
  $20.00 gives you the following:

        1.  Automatic upgrades to the program.
        2.  Fixes for any bugs.
        3.  Schematics and instructions for the interfaces.
        4.  A clear conscience.


  Please mail all contributions and problem reports to

     Lydia Rosa
     P.O. Box 414
     Marlboro, N.Y.
     12542

    Thank you for your support.
























DISCLAIMERS                                              2


                RADIO REMOTE CONTROL PROGRAM
  INTRODUCTION



     The  RADIO  REMOTE CONTROL PROGRAM will  allow  you  to
  control your ICOM-R7000, or KENWOOD R-5000 radio  from any
  IBM compatible  PC,XT or AT.  With the  standard interface
  adapters provided by the manufactures of these radios, you
  can  store and  recall  banks of  100  channels.  Using  a
  special interface curcuit, you can scan,  search,  and log
  active channels. This curcuit  is provided  free of charge
  to all registered users.

    The program allows you to  select various baud rates, as
  well  as COM port 1 or 2.  Commands  are buffered,  and an
  interface to a DBASE data file is provided.

    Although  it has not been tested, this program may  work
  with other radio  models produced  by  the manufactures of
  the supported radios.








































INTRODUCTION                                             3


                RADIO REMOTE CONTROL PROGRAM
  REQUIREMENTS



    In order to run this  program you will need an IBM PC,XT
  or AT  running  DOS 3.0  or higher.  The program  requires
  about 128k of available RAM to run.

    If  you are controlling  the R7000, you will need either
  the ICOM CI-V  interface adapter,  or  the modified  RS232
  interface.  If  you  wish  to  use  the  signal  detection
  feature of this program, you will need to use the modified
  interface.

    For the R-5000, you  will need  the  IC-10 option kit. A
  modification must be made to the R-5000 if you wish to use
  the signal detection feature of this program.

    It is highly recommended that the  modified interface be
  used for all radios.  Most of the features of this program
  make  use   of   the  detection  of  an  available  signal
  (SQUELCH).  These radios do  NOT  currently  have  squelch
  detection as part of the standard interface. Although this
  program will  work  fine without  this  signal  detection,
  operations such as SCAN and SEARCH will have no usability.

    The interface curcuit is  a  inexpensive, easy  to build
  project.  All  the  parts  are readily  available  at  any
  electronic  store.  Estimated  cost  for each interface is
  $15. Plans  and  instructions  for  these  interfaces  are
  provided to you when you become a registered user.





























REQUIREMENTS                                             4


                RADIO REMOTE CONTROL PROGRAM
  STARTUP



    To   start  the  program,  make  sure  the  program  and
  datafiles are in the default drive. If running the R-7000,
  enter ICOM at the DOS prompt. If running the R-5000, enter
  KENWOOD.

  The  program  will load,  and  then  execute any  existing
  profile. Once the program loads, the first page panel will
  be displayed.
















































STARTUP                                                  5


                RADIO REMOTE CONTROL PROGRAM
  THE DISPLAY



    The display panel shows you the status of your radio, as
  well as the  status of the program.  At  the top left hand
  corner  of  the screen  is displayed the current BAUD rate
  and COM port  being used to  talk  to  the radio.  At  the
  Bottom of the screen is a status  line showing the various
  parameter settings. If there is a signal  present  on  the
  radio, the word "SIG" will be displayed in  the lower left
  hand  corner.   This  display  is   only   valid   if  the
  modification has been made to detect squelch.

    In the  center  of  the  screen, the  status  of  memory
  channels is displayed. These  channels reflect the current
  setting in the COMPUTER's memory. They  can be used to set
  the  radio's memory if so  desired.  There are  100 memory
  slots available  in  this program.  Since only  20 of them
  can be displayed at a  time,  the PgUp  and  PgDn keys are
  used to  display  the  rest.  Information  can be directly
  entered into most of the fields displayed.

    Toward  the  bottom  of the screen is the  COMMAND line.
  This is where commands  to  the  program  are entered. All
  command data is automatically converted to  upper case. To
  the  right of the command line is the LAST  LOGGED status.
  This   indicates   the   last   information    (frequency,
  modulation) sent by the radio.































THE DISPLAY                                              6


                RADIO REMOTE CONTROL PROGRAM
  DATA FIELDS



     Each  memory   channel  displayed  has  several  fields
  associated  with it. Most of these fields can be  modified
  just moving the cursor to the field and typing.




  VALID



     The  VALID field  determines  whether  or not  SCAN and
  SEARCH will use the frequency currently entered into  that
  channel.  The field is set ON by entering an "X" while the
  cursor is positioned on that  field. The  space  bar turns
  the  VALID flag OFF. The SCAN operation will NOT scan that
  memory   channel   on  the  ICOM   if   the   VALID  field
  corresponding  to  that memory channel  is  OFF.  For  the
  SEARCH operation, any frequency entered in a memory record
  that  has the  VALID flag off will NOT cause the search to
  stop and log.

     Entering  a "P" in  the  valid  field  will  cause  the
  channel to become the current priory channel.




  DELAY



    The  DELAY  field  is use during the SCAN operation.  If
  delay is set ON, scanning  will continue one second  after
  the  signal ends  on that channel.  If  delay  is set OFF,
  then  scanning will continue immediately  after the signal
  ends.  The  field  is set ON by  entering an "X" while the
  cursor is positioned on  that  field. Any other  key turns
  the  DELAY  flag OFF.  Delay affects  only  the  specified
  memory channel.




  FREQUENCY



    The FREQUENCY field is used to record or set the current
  memory channel frequency. When a SCAN or SEARCH stops on a
  channel  or frequency, the frequency  currently set in the
  ICOM is  logged in the appropriate  display channel. If  a
  frequency is entered into  a specific  channel, the memory
  channel on the  ICOM corresponding  to the  channel on the


DATA FIELDS                                              7


                RADIO REMOTE CONTROL PROGRAM
  display is set to that frequency. The frequency is entered
  by positioning the  cursor  to the FREQUENCY field of  the
  desired channel,  and  entering  in the desired frequency.
  Only number input is accepted. The decimal point is always
  assumed, and never  entered.  The  LOAD  command will also
  set  the frequency  to  correspond with the  radio  memory
  channel.




  MODE



    The MODE field  is used  to  display  or set a specified
  memory channels modulation.  If a memory channel is logged
  by the SCAN  operation,  the selected modulation  of  that
  channel  will  be  displayed  in  this  field. A channel's
  modulation  can  be set by moving  the  cursor to the MODE
  field  and  entering   in  the  desired  modulation.  MODE
  recognized by the program are as follows:

     radio                valid modulation
    ICOM                  AM, FM, FMN, SSB, CW ,LSB ,USB
    KENWOOD               AM, FM, FSK, CW, LSB, USB

  Note that the ICOM  will  accept  CW, LSB  and  USB. These
  modes have no meaning  for the R-7000, but are accepted by
  the  ICOM interface.  They  are provided for compatibility
  with other ICOM radios.




  COUNT


     This field  displays  the number of times a signal  was
  detected  on  a  specific  channel. This field  cannot  be
  altered. It can, however  be reset. The RESET command will
  cause this value  to  be  reset to 0.  Ctl-END  will  also
  reset  the  COUNT,  as  well as  all  other  fields on the
  selected information line.




  DURATION


     This field displays the average number  of seconds that
  a signal  was  detected  on a specific channel. This field
  cannot be altered.  It  can, however be reset.  The  RESET
  command  will cause this value to be reset to  0.  Ctl-END
  will also reset the DURATION, as  well as all other fields
  on the selected information line.



DATA FIELDS                                              8


                RADIO REMOTE CONTROL PROGRAM
  SERVICE



     This field is used to record the service for a specific
  channel.  It is not modified by any of the commands except
  DBASE.  This  is   a   scratch  pad  location  to   record
  information about a specific frequency.  The DBASE command
  will fill  in this field from the frequency database if it
  finds a match of the current FREQUENCY.


















































DATA FIELDS                                              9


                RADIO REMOTE CONTROL PROGRAM
  COMMANDS



     All  commands  are entered  from  the COMMAND  line.  A
  command  stack  is  provided,  so  that  a command can  be
  entered  before  the  previous  command  is  complete. The
  number  of  commands   stacked  is  limited  only  by  the
  available memory in your computer.

    When  a command is stacked,  the  status  line  (on  the
  bottom  of  the screen) is updated  to show the number  of
  commands  queued.  The "Q" indicator shows  the  number of
  stacked commands. Pressing ESC will terminate the  command
  in process, and cause the next command  in the queue to be
  processed.

     If a command is not valid when entered, the system will
  "BEEP" and the invalid command will be left in the COMMAND
  line, so  that it can be changed. This will also happen if
  there are too many commands in the command stack.




  BAUD  {value}


     The communication  baud rate between the RS232 port and
  the  radio is set with  this  command. The default is 1200
  baud.  Any  valid baud rate  can be set. However, for  the
  program to work, the radio and the computer MUST be set to
  the same baud rate.  The ICOM supports  9600, 1200 and 300
  bauds ONLY.  The ICOM  baud rate  is selected by  a jumper
  inside the unit. It is set at the factory to 1200 baud. It
  is recommended  that  9600  be  used,  for  efficiency  in
  communications between the computer and radio. This is the
  default baud rate for  the  ICOM  program. The KENWOOD  is
  hard-wired for a 4800  baud rate. This is the default baud
  rate for the KENWOOD program.




  CHANNEL {channel-number}


     The  CHANNEL  command  sets  the  radio  to  a specific
  channel.  Example: CHANNEL  3  will set the selected radio
  to memory channel 3.










COMMANDS                                                10


                RADIO REMOTE CONTROL PROGRAM
  CLEAR


     The CLEAR  command will clear all memory  channels from
  the computer's memory. All  FREQUENCY and  SERVICE  fields
  are reset to blanks. The DELAY fields are set off, and the
  COUNT  and  DURATION fields are reset to  0.  The first 20
  frequencies are marked as VALID, and the rest of the VALID
  fields are set off.

     This command only affects the COMPUTER memories. It has
  no affect on the radio channels.




  COM1


    This command  sets the communications port for the radio
  to COM1.  This is the default  setting. After this command
  executes, all communication between the  computer  and the
  radio will be through the COM1 port.




  COM2


    This command sets the  communications port for the radio
  to COM2.  After  this command  executes, all communication
  between  the  computer and the  radio  will be through the
  COM2 port.




  DBASE


    A sample  DBASE compatible  file  is  provided  to  hold
  details  about  various  frequencies.  This  file  can  be
  updated using DBASE-III or any clone capable of updating a
  DBASE  type file.  The  file is called  FREQLIST.DBF.  The
  sample  file contains information on  nationally allocated
  frequencies.

    When  the  DBASE  command is issued,  this  database  is
  searched  for  matching frequencies. If  a match is  found
  between the FREQUENCY field, and the database, the SERVICE
  field is copied from the database. This is an  easy way to
  update  the SERVICE field.  Please  note  that  the  DBASE
  command can take a long time  to  complete,  based  on the
  size of the database file and the available memory.

    When  processing  the  DBASE command,  the program  will
  attempt to  buffer  as much information  in free memory as


COMMANDS                                                11


                RADIO REMOTE CONTROL PROGRAM
  possible. Since  processing from disk  takes  a lot longer
  than processing from memory,  this will speed up the DBASE
  search. The memory for this buffering comes from the  free
  memory left  over after the program  is  loaded. The  more
  free memory available,  the  faster the DBASE  search will
  finish.

    It is  very important that the structure of the provided
  DBASE file be maintained. This program will not be able to
  process this file if certain field structures are altered.
  See  the section  on  data file formats for the details on
  this file.




  DIR  {filespec}


    When issued, this command displays files on  the current
  drive/directory.  If  issued  by  itself,  ALL  files  are
  listed.  If  a filespec  is  included,  only  those  files
  matching  the spec  are  listed. This  command CANNOT list
  files on a drive/directory other than the current one.




  FILENAME  {filespec}


    The FILENAME command  will set the current file used for
  SAVE  and  RECALL commands.  Please  note  that  only  the
  filename  and extension should be  entered.  Paths  should
  NOT be included. This  program  can only save or load from
  the current directory.




  FKn {command}


    The FK command allows setting of function keys 1-10. "n"
  is the  function key you wish  to  set. Any valid  program
  command can  be set  to the  selected  function  key.  The
  program  comes with a few  of the  keys  already  defined.
  These can be overridden using the FK command.

   Example: FK2 QUIT
   After execution  of this command, pressing Function key 2
  will cause the program to terminate.

   DEFAULT settings:
     F1 - HELP, F3 - QUIT, F5 - SCAN, F7 - HALT





COMMANDS                                                12


                RADIO REMOTE CONTROL PROGRAM
  HALT


    If the program is SCANning, SEARCHing,  or LOADing, this
  command will terminate  that function. It is equivalent to
  pressing the ESC key.




  HELP


    The  HELP  command  will  display a  list of  ALL  valid
  commands, and  a short  description  of  each. The current
  setting of function keys is also displayed.




  INC {value}


    The  INC  command  sets  the  increment  value  used for
  SEARCH.  The  value  entered will be added to  the current
  frequency  for  each  step  of  the  SEARCH  routine.  The
  increment value is assumed to be in kilohertz, and must be
  in the rang of .1 to 999.9.




  LOAD


     This command  loads  the  computer memory channels with
  the  contents  of the  radio's memory  channels.  All  the
  COUNT,  and  DURATION  values are  set to  0.  The SERVICE
  fields are clears, and all DELAY flags are turned off. The
  first  20 channels are  marked as  valid. This  command is
  useful initializing the program's memory channels.




  LPT1


    LPT1 sets the default printer port to LPT1.  The printer
  port is  used  by the PRINT command.  This is the  default
  printer port for this program.









COMMANDS                                                13


                RADIO REMOTE CONTROL PROGRAM
  LPT2


    LPT2 sets the default printer  port to LPT2. The printer
  port is used by the PRINT command.




  NOSIGNAL


    This command turns off the signal sensing for the radio.
  The signal sense is the  CARRIER DETECT line of the  RS232
  port.  If the modified  interface is  not  installed, this
  signal does not reflect  the state of the radio's squelch.
  Issuing the  NOSIGNAL command  tells the program to ignore
  the state of this line. When signal  detection is off, the
  signal status field displays the word OFF constantly.




  PRINT


    When  issued,  this  command  prints the contents of the
  computer's memory channels to the default printer.




  PRIORITY  {channel-number}


    Any of the  100  channels can be selected  as a priority
  channel.  During  SCAN, the  selected  priority channel is
  polled once  a  second.  If  there  is  a  signal  on  the
  priority  channel,  scanning will  stop  on  the  priority
  channel until the signal is  no  longer present.  Scanning
  will  then resume  with the last  channel that was scanned
  before the priority channel activated.

    To turn off the priority  scan,  enter  PRIORITY with no
  channel number.




  QUIT


    This command terminates the program and  returns to  DOS
  (or the calling environment).






COMMANDS                                                14


                RADIO REMOTE CONTROL PROGRAM
  RECALL {filename} {SET}


    RECALL  loads  the  computer  memories  with  the values
  specified  in  the  current file.  If  a  channel  is  not
  included in the file, then it will not be set. The radio's
  memories  are  not  affected  unless  the  SET  option  is
  included in command. If  a  filename is included  with the
  command, the file specified will  be read, and the current
  filename will be set to the file entered. If a filename is
  NOT included  in  the  command, then  the current filename
  will be used.

  NOTE:If the filename you wish to recall is called SET, and
  you do  NOT wish to set the  memories,  you  will  need to
  first issue the FILENAME command, then  the RECALL with no
  options. This is because  the program will  not be able to
  tell that  the SET keyword is a filename and NOT a command
  option.




  RESET


    When this  command  is  issued, all  COUNT  and DURATION
  values are reset to 0.




  RESUME {value}


    The value entered here controls how long SCAN  or SEARCH
  will  remain  on  a channel after a signal  is detected. A
  value  of  0 causes  scanning to continue ONLY  after  the
  signal  is  no longer  present. Any other value will cause
  scanning to  resume  after  the number  of seconds entered
  have elapsed.

      For example if the command RESUME 3 was entered, and a
  SCAN operation detected  a squelch on  channel 1, scanning
  would stop on channel 1 for 3 seconds, then continue on to
  the next channel.





  SAVE  {filename}


    This command  will save  the  contents  of the  computer
  memory to the current filename specified.  If the filename
  is  not specified, the current filename will be used. If a
  file  already exists,  it  is  updated  with  the  current


COMMANDS                                                15


                RADIO REMOTE CONTROL PROGRAM
  settings.




  SCAN


    The  SCAN  command  starts the  radio  scanning  through
  selected memory channels. Memory channels that are flagged
  with the VALID field  will  be  scanned. Channels with the
  VALID  flag  off  will  be  bypassed.  When  a  signal  is
  detected, scanning will stop, and the memory channel being
  scanned  will  be displayed  in inverse.  When the  signal
  stops, scanning will continue.

    Several  parameters and  memory  channel settings affect
  the operation  of  SCAN.  Each  channel  has a  VALID flag
  associated  with  it.  If  this  flag  is  set   off,  the
  corresponding memory channel  in  the  radio will  NOT  be
  scanned. If the DELAY  field  of the corresponding  memory
  channel is set, the program will delay 1  second after the
  signal stops before resuming scan.

    The SPEED setting  determines how fast each channel will
  be  scanned. In  the event  that a  scan  is  too fast  to
  respond to certain frequencies, it can be  slowed with the
  SPEED settings.

    The  RESUME  setting determines  the  action  after  the
  squelch breaks. If RESUME is set  to  0, scanning will not
  continue until  the  signal  ends. If  RESUME is any other
  value, scanning will resume  after  the number  of seconds
  specified by RESUME.

    If a channel is set to be a PRIORITY channel, it will be
  scanned  once every second. If a signal is detected on the
  priority  channel normal scanning stops, and the radio  is
  set to receive the  priority channel. Normal scanning will
  resume  when  the  signal  is  no  longer present  on  the
  PRIORITY channel.

    Note  that  any  of  the parameters  or  memory  channel
  settings can  be set either before the scan is started, or
  during  the  scan.  The  new parameters  will take  effect
  immediately in either case.




  SEARCH


     SEARCH allows you  to  scan a range  of frequencies for
  action.  The  range  is  selected  by  the  START and STOP
  values. The INC  value determines  the step size for  each
  frequency increment. The SPEED  value determines how  fast
  the next increment will be selected.


COMMANDS                                                16


                RADIO REMOTE CONTROL PROGRAM

    During a SEARCH operation, a frequency is  set into  the
  radio, and a check is  made for a signal. If no  signal is
  found, the frequency is  incriminated by the INC value and
  the operation  repeated.  When  the  frequency reaches the
  STOP value, the search starts again at the START value.

    If a signal is  found during SEARCH, the memory channels
  are  searched  for  the  active  frequency. If the  active
  frequency is found in one of the computer memory channels,
  and the channel is marked as VALID, the COUNT and DURATION
  fields  will  be  updated.  If the memory channel  is  NOT
  marked  as  VALID,  searching  continues  with  the   next
  frequency.

    If  a  signal  is  found during SEARCH,  and  the active
  frequency  is  NOT  found  in one  of the  computer memory
  channel, the active frequency is logged in the first clear
  memory channel.  If there are no free memory channels, the
  FULL status  indicator will be displayed,  and the  log of
  the  current  active channel will be  lost. You can free a
  memory channel during SEARCH by moving the cursor  to  the
  row of  the  selected channel and  pressing CTL-END. Since
  there  are only 100  channels available, this mean that  a
  search   can  only  locate   a   maximum   of  100  active
  frequencies.

    The RESUME  value controls SEARCH  in the same manner as
  SCAN. If RESUME  is  set to 0, searching will resume AFTER
  the signal  is no longer present.  If RESUME is set  to  a
  number  greater than 0,  searching will resume that number
  of seconds after signal has been detected.



  SET


    SET causes the values in the computer memory channels to
  be set into the radio's memory  channels. All 100 channels
  are set.  Note that it may take a minute or so for all the
  memories to be set.




  SIGNAL


    SIGNAL turns the sense for the signal detection on. This
  is  the  default  condition for the  program.  It  is  the
  opposite command of NOSIGNAL.








COMMANDS                                                17


                RADIO REMOTE CONTROL PROGRAM
  SORT


    SORT  will sort  the memories by frequency in  ascending
  order. It is most  useful  to  do a sort during or after a
  SEARCH operation.




  SPEED {value}


    This  command sets the scanning and searching speed. The
  value  should be a  number  between  0 and  32768. A Speed
  value  of  0  will  result  in  the fastest scan possible.
  Higher numbers cause a slower scan. The number is used  as
  a countdown in the scan loop. The larger the  number,  the
  slower the scan/search rate.




  START {value}


    The  value set  in  this command controls  the  starting
  frequency for the SEARCH  operation.  The  value  must  be
  frequency in the range of the radio.




  STOP  {value)


    The value  set  in  this  command  controls  the  ending
  frequency  for  the SEARCH operation. The  value  must  be
  frequency in the range of the radio.




  TXADR {value)


    ICOM radios can be set to respond to various  addresses.
  This allows multiple  radios to  be connected on  the ICOM
  C-IV bus.  The default address of the R-7000 is 8. This is
  the default setting for this program. The TXADR allows the
  program to talk  to radios with  a  different address. The
  value entered must be an  integer between  1 and 255. This
  command has no affect when running the KENWOOD program.

  NOTE:If the program does  not  appear  to  be comunicating
  with your radio, make sure that the TXADR value is matched
  with the remote control address of your radio. This is set
  by a jumper inside ICOM radios.


COMMANDS                                                18


                RADIO REMOTE CONTROL PROGRAM




























































COMMANDS                                                19


                RADIO REMOTE CONTROL PROGRAM
  SPECIAL KEYS






  ENTER


    The ENTER key finalizes input to the program. If pressed
  while on the COMMAND line, the entered command is executed
  (if valid). If pressed while  on the  FREQUENCY field, the
  entered frequency  is set into the radio's memory, and the
  cursor is moved to the MODE field. If pressed while on the
  MODE  field,  the  entered   modulation  is   checked  for
  validity.  If the modulation is  valid, it is set into the
  radio's memory, and the cursor moves to the SERVICE field.

   If the  cursor is on any other  field, ENTER will move it
  to the next field in the current row.




  ESC


    Pressing  ESC  terminates the current  operation.  It is
  equivalent to the HALT command.




  Backspace


    The destructive backspace key only works  on the command
  line. When  entered, the current character is deleted, and
  the cursor moves to the previous character.




  HOME


    The  HOME  key will move  the cursor to the beginning of
  the current field.











SPECIAL KEYS                                            20


                RADIO REMOTE CONTROL PROGRAM
  END


    If pressed  while  on the SERVICE field,  the  cursor is
  moved  to the last  entered  character  in that field.  If
  pressed while on the command line, the cursor is moved  to
  the last entered character in the command.




  ctl-END


    This   key  clears  all  information  from  the  current
  channel.  The  current channel  is the line  on which  the
  cursor is currently on.  When pressed, the VALID and DELAY
  flags  are cleared, the FREQUENCY field  is set to blanks,
  the MODE  field  is set to '???',  the COUNT and  DURATION
  fields are zeroed, and the SERVICE field is set to blanks.
  This key  only  affects the computer memory. The  radio is
  left un-affected.




  ctl-HOME


    This key will move the  cursor between the command  line
  and the memory  channel fields. It allows  for  a  hot-key
  switch between field editing and command editing.




  Cursor keys


    Cursor keys allow movement around the screen to edit the
  various fields, and contents of fields. The left and right
  keys  move within  a  field. The up  and down arrows  move
  between rows. The program will only allow the cursor to be
  placed on a changeable  field.




  PgDn/PgUp


    These keys move  between the pages of the display. There
  are 5  pages of channel  displays.  Each  page displays 20
  channels. PgDn  selects the next  page, PgUp  displays the
  previous page.





SPECIAL KEYS                                            21


                RADIO REMOTE CONTROL PROGRAM
  INS


    INS selects or cancels  insert mode. Insert mode  allows
  inserting of characters in a field.




  DEL


    The  DEL  key  deletes  the  characters  at  the  cursor
  location.




  Function keys


     Function  keys F1-F10 can be set by the  user using the
  FK command.  When  one  of  these  keys  is  pressed,  the
  current command assigned to this key is executed. Function
  keys that have not been set do not cause  any action to be
  taken.


































SPECIAL KEYS                                            22


                RADIO REMOTE CONTROL PROGRAM
  PROFILE



    The  profile   is   a   file  named  pgrname.PRO,  where
  "progname"  is  the  name  of  the  program  you  started.
  EXAMPLE:  KENWOOD.PRO   is   the  profile  that  would  be
  executed when the KENWOOD  program  was run.  The  profile
  contains a collection of valid commands.  The  primary use
  of the  profile is to set up the program for your specific
  setup. Any  valid command can be included in  the profile.
  A sample profile for each of program  has been included on
  the distribution disk.  If you  do not wish any profile to
  be run, it may be deleted.














































PROFILE                                                 23


                RADIO REMOTE CONTROL PROGRAM
  DATA FILE FORMATS




    There  are several files that this program makes use of.
  These  files are  used  to store and retrieve data used by
  the program.




  FREQLIST.DBF



    This  is  a  standard  DBASE  III+  type data  file.  It
  contains   frequencies  and  allocations   for  the  radio
  spectrum. There  are three fields that are  used  by  this
  program.

    field name     allocation       description
    -----------------------------------------------------------
    FREQUENCY      decimal 9.4      holds the frequency in Mhz
    DESCRIPT       character 50     usage of the frequency
    ACTION         logical          flags the frequency in use

    If the ACTION field is not present, the program will use
  the DESCRIPT  field to  determine ACTION. A blank DESCRIPT
  field signals an inactive channel.

    The length of the  DESCRIPT field can be changed,  if so
  desired.  This  program  only uses the first  38  chars of
  this field.

    Any other fields  can be added or deleted from this file
  without affecting the operation of  the program.  However,
  if either the  FREQUENCY or DESCRIPT field  is not present
  in the database, the DBASE function will not operate.




  frequency data files



    The  SAVE  command  creates  a  file  with  the  current
  settings  of memory channels, and various scan parameters.
  The file created is an ASCII readable file. Each record is
  terminated by a CR/LF sequence.  One record represets  one
  memory channel or  one scan parameter. Each field is blank
  delimited.  The file can be altered (or created) using any
  standard text editor.

   If the first  non-blank character in a record  is  a '*',
  that  record  is  ignored. This  provides  a way  to imbed
  comments in any data file.


DATA FILE FORMATS                                       24


                RADIO REMOTE CONTROL PROGRAM

   The format for a memory channel entry is as follows:

    field   name       value range      description
    ----------------------------------------------------------------
        1   CHANNEL     0-100           channel number to set
        2   FREQUENCY   0-999.9999      frequency in Mhz
        3   MODE        3 chars         valid modulation for radio
        4   COUNT       0-999999        count of squelch breaks
        5   DURATION    0-999999        total duration of squelch
        6   VALID       VALID/NOTVALID  indicator of channel valid
        7   DELAY       DELAY/NODELAY   indicator of channel delay
        8   SERVICE     38 chars        service for channel

   The  service  field follows  the first blank after DELAY.
  All  chars  up to the  CR/LF are taken.  If there are more
  then 38 chars in the service field, they are ignored.

   The format for a scan parameter entry is as follows:

             parm   value

   The valid parameters and there values are as follows:
    parmameter         value       description
    START              0-999.999   start frequency in Mhz
    STOP               0-999.999   stop frequency in Mhz
    INC                .1-99.9     increment in Khz
    SPEED              0-32768     scanning speed
    RESUME             0-32768     resume value




  profile



    The  profile is a  file with  valid  commands that  gets
  executed when the program starts. The profile name is
                 progname.PRO  where  "progname" is the name
  of the program running.

   Any  command that can be executed on the command line can
  be placed  in  the profile.  Each  record  in  the profile
  contains  one  command  (and  parameters)  followed  by  a
  CR/LF. If the  first non-blank character in  a record is a
  '*',  the  record is ignored.  This  allows  the  user  to
  comment the profile.












DATA FILE FORMATS                                       25


                RADIO REMOTE CONTROL PROGRAM
  RS232 INTERFACE




    This   program   is   designed   to   use   the   serial
  communications port  (RS232) of the IBM computer. In order
  to interface a radio to this port, an interface adapter is
  needed  designed   for  the  specific  radio.  Each  radio
  manufacturer makes such an adapter.  However, none  of the
  adapters   supplied  from  the  manufacturer  provide  for
  squelch  detection.  Without  this detection,  the  signal
  sensing functions of this program will not work.

    For each radio supported, a circuit and instructions are
  available.  This circuit  provides the  squelch  detection
  needed  by this program.  The interface circuits are  easy
  to build, and require few parts.  All of the  parts can be
  obtained  cheaply at  any electronics  supply  store.  The
  schematics and instructions are provided to all registered
  users.







































RS232 INTERFACE                                         26