The code speed standard used by the morse code tranceiver program is 
based on a word length of 50 elements. An example is "PARIS" consisting of (10 
dots x 1 elm. = 10) + (4 dash x 3 elm. = 12) + (9 dot or dash elm space x 1 
elm = 9) + (4 ltr space x 3 = 12) + (1 word space x 7 = 7) = 50. One word per 
minute is then 60 sec./ 50 elements = 1.2 sec/elm or 1200 mili-seconds/elm. 
Therefore Element time in ms = 1200/WPM or  WPM = 1200/elm time in ms.

        The default fixed speeds are: S5, f5, 7.5, 10, 13, 15, 18, 20, 25, 30, 
35, 40, 45, 50, 55, 60, 65 and 70 WPM. Slow fixed speeds use expanded spacing. 
As an example the dot, dash and element space of s5 (slow 5) are at a 13 WPM 
rate (elm length = 92.3ms) with character and word spacings expanded to 
produce an overall 5 WPM rate described as 13e5. Similarly f5 (fast 5) is 
16e5, 7.5 is 16e7.5 and 10 is 16e10. Speeds from 13 to 70 WPM use normal 
character and word spacings.    

        Speed   Dot     Dash    Elmsp   Chrsp   Wrdsp
        WPM     Ms      Ms      Ms      Ms      Ms

                x1      x3      x1        Expanded
        13e5    92.3    276.9   92.3    1442.9  3366.8   

        16e5    75      225     75      1527.6  3564.5   

        16e7.5  75      225     75      896.1   2090.8   

        16e10   75      225     75      580.3   1354   

                x1      x3      x1      x3      x7
        13      92.3    276.9   92.3    276.9   646.2   

        15      80      240     80      240     560   

        18      66.7    200     66.7    200     466.7   
                       
        20      60      180     60      180     420   
                       
        25      48      144     48      144     336   

        30      40      120     40      120     280   

        35      34.3    102.9   34.3    102.9   240   
                              
        40      30      90      30      90      210   
                             
        45      26.7    80      26.7    80      186.7   
                                
        50      24      72      24      72      168   
                             
        55      21.8    65.5    21.8    65.5    152.7   
                              
        60      20      60      20      60      140   
                             
        65      18.5    55.4    18.5    55.4    129.2   
                              
        70      17.1    51.4    17.1    51.4    120   

        The main program CW.EXE contains the fixed tx speed control data 
required to produce the 18 default fixed Tx speeds as listed above. Upon CW 
program initialization the file CW_FXS.OVL if it found is read from the disk 
replacing the default fixed tx speed control data. This procedure allows the 
the fixed Tx speeds to be changed or calibrated by editing the file CW_FXS.OVL 
with "debug" or any other hex editor. The file is structured as follows:
        The first 54 bytes at offset 0 through 53 (35h) are the 18 three byte 
ASCII speed values. Each value must be unique and right justified with leading 
blanks as required for the three byte length. These ASCII speed values are 
used to select and then display the selected fixed tx speed.
        The next 180 bytes at offset 54 (36h) through 233 (E9h) are, in the 
same sequence as the ASCII speed values, the 18 five word (10 bite) binary 
speed control values. Each group of 5 words consist of, in sequence, the dot 
length, dash length, element space length, character space length and the 
word space length value. Please note that the word space length value is 
equal to the required word space length less the character space length.
        In fixed speed mode the resolution of all CW element lengths is 100 
micro seconds. (0.1 Ms). The approximate CW element speed control value is 
therefore equal to: required length in ms / 0.1.
   
CALIBRATION PROCEDURE

        1. Equipment required: A high quality counter capable of time interval 
measurment. Set resolution to read .001 or .1 ms as desired.  Connect to 
selected output port pin 20 (DTR). 

        2. Load five message buffers with about one line of the following 
sequences. 1. Series of E's.  2. Series of T's.  3. Series of 5's.  4. Series 
of 0's.  5. Series of E's and spaces.

        3. Set leading edge trigger positive (+) and trailing edge trigger 
negative (-) to measure dot or dash length. Set leading edge trigger negative 
(-) and trailing edge trigger positive (+) to measure Character, Element or 
Word spacing. 

           Signal         Trig          Trig
                          + -           - +
           E's            Dot           Character space
           T's            Dash          Character space
           5's            Dot           Element space
           0's            Dash          Element space
           E & space      Dot           Word space

        4. Adjust CW_FXS.OVL speed control values as required.


        The default fixed tx speed control values were obtained by use of the 
above calibration procedure with the CW program running on a Turbo XT machine 
using a 8088 processor. Slightly faster (shorter CW element lengths) were 
measured on a AT 286 machine.