" MORSCOM1.DOC "                              16:18:48  1/4/1988



MORSCOM1.EXE is a short assembler program to allow the connection of
a morse code "key" to the COM1 serial port of a PC. When the program is
running, pressing the key will cause a beep from the PC. Releasing the key
will cause the tone to stop. This way a PC can be used for morse code
practice with the actual amateur radio key rather than using a key on the
PC's keyboard.

The two leads from the key must be connected to pins 8 and 20 on the first
serial port COM1. (If you have a 9 pin serial connector, that would be pins
1 and 4).

IMPORTANT: Be careful when monkeying around with the serial port. I will
accept no responsibility for frying out someone's serial port.

        **>>   Use this program at your own risk!!    <<**

There, now that the unpleasantries are out of the way, we'll move on to how
the program works. First, it initializes the serial port and raises Data
Terminal Ready (DTR). This signal provides the voltage for setting Carrier
Detect (CD) when the key is pressed. The program then alternates between
checking the keyboard for the ESC key and checking the serial port for CD.
If CD is high, it starts a tone. When CD goes low, it stops the tone. If
the ESC key is pressed, the program stops the tone and bails out.

Bob Gallagher, Jr.

ST1418     The Source
76044,504  Compuserve
62924782   EasyLink
ID1239     Gene Plantz's BBS in Hoffman Estates, IL.