INTERFER.BAS DOCUMENTATION

                     ANALYZING RECEIVER INTERFERENCE

     Receiver  interference  caused  by cross-modulation products  can  be 
extremly  difficult,  if not impossible,  to analyze without the help of a 
computer.   This type of interference is often generated by non-linearity, 
which  causes the mixing of sum,  difference and/or harmonics  of  various 
signals.
     In  an environment with a large number of communication and broadcast 
transmitters, the potential for interference to an STL receiver is likely.  
The  cause  may  be difficult to trace,  particularly  if  the  offending 
transmitters are only on the air intermittently.   Using a calculator in a 
complex multi-user site could take days, or even weeks.
     A better approach relies on the use of a computer and a program  that 
will  analyze the various combinations of frequencies.   These tools  will 
enable  the  engineer  to determine the most likely cause for  current  or 
potential interference.
     Audience  complaints  about receiver interference can be  a  frequent 
source of irritation to the engineer.   These complaints are often  passed 
off as receiver inadequacy when in reality they may be because of spurious 
emission.   Running  an  interference  analysis on these  complaints  will 
certainly remove any doubt.

                               THE PROGRAM

     The analysis program is written to run on Microsoft Basic and is IBM-
PC compatible.   If you manually key in the program,  be careful to follow 
the listing.   Any errors in entering the program will,  of course, affect 
the results.   There is no quarantee that the program will work with other 
versions of Basic.   It is likely, however, that it can be modified if you 
are familiar with your particular version of Basic.
     The  program begins by gathering transmitter frequency and  bandwidth 
data  until  terminated  by  the operator by entering  a  zero  frequency.  
Receiver information is then requested.  The receiver's IF frequencies and 
bandpass  must  be known.   The program requires that data be  entered  in 
megahertz.   The  line  printer  then prints all  the  entered  test  data 
followed by the interference analysis report.
     The  frequencies are paired in such a way that each signal is  tested 
with each other frequency in the database.  The frequencies are calculated 
to  their  extremes based on bandwidth,  then are  added,  subtracted  and 
multiplied by the harmonic number.
     The  result  is  27 test frequences to be compared with  14  receiver 
parameters.   The  receiver  parameters are frequency  extremes  based  on 
bandwidth.   The receiver frequency, first and second IF, first and second 
IF image, and both local oscillators are used as receiver test parameters.  
The  computer must make a total of 400 checks on each pair of frequencies.  
The test is made within the five levels of nested loops.   Line 222 is  th 
heart of the program and tests for an overlap of the low and high receiver 
parameter with the high and low frequency parameter.
     Don't  expect  an  instant solution from even the  fastest  computer.  
Because   of  the  large  quantity  of  calulations  performed,   a   4Mhz 
microprocessor will require ((n/2)*(n/2))/650 hours to complete the tests.  
A test of a site with 60 transmitters requires approximately two hours.  A 
test of 10 requires only about two minutes.

                            USING THE PROGRAM

     Enter all the transmitter frequencies that are in close proximity  to 
the  problem receiver along with their associated bandwidths in megahertz.  
Enter a zero frequency when finished and the screen will request  receiver 
information.   Enter  the receive frequency,  both IF frequencies and  the 
bandpass  of  the  receiver,  all in megahertz.   If a  single  conversion 
receiver is involved, use a zero in the second IF prompt.
     The  printer  will  then begin printing an  analysis.   If  you  have 
entered  a large number of transmitters for analysis,  plan on having  the 
system  tied  up  for  a  few hours.   Be  sure  to  enter  data  for  all 
transmitters at the site;  their relationships must be checked at the same 
time.

                                 RESULTS

     Study the printout carefully,  considering the power levels, possible 
strength  of  the harmonics and proximity to the  receiver  antenna.   The 
suspected  offending frequencies should then be tested by keying  the  two 
frequencies simultaneously and carefully monitoring the receiver output.
     A  spectrum  analyzer  would  be  helpful  at  this  point,  but  not 
mandatory.  In high-level RF environments, however, a low-level signal may 
often be masked by the noise level.   This is especially true if the exact 
frequency  is  not known.   If a pair of frequencies are proved  to  cause 
interference, a trap may be required.  Frequently, an ac power-line filter 
will  prevent  interference without the use of expensive trps.   Some  STL 
receivers  have ineffective or non-existent EMI filters.  Ground loops  in 
the  receiver  coaxial  cables  are also  frequent  sources  of  problems.  
Relocating the receive antenna can solve some problems,  but this approach 
is often impractical.
     As  broadcasting  becomes more competitive,  the need  for  technical 
excellence  is  of the utmost importance.   The pressures on  the  station 
engineer  to provide that extra measure of excellence may require the  use 
of new tools,  such as the computer.   In this particular example, you can 
see that the application of a computer to a relatively complex problem was 
actually  quite simple.   The key was in letting the computer perform  the 
large number of calulations for you.   There may be other tasks where  the 
computer can help.  Look around your station and see what the computer can 
do for you in your job.

Re-printed by permission of Intertek Publishing Corporation.he most likely cause for  current  or 
potential interference.