Sysop Manual for
     AMTOR/PACKET Link (APLINK) Version 5.04, June 1, 1991 

         Copyright (c) 1989-1991 - Victor D. Poor, W5SMM


              Introduction . . . . . . . CHAPTER 1

              Hardware Installation  . . CHAPTER 2

              Software Installation  . . CHAPTER 3

              The Configuration File . . CHAPTER 4

              The Forwarding File  . . . CHAPTER 5

              Starting the System  . . . CHAPTER 6

              Bulletins  . . . . . . . . CHAPTER 7

              System Logs  . . . . . . . CHAPTER 8

              Console Operation  . . . . CHAPTER 9

              Program Distribution  . . CHAPTER 10

              Packet Channel Commands . APPENDIX A

              AMTOR Channel Commands  . APPENDIX B

                            CHAPTER 1

                          Introduction

WHAT THE SYSTEM DOES...

     The AMTOR/PACKET Link (APLINK) is a software system that
runs under MS-DOS 3.x or higher on an IBM-XT or compatible
computer.  It runs an AMTOR MBO and a PACKET BBS concurrently
using a common set of message files.  (For whatever reason, the
AMTOR community refers to these things as mailboxes [MBO] and the
PACKET community as bulletin board systems [BBS].  In this
document MBO will refer to the AMTOR side and BBS to the PACKET
side of the system.)

     Both sides of the system conform as closely as possible to
the conventions that have evolved for the use of PACKET BBSs.
There are differences necessitated by the nature and constraints
of the AMTOR mode.  AMTOR has a very restricted character set and
is subject to transmission errors.  For this reason, as well as
the fact that AMTOR does not automatically identify a sending
station, the MBO requires positive identification during login. 
The MBO will also request confirmation of the addressee when
entering messages into the system (unless the user has selected
'EXPERT' mode).

     Why use AMTOR at all, given its limitations?  AMTOR will
work under difficult radio conditions that would pack in a PACKET
link (pardon the pun).  The author of this system lives on a
sailboat and maintains communications with friends and family via
ham radio. AMTOR has worked reliably for that purpose, day in and
day out, while running with low power, long hauls, and abominable
radio conditions. Only CW could improve on its record for
reliability.

     The MBO provides all of the features that any MBO in use
today would normally supply.  The BBS is a subset of what packet
operators who use the W0RLI or WA7MBL systems are used to.  It is
not intended that this system be used as your local PACKET BBS
although it could be in a pinch.

     No provision is made for handling anything but ASCII text
files in regular message format.  There are no W, D, or U
commands in the system.  The L commands are more limited and work
slightly differently from other systems, but should be sufficient
for the mission.

     When a message is transmitted to an AMTOR station all lower
case characters are converted to upper case and all punctuation
is converted to the closest available character in AMTOR or, if
there is nothing close, to an equal sign (=).  


                            CHAPTER 2

                      Hardware Installation

The equipment required to run this system includes:

     1. IBM-XT or close clone running MS-DOS 3.x or higher and a
hard disk. At least two COM ports must be installed and
available. (Only one COM port is required if you are using a HAL
PCI-3000.)  The minimum acceptable free memory is 256k.

     2. An AMT-1, a PK-232 AEA AMTOR Terminal Unit, or a HAL
Communications PCI-3000 Terminal Unit.

     If the AMT-1 is used it should be configured for 110 baud. 
All soft configuring is done by APLINK at startup.  Only Rx and
Tx signals are used between the AMT-1 and the computer.  Flow
control is performed through use of the status byte from the
AMT-1.  The COM port of choice must be set in the APLINK.CNF
configuration file (see below).

     If a PK-232 AEA Terminal Unit is used on the AMTOR channel
the interconnecting cable between the PK-232 and the serial port
should include wires 1 through 8 and 20 and no others.

     If a HAL PCI-3000 is used, simply install the unit as
received from the factory.  Do not use a serial port or connect
to the "host" port on the PCI-3000.  The interface between the
PCI-3000 and APLINK is on the internal PC bus.

     3. A Packet TNC.  Any TNC that recognizes Control-C to enter
command mode, responds to CONOK ON and OFF should work.  The
program looks for the "*** Connected to..." sequence as well as
the DCD control line (pin 8) to control the state of the BBS.

The critical TNC parameters are:

      ECHO OFF
      FLOW OFF
      NEWMODE ON
      NOMODE OFF
      BBSMSGS ON
      XFLOW OFF
      XON $00
      XOFF $00
      START $00
      STOP $00
      MONITOR OFF 
      MYCALL <your call>
      
      Parity: None
      Characters: 8-bits
      Baud rate to the computer: The same as set in the 
         APLINK.CNF file.

     These parameters are NOT set by APLINK.  Since it is
intended that APLINK work with any TNC, no effort has be made to
automatically configure the TNC.  Be sure your TNC is properly
configured before trying to run the system on the air.  You may
bring up the system and use the keyboard to set up the TNC.  The
TNC must be connected to the COM port specified in APLINK.CNF. 
As a general rule pins 1 through 8 and pin 20 must be connected
between the TNC and the serial port. Hardware flow control is
used (both ways); the only other RS-232 status signal used is pin
8, carrier detect (CD).  Your TNC must be capable of asserting
this signal on connect.  For the PK-232, parameter DCD ON must be
set, for the PK-87, Jumper JP6 must be set to the B position. 
Other TNC's will have similar settings that must be changed,
consult your manual.

     4. The r.f. hardware I will leave to your imagination. 
Since this system is fully concurrent, both channels must be able
to work without mutual interference.  AMTOR would be set up on
your h.f. frequency of choice and the TNC on a suitable v.h.f.
channel.



                            CHAPTER 3

                      Software Installation

     The delivery disk normally contains a self-extracting
archive file.  Create a temporary directory on your hard disk and
copy the archive file into that directory and then run it.  The
following files should appear in the temporary directory:

   APAMT.EXE - The main program when using the AMT-1 on the AMTOR 
        channel,    
   AP232.EXE - The main program when using the PK-232 on the      
        AMTOR channel,    
   APPCI.EXE - The main program when using the HAL PCI-3000 on    
        the AMTOR channel,   
      
   README.NEW - Read it!,
   COPYRITE - Author's copyright statement,
   APLINK.DOC - The Sysop manual (ASCII format),
   APLINK.WP - The Sysop manual (Word Perfect 5.1 format),
   USERS.EXE - The users' file editor,
   APLINK.CNF - A sample system configuration file,    
   ROUTE.APS - A sample packet routing file,
   SIGNON.PKT - The PACKET signon file,
   HELP.AMT - The AMTOR help file,
   HELP.PKT - The PACKET help file,
   INFO.AMT - The AMTOR info file (should be Sysop edited),       
   INFO.PKT - The PACKET info file (should be Sysop edited), and  
   USERS.APS - The file of registered AMTOR users,
   HELP1. thru HELP9. - Help files the Sysop will install using   
        the SH command.
   INTRCPT.APS - A sample intercept file,
   MBBIOS.COM - A TSR communications port driver,
   MBBCONFG.EXE - The MBBIOS.COM configuration program,
   MBBIOS.DOC - Documentation for MBBIOS.COM,

In addition the Sysop must obtain a copy of the Norton Editor.

NOTICE:  If you are upgrading an already
running APLINK and are running a version
earlier than 5.00 then you must use the MCB
editor and set all of your existing bulletin
and help messages to PENDING before you shut
down the old system.  Once the new system is
running you should restore each of those
messages to STATIC.

     To install the system for the first time, simply copy all of
the above files and the Norton Editor (renamed E.COM) into a hard
disk subdirectory named \APLINK.  Make a sub-subdirectory named
\APLINK\ARCHIVE.  Rename either APAMT.EXE, AP232.EXE, or
APPCI.EXE to AP.EXE, depending upon which AMTOR terminal you are
using.  Add \APLINK\MBBIOS.COM to your AUTOEXEC.BAT file.

     If you are using a PK-232 for on the AMTOR channel you may
have to use MBBCONFG.EXE to change the configuration of slot
number 1 to hardware handshaking equal to 'Y'.

     Using the Norton Editor, edit APLINK.CNF, ROUTE.APS,
ROUTES.APS, INTRCPT.APS, INFO.AMT, and INFO.PKT to fit your
station.  Edit USERS.APS with USERS.EXE to add or delete whatever
stations you wish or just let each station be entered into the
USERS.APS file as they log on for the first time.

     Several other files will be created by the system in the
APLINK directory when it is first run.

     Your computer's system clock (TIME and DATE command in MS-
DOS) should be set to your local time.  You should add the
following line to your AUTOEXEC.BAT file: 'SET TZ=aaann' where
aaa is a three letter code for your local time zone and nn is the
number of hours difference between your local time zone and GMT
(UTC).  Use a positive number if your are west of Greenwitch and
a negative number if you are east.  For example:

SET TZ=EST5

should be used for Eastern Standard Time (USA).

The file CONFIG.SYS in your root directory should have BUFFERS=20
and FILES=20, at least.

     Look at the sample INFO.AMT and INFO.PKT files with the
Norton Editor.  You will see what needs to be done there.  

     Read the ROUTE.APS file with the Norton Editor.  Change the
entries as required for packet forwarding at your station.

     The intercept file, INTRCPT.APS, provides a very special
service.  Each line of the file should contain station's call
letters, white space, and an h-route - AND NOTHING ELSE.  Each
time a message is received by APLINK the file is searched for a
match to the TO field of the incoming message, if nothing is
found then an search is made on the first token of the AT field. 
If the first call on any line matches, then the h-route is placed
in the AT field of the message.   Note in the sample provided
that the first line of the file reads:

W5SMM   WA8DRZ.#NOCAL.CA.USA.NA

This means that any message for W5SMM arriving in the system will
be forwarded to him at WA8DRZ.  (In fact, W5SMM requests that all
sysops leave his call in the intercept file as shown.)


                   INSTALLATION NOTE

If you are using Desqview be sure to allow APLINK 
enough time to run.  There is not hard and fast rule
since it depends strongly on the speed of your
computer.  If the time allotment gets too short the
system is painfully slow for your users and in some
cases will fall far enough behind (typically when both
PACKET and AMTOR ports are active at the same time) to
cause timeouts.  This is especially true if you are
using the PK-232 on the AMTOR port.  The software
overhead to run a PK-232 on AMTOR is very much higher
than for other AMTOR controllers.


     Now set up the configuration file as described in the next
chapter.


                            CHAPTER 4

                     The Configuration File

     For APLINK to run you must first edit the APLINK.CNF file to
suit your particular station.  The following parameters must be
included in the file for the system to function.  

MYCALL=W5XYZ       The call letters for your station.
MYSELCAL=WXYZ      The selcal for your station.

The remaining parameters are optional and the system will assume
A default value if nothing is given.  Typical values are shown
here for illustration.

AMTPORT=1           The COM port to be used by the AMTOR
                    terminal.  Default: 1.  (Not required when
                    using the HAL PCI-3000.)
                    
AMTRATE=2400        The baud rate used by the COM port connected
                    to the AMTOR terminal.  Default: 2400.  (Only
                    required when the PK-232 is used as the AMTOR
                    controller.)                    
                    
PKTPORT=2           The COM port to be used by the PACKET TNC.
                    Default: 2.
                    
PKTRATE=2400        The baud rate used by the COM port connected
                    to the PACKET TNC.  Default: 2400.

PKTBBS=W1ABC        Specifies the packet bbs call that you
                    forward to.  It should NOT include the call
                    extension, i.e. W1ABC-3.

MYSUFFIX=4          An extension to your call such as a different
                    call area.  Do not include the / in the
                    entry.  Default: nothing

MYROUTE=WA8DRZ.#NOCAL.CA.USA.NA  If you set MYROUTE to the full
                    h-route for you station it will appear in
                    headers generated by APLINK.  Default is your
                    own call without any h-routing.  You must
                    still set the parameter MYCALL as well,
                    without any extensions.

QTH=MIAMI, FL Z:32132  Your QTH and postal code.  This text will 
                    appear in your message headers.  Default:
                    nothing

TFWD=35             Sets the number of minutes past the hours
                    that PACKET forwarding begins.  Set to 999 to
                    turn PACKET forwarding off.  Default: 999

TUPDATE=9           Set the hour of the day (local time) that the
                    system update will occur automatically.  Set
                    to 999 to prevent automatic updating. 
                    Automatic updating is strongly recommended. 
                    Default: 999

ALMOFF=7            Set the hour of the day (local time) to turn
                    off the sysop alarm.  Default: nothing

ALMON=15            Set the hour of the day (local time) to turn
                    on the sysop alarm.  Default: nothing

ARCHIVE=C:\APLINK\ARCHIVE\  The path for archiving messages
                    removed from the system. (Note: the trailing
                    \ must be included.  Default:
                    C:\APLINK\ARCHIVE\

SIGNON=NEED HELP? TYPE 'HELP+?'  The pre-login message.  Default: 
                    IF YOU NEED HELP TYPE 'HELP(CR/LF)'

SYSMSG=IMPORTANT: READ MESSAGE 1234  The post-login message.
                    This is not normally set but may be used to
                    draw attention to an important bulletin. 
                    Default: nothing

ALOG=AMTLOG         The path/filename for the AMTOR log file.
                    Default: AMTLOG

PLOG=PKTLOG         The path/filename for the PACKET log file.
                    Default: PKTLOG

PRINTER=LPT1        The path to your system printer.  Default:
                    NONE

PRTLOG=1            Specifies the channel that prints to your
                    printer when the system starts.  

                    PRTLOG=1 for system printer (default),        
                    PRTLOG=2 for AMTOR channel printer, or        
                    PRTLOG=3 for PACKET channel printer.

MSGFF=0             1 enables automatic form feed at the end of a
                    message printed on the system printer.
                    Default: 0
                    
MAXLINES=60         Sets the number of printed lines on your
                    printer between form feeds.  Default: 60

CALL=W1ABC          Sets the internally stored call for a station
                    you may wish to link with on AMTOR (manually)
                    when you bring the system up.  Default:
                    nothing

SELCAL=WABC         Sets the internally stored selcal for a
                    station you may wish to link with on AMTOR
                    (manually) when you bring the system up. 
                    Default: nothing

LOGFEC=1            0 prevents FEC mode signals from appearing in
                    the amtor log. Default 1

APPL=$08            Application code for use with G3BPQ node
                    software.  Default: nothing

SHORTHEADERS=1      If SHORTHEADERS is set to 1 only the first
                    and last header will be forwarded on AMTOR. 
                    Intermediate headers will be dropped.  This
                    only acts on messages forwarded on AMTOR. 
                    All the headers will still be forwarded on
                    packet.  Default: 1

PKTBBS=W1ABC        The call letters of the packet bbs that you
                    automatically forward to.  You must NOT
                    include the call extension (i.e., W1ABC-1).  

HOLDFWD=6           Packet forwarding hours may limited.  This
                    parameter, set to a given hour, will prevent
                    forwarding during that hour.  Any number of
                    entries of this parameter are allowed in the
                    APLINK.CNF file.  (Manual forwarding can be
                    initiated at any time.)  (Local time).

BULFWD=12           Bulletins will only be forwarded on packet
                    during the hour set in this parameter.  Any
                    number of entries of this parameter are
                    allowed in the APLINK.CNF file. (Local time).

TFCONLY=1           When set to 1 packet forwarding will only be
                    initiated if there is traffic to forward. 
                    (Manual forwarding can be initiated at any
                    time.)  Default: 0

FRIENDLY=1          This applies only if you are operating under
                    Desqview.  It seems that under certain
                    circumstances when sharing Desqview with an
                    "unfriendly" program that APLINK will run
                    slower than it should. The RLI bbs seems to
                    be one of those.  The only solution is to
                    fight fire with fire and make APLINK
                    "unfriendly" also.  Beginning with this
                    version there is a config option to do that. 
                    Simply include "FRIENDLY=0" in the APLINK.CNF
                    file and APLINK will hang on to it's time
                    slice, busy or not.  If APLINK seems to run
                    too slow under Desqview and tuning the time
                    slices does not fix it then try setting
                    FRIENDLY=0 and see what happens.
                    Default: 1

     You may change the colors displayed on the screen.  Use the
following range of numeric values to set the color parameters.
                    
      0  BLACK
      1  BLUE
      2  GREEN
      3  CYAN
      4  RED
      5  MAGENTA
      6  BROWN
      7  LIGHT GREY
      8  DARK GREY
      9  LIGHT BLUE
      10 LIGHT GREEN
      11 LIGHT CYAN
      12 LIGHT RED
      13 LIGHT MAGENTA
      14 YELLOW
      15 WHITE
    
Backgrounds may only use 0 thru 7.

STATFORE=0          Status line foreground.  Default: BLACK

STATBACK=7          Status line background.  Default: LIGHT GREY

WDOFORE=15          Text windows foreground.  Default: WHITE

WDOBACK=1           Text windows background.  Default: BLUE
                    (Black on black and white screens) 

POPFORE=15          Popup windows foreground.  Default: WHITE

POPBACK=7           Popup windows background.  Default: LIGHT
                    GREY

     The following parameters would only be set in special
circumstances and are best left omitted from the APLINK.CNF file
for normal operation.

TEXNET=1            If the packet BBS that you autoforward to is
                    reached via Texnet this parameter should be
                    set to 1.  In all other cases it should be
                    set to 0.  Default: 0

HEAP=1              If set to 1 the amount of free memory
                    remaining available to APLINK is displayed on
                    the keyboard status line.  Default: 0

AMODE=1             If AMODE is set to 0 the AMTOR channel will
                    come on initially in KSR mode and will not
                    automatically return to MBO mode on timeout.
                    Default: 1

PMODE=1             If PMODE is set to 0 the PACKET channel will
                    come on initially in KSR mode and will not
                    automatically return to BBS mode on timeout.
                    Default: 1

AAB=1               0 defeats the system's automatic answerback.
                    Default: 1

AUTOLOG=1           0 defeats the system's automatic logon
                    system.  Default: 1

PCISCAN=0           For the PCI-3000 only.  0 causes scan lock
                    signal remain low during an ARQ link, 1
                    causes a momentary signal at the beginning of
                    an ARQ link.  See PCI-3000 Instruction Manual
                    5.3.5.  Default: 0

PCICD=0             For the PCI-3000 only.  Sets the value of the
                    control delay in the PCI-3000 in
                    milliseconds.  0 uses the default values in
                    the PCI-3000 at startup.  Default: 0

PCITD=0             For the PCI-3000 only.  Sets the value of the
                    transmit delay in the PCI-3000 in
                    milliseconds.  0 uses the default values in
                    the PCI-3000 at startup.  Default: 0

PCIAD=0             For the PCI-3000 only.  Sets the value of the
                    audio delay in the PCI-3000 in milliseconds. 
                    0 uses the default values in the PCI-3000 at
                    startup.  Default: 0

PCIPD=0             For the PCI-3000 only.  Sets the value of the
                    ptt delay in the PCI-3000 in milliseconds.  0
                    uses the default values in the PCI-3000 at
                    startup.  Default: 0

PCIDLY=0            For the PCI-3000 only.  Use 0 for 32 'chirps'
                    to end the link if the path fades and use 1
                    for 128 'chirps'.  Default: 0

ADELAY=2            For the PK-232 only.  Set the value of the
                    transmit delay for the PK-232.  Multiply the
                    parameter by 10 milliseconds.  Default: The
                    setting in the PK-232 at startup.

Once you have set up the APLINK.CNF file you need to create a
forwarding file as described next.

                            CHAPTER 5

                       The Forwarding File

     The method of routing messages for autoforwarding has been
completely revised to use hierarchical routing (h-routing) as is
now used by the packet network.

     Routing is strictly a function of the station you are linked
to and is independent of whether you are linked on AMTOR or
packet. The old AMTFWD.APS file is no longer used but should
remain in your system until this new scheme has been proven just
in case you need to go back a version.

     Using the Norton editor, create an ASCII file named
FORWARD.APS.  Make entries into the file that look something like
this (assume you are WA8DRZ for this example and that N6IIU is
the packet bbs you normally forward to):

. A line beginning with a period is ignored
. Blank lines are ignored

. The first entry should be your call typically (see below)
WA8DRZ      WA8DRZ  
. The second entry should be the packet bbs you forward to.
N6IIU       N6IIU   
VK2AGE      AH6D   VK2AGE VK3EHQ
TG9VT       TG9VT
#SOCAL.CA   N0IA
#NOCAL.CA   N6IIU  
. This entry routes all NTS traffic with a zip code starting with
. 78 to KE5HE
78*         KE5HE
. The next entry would hold all Alaska traffic in the system
AL          WA8DRZ  
. The following state code entries are exceptions to the rule
. that USA traffic goes to N6IIU
HI          AH6D
TX          KE5HE
IL          WA1URA WB7QWG
IN          WA1URA WB7QWG
USA         N6IIU
AUS         AH6D   VK2AGE VK3EHQ
EU          TG9VT  ZF1GC  
NA          N6IIU
AS          TG9VT  ZF1GC
OC          AH6D
SA          TG9VT  ZF1GC
AF          TG9VT  ZF1GC

and so on.  The first entry on a line is a routing token and the
remaining entries on the same line are bbs/mbo stations that
messages with those routing tokens may be sent to.  Messages that
have nothing in the 'at' field will not move unless there is an
exact match to the 'to' field.  

     You may use a wild card (a '*') on the left hand token.  DO
NOT USE WILD CARDS EXCEPT FOR ZIP CODES OR WHERE THE FIRST THREE
LETTERS ARE 'NTS'.  Wild cards on anything else will potentially
confuse the h-routing scan process.  

     If you have a token with a leading '#' then the expected
following token must be included also: see #NOCAL.CA above.  

     If you put a call (other than your own and the call of the
packet bbs you forward to) in a routing token field then also put
that call in the intercept file with full h-routing so that down
stream stations will know how to deal with it.

     Put the most specific tokens first, such as call letters,
followed by tokens beginning with '#', followed by zip codes
(including zip codes with wild cards), followed by state codes,
followed by country codes, followed by continental codes.  The
scanning process is complicated and the order of entries in
FORWARD.APS is very important.  For example, if a message has
HI.USA in the 'at' field it will not forward to N6IIU in the
above sample file because it will have 'hit' on AH6D first and
the system will hold the message for that station.  Put your own
call in the first line in both the first and second field to
insure that traffic addressed 'at' your station stays there.

     Messages that do not match any routing on the list will not
move - even on packet.  Packet is no longer the default if
nothing matches.  Make sure that the call of the packet station
you forward to has some broad coverage tokens to pick up the bulk
of the traffic that does not otherwise move out on AMTOR.

     Messages with your own call in the 'to' field will not move
unless you have put 'CALLFWD=1' in the APLINK.CNF file.  Messages
with the call of the station that you are linked to in the 'to'
field move unconditionally to that station.

     Any number of bbs calls can follow the routing token as long
as they are separated by one or more spaces and do not exceed a
total line length of 80 characters.

     The routing table is then kept in memory to speed things up
a bit.  If you change FORWARD.APS the system will see a change in
the file time stamp and reload the routing table the next time
routing is requested.


HINTS

     Do not try to put every possible h-routing token in your
FORWARD.APS file.  It is enough to put 'USA' and/or 'NA' for the
station(s) that handles most of your U.S. traffic and then just
enter the state codes that are exceptions ahead of it.  Use 'EU'
for the station(s) that take your European traffic, etc...  If
your FORWARD.APS file is growing large you may not be making the
best of it.  Make sure there is at least one entry for each
continental code.


FORWARDING ON THE AMTOR LINK

     There are two methods of forwarding on the AMTOR channel. 
The 'old' protocol that all versions up to 5.00 use and a 'new'
protocol that is now available beginning with APLINK version
5.00.  The new version uses full h-routing and BIDS or MIDS
(bulletin ids or message ids) to protect against duplicate
messages or 'round robin' routing.

     By default the system continues to use the old protocol with
any station you forward to unless you use the USERS.EXE program
to change the HFWD status to YES for the station you are
forwarding to.  You must co-ordinate this with the other station. 
BOTH of you must change the HFWD status for the other at the same
time.  There are many advantages to using the new protocol and
you are encouraged to make the change as soon as anyone you are
forwarding to has installed version 5.00 or later.

     Before too long the old protocol will be dropped from the
system altogether.


FORWARDING ON THE PACKET LINK

     APLINK still has the limitation that you may only forward to
one packet bbs automatically (The station set into the PKTBBS
parameter in the APLINK.CNF file).  This restriction will be
removed in a later version.  

     There no longer is a restriction on other packet stations
linking to you and initiating reverse forwarding.


REJECTED MESSAGES

     If the system attempts to forward a bulletin and it is
rejected (usually meaning that the other station already has it)
its status is changed to STATIC and it is left in the system for
all to read.

     If a private or NTS message is rejected it is marked as
REJECTED and held for the sysop to take action on it.  A
rejection of a private or NTS message usually means there is some
problem, typically a case of "round robin" routing.  In any case
the sysop should look into it.  When the sysop does a message
listing rejected messages will show a '*' in the status column,
or '**' if it is over 24 hours old.  The message status is
restored, of course, by the MCB editor once the problem has been
solved.


                            CHAPTER 6

                       Starting the System

     If you have not already done so, re-boot the system to make
sure MBBIOS.COM has been loaded.  To start the system the first
time, keep your transmitters turned off but your AMTOR terminal
unit and your TNC turned on, and run AP.EXE.  The system will go
through its initialization procedure and when it is ready for
service will display the copyright notice on the screen.

     Type the following sysop commands to enter the tutorial help
files (if you are upgrading from an earlier version, delete your
old help files):

SH AMTOR HELP1(return) 
SH AMTOR HELP2(return) 
etc. thru HELP9

To see if it all worked type:

LH(return)

and you should get the message list with the help files showing. 
If uncertain about this procedure read KEYBOARD OPERATION and
SYSOP COMMANDS sections first.

     This completes the installation.  You should be up and
running unless the AMTOR terminal unit or TNC installation has
not been previously checked out.  You can use the AP.EXE program
to do that by simply switching off the related MBO or BBS
function and using it as an ordinary terminal, following the
installation instructions.


SPECIAL NOTE REGARDING THE PK-232

     The AMTOR PK-232 driver has been enhanced.  You may now
'cold start' the PK-232 provided you have the PK-232 19 July 1990
(or later) ROM installed.  You can continue as your are now or
you can remove the battery (or pull jumper JP-1) and simply turn
the PK-232 on just before running APLINK and APLINK will do a
full configuration including setting the baud rate to whatever
you have set in the APLINK.CNF file (AMTRATE=nnnn, default is
2400).  This should work OK where you want the system to
automatically restart from a power failure.


                            CHAPTER 7

                            Bulletins

     Bulletins entered into the system from the AMTOR channel or
by the Sysop are visible to everyone who uses the system. 
Because of the proliferation of bulletins that arrive at any BBS
via PACKET, bulletins that enter the system from the PACKET
channel will not be visible to AMTOR users unless the Sysop uses
the MCB Editor to change the "Channel" field from PACKET to
SYSOP. 

     Bulletins may be entered by any station.  If there is no
entry in the 'at' field then the bulletin will remain in the
system but will not be forwarded to any other station.  If there
is an entry in the 'at' field the bulletin will be forwarded once
only to the station indicated by the FORWARD.APS file for that
routing.  APLINK does not do "flood" forwarding of bulletins.  If
the bulletin is forwarded to a packet bbs however, that bbs may
"flood" the bulletin to many stations.

     Bulletins entering the system via PACKET are deleted after
21 days unless the Sysop changes the channel designator with the
MCB Editor.  All other bulletins are held in the system until
deleted by the sysop or the originating station.


                            CHAPTER 8

                           System Logs

     The system maintains three log files.  The paths (file
names) of two are declared in the APLINK.CNF file.  These are the
AMTOR and PACKET text logs.  They record everything transmitted
or received on their respective channels.  Their main purpose is
diagnostic and can be turned off once the system is known to be
stable and free of programmer errors. In order not to fill the
disk with endless text logs, the current text logs are renamed
AMTLOG.OLD and PKTLOG.OLD when UPDATE is executed and the
previous AMTLOG.OLD and PKTLOG.OLD files are deleted.

     The third log is a text format event log file that records
logons, logoffs, filing of messages, reading of messages, etc.,
etc.  It is named EVENTLOG.APS.

     The current AMTOR log may be read with the F7/F2 command
when the keyboard is in AMTOR mode, the current PACKET log with
the F7/F2 command when the keyboard is in PACKET mode and the
EVENT log with the F7/F2 command when the keyboard is in SYSOP
mode.

     If a failure occurs during system operation the three log
files should immediately be saved to give the programmer half a
chance at finding what happened.

                           CHAPTER 9

                        Console Operation

     When the system is started, three windows will be displayed
with the copyright notice showing on the top window when the
system has completed initialization.

     The top window is always devoted to displaying characters
received on the AMTOR channel, the middle screen to characters
received on the PACKET channel, and the bottom window to
characters received from the keyboard or files being transmitted. 
Over each window is a status bar related to that window (and
channel).

     The keyboard has four normal operating states; OFF, AMTOR,
PACKET and SYSOP.  There are two additional states, ATEST and
PTEST, that the Sysop will not normally use - they are for
diagnostic purposes only.

     If the keyboard is OFF the console will beep as a reminder
whenever a key is pressed.  The numeric key pad is used to re-
assign the keyboard:

   9 (PgUp) for AMTOR, 
   6 (Right Arrow) for PACKET, 
   3 (PgDn) for SYSOP and 
   7 (Home) for OFF.  
   
The labels on the keys don't make much sense but, given a normal
keyboard layout, it 'feels right' for the purpose.

     In PACKET and SYSOP mode the keyboard is line buffered.
Characters are transmitted only when return is pressed allowing
backspace over the whole line.  In AMTOR mode the keyboard is
word buffered. Characters are transmitted when the spacebar,
return, a control character, or +? is pressed.

     If a 'T' (talk to the Sysop) command is received on one of
the channels during a session the keyboard is automatically
assigned to that channel for 5 minutes when the Sysop alarm is
sounded.  After 5 minutes the keyboard reverts to its pervious
assignment.

     Some of the function keys are always active and some will
respond only if the keyboard is assigned to the relevant channel. 
This will make sense to you when you use the system.

     Here is the meaning of the status bar indicators:



AMTOR:aaa/bbb:cccc  <gmt time and date>  ddd/eee/fff  

     aaa = MBO when the AMTOR Mailbox is alive and well.    
     aaa = KSR when the SYSOP has shut off the mailbox by         
          one or another means.

     bbb = SBY when the MBO is waiting for a logon.    
     bbb = OPN when someone has logged on, but there is no        
          command outstanding.
     bbb = INP when receiving a file.
     bbb = OUT when transmitting a file.
     bbb = TSF when transmitting files in response to an RN
          command.    
     bbb = CFM during the time a message header is being
          confirmed.

     cccc = Is the call of the last user to have signed onto the  
          AMTOR mailbox; or, if the system has just been
          initialized, it is the call specified in the CALL
          parameter of the configuration file.

     ddd = RCV when the AMTOR link is in the receive direction.   
     ddd = SND when the AMTOR link is in the transmit direction.

     eee = FEC during standby and when operating in FEC mode.    
     eee = ARQ when linked or operating in ARQ-Listen mode.

     fff = ERR, RQ, TFC, IDL, OVR, PHA, SBY, or ESC depending on
     the state of the AMTOR controller.  See your controller
     manual for explanations.


PACKET:aaa/bbb:cccc  <local time and date> !RTS:dd/CTS:ee  

     aaa = BBS when the Packet BBS on.
     aaa = KSR when the Sysop has turned off the BBS.

     bbb = SBY when the BBS is waiting for a logon.    
     bbb = OPN when someone has connected but there is no command 
          outstanding.
     bbb = INP when receiving a file.
     bbb = OUT when transmitting a file.
     bbb = TSF when transmitting files in response to an RN
          command.
     bbb = SBJ while waiting for the subject input for a message.

     cccc = Is the call of the last user to have signed onto the  
          PACKET mailbox.

     !  = A '!' appears here when the internal send buffer is
          full and waiting for the packet port to accept more
          characters.
     dd = OK when RTS is sent to the TNC.
     dd = NO when RTS is not sent to the TNC.
     ee = OK when CTS is received from the TNC.
     ee = NO when CTS is not received from the TNC.


KBD:aaaaa                                        PTR:bbb

     aaaaa = KOFF when the keyboard is off.  
     aaaaa = AMTOR when the keyboard is assigned to the AMTOR     
          channel.
     aaaaa = PACKET when the keyboard is assigned to the PACKET   
          channel.
     aaaaa = SYSOP when the keyboard is assigned to the SYSOP     
          command handler.
     aaaaa = *ATEST* when the keyboard is assigned to the AMTOR   
          test routine.
     aaaaa = *PTEST* when the keyboard is assigned to the PACKET  
          test routine.
   
     bbb = NCF when the printer is not configured.
     bbb = SYS when the printer is assigned to the system.
     bbb = AMT when the printer is assigned to the AMTOR channel. 
     bbb = PKT when the printer is assigned to the PACKET
          channel.


FUNCTION KEY COMMANDS

     The function key assignments will 'feel' right with the
function keys arranged vertically at the left hand edge and the
Gray + and - keys are on the right hand edge (standard XT
layout).  If your keyboard arranges the function keys along the
top they will be more awkward to use.  Note: The keys described
below are active when the keyboard is in the relevant mode.


Keys           Function
----           --------
Grey +         ARQ/FEC receive mode.  In the ARQ mode, a +? is    
               transmitted and in the FEC mode a begin transmit
               command is issued to the AMTOR terminal unit.

Grey -         ARQ/FEC transmit mode.  In either mode an
               appropriate break command is issued to the AMTOR
               terminal unit.  (Note: The PK-232 will not execute
               this command until it sees an IDLE status.)

Esc            Stops any file transmission in progress and clears 
               all keyboard and send buffers.

End            In AMTOR mode - closes the ARQ link.  In PACKET
               mode - send and END command to the TNC.

Del            Issues a return-to-letters-case command to the
               AMTOR terminal unit.  This provides an immediate
               manual override when text is being received if
               figures-case.

F1             Displays a short help menu.

F3             Displays the Mode Selection menu.

F3 F2          In AMTOR mode, forces the AMTOR terminal unit into
               STANDBY mode.  (With the PK-232 there may be some
               delay in execution.)

F3 F4          In AMTOR mode switches the MBO on and off.  In the 
               PACKET mode switches the BBS on and off.

F3 F6          In the AMTOR mode commands the AMTOR terminal unit
               to monitor ARQ.

F3 F8          In the AMTOR mode, begins an AMTOR automatic
               forwarding cycle; in the PACKET mode, begins the a
               PACKET automatic forwarding cycle.

F3 F10         Ends the APLINK program and returns to the
               operating system.

F5             Displays the Clear Selection menu.

F5 F6          Clears all windows.

F5 F10         Sends a formfeed command to the printer.

F7             Displays the File Operations menu.

F7 F2          Read or edit a log file.  In AMTOR mode, the AMTOR
               log file; in PACKET mode, the PACKET log file; and
               in SYSOP mode, the EVENT log file.

F7 F4          Invoke the Norton Editor to edit any ASCII file.

F7 F6          Invoke MS-DOS as an overlay.  APLINK will be       
               suspended but will remain resident.  Type exit at  
               the DOS prompt to return to APLINK.

F7 F8          Prompts for a file name and then transmits that
               file.

F7 F10         Switch the printer to print the channel indicated
               by the current mode.  If in SYSOP mode the printer
               is switched off.

F9             Display the AMTOR On-Line Commands menu.

F9 F4          Enter call letters and optionally the selcal for a
               station to be called.  If the selcal is not
               entered then it will be generated automatically
               from the call letters by APLINK.

F9 F6          Begin an ARQ call.

F9 F8          Switch on a steady carrier to the AMTOR
               transmitter for testing or tuning.

F9 F10         Send an identification sequence on the AMTOR       
               channel.

Alt-F9         Send an identification sequence followed by a
               LOGOUT command on the AMTOR channel.


SYSOP COMMANDS

     Remember, the following are SYSOP commands.  They are not
the same as the commands used over the air by a remote station. 
These commands are not normally invoked while linked but may be
usually without harm unless autoforwarding is in progress.  The
system will delay response to an online user while SYSOP commands
are being executed.

     In the table below <number> is any integer between 0 and
29999, <id>, <id1> and <id2> are standard 1 to 6 character PACKET
routing designators (usually call letters), and <filename> is any
valid MS-DOS path/filename. 

COMMAND                  FUNCTION
-------                  --------
CANCEL <number>          Marks message <number> as CANCELED.  It
                         will no longer appear on any be the
                         Sysop's message lists.  This is normally
                         used to remove bulletins from the system
                         but may be used to remove a defective or
                         possible illegal message as well.  The
                         next UPDATE will archive all canceled 
                         messages PRIVATE and NTS messages and
                         will delete all canceled bulletins.

CANCEL <number 1> <number 2>  Marks all messages from <number 1>  
                         through <number 2> as CANCELED.
                         
E <number>               Invokes the Message Control Block Editor
                         for message <number>.  See the separate
                         section describing the MCB Editor.       
                  
K <number>               Same as CANCEL <number>.

K <number 1> <number 2>  Same as CANCEL <number 1> <number 2>.

KB <number>              Same as CANCEL <number> except bulletins
                         only.

KB <number 1> <number 2> Same as CANCEL <number 1> <number 2>
                         except bulletins only.

L                        List all messages in the system except
                         bulletins.

L <number>               List all messages in the system equal to
                         or greater than <number>, except
                         bulletins.

LP                       List all "pending" messages; messages
                         awaiting forwarding or delivery.

LT                       List all messages addressed to this
                         station and to "SYSOP".

LT <id>                  List all messages to <id>.

LF                       List all messages from this station.

LF <id>                  List all messages from <id>.

LB                       List all bulletins.

LH                       List all help files.

LR                       List users logging into the system in
                         the last 24 hours.

LU                       List all users registered in the system.

NTS                      List all NTS messages in the system.     
                         (Note: This command when invoked on the
                         AMTOR or PACKET port will only list NTS
                         messages marked as FILED or ACCESSED.

P <number>               Print message <number> to your printer.
                         If the message is addressed to your
                         station it will be marked as forwarded.

PN                       Print all new messages to your station
                         and mark them as forwarded.

R <number>               Read message <number>.  This invokes the
                         Norton Editor with message <number>. 
                         Not only can the Sysop read but he can
                         also modify any message in the system. 
                         It is generally not socially acceptable
                         to modify other people's messages.  Any
                         message accessed in this way addressed
                         to your station will be marked as
                         forwarded.

RESTORE <number>         Restores a canceled message provided it
                         has not been archived.

SP <id1> [AT <id2>] [<filename>]   If file name is included,
                         copies <filename> into APLINK as a
                         message to <id1>.  If <filename> is not
                         included then the Norton Editor in
                         invoked.  After the message has been
                         typed and edited, exiting the editor
                         stores the message into APLINK.  If the
                         Norton Editor is exited without saving
                         the text (i.e., F3 Q Y) then the
                         operation is canceled.

SB . . .                 Same as the SP command above except the  
                         message is marked BULLETIN.

ST . . .                 Same as the SP command above except that 
                         the message is marked NTS.  Certain
                         restrictions may apply to NTS messages. 
                         See the section on NTS operations.

SH . . .                 Same as the SP command above except the  
                         "message" is a help file only.          

UPDATE                   Manually initiates the system update
                         routines.  This is normally done by
                         setting the 'TUPDATE' parameter in the
                         APLINK.CNF file.


IN AND OUT OF AMTOR MBO MODE

     With the keyboard in AMTOR mode he system is toggled in and
out of MBO mode by pressing F3 F4.  The system will automatically
return to MBO mode after about ten minutes time, once the system
is no longer linked, in the highly unlikely event that the Sysop
forgets to return it.

     If a user is using the MBO when F3 F4 is invoked, all
operations will stop, any open message files closed and the
system will send:

      PLEASE STANDBY...

At that point you may converse with the user.  F3 F4 again will
return the system to MBO mode.  Once out of MBO mode the program
operates as an ordinary AMTOR terminal program and may be used to
call stations, send files manually, etc.

     If a station that you want to talk to has logged off before
you could catch them just press F9 F6 with the keyboard set to
AMTOR and if the other station is still on the frequency the link
will be re-established.

Whenever an ARQ call is initiated (F9 F6) the MBO mode is
switched off.  It may be restored by the F3 F4 toggle.


USING THE PRINTER

     If the printer has been declared in the configuration file
it is available to the Sysop for either logging or printing
messages.

     To log a channel to the printer, put the keyboard in that
channel mode and press F7 F10.  To return the printer to standby
put the keyboard in SYSOP mode and press F7 F10.


THE MCB EDITOR

     Each message in the system has a tag record called a message
control block maintained in a separate file.  This record
contains pertinent information about the message such as its
type, filing time, from and to fields, etc., etc.  Any item of
data in the MCB may be changed by the Sysop except the message
number and the filing and forwarding times.  This is done with
the MCB Editor which is invoked on the Sysop's command line with:

   E <message number>

Once the Editor's window is opened on the display, typing any of
the following key words (upper or lower case) will change the
appropriate parameter in the MCB:

     AMTOR, PACKET, SYSOP, PRIVATE, BULLETIN
     NTS, HELP, CANCELLED, PENDING, FORWARDED, STATIC
     BID... TO... AT... FROM... BBS...

The TO, AT, FROM, and BBS fields may be changed by typing:

   TO <new field>,
   AT <new field>, etc...
      
Pressing return with no other entry will record any changes and
return to the SYSOP command line.


THE USER FILE MAINTENANCE PROGRAM

     Supplied with APLINK is the program USERS.EXE.  This program
can only be run when APLINK is not running, even if you are using
a multitasking system such as Desqview.  Operation of the program
is reasonably selfevident.  A user is automatically entered into
the USERS.APS file upon the first logging into APLINK.  A call
may also be entered directly with USERS.EXE.  

     There are a number of parameters that may be set for any
given user using USERS.EXE.  Here is a list and their meanings:

     NTS - No longer used.  Will eventually be replaced.

     MBO - Set this to YES for any APLINK station that you
          directly autoforward traffic to on AMTOR.  This enables
          that station read any uncancelled message in your
          system in order to obtain fills, and to enable the RF
          and RI commands.  

     DO NOT PURGE - Prevents removal of the station from the file
          when the user file maintenance program purge command is
          used.

     HFWD - Set this to YES for any APLINK station that you
          directly autoforward traffic to on AMTOR provided the
          other station has set this parameter for you.  The
          activates the new AMTOR autoforwarding protocol that
          provides for h-routing and bids/mids.  This is only
          available on version 5.0 or later.

     EXPERT - YES sets EXPERT mode for a user.  

     LOCKOUT - YES prevents the indicated call from logging into
          your system on AMTOR or PACKET.

     The LAST MESSAGE and LAST BULLETIN parameters cannot be
changed except to set them to zero with the zero command.  These
two parameters determine what number the message and bulletin
lists begin with.  

     LAST LOGIN shows the time and date of the last time the
indicated call logged into the system.  The purge command removes
all calls from the file that have not logged in within the last
180 days.


                           CHAPTER 10

                      Program Distribution

     APLINK is now being distributed by three methods.  There is
a free landline bbs at 512-690-5312 (San Antonio, TX).  It
accepts 1200 or 2400 baud, 8-bits, no parity, one stop pulse. 
Log in with your name and follow the instructions.  Load the file
named APFILES.EXE using XMODEM.  When APFILES.EXE is run it will
decompress in to a full set of program files.

If you have access to Compuserve (CIS), the latest version may be
downloaded from the Hamnet forum.  

A disk with all the APLINK files may be obtained by mail from
TAPR.  Send $2.00 US plus cost of postage if outside of North
America and specify that you want an APLINK disk.  It will come
in 5-1/4", 360 Kb, MS-DOS format.

      Tucson Amateur Packet Radio (TAPR)
      PO BOX 12925
      Tucson, AZ 85732
      USA
      
      TAPR Telephone: 602-749-9479


SYSOP ASSISTANCE

If you are having problems bringing up APLINK for the first time
please read, and then re-read the documentation provided on the
disk. Most questions received to date are covered in this
information.

If you still are having problems, or have other questions
relating to APLINK system operation please direct them, in
writing, to Craig, WA8DRZ/6:

     Craig McCartney, WA8DRZ
     160 Montalvo Road
     Redwood City, CA 94062
     USA
 
Via AMTOR, leave an note on the WA8DRZ/6 APLINK system on 20 or
30 meters.

Via Packet, send a message to: 

      WA8DRZ @ WA8DRZ.#NOCAL.CA.USA.NA  

Via CIS send a note on Hamnet or Email to user id 73126,3260.


                           APPENDIX A

                     Packet Channel Commands

     The following is a verbatim copy of the packet channel help
file included in the APLINK distribution:

APLINK PACKET Channel Commands:

B                   Bye - Log off the BBS.  Just disconnecting does
                    the same thing.

H                   Help - Sends this file.

I                   Info - Sends the Information file.

L                   List - Lists all messages.
L #                 List # - List all files from message #.
LB                  List all bulletins.
L< <call>           List From <call> - Lists all messages to
                    <call>.  If <call> is omitted it lists all
                    messages from you. 
L> <call>           List To <call> - Lists all messages to <call>. 
                    If <call> is omitted it lists all messages to
                    you.
LH                  List all help files.
LR                  List all users who have signed into the system in
                    the last 24 hours.
LP                  List all pending traffic (for MBO operators only).

LOGIN <call>        Logs you into the system by a call other than
                    the one that began the link.

NTS                 List all NTS messages that have not been
                    forwarded.

R #                 Read # - Read message #.
RN                  Read New - Read all new messages addressed to
                    you.

SP <call> @ <route> Send - Send a message to <call> (optionally)
                    at <route>. 
SB <name> @ <route> Send a general interest bulletin of <name>
                    (optionally) via <route>.
SB <name> @ <route> $<bid>  Send a general interest bulletin of <name>
                    via <route> using <bid>.  Note: A bid will be
                    assigned by the system if not entered by the user.
ST <id1> @ <id2>    Send NTS traffic using current conventions.

T                   Talk - Signal the Sysop.

V                   Version - Read system version number.

CANCEL #            Cancels message # if you are the originator.

There is no Kill command.  Messages that have been read or
forwarded will be deleted automatically from the system after 24
hours.  Unread messages will be deleted automatically after 21
days.  Bulletins will remain until the originator or the Sysop
cancels them.


                           APPENDIX B

                     AMTOR Channel Commands

     The following is a verbatim copy of the AMTOR channel help
files included in the APLINK distribution.

(File: HELP1) AMTOR CHANNEL COMMANDS

TYPE ANY OF THE FOLLOWING COMMANDS ON A NEW LINE AND END WITH
EITHER (CR/LF) OR THE + ? SEQUENCE (BUT NOT BOTH).  IF YOU DO NOT
USE THE + ? SEQUENCE THE SYSTEM WILL CHANGE THE DIRECTION OF THE
LINK FOR YOU WHEN IT RECOGNIZES A VALID COMMAND. 

H OR HELP - SEND THE HELP FILE

CNCN - CANCEL WHATEVER IS IN PROGRESS. (USUALLY A MESSAGE YOU ARE
       ENTERING INTO THE SYSTEM)
       
LOGIN (YOUR CALL) - LOGS YOU IN
LOGON (YOUR CALL) - SAME AS LOGIN

L - LIST ALL AVAILABLE MESSAGES IN THE SYSTEM, NOT INCLUDING
    BULLETINS (SEE NOTE)
L (NUMBER) - AS ABOVE EQUAL OR GREATER THAN (NUMBER) 
LTO OR LM - LIST ALL MESSAGES TO YOU
LTO (CALL) - LIST ALL MESSAGES TO (CALL)
LFM - LIST ALL MESSAGES FROM YOU
LFM (CALL) - LIST ALL MESSAGES FROM (CALL)
LT - LIST ALL NTS MESSAGES
LB - LIST ALL GENERAL INTEREST BULLETINS (SEE NOTE)
LB (NUMBER) - AS ABOVE EQUAL OR GREATER THAN (NUMBER) 
LR - LIST AMTOR USERS WHO HAVE LOGGED ON IN THE PAST 24 HOURS 
LP - LIST ALL PENDING TRAFFIC (FOR OTHER MBO STATIONS ONLY)

NTS - LIST ALL UNFORWARDED NTS MESSAGES

RN OR RM - READ ALL NEW MESSAGES ADDRESSED TO YOU 
R (NUMBER) - READ MESSAGE (NUMBER)
RH (NUMBER) - READ MESSAGE (NUMBER) INCLUDING ROUTING HEADERS

SP (CALL) - SEND A MESSAGE TO (CALL), END WITH NNNN 
SB (NAME) - ENTER A BULLETIN WITH (NAME), END WITH NNNN 
SB (NAME) AT (ROUTE) BID (BID) - ENTER A BULLETIN WITH (NAME) AT
            (ROUTE) WITH A BID OF (BID)

SP (CALL) AT (ROUTE) - SEND A MESSAGE TO (CALL) TO BE FORWARDED
   VIA (ROUTE)
ST (ZIPCODE) AT (NTS STATECODE) - SEND AN NTS MESSAGE (USE       
   ACCEPTED NTS SUBJECT AND MESSAGE FORMAT)
 
NNNN - END A MESSAGE.  MUST HAVE BEEN STARTED WITH SP, SB, OR ST. 
   
CANCEL (NUMBER) - CANCELS MESSAGE (NUMBER) IF ORIGINATED BY YOU

T - TALK TO THE SYSOP

I - INFORMATION ABOUT THIS SYSTEM

V - READ VERSION NUMBER

A - (AFTER SEIZING THE LINK) ABORT A FILE BEING RECEIVED

LOGOUT - LOGS YOU OFF
LOGOFF - SAME AS LOGOUT

/// - ANYWHERE ON THE LINE CANCELS THE LINE (EXCEPT IN MESSAGES)

NOTE: THE L, AND LB COMMANDS WILL ONLY LIST MESSAGES YOU HAVE NOT
PREVIOUSLY LISTED.  FOLLOW THE COMMAND WITH A NUMBER TO OVERRIDE
THIS FEATURE.  USE 0 TO LIST ALL MESSAGES IN THE CATEGORY.

HERE IS SOME SPECIAL COMMANDS FOR THE EXPERT USER:

EXPERT - TOGGLES THE 'EXPERT' MODE
RI - READS THE MBO'S INTERCEPT FILE 
RF - READS THE MBO'S AMTOR AUTOFORWARD ROUTING FILE 
   NOTE: RI AND RF ARE AVAILABLE TO OTHER MBO'S ONLY
F - (AFTER SEIZING THE LINK) ABORT A FILE BEING RECEIVED AND MARK
 IF FORWARDED IF IT IS FOR YOU.  (THIS IS FOR USE WITH          
 DUPLICATE MESSAGES.)


(File: HELP2) LOGGING IN ON AMTOR

THIS MBO HAS AN AUTOMATIC LOGIN PROCEDURE FOR REGISTERED STATIONS
WITH AUTOMATIC ANSWERBACK (AAB) ENABLED.  WHEN YOU FIRST LINK WITH
THE SYSTEM, IT SEIZES THE LINK, IDENTIFIES, SENDS A 'WRU' CHARACTER
(FIGS-D), AND WAITS FOR AN ANSWERBACK RESPONSE.  THE EXPECTED
RESPONSE IS: 

(CR/LF)QRA CALL SELCAL + ?

OR 

(CR/LF)DE CALL SELCAL + ? 

FOR EXAMPLE '(CR/LF)QRA WA8DRZ WDRZ + ?' IS TYPICAL RESPONSE.

IF NO AAB RESPONSE IS RECEIVED THE SYSTEM SENDS A MANUAL LOGIN
REQUEST FOLLOWED BY THE + ? SEQUENCE.  AT THIS POINT A USER SHOULD
SEND EITHER 'LOGIN (CALL)(CR/LF)' OR 'LOGON (CALL)(CR/LF)'.  IF THE
CALL HAS BEEN REGISTERED THE SYSTEM WILL RESPOND WITH A 'GA'
PROMPT.  IF AN ERROR WAS RECEIVED OR THE CALL IS NOT REGISTERED THE
SYSTEM WILL ASK YOU TO CONFIRM THE CALL.  IF YOU ANSWER THE
CONFIRMATION REQUEST WITH 'YES' THE CALL BECOMES REGISTERED.

APLINK WILL DISCONNECT AFTER THREE MINUTES IF NO LOGIN HAS BEEN
RECOGNIZED.

ONCE YOU HAVE LOGGED ON, THE SYSTEM IS READY FOR YOUR COMMAND
WHENEVER IT SENDS A 'GA' (GO AHEAD) PROMPT.

YOU MAY LOG OUT OF THE SYSTEM WITH 'LOGOUT(CR/LF)' OR 'LOGOFF(CR/LF)'.
ANY TIME THE LINK IS LOST THE CURRENT USER IS AUTOMATICALLY LOGGED
OUT.

IF A MESSAGE IS BEING SENT TO THE SYSTEM DURING A LINK FAILURE,
THAT PART OF THE MESSAGE THAT WAS RECEIVED IS FILED AND IS
AVAILABLE TO THE ADDRESSEE.


(File: HELP3) RECEIVING YOUR MESSAGES ON AMTOR

THE QUICKEST AND SIMPLEST WAY TO RECEIVE YOUR MESSAGES IS TO GIVE
THE 'RN' (MEANING 'READ NEW') COMMAND AS SOON AS YOU SIGN ON.  ALL
MESSAGES IN THE SYSTEM NOT ALREADY MARKED 'FORWARDED' WILL BE
TRANSMITTED TO YOU AUTOMATICALLY WITHOUT FURTHER ACTION ON YOUR
PART.  AS EACH MESSAGE IS COMPLETELY FORWARDED TO YOU IT IS MARKED
'FORWARDED' AND WILL NOT BE TRANSMITTED AGAIN WITH THIS COMMAND. 
(YOU MAY READ IT AGAIN WITH THE 'R (NUMBER)' COMMAND.

IF YOU ARE RECEIVING AN UNFORWARDED MESSAGE AND THE LINK IS LOST
IT WILL STILL BE AVAILABLE TO THE 'RN' COMMAND.

IF YOU HAVE LOGGED INTO THE SYSTEM WITH YOUR AUTOMATIC ANSWERBACK
THEN THE SYSTEM WILL MARK YOUR MESSAGES 'FORWARDED' ONLY AFTER IT
TRIGGERS YOUR ANSWERBACK AT THE END OF EACH MESSAGE.

YOU DO NOT HAVE TO (IN FACT, CANNOT) DELETE A MESSAGE.  ONCE IT IS
FORWARDED THE SYSTEM WILL DELETE IT 24 OR MORE HOURS LATER.  IN THE
MEANTIME IT MAY BE READ AGAIN USING THE 'R (NUMBER)' COMMAND.

USE THE LIST COMMANDS TO SEE WHAT MESSAGES ARE AVAILABLE.


(File: HELP4) ENTERING A MESSAGE ON AMTOR

MESSAGES MAY BE ENTERED DIRECTLY FROM YOUR KEYBOARD INTO THE
SYSTEM, HOWEVER IT IS BETTER IF YOU PREPARE A FILE BEFORE LOGGING
ON AND THEN SEND IT AT MACHINE SPEED.  THIS REDUCES THE CONNECT
TIME TO THE SYSTEM AND THE POTENTIAL FOR TRANSMISSION ERRORS.

YOU MAY SEND THREE KINDS OF MESSAGES:

'SP (CALL)' WHICH IS A MESSAGE TO A SPECIFIC STATION AND MAY ONLY
BE READ BY THAT STATION (OR YOU OR THE SYSOP) AND WILL APPEAR ON
THE MESSAGE LIST ONLY FOR THOSE STATIONS.  FOR OTHERS, IT SIMPLY
ISN'T THERE.  'SP' MESSAGES WILL REMAIN IN THE SYSTEM FOR 21 DAYS
OR 24 HOURS AFTER BEING MARKED 'FORWARDED', WHICHEVER COMES FIRST.

'SP' TYPE MESSAGES MAY ALSO BE ENTERED FOR AUTOMATIC FORWARDING TO
ANOTHER MBO/BBS.  THEY MAY BE ENTERED IN THE FORM 'SP (CALL) TO
(ROUTE)' WHERE (CALL) IS THE ADDRESSEE AND (ROUTE) IS THE
HIERARCHICAL ROUTE TO HIS LOCAL MBO/BBS.  SINCE AMTOR DOES NOT
PROVIDE FOR A NUMBER SIGN CHARACTER, USE THE EQUAL SIGN CHARACTER IN
ITS PLACE WHEN REQUIRED IN AN H-ROUTE ADDRESS AND APLINK WILL CONVERT
IT TO A NUMBER SIGN CHARACTER.

'ST (ZIPCODE) TO (NTS STATECODE)' IS USED TO ENTER A MESSAGE TO
ANYONE TO BE DELIVERED BY THE NATIONAL TRAFFIC SYSTEM. THE SUBJECT
(FIRST LINE) SHOULD READ: QTC (CITY, STATE) AND THE BODY OF THE
MESSAGE SHOULD BE IN STANDARD ARRL MESSAGE FORMAT.

'SB (ID)' ADDRESSES A MESSAGE TO 'ID' AND MARKS IT AS A BULLETIN. YOU
MAY ALSO INCLUDE A BULLETIN IDENTIFICATION (BID) BY ADDING 'BID '
FOLLOWED BY THE BID ON THE SAME LINE.  FOR EXAMPLE:

   SB ALL BID 12345W1ABC
   
IS A MESSAGE TO 'ALL' WITH A BID OF 12345W1ABC.   BULLETINS WITHOUT A
BID WILL NOT BE FORWARDED.

BULLETIN TYPE MESSAGES WILL REMAIN IN THE SYSTEM UNTIL REMOVED
(CANCELLED) BY EITHER THE ORIGINATOR OR THE SYSOP.

TO SEND A MESSAGE, TYPE THE COMMAND (I.E., 'SP W5SMM(CR/LF)') AND
WAIT FOR A RESPONSE FROM THE SYSTEM.  THE LINE WILL BE TYPED BACK AND
YOU WILL BE REQUESTED TO CONFIRM WITH 'YES' OR 'NO'.  AT THE 'GA
SUBJ/MSG' PROMPT TYPE THE SUBJECT OF THE MESSAGE ON ITS OWN LINE AND
THEN ENTER THE TEXT OF THE MESSAGE.

AT THE END OF THE MESSAGE SEND 'NNNN' ON A NEW LINE.  'NNNN'
EMBEDDED IN TEXT IS IGNORED.  AFTER SENDING 'NNNN' WAIT FOR A NEW
'GA' PROMPT TO ENTER A NEW COMMAND.

IDENTIFY YOUR STATION AT REGULAR INTERVALS BY SENDING YOUR
IDENTIFICATION AFTER A 'GA' PROMPT.  ANY CHARACTER SEQUENCE THAT
IS NOT A VALID COMMAND IS IGNORED BY THE SYSTEM.

IF YOU HAVE ALREADY SENT A PARTIAL COMMAND LINE AND WANT TO CANCEL
THE LINE JUST SEND THREE OR MORE '/'S IN A ROW ANYWHERE ON THE
LINE.  THAT LINE WILL BE IGNORED.  THIS ONLY WORKS ON COMMAND
LINES.  /// IMBEDDED IN A MESSAGE WILL BE PASSED ON TO THE
ADDRESSEE.

AFTER YOU HAVE TRANSMITTED A MESSAGE YOU MAY CANCEL IT WITH THE
'CANCEL (NUMBER)' COMMAND.  THIS IS NORMALLY USED TO ONLY REMOVE
A BULLETIN YOU HAVE PLACED IN THE SYSTEM, BUT IT MAY BE USED TO
REMOVE ANY MESSAGE YOU HAVE PREVIOUSLY SENT.


(File: HELP5) MESSAGE LIST EXPLANATION

THE FORMAT FOR THE MESSAGE LIST IS SIMILAR TO THAT OF COMMONLY USED
PACKET BBS PROGRAMS.  THE SYMBOLS FOR TYPE AND STATUS ARE
CONSISTENT WITH THE PACKET SYSTEM.

MSG = MESSAGE NUMBER (ASSIGNED BY THE SYSTEM)

T = MESSAGE TYPE AS FOLLOWS:
 P - A PRIVATE MESSAGE, MAY ONLY BE READ BY THE ADDRESSEE,       
     ORIGINATOR OR SYSOP  
 B - A BULLETIN
 T - AN NTS MESSAGE

S = STATUS AS FOLLOWS:
 N - MESSAGE NOT YET ACCESSED BY, DELIVERED, OR FORWARDED TO THE
     ADDRESSEE  
 + - SAME AS 'N' EXCEPT OVER 24 HOURS OLD
 ++ - SAME AS 'N' EXCEPT OVER 48 HOURS OLD    
 Y - MESSAGE FORWARDED TO THE ADDRESSEE OR ANOTHER MBO/BBS  

TO = CALL OF ADDRESSEE

AT = CALL OF ADDRESSEE'S BBS (IF FOLLOWED BY A PERIOD WHEN HIERARCHICAL
     ROUTING IS USED.

FROM = CALL OF ORIGINATOR

FILED = DATE/TIME MESSAGE WAS ENTERED INTO THE SYSTEM

SUBJECT = THE SUBJECT LINE OF THE MESSAGE


(File: HELP6) LISTING MESSAGES

THERE ARE SEVERAL COMMANDS FOR LISTING MESSAGES THAT ARE IN THE
SYSTEM.  THE 'LTO (CALL)', AND 'LFM (CALL)' ('LIST TO' AND 'LIST
FROM') DEFAULT TO THE CALL OF THE USER LOGGED INTO THE SYSTEM IF
NO ARGUMENT IS GIVEN.  

THE 'L', AND 'LB' COMMANDS WHEN GIVEN WITHOUT ARGUMENTS WILL LIST
ONLY MESSAGES NOT PREVIOUSLY LISTED FOR YOU.  YOU MAY OVERRIDE THIS
FEATURE BY ADDING A NUMBER FOLLOWING THE 'L', OR 'LB'. THE ARGUMENT
0 WILL LIST ALL THE MESSAGES IN THE CATEGORY.

NTS MESSAGES THAT ARE WAITING TO BE DELIVERED MAY BE LISTED WITH THE
'NTS' COMMAND.  THIS IS THE PREFERED WAY TO LIST NTS TRAFFIC.  THE
'LT' COMMAND WILL ALSO LIST NTS TRAFFIC BUT INCLUDES TRAFFIC THAT HAS
ALREADY BEEN PICKED UP.

MESSAGES THAT HAVE BEEN CANCELLED WILL NOT APPEAR ON THE MESSAGE
LIST EVEN THOUGH THEY MAY STILL BE IN THE SYSTEM.

MESSAGES THAT ARE TYPE 'PRIVATE' WILL ONLY APPEAR ON LISTS FOR THE
ADDRESSEE AND ORIGINATOR OF THE MESSAGE.

READ THE HELP FILES NAMED 'SYSTEM MAINTENANCE' AND 'MESSAGE LIST
EXPLANATION'.


(File: HELP7) SYSTEM MAINTENANCE

THE MAINTENANCE ROUTINES FOR THIS SYSTEM ARE TYPICALLY RUN ONCE A
DAY BY THE SYSOP.  AT THAT TIME THE FOLLOWING RULES APPLY TO ALL
MESSAGE FILES:

1. ALL MESSAGES MARKED CANCELLED ARE REMOVED.

2. ALL MESSAGES MARKED AS FORWARDED FOR MORE THAT 24 HOURS ARE
REMOVED.
   
3. ALL MESSAGES EXCEPT BULLETINS THAT ARE OVER 21 DAYS OLD ARE
REMOVED.


(File: HELP8) AMTOR PORT OPERATING HINTS

IF YOU HAVE BEEN SITTING IDLE FOR A FEW SECONDS BEFORE TYPING A
COMMAND, TYPE CR/LF JUST BEFORE ISSUING THE COMMAND.  THIS CLEARS
ANY STRAY LEADING CHARACTERS FROM THE BUFFER THAT MAY HAVE BEEN
RECEIVED IN ERROR DURING THE IDLE PERIOD.

IF YOU GET A LONG FILE STARTED AND WOULD LIKE TO ABORT, SIMPLY
SEIZE THE LINK, WAIT FOR IDLE STATUS ON YOUR AMTOR TERMINAL, AND
TYPE 'A' (CR/LF).  THE SYSTEM WILL RETURN A 'BK GA' PROMPT AND
ACCEPT A NEW COMMAND FROM YOU.

REMEMBER THAT THE FIRST LINE OF A MESSAGE WILL APPEAR ON THE
MESSAGE LIST AS THE SUBJECT.  MAKE IT MEANINGFUL TO SOMEONE
SCANNING THE LIST.


(File: HELP9) USING 'EXPERT' MODE

AN 'EXPERT' MODE HAS BEEN ADDED.  IT IS TOGGLED BY THE AMTOR USER BY
ENTERING THE COMMAND 'EXPERT'.  THE EXPERT MODE SHORTENS THE EXCHANGE
WHEN ENTEREING A NEW MESSAGE.  WHEN ON, THE BEGINNING OF A MESSAGE
LOOKS LIKE THIS:

FROM USER:    SP W1ABC AT WA8DRZ.=NOCAL.CA
FROM SYSTEM:  SP W1ABC AT WA8DRZ.=NOCAL.CA GA SUBJ/MSG+?

IF THERE IS A HIT IN THE RESPONSE THE USER MUST TYPE THE 'CNCN' COMMAND
TO KILL THE MESSAGE AND START OVER.  NNNN, OF COURSE, FILES THE MESSAGE.
CNCN MAY BE TYPED ANYWHERE IN THE MESSAGE ON A LINE BY ITSELF.