Configuration file - BPQCFG.TXT



PORTS Section.


This section of the configuration file defines the links from the switch
to the outside world. These will normally be Radio links, but could also
be a link to another computer running another copy of the switch, or similar
software (eg NOS).

Please note that there is no relationship between the 'Virtual' COM ports
defined in the TNCPORT section, which are used by the BBS or other program
running abouve the switch, and these external links. You may use your 
'real' COM1 port to connect to a KISS TNC, even if you have defined a 
'Virtual' COM1 in the TNCPORT section. 


There are two basic classes of links supported by the switch. One uses 
normal ASYNC ports to communicate with TNCs running in KISS mode, and the
other uses special HDLC cards which fit inside the PC, and interface to
the radio via either an inbuilt or external  modem. Those currently supported
are the PacCom PC120, DRSI PC-PA, and Thor RLC100.


Interrupt levels may be shared by any cards with suitable hardware.
Examples are all but the earliest DRSI cards, and a MS400 ASYNC card 
modified as described by AA4RE in his MBBIOS documentation. However
there is a significant overhead in using the shared interrupt feature
- try to use it on relatively low speed links, and watch out for TX
underruns/RX overuns.


Each port is defined by a set of statements of the form:


PORT

	PARAM=VALUE
	..
	..

ENDPORT


Samples of various configurations are given later, but the full list
of PARAM values supported is given below


PORTNUM=n	; Number for use in PORTS display, connects, etc.
		; Default is next sequential number.

ID=text string *; Up to 30 chars, appears on PORTS display

TYPE=ASYNC/DRSI/PC120/RLC100/QUAD/INTERNAL *

		; ASYNC is for a normal ASYNC card, or a shared interrupt card 
		; such as the MS400

		; PC120, DRSI and RLC100 are the internal HDLC cards - and
		; support 2 channels.

		; QUAD is the Quadram Quadport, which allows up to 5 async
		; links. This version only supports a single Quadport. See
		; later section for setup details.

		; INTERNAL defines a 'loopback' port - anything
		; sent on it will be received.Intended to allow KISS
		; applications (eg TCP/IP) to talk to the switch.

PROTOCOL=HDLC/KISS/NETROM *

		; NETROM is to connect to the async port of a real NETROM  

IOADDR=xxxH *	; in hex, H is needed

INTLEVEL=n *	; 2,3,4,5 or 7 - supports shared interrupt cards

SPEED=nnnn *	; Radio speed for DRSI, etc, async link speed for KISS
		; If set to zero, the modem must supply a 1x clock. 
		; (TXC on RTXC pin, RXC on TRXC pin.)

CHANNEL=A/B/..*	; Selects port on DRSI/PC120, dual port KISS (eg KPC4) or
		; Multidropped KISS

BBSFLAG=NOBBS	; Stops direct connects to the BBS on this port.

QUALITY=nnn *	; Default quality for nodes heard on this port. Set to zero
		; to suppress all level 3/4 activity (including NODES
		; broadcasts) on this port.

MAXFRAME=n *	; Maximum outstanding frames

TXDELAY=nnn *	; TX Keyup delay in milliseconds

SLOTTIME=100 *	; CSMA interval timer (milliseconds)

PERSIST=nnn *	; 'Probability to transmit' value (1-255)

FULLDUP=0/1	; Passed on to TNC if using KISS. Used to allow transmission
		; whilst DCD is active on HDLC cards, and to allow connection
		; of a NETROM cluster via a diode matrix.

SOFTDCD=0/1	; not yet supported

TXTAIL=nnnn	; TXTAIL timer in ms. Used only by KISS TNCs. If running on
		; HF at 300 baud, the default is probably too short. If others
		; have trouble copying your frames, try a value of 50 - 100.

FRACK=nnnn *	; Level 2 timout in milliseconds

RESPTIME=nnnn *	; Level 2 delayed ack timer in milliseconds

RETRIES=n *	; Level 2 maximum retry value

PACLEN=nnn *	; default maximum packet length for this port

CWID=CALL	; Currently only supported on DRSI/PC120/RLC100 

PORTCALL=CALL	; Additional callsign/alias for level 2 connects to the
PORTALIAS=ALIAS ; node for this port. Should not be the same as BBSCALL

ALIAS_IS_BBS=0/1; If set then PORTCALL and PORTALIAS give access to the BBS
		; rather than the node. 

VALIDCALLS=CALLS; Up to about 40 callsigns, separated by single commas.
		; If present, only stations in the list will be allowed
		; to connect to you on this port. The SSID should not 
		; be specified, and multiple VALIDCALLS lines may be 
		; included. End all but the last line with commas. The
		; total length of the list, including commas, is 256 bytes.

QUALADJUST=NNN	; Percentage to reduce the quality of a NODE in the NODES 
		; broadcast, if the best neighbour is on the same port as
		; the broadcast. Designed to improve throughput if more than
		; one channel is available, by discouraging routes which 
		; cause a node to send a packet on the same port that it
		; received it on.


DIGIFLAG=0/1/255; Digipeat control flag for this port
		; 0 = dont digi, 1 = digi everything, 255 = digi UI frames only


DIGIPORT=N	; Port to send digied frames on. Zero means the port it was
		; received on, any other number means send on that port. 
		; This is intended mainly to allow a BBS on another machine,
		; connected via a wire link, to send out 'MAIL FOR' messages.


USERS=N		; This limits the number of L2 sessions to the supplied 
		; number. Zero means no limit. The limit applies to all
		; L2 sessions (even those with other nodes), but is only
		; checked for incoming connects (ie you can make outgoing
		; connects even when the limit is reached). Intended mainly
		; to control the number of users on busy user access ports
		; (especially 2m)


UNPROTO=	; Unproto destination and digi string for this port. 
		; Use commas between calls, and dont include the VIA.

L3ONLY=0/1	; If set, will stop users (but not HOST sessions) issuing
		; downlink connects on this port. 

INTERLOCK=n	; Allows groups of ports to be defined which will not transmit
		; at the same time. A value of zero indicates no locking, if
		; any other value is specifed the code will make sure that no
		; two ports with the same value can transmit at the same time.

KISSOPTIONS=POLLED,CHECKSUM,ACKMODE

	These select my extended KISS mode.
	
	These extended KISS options are supported by my BPQKISS EPROM for
	the TNC2 and clones, and by special EPROMS for the KPC2, KPC4 and
	KAM, available from Kantronics.

	POLLED selects multi-dropped mode, where the TNC only
	transmits when requested (Polled) by the PC. This allows
	several TNCs to share an async port without any risk of
	collisions.
	
	CHECKSUM selects a mode where a checksum byte is appended
	to each data message, and checked by the other end. This
	reduces the risk of data corruption if errors occur on the
	link from PC to TNCs. It may be used on its own, but should
	always be used if POLLED mode is selected.
	
	ACKMODE enables the transmission of 'ACK required' frames.
	There cause the TNC to send a reply when the frame has been
	transmitted. This will improve link performance by avoiding
	the possibility of a retry being sent before the original
	frame has even left the TNC. This mode should always be used
	if the TNC support it.
	
	


Parameters marked with a * must be included, the rest are optional. The 
validation is not good, and defaults are generally zero, so if you miss 
out any of the essential ones, odd things may well happen!



Sample PORT Configurations:


1. 2 Port DRSI card set for IO addr = 300h, int level 5


PORT
	ID=144.650 MHz 1200 Baud
	TYPE=DRSI
	PROTOCOL=HDLC
	IOADDR=300H
	INTLEVEL=5
	SPEED=1200
	CHANNEL=A
	QUALITY=10
	MAXFRAME=1
	TXDELAY=500
	SLOTTIME=100
	PERSIST=64
	FULLDUP=0
	SOFTDCD=0
	FRACK=7000
	RESPTIME=2000
	RETRIES=10
	PACLEN=120
	CWID=G8BPQ

ENDPORT
;
PORT
	ID=432.675 MHz 1200 Baud
	TYPE=DRSI
	PROTOCOL=HDLC
	IOADDR=300H
	INTLEVEL=5
	SPEED=1200
	CHANNEL=B
	BBSFLAG=NOBBS			; IF MY BBS LICENCE IS ONLY FOR 2M
	QUALITY=10
	MAXFRAME=1
	TXDELAY=500
	SLOTTIME=100
	PERSIST=64
	FULLDUP=0
	SOFTDCD=0
	FRACK=6000
	RESPTIME=1500
	RETRIES=10
	PACLEN=120
	CWID=G8BPQ
	PORTCALL=G8BPQ
	PORTALIAS=NOTTM
;
ENDPORT


2. Standard KISS TNC on primary ASYNC card. (COM1). To use the secondary
   ASYNC card (COM2), change IOADDR to 2F8H, and the INTLEVEL to 3.  


PORT
	ID=144.650 Mhz 1200 Baud
	TYPE=ASYNC
	PROTOCOL=KISS
	IOADDR=3F8H
	INTLEVEL=4
	SPEED=9600
	CHANNEL=A
	QUALITY=10
	MAXFRAME=2
	TXDELAY=500
	SLOTTIME=100
	PERSIST=64
	FULLDUP=0
	FRACK=7000
	RESPTIME=2000
	RETRIES=10
	PACLEN=120

ENDPORT

The second port of a multiport TNC (Such as the KAM or KPC 4) is defined as
follows:

	ID=432.675 Mhz 1200 baud
	TYPE=ASYNC
	PROTOCOL=KISS
	IOADDR=3F8H
	INTLEVEL=4
	SPEED=2400
	CHANNEL=B
	QUALITY=10
	MAXFRAME=2
	TXDELAY=500
	SLOTTIME=100
	PERSIST=64
	FULLDUP=0
	FRACK=7000
	RESPTIME=2000
	RETRIES=10
	PACLEN=120
	QUALADJUST=5

ENDPORT



3. Quadram Quadport.

The Quadram Quadport card supports up to 5 (yes I know it says quadport!!)
async ports. This version only supports one card - if anyone needs more,
let me know. You do not need to define all ports, but you must start with
the first, and not leave any gaps.

The card should be configured with first port at 280h, and software 
selectable interrupts (3 or 4 may be used)

The card will support KISS TNCS (either normal, or KPC4 type dual port), or
NETROM links (or a combination of both). 


The following sample config file is for a Dual Port KPC4 on channel 1,
a normal KISS TNC on channel 2, and a NETROM async link on channel 3.


PORT
	ID=KPC4 PORT 1
	TYPE=QUAD
	PROTOCOL=KISS
	IOADDR=280H
	INTLEVEL=3
	SPEED=2400
	CHANNEL=A
	QUALITY=10
	MAXFRAME=2
	TXDELAY=500
	SLOTTIME=100
	PERSIST=64
	FULLDUP=0
	FRACK=7000
	RESPTIME=2000
	RETRIES=10
	PACLEN=120

ENDPORT

PORT
	ID=KPC4 PORT 2
	TYPE=QUAD
	PROTOCOL=KISS
	IOADDR=280H
	INTLEVEL=3
	SPEED=2400
	CHANNEL=B
	QUALITY=10
	MAXFRAME=2
	TXDELAY=500
	SLOTTIME=100
	PERSIST=64
	FULLDUP=0
	FRACK=7000
	RESPTIME=2000
	RETRIES=10
	PACLEN=120

ENDPORT

PORT
	ID=NORMAL KISS
	TYPE=QUAD
	PROTOCOL=KISS
	IOADDR=290H
	INTLEVEL=3
	SPEED=2400
	CHANNEL=A
	QUALITY=10
	MAXFRAME=2
	TXDELAY=500
	SLOTTIME=100
	PERSIST=64
	FULLDUP=0
	FRACK=7000
	RESPTIME=2000
	RETRIES=10
	PACLEN=120

ENDPORT

PORT
	ID=NETROM BACKEND
	TYPE=QUAD
	PROTOCOL=NETROM
	IOADDR=2A0H
	INTLEVEL=3
	SPEED=2400
	CHANNEL=A
	QUALITY=10
	MAXFRAME=2
	TXDELAY=500		; THESE AREN'T USED, BUT I SUGGEST  
	SLOTTIME=100		; YOU PUT THEM IN IN CASE ONE DAY
	PERSIST=64		; THEY ARE!
	FULLDUP=1		; THIS IS NOW NEEDED FOR A SINGLE NETROM
				; TNC. SET TO 0 IF USING A DIODE MATRIX.
	SOFTDCD=0
	FRACK=7000
	RESPTIME=2000
	RETRIES=10
	PACLEN=120

ENDPORT