Name: NBSTIME

Usage: NBSTIME [ -d ]

     This program is used to set or check the date and time on an IBM personal 
computer (or equivalent) using data obtained by dialing the NBS using a Hayes 
compatible modem connected to the computer via one of the COM ports. It can 
also be used to provide an output pulse on the line-printer port once per 
second to synchronize other devices.
     The different operating modes are selected by means of a configuration 
file.  A separate program called MAKCFG (described in more detail below) can be 
used to make this file based on your answers to a series of questions. You may 
also generate or modify this file using any text editor.  Once the 
configuration file is prepared, you start the program by typing the command  
NBSTIME <return> in response to the system prompt.
    The switch -d on the command line is optional.  If present, it specifies 
debug mode, and causes various intermediate parameters to be written to the 
screen.  The default is no debug mode.  The brackets enclosing the -d are meant 
to signify that the switch is optional.  They are never entered on the command 
line.
     See the section below on operating instructions for more information.

                                       The Configuration File

    The name of the configuration file is nbstime.cfg.  It must be located in 
the same directory from which the program will be run.  The configuration file 
may be prepared with a text editor such as EDLIN.  Alternatively, it may be
generated using program MAKCFG, described below.
     The file contains 5 lines in the following format:

     Line 1: Dialing mode and telephone number.  The first character on line 1
must be P, T or M.  P means that the modem will dial the telephone number
using pulse mode (which emulates a rotary dial mechanism), T is for tone mode
(which emulates push-button telephones) and M is for manual dialing (which
means that the telephone connection will be completed manually outside of the
program).  In pulse mode or tone mode, the remaining characters on the line
are the digits 0 - 9, a space or a comma.  (Some modems will also accept the *
and # symbols as part of the telephone number in tone mode and will dial them
as well).  The telephone number is not modified by the program and the entire
string is passed to the modem.  This line must contain the complete telephone
number including long-distance access and area code (if necessary) and any
other accounting digits as needed.  A comma signifies a pause for 2 seconds to
wait for another dial tone, and spaces may be inserted to improve legibility.
For example:  T 9, 987 6 5 4 3 means dial 9, wait 2 seconds and then dial the
remaining digits.  All digits are dialed in tone mode.  The telephone number
must be less than 30 characters long including embedded blanks.  If the first
character is M, then manual dialing is specified and the remainder of the line
is ignored.  The program will prompt you to dial the telephone manually and
will wait until you indicate that the connection is completed.

     Line 2: The first character must be 1 or 2 to specify communication via
COM1 port or COM2 port, respectively.  This character must be set to match the
port to be used.
     The second character on the line may be B (or b) or E (or e).  This
character specifies whether the program is to expect responses to various
dialing commands from the modem.  E specifies echo mode:  the program expects
that characters sent to the modem in command mode will be echoed and that the
modem will respond OK to a command; B specifies blind operation.  Some modems
can be configured either way either by a switch or the Q command.  (A modem
configured by the Q command will revert to the switch default upon reset.)  If
the second character on the line is neither B nor E, then E is set by default.
Note that when the program is configured for echo mode (by specifying E
explicitly or by default) then it will insist on responses and will abort if
they are not received.
    The third character on the line specifies the communication speed (and,
implicitly, the communication protocol).  If the third character is h (or H),
then 1200-bits/s high-speed communication is selected using the 212A-type
protocol.  If l (or L) is used, then 300-bits/s low-speed service is selected
using 103-type protocol.  Many modems are capable of operating at either
protocol (such dual-speed modems are often identified as "300-1200" type) and
will switch to the correct speed and protocol automatically when then are
activated.  Triple-speed modems of the "300-1200-2400" type may also be used
at either 300 or 1200 bits/s.
     Different messages are transmitted depending on the speed selected.  The
message transmitted at 1200-bits/s contains the full date and time, including
the Daylight-Savings Time flag and other information.  This service is
intended for users who want to set or check the time of the computer clock
with an uncertainty on the order of 10 - 20 milliseconds limited by the
resolution and accuracy of the internal computer clock.  See the discussion
below for more information.
     The message transmitted at 300-bits/s is shorter because of the slower
transmission speed, and contains only the time and the estimated line delay in
milliseconds.  Therefore, it is not possible to set the computer clock since
neither the date nor the correction for Daylight Savings Time are transmitted
(the conversion to local time in the United States, for example, will change
the date about 30% of the time, and the correction for Daylight Savings Time
is necessary about 50% of the time.  It would be possible to assume that the
computer date is correct, but the program does not do so.).  This service is
intended for users who are more interested in the timing pulse capability (to
be described below) or who design special-purpose systems that can make use of
the full capability of the transmissons.
     The fourth character on this line selects a timing-pulse capability. If
this character is y (or Y), then a negative-going pulse (from +5 v to 0 v) is
sent to the strobe line of the line-printer port (LPT1) every second upon
receipt of the on-time marker (the * or # symbol at the end of each
transmitted line) from NBS.  The pulse is sent to pin 1 of the DB25 female
connector used for the standard line-printer interface.  Pin 25 of the same
connector is at ground potential.  The leading-edge of the pulse is delayed
from receipt of the on-time marker by a time on the order of micro-seconds,
depending on the speed of the computer.  The pulse is approximately 20 micro-
seconds wide.  This pulse is normally used by the printer interface software
to transfer a character from the computer to the line printer (-strobe), so
that the printer should be disconnected if this capability is enabled.
     There are three types of commonly used line-printer interfaces.  One of
them is part of a combined monochrome display and printer adapter.  The second
is just a printer adapter and the third is a combined serial/parallel adapter
that is normally found only on AT-type machines.  The command register address
for the first type is 3be (hex), while the second types both use 37a (hex).
If the strobe capability is enabled, the program tries to decide which type of
adapter is present by pulsing both addresses and finding the one that
responds.  If both are present, 37a will be used.  If neither responds as
expected, the program will print a diagnostic message to that effect, the
pulsing capability will be disabled and the program continues.
     The fifth character on the line determines whether or not the received
data will be used to set the computer clocks or merely to check them.  If this
character is s (or S), then the clocks are set and then verified by comparing
the time read from the internal clocks with the next line received from the
NBS (both the received time and the internal clocks will have advanced by one
second between the time they were set and when they were checked).  This mode
does not preserve the time of the clocks before they were set and does not
provide any information on the performance of the clocks.  If this character
is d (or D) then the clocks are only compared.  The NBS time, the computer
time and their difference are typed on the screen.  This mode preserves the
time of the clock (since it is not set), and can also be used to give an
estimate of the rate error (how much the computer clock is gaining or losing
with respect to NBS).  The rate error (expressed in seconds per day, for
example) is simply the time difference in seconds reported by the program
divided by the number of days since the clock was last set.  This mode of
operation is intended for users who want to characterize the performance of
their clocks by observing their accuracy over extended periods of time.
    The effect of this switch also depends on the the AT switch (described
below).  An IBM AT-type machine has two clocks -- one whose time is stored in
the volatile memory and which is updated by the ROM BIOS only when the
computer is turned on and one which is powered by a battery and which runs
continuously.  Other models (such as the XT-class machines) do not have a
battery clock.  This switch enables or disables the setting of BOTH clocks for
an AT-class machine and only the memory-based clock for other models.  That
is, both clocks are either set and verified or just compared.
     The sixth character on the line is used to enable storing time-difference
measurements in a file for subsequent more detailed analysis.  If this
character is a (or A), the time difference between the computer clocks and the
NBS is stored in a file named NBSTIME.DIF.  The program writes the current
time difference to the end of the file (if it currently exists) or creates a
new file if it does not.  The time difference is written in the form: year,
month, day, hour, minute, second, difference of volatile memory clock and
difference of battery clock (if it exists).  The year, month, etc. are taken
from the NBS transmission and the difference is a signed number which is
positive if the computer clock is fast and negative if it is slow.  The
difference is followed by a single letter giving the units: d, h, m, s for
days, hours, minutes and seconds respectively.  This computation is separate
from the setting or checking modes described above.  It is performed when the
fifth line is received from NBS, so that the difference will be written to the
file BEFORE the clocks are set (if that option is specified).  Although the
action of this switch is independent of whether the clocks are set, the
interpretation of the data is not.  If the fifth character specifies that the
clocks shall always be set, then the difference written to the file by this
operation is the time error that has accumulated since the last NBS access,
since the clocks were corrected at that time.  If the fifth character
specifies that the clocks are not to be set, however, then the time error is
the cumulative error since the clocks were last set, and the error since the
last NBS access is the difference between the current and previous values for
the differences.  If this character is n, then the time difference is not
stored in the archive file.
     The remainder of this line is ignored and may contain any characters.

     Line 3:  This line specifies the time zone of the user.  This parameter
is used to convert the time transmitted by the NBS from universal time to
local time.  The parameter represents the value of local time minus Universal
time in hours.  Locations West of Greenwich are negative, while those East are
positive.  If specified by value, the value should not exceed 12 hours, but
this is not checked.  The zone may be specified by name or numerically as
follows:

First character on line      Action            Offset in hours

P or p                       U. S. Pacific Time    -8

M or m                       U. S. Mountain Time   -7

C or c                       U. S. Central Time    -6

E or e                       U. S. Eastern Time    -5

Z or z                       Greenwich Time         0

+ or - or digits             Number read            defined by number

In all cases, the remainder of the line is ignored.  Thus the following lines
are equivalent:

Mountain Standard Time
m
-7     The Rocky Mountains are here

The program does not support conversion to local time in half-hour zones (i.e.
zones where the time difference between local time and Universal time is not
an integral number of hours).

     Line 4.  If the first character is 1, then the user observes Daylight
Savings Time, and the local time will be adjusted accordingly if necessary,
based on the Daylight Savings Time flag transmitted by NBS.  If the first
character is 0, the Daylight Savings Time flag is ignored and no such
adjustment will be made.  No other characters are permitted on this line.
If you use a 1 here, then the time will be advanced by one hour if the NBS
transmission indicates that Daylight Savings Time is currently in effect.
You will need to use 0 if you live in an area that does not observe Daylight
Savings Time at all (such as Arizona), or if you change to Daylight Time on a
different day from the national standard.

     Line 5.  This is called the AT-flag.  If the first character is 1, the
user has an AT-type machine with a CMOS battery clock, and the program will
set or check it (in addition to the clock that is stored in memory).  If the
first character is 0, the CMOS clock is neither set nor checked.  Zero is
appropriate for users who do not have a CMOS battery clock or who have this
type of equipment but do not want it to be used. Note that the time stored in
the volatile memory clock is lost when the power is removed, so that you
should probably set and check the battery clock if you have it.

                              Hardware Requirements

     The program will run on an IBM computer or equivalent.  The computer must
contain at least one serial port configured as a standard COM port with an
external modem compatible with the Bell System 212A standard (1200 bits/s) or
the 103 standard (300 bits/s) and capable of responding to the Hayes dialing
commands.  Internal modems and multiple speed modems that emulate these
configuration are acceptable.

     If the output pulse capability is selected, the computer must have a
parallel output port for a line-printer that is configured as LPT1.  The
address of the port can be either 37a (hex) or 3be (hex).  The former is used
by the printer adapter and the combined serial/parallel adapter, while the
latter is used for the printer portion of the combined monochrome
display/printer adapter.  If this capability is enabled, the printer should be
turned off or disconnected from the computer before the program is started.

                              Software Requirements

     The program uses calls to the Standard IBM DOS and BIOS routines except
for the output pulse option that directly accesses the parallel output port. 
It was written entirely in Borland Turbo C under DOS 3.2, but is likely to
work under earlier versions of DOS back to 2.0.  It contains no assembly code.

                               Transmission Format

     When the telephone connection to the NBS time service is completed, the
NBS hardware sends timing information at either 300 bits/s or 1200 bits/s
using standard ASCII characters.  A line of information is sent every second,
and the transmission continues for a predetermined number of seconds after
which the connection is automatically broken.  The two transmission speeds use
different formats.
      In the high-speed (1200 bits/s) service, each line begins with a five-
digit integer giving the Modified Julian Day Number (which advances by 1 every
day and is about 47000 in 1988), and the year, month, day, hour, minute and
second in Universal (Greenwich) Time.  This time will be correct upon receipt
of the terminating character (* or #) to be described below.
     The next parameter is the Daylight Savings Time flag.  Values from 50 to
1 indicate the Daylight Savings Time is currently in effect; other values (99
to 51 and 0) indicate that Standard Time is currently in effect.  Values other
than 50 or 0 indicate both the current time and the number of days left before
a transition to the other time is needed.
     Next is the leap-second flag.  Zero is the normal case.  A value of 1
indicates that an extra second will be added following 23:59:59 (Universal
Time) on the last day of the current month.  This second will be called
23:59:60, and the second after it will be 00:00:00.  A value of 2 indicates
that a second is to be dropped on the last day of the current month.  The
second following 23:59:58 will be 00:00:00.  Leap seconds are usually required
about every 18 months and are most commonly added at the end of June or
December.  It is unlikely that the dropping of a second will be necessary in
the near future. Note that the leap second transition is linked to Universal
TIme, unlike the Daylight Savings transition which is linked to local time.
     The next number is the estimated offset between UT1 (a time scale derived
from the rotation of the earth) and UTC (a time scale derived from frequency
standards).  The units are in seconds in steps of 0.1 second. 
     The next parameter is the estimated telephone-line time delay in
milliseconds as determined by the NBS hardware.  It is estimated as one-half
of the average time it takes the terminating character to be sent to the user
and returned. (Any user who intends to make use of this delay must echo the
terminating character back using either hardware or software methods.  If the
terminator is not echoed back to NBS, a nominal delay is assumed.)   The
remaining characters on the line are UTC(NBS) and the terminating character.  
    The terminating character will be a * if the delay has not yet been
measured or is not stable, and will change to a # if 4 consecutive
measurements yield consistent values.  The NBS hardware uses the time delay
estimated in this way to transmit the subsequent terminating character so that
it will arrive on time at the user.  If the user does not echo the terminator
back to NBS, then a nominal delay is assumed and the terminator is sent using
this nominal value.  This nominal value is unlikely to be in error by more
than 0.1 second unless the circuit is transmitted via satellite.
 
                             Operating Instructions

     The program may be run from any directory on any disk.  If necessary,
copy the two files nbstime.exe and nbstime.cfg to the appropriate directory. 
If you will use program makcfg, then copy makcfg.exe to the same directory. 
Make that directory the default using the cd command.  Edit the configuration
file nbstime.cfg if necessary (or run program MAKCFG).  Any text editor, such
as EDLIN may be used for this purpose.  (Word processing programs can also be
used to edit the file provided that the output file is in standard DOS format. 
Note that this is not the default output format for most word processors.)
     When the files are ready, connect the modem to the telephone line and to
the computer and execute the program.  If the program is to be run from
directory blah on disk c, for example:

copy nbstime.*    c:\blah                copy the files.
copy makcgf.exe  c:\blah

c:                                      change to c disk if necessary

cd \blah                                set directory if necessary

type nbstime.cfg                        type the configuration file on the
                                          screen to see if it needs to be       
                                          modified.  If it does, you may do     
                                          so using an editor such as edlin,     
                                          as shown below.  Or, you may run      
                                          program MAKCFG, described below       
                                          to produce a new nbstime.cfg file.    

edlin nbstime.cfg
   .
   .
   .                                     edit configuration file if necessary

ex                                       exit from the editor

nbstime                                  run program

                               Operating Sequence

     This is what happens when the program is run:

1. The command line is examined to see if it contains -d.  If it does, then
set the debug mode to 1 (turn it on); otherwise leave debug at 0.  This
parameter is used for testing the program and should not normally be
specified.

2.  Read the configuration file nbstime.cfg and set the various parameters. 
If an error is detected in reading the file, print a message and stop.  If the
configuration file does not exist in the default directory, then use a default
configuration which is identical to the sample configuration file.

3.  Initialize the com port to 300 or 1200 bits/s, no parity, 1 stop bit.  If
output pulses are requested, determine the address of the parallel printer
port.  If the address cannot be determined then print a diagnostic message and
disable the output pulse selection.

4.  Dial the number if necessary.  If remote modem answers print connect
message and proceed.  If no answer or busy then print message and stop.  If
manual dialing was specified, print a message for manual dialing and wait for
connection.

5.  Read the first 6 lines and echo the terminating character back to NBS for
measuring the transmission line delay.  Send an output pulse when each
terminating character is received if that capability was specified in the
configuration file.  Print these lines on the screen.  The terminating
character will be * initially and will change to # if the NBS hardware
measures a stable transmission delay.  If 300-bits/s service was specified,
continue reading lines in this manner until the NBS breaks the connection;
then hangup the local modem and exit.

6.  If 1200 bits/s service and archive mode is specified, the time difference
between the computer clocks and the NBS transmission is computed when the
fifth line is received and stored in file NBSTIME.DIF.

7.  If 1200-bits/s service is specified, then use the time of the 7th line to
set the computer clock (if setting was enabled).  If the AT flag is on, then
both the memory clock and the CMOS battery clock are set.  Adjust the time to
local time and for daylight savings time as specified in the configuration
file.  Echo the terminator of this line back to NBS and send an output pulse
if pulse selection is enabled.

8.  Read the time of the next line received from NBS and compare the time with
the current values of the computer clocks.  (All of the clocks should have
advanced by 1 second.)  Print both the times and the time difference values on
the screen.  If the AT flag in the configuration file is set, then compare
both clocks with the time received from NBS and print both sets of times and
time differences on the screen.  The memory-based clock "ticks" 18.2 times per
second, while the CMOS battery clock in an AT-type computer "ticks" once per
second.  It is not possible to read or set either clock to better than one of
its ticks, so that differences of one tick or less are not significant. (This
is discussed in more detail below.)

9.  If output pulses are not enabled, then hang up the modem and exit.  If
automatic dialing was selected, a % character is sent to NBS and the Hayes
hang-up sequence is sent to the local modem.  If manual dialing was selected,
then the local modem is presumed to not understand the Hayes commands and the
Hayes hang-up sequence is not sent.  If output pulses are enabled then do not
hang-up the telephone, but continue receiving lines as in paragraph 5 above
until the NBS disconnects the call.

                                 Timing Accuracy

     The volatile memory clock in personal computers of this type (IBM-pc or
equivalent) ticks approximately 18.2 times/second (about every 56
milliseconds), and the time is kept as the number of ticks past midnight.  It
is not possible to alter the tick fraction using calls to either DOS or the
ROM BIOS.  This has two significant consequences:

1. Since there are not an integral number of ticks/second, not all times can
exist.  For example, 00:00:01.00 is not an integral number of ticks after
midnight and therefore can not be set and will never be read.  The nearest
times are 00:00:00.98 and 00:00:01.04.  The average offset between any given
time and the nearest time that can be set is 0.5 ticks or about 28
milliseconds.

2. Time intervals are also uncertain by up to 1 tick since the tick fraction
when the time is read cannot be known to the program.  Again, the average
offset is 0.5 ticks (28 milliseconds).

    The CMOS clock in AT computers cannot be set to better than a second since
it does not store fractions of a second.  The seconds fraction must therefore
be truncated or rounded when the CMOS clock is addressed.  This will further
limit the accuracy of the time following a re-boot of the system (since the
CMOS clock is copied into the system RAM clock at that time).  

     In addition to these errors in setting and reading the clock in this type
of computer, there is a possible error in the computation of the telephone
line delay.  This delay is measured at the NBS as one-half of the time it
takes the terminating character (* or #) to be sent from NBS to the distant
computer and return to the NBS hardware.  This method depends on the
assumption that the transit time is reciprocal, i.e. that the time from NBS to
the computer is the same as from the computer to NBS.  This may not be true if
the two paths are different;  many 1200 bits/s modems also have delays that
are not reciprocal.  Modem delays vary from brand to brand and are on the
order of tens of milliseconds.   

     The accuracy of the computer clocks after they have been set is
determined by the accuracy of the rate of the internal crystal-controlled
oscillators.  These rates are usually sensitive to temperature and other
factors and are unlikely to be stable to better than about 1 part-per-million
(about 0.1 seconds/day), so that errors in the time of this order are likely
even if the time is set exactly initially.

    There may also be a problem with the date if the machine is run
continuously, since the date in some computers is not advanced when the time
passes through midnight.  (This comment applies to the clock stored in memory
only.  The CMOS clock in AT-type machines advances the date properly, but this
clock is only used to set the time initially when the computer is started.) 
This is a "feature" of the BIOS routines that manage the memory-based clock.

     The accuracy of the output pulse is limited primarily by the stability of
the telephone line delay, since the delays within the computer are likely to
be very small by comparison.  Many modems contain equalizing circuits that
attempt to measure the characteristics of the telephone line to which they are
connected.  The operation of these circuits may adversely affect the stability
of the measured time delay.  Although the measured delay may be quite stable
from second to second (with fluctuations of less than 50 micro-seconds), it
often changes significantly every few seconds (as much as 500 micro-seconds)
as the equalizing circuits operate.  The equalizing circuits are usually more
important at the higher speeds so that this effect is likely to be smaller at
300 bits/s.

                                 Fixing Problems

     If the program does not work, the following suggestions may be helpful.  

1.  First check the hardware configuration to be sure that it is connected, is
in working order and is an IBM personal computer or functional equivalent. 
Likewise be sure that the modem is connected to the computer and to the
telephone line and that it responds to the Hayes protocol.

2.  Many modems have a small loudspeaker that is connected to the telephone
line until the connection is made.  Some modems also have lights to show the
status of the call.  The modem should start dialing within a few seconds after
the program is initiated.  If a loudspeaker is present, the dial tone should
be heard followed by the dialing sequence.  If lights are present, OH (off-
hook) should light and SD and RD (send-data and receive data) should flash. 
If none of these things happens, be sure that the hardware is properly
configured and that the configuration file specifies the correct port (COM 1
or COM 2).  The IBM BIOS checks for various status indicators from the modem
and will not initiate a transmission to the modem unless these status
indicators are correct.  In particular, DSR (Data Set Ready) must be true.  In
some modems this line follows DCD (Data Carrier Detect) and therefore will not
be true until the telephone connection has been completed (this is logical for
a modem used to answer incoming calls, but not for modems that can originate
calls since they should be "ready" to accept a dialing command before the call
is established).  In this case, the modem will never be sent dialing
instructions, since it will appear not ready at the start of the program. 
This may usually be changed by a switch in the modem.  When set appropriately,
this switch forces DSR and DCD to be true continuously.  This adjustment is
described in the instruction manual for the modem.  It is often implemented as
switch number 6.  Note that changing the setting of this switch may change the
operation of other programs, especially some terminal emulators that access
the COM ports directly and not via the BIOS commands.  In particular, Data
Carrier Detect is normally used to indicate that the modem is receiving a
signal from a distant modem over the telephone connection, and if this signal
is forced to be continuously true, some terminal emulators may refuse to dial
the modem, assuming that the connection is already established.  

3.  The error message, "No response from modem." means that the modem did not
respond to the dialing sequence as expected.  The message is followed by a
number indicating how far into the sequence the error was sensed.  Number 1
signifies no response to the initial command to reset the modem (ATZ).  If
this message is received, be sure that the hardware is okay and that the modem
is connected to the COM port specified in the configuration file.  Numbers 2
through 4 indicate no response to various parts of the set-up sequence.  If
this occurs, be sure that the echo/blind parameter on the second line of the
configuration file is set appropriately and edit the configuration file (or
rerun program MAKCFG) if necessary.  A response of 5 is probably a telephone
line problem -- since modem problems are likely to have resulted in a failure
at an earlier stage in the process.  These problems can usually be diagnosed
by listening to the progress of the call on the built-in loudspeaker, if
possible.  Be sure that the telephone number is correct and that any long-
distance codes have been entered correctly. If a pause for a second dial-tone
has been inserted, be sure that it is long enough, and add extra pause
commands (,) if necessary.

4.  If the connection is established, but the time is not set correctly,
verify that the lines printed on the screen show the correct date and time. 
If 1200-bits/s service is selected, the first number on each line is the
Modified Julian Day (MJD) Number, which advances by 1 every day and is about
47000 in 1988.  It is not used by the program.  The next numbers are year,
month, day, hour, minute and second in order, where the hour is in Universal
Time (UTC), followed by the Daylight Savings flag, which is an integer from 0
to 99.  The remainder of the line is not used by the program.   If 300-bits/s
service is selected, each line contains the time, the estimated line delay in
milliseconds and the terminating character that is used for synchronization. 
As discussed above, the time is not set in this mode, so that only the
presence of the terminating character is significant.  If the lines are
partially garbled then either the telephone line or the modem should be
suspected.  If the lines are totally garbled, it is likely that the modem
cannot communicate at the selected speed or does not conform to the
corresponding standard.  It is also possible that there is a problem with the
receive portion of the COM port, although this is less likely since the
dialing commands use the same hardware.

5.  If only the CMOS clock is not set correctly (using 1200 bits/s service),
verify that it conforms to the IBM standard and that the configuration file is
set correctly.

                                 Error Handling

     The program deals with only certain types of errors:  Syntax errors in
the configuration file are likely to be detected, although the program does
not place any limits on the telephone number, and an error in specifying it is
unlikely to be sensed until the modem responds erratically.  Hardware problems
or inconsistencies between the hardware and the configuration file will also
be sensed since they will most likely result in no response from the modem or
in a protocol error.

     The most likely source of error in a nominally healthy and properly
configured system is a transmission error.  We can distinguish several
different types of problem depending on where the error occurs.

     1.  The line terminating character (* or #) is garbled or lost.  The
program will not detect the end of the line and will concatenate the line with
the following one.  If output pulses are enabled, no pulse will be sent.  If
the line in error is the line that is used either for setting the clock or
checking it, then an error of 1 second will occur either in setting the clock
or in comparing it.  If this is not either of those lines then the program
will simply continue with no error (the other lines are displayed but are not
used in any other way).  Since the length of the line is known, this error
could be detected in principle, but the current version of the program does
not do so.

     2.  Another character on the line is converted to the terminator (* or
#).  The program will detect a premature end-of-line and synchronization with
the NBS will likely be affected.  If output pulses are enabled, a pulse will
be sent at the wrong time.  The error introduced in setting the clock depends
on which line this occurs in just as in 1 above.  Note that this error is
rather unlikely since there are 128 characters that an error might produce,
but only 2 of them are legal terminators.  This error could also be detected
in principle by a line-length check as above, but the current version of the
program does not do so.

     3.  A digit of the time is transformed into another character that is not
a digit.  This could be detected in principle by carefully checking each
character on the line, but the current version of the program does not do so. 
If this is the line that is used either to set the clock or check it, then the
discrepancy between the local time and the NBS time is likely to be large,
since the error is unlikely to occur in the same position in both the line
used to set the time and the line used to check it.  If output pulses are
enabled, this type of error has no effect on them since they are governed only
by the receipt of the terminating character.

     4.  A digit of the time is transformed into another legal digit.  This
error cannot be detected by examining the line.  The probability is rather
small, however, since there are only 10 legal digits out of 128 possibilities. 
As with 3 above, if this is the line that is used either to set the clock or
to check it, then the discrepancy between the local time and the NBS time is
likely to be large since the transmission error is unlikely to occur in the
same position in the two lines.  As in 3 above, there is no degradation of the
output pulse timing.

     Errors 3 and 4 could also be dealt with by assuming some previous
knowledge of the time or date and rejecting values that deviated from this
assumed date and time by too great an amount.  Illegal month and day
combinations could also be detected in this way.

Name: MAKCFG

Usage: MAKCFG

    This program constructs a file named NBSTIME.CFG based on the answers to a
series of questions.  The program may be run from any directory of any disk,
but is most conveniently run from the same directory in which program NBSTIME
is located.

     The number of each question refers to the line of the output file that is
being assembled.  Thus questions 1a, 1b, ... are used to assemble the various
parameters for the first line.  The contents of each line are described in the
description for the NBSTIME program.

     All of the acceptable responses for each question are listed as part of
question.  Alphabetic answers may be given in upper or lower case.  All
answers must be terminated with a carriage return (or enter), and this fact is
denoted by the symbol <return> in the description for each response.  If you
respond to any question with ? <return>, additional information will be
printed out and the question will be repeated.  If your response is not one of
the expected responses, the message, "I don't understand ..." is printed and
the question is repeated.  

     Your response is not passed to the program until the <return> key is
pressed, so that errors may be erased using the delete key as usual and the
corrected response may then be entered.  If the expected response is a single
letter or digit, then all characters after the first one on the line are
ignored.  Thus if when

          y <return>

is expected, you enter instead,

          yes, we have no bananas <return>,

the two responses will be treated identically since only the first character
is parsed and the remainder of the line is discarded.

     This program checks to see if a configuration file already exists in your
directory.  If it finds the file, it will print a message and give you the
choice of renaming the old file, over-writing the old file or stopping to
think about it.  If you choose to rename the file, the existing file will be
renamed config.old.  This process will fail if a file of THAT name already
exists, and the program will give up if that happens.  You must then erase one
of the configuration files or copy them to another directory or sub-directory
so that the program won't find them.