900227.23:07 ral hfmagic1.doc

	      HF MAGIC VERSION 1.0 DOCUMENTATION


	      1.  INTRODUCTION

	      HF MAGIC 1.0 is an HF propagation prediction program which is
    different from those available from other sources today.  This program
    is designed for use by the amateur or shortwave listener who wants to
    maximize communications over "practical" HF distances, generally up to
    2500 miles in length.  It not only presents the maximum usable
    frequency (MUF), which is only part of the story, but computes the
    received signal strength in "S" units including the very important
    contribution of "D region absorption".  This factor is often missing
    from propagation models, but is very important in determining total
    signal strength during the daytime hours.  The program is based on
    MINIMUF and NBS absorption expressions.

	      The outstanding features of this program include very compact
    size and rapid execution.


	      2.  PROGRAMS

	      The program package consists of 4 files:

	      HFMAGIC1.FNL    main BASIC program

	      MAGICSRC.BAT    batch for screen output

	      MAGICFIL.BAT    batch file to send output to a file

	      MAGICPRT.BAT    batch file to send output to line printer

	      The version which provides only screen output can be directly
    executed by entering the command:  BASICA HFMAGIC.FNL .  The file
    version will load the output into a file A:MAGICOUT.FIL; you can edit
    the batch file MAGICFIL.BAT to create the output file on any desired
    drive or directory.


	      3.  INPUT DATA REQUIRED

	      The program will issue prompts for all required data.

	      The first prompt will be for which version of the program is
    desired; enter 1 if you desire S-meter predictions for the 5
    traditional ham bands (80,40,20,15, and 10 meters); enter 2 if you
    desire 9 bands (5 traditional plus 160, 30, 18, and 12 meters); enter 3
    if you desire the computation for arbitrary frequencies which you can
    input; and enter 4 if you are only interested in MUF predictions.

	      The next prompt will ask for the number of solar flux points
    and increment.  This permits you to have multiple runs which can be
    referred to in order to evaluate the best band to use for a particular
    set of solar flux conditions.  If only a single run is desired, enter
    1,1 at this prompt.

	      The next prompt will ask for the number of runs to be
    executed.  If you desire computations for more than 1 set of
    conditions, enter the appropriate number here else 1 for only a single
    set of conditions.

	      The fourth prompt will ask for the details for the path being
    computed.  This data should be entered with a comma between each number
    as a delineator.  The data consists of the latitude and longitudes of
    the two endpoints of the path (in degrees and decimal degrees, north
    and west positive), day of the month as a number, month as a number,
    the starting value of solar flux (if multiple flux values are being
    computed, else the particular flux value desired for the computation),
    and a field of alphanumeric characters to document the run (these will
    be printed out on the output). Current values of solar flux can be
    determined by listening to station WWV or WWVH (2.5,5,10,15,20 Mhz) at
    18 minutes past the hour.

	      After completion of the data entry, the entered parameters
    will be echoed back for confirmation.  Hit enter if the string is
    correct.

	      4.  OUTPUT

	      The output will consist of a matrix of time, frequency, and
    signal strengths (in dB over/under S-9) based on the assumption of 100
    watts transmitted and the use of non-directive antennas such as
    vertical and dipole antennas.  A value of -98 in the output indicates
    that the band will not be open, and a value of -99 indicates very high
    D-region absorption.  The normal range of useful communications will be
    down to an amplitude of -54, corresponding to 54 dB below S-9, or S-0
    (an S unit is 6dB by convention).  An output of 20 indicates a signal
    level of 20dB over S-9.

	      The time presented is Universal Time (UT), based on the local
    time at the prime meridian at Greenwich, England.  Remember to convert
    this time to your local time.


	      5.  ACCURACY

	      Most people who have used this program have reported that the
    predictions match the actual conditions with a reasonable degree of
    accuracy in predicting the best band to use and the signal strengths
    which will result.	The accuracy is quite good for distances up to
    about 2500 miles.


	      6.  COMPENSATION

	      Disemmination of this program via BBS systems is encouraged
    so that many people can use it.  If you feel that this program is
    useful for you, please send a token fee ($10 suggested) to:

	      Dick Lodwig W2KK	2201 Duvall Rd.  Woodbine, Md.	21797


	      7.  EXAMPLE OUTPUT

	      An example output for the case of a Maryland to Florida path
    on the 27th of February with a solar flux of 200 is provided below.
    Note that for communicating at midnight Eastern time (5 UT), the 160
    thru 30 meter bands will give a path, but since the atmospheric noise
    is much larger for the lower bands, the 40 or 30 meter bands will give
    the best results.

	      For communicating at noon Eastern time (17 hrs UT), the 20
    thru 12 meter bands will all give equivalent results and the choice of
    band can be made based on equipment capabilities and QRM observed on
    the bands.

   ------------------------------------------------------------------------


ENTER:
  1-5 VAL SM
  2-9 VAL SM
  3-ARBITRARY SM
  4-3 VAL MUF
? 2
ENTER NUM OF SF PTS,INCREMENT
? 1,1
NUMBER OF RUNS
? 1
STR FORMAT LAT,LON,LAT,LON,DAY,MO,SF START,ALPHA TITLE
ENTER STRING NO. 1
? 39,77,23,80,27,2,200,Md-Fla

FLUX PTS,INCR 1  1
INPUT DATA STRINGS
 39  77  23  80  27  2	200 Md-Fla

PRESS ENTER TO CONTINUE?

HFMAGIC 1.02 FOR Md-Fla BY W2KK.-

DATE: 27 FEB
TRANSMITTER LOCATION
 LATITUDE 39  LONGITUDE 77
RECEIVER LOCATION
 LATITUDE 23  LONGITUDE 80
  SUNSPOT NUMBER=  155	 SOLAR FLUX=  200  (WWV AT HR+18 MIN)


	 RECEIVED SIGNAL FOR 100W TRANSMITTED. PERFECT
	 NON DIRECTIVE ANTENNAS. DB OVER/UNDER S9

UT	       FREQUENCY
HR  MUF    1.9	3.8  7.2 10.1 14.2 18.1 21.3 24.9 28.5
--  ---   ---- ---- ---- ---- ---- ---- ---- ---- ----
 0 20.4     19	 13    7    5	 2   -1  -98  -98  -98
 1 17.8     19	 13    7    5	 2  -98  -98  -98  -98
 2 16.3     19	 13    7    5	 2  -98  -98  -98  -98
 3 15.0     19	 13    7    5	 2  -98  -98  -98  -98
 4 13.9     19	 13    7    5  -98  -98  -98  -98  -98
 5 13.0     19	 13    7    5  -98  -98  -98  -98  -98
 6 12.3     19	 13    7    5  -98  -98  -98  -98  -98
 7 11.7     19	 13    7    5  -98  -98  -98  -98  -98
 8 11.1     19	 13    7    5  -98  -98  -98  -98  -98
 9 10.7     19	 13    7    5  -98  -98  -98  -98  -98
10 10.4     19	 13    7    5  -98  -98  -98  -98  -98
11 13.0     -4	  7    6    4  -98  -98  -98  -98  -98
12 19.2    -99	-21   -2   -0	-1   -2  -98  -98  -98
13 22.6    -99	-54  -11   -5	-3   -3   -4  -98  -98
14 24.7    -99	-85  -20   -9	-5   -5   -5  -98  -98
15 26.2    -99	-99  -27  -13	-7   -6   -6   -6  -98
16 27.2    -99	-99  -32  -16	-9   -7   -6   -7  -98
17 27.7    -99	-99  -35  -17	-9   -7   -7   -7  -98
18 28.0    -99	-99  -34  -16	-9   -7   -7   -7  -98
19 27.9    -99	-99  -30  -15	-8   -6   -6   -6  -98
20 27.4    -99	-99  -24  -11	-6   -5   -5   -6  -98
21 26.6    -99	-69  -15   -7	-4   -4   -5   -5  -98
22 25.3    -99	-37   -6   -2	-2   -3   -4   -4  -98
23 23.4    -54	 -5    2    2	 0   -1   -3  -98  -98

GRT CIR DIST=  1800 KM	 1125 STAT MILES   978 NAUT MILES.
PATH MIDPOINT=	78.6  LON    31  LAT

HFMAGIC 1.0 COPYRIGHT W2KK 2201 DUVALL RD. WOODBINE, MD 21797
    ---------------------------------------------------------------------