LORAN LOCATOR SYSTEM
                           USER'S GUIDE

                               By
                        Ronald D. Stange
                      Fundamental Services
                      1546 Peaceful Lane N.
                    Clearwater, FL 34616-170O



                              CV1.1





                       TABLE OF CONTENTS




          INTRODUCTION 
             THEORY OF OPERATION -----------------    1
          FEATURES
             MULTIPLE FILE SUPPORT ---------------    2
             SCRATCH PAD -------------------------    2
             SUBSIDIARY FILES --------------------    2

          DESIGN LIMITATIONS ---------------------    3
          
          TRANSMITTAL DISKETTE -------------------    3

          INSTALLATION      
             INITIAL   ---------------------------    4
             UPGRADES  ---------------------------    4
             START-UP  ---------------------------    4

          OPERATION 
             MAIN FUNCTIONS   --------------------    5 
             UTILITIES        --------------------    7


          APPENDIX A
             MAIN MENU SCREEN --------------------   A1
             UTILITIES MENU SCREEN ---------------   A1
             ALTER/DISPLAY SCREEN ----------------   A2
             DEFAULTS DISPLAY SCREEN -------------   A2
             WAYPOINT DETAIL PAGE ----------------   A3 
             WAYPOINT REGISTER -------------------   A4


          APPENDIX B
             FLAG DEFINITIONS --------------------   B1
             TYPE CODES --------------------------   B1








The LORAN C Waypoint Organizer is a program designed to allow the 
user to store all known LORAN fixes and to use this data in an 
efficient manner. It is assumed that the user is familiar with 
the use of LORAN and its buzzwords. 

The output of this program is to be used as a guide ONLY. Your 
own common sense and proper navigational charts take precedence. 
Fundamental Services is not responsible for your actions on the 
water.





                 THEORY OF OPERATION

The LORAN LOCATOR SYSTEM accepts information about any waypoint 
by prompted keyboard input and stores a record containing this 
information in a random disk file. This data includes the name of 
the waypoint, its LORAN TDIs, and other pertinent data. If SCRATCH 
PAD was used with this waypoint then the record will contain a 
pointer to the scratch pad information in another file. 
(DETAIL.DAT)

Once a waypoint is entered any data item in the LOCATION file can 
be displayed and or altered. You are asked to select the field to 
be altered and then enter the data to be inserted in that field. 
The record is not updated on disk until you specifically request 
it.

The primary function of the program is to provide a relationship 
of any waypoint in the file with any other, or all other, way-
points in the file. The output of this function is a single sheet 
of paper providing you with bearing and distance to all the other 
waypoints in the file. This output is sorted by distance with the 
closest being printed first. The print-out defaults to printing 
only the closest forty waypoints to keep the output on a single 
page. This can be overridden under control of flags in the data 
record. See Appendix A3 for a sample of this printed page.

This is accomplished by retrieving the record of the selected 
waypoint and storing it in memory. The LOCATION file is then 
sequentially scanned and the heading and distance of each way-
point is calculated and stored in the disk file RELATION.DAT. An 
index is built for RELATION.DAT and then it is sorted by the 
distance field. The records are read using the index and printed 
on the printer.





                               FEATURES

MULTIPLE FILES - The program allows for the use of more than one 
LOCATION file. LOCATION.DAT is the default default for the way-
point file. That is to say, when the program is shipped to you 
the permanent default for the waypoint file is LOCATION.DAT. If 
you intend to only use a single waypoint file then you need do 
nothing and your data file will always be LOCATION.DAT.

If you require more than one waypoint file, you can, through the 
utilities menu, change the suffix of the filename to any three 
characters that conform to the filename convention of the opera-
ting system being used. This can be done in two different ways, 
permanently or temporarily. A permanent change will write the new 
default suffix to the DEFAULTS file and this new filename will be 
activated each time the program is initiated. A temporary change 
will be in effect only for the duration of the current execution 
of the program unless you change it again.

You might ask when would you ever want more than one file. One 
case is when you have more than 500 waypoints to store. Another 
is when there will be no relationship between the two groups of 
waypoints. For instance, if you had some numbers here around the 
Tampa Bay area and also some numbers in the Keys, you might want 
to keep them separate to speed processing(sorts and searches) 
since you would never go from one to another by boat.



SCRATCH PAD - The scratch pad function allows you to record notes 
concerning any waypoint in the file. You can show dates and 
conditions when fish were caught at that waypoint, or any other 
choice tidbits of information you desire. You are limited to four 
lines of 64 characters for each waypoint. This function is ac-
cessed in ALTER/DISPLAY mode by selecting option "D". You will be 
prompted for your message. These notes will be printed on the 
waypoint detail page for your reference.


SUBSIDIARY FILES - Subsidiary files may be used to sub-divide a 
LOCATION file that is getting large or contains waypoint informa-
tion that relates to multiple points of access to the water. The 
third position of the flags field is used to identify the best 
access point for that particular waypoint. This function is 
accessed thru the UTILITIES MENU item #7. The data in the FLAGS 
field must be entered in the ALTER/DISPLAY function.



                     DESIGN LIMITATIONS

1.  The program allows for a maximum of 500 waypoints in any 
    single LOCATION.xxx file.

2.  You must have a wide (14") printer to print the expanded 
    (50 mile) chart.


                           DISK FILES

The files supplied with the program are described below:

PROGRAM FILES:  LX.EXE          Main program module
                LXCHART.EXE     Chart print program

DATA FILES:     LOCATION.DAT    Contains waypoint information.
                DETAIL.DAT      Contains scratch pad notes.
                DEFAULTS        Contains default constants.    
                LOC-DAT.NDX     Index of LOCATION.DAT
                REGISTER.DOC    Registration Form
                READ.ME         Last minute instructions

BATCH FILES:    INSTALL.BAT     Commands to build new system.
                UPDATE.BAT      Command to update system.
              

You may see other files on your diskette as a result of running 
this program. They are:

         RELATION.DAT    Intermediate storage of relative
                         waypoint information.
         LOCATION.MAS    Output of merge function. 
         LOCATION.NEW    Output of RE-ORG function.

If you use multiple LOCATION files, there will be LOCATION.xxx 
and LOC-xxx.NDX files present on your diskette.




                          INSTALLATION


INITIAL:
Take another new blank diskette, format it, and put the appro-
priate operating system for your hardware on it. You should know 
how to do that so I won't tell you here.

With the TRANSMITTAL DISKETTE in the "A" drive and your TARGET 
diskette in the "B" drive and the "A" prompt is displayed, enter 
the command "INSTALL". This will copy all required files from the 
transmittal diskette to your system diskette.

WARNING: Do not use NEWSYS on a previously installed system with 
         data in LOCATION.DAT. LOCATION.DAT is initialized and 
         existing data will be DESTROYED.

Verify that the following files were copied to your working 
diskette in drive "B":
                       LX.EXE
                       LOCATION.DAT
                       DETAIL.DAT
                       DEFAULTS
                       LOC-DAT.NDX
                       READ.ME
                       REGISTER.DOC

UPGRADES:
With the TRANSMITTAL DISKETTE in the "A" drive and your SYSTEM 
diskette in the "B" drive and the "A" prompt is displayed, enter 
the command "UPGRADE". This will copy only the changed programs 
to your system. In some cases your DEFAULT data will be lost and 
you will have to re-enter it. Proceed as usual with program 
operation.


                         START UP

All you have to do is enter the command LX at the DOS prompt.
The LORAN main menu will be displayed on the screen. If the main 
menu does not appear, review the installation procedure to see 
that all copy commands executed correctly.

Now read through this entire manual to get a feel for it function
before you do anything else with the system.

                            INITIALIZATION

The first operation you should perform with your new system is 
to update the default file to your constants. This is done by 
selecting the utilities function from the main menu and executing 
the UPDATE DEFAULTS function from the utilities menu. Enter your 
personal data in all fields applicable.

Be sure that you select the correct GRI coordinates for the LORAN 
chain that serves your geographical area.

                      MAIN MENU FUNCTIONS

(1)ADD NEW RECORD - You will be prompted for each required 
waypoint data item. Enter each item requested. You will then be 
asked to verify the data just entered. If all is well, the record 
will be written to disk. If you do not verify then you will be 
prompted to enter the complete record again. If just one field is 
in error you might consider verifying the record and going into 
ALTER/DISPLAY mode to make the correction later. 

Appendix B1 contains a chart that describes all the FLAGS and 
TYPE codes currently being used. You should use these codes when 
requested by the prompt.


(2)ALTER/DISPLAY RECORD - ALTER/DISPLAY mode first asks you to 
select the record/page number desired. (The words RECORD and PAGE 
are used interchangably throughout this document.) The PAGE num-
ber of the waypoint book is the record number of that waypoint in 
the LOCATION file.

The selected waypoint record is now displayed on the screen. A 
sample of this screen is shown in Appendix A2. The bottom third 
of the screen summarizes the options available to you at this 
time. Lets look at them all one by one. 

         (-)  Entering the minus sign will cause a display of the      
              previous page. If you were at page one you will
              remain at page one.

         (W)  Entering the letter "W" will cause the record being      
              displayed to be written to disk. You MUST enter a      
              "W" to permanently change the data on disk.

         (D)  Entering the letter "D" will take you to the 
              scratch pad function. The scratch pad record for 
              the waypoint being displayed will now be displayed.
              You may make updates to this information as 
              prompted.

    (number)  Entering any number from 1 to 8 will prompt you to 
              change that data item as displayed on the screen. 
              Remember, you must enter a "W" to permanently write 
              that change to the diskette.

  MAIN MENU FUNCTIONS(cont'd)

(2)ALTER/DISPLAY RECORD(cont'd)
         (+)  Entering a plus sign(or an equal sign) will cause 
              the next page to be displayed. If you are at the last 
              page in the file nothing will happen.

         (S)  Entering an "S" will cause the record search 
              prompt. You should then enter the record/page 
              number desired and it will be displayed.


         (X)  Entering an "X" will cause the record being 
              displayed to be marked for deletion. The actual 
              deletion will not take place until the LOCATION 
              file is re-organized.

         (E)  Entering an"E" will cause you to end this function 
              and return to the main menu.           

        NOTE: Entering any other keys will not have any effect. 
              You do not have to press the enter key to select
              these functions.


(3)COMPUTE ADJACENT POINTS - This function allows you to print a 
waypoint detail page for any waypoint record in the active LOCA-
TION file. You will be prompted for the page number of the way-
point desired. At this prompt you may enter any valid page number 
or the value 999. If you enter 999 a waypoint detail page will be 
printed for every record in the LOCATION file.

You may cause the same information to be displayed on the screen 
instead of being printed by entering a page number which is one 
THOUSAND plus the page number desired. To DISPLAY page six you 
must enter "1006" at the prompt.

(4)ON BOARD FUNCTIONS - Selecting this function will allow you to 
calculate heading and distance from any set of LORAN TDIs to any 
other set of LORAN TDs entered. If either position is a position 
in the LOCATION file you need only to enter the page number of 
that position. The program will get the LORAN TDIs from the file 
and plug them in for you.

In addition, the program will compute a chart of time underway 
against various speeds underway.


  MAIN MENU FUNCTIONS(cont'd)


(5)GENERATE FLOAT PLAN - A float plan is like a flight plan 
except it relates to boats rather than airplanes. The float plan 
records up to six waypoints for a day at sea. It also contains 
passenger information. If you desire a chart of the selected 
waypoints to be printed you may indicate so at that prompt. You 
may also select waypoint detail pages be printed for those 
waypoints in the float plan.

You might want to make two copies of the float plan so you can 
leave one on shore. It makes a good place to start looking when 
you don't get back on time.

(6)PRINT WAYPOINT REGISTER - This function will cause a listing 
of all the waypoints in the active LOCATION file. The listing 
will be ordered by waypoint name. This function uses the current 
index for the active LOCATION file. If one does not exist, it 
will build one for you. Be sure your index is current before 
using this function.

(7)DISPLAY WAYPOINT REGISTER - This function will display on the 
video screen fifteen waypoints beginning at the waypoint you 
select. You will be prompted to enter the page number of the 
first waypoint to be displayed. Once the first fifteen waypoints 
are displayed you may elect to see more or end the function as 
prompted. 


(8)RE-ORG LOCATION FILE - This function causes the active loca-
tion file to be re-ordered by waypoint name. Any records marked 
for deletion will be deleted at this time. The output of this 
function is a file named LOCATION.NEW. In order for you to use 
this file you must either rename the file or select LOCATION.NEW 
as the active file, either permanently or temporarily.


(9)RUN UTILITIES

         MERGE FILES - This feature allows you to merge two or 
         more LOCATION files into one file and names the new file 
         LOCATION.MAS. Enter information as prompted.

         UPDATE DEFAULTS - This function allows you to put your 
         individual information into the DEFAULTS file. The 
         default record will be displayed. You will be prompted 
         to select the fields you wish to change. No defaults 
         will be updated on disk until you select item 9, RETURN 
         TO UTILITIES MENU.



(9)RUN UTILITIES(cont'd)

         BUILD LOCATION INDEX - This function builds an index of 
         the active LOCATION file and writes it to disk. The name 
         of the file will be LOC-xxx.NDX; where xxx is the suffix 
         of the active location file.  


         PRINT TAMPA BAY CHARTS) - Plots your waypoints on a map 
         of the Gulf of Mexico in the area of Tampa Bay. There 
         are two or three modes of this printing. An Epson or 
         Epson compatible printer is required for this function. 
         You must have a wide carraige printer (14") to use this 
         function. You need program LXCHART.EXE to execute this 
         function


         BUILD SUBSIDIARY FILE - This function creates, or over-
         writes, a file of waypoints selected from the currently 
         active LOCATION file. Every waypoint can be associated 
         with its closest or best saltwater access point. The 
         major Florida access points have been identified and 
         allocated a unique file suffix to be used with LOCATION. 

         In order to use this function you will have to enter the 
         associated access code in the third position of the 
         FLAGS field of the data record. These flags are shown in 
         Appendix B1. 

         To build the sub file you will be prompted to enter the 
         flag desired. When a valid flag is entered the program 
         will perform the function.






                          MAIN MENU SCREEN
   ___________________________________________________________________
  /                                                                   \
 /LORAN C WAYPOINT ORGANIZER    *CV01.0*        By Fundamental Services\ 
| RECORD COUNT: 85                               FILENAME: LOCATION.DAT |
|                             MAIN MENU        ACTIVE GRIs: 7980W 7980Y |
|                                                                       |
|                       1. ADD NEW RECORD                               |
|                       2. ALTER/DISPLAY RECORD                         |
|                       3. COMPUTE ADJACENT POINTS                      |
|                       4. ON BOARD FUNCTIONS                           |
|                       5. GENERATE FLOAT PLAN                          |
|                       6. PRINT WAYPOINT REGISTER                      |
|                       7. DISPLAY WAYPOINT REGISTER                    |
|                       8. RE-ORG LOCATION FILE                         |
|                       9. RUN UTILITIES                                |
|                                                                       |
|                                                                       |
|                                                                       |
|                                                                       |
|                                                                       |
|                ENTER SELECTION BY NUMBER(PF10 TO END)                 |
|                                                                       |   
|                                                                       |
 \   Copyright 1983-1988 - Fundamental Services; Clearwater, Florida   /
  \___________________________________________________________________/



                           UTILITIES MENU

   ___________________________________________________________________
  /                                                                   \
 /                                                                     \
|                                                                       |
|                            UTILITIES MENU                             |
|                                                                       |
|                     1.  MERGE INTO LOCATION.MAS                       |
|                     2.  UPDATE DEFAULTS                               |
|                     3.  -----------------------                       |
|                     4.  BUILD LOCATION FILE INDEX                     |
|                     5.  -----------------------                       |
|                     6.  -----------------------                       |
|                     7.  PRINT TAMPS BAY CHARTS                        |
|                     8.  BUILD A SUB-FILE                              |
|                     9.  RETURN TO MAIN MENU                           |
|                                                                       |
|                                                                       |
|                                                                       |
|                ENTER SELECTION BY NUMBER(PF 10 TO END)                |
 \                                                                     /
  \___________________________________________________________________/


                           ALTER/DISPLAY SCREEN
   ___________________________________________________________________
  /                                                                   \
 /                                                                     \
|                                                                       |
|LORAN C                GRI = 7980W 7980Y                       LOCATOR |
|RECORD NUMBER: 6                                FILENAME: LOCATION.DAT |
|                    WAYPOINT RECORD DISPLAY                            |
|                                                                       |
|              1. ITD FOR 7980W          14241.7                        |
|              2. ITD FOR 7980Y          44818.3                        |
|              3. Latitude               27 38'53"                      |
|              4. Longitude              83 03'31"                      |
|              5. Location Name          Clearwater Pass Bell           |
|              6. Record Flags           AH                             |
|              7. Structure Type         8                              |
|              8. Comments               Normal return from sea.        |
|              9. Waypoint Memory        29                             |
|                                                                       |
|        UPDATING WAYPOINT INFORMATION - ENTER AS PROMPTED BELOW        |
|                                                                       |
|                    *** ENTER SELECTION NOW ***                        |
|                                                                       |
| - = DISPLAY PREVIOUS RECORD          + = DISPLAY NEXT RECORD          |
| W = WRITE THIS RECORD TO DISK        S = SEARCH FOR ANOTHER RECORD    |
| D = DISPLAY DETAIL RECORD            X = DELETE THIS RECORD           |
| (number) = SELECT FIELD TO CHANGE    E = END THIS FUNCTION            |
 \                                                                     /
  \___________________________________________________________________/


                       DEFAULTS DISPLAY SCREEN
   ___________________________________________________________________
  /                                                                   \
 /                                                                     \
|                          DEFAULT PROCESSING                           |
|                                                                       |
|          1.  NAME OF VESSEL---------------   BOAT NAME                |
|          2.  CAPTAIN'S NAME---------------   CAPTAIN NEMO             |
|          3.  VHF STATION CALL-------------   WAA-1234                 |
|          4.  VESSEL REGISTRATION----------   FL-1234-AA               |
|          5.  MARINE IDENTIFICATION(MIN)---   000-1234-123             |
|          6.  LOCATION FILE SUFFIX---------   DAT                      |
|          7.  GRI #1 ----------------------   7980W                    |
|          8.  GRI #2 ----------------------   7980Y                    |
|          9.  WRITE CHANGES TO DISK AND EXIT                           |
|                                                                       |
|                                                                       |
|                                                                       |
|               ENTER NUMBER OF FIELD TO BE UPDATED                     |
\                                                                      /
 \____________________________________________________________________/



                      WAYPOINT DETAIL PAGE



                            WAYPOINT REGISTER





                               FLAGS

The FLAGS field in the waypoint record is five characters long. 
The first three characters are reserved for the program. The last 
two characters can be user defined.

F1:  A=Primary location. This waypoint will print in bold type on 
       the waypoint detail page.

     B=Secondary location. 

     C=Unverified location. This will not be charted in the chart 
       all waypoints function.

     D=This record is marked for deletion. The ALTER/DISPLAY 
       function requested that this record be deleted but re-org 
       has not yet actually deleted the record.

     T=Tourist attraction. Good dive spot.


F2:  H=Home port of call. This identifies the pass or inlet you 
       use to return to home port. The waypoint detail page for 
       this record will contain all associated related points and 
       not be limited to forty. 


F3:  Used by SUB-FILE function as follows: 
          FLAG             FILE SUFFIX      SALT WATER ACCESS
            A                 .ATL            ATLANTIC OCEAN
            B                 .BAY            BAYPORT
            C                 .CLR            CLEARWATER PASS
            J                 .JPS            JOHN'S PASS
            K                 .KEY            FLORIDA KEYS
            T                 .TAR            TARPON SPRINGS
            X                 .XXX            USER DEFINED
            Y                 .YYY            USER DEFINED
            Z                 .ZZZ            USER DEFINED

F4 and F5      USER DEFINED



                            TYPE CODES

                        1 = Depression
                        2 = Dropoff/Ledge
                        3 = Mound/Rocks
                        4 = Undercut/Cave
                        5 = Pass/Inlet
                        6 = Landmark
                        7 = Manmade Obstruction/Reef
                        8 = Navigation Aid