PMP -- Poor Man's Packet

                                                        Version 0.93 (beta)




















                                             A software TNC for the IBM PC.



                                                                         by

                                                     Andrew C. Payne, N8KEI
                                                                April, 1990



          Disclaimer:

               No guarantees  or warranties  of any kind are expressed
               or implied.  This program is  supplied "AS  IS" without
               any warranty  of any kind, either expressed or implied,
               including, but not limited  to, the  implied warranties
               of  merchantability   and  fitness   for  a  particular
               purpose.  Neither the author  nor  anyone  else  who as
               been involved  in the creation, production, or delivery
               of  this  program  shall  be  liable  for  any  direct,
               indirect,   or   consequential  or  incidental  damages
               arising  out  of  the  use  or  inability  to  use this
               program.


                         Copyright (c) 1990 Andrew C. Payne
                                All rights reserved.






                                  TABLE OF CONTENTS
                                  =================


          Introduction . . . . . . . . . . . . . . . . . . . . . . . .    3

          Getting Started  . . . . . . . . . . . . . . . . . . . . . .    5
               Hardware Requirements . . . . . . . . . . . . . . . . .    5
               Installing, Configuring, and Running PMP  . . . . . . .    5
               Configuration Commands  . . . . . . . . . . . . . . . .    5

          Using PMP  . . . . . . . . . . . . . . . . . . . . . . . . .    9
               Keyboard Commands . . . . . . . . . . . . . . . . . . .    9

          Modem Interface  . . . . . . . . . . . . . . . . . . . . . .   11

          PMPTEST  . . . . . . . . . . . . . . . . . . . . . . . . . .   12
               Commands  . . . . . . . . . . . . . . . . . . . . . . .   12
               Getting your modem to work with PMP . . . . . . . . . .   13

          Beta Test Notes  . . . . . . . . . . . . . . . . . . . . . .   14







                                    Introduction
                                    ============


          What is PMP?

               PMP  is  a  packet  radio  program  that  uses  the software
               approach.  In a  nutshell, this  means that  the things that
               are  normally  done  with  hardware  in  a  conventional TNC
               (Terminal Node Controller) are instead done with software in
               your computer.  The advantage of this method is that most of
               the hardware of a normal TNC  is  no  longer  required.   In
               simplifying the  hardware, you  lose some of the flexibility
               of a TNC.


          Who is PMP intended for?

               PMP is intended for anyone with an IBM PC type  computer who
               wants to get into packet very inexpensively.  PMP is perfect
               for someone who wants to get his/her feet wet before sinking
               a lot  of money  into equipment.   PMP is also ideal for the
               scanner listener who wants  to  monitor  packet  but doesn't
               want to  spend another scanner's worth of money.  Because of
               the minimal hardware required, PMP is also good for portable
               setups.   Modems can  be constructed  to actually fit inside
               VHF/UHF radios, eliminating the need for  a separate  TNC or
               modem box.


          What do I need to run PMP?

               PMP  requires  an  IBM  PC/AT/386/486  or compatible with at
               least 256K of memory and a parallel printer port (many video
               cards have  a parallel port built in).  You also need a Bell
               202  type  modem,  VHF/UHF  radio,  and  cables  to  connect
               everything up.  Finally, you need the PMP software.


          What are the advantages of PMP over a "regular" TNC?

               The advantages  of PMP  are basically  those outlined above:
               minimal hardware and low price.  The only  hardware required
               is a  1200 baud  Bell 202 modem and cables to connect to the
               computer and radio.  We have a single-chip  design that fits
               on a  2 inch  square board  and costs  less than $40.  Also,
               this crystal controlled modem  is a  much better  modem than
               those in many of the TNCs.


          What do I lose by using PMP instead of a TNC?

               PMP doesn't  have all  of the flexibility of a TNC.  It runs
               on PCs ONLY.  Also, since PMP is a program  on your  PC, you






               can't leave  PMP on  (to act  as a  digipeater, for example)
               without tying  up your  entire computer.   Also,  all of the
               packet software  for the PC designed to work with TNCs (such
               as YAPP, the W0RLI BBS, and KA9Q's TCP/IP software) will not
               work with PMP.


          How was PMP developed?

               DIGICOM>64  for  the  Commodore  64  (which  uses  the  same
               software approach) has been  around for  a while.   With the
               popularity  of  DIGICOM>64  and  the  growing  popularity of
               inexpensive IBM PC clones, we asked ourselves:   "Has anyone
               done a  DIGICOM>64-like program  for the  PC?"  Some queries
               about such a program resulted in answers like:  "Nope, never
               heard of  such a  thing.  Sure would be a good idea though."
               At that point, we decided to start the PMP project.   Kevin,
               WB2EMS, concentrated on the hardware design and Andy, N8KEI,
               developed the software.    Within  a  few  weeks,  the first
               prototype  modem  was  built,  and  two weeks after that PMP
               sending and receiving its first packets.


          I have some more questions.  How can I get in touch with you?

               For software  and general  questions, problems, suggestions,
          or comments, write to:

                    Andrew C. Payne, N8KEI
                    Route 3, Box 78-Q
                    Berkeley Springs, WV  25411

               Or, if you have access to Internet e-mail, write to:

                    payne@tcgould.tn.cornell.edu


               For hardware  questions, problems, suggestions, or comments,
          write to:

                    Kevin Feeney, WB2EMS
                    468 Hines Road
                    Ithaca, NY  14850






                                   Getting Started
                                   ===============

          Hardware Requirements
          ---------------------

               The following hardware is required to run PMP:

             - an IBM PC/XT/AT/386/486 or compatible with at least 256K RAM
               and a parallel printer port

             - a Bell 202 type 1200 baud modem

             - A VHF/UHF radio

             - cables  to  connect  the  printer  port to the modem and the
               modem to the radio


          Installing, Configuring, and Running PMP
          ----------------------------------------

               Installing PMP is very  straightforward: only  two files are
          required, one is optional:

               PMP.EXE        The PMP program
               PMP.CFG        The Configuration file
               PMPTEST.EXE    (optional)  An alignment/test program

               To install  PMP on your system, copy these files to a floppy
          disk or a subdirectory on your  hard disk.   To  start, just type
          'PMP' from  the DOS  prompt and  you should see the opening title
          screen in a few seconds.

               The  configuration  file,  PMP.CFG,   contains  options  and
          parameters  specific  to  your  packet  station:   your callsign,
          timing parameters, and other items described in detail below.

               The PMP.CFG file is  a  an  ASCII  text  file  which  can be
          modified with  any standard text editor (such EDLIN supplied with
          DOS).  Lines that begin with  a pound  sign (#)  are comments and
          are ignored.  All other lines are configuration commands for PMP,
          listed below:

          Configuration Commands
          ----------------------

          mycall <callsign>
               Sets your callsign in the form of N8KEI-XX, where XX  is the
               SubStation  Id  (SSID).    The SSID is used to differentiate
               between  multiple  stations  with  the  same  callsign (e.g.
               N8KEI, N8KEI-1,  N8KEI-2, etc).   The  SSID ranges from 0 to
               15, and 'N8KEI' and 'N8KEI-0' are equivalent.  Your callsign
               MUST be correct before transmitting.







          txdelay <milliseconds>
               Sets  the  transmitter  delay.    This is the time PMP waits
               after keying the transmitter and before sending data.   Slow
               transmitters  (synthesized  rigs,  rigs  with  relays in the
               transmit path, etc) will  require longer  to stabilize after
               the transmit  line is  keyed.  These slow rigs need a larger
               'txdelay'.

          retry <#>
               Number of retries attempted  before  dropping  a connection.
               If you  are on a busy channel, you may want to increase this
               value  from  its  default  value  (10)   to  prevent  losing
               connections.

          frack <#>
               Number of seconds used to compute the round trip time before
               resending packet.  If  you are  on a  busy channel,  you may
               want to increase this value.

          pthresh <#>
               Sets I-packet  size threshold.  This is an optimization that
               speeds up the AX.25 protocol for  small packets.   I-packets
               with data  fields of smaller than 'pthresh' are resent (with
               no polling) when no ACK is  received in  the timeout period.
               Longer packets are polled ala standard AX.25 Level 2.

          check <#>
               Specifies the time-out value (in seconds) for the link keep-
               alive timer.  After this  many  seconds  of  inactivity, PMP
               will poll the remote node.

          maxframe <#>
               Specifies  the  maximum  number  of  frames  allowed  to  be
               outstanding (e.g. un-acknowledged).  This parameter  must be
               between 1 and 7.  On busy channels, a lower value is better.

          paclen <#>
               Specifies  the   maximum  packet  length  in  bytes.    This
               parameter must be between 1 and 256.

          normal  <#>
          bright  <#>
          inverse <#>
          status  <#>
          message <#>
               These commands set the attributes (colors)  for normal text,
               bright  text,  inverse  text,  and  the status line.  If not
               specified, the  attributes default  to the  attributes for a
               monochrome video system.

          sound <#>
               Enables or  disables sound.   If  <#> is  non-zero, sound is
               enabled.  If <#> is zero, sound is disabled.







          ctext <string>
               Specifies the welcome message to be sent when other stations
               connect to  you.  If no CTEXT is specified in the .CFG file,
               no  welcome  message  is  sent  during   incoming  connects.
               Multiple CTEXT  lines can  be specified:   all  will be sent
               during incoming connects in the  order  they  appear  in the
               .CFG file.

          capture <#>
               Specifies the  size (in bytes) of the capture memory buffer.
               Capture data is held  in this  buffer, then  flushed to disk
               when the buffer fills.  Smaller capture buffers will require
               more disk writes.  On a floppy based systems, a  large value
               is recommended  to minimizes disk writes.  This value should
               always be a multiple of 512 (the MS-DOS sector size). 

          define <key> <definition>
               Defines a string associated with a  function key.   <key> is
               one of  the function  keys F1 through F4 (F5 through F10 are
               currently used  for debug  functions).   <definition> is any
               string.   Control   characters   may   be  imbedded  in  the
               <definition> string with the  '^'  character  (e.g.  '^M' is
               interpreted as a carriage return).

          beacon <#>
               Specifies the  beaconing interval, in seconds.  Beacons (see
               'btext', below) will be sent at  the specified  interval.  A
               '0' value disables beaconing.

          btext <string>
               Specifies the text sent during beacons.

          baddr <string>
               Specifies the  address (and path) to which beacons are sent.
               Digipeaters are allowed (e.g. "QST VIA W2CXM-1").

          autowrap <#>
               Specifies the column number  at  which  autowrap  is active.
               Autowrap is  a feature similar to most word processors where
               it is not necessary for the user to hit return  after typing
               beyond a  certain column; the line is automatically wrapped.
               A '0' value disables autowrap.

          pttport
          txport
          cdport
          rxport
          init
               These commands implement functions  that  are  currently not
               documented.









               Sample PMP.CFG file:

          #
          #    This is a sample PMP.CFG file
          #
          mycall    N8KEI-2
          txdelay   300
          retry     12
          frack     3
          pthresh   15
          sound     1

          ctext     Hello from Andy in Berkeley Springs, WV.
          ctext     If I'm not around, please leave a message.

          btext     N8KEI, QTH Berkeley Springs, WV
          baddr     QST VIA W2CXM-1
          beacon    300

          #
          #    End of sample file
          #

               All options  in PMP.CFG default to reasonable values if they
          are not specified in the file.  However, a MYCALL  parameter must
          always be present to set your callsign correctly.






                                      Using PMP
                                      =========

               After starting  PMP (by typing 'PMP' at the DOS prompt), you
          should see an opening title screen (with current version number).
          Press any key to advance from this screen to the main screen.

               The main  screen is  divided into  three areas.  Most of the
          upper part of the  screen is  the incoming  data area;   incoming
          data and packets are displayed here.   The second to last line on
          the screen is  the  data  entry  line;  everything  you  type for
          transmission is  entered here.   The bottom line of the screen is
          the highlighted status line, which has the following  items (from
          left to right):

          -    The version number

          -    Your   callsign   (make   sure   this   is   correct  before
               transmitting)

          -    The current connect path (blank if currently not connected)

          -    Outstanding packet bar, there will  be  an  asterisk  (*) on
               this bar for each outstanding packet (a packet that has been
               sent but not acknowledged  by the  other station)   This bar
               will be blank if currently not connected.

          -    TX/RX status lights.  This status indicators will light when
               PMP is transmitting or receiving packets.


          Keyboard Commands
          -----------------

               Most commands in PMP are  ALT  key  combinations  (formed by
          holding down the ALT key and some other key), listed below:

          ALT-C     Connect to  another station.   You will be prompted for
                    the connect station and path in the form:

                         WB2EMS VIA W2CXM-1,WB2TVB

                    Press ESC to abort the connect attempt.


          ALT-D     Starts a disconnection.   If  the  remote  node  is not
                    responding to the disconnect request, press ALT-D again
                    to force a disconnect.

          ALT-B     Sends a beacon packet (with the  text specified  in the
                    'btext' parameter in the configuration file).

          ALT-H     Shows a help screen, listing all keyboard commands.







          ALT-J     Screen snapshot.   Writes  the current screen to a text
                    file.

          ALT-N     Nodes recently heard.   Nodes are  listed starting with
                    the most  recently heard.   Information listed for each
                    node includes the callsign of the  node, the  time last
                    heard, the  number of  packets heard,  and the protocol
                    types used by the node.

          ALT-P     Pause (hold) the screen.  After pausing, press  any key
                    to resume.

          ALT-S     Shows the  status of  PMP:   the number of packets sent
                    and received, error counts, number of bytes free, etc.

          ALT-X     Exits to DOS.

          ALT-U     Text file upload.  You will be prompted for the name of
                    an  ASCII  file  to  send  across a currently connected
                    link.

          ALT-L     Toggle  text  file  capture/download.    You   will  be
                    prompted for  a file  to log  all received data.  "Cap"
                    will appear  on  the  status  line,  indicating  that a
                    capture  is  in  progress.    Press ALT-L again to stop
                    capturing and close the file.

          UP & DOWN The [Up] and [Down] arrows can be used  to move forward
                    and backward  to review  data that has scrolled off the
                    top of the screen.  [PgUp] and [PgDn] will page through
                    the scrollback buffer a screenfull at a time.

          F1-F4     User defined  function keys.   Sends the string defined
                    for  the  key  (see   'define'  in   the  configuration
                    commands).






                                   Modem Interface
                                   ===============

               PMP interfaces to the external modem (and radio) through the
          PC's parallel port.  PMP uses two output pins and  two input pins
          which are connected as follows:

          Parallel
            Port
            Pin     Signal    Dir. Description
          -----------------------------------------
             2       TXD      Out  Transmitted data.

             3       PTT      Out  Push-to-talk,  active-high.    Keys  the
                                   radio to transmit.

             11      CD       In   Carrier  detect,   active-high.     Goes
                                   active when a packet signal is detected.

             15      RXD      In   Receive data.

             25      Gnd      Gnd  Signal ground.


               The PMPTEST  utility is very useful for testing the parallel
          port and modem interface (see next section for more information).

               On most PCs,  the  parallel  port  is  a  female  DB-25 type
          connector and uses standard TTL levels.

               We have  developed a small, inexpensive, two-chip modem that
          works well with PMP.  It is based on the DIGICOM>64 modem that 
          appeared in the February, 1989 issue of 73 (pp. 42-43).






                                   PMPTEST Utility
                                   ===============

               PMPTEST is  a  utility  program  that  aids  in  testing the
          parallel port and modem interface (see MODEM INTERFACE).  PMPTEST
          is started by typing 'PMPTEST' from the DOS prompt.

               Across the bottom of PMPTEST's screen are four indicators:

          Carrier Detect (CD)      Indicates the current input level of the
                                   Carrier Detect line.

          Receive Data (RXD)       Indicates the current input level of the
                                   Receive Data line.

          Transmit Data (TXD)      Indicates the  current  output  level of
                                   the Transmit Data line.

          Push To Talk (PTT)       Indicates  the  current  output level of
                                   the Push To Talk line.


          Commands
          --------

               PMPTEST has several commands:

          [ESC]     Exits program.

          [SPACE]   Toggles transmit  (PTT)  line.    The  current transmit
                    status will be indicated with the PTT indicator.

          [F2]      On-air modem alignment mode.  (see below)

          [F3]      Toggle transmit data level.  The current transmit level
                    is indicated with the TXD indicator.

          [F5]      Transmits a 600hz test signal.   PTT will  be set high,
                    and the  transmit data  will be  toggled at 600hz.  Any
                    key will cancel the test.

          [F6]      Loopback alignment (currently not implemented).







          Getting your modem to work with PMP
          -----------------------------------

               This section describes some simple tests using PMPTEST.

          Carrier Detect

               Adjust your radio  and  modem  so  that  the  Carrier Detect
               accurately reflects  channel activity.   The CD status light
               should indicate channel activity.

          Receive Data

               The RD indicator should  flicker (on  and off)  when data is
               being received.

          PTT

               Use the [SPACE] bar to toggle the transmit on and off.  Your
               radio should start transmitting when PTT goes high  and stop
               transmitting when PTT goes low.

          Transmit Data

               Use the  [SPACE] bar to toggle your radio into transmit mode
               and use the [F2] key to  toggle  the  transmit  data.   Your
               radio should  transmit a  high or low tone, depending on the
               transmit data level.

          Receive Alignment

               Many modems  (including our  design) have  a receive section
               that must  be properly  aligned.   Tune your radio to a busy
               packet channel, and make  sure that  the Carrier  Detect and
               Receive  Data  lines  are  functioning (as described above).
               Use [F1] to enter  the alignment  mode.   As each  packet is
               received,  it's  timing  will  be  analyzed  and  two  error
               percentages will be displayed  on the  screen.   Adjust your
               modem  so  that  these  two  numbers are as close to zero as
               possible:  between -5% and +5% is ideal.   Use  long packets
               to make your adjustments; short packets or noise bursts will
               give inaccurate error readings.






                                   Beta Test Notes
                                   ===============

               This version  is  a  beta  test  version  of  PMP.   Several
          debugging  features  are  implemented  (using  function  keys  F5
          through F10) to aid in tracking problems. 

               At present, the only key useful for most testers is  the F10
          key which  toggles the log mode on and off.  With the log mode on
          (as indicated by a small square in the extreme lower  left of the
          screen), all  packets send and received are logged in memory.  On
          exit, the user is prompted for a log  file to  write the  log to.
          If any  problems are  encountered with  PMP, the  log file are of
          great use for debugging.

               The function keys F5-F9 currently implement various features
          that will change from version to version.