ADDITIONAL NOTES FOR THE "RU" RTTY UTILITY

This program is a slightly modified from the original RTTYU program
by KF4NB.  It's operation is mentioned in the documentation for his
RTTY program on this system.

Changes to look for are:

1) Prompt for drive that has pix; with "B" being the default.  Simply
   hitting enter will save having to type the "B:" every time when
   printing pix. If you want to override the default type "d:", with
   "d" being the desired drive.

2) Request for pix size - with "Small" being the default.  This results
   in a much better picture. The matrix printers used are rather thin
   in putting ink on paper so the pix that look OK on a Teletype
   machine look weak and washed out on the IBM Grafix printer.  In the
   Small (default) mode the pix look great!

   This change simply sends a printer modification command before the
   pix is printed.  The command will set the printer to compressed
   print and 6/72 " line spacing (I think).  This makes for a nice
   tight pix that looks fantastic. If you have another type of printer
   that can't handle this, use Full for full size pix or modify the
   basic RU program to suit your printer, and recompile.  The basic
   version runs very slow with out compiling.

3) When the quote (') is sent I suppressed the corresponding "BELL" or
   annoying beep.  Some pix have thousands of 's in them and running
   thru a pix can make the computer more annoying than the old noisy
   TTY machines we just got rid of!

4) Not a change - just a note:  When you save a file you will be
   prompted for additional info regarding compression.  If you say
   Yes then the file will be saved as compressed data.  I have found
   that most pix will shrink to 50% of the original size.  This depends
   how many redundant characters there are in a pix, of course.

   Another note, you can send the compressed pix right from your RTTY
   program as it will un-compress it as it is sent out. NOT necessary
   to un-compress with RU and then send it with RTTY.

5) For this program to operate correctly, a received RTTY pix must have
   been received with the RTTY program in "ART" mode.  This is done with
   the ALT-A key while the RTTY program is running, but before a pix
   has started to be received. Of course, you will have hit F3 to
   receive a file to disk!

   A file that has been properly received for RTTY ART will have special
   characters added to each line for carriage control and line feed
   control.  Those characters are listed below.

           Backwards "P" or paragraph symbol will cause a LINE FEED

           The "vertical arrows" will cause a carriage return.


   Note that if the pix has overline printing there will be the
   vertical arrows without the backwards P.  This of course, will
   cause a carriage return with no line feed. The result is over-
   striking capability.

6) File sizes are listed below.  Use to verify that the download
   is OK. This size should show up on a directory list on your PC.

             RU.BAS       - 5338  bytes
             RU.EXEBIN    - 22784
             PARMS.RTY    - 175
             GARFIELD.PIX - 7629
             TUMBLWEE.PIX - 6779

"Happy Pix"   - de W9HLQ