The Phaselock programs are really general purpose feedback �
control programs. I have included a data file of a -9db/Octave �
loop filter, normalized to unity gain at 1 rad/sec.

     For a sample run, follow the steps below.

     1) Engage CAPS LOCK.
     
     2) Type PHASLOK.

     3) When the menu appears type A.

     4) At the prompt, type OPNLOOP.DAT. These are the frequency �
variables of a -9db/Octave loop filter normalized to unity gain �
at 1 rad/sec.

     5) When the menu reappears, type C. You will see the system �
poles and zeroes.

     6) Type N to edit prompts.

     7) Type E.

     8) Type .1# at the loop gain prompt.

     9) Type N at the plot prompt.

    10) Type .1# at the start frequency prompt.

    11) Type 2.0# at the number of decades prompt.

    12) Type .1# at the decade increment prompt.

    13) A tabulation of the open and closed loop gain and phase �
will appear. This display is usefull to adjust the loop gain for �
minimum open loop phase at the unity gain crossover frequency.
     
     14) Make a note of the closed loop ,-3dB frequency. A �
frequency that gives anything more than -3dB is adequate.

     15) Type N to the new gain prompt.

     16) When the menu reappears, type F.

     17) Type .1# at the loop gain prompt.

     18) Type the appropriate -3dB frequency earlier noted.

     19) The loop noise bandwidth will appear. This is useful for �
determining total carrier phase deviation.

     20) Type N at the new gain prompt.

     21) When the menu reappears, type G.Š
     22) Type .1# at the loop gain prompt.

     23) The transfer function, F(s) will be displayed as the     �
     ratio of two polynomials.

     24) Press any key.

     25) When the main menu reappears, type C.

     26) You will now see the closed loop frequency variable.     �
     Note that the closed loop zeroes are the same as the open �
loop zeroes.

     27) Type N at the edit prompt.

     28) When the menu reappears type H.

     29) The impulse response h (t) will be tabulated.

     30) Press any key.

     31) Type 0 for start time.

     32) Type 25 for stop time.

     33) When the annotation prompt appears type N.

     34) When the line type prompt appears type 1.

     34) Type N at the min/max prompts.

     36) Type 0 at the screen oplot prompt.

     37) The loop impulse response will be displayed.

     38) Press any key.

     39) When the menu reappears, type C.

     40) Type N at the edit zeroes prompt.

     41) Type Y at the edit poles prompt.

     42) Type A at the edit options prompt.

     43) Type 1 at the how many?  Prompt.

     44) Type 0 for the real part prompt.
         Type 0 for the imaginary part prompt.
         The frequency variable list now contains the step          �
response spectral function, namely, a pole at the
         origin.
Š     45) When the menu reappears, type C to inspect the new       �
   frequency variable list.

     46) Type N at the edit prompt.

     47) Type H.

     48) The step response, h(t), will be tabulated.

     49) Press any key.

     50) Type 0 at the start time prompt.

     51) Type 25 at the stop time prompt.

     52) Type N at the annotation prompt.

     53) Type 1 at the line type prompt.

     54) Type N at the min/max prompts.

     55) Type 0 for the screen plot.

     56) The loop step response will be displayed.

     This completes a simplified "run through" of the program.  

     The programs IFTLOOP, and SMPLOOP, are similar in operation, �
but very different in the transient response algorithm.  The �
first thing you will notice is that the time response takes �
longer to compute.  This is because they compute 1024 open loop �
gain and phase points, subsequently 1024 closed loop gain and �
phase points, and then performs a 1024 point inverse Fourier �
transform.

     The step response is the numerical integration of the �
impulse response.

     You will notice there is a zero response delay prior to the �
beginning of the time response.  This delay is generated by a �
linear phase generator used for normalization purpose.

     In using these programs you should always run the impulse �
response first, making sure it has settled completely to zero at �
the end of the time base chosen.  This ensures the correct �
calculation of the step response.

     SMPLOOP includes the sinc x characteristics of a sampling �
phase detector, and also includes the excess loop pole generated �
by non-ideal sampling.  HP has an excellent application note on �
sampling phase detectors.