FERRITE.COM User's Guide
                                      Version 1.0
                       Copyright (c) 1986 by Scott R. Grabowski
                                  All Rights Reserved
        
        
        Program Overview
        
        This  program  package  consists  of the following files: FERRITE.DOC, 
        FERRITE.COM,  and  CHART1.TXT.  The FERRITE.COM program calculates the 
        inductance  of  windings  placed  on  an  iron-powder  toroidal  core.  
        Inductance  versus  turns  data  is presented in tabular format on the 
        screen  and  may  be printed, if the printing option is selected.  The 
        files  FERRITE.DOC  and CHART1.TXT are text files that provide on-line 
        documentation  and  a  reference chart of maximum windings that can be 
        wound on the core.
        
        The  FERRITE.COM  program  package  is  distributed  as User-Supported 
        Software;  consequently,  even  though  it  is  copyrighted, it may be 
        copied  and  distributed  without restriction providing that: both the 
        program   and  documentation  files  are  distributed  together  as  a 
        package, neither is modified, and no fee is charged for the package.
        
        System  requirements  for  FERRITE.COM are an IBM Personal Computer or 
        compatible  computer system using either a monochrome or color display 
        and operating in the PC-DOS 2.0, or higher, environment.
        
        
                                      Page 1 of 4
        
        

        Operation
        
        At  the  DOS  prompt,  type  IRON  <return>  to invoke the program.  A 
        series  of  screen  prompts  will appear to assist you in entering the 
        necessary parameters.
        
        The  part number field may be used to identify the size and mixture or 
        type  of  core;  for  example,  a  typical  entry  might  be "T-50-2", 
        indicating a toroidal core one-half inch in diameter of mixture 2.
        
        The  wire  size  field may be used to identify the size (American Wire 
        Gauge)  of  the  wire  used for winding.  This data is not used in the 
        calculation  of  inductance;  however,  keep  in mind that the maximum 
        number  of turns that can be physically wound on a core is affected by 
        the  wire  diameter.   If  a  general  table  of  inductance  is being 
        prepared,  the  response  "Any"  or simply a <return> might be used in 
        this  field.   Refer  to the file CHART1.TXT for the maximum number of 
        turns  that  can  be  accommodated  on  different  size  forms for the 
        various AWG wire sizes.
        
        For  convenience, a printed copy of the chart can be obtained by using 
        the DOS commands; for example, TYPE CHART1.TXT >PRN.
        
        The  uH/100-T  field  is  the  permeability  of  the core expressed in 
        microhenries  per  hundred turns.  This parameter is obtained from the 
        data  sheet  supplied  by the core manufacturer.  All calculations are 
        based upon this parameter.
        
        The  minimum  and maximum number of turns fields are used to specify a 
        range  of  turns.   The default values are 1 and 60 respectively.  The 
        screen  and  printout always have a range of 60 turns.  The inductance 
        of  coils  having between 61 and 120 turns may be found by entering 61 
        as  the  minimum  number  and  120  as  the maximum number.  This same 
        technique can be used to extend the range even further if necessary.
        
        Once  all  parameters  have been entered, a table of inductance versus 
        turns  is  calculated  and displayed on the screen.  Also, the printer 
        prompt  will  appear  on  the  screen.   If a printed copy is desired, 
        enter Y <return>; otherwise, enter N <return>.
        
        Then,  the  prompt  "do  another"  will  appear  on  the screen.  When 
        Y <return>  is  selected,  the program will return to the beginning so 
        that  you  may  enter  parameters.   When  N <return> is selected, the 
        program  reverts  to  the  registration  screen.  Pressing <return> in 
        response to the prompt will return the system to DOS.
        
        The  program may be aborted at any time by pressing the CTRL and BREAK 
        keys simultaneously.
        
        
                                      Page 2 of 4
        
        

        Disclaimer
        
        The  Author reserves the right to make changes to this program package 
        in  order  to improve the reliability, function and/or design and does 
        not  assume  any  liability from either the application or use of this 
        material.   Under  no  circumstance  shall the Author be liable to you 
        for  any  damages,  including  but  not  limited to lost profits, lost 
        savings,  or  other  incidental  or consequential damages arising from 
        the  use  of or inability to use this material.  Further, although the 
        information  presented  herein  has been checked and is believed to be 
        reliable, no responsibility is assumed for inaccuracies.
        
        
        Registration
        
        The   FERRITE.COM  program  package  is  being  distributed  as  User-
        Supported  Software.   This  gives you the opportunity to evaluate the 
        program  at your convenience, on your own system in order to determine 
        whether  or  not  it  serves  your application requirements.  In other 
        words,  the  user-supported  software concept let's you try before you 
        buy.
        
        In  return, the Author requests that you become a registered user once 
        you  determine  that  the  program  is  useful  to  you.   To become a 
        registered  user,  a contribution of $5.00 for an individual or $50.00 
        for  a  corporation would be appreciated.  Your contribution will help 
        offset  development  costs  incurred  by  the Author and assure future 
        updates   as  well  as  new  product  offerings.   In  addition,  each 
        registered user is placed on a mailing list for future notification.
        
        Regardless  of  whether  or  not  you become a registered user, please 
        continue to copy and share this program with others.
        
        The  Author  welcomes ideas and suggestions that might be incorporated 
        into  future  versions  of  this program package.  Please address your 
        contribution and/or correspondence to:
        
                                  Scott R. Grabowski
                                     P.O. Box 471
                                  Newbury, OH  44065
        
        For  those individuals requiring an invoice for tax recording purposes 
        or  for initiating payment through your company accounting system, the 
        following form is provided.
        
        
                                      Page 3 of 4
        
        

        
        
        
        
        
        
                                        INVOICE
        
        
                                                     From: Scott R. Grabowski
                                                                 P.O. Box 471
                                                           Newbury, OH  44065
        
        
                                                     Date:                   
        
        
        Sold To:
        
        
        
        
        
        
        
        ITEM                                                           AMOUNT
        
        
        Registration Fee For: FERRITE.COM Program Package
        
                               [ ] Individual Registration              $5.00
        
                               [ ]  Corporate Registration             $50.00
        
        
                                           Amount Enclosed                   
        
                                                Sales Tax*
        
        
                                              TOTAL AMOUNT
        
        
        
        
        *Ohio residents please include 5% state sales tax.
        
        
                                       Thank You
        
        
                                      Page 4 of 4