PCROUTE

                                    Version 2.210
                                     Users Manual
                                  September 16, 1989









                                          by












                                  Douglas E. Ehlers

                                  Copyright (C) 1989








                                                                          2

                                  Table of Contents



          Notice of Copyright.......................................3

          Introduction..............................................4

          Installation..............................................5

               System Requirements..................................5

               Software Setup.......................................5

          Input/Output Menu.........................................6

          Board Definition Menu.....................................8

               Chip Definition......................................7

               Chip Placement.......................................8

          Interactive Router.......................................13

          Autorouter...............................................16

          Board Statistics.........................................17

          Printer Menu.............................................18

          Exiting the program......................................18

          Keyboard control summaries...............................19

          Brief Tutorial...........................................20

          Order Form...............................................22








                                                                          3

                                 Notice of Copyright



               This program  is protected  by a  copyright held  by me  and

          filed with the  United States Government.  Although  this program

          is being distributed  as Shareware, that  does not make it  free.

          You are granted  limited use of this  program to test it  out and

          see if it will  fulfill your needs.  If you  find that your needs

          can be satisfied  by this program and  you decide to use  it, you

          are obligated to pay  the 65 dollars to register your  copy.  You

          are allowed  and  encouraged to  give  unaltered copies  to  your

          friends to try out.  This same agreement applies to them.








                                                                          4

                                     Introduction



               PCROUTE  is  a  computer aided  design  program  for printed

          circuit boards.  It contains board layout routines that should be

          quite  for  most purposes.    It  also contains  a  full featured

          autorouter that averages around  a 93% completion rate.   It also

          supports three of the more popular printers for its output.

               This program is  to my knowledge the first of its type to be

          released as shareware.  Although it lacks several of the features

          of  similar  products that  are  commercially available,  it also

          lacks a $1000 price tag.  

                    Key features include:
                         1.   Autorouting
                         2.   Interactive routing
                         3.   Board layout functions
                         4.   Flexible pinouts for devices
                         5.   2X output for use in making PC boards
                         6.   Disk functions built into the software
                         7.   Sophisticated component and connection 
                              entry systems
                         8.   General statistics
                         9.   Up to 300 components and 1800 connections
                        10.   The authors continued support








                                                                          5

                                     Installation

          Contents of Archive/Disk:

               PCROUTE .EXE -  The main program
               PCROUTE .DOC -  The documentation for PCROUTE.EXE
               HPLASER .DAT -  Printer data for the HP Laserjet II
               SG10    .DAT -  Printer data for the IBM PC printer
               PAN1124 .DAT -  Printer data for the EPSON LQ-2500
               SMALL   .CDT -  Sample board that can be edited and routed
               DIP24V6 .DEF -  24 PIN DIP chip definition-vertical .6 wide
               DIP20V3 .DEF -  20 PIN DIP chip definition-vertical .3 wide
               DIP40V6 .DEF -  40 PIN DIP chip definition-vertical .6 wide
               PAD     .DEF -  Definition of a single pad
               2PAD50V .DEF -  2 PADS 0.5 inches apart-vertical
                               works well for 1/4 watt resistors
               2PAD15V .DEF -  2 PADS 0.15 inches apart-vertical
               2PAD10V .DEF -  2 PADS 0.10 inches apart-vertical
               PRINTDOC.BAT -  Prints the documentation stored on disk

          System Requirements:

               To run this program requires:
                         1. CGA or better graphics
                         2. 640k of memory (must all be available)
                            no other memory residents can exist as they may
                            lock up the system, you'll  have to experiment 
                          on this part.
                         3. 1 floppy disk drive
                         4. One of the following printers:
                              a. IBM PC or compatible printer
                              b. EPSON LQ-2500 or compatible printer
                              c. Hewlett Packard Laserjet II or compatible
                         5. Hard-Disk (not essential but recommended)
               A fast processor is also nice.

          Software Setup:

               If  you are  going to run  this program  from a  floppy disk
          system, simply copy all the files that came in the archive  or on
          the  distribution  disk onto  an empty  formatted floppy  disk by
          using the following command:

                                   COPY A:*.* B:

          Where A: contains the  original PCROUTE disk and B:  contains the
          empty formatted  floppy disk.   All  the files  that came on  the
          diskette are required to  run the program except the  PCROUTE.DOC
          file.  The PCROUTE.DOC file may be deleted from the run disk.

               If you  will be using a hard disk to run the program, make a
          directory  in  which to  place the  program.   Use  the following








                                                                          6

          commands to accomplish this:

                              1.   cd \
                              2.   md pcroute
                              3.   cd pcroute
                              4.   copy a:*.*

          Where A: holds the original PCROUTE files.

               For PCROUTE to  run reliably, you must  also have a line  in
          your config.sys file setting  files=20.  If you are  running most
          any major applications program this  command probably exists, but
          you should check.   To execute  the program type PCROUTE from the
          DOS prompt.



                                  Input/Output Menu

          1. Load Data:
                    This  function  is  used  to  retrieve  from  disk  the
               necessary  information to  design a  printed circuit  board.
               Select this function from the menu  and when prompted, enter
               the file name.  No  extension is used, the program  will add
               the  .CDT extension for you.  The  drive and path should not
               be used  on the filename itself.   There is a  function that
               will be  discussed later  to set  the drive  and path  name.
               After entering the filename, press Return.  The program will
               ask if this is the correct name, enter Y or N to answer.  If
               the file is  not found you will have a chance to reenter the
               file name.  You can also use the ESC key to jump back to the
               main menu instead of entering the file name.

          2. Save Data:
                    This function will  save a complete description  of the
               design layout, component list, and connection list.  It does
               not  save the information  used for  deleting traces  in the
               interactive  router  which will  be  discussed later.   When
               prompted, enter the filename.  Again do not specify the file
               extension, drive designation,  or path  name.  PCROUTE  will
               ask after entering the  file name if everything  is correct,
               enter a  Y or N.  If the file exists the program will ask if
               you want  to overwrite  the file.   If you  say no,  it will
               prompt for a new file name.  ESC also works to return you to
               the I/O menu instead of entering the file name.

          3  Write Autocad file:
                    This function will  write a  file that can  in turn  be
               read into and edited with Autocad.  The  process is one way,
               you can not  read an autocad  file back into PCROUTE.   Call
               this  function  from  the I/O  menu  and  give  a name  when
               prompted.  Here as usual, specify no path or file extension.








                                                                          7

               The extension  .scr will  be added to  the file.   Once  the
               program is done  writing the file,  you may run Autocad  and
               use  the  command  "SCRIPT"   from  the  "Command:"  prompt.
               Autocad will ask for the script file name.  Specify the same
               name  (with path if  needed) as the one  you used in PCROUTE
               and Autocad will read in the file.  It may take awhile so be
               patient.    Autocad  will  display  three   layers:  solder,
               component, and silkscreen.   You may  edit them however  you
               like and save  them as  Autocad drawing files.   Doing  this
               greatly increases the number of  printers you can output  to
               as Autocad supports mega-hardware.

          4. Erase Data:
                    This  routine  clears the  memory of  the program.   It
               erases the  boards, stacks,  component list,  and connection
               list.  The program will ask if you are sure that you want to
               erase  the data in memory.  Answer Y or N.  The program will
               respond with "Erasing..."  and after a few  seconds drop you
               back to the I/O menu.

          5. Disk Directory:
                    This function displays a directory of the current drive
               and path.  Use the  space bar to view twenty file names at a
               time.  When no more  files exist, the space bar  will return
               you to the I/O menu.

          6. Change drive/path:
                    This function changes  the current  drive and or  path.
               The  ESC  key will  back  you  out of  the  function without
               changing the  path.  The  function will display  the current
               drive and path  and then prompt for  a new one.   Just enter
               the new one and  press Return.  You will be  returned to the
               I/O menu.


                                Define/Edit Board Menu

          1. Component Edit/Entry:
               This function is used  to enter components into the  system.
          Once  you  have entered  this  function  you will  placed  in the
          entry/editing environment.   If no  components have been  entered
          you will see only two possible  commands, if there are components
          in memory you  will have the option  to delete, copy and  perform
          other functions. 

          New Component Entry:
               Hitting an "A" will  allow you to enter new components.  The
          program will  display the component number being entered and then
          prompt  for the name.   The name is up  to 15 characters long and
          serves only to  remind the designer of  what the device is.   ESC
          can  be used  at this  point to return  you to  the entry/editing
          environment.








                                                                          8

               The  next  question is  for the  designation.   This  is the
          unique  name that  you will  give the  component  and use  in the
          future to refer to it.   Typical names include IC1, R1, IC2,  and
          A1.  The only  reserved designation is for vias. (A via  is a pad
          with no device  attatched to it.  It is just  to connect a  trace
          from one side of the board to the other)  Designations that start
          with "V" and  then have a number  after that, are not  allowed in
          the system.   So V1 would not  be accepted by VI1 would  be.  ESC
          may be  used to back  up while  entering the designation  name to
          reenter the component name.
               Third the program will prompt for the definition file  name.
          This is the name of a file that tells the program how the pins on
          the device being entered are situated.  The program first shows a
          list of possible definition  file names at the  lower right.   At
          the end of the  list the program will prompt for a  name.  Do not
          enter a file extension, the program will add it  for you.  If the
          name of the file  entered exists, it will read the  file for you,
          and display the  chip definition for you to see if it is correct.
          If  you answer  yes that  it is  the correct definition  you will
          continue to the  next question.   If the file  did not exist  you
          will be  asked if  you wish  to create  the definition.   If  you
          answer no,  the program  will re-prompt  for the  definition name
          after showing you  the possible files.  Otherwise it makes a  new
          definition.  ESC may be used to back up and reenter the component
          designation.

               Creating New Definition Files:
                         The program needs to know the exact  pin layout of
                    any  component  placed  on the  board.    This function
                    allows you to create these definitions.  Upon entry you
                    will see a graphic screen  with some information at the
                    bottom and a green square in  the middle of the screen.
                    In the top left of the box is your cursor.  You use the
                    cursor keys  to move  the cursor around  to define  pin
                    locations.  The pins are entered in the order from 1 to
                    up to 40.  Move the cursor to the position of the first
                    pin  and hit  return to  place it.   Then  move to  the
                    second position and hit return to place pin 2.  You may
                    also remove pins in  the reverse order you placed  them
                    by positioning your  cursor over  the last pin  entered
                    and  hitting  the backspace  key.   This key  will only
                    delete the  last entered pin.   The information  at the
                    bottom of the  screen will  tell you what  pin you  are
                    entering,  as  well  as its  relative  location  on the
                    screen.  When you  have placed 40 pins or  are finished
                    with the component definition, hit ESC to  finish.  The
                    program will ask if you want  to reedit.  Answering yes
                    will  clear  the screen  and you  can  start over.   By
                    answering no you will receive  the prompt asking if you
                    want to keep the definition or not.  Answering yes will
                    save the definition for later use, no will give you the
                    list of existing  definitions on the previous  screen. 








                                                                          9

                    All components are moved to the upper  left most corner
                    for saving.   This  is  for internal  reasons; you  can
                    design the chip anywhere in the  square.  You will need
                    to make  definition files for  all your components.   I
                    would  suggest  a meaningful  system  for  naming them.
                    Maybe something like DIP16V and DIP16H for 16  pin Dual
                    Inline   Package   Vertical  attitude   and  Horizontal
                    attitude respectively.
                    ***Note:  Most  chip dimensions  are available in  data
                    books such as RCA cross reference manuals.  Radio Shack
                    also  puts  device  dimensions  on  the back  of  their
                    packages.

               The next question the  program will ask is if  everything is
          correct.    Answering  no  will  restart  this  process with  re-
          prompting for the name.  Answering yes will get the next prompt.
               The  next  prompt  is  if  you  wish to  keep  this  device.
          Answering no  will skip the  next prompt and  ask if you  wish to
          enter another device.  Answering yes gives you the next prompt.
               This  prompt  asks if  you  wish  to place  the  device now.
          Entering  no  will allow  you  to delay  this until  later.   All
          devices must be placed somewhere on the board before  they can be
          connected.  Placing a chip goes as follows:

               Placing Chips:
                         When  this graphic screen comes  up you will see a
                    representation of  the current  circuit board with  all
                    other placed components  and ground planes shown.   The
                    chip you are entering  will be shown in the  upper left
                    corner of the  board.   The arrow keys  will move  this
                    chip  around  on  the  board.  By using  a  shift-arrow
                    combination the chip  can be  moved faster.   Move  the
                    chip to where you want it and press return.  You cannot
                    overlap  chips.    The  chip  is  now  placed  in  this
                    location.  If you change your mind you can press ESC to
                    exit without placing the chip.  You will be prompted if
                    you are sure you want to abandon chip placement or not.
                    Yes will go to the  next prompt, no will put you  right
                    back where you were before hitting ESC.

               The last prompt is if you wish to enter another chip or not.
          Answering yes will  put you back up  at the name prompt  to enter
          another  chip.    No  will  put  you back  in  the  entry/editing
          environment.

          Editing Component Definitions:
               Selecting E from the entry/editing environment will give you
          the ability to change any part of each definition.  Simply select
          the  letter of the  item to change.   For example,  to change the
          name, hit A after hitting E and you will be  prompted for the new
          name.  Either enter the  new name, or you can press ESC  to leave
          it  unchanged.   When you  are done  editing, press the  key that








                                                                         10

          corresponds to exiting the edit.

          Deleting Component Definitions:
               This  function  allows  you  to delete  a  component.    The
          component that will be deleted is  the one currently displayed on
          the screen.  Press D and you will be asked if you are sure if you
          want to delete this  component or not.  Answer  accordingly.  All
          connections  that  contained the  deleted  function will  also be
          deleted.

          Copying Components:
               This function will let you make  copies of a chip definition
          to speed the  entry of chips.   It will copy everything  from the
          displayed  definition  to   a  new  definition  except   for  the
          designation  from  which it  will take  the  alpha part  and then
          increment the numerical part to the next available part.  It also
          does not put the chip in the same location.  You will be asked if
          you wish to place the chip now or later.

          Searching for a Component:
               Sometimes finding the component  you wish to edit or  delete
          can take some time on a large board.  This function allows you to
          search for components  by the designation.   When prompted  enter
          the designation, PCROUTE will  change the case to upper  for you.
          If  it exists the program will display  that device's number.  If
          it doesn't exist, you will continue right where you were.

          Incrementing and Decrementing the displayed Component:
               Using  +  and -  will  change  the displayed  component.   +
          increments and - decrements.  The  display is circular in nature,
          therefore hitting  + at the  last component  will put you  at the
          first and hitting - at the first will put you at the last.

          Exiting the Entry/Editing Environment:
               Use the N key to end these functions and return to the board
          definition menu.

          2. Connection Edit/ Entry:
               This  system  allows  for  entry  and  editing  of  all  the
          connections that need  to be made  between the components in  the
          system.    The  functions  are  very  similar  to  the  component
          functions.

          New Connection Entry:
               Typing an "A" will allow you to enter new connections.   The
          program will display the connection number being entered and then
          prompt for the  name of  the source designation.   The name  must
          exist in memory as a component.  ESC can be used at this point to
          return you to the entry/editing environment.
               The next question is for the source chip pin number.   Enter
          the number of the pin that you want the trace to connect to.  ESC
          will back you up to the previous prompt. 








                                                                         11

               The program will now prompt for  the name of the destination
          designation.  The name must exist in  memory as a component.  ESC
          can be used at this point to return to the previous prompt.
               The next  question if for  the destination chip  pin number.
          Enter the number  of the pin that  you want the other  end of the
          trace to  connect  to.   ESC will  back you  up  to the  previous
          prompt.
               The program will now ask if this is a priority route or not.
          By answering yes, this trace will be routed before all other non-
          priority  routes  no matter  how long  it may  be and  what other
          routes it may block.  This might be used for making sure a memory
          access bus is all done in  copper instead of using jumpers for  a
          vital connection.
               The next question the  program will ask is if  everything is
          correct.   Answering no will restart  this process by reprompting
          for the source designation.  Answering yes will bring up the next
          prompt.
               The next  prompt is  if you  wish to  keep this  connection.
          Answering  no will skip  the next prompt  and ask if  you wish to
          enter  another  connection.   Answering  yes gives  you  the next
          prompt.
               The  last  prompt   asks  if  you  wish   to  enter  another
          connection.  Answering yes,  will put you  back up at the  source
          designation  prompt to enter another connection.   No will places
          you back in the entry/editing environment.

          Editing Connection Definitions:
               Selecting E from the entry/editing environment will give you
          the ability to change any part of each connection.  Simply select
          the letter  of the item  to change.   For example, to  change the
          source  designation,  hit  A after  hitting  E  and  you will  be
          prompted  for  the  new  designation.     Either  enter  the  new
          designation, or  press ESC to  leave it unchanged.   When you are
          done editing, press the key that corresponds to exiting the edit.


          Deleting Connection Definitions:
               This  function allows  you  to  delete  a connection.    The
          connection that will be deleted is the one currently displayed on
          the screen.  Press  D and you will  be asked if you are  sure you
          want to delete this connection.  Answer accordingly.

          Searching for a Connection:
               Sometimes finding the  connection you wish to edit or delete
          can take some time on a large board.  This function allows you to
          search for connections by the  designation.  When prompted  enter
          the designation sought.  PCROUTEwill change the case to upper for
          you. PCROUTE then will search from  the current connection to the
          end.  It  looks at both  the source and destination  designations
          for a match.   If  it finds  the search string  the program  will
          display that connection's information.  If it doesn't  exist, you
          continue right where you were.








                                                                         12


          Incrementing and Decrementing the displayed Connection:
               Using  +  and -  will change  the  displayed connection.   +
          increments and - decrements.  The  display is circular in nature,
          therefore hit + at the last connection  will put you at the first
          and hitting - at the first will put you at the last.

          Exiting the Entry/Editing Environment:
               Use the N key to end these functions and return to the board
          definition menu.
          3. Ground Plane:    This  function  is used  to  set up  a ground
                              plane.  The program will display a picture of
                              the board.   It will prompt for  the width of
                              the ground plane  on all  four sides on  both
                              the  component side  and solder  side of  the
                              board.  Each digit entered corresponds to .05
                              actual inches.  You may  come back and change
                              the ground plane sizes at any time.  ESC will
                              also back you  out of  the first prompt  only
                              (top-solder side).
                              ***   Please note  that this  function erases
                              any  work  done  in  the  interactive  router
                              (discussed later).

          4. Define Board Size:    This  function  is  the  first  function
                                   used.  It defines the  dimensions of the
                                   board.  The maximum board size supported
                                   by PCROUTE is  11" X 8".   When prompted
                                   for numbers, you must  enter the numbers
                                   as  multiples   of  5.     Each   number
                                   represents 0.05" of actual  size.  So an
                                   entry  of  100 would  correspond  to 5".
                                   You may change  board sizes at any  time
                                   during the design process by calling the
                                   routine.  If you make the board smaller,
                                   the chips  that  were  outside  the  new
                                   border will  have to be  replaced.   ESC
                                   will  back up to the previous prompt, or
                                   jump out  of  the  routine  leaving  the
                                   board size unchanged.

          5. Spider Web: This  function is useful for checking  to see if a
                         chip  would  be  more logically  placed  somewhere
                         else.   By using the +  and - keys, you can toggle
                         through the chips.   As each chip  is selected, it
                         as  well  as  all  traces   connected  to  it  are
                         highlighted in red.   Once a chip  is highlighted,
                         you can select M to move the chip.  After pressing
                         M, the  arrow keys become  active and the  chip as
                         well as all its connections  will be rubber banded
                         around the board.  You can hit RETURN to place the
                         chip  at the current  location, or hit  ESC to not








                                                                         13

                         place  the chip and  put it  back at  its original
                         location.  The  ESC or  E key will  exit you  from
                         this function.
                         *** Please note,  if you move any  chips, the work
                         done by the interactive router is erased.


                                  Interactive Router

               This board editing system allows you to interactively design
          a  board. It can be very  useful for finding possible routes that
          the autorouter was unable  to find.   Upon entry to this  section
          the program  generates the borders and places the pads of all the
          chips.  It will also ask you to place all the chips that have not
          been placed yet.   If you intend  to route the entire  board this
          way,  place your chips  and then leave them.   Moving them around
          after placing  the chip will distort your  board.  PCROUTE has no
          way of connecting  traces up to a chips new location.  The screen
          will  show all the  chips with  their designations  centered amid
          each components pins.  This system  has many keys that are active
          while in this environment.  An explanation of each follows.

          S - switch sides:   This function  changes the side  of the board
                              displayed.   When you  enter S,  you will  be
                              shown  the  other  side of  the  board.   The
                              program  supports  only 2  sides,  solder and
                              component.

          E or ESC - end:     Pressing  E  or ESC  will  exit you  from the
                              interactive router.

          Cursor Keys:   The cursor keys move the solid block around on the
                         board.   Each time you  press the  arrow key,  the
                         cursor will  move 1  space.  Relative  coordinates
                         are displayed at  the bottom of the screen.  Using
                         Shift-Arrow moves the  cursor 10  spaces.  If  you
                         come to the edge of the screen but not the edge of
                         the board, the  screen will  shift the board  over
                         for you.

          Function Keys:
               The function keys numbered F1-F8 do the majority of the work
          in PCROUTE.   They allow you  to place  vias, run traces,  delete
          traces, blank old traces, and delete vias.

          F1 - Set Source:    By  positioning  the cursor  over  a pad  and
                              hitting F1 you select that pad as your source
                              location.  The bottom  status line will  tell
                              you exactly what chip and pin number you have
                              selected.

          F2 - Set Dest.:     This  function   works  exactly  as   the  F1








                                                                         14

                              function but selects the destination pin.

          F3 - Run Trace:     Once  you   have   defined   a   source   and
                              destination,  hitting  F3  will   attempt  to
                              connect the two pins with a  trace.  If it is
                              successful, you  will see  the trace  appear.
                              If  it  cannot  complete  the  route it  will
                              notify you at  the bottom.  At this point you
                              might try placing a via  and routing from the
                              source to it on one side  and from the via to
                              the destination on the other.

          F4 - Delete Trace:  This  function will  delete traces  that have
                              been  routed since the  program has been run.
                              If  you  have just  loaded  the board  up and
                              decide to  delete a trace  this function will
                              not work.   Saving  the board  does not  save
                              deletion information.   Assuming the  data is
                              in memory to perform the  delete, the program
                              will highlight the  trace to delete.   If the
                              highlighted  trace is the  one to  be deleted
                              answer  Yes when  prompted.   Hitting N  will
                              advance to the next trace if it is available.
                              Hitting ESC will drop you  back to the cursor
                              control mode.

          F5 - Add Via:  This function key  will add a via  at the location
                         of the cursor.   It will  be V and  then the  next
                         available number.  Use these for multilevel routes
                         or just extra pads needed.  You cannot place a via
                         adjacent to  an existing pad.   You can  place one
                         diagonally  from  one though.    You also  may not
                         place a  via in the  middle of a trace.   All vias
                         are deleted by the autorouter when it is invoked.

          F6 - Del Via:  This  function  deletes  the  via  at  the  cursor
                         location if one exists there.

          F7 - Erase Space:   This  function will remove the trace piece at
                              the location of the cursor.  This function is
                              useful if you deleted a  series of traces and
                              left   something   unconnected.     Use  this
                              carefully.

          F8 - Check Route:   This function will check to see if a selected
                              pair  of  pads  can be  connected.    It will
                              report back as  to whether  the route can  be
                              completed.  This is  useful for doing  multi-
                              layer routes  using  vias.   Checking for  an
                              available  route  before  laying  the  actual
                              trace will save  a bunch of deletes  if later
                              your path is blocked.








                                                                         15

          F9 - Manual Route:  This  function allows  you to  manually route
                              traces.  Place the cursor on the starting pad
                              or trace and press F9.   If the cursor is not
                              on  a  valid  starting  point,  nothing  will
                              happen.  Now  use the cursor control  keys to
                              route your trace.  Every  time you move, your
                              trace is lengthened.  When  you are done, you
                              can either stop  in and open space  and press
                              F9 or you can stop on  a trace or pad and hit
                              F9,  the  correct  connecting piece  will  be
                              added  to make  the connection.   Please note
                              that  if  you  go  over  an  existing  trace,
                              PCROUTE will cut  that trace in favor  of the
                              new path.  This works  well for putting short
                              jumpers on the  board.   This is very  useful
                              for routing traces  that would normally block
                              other  routes if  they were  not placed  this
                              way.     As  my  autorouter   algorithm  gets
                              "smarter" hopefully we won't need this.








                                                                         16

                                     Autorouting

               Selecting this from the menu will  enable you to connect all
          or most  of the connections you  desire.  The program  will first
          draw borders, place  pads, and set  up the ground  planes.  If  a
          component has not  been placed, you  will be asked  to place  it.
          The  program requires all chips to be placed before it can route.
          There are  four routing  strategies that  can be  employed.   You
          select each  strategy by hitting  Y or N  as the cursor  moves to
          each option.   If you hit Y for  single or double via routing you
          will  also be prompted for the  maximum number of tries for each.
          Just  enter  a number.    Bigger  numbers are  better  for bigger
          boards, smaller number for small boards.
               The  PCROUTE  system  is  totally  re-entrant.    The  first
          question  you are  asked  is if  you wish  to  clear all  traces.
          Answering yes clears anything  currently on the board.   No would
          keep what was on  the board such as work done  by the interactive
          router.  You can hit ESC during any routing strategy to exit that
          routine and the  autorouter.  The program will then show the list
          of all unconnected routes still existing.   If the router has not
          completed one  run-through and you have routed before, traces may
          have been completed by the earlier route and still be reported as
          unconnected.  You  can do a design  check to see which  routes in
          you connection  list have not been connected either by hand or by
          autorouter  by running the autorouter and not erasing the current
          traces.  Just select the double or single sided route system.  It
          will report any routes that  are incomplete.  Any route that  was
          completed  before will be  marked as  complete and  not reported.
          The program will report whatever routes weren't done and the ones
          it couldn't complete.

          Single Sided Route: This function will  attempt to place  all the
                              routes  on the solder side of  the board.  It
                              is the  least efficient strategy but is great
                              for  small projects where  ease of making the
                              board itself  is a  priority.   This function
                              cannot be  used in conjunction  with the next
                              three strategies.

          Double Sided Route: This  function  will do  its  routing  on two
                              sides  of  the  board.     It  has  a  higher
                              completion percentage than  the single  sided
                              strategy.

          Single Via Route:   This function requires that the double  sided
                              strategy be select  first.  This  function is
                              used after the  double sided strategy to  try
                              to  complete  any  uncompleted  routes.    It
                              places a via and tries to do the single route
                              with a trace  on each side  of the board.   A
                              number such as 50 is  good for maximum number
                              of tries.








                                                                         17


          Double Via Route:   This  function  also  requires  double  sided
                              routing be  selected to  work.   It uses  two
                              vias to  attempt to  complete the  route.   A
                              good maximum  number of  tries is  30 or  so.
                              This function can  take a great deal  of time
                              so be patient.


                                   Board Statistics

          This function displays 3 statistics that may be of some interest.

          Equivalent Integrated Circuit Count:    This   function   is  the
                                                  total   number  of   pins
                                                  divided by 16.

          Board Density: This is the  amount of space total  that each chip
                         has  to occupy.   It is  calculated by  taking the
                         area of the  board and dividing by  the Equivalent
                         IC count.

          Total Trace Length: The function  gives the total  length of  all
                              the traces  on the  board.   The smaller  the
                              number, the better the design.








                                                                         18

                                     Printer Menu

          1. Print Component List: This function  will generate  a list  of
                                   all the components.  It can be sorted by
                                   name or designation.  

          2. Print Connections:    This  function will  generate a  list of
                                   all the  connections in memory.   It can
                                   be sorted  by the source  or destination
                                   designation.

          3. Print Solder Side of Board:
                    This function  will generate  the artwork  to make  the
               printed circuit board.   The program will ask if you want to
               mirror  the  board.   This  may  be necessary  if  your film
               requires  printing on a  particular side.   The mirroring is
               done left to right.  Next it will ask if you want a negative
               made.  This  will make the  traces white and the  background
               all black.   On Laser printers you  also have the  option of
               making an actual size printout, or the standard 2X size that
               the dot matrix printers print.  The ESC key will exit out of
               the printout at any time.

          4. Print Component Side of Board:
                    This function  is identical  to number  3 above  except
               that it prints the component side of the board.

          5. Print a Silkscreen Representation:
                    This function will generate a pseudo-silkscreen.  It is
               not  the same  scale as numbers  3 and  4 but is  useful for
               remembering where components  are to be placed.   Select the
               printer to be used and watch it go.


                                 Exiting the Program

               Selecting 7 from  the main menu  will drop you from  PCROUTE
          back to DOS.  If you have data in memory you will be asked if you
          wish to save it. Answering Yes  will prompt you for a file  name.
          Enter the file name as you would in the save data function in the
          Input/Output menu.   You can hit  ESC to abort  the save, but  it
          will not  return you to  the program.   Answering No to  the save
          query, will drop you immediately to DOS.








                                                                         19

                                  Keyboard Summaries

          Chip Placement Screen:
               ESC                 - Option to Abandon Placement
               RET                 - Place chip at current location
               Cursor Keys         - Moves chip one space for each 
                                     depression
               Shift Cursor Key    - Moves chip 10 spaces for each 
                           depression

          Define Chip Definition:
               ESC                 - Option to Abandon Definition
               RET                 - Place pin at current location
               Cursor Keys         - Moves cursor one space for each stroke
               BACKSPACE           - Removes last placed pin

          Spider Web System:
               M*                  - Set system to move highlighted chip
                    Cursor keys    - Move chip one space on board
                    RET            - Place chip at current location
                    ESC            - Abandon placement
               +,-*                - Increment and Decrement through chips
               E*                  - Exit Web System

          * - Denotes that this selection is displayed on screen.

          Interactive Router:
               S                   - Display other side of board
               E,ESC               - Exit interactive router
               F1                  - Select source pad
               F2                  - Select destination pad
               F3                  - Attempt to connect source and 
                                     destination
               F4                  - Delete traces connected since system 
                                     started
               F5                  - Place via at cursor location
               F6                  - Delete via at cursor location
               F7                  - Remove trace piece at cursor location
               F8                  - See if route is possible between 
                                     source and destination pads
               F9                  - Enters and exits the manual router








                                                                         20

                                    Brief Tutorial

               The following  is intended  as a  method of  getting up  and
          running with the program.  It will give a general idea of how the
          program works.  It is not intended as a "learn all" tutorial.

          1.   Begin by  running PCROUTE.   This information  can be  found
               back in the section on setting up PCROUTE for your machine.

          2.   Once at the main menu, hit 3 for define/edit board, and then
               select 4 for define  board dimensions.  For our  purposes we
               will use  a board size of 80 x 80, which translates into a 4
               inch square board.

          3.   Select function 1  to enter  new components.   You will  see
               that no data has been entered yet.  Hit A to enter data.  We
               will put three chips on the board and two resistors.  Answer
               each prompt below  with the following  data.  When asked  to
               place each chip  answer Y and place the chip with the cursor
               keys.  After you have entered the last item, answer N to the
               "Enter another component?" prompt.

               Name: 8051 uP                 Designation:  IC1
               Definition file: DIP40V6      Placement: Left side of board

               Name: 74ls373                 Designation:  IC2
               Definition file: DIP20V3      Placement: Upper right

               Name: 2716                    Designation:  IC3
               Definition file: DIP24V6      Placement: Lower right

               Name: 100k resistor           Designation:  R1
               Definition file: 2PAD50V      Placement: Upper middle

               Name: 10k resistor            Designation:  R2
               Definition file: 2PAD50V      Placement: Lower middle

          N exits you to the board definition menu.

          4.   Next, we want to  enter some connections to be  made between
               the chips.  Select 2 from  the menu to enter the  connection
               entry  section.  Enter the following  connections.  Answer N
               to each prompt  of "Is this  a priority connection?".   When
               you have entered the last connection  answer N to the "Enter
               another connection prompt?".

               Source Defice       Pin       Desitination Device      Pin
                    IC1            2              IC3                 2
                    IC1            3              IC2                 16
                    IC3            22             IC2                 6
                    R1             1              IC2                 4
                    R2             1              IC1                 8








                                                                         21

                    R2             2              IC3                 6
                    R1             2              IC1                 31
                    IC2            8              IC3                 17
                    IC1            21             IC1                 15
                    IC2            8              IC3                 8
                    IC2            9              IC3                 9
                    IC2            10             IC3                 10
                    IC1            14             IC2                 9

          N returns you to the menu.

          5.   Ok, lets autoroute  the board.  Go back to the main menu and
               select  4  to autoroute  the board.    When prompted  to use
               single sided routing or not, answer Y.   Now hit the ESC key
               and  watch the  machine  route.   When it  is  done is  will
               display the list  of uncompleted connections to  the printer
               or screen.   Select  whichever  you wish.   We  will now  be
               dropped back to the  main menu.  We can take  a look at what
               we have  done by selecting number 5 from  the menu.  You can
               cursor around and see  a representation of the board  on the
               screen.  Hit ESC when done.

               Now lets re-route  the board using double  sided techniques.
               This time say  N to single sided  and Y to double  sided and
               then hit ESC.  The machine will route double sided and again
               give a list of incomplete connections  if any exist.  Select
               printer or screen  for this list.   Lets take a look  at the
               board again.  This time we may also want to use the S key to
               change sides of the board that we are viewing.  When you are
               done hit ESC.

          6.   From the main  menu, hit  6 for statistics.   Displayed  are
               three statistics that tell you how good your design is.  Hit
               space when you are done with this.

          7.   Last of all  we'll print this baby  out.  Hit 2  for printer
               menu.  Now select silkscreen.   Select your printer and then
               hit  N for mirrored  image.  Your  printer will  now print a
               quick mockup of the  board.  This is useful  for remembering
               what  chip goes where.   Now hit  3 to print  out the solder
               side of the board.  Select your printer and answer N to each
               prompt. Your printer will shortly come to life and print out
               a 2X print  of the copper patern  on your printer.   You may
               hit ESC  to abort the  printout if you are  tired of sitting
               around.








                                                                         22

                                      Order Form
                       Please enclose this form when ordering.

          Name:     __________________________________________


          Address1: __________________________________________


          Address2: __________________________________________


          City:     _________________   State:    _______   Zip:_________


          Phone Number:  (________) ________-______________


          Computer name: _____________________________________


          Processor: 8086  8088  80186  80188  80286  80386  80386SX


          Printer type:  _____________________________________

          Suggestions/comments/other information:

          ____________________________________________________

          ____________________________________________________

          ____________________________________________________

          ____________________________________________________

          ____________________________________________________

          ____________________________________________________

          ____________________________________________________

          ____________________________________________________


          Please also  enclose the $65 check  or money order,  (do not send
          cash) made payable to:

                                   Douglas E. Ehlers
                                   4520 S. 58th
                                   Lincoln, NE  68516
                                   (402) 435-8440