KANODE.DOC

Notes on using KA-Nodes in FWD.MB for forwarding connects:
----------------------------------------------------------

(For use with W0RLI V9.xx and later software and Kantronics KPC-2, KPC-4 and
KAM with V2.85 ROMs or later.)

Date: March 25, 1989
From: Greg Day - KC8JN @ KC8JN
      Wintersville, OH 43952


GENERAL INFORMATION
-------------------

This information is provided for those SYSOPs using Kantronics KA-Nodes in
their forwarding connect paths to remote BBSes.  The W0RLI software is designed
to handle NET/ROM type connects automatically, but because the KA-Node issues a
sign-on message when accessed, has different status messages, and the W0RLI
software is not designed to handle this type of information, it is necessary to
implement a special sequence to handle these KA-Node connects.


ALTERATIONS TO FWD.MB
---------------------

The following is the standard sequence to be placed in the FWD.MB file within
a path list:

     xC kanode-n
     Sm destcall-n
     R!
     R!
     R!
     R?###LINK MADE

Where......

     x = C or N depending on whether or not this is s direct connect (C) or a
         connect made from a NET/ROM node (N) - see the FWD.DOC documentation
         with the W0RLI software

     kanode-n = call sign of the KA-Node with which you wish to be connected
                (-n is the SSID, if any)

     m = mode for KA-Node, C is a direct connect, X is a cross (Gateway)
         connect (to the opposite port on the KPC-4 or KAM - if the GATEWAY
         parameter is ON)

     destcall-n = call sign of the next station with which you wish to be
                  connected (-n is the SSID, if any)

Examples of connect path records from FWD.MB:

     CC K8AL-1          (make initial connect to NET/ROM node)
     NC NG8P-1          (connect to the KA-Node from the NET/ROM node)
     SC AD8I            (make a direct connect to the destination BBS)
     R!
     R!
     R!
     R?###LINK MADE
     FA0023AD8I
     @C:\BBS\AD8I.FWD
     *** EOF

OR......

     CC K8AL-2          (make initial connect to NET/ROM node)
     NC NG8P-1          (connect to the KA-Node from the NET/ROM node)
     SX K1LT-2          (cross connect using other radio port via GATEWAY)
     R!
     R!
     R!
     R?###LINK MADE
     NC AD8I            (continue with NET/ROM node style connects)
     FA0023AD8I
     @C:\BBS\AD8I.FWD
     *** EOF

Be sure to type in the required information, especially the "R?###LINK MADE"
line, EXACTLY as shown, otherwise the forwarding will fail!


SPECIAL CASES
-------------

Please note that you should test ALL KA-Nodes you use to be sure of the data
they send upon connect.  You may need to make the following changes for those
KA-Nodes that have earlier ROMs (prior to V2.85) or have the NTEXT message set
to null:

     Earlier KA-Nodes or those with V2.85 ROMs and NTEXT set to NONE......

          Delete one (1) line of "R!" to allow for only two message lines being
          sent upon connect.

     Earlier KA-Nodes with a different prompt character - V2.85 uses a "?" but
     earlier ROMs have a ">" instead......

          Change the "?" (after the "R" in the LINK MADE line) to a ">" - this
          is the prompt for some earlier KA-Nodes.


CONCLUSION
----------

If you have any questions regarding the use of the Kantronics KA-Nodes in
forwarding with the W0RLI Mailbox, pleae contact me via packet "@ KC8JN",
located in eastern Ohio.

73, Greg - KC8JN