THIS PACKAGE IS A USEFUL ANTENNA ANALYSIS PROGRAM FOR THE RADIO
  AMATEUR, PROFESSIONAL, TECHNICIAN AND STUDENT INTERESTED IN ANTENNA DESIGN.
  IT IS STILL UNDER DEVELOPMENT AND YOUR COMMENTS WILL BE USEFUL
  TO THE AUTHORS. TO USE THESE PROGRAMS YOU MUST:
  1. Add GWBASIC to the disk.
  2. You should compile the programs you wish to use or else they are too
     slow although still useful.
  3. The manual describes a menu system but this feature is not included
     in this package. Programs can be loaded separately an run.
  The manual is lacking in a few line diagrams that are included
  with the original printed and bound version.

  Any comments can be addressed to:
                   A. J. Ferraro
                   RM 225 EEE
                   University Park, Pa.
                               16802


                          INTRODUCTION

        Concepts and ideas can be more easily understood when one
   can feel and visualize what is being discussed.  This is ever
   more so in the teaching of electromagnetic theory where there is
   so much abstraction.  The instructor has the arduous task of
   formulating his ideas and presenting it to the students who have
   no other alternative but to try to understand as much as they
   can.  An application of the electromagnetic theory is antenna
   engineering.  This is an area where many discussions are centered
   around the "invisible".  Describing an antenna pattern is not an
   easy job and when there are many cases to study, drawing many
   patterns is no fun either.  This is where this courseware
   package comes in.

        This package was designed in the Electrical Engineering
   Department at Pennsylvania State University.  It is aimed at
   both the students and faculty.  To the undergraduate students,
   the approach to this package is to treat it as an antenna
   engineering laboratory.  Instead of hooking up wires and
   equipment, students can carry out experiments on the computer.
   This saves time and effort since changing several parameters can
   be done quickly and results are immediately displayed.  Graduate
   students who are preparing for the candidacy examinations can
   use it as a review or to get some information in a limited time. The
   faculty can use it to try new ideas and also to formulate exam
   questions.

        Basically, this courseware covers courses EE361, EE411,
   EE432, EE438 and EE538 offered by the Electrical Engineering
   Department at Penn State.  Presently, only topics which are
   related to antenna engineering are covered.  The package can be
   divided roughly into six areas.  These are Transmission line
   problems, wire antennas, arrays, broadband antenna, aperture
   antenna and antenna synthesis.

        Transmission line problems can be used by students taking
   courses EE361, EE432 and EE438.  It involves simple matching
   methods.  Wire antennas includes the straight wire dipole, the
   folded dipole and the Yagi-Uda antenna.  This module can be used


   to study the radiation patterns, self impedance of a single
   element and the mutual impedance between two elements.  This
   module is particularly relevant to students in EE361 and EE438.

        The third module is Arrays.  Mutual impedance between
   several elements are studied.  Array characteristics such as the
   driving point impedance, efficiency and directivity can be found
   for various linear array configuration.  Feed line designs for
   the array are also included.  The radiation pattern of
   rectangular and circular planar arrays can be computed for
   different array configuration.  Students taking EE432, EE438 and EE
   538 should find this module useful.

        The next module is Broadband antennas.  The design of the
   Log periodic dipole array is made easy using this module.  Other
   topics include linear, rectangular and circular aperture, the
   parabolic antenna and the horn antenna.  These antenna are
   discussed in EE438 and EE538.

        The study of antenna engineering is incomplete without
   knowing antenna synthesis.  In normal antenna design, the
   radiation pattern and array factor are calculated after the
   antenna configuration is established.  However, in antenna
   synthesis, the desired pattern are first specified.  This is then
   followed by a procedure to find the best antenna configuration
   that meets the pattern requirement.  The classes of synthesis
   method which are covered are the Woodward-Lawson line source and
   array factor, the Chebychev synthesis and the Taylor line source
   method.  This last module is fully covered in the graduate course
   EE538.
03


                    ANTENNA ENGlNEERlNG COURSEWARE

                                  by

          AHMAD FAlZAL MOHD. ZAlN and DR. ANTHONY J. FERRARO

                  ELECTRICAL ENGlNEERlNG DEPARTMENT
                    PENNSYLVANlA STATE UNIVERSITY


   The authors have made every conceivable effort to ensure the correctness and
   accuracy of the programs.  However, no implied warranty of guarantee of any
   kind
   is made with respect to the accuracy, completeness and effectiveness of
   these
   programs.

  
   Under no circumstances will the authors be liable for incidental or
   otherwise
   consequential damages in connection with the furnishing of, or the
   performance


   of, or as a result of the use of any of these programs.
                         USING THE COURSEWARE

   1.  Switch on the computer.
   2.  You will be presented with an option to type in the date and
       time.  Press return twice if you do not wish to do so.
   3.  A disclaimer notice will then be displayed.  Please read it
       carefully.
   4.  After striking any key, a menu screen would the come up.
       This is similar to the map in Fig. 1.
   5.  Select your choice by pressing the appropriate function
       keys labelled Fl to F10 on the left side of the keyboard.
   6.  Pressing F10 will return you to the previous menu.


   GETTING HARDCOPIES

   If you would like to get a hardcopy of the plots or the screen,
   just press the keys <SHIFT> and <PrtSc> together.  Make sure the
   graphics printer is turned on!
                       SELF IMPEDANCE OF A DIPOLE

        The self impedance of a dipole antenna depends on its
   length and radius of wire used.  This program will calculate the
   self impedance of a straight wire dipole given its length and
   radius using the approximate induced emf method (refer to Jordan
   and Balmain).  The radiation resistance is referred to the loop
   current.  The resistance referred to the base is R(loop)/sin H.
   Thus for antenna length which are a multiple of half-wavelength, the
   input resistance, R(base), would theoretically be infinite.  Thus we
   need to use a different method.
        For those cases, you are referred to a program called
   MININEC in the book 'MICROCOMPUTER TOOLS FOR COMMUNICATIONS
   ENGINEERING  by Shing Ted Li et al.  It is published by Artech House.
   The program uses the moment method to compute the current
   distributions, impedance and patterns of any antenna composed of
   wires arbitrary oriented in free space or over perfect ground.


   PROGRAM NAME : SELFIMP

   VARIABLE LIST:

   H       : Length of dipole in terms of lambda
   A       : Radius of dipole in terms of lambda
   RIN     : Real part of self-impedance
   XIN     : Imaginary part of self-impedance

   PROCEDURE:

   Choose F2 (WIRE ANTENNAS) from main menu.  Then choose Fl
   (DIPOLE (STRAIGHT WIRE)).  Finally choose F2 (Self-impedance of
   dipole).

   EXPERlMENT



   1.  For a half wavelength dipole with radius 0.0035 lambda, find
   the self impedance.

   2.  Try the same experiment with a smaller radius, say .00014
   lambda.

   3.  For both the antennas above, what is the resonant length of
   each?  What can you conclude?  Which antenna is better for
   broadband use, a thicker or a thinner one?

   4.  What is the self impedance of a monopole of half the height
   of the dipole?
                 MUTUAL IMPEDANCE BETWEEN TWO DlPOLES
                     OF ANY LENGTH AND SEPARATION

        The mutual impedance of two dipoles changes with distance
   of separation between them.  This program allows one to change
   both the distance of separation and length of two identical
   dipoles and computes the mutual impedance.  This is useful for
   finding the driving point impedance of a linear array of
   dipoles.

   PROGRAM NAME : MUTUAL

   VARIABLE LIST:

   H       : Length of dipole in terms of lambda
   D       : Separation between the dipoles in terms of lambda
   R21     : Real part of mutual impedance
   X21     : Imaginary part of mutual dipole

   PROCEDURE:

   Choose F2 (WIRE ANTENNAS) from main menu.  Then choose Fl
   (DIPOLE STRAIGHT WIRE)).  Finally choose F3 (Mutual-impedance of
   2 dipole).

   EXPERIMENT

   1.  Find the mutual impedance between two half wavelength
   dipoles separated by .25, .5 and 1 lambda.

   2.  What happens if the separation is 0 lambda?

   3.  Plot a graph of the mutual resistance and reactance with
   respect to separation for dipoles of half wavelength in a side
   by side configuration.  Do the same for a collinear
   configuration.  Which one gave more reactance?  Why?

   4.  For a side by side configuration, plot the mutual resistance
   and impedance with respect to separation for dipoles of length
   0.4, 0.45 and 0.55 lambda.  What happens to the mutual impedances
   as the length is increased?
                       DRIVING POINT IMPEDANCE



        This program will compute the driving point impedance of an
   array of parallel side-by-side evenly spaced half-wavelength
   dipoles.  It will also calculate the power radiated, directivity
   and efficiency of the array.  Feedline design using quarter
   wavelength line is also included.

   PROGRAM NAME : DRIVPT

   VARIABLE LIST:
   N         : Number of elements
   LAMBDA    : Element spacing
   I(J)      : Excitation currents
   A(J)      : Phase of excitation currents
   ZDR(ROW)  : Real part of driving point impedance
   ZDX(ROW)  : Imaginary part of driving point impedance
   WATT(ROW) : Power radiated by each element
   WATTRAD   : Total power radiated by array
   DIRECTDB  : Directivity in dB
   Z0        : Characteristic impedance of main line
   Z0(I)     : Characteristic impedance of feed-lines
   RIN(I)    : Input impedance of feed-lines
   FREQ      : Working frequency
   ECD       : Efficiency of array

   PROCEDURE :

   Choose F3 (ARRAYS) from main menu.  Then choose Fl (LINEAR
   ARRAY).  Finally choose Fl (Driving-point impedance).


   EXPERIMENT

   1.  Find the driving point impedance of a 2-element array of
   parallel side-by-side lambda-by-two dipoles spaced half
   wavelength apart and fed with currents of equal amplitude and
   zero phase shift between them.

   2.  Try with a phase shift of 90 and 180 degrees.  Which has
   better directivity?

   3.  Change the second current to twice the first with zero phase
   shift.  What happens?

   4.  Design a 3-element array of three half-wavelength dipoles
   separated .65 lambda apart.  The currents are I1=1, I2=2 and
   I3=1.  All have zero phase shift.  The transmitter is rated at
   10 kW at 500 MHz and is to be matched to a 75 ohm coaxial main
   feed line.


   NOTE:  The feedlines of quarter wavelength long are all
   connected at one point.  The quarter wavelength lines can be
   extended by half wavelength lines if they are too short due to
   physical constraint.


               RADIATION PATTERN PLOT OF DIPOLE ANTENNA

       This program will plot the radiation pattern of a dipole of
   any length.

   PROGRAM NAME : DIPOLE

   VARIABLE LIST:

   L         : Length of dipole in lambda

   PROCEDURE:

   Choose F2 (WIRE ANTENNAS) from main menu.  Then choose Fl
   (DIPOLE (STRAIGHT WlRE)).  Finally choose Fl (Pattern of any
   length).


   EXPERIMENT

   1.  For a half-wavelength dipole, plot the radiation pattern.
   What is the HPBW and directivity?

   2.  Repeat 1) with dipoles of wavelengths 0.25, 0.75, 1, 1.5 and
   2 lambda.  When do you get multiple lobes?


   NOTE:  The dipole is oriented vertically in the polar plot.
                          TRANSMISSION LINE

        This program calculates the input impedance of a lossless
   transmission line, given the characteristic impedance, the load
   impedance and its length.  The reflection coefficient and SWR is
   also computed.

   PROGRAM NAME : TXNLINE

   VARIABLE LIST:

   FREQ      : Working frequency
   Z0        : Characteristic impedance
   RL        : Real part of load impedance
   XL        : Imaginary part of load impedance
   L         : Length of line in meters
   REAL      : Real part of input impedance
   IMAG      : Imaginary part of input impedance
   GAMMA     : Magnitude of reflection coefficient
   ANGAMMA   : Angle of reflection coefficient
   S         : SWR

   PROCEDURE :

   Choose Fl (TRANSMISSION LINE PROBLEM) from main menu.  Then
   choose Fl (Input impedance, load , etc.)




   EXPERIMENTS

   1.  For an open circuit line of .2 m at 300 MHz, what is the
   input impedance?  What is the input impedance for a line of .6 m
   at the same frequency?  What about a .25 m line?  Can you plot a
   9raph of the input impedance versus length at 300 MHz?

   2.  Try the same experiment for a short circuit line.

   3.  When are the input impedance of an open circuit and a short
   circuit line the same?

   4.  What does a quarter wavelength do to the load?

   5.  What is the input impedance of a half wavelength line?  Try
   the experiment using an open circuit, a short circuit and with a
   load of 30+j80 ohms at 300 MHz.

   6.  What is the reflection coefficient and SWR of an open and
   short circuit line?  What about a matched load?

   7.  What happens to the reflection coefficient for a resistive
   load which is greater than the characteristic impedance?  What
   about a smaller load?

   8.  Given a transmission line of half a meter, with a load of
   25+j75 ohm, what is the input impedance of the line at 300 MHz?

   9.  What is the reflection coefficient and SWR?

   10.  What happens to the input impedance when the length is
   changed to a quarter meter?
                         SINGLE STUB MATCHING

        This program will compute the length of the short circuit
   stub and its distance from the load needed for matching.  Two
   solutions are given.  The program requires the operating
   frequency, the characteristic impedance and the load as input.

   PROGRAM NAME : STUBMATC

   VARIABLE LIST:

   FREQ     : Working frequency
   Z0       : Characteristic impedance of line
   RL       : Real part of load impedance
   XL       : Imaginary part of load impedance
   Sl,S2    : Stub lengths
   Dl,D2    : Stub distance from load
   B        : Stub reactance

   PROCEDURE:

   Choose Fl (TRANSMISSION LINE PROBLEM) from main menu.  Then


   choose F2 (Single stub matching).


   EXPERIMENT

   1.  A 50 ohm transmission line is connected to a load of
   impedance 25-j75 ohm.  Find the position and length of a short
   circuited stub needed to match the line.

   2.  Using the transmission line program, what is the SWR before
   and after matching?

   3.  Try the experiment with a load impedance of 50 ohm.
   4.  Can you match a load of 100+j100 ohm to a 50 ohm line?
                      LOG PERIODIC DIPOLE ARRAY

        The Log-periodic dipole array (LPDA) is a very broadband
   array.  This program computes the number of elements, lengths
   and spacings for a certain frequency bandwidth determined by the
   desired maximum and minimum frequencies that the LPDA is to
   operate over.

   PROGRAM NAME : LPDA
   VARIABLE LIST:

   FMIN     : Minimum frequency (MHz)
   FMAX     : Maximum frequency (MHz)
   TAU      : Scale factor
   SIGMA    : Spacing factor
   ALPHA    : Vertex angle
   N        : Number of elements
   L(I)     : Length of elements
   X        : Length of array

   PROCEDURE:

   Choose F4 (BROADBAND ANTENNAS) from the main menu.  Then choose
   Fl (Log-periodic dipole array).

   EXPERIMENT

   1.  Design a LPDA to operate from 54-216 MHz.

   For details on the geometry and definition of the parameters
   sigma, tau and alpha, see Antenna Theory and Design by Stutzman
   and Thiele, John Wiley and Sons, 1981, page 287.
                            YAGI-UDA ARRAY

        The Yagi-Uda array is a very directive and high gain array.
   In this program, the three-element Yagi is studied.  The
   reflector and driver is of half-wavelength.  The length of the
   director can be varied by changing its reactance.  The distance
   between the reflector and driver and the director and driver is
   set with the provision of changing the director spacing during
   the program.  This permits the front-back ratio to be determined


   for various setting of director lengths and spacings.

   PROGRAM NAME : YAGI

   VARIABLE LIST:

   SR       : Spacing between driver and reflector
   SD       : Spacing between driver and director
   XZ(3,3)  : Director reactance
   ZR(0)    : Director resistance
   ZDR      : Driving point impedance of YAGI (real part)
   ZDX      : Driving point impedance of YAGI (imaginary part)
   MAGEFTOB : Front/Back ratio
   D        : F/B Directivity
   DBACK    : B/F Directivity

   PROCEDURE:

   Choose F2 (WIRE ANTENNAS) from main menu.  Then choose F3 (Yagi
   Uda antenna).


   EXPERIMENT

   1.  Find the optimum F/B ratio for a three-element Yagi with a
   spacing of 0.1 lambda between the elements.  What is the driving
   point impedance and directivity at that value?  (Tabulate the
   F/B ratio for different director reactance).

   2.  For a fixed length of elements and a distance of 0.1 lambda
   between the reflector and driver, find the distance between
   the director and driver which gives the optimum F/B ratio.  What
   is the driving point impedance and directivity of the array?  (Tabulate the
   F/B ratio for different director spacing).

   3.  When does the reflector functions as a director?

   4.  What is the advantage of using a Yagi array?
                     UNIFORM LINEAR PHASED ARRAY

        Linear array will plot out the array factor for an
   equispaced, isotropic sources excited with equal magnitude of
   current with progressive phase shift.

   PROGRAM NAME: LINPHASE

   VARIABLE LIST:
   ALP  : Progressive phase shift in degrees
   D    : Element spacing in lambda
   N    : Number of elements
   THE0 : Main beam direction


   PROCEDURE:



   From the main menu choose F3 (ARRAYS).  Then choose F2 (ARRAY
   FACTOR) from the next menu.  Finally choose Fl (Uniform linear
   phased array).


   EXPERIMENT

   1.  Plot the array factor of a 2-element array with .5 lambda
   spacing and zero phase shift.  Where is the main beam?

   2.  Now increase the phase shift by 180 degrees.  (The phase
   shift can be incremented or decremented by 10 degrees using the
   up or down arrow cursor keys.  However, you are recommended to
   quit and rerun program if the change in phase shift required is
   large).  Where is the main beam?  Is the directivity the same as
   before?

   3.  Tabulate the HPBW and directivity for an array with 5, 10,
   20, 50 and 100 elements.

   4.  Do the same as above, but this time steering the beam by 45,
   90 and 180 degrees?  Does the HPBW and directivity stay the
   same?  If not, why?

   5.  What is the advantage of increasing the number of elements?
   What is the better trade-off, HPBW or directivity?


   NOTE:  The isotropic elements are placed horizontally in the
   polar plot.
                     LINEAR ARRAY (BEAM STEERING)

        Linear array will plot out the array factor for an
   equispaced, isotropic sources excited with equal magnitude of
   current with progressive phase shift.  The user can specify the
   main beam direction and it will compute the required phase
   shifts required and also plot the array factor.

   PROGRAM NAME: LINSCAN

   VARIABLE LIST:

   ALP   : Progressive phase shift in degrees
   D     : Element spacing in lambda
   N     : Number of elements
   THE0  : Main beam direction


   PROCEDURE:

   From the main menu choose F3 (ARRAYS).  Then choose F2 (ARRAY
   FACTOR) from the next menu.  Finally choose F2 (Linear array
   (beam steering)).




   EXPERlMENT

   1.  plot the array factor of a 5-element array with .5 lambda
   spacing and main beam directed at 0.  What is the phase shift
   required?

   2.  Now steer the beam to ten degree.  What is the required
   phase shift?  ls the directivity the same as before?

   3.  Tabulate the HPBW and directivity for an array with 5, 10,
   20, 50 and 100 elements.

   4.  Do the same as above, but this time steering the beam by 45,
   90 and 180 degrees?  Does the HPBW and directivity stay the
   same?  If not, why?

   5.  What is the advantage of increasing the number of of elements?  What is
   the better trade-off, HPBW or directivity?


   NOTE:  The isotropic elements are placed horizontally in the
   polar plot.
                       PLANAR RECTANGULAR ARRAY

        Given the direction of the main beam required (both theta and
   phi), this program will compute the progressive phase shift for a
   rectangular planar array.  The user can also specify the phase
   shifts, and it will calculate the main beam direction.  It will also
   plot the array factor in both the xz-plane and yz-plane.

   PROGRAM NAME : RECTPLAN
   VARIABLE LIST:
   THE0      :Main beam direction in THETA
   PHI0      :Main beam direction in PHI
   M         :Number  of elements in x-direction
   N         :Number of elements in y-direction
   DX        :Element spacing in x-direction
   DY        :Element spacing in y-direction
   ALPX      :Progressive phase shift in x-direction
   ALPY      :Progressive phase shift in y-direction


   PROCEDURE:

   From the main menu, choose F3 (ARRAYS).  Then choose F2 (ARRAY
   FACTOR) from that menu.  Finally choose F3 (Planar rectangular
   array).


   EXPERIMENT

   1.  Design a 10 x 8 (10 elements in x-direction and 8 elements
   in y-direction) element uniform planar array so that the main
   beam maximum is oriented along  theta=10 and  phi=90.  For a spacing of
   dx=dy= 1/8 between the elements, find the



   a) progressive phase shift between the elements in the x and y
   direction.
   b)  directivity of the array.
   c)  half-power beamwidths (in the perpendicular planes) of the
   array.

   2.  Repeat 1) such that  theta=80 and  phi=90.
     Why does the directivity and half-power beamwidth change?
                        PLANAR CIRCULAR ARRAY

        Given the direction of the main beam required, this program
   will compute the phase excitation for a uniform circular planar
   array.  It will also plot the array factor in both the xz-plane
   and yz-plane.

   PROGRAM NAME : CIRCULAR

   VARIABLE LIST:

   THE0      :Main beam direction in THETA
   PHI0      :Main beam direction in PHI
   N         :Number of elements
   A         :Radius of array
   ALPN      :Phase excitation


   PROCEDURE:

   From the main menu, choose F3 (ARRAYS).  Then choose F2 (ARRAY
   FACTOR) from that menu.  Finally choose F4 (Circular Planar
   array).


   EXPERIMENT

   1.  For a 10 element circular array with main beam in the  theta=0
   and  phi=90, find the phase excitation required.  The radius of the
   array is 1.591 lambda.  Plot the array factor in both the xz and
   yz plane.  Calculate the directivity.

   2.  Using the same number of elements and main beam direction,
   increase the radius to 2,2.5, 5, 10 lambda.  What is the
   directivity?
                 THE WOODWARD-LAWSON SYNTHESIS METHOD

        The Woodward-Lawson method allows one to input a desired
   pattern.  It will then plot the pattern and the current
   distribution.  WOODLS is used to synthesize the line source and
   WOODAF is used in array synthesis.

   PROGRAM NAME : WOODLS and WOODAF

   VARIABLE LIST:
             WOODLS                                WOODAF



   L     : Line source length           NE    : Number of elements
   W(I   : Sampling point               D     : Element spacing
   A(I)  : Desired pattern              A(I)  :Desired pattern
   I(I)  : Current magnitude            I(I)  :Current magnitude
                                        PHI(I):Phase shift

   PROCEDURE:

   Choose F6 (ANTENNA SYNTHESIS) from the main menu.  The choose F3
   (Woodward-Lawson line source) or F4 (Woodward-Lawson linear
   array).
   EXPERIMENT

   USING F3 OPTION

   1.  The desired pattern is unity from w=-0.5 to 0.5 and zero
   elsewhere.  It is to be synthesized with a ten-wavelength line
   source using the Woodward-Lawson method.

   a) Plot the pattern in linear rectangular form.
   b) Plot the current distribution.

   Repeat the synthesis using a) f(theta)=0.5 at w=-0.5 and w=0.5 and b)
   f(theta)=0 at w=-0.5 and w=0.5.

   Which choice is closer to the desired pattern? Can you explain
   why?


   USING F4 OPTION

   2.  The sector pattern above with f(theta)=0.5 at w=0.5 is to be synthesized
   with a 10 element, half-wavelength spaced array.  Determine the element
   position, current excitation and phase.  Plot the synthesized pattern.

   Repeat the above using increasing number of elements (say 15,
   20, 50, 100, etc.).  What is a reasonable number of elements you
   would use to achieve the desired pattern?

   3.  A collinear array of 18 half-wave dipole antennas is to be
   used to synthesize a sector pattern with a main beam sector over
   the region 70 <theta< 110, that is f(theta)=1 over this region and zero
   elsewhere.

   a) For 0.65 lambda spacings determine the input currents
   required for Woodward-Lawson synthesis of the complete pattern.
   Account for the element factor.

   b)  Plot the total array pattern.

   4.  Repeat experiment 3 for a cosecant desired pattern where
   f(theta ) is 1 for 80 <  theta < 90, cos 80/cos(theta)   for 0 <  theta <
   80,
   and zero elsewhere.




                   DOLPH-CHEBYCHEV SYNTHESIS METHOD

        The Dolph-Chebychev method give a compromise between narrow
   beamwidth and low side lobe levels.  This program will generate
   the excitation currents and plot the array factor for a broadside,
   equispaced linear array.

   PROGRAM NAME : CHEBY

   VARIABLE LIST:

   NE       : Number of elements
   D        : Element spacing
   RR       : Side-lobe level (-dB)
   HP       : Half-power beamwidth
   A(N)     : Excitation currents


   PROCEDURE:

   Choose F6 (ANTENNA SYNTHESIS) from the main menu.  Then choose
   F2 (Dolph-Chebychev array).


   EXPERlMENT

   1.  For a five-element, broadside, -20 dB sidelobe, half-
   wavelength spaced Dolph-Chebychev array,

   a)  Obtain the pattern plot
   b)  Verify the sidelobe level and beamwidth from your pattern.

   2.  Design a Dolph-Chebychev broadside array of five, half
   wavelength spaced elements for a -30 dB sidelobes.

   a)  Obtain the current distribution.
   b)  Compute the directivity.

   3.  Design a broadside Dolph-Chebychev array with six, 0.6
   lambda spaced elements for -25 dB sidelobes.

   a)  Obtain the element currents.
   b)  Plot the pattern.
                     TAYLOR LINE SOURCE SYNTHESIS

        The Taylor line source synthesis method allows for narrow
   main beam with the first few sidelobes having nearly equal level
   and decreasing far-out sidelobes.

   PROGRAM NAME : TAYLOR

   VARIABLE LIST :



   NB       : Number of equal side-lobes
   RR       : Side-lobe level (-dB)
   L        : Aperture length
   A(J)     : Sampling currents
   W(J)     : Sampling points
   HPWI     : Half-power beamwidth w.r.t wi
   HP       : Half-power beamwidth

   PROCEDURE:

   Choose F6 (ANTENNA SYNTHESIS) from the main menu.  The choose Fl
   (Taylor line source).
   EXPERIMENT

   1.  Design an eight-wavelength Taylor line source (nbar=7) with
   -30 dB sidelobes.

   a) Obtain and tabulate the sample values and locations.
   b) Plot the pattern in rectangular logarithmic form.
                     UNIFORM RECTANGULAR APERTURE

        Given the width of the aperture in both the x and y
   direction, this program will compute the half-power beamwidths
  
   in the xz and yz-plane.  The directivity is also calculated.  The programs
   the
   plots the radiation patterns in both the principal planes.

   PROGRAM NAME : RECTAPER
   VARIABLE LIST:
   LX           : Width in x-direction in terms of lambda
   LY           : Width in y-direction in terms of lambda
   HPX          : Half-power beamwidth in xz-plane
   HPY          : Half-power beamwidth in yz-plane
   D            : Directivity

   PROCEDURE:

   From the main menu, choose F5 (APERTURE ANTENNAS).  Then choose
   Fl (Uniform rectangular aperture).

   EXPERIMENT

   1.  Find the half-power beamwidths for a uniform rectangular
   aperture which has Lx=20 lambda and Ly=10 lambda.  Plot the
   pattern.  What is its directivity?

   2.  Do the same thing for an aperture with Lx=3 lambda and Ly=2
   lambda.
                              REFERENCES

   1.  Antenna Theory and Design by Warren L. Stutzman and Gary A.
       Thiele
       - John Wiley & Sons, 1981



   2.  Antenna Theory by Constantine A. Balanis
       - Harper & Row, 1982

   3.  Antenna Design using Personal Computers by Pozar
       - Artech House

   4.  Microcomputer Tools for Communication Engineering by
       Shing Ted Li et. al.
       - Artech House, 1983
                           EVALUATION FORM

        Contrary to popular beliefs, this evaluation form will be
   fully scrutinized.  So please fill it with care.  This will not
   only help us to understand your needs, but it will also allow us
   to modify and further improve the courseware.

   IF YOU=STUDENT THEN FILL SECTION A
     ELSE GOTO SECTION B


   SECTION A

   1.  Circle one :  FRESHMAN SOPHOMORE JUNIOR SENIOR
                     MASTERS PRE-CANDIDACY POST-CANDIDACY

   2.  Circle the courses that you have taken :
       Write the grade you obtained beside the courses you circled.

             EE361    EE411    EE432    EE438    EE538
   3.  Circle the courses that you are currently registered :
             EE361    EE411    EE432    EE438    EE538
   4.  Circle the courses you plan to register in future :
             EE361    EE411    EE432    EE438    EE538
        If you had not used this courseware, would you still had
   plan to registered for these courses?

        EE361 Y/N EE411 Y/N EE432 Y/N EE438 Y/N EE538 Y/N
   5.  Would you choose Antenna Engineering as a career? Y/N

   SECTION B
   1.  Circle the programs that you used :
        TXNLINE STUBMATC DIPOLE SELFIMP MUTUAL YAGI
        DRIVPT LINPHASE LINSCAN RECTPLAN CIRCULAR LPDA
        RECTAPER TAYLOR CHEBY WOODLS WOODAF

   2.  On the scale of :  1 - POOR
                          2 - FAIR
                          3 - GOOD
                          4 - VERY GOOD
                          5 - EXCELLENT

        how would you rate each program?  Write your rating beside
   each of the programs below.

        TXNLINE   STUBMATC  DIPOLE    SELFIMP   MUTUAL    YAGI



        DRIVPT    LINPHASE  LINSCAN   RECTPLAN  CIRCULAR  LPDA

        RECTAPER  TAYLOR    CHEBY     WOODLS    WOODAF

   3.  Circle your ratings below:

        a.  Increased understanding of
            Antenna Engineering                 1  2  3  4  5

        b.  Easiness of understanding
            concepts                            1  2  3  4  5

        c.  Visualization of the
            concepts presented                  l  2  3  4  5

        d.  Expectation                         1 2 3 4 5
        e.  Learnt something new                1 2 3 4 5
        f.  Overall performance                 1 2 3 4 5
        g.  Documentation                       1 2 3 4 5
        h.  Ease of use                         1 2 3 4 5
        i.  Value                               1 2 3 4 5

   4.   Would you recommend others to use it? Y/N

   5.  Please write your remarks and comments below









       Thank you.
       8/14/86