LAN-LINK VERSION 1.50  PAGE 1












                     LAN-LINK Version 1.50 (c) 1988 by G3ZCZ


                    (C) Copyright 1988 - All Rights Reserved

                               By Joe Kasser G3ZCZ
                                    POB 3419,
                                 Silver Spring,
                               Md., 20901, U.S.A.
                                 (301) 593 6136

                       USA Packet BBS Routing G3ZCZ @ N4QQ

                 World Packet BBS Routing G3ZCZ @ N4QQ.MD.USA.NA



        LAN-LINK  is  a Personal Packet Terminal Program  for  the  TNC1,
        TNC2,  KPC-2  and  most  of  all  a  smart  multi  mode   digital
        communications controller for the KAM and the PK-232.


                LAN-LINK is written and supported by Joe Kasser, G3ZCZ.

























        LAN-LINK.DOC (c) G3ZCZ 1988





        LAN-LINK VERSION 1.50  PAGE 2


                                TABLE OF CONTENTS

        1.0  INTRODUCTION

             1.1  PROGRAM HIGHLIGHTS

        2.0  Getting Started

             2.1 Upgrading from YAPP.

        3.0  Things You Should Know

        4.0  Function Keys

             4.1- Capture to Disk Toggle
             4.2  Section intentionally blank.
             4.3- Transmit Callsign Sequence
             4.4  Section intentionally blank.
             4.5- Show Packet MHlist.
             4.6  Auto CQ Call.
             4.7- Activate Type Ahead Buffer
             4.8- Disconnect/Receive.
             4.9- Put TNC in CMD mode
             4.10- Put TNC in CONVERSE /Transmit mode /AMTOR FEC

        5.0  Main menu

        6.0 The Call Menu

             6.1 Alert Call
             6.2 Connect/Call
             6.3 Enter Call
             6.4 reMember Path
             6.5 Call CQ
             6.6 Retry
             6.7 Show Directory
             6.8 Target Call
             6.9 aUto CQ
             6.10 Zap BBS

        7.0  Return to DOS

        8.0 Files Menu

             8.1  Send Brag Tape
             8.2  File Directory
             8.3  Erase File
             8.4  Rename File
             8.5  Send File

        9.0 Help Menu






        LAN-LINK.DOC (c) G3ZCZ 1988





        LAN-LINK VERSION 1.50  PAGE 3


        10.0 Log Menu

             10.1 Show last Few Entries
             10.2 Log Entry
             10.3 Print Log
             10.4 Scan Log

        11.0 Message Menu

             11.1 BBS Command Files
             11.2 Current Messages
             11.3 Scan Message
             11.4 Leave Note
             11.5 Old Messages
             11.6 QSP LAN-LINK
             11.7 QRU LAN-LINK
             11.8 Time tag

        12.0 TNC Menu

             12.1 Set TNC Date/Time
             12.2 Flush TNC Buffer
             12.3 Initialize TNC
             12.4 Show Calls Monitored List
             12.5 Show Connect Status
             12.6 Change CQ Text
             12.7 Change Ctext

        13.0 Parameter Menu

             13.1 Turn Beacon Mode On/Off
             13.2 Clear Connect Count
             13.3 Turn Digipeat Detect On/Off
             13.4 Display DeFaults
             13.5 Set Message Count
             13.6 Turn NETROM Drop Out On/Off
             13.7 Turn Printer On/Off
             13.8 Set CQ delay time
             13.9 Turn Relay On/Off
             13.10 Turn Sound On/Off
             13.11 Turn Contest Mode On/Off

        14.0 Q Codes [NC/L]

        15.0 Run DOS Command

        16.0 CommunicationS Modes

             16.1 VHF PACKET
             16.2 HF PACKET
             16.3 ASCII (RTTY)
             16.4 BAUDOT (RTTY)
             16.5 MORSE (CW)
             16.6 AMTOR (STANDBY RECEIVE)
             16.7 AMTOR (ALIST [chirpcopy])


        LAN-LINK.DOC (c) G3ZCZ 1988





        LAN-LINK VERSION 1.50  PAGE 4


             16.8 SIGNAL
             16.9 NAVTEX

        17.0 Terminal Mode Menu

             17.1 Packet Terminal Menu
                  17.1.1 Change Packet Baud Rate
                  17.1.2 CQ/Beacons
                  17.1.3 Everything
                  17.1.4 Read the Mail
                  17.1.5 Just My Station (Solo)
                  17.1.6 All Traffic
                  17.1.7 Multiple User Connects
                  17.1.8 Single User Connects
                  17.1.9 Conference
                  17.1.10 Conference Bridge On/Off

             17.2 AMTOR Terminal Menu

                  17.2.1 Force Break [ACHG]
                  17.2.2 Start Mode B [FEC]
                  17.2.3 Force LETTERS case
                  17.2.4 Read the Mail [ALISTEN]
                  17.2.5 Override ROBOT/Mailbox
                  17.2.6 Standby Receive [ARQ]
                  17.2.7 Set ROBOT/Mailbox
                  17.2.8 CW Identification

             17.3 Baudot Terminal Menu

                  17.3.1 Set Baud Rate
                  17.3.2 Select Shift
                  17.3.3 NAVY MARS Message Protocol
                  17.3.4 USOS Off
                  17.3.5 SELCAL set/reset
                  17.3.6 CW Identification

             17.4 ASCII Terminal Menu

                  17.4.1 Set Baud Rate
                  17.4.2 Select Shift
                  17.4.3 SELCAL set/reset
                  17.4.4 CW Identification

             17.4 CW Terminal Menu

                  17.5.1 Lock to Receive Signal
                  17.5.2 Set Morse Speed
                  17.5.3 Unlock Morse Speed

        18.0 Hot Keys

             18.1 Alt C- Call/Connect to
             18.2 Alt D- Disconnect or Receive
             18.3 Alt L- Edit Log


        LAN-LINK.DOC (c) G3ZCZ 1988





        LAN-LINK VERSION 1.50  PAGE 5


             18.4 Alt M- Message Scan
             18.5 Alt R- Retry Call/Connect
             18.6 Alt X- eXit to DOS
             18.7 Alt Z- ZAP BBS
             18.8  End- > +?  [Over]
             18.9 PgUp- Scrollback (Scrolls back incoming text).
             18.10 The HOME Key
             18.11 The DOWN ARROW key
             18.12 Shift/Baudrate Control keys
             18.13 Control Z (^Z)

        19.0  LAN-LINK disk files

             19.1  LAN-LINK.COM
             19.2  LAN-LINK.SYS
             19.3  LAN-LINK.RUN
             19.4  LAN-LINK.LOG
             19.5  LAN-LINK.DIR
             19.6  CONFIG.SYS
             19.7  *.MBX
             19.8  *.BBS

        20.0 Mailbox features

             20.1 Answering Machine.
             20.2 Mail Beacon (Annunciator).
             20.3 How to leave a message
             20.4 Remote Beacon shutdown.

        APPENDIX 1. BUGS and Anomalies.

             A1.1 Command/Converse mode anomalies.
             A1.2 Buffer messages in AMTOR Beacon CQ mode.
             A1.3 FEC +? responses in AMTOR Beacon CQ mode.
             A1.4 Using a CGA card with a monochrome monitor.
             A1.5 The Packet Conference Mode.
             A1.6 Packet Conference Mode disconnects.
             A1.7 Strange Events.
             A1.8 *** DISCONNECTED.
             A1.9 *** CONNECTED.
             A1.10 Greek Characters on Incoming Screen.
             A1.11 Dumb TNC.

        APPENDIX 2. Local Area Network Capability

             A2.1 LAN Protocol (G3ZCZ Version).
             A2.2 Message Format.
             A2.3 File Uploading/Downloading.
             A2.4 Path Determination to a DX Station.

        APPENDIX 3. NC/L Dictionary.

             A3.1 :QBM:
             A3.2 :QDB:
             A3.3 :QMH:


        LAN-LINK.DOC (c) G3ZCZ 1988





        LAN-LINK VERSION 1.50  PAGE 6


             A3.4 :QSM:
             A3.5 :QSP:
             A3.6 :QRT:
             A3.7 :QRU:
             A3.8 :QNO:
             A3.9 :QJG:
             A3.10 :QRV:
             A3.11 :QSL:
             A3.12 :QTC:
             A3.13 :QYU:
             A3.14 :QYD:

        APPENDIX 4. USING OTHER TNC'S.

             A4.1 TNC2 (MFJ 1270) Version 1.1.2
             A4.2 TNC1 (HD-4040)
             A4.3 Kaypro KPC-2
             A4.4 KAM EPROM Version 2.8.2.
             A4.5 PK-232 EPROM Version 30 AUG 1988

        APPENDIX 5. Registration Form.

        APPENDIX 6. Problem Reporting Form.


































        LAN-LINK.DOC (c) G3ZCZ 1988





        LAN-LINK VERSION 1.50  PAGE 7


        1.0  INTRODUCTION

        LAN-LINK  is a Personal Digital Communications  Terminal  Program
        for a Packet Radio TNC.  The program is designed to optimize  the
        configuration  of  the  TNC in each communications  mode  and  to
        provide some smart terminal features.  It takes advantage of  the
        extra   features  of  the  PK-232  which  is  made  by   Advanced
        Electronics  Applications Inc. It is designed to allow anyone  to
        use and get the most out of their packet TNC as well as from  the
        PK-232 and KAM for Morse, ASCII, BAUDOT, AMTOR as well as  Packet
        Radio communications without having to keep the manual handy.

        LAN-LINK  is  a  sophisticated program.  In its  basic  state  it
        allows  you to use the TNC in an optimal manner.   It  configures
        the TNC for you to maximize the communications efficiency in  the
        communications  mode  of your choice.  That means,  for  example,
        when working Packet on HF you need to program the TNC  parameters
        to different values than you would use on VHF to make maximum use
        of  the  mode.  One significant difference is the length  of  the
        packet itself, for the longer it is, the greater the  probability
        of  QRM  destroying  it.  This program  will  adjust  the  packet
        parameters for you.

        Since  the  computer is now involved, other  features  have  been
        added  to  simplify  operation, and several  features  have  been
        automated.   All these operations are performed using  menus  and
        function keys as documented below.  It will take a while to learn
        how  to  use this program in a manner that suits you,  read  this
        document and have fun, after all, isn't that one of the  purposes
        of Amateur Radio.


            1.1  PROGRAM HIGHLIGHTS

            Function key and Menu driven.

            Automatic logbook entries for Packet and Mailbox/Beacon  mode
            AMTOR  Connects,  semi automatic logbook  entries  for  other
            modes.

            Log  file can be processed by the DBASE  Logbook  Package  of
            PC-HAM  by G3ZCZ for indexed listings, tracking of  DXCC  and
            other AWARDS, etc.

            Contest  operation, sends standard message and  automatically
            increments QSO count.

            Automatic  optimized configuration of the TNC for  each  com-
            munications mode.

            All mode Function key  'OVER' feature (End).






        LAN-LINK.DOC (c) G3ZCZ 1988





        LAN-LINK VERSION 1.50  PAGE 8


            1.1.1     PACKET RADIO

            Automatic capture to disk disk of all packet radio  connects.
            Automatic indication of the number of Packet connects.

            Local   Area   Network  (LAN)  message  store   and   forward
            capability.

            Capable of automatic connect attempts to download a QTC  from
            an other station in the LAN.

            Capable  of  automatic connect attempts to a  packet  BBS  to
            download  your incoming messages, when your callsign  appears
            on the BBS mail beacon annunciator.

            Capable  of  automatically requesting Bulletins  on  subjects
            that interest you from your local packet BBS.

            Digipeat monitoring and capture.

            Alert signal to let you know when a predetermined call  shows
            up in a packet header on frequency.

            Conference mode in multi- connect situations.

            Bridge mode in multi- connect situations.

            Path determination to Dx station via :QMH:.

            Indicator that a specific station designated as the  'target'
            call   connected   in  Packet  mode,  or  linked   to   AMTOR
            Beacon/Mailbox while you were away.

            Automatic  NET/ROM and KA Node path set up from  LAN-LINK.DIR
            call/path directory file.

            Selective  answering machine and MAILBOX using  NC/L  command
            dialog.

            Screen  indication  of  connect by  desired  station  (target
            call).

            Automatic Beacon Mode CQ caller.

            Will  call  CQ repetitively and either work the  connect  and
            keep  going  after disconnect or signal you when a  reply  is
            received.

            1.1.2     AMTOR

            Automatic  CQ caller.  Will call CQ repetitively  and  signal
            you when a reply is received.

            Local   Area   Network  (LAN)  message  store   and   forward
            capability.


        LAN-LINK.DOC (c) G3ZCZ 1988





        LAN-LINK VERSION 1.50  PAGE 9



            Selective  answering machine and MAILBOX using  NC/L  command
            dialog.

            Function  key  change from monitoring FEC CQ's  to  QSO's  in
            progress (chirpcopy).

            Automatic Beacon Mode CQ caller.

            1.1.3     MORSE/BAUDOT/ASCII

            Automatic  CQ caller.  Will call CQ repetitively  and  signal
            you when a reply is received.

            RTTY SELCAL.

        2.0  Getting Started

        MAKE  A  BACK UP COPY OF THIS DISK, BEFORE YOU REMOVE  THE  WRITE
        PROTECT TAB.

        If  you don't have a PK232 then rename the LAN-LINK.SYS  file  to
        PK232.SYS  and  rename your TNC.SYS file  as  LAN-LINK.SYS.   For
        example,  if  you  are  using  a  TNC2,  perform  the   following
        operations in DOS.

        RENAME LAN-LINK.SYS PK232.SYS
        RENAME TNC2.SYS LANLINK.SYS

        Edit the LAN-LINK.SYS file replacing G8BTB with your callsign and
        Selcal information.  If your TNC does not support AMTOR you still
        need a dummy entry in that line.

        For details of the rest of the customization possibilities in the
        'LAN-LIN.SYS' file, read Section 19.2.

             2.1 Upgrading from YAPP

             LAN-LINK uses the PK232 in a different configuration to  the
             way  that YAPP does. In particular, LAN-LINK  uses  software
             flow control.

             To  facilitate conversion from YAPP to LAN-LINK  a  YAPP.CNF
             file   is   provided  in  this  package.   YAPP.CNF   is   a
             configuration  file for YAPP Version 2 that  will  configure
             the PK232 for YAPP and then back to LAN-LINK.

             If you are currently using YAPP, replace your YAPP.CNF  file
             with this one and load YAPP.  Then terminate the program  in
             the  normal manner by using the Alt-X key.  You should  then
             be able to load and run LAN-LINK without any problems.  Each
             time  you sub-sequently want to run YAPP, YAPP will  set  up
             the  PK232, execute and then reconfigure the PK232 back  for
             LAN-LINK.



        LAN-LINK.DOC (c) G3ZCZ 1988





        LAN-LINK VERSION 1.50  PAGE 10


             If you are using a YAPP.DIR file, rename it to LAN-LINK.DIR.

        3.0  Things You Should Know

        Any  Terminal  Node  Controller  (TNC)  is  a  complex  piece  of
        equipment.   It can operate in a Command Mode, in which you  tell
        it to do something, or in a Converse Mode in which you are  using
        it  to talk to other stations.  Many people confuse the two  when
        first  getting on Packet.  If you monitor the channels  you  will
        recognize command mode TNC instructions on the air, and when  you
        use  the  TNC you will receive the "error" reply  when  you  type
        something  thinking  that you are in the Converse  Mode  but  are
        really in the Command Mode.  LAN-LINK is designed to make  Packet
        operation  simple  using Menus and high level (Function  and  Hot
        key) commands.

        Morse,  ASCII, BAUDOT communication modes are HALF  DUPLEX.   One
        station  is transmitting at any time.  You thus have to  use  the
        Transmit/Converse  and Receive/Disconnect function keys  to  turn
        the transmitter on and off respectively.

        AMTOR is also HALF DUPLEX but has some of the attributes of  full
        duplex.   In  this  mode  you  control  who  is  talking  through
        software,  only one station can send data at a time, but you  can
        type  characters  in to the buffer and they will  be  transmitted
        automatically  when the other station turns the QSO over to  you.
        Once   you  have  linked  with  someone,  you  do  not  use   the
        Receive/Disconnect function UNTIL THE QSO IS OVER.  Both stations
        are  communicating automatically thanks to the TNC.  If you  want
        the  other operator to respond type the +? key sequence  (or  use
        the 'END' key).

        Packet  Radio communications  on the other hand is a full  duplex
        mode  of communications.  Once you have connected  with  someone,
        you  do not use the Receive/Disconnect function UNTIL THE QSO  IS
        OVER.   Both stations are communicating automatically  thanks  to
        the  TNC.  If you want the other operator to respond type  the  >
        key followed by the 'Enter' key, better yet, use the 'end' key.

        Note  that  Morse,  AMTOR, ASCII and BAUDOT  are  character  mode
        communications  in  that each character you type is sent  as  you
        type them.  In Packet Communications, the TNC stores them up  and
        sends out a burst or packet when you type the 'Enter' key or  you
        type  enough characters to fill up a packet.  Studies have  shown
        that the human attention span when sitting at the keyboard is  of
        the  order  of 2 seconds. If you are in a  keyboard  to  keyboard
        packet  radio connect, remember this and don't forget to use  the
        'Enter'  frequently,  especially before you stop to  think  about
        what to send next.

        LAN-LINK  has  the following functions built in to it in  a  menu
        driven format.

        Morse Code  20 wpm (10 wpm for the KAM).



        LAN-LINK.DOC (c) G3ZCZ 1988





        LAN-LINK VERSION 1.50  PAGE 11


        BAUDOT  with default of 45 WPM narrow shift (LSB).  You  may  set
        other  baud rates directly, or use the left and right arrow  keys
        to change the baud rate (see below).

        ASCII  with  default 110 BAUDS narrow shift (LSB).  You  may  set
        other  baud rates directly, or use the left and right arrow  keys
        to change the baud rate (see below).

        Packet VHF or HF baud rates and shifts (LSB).

        AMTOR 100 BAUDS narrow shift (LSB).

        All communications between the computer and the TNC normally  use
        the  8  BIT  NO  PARITY  and  1  stop  bit  RS-232  Serial   Port
        configuration. You CAN THUS SEND FOREIGN LANGUAGE CHARACTERS FROM
        THE KEYBOARD OR FILES.  If you want to limit the character set to
        the  7  bit ASCII set, set the TNC parameters  accordingly.   The
        baud rate defaults to 1200, but you may set it to 2400, 4800 9600
        or even 19200 if your CPU clock is fast enough.

        Access  to  the  TNC Command mode is provided in  case  the  user
        wishes to override any of these defaults.

        IF YOU USE THIS PROGRAM, YOU STILL MUST READ THE TNC MANUAL.

        Note   that   AMTOR  and  PACKET  are  full   duplex   modes   of
        communications.  When you connect with someone, there is no  need
        to use the transmit and receive function keys.  In fact you  will
        have  problems  if you do.  Do not disconnect or break  the  link
        until the QSO is over.

        WARNING  ....   THIS PROGRAM OPERATES IN AN OPEN LOOP  MODE.   IT
        REMEMBERS WHAT INSTRUCTIONS OR COMMANDS IT GAVE THE TNC.  IF  FOR
        SOME REASON, THE TNC IS NOT SYNCHRONIZED TO THE PROGRAM YOU  WILL
        NOT GET CORRECT DISPLAYS ON THE SCREEN.

        4.0  Function Keys

        Function  keys  are  used to perform  operations  common  to  all
        communications modes, or to allow fast performance of a  function
        without  having  to  go through several  layers  of  menus.   The
        function keys listed below are active.

             1- Capture to Disk Toggle.
             3- Transmit Callsign Sequence.
             5- Show Packet 'MH'list.
             6- Auto CQ Call.
             7- Activate Type Ahead Buffer.
             8- Disconnect or Receive.
             9- Put TNC in CMD mode.
             10- Put TNC in CONVERSE /Transmit mode /AMTOR FEC.
             End- > +?  [Over].
             PgUp- Scrollback (Scrolls back incoming text).
             ESC- Activates the Main Menu.



        LAN-LINK.DOC (c) G3ZCZ 1988





        LAN-LINK VERSION 1.50  PAGE 12


        The  action  of  each of the function keys is  described  in  the
        following sections.

             4.1- Capture to Disk Toggle

             This  key toggles the "capture to disk" command.   When  the
             "capture  to disk" is active, all incoming  text  (including
             'Echo as sent' outgoing text) is stored on a disk (floppy or
             hard)  in a file called 'LAN-LINK.RUN'.  If this  file  does
             not  exist  the first time that LAN-LINK is  loaded,  it  is
             created.   From that time on, successive activations  append
             new data to the contents of the file.

             Each time the command is activated a datestamp (or  timetag)
             will be written to the file.

             When  a  Packet station connects "capture to disk"  will  be
             activated  automatically.   Packet  connects  will  thus  be
             recorded in their entirety automatically unless you turn off
             the "Capture to disk" during the course of the QSO. "Capture
             to disk" will be stopped at disconnect time unless you  have
             commanded it on manually.

             You  may later edit the file at your convenience  with  your
             favorite word processor.

             LAN-LINK will automatically close the "capture to disk" file
             when you terminate the program and return to DOS.

             4.2  Section intentionally blank.

             4.3- Transmit Callsign Sequence

             This command lets you transmit the following sequence <other
             call) DE <your call>.  For example if you are 4X6AA and  you
             are  working  G3ZCZ  then this command  would  transmit  the
             sequence  G3ZCZ  de 4X6AA.  You use this at the start  of  a
             transmission in any mode except Packet.

             4.4  Section intentionally blank.

             4.5- Show Packet 'MH'list

             This  command  lets  you see what calls the  TNC  has  heard
             recently on the Packet channels.  You can see up to 18, with
             the  data and time they were last logged by the TNC.   Refer
             to the 'MH' command in the TNC manual for the particulars of
             the display.

             The  MH list shows up in a special window and freezes  until
             you depress any key.  While the list is frozen, LAN-LINK  is
             not monitoring received data, so don't freeze it too long.

             If  the MH list is blank, or information comes in  from  the
             TNC  between the time you entered the command and  the  time


        LAN-LINK.DOC (c) G3ZCZ 1988





        LAN-LINK VERSION 1.50  PAGE 13


             the  list is sent back,  subsequent text from the  TNC  will
             show up in the MH window until the next 'Cmd:' appears or 18
             lines of text have been received.

             This command does not work on the TNC1.

             4.6  Auto CQ Call.

             This command will send a CQ sequence, wait about a minute or
             so  and then repeat the CQ sequence every minute or so until
             it receives your call back from someone else.  When it  does
             so, it will alert you with a Connect Alarm signal and  reset
             to the normal or listening mode.

             When   the  Automatic  CQ  sequence  is  in  operation,   an
             indication  will  be  shown  in  the  status  window.    The
             indicator  will be steady while the transmitter  is  sending
             the CQ text, and will blink while the receiver is  listening
             for a reply.

             The time delay between calls is set using 'Q' command in the
             Parameters Menu (Set CQ delay time).

             The  automatic  CQ  command will only work in  the  TNC  non
             Packet  modes if the 'Echo as Sent' mode is set to 'ON'  per
             the LAN-LINK.SYS file.  In other words, you must be able  to
             see  the CQ text slowly echo in the incoming window for  the
             command to work.  The reason for this is that the "K K K"  (
             or  "+?" in AMTOR) sequence is used to arm the  software  to
             look for a reply

             In  AMTOR  you  will get the connect  alarm  only  when  the
             replying station transmits the '+?' character combination.

             The check for the detection of your callsign and the connect
             alarm  sequence only occur after a line feed character  have
             been received.

             Under  most conditions in AMTOR, many in RTTY, and  some  in
             MORSE,  LAN-LINK will recognize the callsign of the  station
             answering  your CQ and display it in the status window.   In
             the  event  that it fails completely, the  sequence  '--?--'
             will  show up in the status window.  Since  the  recognition
             algorithm use just look for the first word following the 'DE
             space'  sequence  and assumes that it has the  callsign,  be
             careful  to  check it when operating under  QRM  conditions.
             You can override the automatic call selection with the Enter
             Callsign command in the Call Menu.

             The automatic CQ sequence is canceled when an incoming  call
             is detected (only if the beacon or robot/mailbox mode is not
             selected), if you push the disconnect command key, or if you
             change communications modes.




        LAN-LINK.DOC (c) G3ZCZ 1988





        LAN-LINK VERSION 1.50  PAGE 14


             4.7- Activate Type Ahead Buffer

             The use of this key sets LAN-LINK to the "Type Ahead"  mode.
             Any  characters  then typed at the keyboard will  be  placed
             into  the TNC transmit buffer.  The contents of  the  buffer
             will  be transmitted over the air when the transmit  command
             is invoked [FK10].

             This  feature  allows you to 'type-ahead' as you  can  enter
             text  into the transmit buffer while viewing incoming  words
             in  the  INPUT window in the screen.  Any  characters  typed
             from  the keyboard will be echoed in the OUTGOING window  on
             the screen.

             THIS  command  IS NOT ACTIVE IN THE AMTOR or  PACKET  modes.
             Packet  is full duplex, while in AMTOR the TNC  buffers  the
             data until you receive the next +? sequence.

             4.8- Disconnect, Disengage or Receive

             This  command  key  returns  the  station  to  the   receive
             communications  (TNC command) mode.  It may also be used  to
             abort  the automatic CQ sequence.  If you use it to abort  a
             CQ  sequence while the transmission is in progress, you  may
             also  want  to flush the PK-232  transmit buffer  the  Flush
             command in the TNC Menu.

             In a multi connect situation the program will prompt you  to
             tell it which IO channel to disconnect.

             In  AMTOR  this  command key toggles  LAN-LINK  between  the
             Chirpcopy  mode  (listening  to  a  QSO  in  progress)   and
             monitoring FEC transmissions (CQ calls).

             In MORSE this key also disengages the receive speed lock  in
             the PK-232 to unlock the PK-232 from the last signal copied.
             It lets you lock onto another signal faster.

             4.9- Put TNC in CMD mode

             This  command puts the TNC into the command mode.   At  this
             time, the program is transparent and acts as a dumb terminal
             (except  for  placing  incoming and  outgoing  text  in  the
             relevant windows).  you use this mode for overriding any  of
             the TNC default conditions.  (SEE I TOLD YOU THAT YOU HAD TO
             READ THE TNC MANUAL).

             4.10- Put TNC in CONVERSE /Transmit mode /AMTOR FEC

             This  command places the TNC into the transmit  or  converse
             mode.  The transmitter is turned on and the contents of  the
             transmit   buffer  are  transmitted.   In  the  non   packet
             communications modes, the outgoing characters will be echoed
             back  from the TNC and displayed in the INCOMING  window  on
             the CRT as they are transmitted on the air.


        LAN-LINK.DOC (c) G3ZCZ 1988





        LAN-LINK VERSION 1.50  PAGE 15



             In the AMTOR modes this key puts the TNC in the FEC mode and
             turns the transmitter on.

        5.0  Main menu

        When  you  touch the ESCape key, the Main Menu  appears  on  your
        screen  and provides a number choices which are described in  the
        following sections.

        C Call Menu
        D Return to DOS
        F Files Menu
        H Help Menu
        L Log Menu
        M Message Menu
        N TNC Menu
        P Parameter Menu
        Q Q Codes [NC/L]
        R Run DOS Command
        S communicationS Mode Menu
        T Terminal Mode Menu
        X eXit LAN-LINK

        Type in the single letter to make your choice.

        6.0 The Call Menu

        The Call Menu provides the following choices.

        A Alert Call
        C Connect/Call
        E Enter Call
        M reMember Path
        Q Call CQ
        R Retry
        S Show Directory
        T Target Call
        U aUto CQ
        Z Zap BBS

        Type in the single letter to make your choice.

             6.1 Alert Call

             The Alert call feature is used in the Packet  communications
             mode  when disconnected and the terminal set for  'TRFC'  or
             'CQ/BEACON'.  LAN-LINK will scan the packet headers received
             from  the  TNC, and, when it sees a  packet  originated  (or
             digipeated if the MRPT parameter in the TNC is set to 'ON'),
             by  the station whose call you have entered as  the  'Alert'
             call,  it  will sound an alarm at the  console.    The  line
             containing the packet header will also be displayed in light
             green.



        LAN-LINK.DOC (c) G3ZCZ 1988





        LAN-LINK VERSION 1.50  PAGE 16


             This  option toggles the Alert call feature on and off.   If
             it  is  off, you are prompted for the call to  be  monitored
             for, if it is on, it is turned off.  The toggle is set  when
             you  enter  a  callsign, and cleared when  you  depress  the
             'Enter' key instead of a callsign.

             The  Alert call will be shown flashing in the status  window
             when in the disconnected state.

             NOTE: If the terminal is set for 'CQ/BEACON' the Alert  will
             only  sound if the specified station transmits CQ or  BEACON
             packets.

             6.2 Connect/Call

             This  option  works in almost the same manner  in  both  the
             Packet  and Non Packet communications modes as described  in
             the following sections.

             6.2.1 Non Packet Modes

             You  use  this option to call a station heard on  the  band.
             You may also use it to call 'QRZ' or even 'TEST'.

             In  AMTOR the link request will be sent in the ARQ  mode  to
             the SELCAL of the desired station.

             6.2.2 Packet Mode

             You use this option to attempt a connect with another packet
             station.   In  a multi connect situation  the  LAN-LINK will
             automatically select a free IO channel to try the connect.

             6.2.2.1 Names, Handles and Paths

             If  you so desire, you can create a directory file  (default
             name  is  LAN-LINK.DIR)  and  keep  a  list  of  names   and
             callsigns.   The computer will look up a name and  call  the
             station by its callsign.  For example if you put

                       Joe G3ZCZ

             as a line in the file, when you tell the computer to connect
             to Joe, it will try to connect to G3ZCZ.  If you enter

                       4X4HF 4X4HF V 4X1AA, 4Z4ZB, 4X4IL

             you only need to type '4X4HF' to set up the correct  connect
             path.

             6.2.2.2 NET/ROM and The Link.

             You  can  use  this  feature  to  automate  a  NET/ROM  path
             connection.  In the manual NET/ROM path setting up mode, you
             would  first connect to your local node, then when  you  are


        LAN-LINK.DOC (c) G3ZCZ 1988





        LAN-LINK VERSION 1.50  PAGE 17


             connected  with  it,  connect to the next node,  and  so  on
             through any intermediate nodes within the whole path  before
             you finally connect with your destination station.  You  may
             have digipeaters in any of the paths.

             For example if you wish to connect to K1HTV who is in  range
             of  the SSCT node, and you are in Washington DC,  you  might
             first have to connect to your local NET/ROM node (ELK) via a
             digipeater, then each of the intermediate nodes, SNJ3,  NNJ,
             WMA before you could try to connect with K1HTV.

             Consider the manual sequence to make the connection.   K1HTV
             is  the station the contact is being attempted with, and  he
             is  located  within  range of the SCCT  NET/ROM  node.   The
             station attempting the connect is located in the  Washington
             DC area one digipeat away from the ELK NET/ROM node.

             The  connection to the local node is performed  first.   the
             operator has to type ' C ELK v WB4APR-5' to make that  link.
             When  the  connect with the node is achieved,  the  operator
             must  type 'C SNJ3' to connect to the next node.  Each  time
             the  connection  is  made, the operator  must  type  in  the
             command to make the next one, until finally the last node is
             reached and a connect request can be made to the destination
             station  (either  direct or via  a  digipeater).   Sometimes
             there may be an intermediate non NET/ROM connection  between
             two stations somewhere in the path.

             This procedure is tedious and time consuming, because it may
             take  several  seconds to complete each stage of  the  link.
             LAN-LINK automates this sequence by scanning the line in the
             LAN-LINK.DIR  file associated with the callsign entered  and
             transmitting each section of the line when it recognizes the
             'Connected  to ' reply from each NET/ROM node in  the  path.
             When it finally gets to the destination it sounds a chime to
             alert you that the connect has been achieved.

             The LAN-LINK.DIR file entry for this path is as follows.

             K1HTV ELK v WB4APR-5! SNJ3! NNJ! WMA! SCCT! K1HTV

             where the '!' separates each stage of the link.

             The key word is K1HTV.  LAN-LINK then scans the line to  see
             if  there is a '!' in it.  If there is it knows that  it  is
             dealing  with  a  NET/ROM path.  It then tells  the  TNC  to
             attempt a connect with the characters following the key word
             up  to  the  first '!'.  In this case it tells  the  TNC  to
             connect  to  ELK via WB4APR-5. When the TNC sends  back  the
             connected message, LAN-LINK tells the TNC to try to  connect
             to  the next node in the path, namely in this example  SNJ3.
             The sequence continues each time a connection is made  until
             the link is complete.

             To set up a directory entry just use the format shown above.


        LAN-LINK.DOC (c) G3ZCZ 1988





        LAN-LINK VERSION 1.50  PAGE 18


             Place  a '!' sign after the uplink path and  different  node
             segments. Do not place one after the downlink path.

             Depending  on  the  configuration,  LAN-LINK  will  issue  a
             'disconnect' command to the TNC in the event the NET/ROM  or
             KA-Node connect attempt fails.  This feature is designed for
             known paths not for general path determination.

             6.2.2.3 KA-Nodes

             You  can  connect  or crossconnect via  KA-Nodes  using  the
             directory file.  You must still use the ! separators as well
             as two new symbols %  and &.  Use % for 'C' and & for 'X' in
             KA-Node links..

             For  example,  given that a path to W9TNN-2 is  first  to  a
             local  KA node [JRW] then to a second node on the  same  vhf
             frequency  [W3EAX-7]  and lastly via a cross connect  on  40
             Meters  to W9TNN2-, the line in the LAN-LINK.DIR file  would
             be as follows.

             w9tnn-2  jrw !% w3eax-7 !& w9tnn-2

             You should be able to mix NET/ROM and KA-Node paths as in

             n7dva      ! w3eax-7 !& ww7zz !& w7zzz !% n7dva v nn7nn

             The different symbols are used for the KA node to tell  LAN-
             LINK which replies to look for as well as what to prefix the
             call with.

             Depending  on  the  configuration,  LAN-LINK  will  issue  a
             'disconnect' command to the TNC in the event the NET/ROM  or
             KA-Node connect attempt fails.  This feature is designed for
             known paths not for general path determination.

             6.2.2.4 Loop Backs

             In the Packet communications mode, if you want to loop  back
             through someone else enter the '/' character followed by the
             call  of  the station you want to loop  back  through.   For
             example if I (G3ZCZ) want to loop back through 4X6AA, I just
             need  to  enter  /4X6AA as the call to connect  to  and  the
             LAN-LINK  will tell the TNC to try to connect to  G3ZCZ  via
             4X6AA,  namely  issue the command 'C G3ZCZ V 4X6AA'  to  the
             TNC.

             6.3 Enter Call

             This  option lets you enter the call of any station  calling
             you into the program. If you type the enter key in  response
             to the prompt, you can later use the F3 (function key 3)  to
             transmit the sequence "de <yourcall>". You may also use  the
             Retry feature to call that station in the non AMTOR modes.



        LAN-LINK.DOC (c) G3ZCZ 1988





        LAN-LINK VERSION 1.50  PAGE 19


             In  AMTOR,  you use the feature to enter  the  callsign  and
             SELCAL  of the station you are listening to and may want  to
             call.

             6.4 reMember Path

             You may use this option to put an entry in the  LAN-LINK.SYS
             file.

             6.5 Call CQ

             You  use  this  command  key to  call  CQ.   In  the  Packet
             Communications  mode, the TNC will transmit a line  of  text
             along with the CQ packet.  The line of text is set up in the
             LAN-LINK.SYS file described in section 19.

             In  the  AMTOR  communications mode,  your  SELCAL  will  be
             transmitted along with the CQ call in the FEC mode.

             6.6 Retry

             This  option  allows you to retry a connect  that  for  some
             reason did not go through the first time.  It save wear  and
             tear  on  your fingers particularly if the  desired  connect
             path is via a number of digipeat relays or through a  number
             of NET/ROM NODES.

             In the non packet modes, it allows you to retransmit a  call
             to another station without having to re-enter the call.

             If you have previously used Enter feature to put a  callsign
             in the program when you hear that station, you can then  use
             the Retry command to call him later when the QSO in progress
             terminates.

             6.7 Show Call Directory

             This  option displays the contents of the LAN-LINK.SYS  call
             directory file.

             6.8 Target Call

             The Target call feature is used in the Packet communications
             mode when disconnected. LAN-LINK  will monitor the  stations
             connecting  to  you. When it sees a connect by  the  station
             which you have entered as the 'Target' call, it will set the
             flashing Connect Count display to show a 'happy face'.

             This option toggles the Target call feature on and off.   If
             it is off, you are prompted for the call to be monitored, if
             it  is  on, it is turned off.  The toggle is  set  when  you
             enter  a callsign, and cleared when you depress the  'Enter'
             key instead of a callsign.

             The Target call will be shown flashing in the status  window


        LAN-LINK.DOC (c) G3ZCZ 1988





        LAN-LINK VERSION 1.50  PAGE 20


             when in the disconnected state.

             6.9 aUto CQ

             This option is the same as function key 6.

             6.10 Zap BBS

             This  key  initiates  a  BBS  mail  download  sequence.   It
             initiates the same sequence as the BBS_Mail_Snatch.  You use
             this key if you connect to a BBS before you hear its beacon,
             or  if you have disabled the BBS_Mail_Snatch feature.   This
             key  must be used ONLY when connected to the BBS and  BEFORE
             the first '>' is received.  Note: it is that first '>'  that
             triggers  the sequence.  If you have already  received  that
             first '>', send the BBS any command, and the sequence should
             begin when the BBS signals that it has completed  processing
             that command.

             The sequence performed by the BBS_Mail_Snatch is as follows:

             RM        To read your messages, (Configurable)
             L         To let you know what is new on the BBS,
             LM        To list ALL your messages on the BBS,
             B         To log you off the BBS.

             LAN-LINK will wait for the '>' as the last character of  the
             line of text being received from the BBS, before issuing the
             next command in the sequence.  Your messages will be  placed
             in a message file <yourcall.OUT> as if someone else had left
             a message for you.

             When  you use this command you will be asked if you want  to
             Upload  or download. If you want to download, just push  the
             'Enter'  key.   A Download (Mail from the BBS to  you)  will
             automatically  be  followed by an Upload if the  *.BBS  file
             exists.

             The 'RM' may be customized in the LAN-LINK.SYS file to  'RN'
             or 'VM' depending on the software in your local BBS and your
             preference as shown in section 19.

             During  the  time  that the BBS is  responding  to  the  'L'
             command  with a list of new messages, LAN-LINK  is  scanning
             the  messages to see if it finds one containing a Scan  Word
             (See  Section  19).  If it does it will queue a  request  to
             download that message.

        7.0  Return to DOS

        When  you exit the program, the TNC is put into the  VHF  default
        mode  in which it rejects calls from any other  stations.   (Read
        about  the 'CFROM' command in the TNC manual).  you can  thus  if
        you  wish leave it powered, and if you also leave the  VHF  radio
        powered  up, you will be active as a digipeater, but at the  same


        LAN-LINK.DOC (c) G3ZCZ 1988





        LAN-LINK VERSION 1.50  PAGE 21


        time  anyone  trying  to connect with you  will  receive  a  busy
        signal.   The MBX command (Reading the Mail) is also  cleared  at
        this time.

        You may customize the TNC state at shut down as shown in  section
        19.

        8.0 Files Menu

        The Files Menu provides the following choices.

        B Send Brag Tape
        D File Directory
        E Erase File
        R Rename File
        S Send File

        Type in the single letter to make your choice.

        During  the file transfer, the outgoing text will appear  in  the
        OUTwindow.  If the text is long enough and fills the TNC  buffer,
        you will see it stop, and then continue when the TNC is ready  to
        accept  more text, the message sequence will resume.   NOTE  that
        ^S/^Q software flow control is used.

        When you transmit a file (B or S) you are returned to the receive
        mode  after the file is sent except in the Packet  communications
        mode.  In the Packet Communications mode, when the file has  been
        loaded into the TNC the computer will add the ^Z character to the
        outgoing   text  to  signal  to  the  recipient  that  the   file
        transmission is over.

        The computer will signal you (using the bell character, when  the
        file has been loaded into the TNC,  Note that is not the same  as
        the  time that the TNC has transmitted the file, because the  TNC
        incorporates a character buffer.

             8.1  Send Brag Tape

             This  command  allows you to transmit a standard  text  file
             historically  known as a "Brag Tape".  The default  name  of
             the brag tape file is LAN-LINK.TXT, and it should be created
             with a word processor in the non-document mode.

             8.2  File Directory

             This command shows you the directory of the disk drive.

             8.3  Erase File

             This command allows you to erase or delete a file.

             8.4  Rename File

             This  command  allows you to rename a file.  You  could  for


        LAN-LINK.DOC (c) G3ZCZ 1988





        LAN-LINK VERSION 1.50  PAGE 22


             example  rename a document file to a "callsign.OUT" file  so
             that  someone will receive it automatically next  time  they
             connect.

             8.5  Send File

             This  command allows you to transmit an ASCII file  via  the
             PK-232.

        9.0 Help Menu

        This option will activate the HELP display. Help displays a brief
        summary of the function and hot keys.  This window will remain on
        display until a character is typed at the keyboard.

        10.0 Log Menu

        The Log Menu provides the following choices.

         F Show last Few Entries
         L Log Entry
         P Print Log
         S Scan Log

        Type in the single letter to make your choice.

             10.1 Show last Few Entries

             This  command displays the last few log entries made  during
             the  active  session. If no QSO's have been made  since  the
             program was loaded the display window will be blank.  Up  to
             5 log entries will be displayed in the window.  You use this
             command for a quick look at which stations have connected to
             you most recently in your absence.

             10.2 Log Entry

             LAN-LINK  performs automatic logbook entries for Packet  and
             AMTOR  Beacon  mode  Connects, and  semi  automatic  logbook
             entries for other modes.  The Log file is compatible to that
             of  the CONTEST program in the G3ZCZ PC-HAM package and  can
             be  processed  by  the DBASE  Logbook  Package  for  indexed
             listings,  tracking of DXCC and other AWARDS, etc.  This  is
             ideal  for special event stations and DX-peditions, for  the
             whole QSL process and further statistical analyses of  their
             operation has.

             For  this  feature to work, the file  LAN-LINK.LOG  must  be
             present  on the disk.  If it isn't, it will be  created  for
             you. After one logging operation has occurred, edit out  the
             initial  text.   You  must perform  this  editing  operation
             before  appending  the contents of the logbook file  to  the
             logbook  database of the PC-HAM LOGBOOK Package.   Edit  the
             log  before appending it to the DBASE package, as there  may
             be some null characters at the end of the file which may  be


        LAN-LINK.DOC (c) G3ZCZ 1988





        LAN-LINK VERSION 1.50  PAGE 23


             recognized as a blank entry by DBASE.

             It  is  also advisable not to let the logbook file  get  too
             big.

             When  an  AMTOR beacon mode or packet  connect  occurs,  the
             connect  is automatically logged.  In the Packet  mode,  the
             connect  path  is  placed in the  comments  section  of  the
             logbook entry.  In the non packet modes, the log data  entry
             is  set up for you with default 599 values for  the  reports
             exchanged.

             You invoke this option to enter the data into the log or set
             the  band and power for subsequent automatic logging.   When
             you invoke the command you will be presented with a  typical
             menu in the menu window and a current entry line in the  log
             window.

             You  should choose the character associated with each  item.
             For  example,  if  you want to change the  Band,  enter  the
             letter  'B', to change the Comments, enter the  letter  'O'.
             Enter  the text when prompted.  You will then  be  presented
             with an updated entry.

             To  enter  the data into the logbook, use the 'L'  key.   To
             save  the  data  but  not  make a  log  entry  use  the  '*'
             character,  for  example you would do that if  you  want  to
             change the band or power information.

             You  may use the 'qSl sent' entry to tag the fact  that  you
             have written out a QSL card.

             The  band and power information are set up from the  default
             values stored in the configuration file LAN-LINK.SYS.   They
             are  displayed in the status window.  If you are  using  the
             logging  command,  you  should  change  them  when  changing
             bands/powers  and  exit  the logging command  with  the  '*'
             character  so  that  you don't put a blank  entry  into  the
             logbook.

             Note that you can also use this command to enter the odd SSB
             contact  into  the  logbook  file.   If  you  do,  use   the
             characters  'SSB'  or 'FM' for those voice modes  to  remain
             compatible with the rest of the DBASE logbook package.

             NOTE   Do  not use the comma character ',' in  the  comments
             field.   If you examine the logbook file you will  see  that
             all  items  are separated by comma's.  If you  use  a  comma
             character in the comments you will screw up the transfer  of
             data into the logbook package.

             The comments field in the logbook is restricted to a maximum
             of  10 characters.  If you try and enter more than  10,  the
             surplus will be ignored.



        LAN-LINK.DOC (c) G3ZCZ 1988





        LAN-LINK VERSION 1.50  PAGE 24


             10.3 Print Log

             This command prints the contents of the LAN-LINK.LOG file in
             a formatted manner to the printer. It requests the  callsign
             of  the  log  entry to be displayed. If you  want  to  print
             entries  for particular calls or parts of call, enter  those
             call  or parts of calls.  Valid entries are G, G3, G3Z  etc.
             If  you  want  to print every entry in  the  log  enter  the
             asterisk '*' character.

             10.4 Scan Log

             This command displays the contents of the LAN-LINK.LOG  file
             in  a  formatted  manner on the  screen.   It  requests  the
             callsign  of the log entry to be displayed. If you  want  to
             see  entries  for particular calls or parts of  call,  enter
             those  call or parts of calls. Valid entries are G, G3,  G3Z
             etc.  If  you want to see every entry in the log  enter  the
             asterisk '*' character.

        11.0 Message Menu

        The Message Menu provides the following choices.

        B BBS Command Files
        C Current Messages
        M scan Message
        N leave Note
        O Old Messages
        P QSP LAN-LINK
        U QRU LAN-LINK
        T Time tag

        Type in the single letter to make your choice.

             11.1 BBS Command Files

             This option shows you a list of the BBS command files on the
             default directory.  In other words, all files with the  file
             extension of '.BBS'.

             11.2 Current Messages

             This  option shows you a list of the outgoing messages  that
             have not been sent. In other words, all files with the  file
             extension  of '.OUT'.  See Section 20 for a  description  of
             outgoing  messages  in your "Smart  Packet  Radio  Answering
             Machine".

             11.3 Scan Message

             This  feature allows you to scan messages in  the  computer.
             After  depressing the key you will be prompted for  INcoming
             or  OUTgoing  (I/O)  messages.   If  you  request   Incoming
             messages  you  will  see  the  messages  addressed  to  your


        LAN-LINK.DOC (c) G3ZCZ 1988





        LAN-LINK VERSION 1.50  PAGE 25


             callsign.   After scanning your messages,  the file will  be
             renamed  to  yourcall.n. where n is an  incrementing  number
             from 1 to 999.

             11.4 Leave Note

             In  all  modes  you can leave a  brief  note  (message)  for
             another station.  When you invoke this command the header is
             written  to the message file, then as you enter the text  it
             is stored on the disk in the usual format.

             WHILE  WRITING YOUR NOTE, LAN-LINK can't receive  characters
             from  the  TNC. All other features ARE INHIBITED  OR  LOCKED
             OUT.  THUS IF SOMEONE CONNECTS TO YOU, THE TNC WILL KNOW THE
             BUT LAN-LINK WILL NOT.  BE WARNED !!!

             After you have left the note and received the 'QSL'  message
             from LAN-LINK, if you are in the Packet communications mode,
             push  function  key  8 Alt-D to load  the  callsign  of  the
             recipient into the beacon.

             When  you  leave a note, leave it for the root call  of  the
             connectee, for example to leave a note for G3ZCZ/W3 leave it
             for G3ZCZ, similarly to leave a note for  WB8WKA-1 leave  it
             for  WB8WKA.  LAN-LINK is smart enough to extract  the  root
             call from any callsign it links/connects with.

             11.5 Old Messages

             This feature shows you a list of the messages that have been
             sent.  In other words, all files with the file extension  of
             '.OLD'.

             11.6 QSP LAN-LINK

             LAN-LINK contains store and forward routines for messages in
             a Local Area Network (LAN) as described in Appendix 2.

             When connected to another LAN-LINK station, you may use  the
             NC/L :QSP: command to leave a message at that station.  This
             QSP  command  automates that feature for you.  It  lets  you
             just  enter the callsign of the station you wish to leave  a
             message  for.   It will then send the  text  sequence  :QSP:
             <callsign>.   The  other LAN-LINK HOST station  will  either
             reply  :QNO: followed by a number or :QRV: <callsign>.   The
             'QNO'  message means that the other computer  cannot  accept
             the message, the :QRV: message means that it is waiting  for
             you to send it.

             If  you get the :QRV: reply, go ahead and type the  message,
             or  send the text file containing the message.  If you  type
             the  message,  use a control Z (^Z) character  and  carriage
             return  to terminate the message.  (In AMTOR, LAN-LINK  will
             translate the ^Z to :EOF: +? to terminate the message).  You
             will  then  receive either a :QSL: from  the  other  station


        LAN-LINK.DOC (c) G3ZCZ 1988





        LAN-LINK VERSION 1.50  PAGE 26


             meaning that the message is accepted, or a :QNO: followed by
             a  number  which  means that something went  wrong  and  the
             message  was  not  stored.  QNO  numbers  are  described  in
             Appendix 3.

             11.7 QRU LAN-LINK

             The  NC/L  QRU  command allows you to  upload  a  number  of
             messages  to  the other station.  You use it when  you  have
             messages  pending on your system and want to pass them to  a
             third  computer for storage in the LAN, while you take  your
             computer off-line.

             You  can only use this option with a station which you  have
             previously  designated  as  a store and  forward  mail  box,
             namely  one for which you have set up a <callsign>.MBX  file
             (see  section  19).   This command may be triggered  by  you
             using this choice or by the connecting station sending you a
             :QRU: command.

             When the sequence is over, the computer sending the messages
             will transmit the NC/L command word :QJG: to signal that the
             sequence is complete.  Should you receive it before you  get
             any messages, then there weren't any pending.

             If  you  want  to download messages  from  another  LAN-LINK
             system,  connect to it and type the sequence :QRU:  followed
             by the 'Enter' character.  That system will then respond  to
             you as if the operator there had initiated a QRU command.

             Appendix 2 contains more information on the LAN capabilities
             of LAN-LINK.

             11.8 Time Tag

             This option is used to place a date time header on a message
             file  previously prepared by a word processor.  The name  of
             the file must be in the format 'CALLSIGN.OUT' (For  example,
             G3ZCZ.OUT).   It requests the callsign of the message  file.
             It then opens a new file, writes the header to the new  file
             and copies the contents of the original '*.OUT' file to  the
             new one.  When all is done, the original filename is  change
             to '*.BAK' and the new one becomes '*.OUT'.

        12.0 TNC Menu

        The TNC Menu provides the following choices.

         D Set TNC Date/Time
         F Flush TNC Buffer
         I Initialize TNC
         M calls Monitored List
         S Show Connect Status
         Q Change CQ Text
         X Change Ctext


        LAN-LINK.DOC (c) G3ZCZ 1988





        LAN-LINK VERSION 1.50  PAGE 27



        Type in the single letter to make your choice.

             12.1 Set TNC Date/Time

             This  feature puts the TNC into the command mode  and  loads
             the date into it from the computer time of day clock.

             This command does not work on the TNC1.

             12.2 Flush TNC Buffer

             This  option  is used to flush the program's  outgoing  text
             buffer and that of the PK-232.

             12.3 Initialize TNC

             This feature sets up the defaults for the TNC from the  file
             LAN-LINK.SYS.   If  you have put batteries in the  TNC,  you
             should normally only have to run this command when you first
             power up the TNC or change the batteries.

             It  will also set the date and time within the TNC from  the
             computer  clock, and, when it has loaded  the  configuration
             file,  may prompt you to set the TNC Terminal mode.  If  you
             are  using a TNC1 or a TNC2, it will not prompt you  because
             it assumes that they only operate on VHF packet. If you  are
             using a KPC-2, you may select 'H' or 'V', and of course,  if
             you have a PK-232, you may chose any of the options.

             12.4 Show Calls Monitored List

             This feature performs the same operation as Function key  5.
             It is equivalent to the TNC 'MH' command.

             12.5 Show Connect Status

             When you are in the Packet communications mode, this command
             lets you see the state of the connection.  It will show  you
             if  there  are any unacknowledged packets en  route  to  the
             other  station.   If  you  have been  sending  text,  it  is
             advisable  to  use this command before  you  disconnect,  to
             ensure that all the data has been received and  acknowledged
             by the other party.  You may use this command in either  the
             TNC Command or the TNC Converse mode.

             In a multi connect situation, it will show you the status on
             all the IO channels.

             You  may  also use this command to reset the  status  window
             display  after  a relink or any other event  which  was  not
             reflected in the status window.





        LAN-LINK.DOC (c) G3ZCZ 1988





        LAN-LINK VERSION 1.50  PAGE 28


             12.6 Change CQ Text

             This  feature  allows you to change the contents of  the  CQ
             text message string. This is the string that is  transmitted
             along  with the CQ call.  The default value is  loaded  from
             the LAN-LINK.SYS file.

             12.7 Change Ctext

             This  feature allows you to change the message that will  be
             received by another packet station when it connects to  you.
             Refer to the 'CTEXT' command in the TNC manual.

        13.0 Parameter Menu

        The Parameter Menu provides the following choices.

        B Turn Beacon Mode On/Off
        C Clear Connect Count
        D Turn Digipeat Detect On/Off
        F Display DeFaults
        M Set Message Count
        N Turn NETROM Drop Out On/Off
        P Turn Printer On/Off
        Q Set CQ delay time
        R Turn Relay On/Off
        S Turn Sound On/Off
        T Turn Contest Mode On/Off

        Type in the single letter to make your choice.

             13.1 Turn Beacon Mode On/Off

             This command toggles the beacon option for the automatic  CQ
             caller  in the AMTOR and Packet communications modes.   When
             it  is active a [B] will be displayed in the status  window.
             In  this mode, the Automatic CQ sequence will  resume  after
             the  AMTOR link is dropped or a Packet  Communications  mode
             disconnect.

             In  the  beacon mode, the last few logbook entries  will  be
             displayed in the logpage window which overlays the  outgoing
             text window at the bottom of the screen.

             In   the  Packet  mode,  the  CTEXT  message  is  the   only
             transmission  from you that the other station will  receive,
             so make it good and don't forget to set 'CMSG ON'.

             In  the AMTOR Mailbox/Beacon mode, the contents of the  LAN-
             LINK.TXT file will be transmitted to the station who  called
             you.   The capture-to-disk will then be turned on to  record
             one  transmission from that station.  The QSO will  then  be
             logged  to  the  logbook file.  Don't forget  to  check  the
             entries  in  the LAN-LINK.LOG and text in  the  LAN-LINK.RUN
             files in case the computer made a mistake in recognizing the


        LAN-LINK.DOC (c) G3ZCZ 1988





        LAN-LINK VERSION 1.50  PAGE 29


             call sign of the other station.

             THE  BEACON MODE IS DESIGNED TO ENCOURAGE PEOPLE TO QSY  OFF
             THE  CROWDED PACKET HF CHANNELS. DO NOT USE IT ON A  CROWDED
             HF CHANNEL OR ON AN ACTIVE VHF CHANNEL.  IF YOU DO, YOU WILL
             SOON FIND THAT OTHER STATIONS HAVE SET THEIR TNC'S TO REJECT
             YOUR  PACKETS, AND YOU WILL NOT WORK ANYBODY, YOU WILL  JUST
             BE A SOURCE OF QRM AND WILL BE KNOWN AS SUCH.

             THE  MODE IS ALSO DESIGNED FOR ROBOT BEACONS FOR THE  HIGHER
             FREQUENCIES.  FOR EXAMPLE IF YOU LEAVE IT RUNNING ON 6 OR 10
             METERS YOU NEVER KNOW WHEN A SHORT OPENING WILL ALLOW A  QSO
             TO  SOME  PART OF THE WORLD,  A DX CONTACT  YOU  WOULD  HAVE
             OTHERWISE  MISSED.    DO NOT LEAVE IT RUNNING ON  20  METERS
             WHEN  THE  BAND  IS  OPEN.   FURTHER  APPLICATIONS  ARE   IN
             METEORSCATTER AND OTHER "EXOTIC" MODES OF COMMUNICATIONS.

             If you are using this mode in a special event station or DX-
             pedition  you may type characters into the transmit  buffer,
             while the other station is sending to you.  When he, she  or
             even  it  turns  it back to you,  you  will  transmit  those
             characters before the sign off sequence.

             In both the Packet and AMTOR communications modes, the robot
             may  be shut down by stations connecting to you and  telling
             you to QRT.

             13.2 Clear Connect Count

             You  use  this option to reset the PACKET and  AMTOR  beacon
             mode  "connect  has taken place indicator"  and  QTC  Snatch
             count.   These  are  flashing [C] and [Q]  displays  in  the
             status  window.  Whenever someone else connects or links  up
             to  you  the [C] display will be  incremented.   The  number
             shown with the 'C' is the number of connects that have taken
             place since the Indicator was last reset.  If a 'happy face'
             is  flashing  along  with the connect  count,  your  "target
             station"  was  amongst those connecting. The  [Q]  indicator
             alerts  you  to the fact that LAN-LINK tried to  connect  to
             another  station  after  recognizing your  call  in  a  mail
             beacon.   Both  are  reset  by  this  option.   If  you  are
             monitoring  Packet traffic on a channel, you may not  notice
             that a connect has previously taken place.  These  indicator
             alert  you to check the contents of the Incoming  mail  file
             ('yourcall.OUT') for any incoming messages.

             If the 'Q' count is much greater than the 'C' count you  may
             be  copying a beacon from a station that you cannot  connect
             with directly.

             13.3 Turn Digipeat Detect On/Off

             This option toggles the digipeat display command on and off.
             If  the Digipeat Display is active, any  signals  digipeated
             through  you will be stored to the LAN-LINK.RUN file  and  a


        LAN-LINK.DOC (c) G3ZCZ 1988





        LAN-LINK VERSION 1.50  PAGE 30


             'beep'  will  be sounded for each packet  being  digipeated.
             The status display window will also contain a [D].

             13.4 Display DeFaults

             This feature lets you display how LAN-LINK was configured by
             the  LAN-LINK.SYS file.  It also displays the state  of  any
             flags  you have set/reset if they are not already  shown  in
             the Status window.  YOU SHOULD USE IT AFTER EDITING THE LAN-
             LINK.SYS FILE TO MAKE SURE THAT EVERYTHING IS CORRECT.

             13.5 Set Message Count

             As  an  alternative to function key 8 or Alt-D,  using  this
             option  will  also load a QTC 'Mail' list into  your  Packet
             communications   mode   Beacon   and   initiate   a   beacon
             transmission every 30 minutes (Refer to the BTEXT command in
             the  TNC manual).  If no messages are present, or  the  only
             message   is   to  you  (incoming   or   snatched),   beacon
             transmissions   are  inhibited.   This  conforms   to   good
             operating practice on crowded Packet channels.

             13.6 Turn NETROM Drop Out On/Off

             When  connecting via NETROM, the normal way of operating  is
             to  disconnect  if  the  connect  attempt  fails.   You  may
             configure the NETROM connect attempt flag to stay  connected
             at the node where the failure occurred.  Use the normal mode
             when  trying  to get through on a known path, and  the  stay
             alive mode when exploring NETROM circuits.

             13.7 Turn Printer On/Off

             This  option  toggles  the printer on  and  off.   When  the
             printer  is turned on, any incoming data will be printed  in
             real  time.  If you intend to print files received  at  1200
             bauds  in  the  packet communications   mode,  use  a  print
             spooler or you may loose data.  The printer is automatically
             turned off in the packet mode when a disconnect occurs.

             13.8 Set CQ delay time

             This  option allows you to change the time that the  program
             waits for a response after a CQ call until the following one
             is  transmitted.  The default value is loaded from the  LAN-
             LINK.SYS file.  You may want to experiment since the  actual
             time  will  depend on the clock frequency of  the  computer.
             Make  it a small number such as 4 or 6 when operating  AMTOR
             or  a  DX-pedition, and make it a larger number such  as  30
             when  operating  on crowded packet  channels.   The  maximum
             allowed value is 255.

             13.9 Turn Relay On/Off

             This  option  toggles the Store and  forward  Message  Relay


        LAN-LINK.DOC (c) G3ZCZ 1988





        LAN-LINK VERSION 1.50  PAGE 31


             Capability of your system on and off.  If the Message  Relay
             Capability is active (toggled on), any one who connects  can
             store a message in your system using the ':QSP:  <callsign>'
             NC/L command. If the Message Relay Capability is not  active
             anyone  who  attempts to ':QSP: a message'  will  receive  a
             ':QNO:  1' "error" message.  The status display window  will
             show a [R] when the Message Relay Capability is active.  The
             default  state  for the Message Relay Capability  is  loaded
             from the LAN-LINK.SYS file.

             When the Store and forward capability is active, the  suffix
             'R' will be added to the

                       '[ZCZ] *** LAN-LINK 1.50'

             message  received  by anyone connecting to  your  system  to
             notify  them that they can store messages.  In  this  manner
             they  don't  have  to try to leave a message  and  then  get
             ':QNO:  1'  error  message to find out  if  the  feature  is
             toggled off.

             13.10 Turn Sound On/Off

             This  option toggles the sound on and off.  If the sound  is
             off,  a flashing indicator will be displayed in  the  Status
             Window.   When the sound is toggled on again, a  chime  will
             sound to verify the audio.

             13.11 Turn Contest Mode On/Off

             This option first toggles the contest mode.  If the  contest
             mode  is active, the word 'TEST' and the number of the  next
             QSO will be displayed in the status window. When the contest
             mode is toggled on, this command then prompts you to set the
             starting  QSO  number  and  write in  the  non  changing  or
             standard  message  that will be transmitted as  part  of  an
             exchange of messages during a contest.

             If  you set the QSO number to '1' it will be transmitted  in
             each  exchange  and  then incremented each time  you  log  a
             contact.   If you set it to '0', it will not be  transmitted
             nor  incremented.  Use the '0' option for contests which  do
             not require serial numbers.

             The contest feature is toggled off the next time you  select
             this  command, or when you change the PK-232  Communications
             mode (for example, switch from Morse to BAUDOT).

             Note  that  while  this does give you  some  semi  automatic
             contest  operation  by  using  command  keys,  there  is  no
             checking of callsigns for duplicates built into the program.
             In  a contest, you enter the callsigns  and call  the  other
             station  in  the normal manner, then use the  'End'  key  to
             transmit  the exchange (QSO number and standard  text).



        LAN-LINK.DOC (c) G3ZCZ 1988





        LAN-LINK VERSION 1.50  PAGE 32


        14.0 Q Codes [NC/L]

        This  option  displays  help information about  the  use  of  the
        Network Communications Language (NC/L) "Q" codes.

        15.0 Run DOS Command

        This option allows you to enter a DOS shell.  Make sure that  you
        restore  the  system  to the directory  which  contains  LAN-LINK
        before  you exit from the shell.  If you don't, LAN-LINK will  be
        searching  the  wrong  directory for  files,  and  display  ERROR
        messages.

        You may use  the DOS shell while in QSO when you have loaded  the
        transfer buffers as well as while monitoring activity.

        16.0 CommunicationS Modes

        This menu allows you to change the communications mode of the PK-
        232.   If  your TNC hardware cannot support  those  modes,  don't
        bother to try them.  This is software not hardware, and in  spite
        of  what  people  tell you, software can't  do  everything.   The
        following communications modes are available.

         V VHF PACKET
         H HF PACKET
         A AMTOR (STANDBY RECEIVE)
         B BAUDOT (RTTY)
         C MORSE (CW)
         M AMTOR (ALIST [chirpcopy])
         S ASCII (RTTY)
         G SIGNAL
         N NAVTEX

        Type  in the single letter to make your choice.  Don't forget  to
        select the correct Radio port on the PK-232.

             16.1 VHF PACKET

             This  is  the  1200  Baud VHF  Packet  mode.  LAN-LINK  will
             optimize the TNC link parameters for this mode.

             16.2 HF PACKET

             This is the 300 Baud HF Packet mode. LAN-LINK will  optimize
             the TNC link parameters for this mode.

             16.3 ASCII (RTTY)

             This is the ASCII RTTY mode. LAN-LINK will configure the TNC
             parameters for this mode at 110 bauds.

             16.4 BAUDOT (RTTY)

             This  is the BAUDOT RTTY mode. LAN-LINK will  configure  the


        LAN-LINK.DOC (c) G3ZCZ 1988





        LAN-LINK VERSION 1.50  PAGE 33


             TNC parameters for this mode at 45 bauds.

             16.5 MORSE (CW)

             This  is  the  CW  mode. LAN-LINK  will  configure  the  TNC
             parameters for this mode at 20 wpm (10 wpm for the KAM).

             In this mode the ALT-D key will disengage the receive  speed
             lock  inside the PK-232 to facilitate locking  onto  another
             signal.

             16.6 AMTOR (STANDBY RECEIVE)

             When  you select the AMTOR standby mode you are placed  into
             the  'standby  receive' mode.  If you are in  AMTOR  standby
             mode,  you  will  not  be able to  display  signals  of  the
             chirpcopy  mode  (which means that you will not be  able  to
             display a QSO in progress).

             The  Alt-D key or function key 8 toggles between  the  AMTOR
             ARQ and the ALIST communications modes.

             16.7 AMTOR (ALIST [chirpcopy])

             If  you  want to read the mail on an existing AMTOR  QSO  in
             progress, select the AMTOR ALIST or chirpcopy mode.

             The  Alt-D key or function key 8 toggles between  the  AMTOR
             ARQ and the ALIST communications modes.

             16.8 SIGNAL

             Use  the 'G' option to select the 'SIGNAL' mode.   Read  the
             PK-232  documentation carefully to understand how this  mode
             works.  Once the PK-232 has identified the digital signal it
             is  tuned  to,  use the Communications Mode  Select  menu  a
             second  time  to select the relevant mode and then  set  the
             baud rates and shift to display the data if necessary.

             16.9 NAVTEX

             Use the 'N' option to select the 'NAVTEX mode.  Read the PK-
             232   documentation  carefully to understand how  this  mode
             works.

        17.0 Terminal Mode Menu

        This menu allows you to set the terminal configuration mode.  The
        Terminal  Menu  provides  different choices  depending  on  which
        communications mode you have selected.

             17.1 Packet Terminal Menu

             The  Packet Terminal mode of operation will be shown in  the
             Status window at the top of the screen.  If you are  reading


        LAN-LINK.DOC (c) G3ZCZ 1988





        LAN-LINK VERSION 1.50  PAGE 34


             the mail on a station, the callsign of that station will  be
             shown  next  to the word "MAIL".  If you  are  connected  to
             someone,  the call (and path) will be shown prefixed by  the
             "*>" sequence.

             In  the Packet Communications mode, you are  presented  with
             the following choices.

              B Change Packet Baud Rate
              C CQ/Beacons
              E Everything
              M Read the Mail
              S Just My Station (Solo)
              T All Traffic
              0 Multiple User Connects
              1 Single User Connects
              F Conference
              R Conference Bridge On/Off

             Type in the single letter to make your choice.

             17.1.1 Change Packet Baud Rate

             In  the PACKET mode you may change the RF baudrate   between
             300, 600, 1200 and 2400 bauds.

             17.1.2 CQ/Beacons

             In  this  mode, you will see CQ and BEACON  packets  on  the
             channel.  (This corresponds to 'MONITOR 1'on the PK232).

             This mode only works on the PK-232 and the KAM.

             17.1.3 Everything

             You can set the TRAFFIC mode to 'Everything'. It corresponds
             to 'MONITOR 6' on the PK-232.

             17.1.4 Read the Mail

             You  can  read the mail on a BBS or other  station  and  get
             bulletins without connecting to that station yourself.   You
             use  this mode to do so.  you will be prompted for the  call
             whose  packets you wish to monitor.  Remember to  enter  the
             call of the station sending the packets, not the call of the
             one  receiving them.  (This corresponds to 'MONITOR  0'  and
             'MBX' callsign). This mode only works on the PK-232.

             You  can also use this command to monitor both  sides  (read
             the mail) on a QSO on a busy packet channel.

             You may want to turn the Digipeat Data Display mode off when
             reading the mail.

             If  you are not using a PK-232 you will see the  headers  as


        LAN-LINK.DOC (c) G3ZCZ 1988





        LAN-LINK VERSION 1.50  PAGE 35


             well as the traffic.

             17.1.5 Just My Station (Solo)

             In  this mode, you will only see messages addressed to  you.
             You  will only get messages from people who connect to  you.
             (This corresponds to 'MONITOR 0').

             17.1.6 All Traffic

             In this mode you will see all of the data packet traffic  on
             channel.   You  can use this mode to check that the  TNC  is
             working. (This corresponds to 'MONITOR 4' or 'MONITOR ON').

             17.1.7 Single User Connects

             This is the normal mode one on one mode of operation ('USERS
             1').

             17.1.8 Multiple User Connects

             When you are in a multiple connect mode, an asterisk will be
             shown in the status window next to the word 'PACKET'.

             LAN-LINK supports two multiple connect modes, individual and
             conference.

             An  extract of an actual 'off the air' CRT display  (showing
             received  text  only) in a multi user mode is  shown  below.
             Note  each line of text as received by the TNC  is  prefixed
             (by  the PK232) with the IO channel number and  callsign  of
             the station its connected to.

             1:4X4IL: *** CONNECTED to 4X4IL via 4X4IC, 4X6JP
             0:4X4IC: joe do u read?
             2:4Z4ZB: *** CONNECTED to 4Z4ZB
             1:4X4IL: Look for me on PR via 4X6JP 73s and Shalom.
             2:4Z4ZB: GE JOE I WILL DIS THEN U CAN GO VIA THE REP....>
             1: *** DISCONNECTED: 4X4IL via 4X4IC, 4X6JP
             0:4X4IC: UNPROTO  CQ
             2:4Z4ZB: GO AHEAD BOYS...DE ALON..>
             0:4X4IC:
             2: *** DISCONNECTED: 4Z4ZB

             This  is the normal Multi Connect Mode as described  in  the
             TNC  manual.  Here you  are connected to up to  10  stations
             and will send different traffic to each of them.  Each  time
             you wish to send something to a particular station, you must
             select  the  IO channel the station is connected  on  before
             typing the text or sending the file.

             The stream change character for all TNCs in the VHF multiple
             connect  modes is '|' ($7C). In the KAM, it is'\' on HF  and
             '|' on VHF.  Its the same key as now but one is in the shift
             case.   Be  careful  on  HF as the  '\'  shows  up  in  file


        LAN-LINK.DOC (c) G3ZCZ 1988





        LAN-LINK VERSION 1.50  PAGE 36


             directories and confuses the computer.

             You select the channel by typing the '|' character  followed
             by (in the TNC) the channel number.  For example if you  are
             connected  to  G8BTB  on IO channel 0 and  to  G3ZCZ  on  IO
             channel 1, then to talk to G8BTB you would type '|0'  before
             any text, and similarly to send something to G3ZCZ you would
             type a '|1' before the text you're going to send me.  If you
             are  not using a PK232, read the TNC manual to determine  if
             the IO streams are identified by numbers or by letters.  The
             TNC2 standard configuration uses letters.

             17.1.9 Conference

             In  the conference mode on the other hand,  everything  that
             you  type  at the keyboard is automatically  transmitted  to
             each  station that you are connected with.  Thus if you  are
             linked  to two stations each line will be packeted twice  by
             the  TNC.  You don't have to worry about sending  the  wrong
             thing to the wrong person, as they will all get the stuff.

             You  enter  this  mode by selecting the 'F'  option  in  the
             Terminal Menu.  You terminate the mode by selecting the  '1'
             option.

             You  connect in the usual manner using Alt-C or the  Connect
             option in the Call Menu.  You MUST WAIT FOR A CONNECTION  TO
             BE  ESTABLISHED OR TIME OUT before attempting to connect  to
             the  next  station.  If you do not, you will  get  an  error
             message back from the TNC.

             In  the conference mode, as the same text is transmitted  on
             all IO channels, the throughput will be reduced.  Slow  down
             your  typing speed or use short packets.  Should  you  check
             the link status or call monitored list, you may not be  able
             to  get  back into the converse mode if you  have  too  many
             packets outstanding. If that happens, wait a while and  then
             try  to set the converse mode with command key 10.  You  may
             have to try it a few times, depending on how good your links
             are.

             DON'T  TRY  TO SEND A FILE IN THE CONFERENCE MODE,  ITS  NOT
             DESIGNED FOR IT. KEEP THE PACKETS SHORT.

             BE ALSO WARNED THAT IF YOU USE THE CONFERENCE (BRIDGE)  MODE
             ON  BAD LINKS (SUCH AS CROWDED HF CHANNELS AND  OTHERS  WITH
             LOTS  OF RETIRES), THE KEYBOARD MAY SEEM TO LOCK  UP,  WHILE
             LAN-LINK  WAITS  FOR SPACE IN THE TNC BUFFER TO  OUTPUT  THE
             TEXT.

             The conference mode will only work in the PK-232 if  DCDCONN
             is  set to ON.  So if you are using a PK-232, LAN-LINK  will
             do it for you when you enter the conference terminal mode in
             case you forgot or/and haven't set the LAN-LINK.SYS file  to
             include the line 'DCD ON', At the same time set LAN-LINK.SYS


        LAN-LINK.DOC (c) G3ZCZ 1988





        LAN-LINK VERSION 1.50  PAGE 37


             default  states to show the calls of other stations on  each
             incoming  line  in the MULTI connect modes.  (Read  the  TNC
             manual for how to do this).

             The conference mode will only work in the TNC2 if DCDCONN is
             jumpered so that Pin 8 of the RS-232 Interface changes state
             when you connect to someone else.  If you get error messages
             and see the characters '|J' on your screen, then the  jumper
             probably isn't set.

             The conference mode does not work on the TNC1.

             In  the  conference  mode,  if  any  one  of  the   stations
             disconnects,  the TNC will return to the command  mode,  and
             you  must  use command key 10 to return the program  to  the
             converse mode before you type another character of text.

             17.1.10 Conference Bridge On/Off

             This option toggles the conference bridge on and off. In the
             Bridge  Multi  Connect  Mode you are  acting  as  a  central
             switch.   You  can link together up to 10  stations  in  one
             multi way connection.  In this mode any packets arriving  on
             any  steam  are echoed to all other streams  that  you  have
             'connects' on except the one that they came in on.  Anything
             you type will be sent to all connected streams.

             In  this  manner, all stations will not see their  own  text
             echoed  back.  Each line of text output by LAN-LINK in  this
             mode  will contain the callsign of the  station  originating
             the  packet. Your packets will contain your call as  entered
             in  line 1 of the LAN-LINK.SYS file.  Thus for  example,  if
             your  call was KB8RP/4X and normally shows up in the  packet
             header as KB8RP here it will show in the data as KB8RP/4X.

             Just remember that the bridge puts out a lot of packets,  so
             do multi way connects on a quiet frequency.  You must be  in
             the  conference  mode  to  turn  the  bridge  on,  and   any
             disconnect  will take the bridge down.  Should that  happen,
             toggle  it on again.  A bridge will be shown in  the  status
             window whenever the conference bridge is up.

             17.2 AMTOR Terminal Menu

             In the AMTOR Communications mode, you are presented with the
             following choices.

              C Force Break [ACHG]
              F Start Mode B [FEC]
              L Force LETTERS case
              M Read the Mail [ALISTEN]
              O Override ROBOT/Mailbox
              S Standby Receive [ARQ]
              R Set ROBOT/Mailbox
              W CW Identification


        LAN-LINK.DOC (c) G3ZCZ 1988





        LAN-LINK VERSION 1.50  PAGE 38



             Type in the single letter to make your choice.

             17.2.1 Force Break [ACHG]

             This  option forces a changeover or 'break in'.  If for  any
             reason  you want to interrupt the other station you  send  a
             'BREAK' signal in software this way.

             17.2.2 Start Mode B [FEC]

             This option places the terminal into the FEC transmit  mode.
             This  puts  you  on  the air,  anything  you  type  will  be
             transmitted.  Function key 10 does the same thing.

             17.2.3 Force LETTERS case

             This  option  lets  you force the  PK-232  receiver  to  the
             letters  case  if for some reason you appear to  be  in  the
             numbers case.  It will return you to the converse mode.

             17.2.4 Read the Mail [ALISTEN]

             This option lets you read the Mail on a QSO.  Unfortunately,
             when  you tune in a chirpy AMTOR QSO in the ARQ  or  standby
             mode you won't get any copy on the QSO in progress.  You can
             however read the mail on one by entering the ALISTEN mode.

             17.2.5 Override ROBOT/Mailbox

             This option lets you override the ROBOT BEACON and chat to a
             station  that  has linked to the ROBOT.  Use  it  after  the
             message in LAN-LINK.TXT has been sent, namely when the other
             station is sending a message to you.

             17.2.6 Standby Receive [ARQ]

             This option returns you to the ARQ standby mode. You must be
             in this mode to receive signals from another station who  is
             calling  you.   When  you  tune for  CQ  calls,  they  sound
             somewhat like fast RTTY with a ringing sound similar to  the
             connect  alarm  used by LAN-LINK (but at  a  faster  ringing
             rate).

             17.2.7 Set ROBOT/Mailbox

             This  option lets you turn on the Mailbox during  a  regular
             AMTOR  QSO so that the other station can leave a message  or
             download  a  file remotely. You must only use  it  when  the
             other station is sending text.

             17.2.8 CW Identification

             This  option is used to send a CW identification.  The  CWID
             is sent in the FEC mode.


        LAN-LINK.DOC (c) G3ZCZ 1988





        LAN-LINK VERSION 1.50  PAGE 39



             The  identification  consists  of  the  sequence  'DE  <your
             callsign>' where your call sign is that entered into the PK-
             232 as  'MYCALL'.

             You  use  this  feature  if your  license  requires  you  to
             identify in morse code as well as in the operating mode.

             17.3 Baudot Terminal Menu

             In  the Baudot Communications mode, you are  presented  with
             the following choices.

              B Set Baud Rate
              F Select Shift
              N NAVY MARS Message Protocol
              U USOS Off
              S SELCAL set/reset
              W CW Identification

             Type in the single letter to make your choice.

             17.3.1 Set Baud Rate

             This feature allows you to set a desired communications baud
             rate  directly.  You will be prompted to enter  the  desired
             rate.  Use this command to avoid having to shift through too
             many intermediate states, if for example, you want to make a
             direct change from 45 to 100 bauds.

             17.3.2 Select Shift

             This  feature lets you select Wide (850 Hz) or  narrow  (170
             Hz) shift directly.  if you have a KAM, you may also  select
             the Commercial Shift (425 Hz).

             The  shift is displayed in the status window at the  top  of
             the screen. It is shown as 'W', 'N' or 'C' for wide,  narrow
             or commercial respectively.

             17.3.3 NAVY MARS Message Protocol

             The Navy Mars option toggles the Navy MARS mode on and  off.
             This  feature is only present on the PK-232.  When  On,  the
             feature provides the following protocol.

             17.3.3.1    Any  Carriage  Return  or Enter  (CR)  from  the
                         keyboard is sent as  CR, CR, (Line Feed) LF.

             17.3.3.2    In  a file transmission lines are terminated  by
                         the same CR,CR,LF sequence.

             17.3.3.3    In a file transmission, blank lines are sent  as
                         a LF (without a CR).



        LAN-LINK.DOC (c) G3ZCZ 1988





        LAN-LINK VERSION 1.50  PAGE 40


             17.3.3.4    In  a  file  transmission, a plus  sign  '+'  is
                         replaced   by   a  sequence  of   12   "letters"
                         characters.   There can be more than one +  sign
                         on a line.

             17.3.3.5    In  a file transmission, the sequence 'NNNN'  is
                         followed   by   a  sequence  of   12   "letters"
                         characters.   There  can  only  be  one   'NNNN'
                         sequence on a line.

             When the NAVY MARS feature is active a [N] will be displayed
             in the status window.

             17.3.4 USOS On/Off

             This  option toggles the Unshift on space (USOS) feature  on
             and  off.   When  the USOS is on, the  TNC  reverts  to  the
             letters shift each time a 'space' character is received.  It
             helps when displaying noisy copy.

             If USOS is active, 'USOS' will be shown in the status window
             at the top of the screen.

             17.3.5 SELCAL set/reset

             This  command  key toggles the SELCAL feature  on  and  off.
             When the SELCAL is activated, as shown in the status window,
             the incoming text from the TNC is scanned.  When either  the
             letters  "ZCZC" or 'your callsign' (as entered in line 1  of
             the LAN-LINK.SYS file) is received the "capture-to-disk"  is
             turned  on.  All subsequent text will be stored in the  LAN-
             LINK.RUN  file  until the letters "NNNN" are  received.   At
             that time the "capture-to-disk" is turned off.

             You  may  use this feature when monitoring  commercial  RTTY
             broadcasts  to  record news and other information,  or  when
             calling CQ to start recording all incoming text and keep the
             QSO on disk.

             You  may  use  function  key 1  turn  the  capture  to  disk
             permanently  on  to override the automatic  turnoff  if  you
             wish.

             17.3.6 CW Identification

             This  option is used to send a CW identification.   You  use
             this if your license requires you to identify in morse  code
             as well as in the operating mode.

             The  identification  consists  of  the  sequence  'DE  <your
             callsign>' where your call sign is that entered into the PK-
             232 as  'MYCALL'.





        LAN-LINK.DOC (c) G3ZCZ 1988





        LAN-LINK VERSION 1.50  PAGE 41


             17.4 ASCII Terminal Menu

             In the ASCII Communications mode, you are presented with the
             following choices.

              B Set Baud Rate
              F Select Shift
              S SELCAL set/reset
              W CW Identification

             Type in the single letter to make your choice.

             17.4.1 Set Baud Rate

             This feature allows you to set a desired communications baud
             rate  directly.  You will be prompted to enter  the  desired
             rate.  Use this command to avoid having to shift through too
             many intermediate states, if for example, you want to make a
             direct change from 110 to 1200 bauds.

             17.4.2 Select Shift

             This  feature lets you select Wide (850 Hz) or  narrow  (170
             Hz) shift directly.  if you have a KAM, you may also  select
             the Commercial Shift (425 Hz).

             The  shift is displayed in the status window at the  top  of
             the screen. It is shown as 'W', 'N' or 'C' for wide,  narrow
             or commercial respectively.

             17.4.3 SELCAL set/reset

             This  command  key toggles the SELCAL feature  on  and  off.
             When the SELCAL is activated, as shown in the status window,
             the incoming text from the TNC is scanned.  When either  the
             letters  "ZCZC" or 'your callsign' (as entered in line 1  of
             the  LAN-LINK.SYS file) is received the  capture-to-disk  is
             turned  on.  All subsequent text will be stored in the  LAN-
             LINK.RUN  disk file until the letters "NNNN"  are  received.
             At that time the capture-to-disk is turned off.

             You  may  use  function  key 1  turn  the  capture  to  disk
             permanently  on  to override the automatic  turnoff  if  you
             wish.

             17.4.4 CW Identification

             This  option is used to send a CW identification.   You  use
             this if your license requires you to identify in morse  code
             as well as in the operating mode.

             The  identification  consists  of  the  sequence  'DE  <your
             callsign>' where your call sign is that entered into the PK-
             232 as  'MYCALL'.



        LAN-LINK.DOC (c) G3ZCZ 1988





        LAN-LINK VERSION 1.50  PAGE 42


             17.5 CW Menu

             In  the CW Communications mode, you are presented  with  the
             following choices.

              L Lock to Receive Signal
              S Set Morse Speed
              U Unlock Morse Speed

             Type in the single letter to make your choice.

             17.5.1 Lock to Receive Signal

             This option locks the PK-232 to the speed of the incoming CW
             signal.

             17.5.2 Set Morse Speed

             This option lets you set the CW speed.

             17.5.3 Unlock Morse Speed

             This option unlocks the PK-232 from the incoming CW  signal.
             It  performs the same task as the Alt-D key.  It is used  to
             speed  up capture of a new signal or to break the lock  when
             the PK-232 appears to have locked up at the wrong speed.

             18.0 Hot Keys

        LAN-LINK  also  contains a number of "Hot" keys to allow  you  to
        perform common operations with a minimum of key strokes.  A  list
        of what is available is shown below, followed by a description of
        what happens when you push each key.

              Alt C- Call/Connect to
              Alt D- Disconnect or Receive
              Alt L- Edit Log
              Alt M- Message Scan
              Alt R- Retry Call/Connect
              Alt X- Exit to DOS
              Alt Z- Zap BBS

             18.1 Alt C- Call/Connect to

             This  key performs the same task as the Call option  in  the
             Call Menu.  The Alt C key has been provided for those people
             whose  fingers  have learnt YAPP and don't wish  to  be  re-
             educated.

             18.2 Alt D- Disconnect or Receive

             This key performs the same task as function key 8.





        LAN-LINK.DOC (c) G3ZCZ 1988





        LAN-LINK VERSION 1.50  PAGE 43


             18.3 Alt L- Edit Log

             This  key performs the same task as the Edit Log  choice  in
             the Log Menu.

             18.4 Alt M- Message Scan

             This  key performs the same task as the Message Scan  choice
             in the Message Menu.

             18.5 Alt R- Retry Call/Connect

             This  key performs the same task as the Retry choice in  the
             Call Menu.

             18.6 Alt X- eXit to DOS

             This key performs the same task as the Exit to Dos choice in
             the Main Menu. It exits the program and returns you to DOS.

             18.7 Alt Z- ZAP BBS

             This key performs the same task as the Zap BBS choice in the
             Call Menu.

             18.8  End- > +?  [Over]

             In  the Packet communications mode this command  sends  your
             callsign  followed by the > and Line feed  characters.   You
             may use this to signal 'OVER' in a packet contact.

             In  the  AMTOR  communications mode  this  command  sends  a
             callsign   sequence  followed  by  the  '+?'   sequence   of
             characters which are the software 'OVER' signal.

             In  the  MORSE and RTTY (Baudot  and  ASCII)  communications
             modes, this command lets you transmit the following sequence
             <other  call) DE <your call> and returns you to  the  PK-232
             Command  Mode.   For example if you are 4X6AA  and  you  are
             working G3ZCZ then this command would transmit the  sequence
             'G3ZCZ de 4X6AA'.  You use this at the END of a transmission
             in any mode except Packet.

             If  you  have typed something into the 'type  ahead  buffer'
             then touch this key, the contents of the buffer will will be
             transmitted followed by the callsign sequence.

             18.9 PgUp- Scrollback (Scrolls back incoming text).

             This key lets you repeat the display of incoming text  which
             has  scrolled out of the incoming window.  you may print  it
             or capture it to disk during the repeat.

             A  small menu displays your options when showing the  scroll
             back information.  You may move the menu window up and  down


        LAN-LINK.DOC (c) G3ZCZ 1988





        LAN-LINK VERSION 1.50  PAGE 44


             with  the left and right arrow keys.  Use the 'ESC'  key  to
             terminate the scrollback mode.

             You can save the contents scrollback buffer displayed on the
             screen by turning the "capture to disk' on, and then writing
             text to the window.  Anything written will be captured.

             18.10 The HOME Key

             The  home key will clear the window screen that  the  cursor
             happens to be in at the time that the key was depressed, and
             will then position the cursor at the top left hand corner of
             that window.

             18.11 The DOWN ARROW key

             The  DOWN  ARROW  key toggles  the  Normal/Reverse  Sideband
             command in all PK232 communications modes except MORSE.  The
             sideband is depicted in the status window by the up and down
             arrows.  If the down arrow is showing, you are set for Lower
             Sideband (LSB) which is the normally used one.

             If you have reversed the sidebands a flashing up arrow  will
             be displayed.

             If you set your transceiver to LSB you will be set correctly
             for all modes.

             For CW operation you may set your rig to the CW position and
             ignore the sideband setting.  If you use FSK just set it  so
             that it works for you.

             18.12 Shift/Baudrate Control keys

             The  following keys are used to control the Shift  (Wide  or
             narrow) and the Radio link baudrate in the BAUDOT and  ASCII
             communications    modes.    In   the   BAUDOT   and    ASCII
             communications modes all baud rates supported by the  PK-232
             may be selected.

                  18.12.1 RIGHT ARROW speeds up the baud rate.
                  18.12.2 LEFT ARROW slows down the baud rate.
                  18.12.3 UP  ARROW toggles the shift from Wide (850  Hz)
                          to Narrow (170 Hz) and back.
                  18.12.4 DELETE toggles the USOS command (RTTY only).

                  The  state of each of the above commands are  displayed
                  in the status window at the top of the screen.  If USOS
                  is active, 'USOS' will be shown.  The shift is shown as
                  'W' or 'N' for wide or narrow respectively.

             18.13 Control Z (^Z)

             This key is used in the Packet communications mode to signal
             the  end  of a file or message, when loading  messages  into


        LAN-LINK.DOC (c) G3ZCZ 1988





        LAN-LINK VERSION 1.50  PAGE 45


             another  LAN-LINK  system  or  into a  BBS.   In  the  AMTOR
             communications mode, it is automatically translated into the
             sequence  ' :EOF: +? ' which can be used as a fast  break-in
             changeover or to terminate a message being stored in another
             LAN-LINK AMTOR mailbox.

        19.0  LAN-LINK disk files

        The following disk files are associated with the program.

             19.1  LAN-LINK.EXE

             This is the program.  You activate it from DOS by typing the
             word  LAN-LINK  followed by ENTER in the  normal  manner  of
             invoking DOS commands.

             19.2  LAN-LINK.SYS

             This  file contains the configuration information  for  both
             the  program and the TNC.  YOU MUST EDIT IT before  you  run
             the  program  on  the air the first  time.   Use  your  word
             processor  in  the NON-Document mode.    There  are  several
             things which you can customize according to your preference.
             YOU  CAN USE OPTION 'F' IN THE PARAMETERS MENU TO CHECK  THE
             DEFAULTS.

             The  first  few lines of the default file together  with  an
             item number are shown below.

             1.   G8BTB
             2.   GBTB
             3.   CQ, This is G8BTB/W3 (Silver Spring) Md. calling.
             4.   2
             5.   10
             6.   4
             7.   1
             8.   1
             9.   KAM
             10.  1200
             11.  LAN-LINK.LOG
             12.  LAN-LINK.RUN
             13.  LAN-LINK.DIR
             14.  LAN-LINK.TXT
             15.  Mail
             16.  1
             17.  1
             18.  0
             19.  8
             20.  0
             21.  1
             22.  1
             23.  \LAN-LINK\FILES\
             24.  RM
             25.  AMSAT
                  ARRL


        LAN-LINK.DOC (c) G3ZCZ 1988





        LAN-LINK VERSION 1.50  PAGE 46


             26.  * end of Scan Words, start of defaults

             Consider the function of each line in turn.

             19.2.1 Full callsign.

             The  first line  contains your callsign.  Please do not  use
             G8BTB.  Replace G8BTB  with yours.  You may use / characters
             if you wish.  This is the call sign that will be used in the
             non- Packet modes.  You may thus use "portable  designators"
             such  as G3ZCZ/A, G3ZCZ/W3 or G3ZCZ/4X, which you cannot  do
             in Packet.

             This is the call that will be monitored for in the  Digipeat
             monitoring  mode.  In this mode which is toggled on and  off
             by the Alt F key, if someone uses you as a digipeater  while
             you  are  not connected to anyone else, the  event  will  be
             logged  to disk.  This mode will only work if your  callsign
             as  stored in this line is a valid (uppercase  only)  packet
             callsign.

             For  example, in the PK-232, if the callsign is  G3ZCZ  then
             the  sequence >G3ZCZ> will be recognized as a  digipeat  and
             the  event logged.  Thus 4X6AA*>G3ZCZ>4Z4ZB would be  logged
             as a digipeat event.

             If you have a / character in your callsign, and use the base
             call  for  packet identifying the location in the  CQ  text,
             then  the  function  will work if you  place  the  "portable
             location" as a suffix.  For example, if the call is G3ZCZ/4X
             and  the packet identification is G3ZCZ, then  the  digipeat
             monitor  will work. If the call was entered as 4X/G3ZCZ  the
             digipeat monitor would check for 4X and would not appear  to
             work.

             Store  your callsign using UPPERCASE characters if you  want
             the DIGIPEAT DETECT option to work (IE. G3ZCZ).  If you  use
             lower  case (ie. g3zcz), recognition will never take  place.
             The TNC automatically converts case to upper case in the non
             packet communications modes.

             If  you  are  using an SSID (e.g.  G3ZCZ-8)  in  the  packet
             communications  mode,  you  should  enter  the  whole   call
             INCLUDING the SSID.

             19.2.2 The SELCAL.

             The  second  line contains the AMTOR SELCAL  configured  for
             your  callsign.  You use it again later to tell  the  PK-232
             what the SELCAL is.  This line just tells it to LAN-LINK.

             If you are not using a PK-232 or KAM, the line must still be
             there.




        LAN-LINK.DOC (c) G3ZCZ 1988





        LAN-LINK VERSION 1.50  PAGE 47


             19.2.3 The CQ Text.

             The third line contains the line of text transmitted by  the
             PK-232 in a CQ call (in any mode except for MORSE). Think of
             this message as a CQTEXT line.  Edit this line as well.

             19.2.4 The Default Band.

             The fourth line contains the band information.  The  default
             value  is 2 for 2 Meters.  Use the Meter value for the  band
             to keep the display correct.  It is displayed in the  status
             window.  If you normally operate on another band change  the
             default  value  in the file to reflect your  custom  default
             state.

             19.2.5 The Default Transmitter Power.

             The fifth line contains the value for the transmitter power.
             The  default value is 10 for 10 watts.  It is  displayed  in
             the  status  window.  If your transmitter uses  a  different
             power level change the default value in the file to  reflect
             your custom default state.

             19.2.6 The CQ Delay.

             The sixth line contains a number which tells the program how
             long to wait for a reply before transmitting a CQ call  when
             in the beacon (automatic) mode.  A value of 4 corresponds to
             about 2 minutes.  This value of time will vary depending  on
             the  clock  speed  of  your  computer.   You  may  have   to
             experiment with different values.  A value of 0 inhibits the
             beacon mode.  The maximum value is 255.

             19.2.7 The Message Relay Flag.

             The  seventh  line  configures the  LAN  store  and  forward
             capacity  of  your system also known as  the  Message  Relay
             Capability.   If  it is a 0 your computer  will  not  accept
             messages for forwarding.  If it is a 1, it will accept them.
             See Appendix 2 for details about LANs.

             Remember,  if  you  configure your  computer  to  store  and
             forward  messages,  you have a moral obligation  to  deliver
             them.

             The state of this feature shows up as an [R] in your  status
             display  and in the connect message which is transmitted  to
             the other station at connect time.

             19.2.8 The Communications Port

             This  line  contains the default Communications  port.   The
             default  value is 1. You may set it at any value  between  1
             and 4.



        LAN-LINK.DOC (c) G3ZCZ 1988





        LAN-LINK VERSION 1.50  PAGE 48


             If  you only have one com port, set the 'SYS' file  to  com1
             even  if  your card is configured as  COM2.   LAN-LINK  will
             ALWAYS assume COM1 for a single card.

             19.2.9 The TNC type.

             This  line tells the program which TNC you are  using.   The
             PK-232 command set is slightly different to those of TNC2 in
             the packet mode and is very different to those of the KAM in
             the  non packet modes.   Thus the command dialog has  to  be
             changed  somewhat to make the 'SOLO, TRAFFIC, CQ/BEACON  and
             MAIL' terminal modes work correctly for different TNC's.
             Valid TNC's are PK232
                             KAM
                             KPC
                             TNC1
                             TNC2          (don't type the '.').

             The  TNC2  used to test LAN-LINK was an MFJ  1270.  The  KPC
             includes  software changeover from HF/VHF.  Most  TAPR  TNC2
             clones should work with the TNC2 setting.

             19.2.10 The Terminal Baud Rate.

             This  line tells LAN-LINK what baud rate the TNC is set  to.
             This is the baudrate on the RS-232 line between the TNC  and
             the computer.  Valid baud rates for LAN-LINK are 300,  1200,
             2400, 4800, 9600 and 19,200.  If you specify something  else
             LAN-LINK will default to 1200.

             If the TNC does not use an interrupt driven serial port  you
             may  experience problems when using baud rates greater  than
             1200.  The PK-232 does not like baud rates faster than 2400,
             and  sometimes  not even that. The PK232 seems to  drop  the
             first  character  of some lines at 4800  bauds.    Use  1200
             until  you have tested and are sure that a faster  one  will
             work.

             This program has been tested on a TNC2 using a terminal baud
             rate  of  9600 bauds and worked correctly.   it  also  works
             correctly on a KAM at 2400 Bauds.

             19.2.11 Logbook File.

             This  is  the name of the file to be used as  your  logbook.
             The default name is LAN-LINK.LOG.

             19.2.12 Capture to Disk File

             This  is the name of the file used to capture incoming  text
             to disk. The default name is LAN-LINK.RUN.

             19.2.13 Call Directory File.

             This  is the name of the file used as your  call  directory.


        LAN-LINK.DOC (c) G3ZCZ 1988





        LAN-LINK VERSION 1.50  PAGE 49


             The default name is LAN-LINK.DIR.

             19.2.14 Brag Tape.

             This  is  the name of the file used as  your  bragtape.  The
             default name is LAN-LINK.TXT.

             19.2.15 Mail_Snatch Trigger Word.

             You can set the mail snatch trigger in the BBS Mail  beacon.
             Most BBS's use word 'Mail' and a string of calls to indicate
             the presence of messages.  If your BBS uses something  else,
             you may customize LAN-LINK on this line to tell it what word
             your BBS uses.

             Note  that  if your BBS uses 'QTC' you may  end  up  calling
             yourself  if you disconnect while traffic is flowing on  the
             LAN.

             19.2.16  The QTC _Snatch or Automatic Connect Attempt Flag.

             If  the  value  entered  on  this line  is  a  1,  then  the
             QTC_Snatch  Flag is enabled.  if the value on the line is  a
             0, then the flag is disabled.

             If  the  QTC_Snatch  flag is  enabled,  LAN-LINK  scans  the
             contents of packets appearing in the Inwindow on the  screen
             while the terminal is disconnected.  Should it recognize the
             three text strings 'LAN-LINK',  ':QTC:', and 'your callsign'
             in  the contents of a packet, it will then issue  a  connect
             request to the callsign of the LAN-LINK station that origin-
             ated  the beacon transmission.  If the connect is made,  the
             other station will send you the message automatically  which
             LAN-LINK will "capture to disk".  The connect will time  out
             and terminate a few minutes later.

             The  normal  connect  request will be  made  DIRECT  to  the
             station.  If you expect messages from stations you can  only
             connect  with via a digipeater, place the path in your  LAN-
             LINK.DIR  directory file.  It should be there anyhow if  you
             connect  to  the  station regularly.  For  example,  if  you
             expect  messages  from  4Z4ZB  whom you  can  only  work  if
             digipeated via 4X1AA then place an entry like

             4Z4ZB   4Z4ZB V 4X1AA

             in the LAN-LINK.DIR  file.

             The  QTC_Snatch  leaves  your messages  in  a  message  file
             <yourcall.OUT>.   It  is  triggered by the first  >  in  the
             initial  connect response of LAN-LINK 1.50R> (note the  '>')
             and  terminated by the 'over' at the end of the message  ie.
             G3ZCZ/W8>  (note the '>'). If you train stations  not  using
             LAN-LINK  who  want to leave you messages  to  trigger  your
             QTC_Snatch, by transmitting the following unaddressed packet


        LAN-LINK.DOC (c) G3ZCZ 1988





        LAN-LINK VERSION 1.50  PAGE 50



             'LAN-LINK :QTC: YOURCALL',

             your  system will connect to them.  (For example to leave  a
             message for me, they would send

             'LAN-LINK :QTC: G3ZCZ '

             as  an  unaddressed  packet  [in  converse  mode  when   not
             connected, or in their beacon text].)

             If they then send you a '>' on a line by itself, followed by
             the  message itself, and terminated by an other '>'  as  the
             last  character  of the line, the message will end up  in  a
             message  file rather than in the LAN-LINK.RUN file  and  you
             can  scan  it  fast using the Alt M key.   It  goes  without
             saying  that the message itself should not contain  the  '>'
             character.   If  it does,by the way, the first part  of  the
             message  will  be in the message file, while  the  remainder
             will be in the LAN-LINK.RUN file.

             19.2.17 The BBS_MAIL_Snatch flag.

             This   line   controls   the   BBS_Mail_Snatch.    If    the
             BBS_Mail_Snatch  is  enabled,  when a  BBS  sends  a  packet
             announcing 'Mail', if your callsign is in the first line  of
             that  message, LAN-LINK will issue a connect request  (again
             via the path in LAN-LINK.DIR) to that BBS.  When  connected,
             it will act as if you have initiated a ZapBBS command.   The
             Zap counter will be incremented each time a  BBS_Mail_Snatch
             takes place.

             Set this line as follows,  0 = Disabled, 1 = Enabled.

             19.2.18 Flag for Shut Down.

             You  may customize the shut down sequence of the  TNC.   You
             have  the  choice  of QRT, QRV and QRV  +  CTEXT  Toggle  as
             described in the following sections.

             Set  this line as follows, 0 = QRT, 1 = QRV 2 = QRV  +  CMSG
             toggle..

                  19.2.18.1 QRT

                  Turns the TNC into a VHF Digipeater and turns CONOK OFF
                  (CFROM NONE for the PK-232).  In this condition the TNC
                  will reject connect requests.

                  19.2.18.2 QRV

                  Allows you to stay alive on turnoff. It will send
                  MON OFF (MON 0 for the PK-232)
                  ^S
                  to  the  TNC at shutdown without  touching  CONOK/CFROM


        LAN-LINK.DOC (c) G3ZCZ 1988





        LAN-LINK VERSION 1.50  PAGE 51


                  {PK-232}, and
                  ^Q
                  at  turn  on.  You will then  have  to  initialize  the
                  terminal  and  communications mode after  reading  your
                  mail.   Connects should then be logged at the time  you
                  read the mail, not at the time they took place.

                  19.2.18.3 QRV + CTEXT TOGGLE

                  This  is the same as the QRV state but CMSG is  toggled
                  on/off.  When stations connect to you while LAN-LINK is
                  active, they will not receive the CText message.   When
                  other  stations  connect to you while LAN-LINK  is  not
                  active, they will receive the CText message

             19.2.19 TNC Data Bits

             You  can  set  the number of data bits on  the  RS-232  line
             between the computer and TNC to 7 or 8.  Use 7 with a TNC  2
             if you have problems with greek characters.

             Set this line to either 7 or 8.

             19.2.20 TNC Parity

             Use  this  line  to set the Parity bit on  the  RS-232  line
             between the computer and TNC as described below.

              0 = None, 1 = Odd, 2 = Even, 3 = Mark, 4 = Space.

             19.2.21 Number of TNC Stop Bits

             You  can  set  the number of stop bits on  the  RS-232  line
             between  the computer and the TNC to 1 or 2.  Use 1  at  all
             terminal (not packet) baud rates except 300.

             Set this line to 1 or 2.

             19.2.22 DCD Status Bit.

             If you are using a KAM or a PK-232 then this line should  be
             set to 1.  If you are using another TNC, if you can set  the
             TNC so that pin 8 on the RS-232 interface changes state when
             connected, do so and set this line to 1.  If you can't, then
             set this line to 0.  If this line is 0, the multiple connect
             modes  will  not work so don't attempt to invoke  them.   If
             this  line  is  o,  the  words  '***  CONNECTED'  and   '***
             DISCONNECTED'  when  seen  in the  LAN  may  cause  spurious
             apparent connects and disconnects in LAN-LINK.

             Set this line to 0 = not connected, 1 = connected.

             19.2.23 QBM Download Directory.

             This is the directory the :QBM: command will search to  find


        LAN-LINK.DOC (c) G3ZCZ 1988





        LAN-LINK VERSION 1.50  PAGE 52


             a  file  to  be  downloaded.  The  default  value  is  \LAN-
             LINK\FILES.  Set them up using DOS.  If you are using a hard
             disk, put LAN-LINK in a LAN-LINK subdirectory.

             19.2.24 Read Request Command.

             This is the command LAN-LINK issues to the BBS during a  Zap
             sequence to request your mail.  The default value is RM  for
             Read  Mine.  On a WA7MBL BBS you may change it to VM  for  a
             Verbose Read of the full packet headers.  On a W0RLI BBS you
             may change it to RN to only request new messages.  If you do
             change it, use the 'F' option in the Parameters Menu to make
             sure  it  is  correct.  If it isn't  correct,  the  Zap  BBS
             feature will not work,

             19.2.25 Scan Words.

             In  the ZAP BBS feature you can now ask the program to  scan
             the  lines read from the BBS and if it sees any of the  scan
             words in the line, it will queue a request for that bulletin
             by  number.  You can only set 10 such Scan words (should  be
             enough) and request up to 63 messages/bulletins at a time.

             NOTE  that  words that show up in the BBS  prompt  line  are
             ILLEGAL.  For example if your BBS prompts you with

             N4QQ BBS>

             then 'N4QQ' and 'BBS' should not be used as Scan Words.

             19.2.26 * marks end of list    ****************************

             This line marks the end of the list of Scan words.

             19.2.27 The Remaining lines.

             The  remaining  lines  contain commands  to  the  TNC.   For
             further  information  about them refer to  the  TNC  manual.
             LAN-LINK  assumes  different defaults in some  instances  to
             those set in the TNC.  The SYS file contains only those that
             are different to the TNC default reset state.

             NOTE: If you are not using a TNC1 you MUST set the  HEADERLN
             parameter  to  ON.  The packet headers and the text  of  the
             packets must show up on your screen on separate lines.   You
             must  also have the "Echo as Sent" feature set ON ('EAS  ON'
             for PK-232 and 'XM' ON ' for the KAM).

             19.3  LAN-LINK.RUN.

             This file contains incoming data from the TNC recorded while
             the  'capture to disk' function was active.  You may  change
             the  default name of the 'capture to disk' file in the  LAN-
             LINK.SYS file.



        LAN-LINK.DOC (c) G3ZCZ 1988





        LAN-LINK VERSION 1.50  PAGE 53


             19.4  LAN-LINK.LOG.

             This  file  contains the log entries.  It  will  be  created
             automatically  to  initialize  the  logging  function.   The
             format  of the logbook file is the same as that  created  by
             the  G3ZCZ CONTEST.BAS REV 2 program and is designed  to  be
             appended  into the G3ZCZ LOGBOOK DATABASE package  presented
             as part of the PC-HAM software package.  It should be edited
             with a word processor in the non document mode to delete the
             first  line and clean it up before the file is  appended  to
             the DBASE logging package data files.

             19.5  LAN-LINK.DIR.

             This  is the directory file as described in  Section  6.1.2.
             You  use it to store connect, NET/ROM, KA-Node  or  digipeat
             paths as well as name/callsign relationships.

             Examples are
             Joe  G3ZCZ
             Alon 4Z4ZB V 4X6AA
             Milt 4X6AA
             LR   4X6LR
             hf-il 4x4hf v 4z4zb 4x4il
             hf-rj 4x4hf v 4z4zb 4z4rj

             You  create  this file with your word processor in  its  non
             document mode.  You must leave AT LEAST one space  character
             between the first (key) word and the connect path.  When you
             type in the key word, the program does not care about  upper
             or lower case.  You may also use the 'reMember Path'  option
             in the Call Menu to make entries in this file.

             If  you already have a YAPP.DIR file just rename it to  LAN-
             LINK.DIR and add the NET/ROM and KA-Node paths.

             NOTE:  All path entries in LAN-LINK.DIR must be on a  single
             80 column line.

             19.6  CONFIG.SYS.

             You must have a CONFIG.SYS file on the boot disk if you  are
             going  to  use the disk logging features.   This  file  must
             contain the line
             FILES = 20
             See the DOS manual for more information about the CONFIG.SYS
             file.

             19.7  *.MBX.

             These  are the files associated with the stations  you  have
             designated as LAN store and forward mailboxes.  Thus if  for
             example  you  want  to  use 4Z4ZB as  a  store  and  forward
             mailbox,  you  will  have to create  an  ASCII  file  called
             4Z4ZB.MBX   using  the  non-document  mode  of   your   word


        LAN-LINK.DOC (c) G3ZCZ 1988





        LAN-LINK VERSION 1.50  PAGE 54


             processor.   In  this file you will put a list of  the  call
             signs of the stations 4Z4ZB can connect to reliably.  If for
             example you want 4Z4ZB to be able to store messages from you
             to 4X6AA, 4X6LR, G3ZCZ, ON8IK, F0WN,and G8BTB, you would put
             those call signs in the file, one call on a line as follows.

             4X6AA
             4X6LR
             G3ZCZ
             ON8IK
             F0WN
             G8BTB

             When  the QRU function is invoked either by you manually  or
             by 4Z4ZB connecting to you and sending you the command :QRU:
             ,  any messages present on your system addressed to  any  of
             those  stations  (E.G.  G3ZCZ.OUT  and  ON8IK.OUT)  will  be
             transferred  from you to 4Z4ZB just as if you had  tried  to
             QSP  the  messages  manually or as if G3ZCZ  or  ON8IK   had
             connected  directly to you.  The file names will be  changed
             to *.OLD.

             You  must  create  one file for each  designated  store  and
             forward station, ie. 4Z4ZB.MBX, G3ZCZ.MBX etc.

             19.8  *.BBS.

             These are BBS AUTO-Upload Command files.

             Each file is named for the callsign of the BBS that you wish
             to access.  It must have exactly the name as the callsign of
             the  BBS.  Thus if the BBS is W9TTN-1 the name of  the  file
             must  be W9TNN-1.BBS, or if the BBS is 4Z4ZB then  the  file
             must  be called 4Z4ZB.BBS.  The file must be an ASCII  file.
             That  means  the  word processor must be used  in  the  non-
             document mode to create it.

             This file contains the command sequence that you would  have
             typed  at  the  keyboard  if  you  were  accessing  the  BBS
             manually.  The ONE difference is that the text of a  message
             (you  are uploading with the S command must be  followed  by
             the   character  string  :EOF:  (on  a  separate  line)   as
             illustrated by the example below.

             The BBS 'S' command (including its variations such as  'SP')
             is the only multiple line command allowed.  You can thus put
             all  the single line commands such as H, ?, L, and R in  the
             command file.

             A  'multiple  command'  is defined in  this  instance  as  a
             command which allows you to enter multiple lines before  the
             BBS  will  send back a '>' character (IE one  that  the  BBS
             tells you to type in text and terminate it with the  Control
             Z character).



        LAN-LINK.DOC (c) G3ZCZ 1988





        LAN-LINK VERSION 1.50  PAGE 55


             The  contents of A TYPICAL *.BBS file are shown below as  an
             example.

             k 1234
             s g8btb
             Test Message
             This is a test message.
             :EOF:
             sp G3ZCZ @ N4QQ
             Greetings
             The text of this message is greetings from LAN-LINK.
             :EOF:
             lm
             r 567
             r 593

             NOTE: the 'K 1234' command was used to delete a message that
             had  already  been read. If you use 'KM' as you  may  delete
             mail BEFORE reading it.   The outgoing mail was placed  next
             in  the  file  in case of an abnormal  disconnect.   The  lm
             command  was used to record the message numbers, and to  see
             what  old messages were still present on the BBS.  Lastly  a
             list  of messages to be read was included (the  numbers  had
             been recorded in the last BBS_Mail_Snatch).  There were also
             no blank lines in the file.

             Each  message  ended with the :EOF:  character  string,  but
             there was no need for any special end of BBS file character.

             In the event of a BBS Mail_Snatch, if the *.BBS file  exists
             for  that BBS, the file will be processed and  the  contents
             sent.   Thus  if you don't get a chance to  send  the  mail,
             before  LAN-LINK  downloads the mail from the BBS,  it  will
             send it for you.

             When the BBS has accepted the commands the name of the  file
             is changed from *.BBS to *.OLD ( IE. the file name  KE8X.BBS
             is changed to KE8X.OLD).

             In the real world however, message formats are non standard,
             and  can  contain  any set  of  characters.   The  algorithm
             developed  here  transmits the next line in the  *.BBS  file
             when LAN-LINK see's a 'trigger' character_string unless  one
             of the 'inhibitor' character_strings is also present on  the
             line of the message text received by LAN-LINK.

             These  'trigger'  character_strings  are '>'  (as  the  last
             character  of the line of text ), 'Enter', 'Subject',  'Sj:'
             and 'Msg:'.  The 'inhibitor' character_strings are 'R:', '<'
             and 'Message'(R: as in routing headers and < and Message  as
             in Message-Id: <message number> in message headers).

             This should cover most simulated manual BBS message  reading
             (WA7MBL and W0RLI/VE3GYQ) and avoid false triggering due  to
             '>'s showing up in message and routing headers.


        LAN-LINK.DOC (c) G3ZCZ 1988





        LAN-LINK VERSION 1.50  PAGE 56



             NOTE than when LAN-LINK finishes processing the *.BBS  file,
             it  will  send  a 'B' command to the BBS  to  terminate  the
             session.  This feature is designed to minimize the time  you
             spend  connected  to  the BBS by allowing you  to  scan  the
             message list when automatically receiving your mail, prepare
             your  replies and download requests off-line and then  later
             read  the  incoming messages or files without tying  up  the
             BBS.  It thus positively disconnects you from the BBS.

             NOTE:  If you upload the 'KM' command from your *.BBS  file,
             you  may  delete messages before reading  them.   Do  delete
             'read'  mail  from your local BBS.  Don't clutter  his  disk
             with your read mail. The 'LM' command is built into LAN-LINK
             to remind you of what you have out there.

        20.0 Mailbox features

        This section describes the mail box and message handling features
        built into LAN-LINK.

             20.1 Answering Machine.

             LAN-LINK  contains an AMTOR (Robot beacon CQ mode only)  and
             PACKET  mode   SMART "answering machine" facility.  You  can
             leave  messages on your disk (in the same directory  as  the
             LAN-LINK.*  files,  if  you  are using  a  hard  disk),  for
             different  stations.  When someone connects to you,  if  you
             left  a message for him, he (or she or even it as  the  case
             may be) and only that station will receive it automatically.
             No one else will normally be able to download that message.

             20.2  Mail Beacon (Annunciator).

             To ensure that people know that you have left a message  for
             them a 'MAIL for' list is loaded into your Packet Beacon and
             transmitted every 30 minutes (Refer to the BTEXT command  in
             the TNC manual) as  ':QTC:' followed by a list of calls.  If
             no  mail is pending, or the only message in your  system  is
             one   addressed  to  you,  the  beacon   transmissions   are
             inhibited.   This  conforms to good  operating  practice  on
             crowded channels (at least inhibiting the beacon does).

             The mail beacon in the AMTOR mode is transmitted as part  of
             the beacon autocq message.  It is automatically updated when
             a message is transmitted.  If you don't set the beacon  (see
             below)  you  will not transmit a mail beacon  text  in  your
             AMTOR CQ message.

             The  Mail  beacon text is set up either when  you  tell  the
             computer  to set it up or when you disconnect a  packet  QSO
             from another station.

             In this manner you may update the list while the program  is
             running,  for example by using Sidekick to write a  message,


        LAN-LINK.DOC (c) G3ZCZ 1988





        LAN-LINK VERSION 1.50  PAGE 57


             or preferably the NOTE feature.

             Any   station   using   LAN-LINK  can   be   configured   to
             automatically  attempt  a connect (QTC_Snatch)  when  seeing
             their callsign in someone else's LAN-LINK :QTC: beacon  mail
             message list.

             If  for some reason the message got lost (e.g.  because  the
             link  was  marginal), :QSM: will get you a  repeat  of  that
             message.

             20.3  How to leave a message.

             You  can use the note feature or type the message as a  non-
             document  file  on  Wordstar, or if  you  use  another  word
             processor, you must leave the message as an ASCII text file.

             If  you  use the Note feature, the message will be  given  a
             header  as  if it came in from someone else.  if you  use  a
             word processor to write the message, you will have to  write
             in a header or show somehow that the message is not  'live'.
             You  may  then later time tag a message  header  on  message
             files  created  by the word processor.  In this  way  people
             will  realize that it is an automatic message by seeing  the
             header.  On the other hand, you may wish to fool people into
             thinking that you are home.

             You  just  name  the message file as  the  callsign  of  the
             station  to whom you wish the message to be sent at  connect
             time.  You must also give it the filetype of 'OUT'.

             For example a message for G3ZCZ would be stored on the  disk
             as  a  file named 'G3ZCZ.OUT', and similarly  a  message  to
             4X6AA would be stored on disk as '4X6AA.OUT'.

             Once the message has been sent, an entry to that effect will
             be made in the LAN-LINK.RUN  data capture file. The  message
             file  will  then  be renamed and given  the  file  extension
             '.OLD'.  At that time any previously existing mail file with
             the  file extension '.OLD' will be deleted.  This stops  the
             addressee  receiving the message on successive  connects  if
             you  can't delete it for some reason (you forget)  while  at
             the same time, the message is still available to you in case
             you need it.

             You  should use a separate utility program if you  want  the
             calls  in the mail beacon sorted.  You may for example  wish
             to  sort them alphanumerically or in the order of  the  date
             that they were left in your answering machine.

             Incoming  messages triggered by the QTC_Snatch will be  left
             in  a message file ( <yourcall.OUT> ), which can be  scanned
             by  using the Alternate 'M' function key.  If you  have  non
             LAN-LINK  friends, train them to trigger the  QTC_Snatch  by
             simulating  a beacon, and pre-fixing and ending  their  text


        LAN-LINK.DOC (c) G3ZCZ 1988





        LAN-LINK VERSION 1.50  PAGE 58


             with lines containing the '>' as the only character.  Better
             yet, give them a copy of LAN-LINK and tell them to  register
             it.

            20.4 Remote Beacon shutdown.

             I recognize that some stations may abuse the beacon facility
             of  this  program.  I have thus built  into  the  program  a
             'remote  shutdown' capability.  If someone running  LAN-LINK
             has their beacon timer set too often, connect to them in the
             AMTOR   or  Packet Communications modes, and  tell  them  to
             :QRT:  which will clear their beacon mode and take them  off
             the air for a while at least.

             In  the  Packet communications mode, the CQ beacon  is  shut
             down  but the 30 minute mail beacon is not touched.  In  the
             AMTOR communications mode, the CQ delay time is set to  255.
             The  Mailbox  will thus still be active in both  modes,  but
             will not beacon on the air at the frequency it was set at.






































        LAN-LINK.DOC (c) G3ZCZ 1988





        LAN-LINK VERSION 1.50  PAGE 59


        APPENDIX 1. ANOMALIES (and BUGS)

        A1.1 Since  the Program has no way to check the  command/converse
             mode  status of the TNC, you may see various Cmd: and  error
             messages  from the TNC when using the menus or function  key
             commands.   Ignore  them  for  now.  If  you  get  an  error
             message, try using the function key again.

        A1.2 In the AMTOR Beacon CQ mode, if the other station drops  the
             link  while you are recording the text, BEFORE the  callsign
             has been recognized as a valid callsign, LAN-LINK will  time
             out  before logging the QSO and restarting the CQ  sequence.
             If  someone else calls in before the time-out has  occurred,
             the text from both stations should be captured to disk,  but
             the  log  entry may not show both stations, thus  the  'LOG'
             must be compared with the 'RUN' file for QSO purposes.

             LAN-LINK  in  the  Beacon/Mailbox mode,  normally  logs  the
             contact  at the end of the line in which it  recognized  the
             callsign as a valid callsign.

        A1.3 In  the AMTOR Beacon CQ or Mailbox mode, if another  station
             sends a +? in the FEC mode, the beacon will attempt to  send
             the  LAN-LINK.TXT  file.  The PK-232 however is not  in  the
             converse  mode at that time and will interpret the  text  of
             the  file  as  commands.   If  by  some  chance,  the   text
             corresponds  to a valid command the PK-232 will  execute  it
             and  put  the  PK-232 in an unknown state and  you  may  not
             notice  that  it did.  As such I recommend  that  the  first
             character  of  each line in the file LAN-LINK.TXT be  a  non
             valid command character such as a number or a period (.)  or
             another punctuation sign.

        A1.4 If  you are using a CGA card with a monochrome monitor,  the
             text  you type into the OUTWINDOW will be fainter  than  the
             incoming  text.  This is because it is set to  light  green.
             If  you  are using a Hercules compatible card you  will  not
             notice any difference.

        A1.5 The  conference  mode has been tested on a  PK-232,  KAM,  a
             SANYO MBC-675 which has a clock speed of 4.7MHz and other PC
             clones with faster clock speeds.  If you have problems  with
             intermittent selection of IO channels try slowing down  your
             CPU  clock.  There is a software delay loop in  the  program
             that  is  used to allow the TNC time to  switch  IO  streams
             after  receipt of the stream change command.  This delay  is
             there  because LAN-LINK tests for a connect on each  channel
             before  outputting  any  text,  so that  it  does  not  send
             unaddressed packets on non connected IO channels.

        A1.6 A  Packet conference Mode disconnect returns the TNC to  the
             command  mode, even if you remain connected to one  or  more
             other stations.




        LAN-LINK.DOC (c) G3ZCZ 1988





        LAN-LINK VERSION 1.50  PAGE 60


        A1.7 Strange Events.

             If the TNC does not use an interrupt driven serial port  you
             may  experience problems when using baud rates greater  than
             1200.  The PK-232 DOES NOT LIKE LAN-LINK to use RS-232  baud
             rates  faster than 2400, and sometimes not even  that.   Use
             1200  until YOU have tested and ARE SURE that a  faster  one
             will work.

             IF  YOU  HAVE ANY STRANGE PROBLEMs AND ARE USING  an  RS-232
             TERMINAL  BAUD RATE to the TNC WHICH IS GREATER  THAN  1200,
             set  the Terminal Baud Rate to 1200 and see if  the  problem
             goes away.

        A1.8 *** DISCONNECTED

             In the Packet communications mode, when you are connected to
             someone and the TNC sends this text string to the  computer,
             LAN-LINK thinks you have been disconnected and resets.  This
             normally  only  happens  when  a  true  disconnect   occurs.
             However, if the text shows up in the middle of a line  being
             sent to you, it WILL HAVE THE SAME EFFECT AND THINK THAT YOU
             HAVE DISCONECTED if the DCD_Flag is not set in the SYS file,
             and the TNC does not use the DCD signal on pin 8 of the  RS-
             232 interface.

        A1.9 *** CONNECTED

             In  the Packet communications mode, when you are  monitoring
             traffic on the LAN someone sends this text string,  LAN-LINK
             thinks you have been connected if the DCD_Flag is not set in
             the SYS file, and the TNC does not use the DCD signal on pin
             8 of the RS-232 interface.

        A1.10 Greek Characters and other garbage in the Incoming Screen.

             If  you  see  greek characters in the  Incoming  screen  you
             probably  have the wrong parity set in the TNC.  first  make
             sure  that the RS-232 baud rate is correct.  If it is,  take
             the  batteries out of it and reset it.  If that fails,  play
             with  the parity.  LAN-LINK sets the serial port to 8  bits,
             no  parity.   If  you still can't get it to  work,  set  the
             interface to 7 bits in the SYS file.

        A1.11 Dumb TNC

             If  the TNC seems to respond to commands but is not  sending
             anything  back, you may have one of two problems.   You  may
             have  a bad RS-232 cable with on wire disconnected.  If  the
             computer  can  operate  the TNC  in  another  communications
             program, try to reset the TNC, take the batteries out,  etc.
             You may also have a not-so-compatible PC.





        LAN-LINK.DOC (c) G3ZCZ 1988





        LAN-LINK VERSION 1.50  PAGE 61


        APPENDIX 2. Local Area Network Capability

        VHF  Packet  radio systems can be considered as part of  a  Local
        Area  Network (LAN) in which messages can be left by one  station
        in the computer belonging to a second station.  At HF the same is
        true,  but the area becomes greater.  The basic problem  here  is
        that  people  can only send and receive messages to or  from  you
        when you are on-line.  To compensate for this, BBS stations  were
        developed which allowed both messages and bulletins to be  stored
        by anyone for later retrieval.

        LAN-LINK  allows you to store messages in your computer so as  to
        use  it  as  an  automatic answering  machine.   By  storing  the
        messages in a file called by the name of callsign, with the  file
        extension  '.OUT',  anyone connecting to the  computer  will  get
        their  message  without  having to request  it.    LAN-LINK  also
        extends  that concept to cover the eventuality of you wanting  to
        take  your computer off-line for some reason.  You may  now  load
        the  message  into any other computer you can  connect  to  using
        elements  of  the  Q  code adapted  to  the  High  Level  Network
        Communications  Language (NC/L) proposed in my book Software  for
        Amateur  Radio, (Book number 1560) published by TAB  Books,  Blue
        Ridge Summit, Pa. 17214 U.S.A.

        A2.1 LAN Protocol (G3ZCZ Version)

        The  protocol  is as follows. When connected to someone  who  has
        their  LAN-LINK  configured  as a host, if you want  to  store  a
        message  you send the following instruction to the other  station
        :QSP:  <callsign>  where  <callsign> is the call of  the  station
        that the message is for, not the callsign of the host station  in
        whose  computer you are storing the message. [Note use  only  one
        space  character  after  the :QSP:].  LAN-LINK  sends  the  :QSP:
        message automatically using QSP option in the Message Menu.

        For  example if you want to store a message for 4Z4ZB in  4X6AA's
        computer  which is configured as a Store and Forward system,  you
        would first connect to 4X6AA and then send the command as

                   :QSP: 4Z4ZB .

        Better  still use QSP option in the Message Menu to automate  the
        sequence.

        The computer at 4X6AA will respond either with a statement saying
        that  it is ready for you to go ahead, or send a  message  saying
        that  it can't comply.  If it is ready you get a  positive  reply
        which will take the form :QRV:  <callsign> which if you know  the
        Q code, means " I am ready to accept a message for  <callsign>".

        At this time you may go ahead and send the message.  If you  type
        the message at the keyboard, you may use either a control Z  (^Z)
        character or the character sequence :EOF: followed by a  carriage
        return  (the  ENTER key) to terminate the message.  If  you  have
        first  written the message into a text file you may then send  it


        LAN-LINK.DOC (c) G3ZCZ 1988





        LAN-LINK VERSION 1.50  PAGE 62


        using  the  'Send  File'  option  of  the  Files  Menu  and   the
        termination sequence is automatic.

        Once  you have completed the message, the other  (host)  computer
        will  either reply that the message has been successfully  stored
        or give you an error message.

        If  the  message  is stored and ready to be sent  next  time  the
        addressee  connects  to that computer, you will see  the  message
        :QSL: on your screen.  If something went wrong, you will get back
        a  negative message taking the form :QNO: followed by  a  number.
        The number tells you why the operation failed.

        A2.2 Message Format

        The  message is stored just as if you had left it in your  system
        (except that a header is added identifying the time of  reception
        and  the call of the sending station).  It will contain a  header
        showing  the  date and time it was received  and  your  callsign.
        Should a message for that station already be in the system, yours
        will be appended to it.  In the event the your upload is aborted,
        the  amount  of text received before the abort occurred  will  be
        stored as the message.

        When  you  disconnect from the other LAN-LINK host  station,  its
        mail beacon will be updated.

        Once the message is loaded in the host, it can only be deleted by
        the operator of the host station.  When the addressee connects to
        the host and receives the message, the file type will change from
        '.OUT' to '.OLD'.

        A2.3 File Uploading/Downloading.

        There  comes a time when you want to leave a file on your  system
        for someone to download later.  You can do this by using NC/L  to
        control the transfer.  You must leave the file in a  subdirectory
        defined  in  the LAN-LINK.SYS FILE called  \LAN-LINK\FILES.   You
        must first create it if it does not exist.  The station who wants
        the message just asks for it using :QBM: <filename>, note they do
        not  need to use the full subdirectory path.  They  must  however
        leave  a single space character between :QBM: and  the  filename.
        In AMTOR the Mailbox must be turned on for remote functions.

        For  example, you have the latest ARRL DX bulletin, and you  want
        to  pass it on.  You could pass it to selected people by  copying
        the  file to individual messages with the filetype  '.OUT',  e.g.
        4X6AA.OUT, 4Z4ZB.OUT or even G3ZCZ.OUT if you want me to get  it,
        which wastes a lot of disk space.

        On  the  other  hand  you could tell people  that  the  file  was
        available  for downloading, either in the CTEXT  connect  message
        line  which everyone gets when connecting to you  by  configuring
        LAN-LINK accordingly, or in individual ('.OUT') messages.



        LAN-LINK.DOC (c) G3ZCZ 1988





        LAN-LINK VERSION 1.50  PAGE 63


        If you include the following in your CTEXT message

        "ARRLDX.015 now available"

        people will know that to download it, they just have to type  the
        line  ':QBM: ARRLDX.015' (one space character between  :QBM:  and
        the  file name) to get the file.  LAN-LINK is not designed  as  a
        BBS,  however,  if you copy the contents of  the  \LAN-LINK\FILES
        subdirectory  into  a  file called DIR (USE DIR >  DIR  in  DOS),
        anyone  can  get a list of the files you have stored  in  it  for
        downloading by typing :QBM: DIR.  Since they do not get the  real
        directory, just what was in it at the time you copied it into the
        file  'DIR',  you may keep "hidden" files in  this  subdirectory.
        You may thus leave a file for someone to download, tell them that
        its  there  by  leaving  them a  message  (which  they  will  get
        automatically when they connect) and no one else connecting  will
        know that it is there.

        :QDB: allows you to upload text or ASCII files.

        A2.4 Path Determination to a Dx station

        If  you want to establish a digipeat path to a  station  somewhat
        out of your direct range, you need to know which of the  stations
        that you can connect to can hear that desired DX station.  If you
        could  get a call monitored (MH list) from the stations that  you
        connect  to,  you  would be able to see if the  station  you  are
        connected to has heard your desired DX station.

        LAN-LINK  uses  the :QMH: command to request such a  list.   When
        LAN-LINK   receives  a :QMH: command, it drops back  to  the  TNC
        command  mode and issues a 'MH' command to the TNC (except  to  a
        TNC1 which does not support it).  It stores the list received  in
        a  temporary  buffer, and then returns to the converse  mode  and
        transmits the list back to the station it is linked to.

        By  judicious  use  of :QMH: you can  determine  paths  to  other
        stations.   Note however, that just because one station can  hear
        another  station,  it  does not mean that it can  work  it.   For
        example,  the station you are connected to may be using  a  power
        level  of 1 watt or so, while the station 200 miles away that  it
        heard was using 100 watts.  Test the path yourself, or/and  leave
        a message asking how reliable the connect path between those  two
        stations is.

        If  you and a small group use a non standard packet  channel  for
        inter-group  communications, you may also use the :QMH:  function
        to  find  out who the station you are connected with,  has  heard
        recently, when you first sign on the LAN channel.

        APPENDIX 3     BASIC NC/L DICTIONARY

        Messages can be transferred into any other LAN-LINK computer  you
        can connect with using elements of the Q code adapted to the High
        Level Network Communications Language (NC/L) proposed in my  book


        LAN-LINK.DOC (c) G3ZCZ 1988





        LAN-LINK VERSION 1.50  PAGE 64


        Software  for Amateur Radio, (Book number 1560) published by  TAB
        Books, Blue Ridge Summit, Pa. 17214 U.S.A.

        NC/L  command words are summarized in the  following  paragraphs.
        There  is  no command word to request your message.   To  receive
        your  message,  you  do do nothing, you will  receive  your  mail
        automatically  when connecting/linking with a  LAN-LINK  station.
        You cannot normally read messages addressed to another person.

        A3.1 :QBM:

             To download a file, send

                   :QBM: filename.type

             The filename.type is the file you want. For example
                  :QBM: dir
                  :QBM: help
                  :QBM: LAN-LINK.doc

        A3.2 :QDB:

             To upload files to another LAN-LINK system send

                  :QDB: filename.typ

             Files  will be uploaded into the same sub-directory as  LAN-
             LINK, and will have a message header inserted at the top  of
             the  file  to allow the operator to know  who  uploaded  the
             file.  If the operator then wants to make the file available
             for  downloading,  he  or  she can  move  it  to  the  \LAN-
             LINK\FILES sub-directory.  The '.TYP' following the filename
             is optional.

             If  you attempt to upload a file which has the same name  as
             one  that  already  exists on the remote  system,  you  will
             receive a :QNO: 14 'error' message.

                  This command is the reverse of :QBM:.

        A3.3 :QMH:

             To  request a call monitored list ('MH') from  the  LAN-LINK
             station that you are connected with, send

                  :QMH:
        A3.4  :QSM:

             To  request a repeat of a message from a station using  LAN-
             LINK, send

                  :QSM:

             This  command will be valid as long as the host station  has
             not  deleted  the <yourcall>.OLD file on his disk.   If  the


        LAN-LINK.DOC (c) G3ZCZ 1988





        LAN-LINK VERSION 1.50  PAGE 65


             file  does  not exist, you will receive a  :QNO:  2  'error'
             response.

        A3.5  :QSP:

             To leave a message, send

                  :QSP: callsign

             the  callsign  is that of the station you wish  to  leave  a
             message for.

        A3.6 :QRT:

             To  shut  down an AMTOR/Packet mode  Mailbox/beacon  station
             which  is  causing QRM, link or connect to the  station  and
             send

             :QRT:

        A3.7 :QRU:

             To upload messages from one LAN-LINK/PK232COM (1.38+) system
             to your computer, send

             :QRU:

             You  may only use the QRU function with stations  designated
             as Store and Forward mailboxes.  Put a list of stations that
             you can connect to reliably in your <callsign>.MBX file  and
             send  it to other stations in your LAN also using  LAN-LINK.
             They  will then be able to dump their mail messages  on  you
             and  you  on them. If they do the same and  send  you  their
             file,  then you will be able to send messages via  them  for
             stations that they can work.

             While  QRU gives you the capability to bulk upload  messages
             to  another station in your local area, when you  take  your
             machine  off line, it may also be used to transfer  messages
             between two LANs via well sighted gateway digipeaters.

        A3.8  :QNO:

             'NO' or error number is a response to a request.

             The  following  error numbers are  associated  with  message
             store and forward operations.

             ?    What you typed was not an NC/L command.
             1    Computer not configured as Store and Forward system.
             2    Requested ASCII file/ message (:QBM:) does not exist.
             3    You made an error in the name of the callsign for  whom
                  the  message  is  intended  (It  must  be  at  least  3
                  characters long).
             4    File creation error in host system.


        LAN-LINK.DOC (c) G3ZCZ 1988





        LAN-LINK VERSION 1.50  PAGE 66


             5    Error occurred during reception and storage of message.
                  Could  be  that the computer ran out of  space  on  the
                  disk,  or  something  else went wrong  in  storing  the
                  message.
             6   :QRU:  You  are not authorized as a  store  and  forward
                  mailbox.
             7   :QRU: Error in opening <callsign>.MBX file.
             8   :QRU: Error in closing <callsign>.MBX file.
             9   :QRU: Sequence  Error in callsign of message to go.  The
                  bad callsign will be shown after the error number.
             14  :QDB:  File  Name In Use Error.  The name you  gave  the
                  file you want to upload already exists on that  system.
                  Try a different name.
             90   NC/L defined function not implemented in this release.
             99   LAN-LINK compatible program, but requested function has
                  not been implemented.

        A3.9  :QJG: is a response to :QRU:

             It confirms that the QRU sequence is complete.  There are no
             more messages pending.

        A3.10 :QRV: callsign is a response to :QSP: callsign.

             The  computer  is  ready you to send the  message.  End  the
             message  with  a control Z (^Z) character, or  the  sequence
             :EOF: .

        A3.11 :QSL: is a response to a command.

             It  confirms receipt of message to that callsign or  that  a
             file has been successfully uploaded and stored to disk.   It
             is also used to acknowledge receipt of a ':QRT:' command.

        A3.12 :QTC: massage list.

             If  LAN-LINK receives :QTC: it will respond with the  beacon
             text showing the mail queue.

             :QTC:  precedes  a list of callsigns for whom  messages  are
             stored up on a computer.  It is used in Packet Beacon  tran-
             smissions or AMTOR Beacon mode CQ calls.

                  PROPOSED EXTENSIONS

             A3.13 :QYU:     YAPP format file upload.
             A3.14 :QYD:     YAPP format file download.

        APPENDIX 4. USING OTHER TNC'S.

        LAN-LINK  is  designed for the PK-232.  However the  PACKET  mode
        capabilities  can  be  used  on other  TNC's.   There  are  minor
        differences  in the command dialog between different TNC's.   The
        dialog differences affecting the operation of LAN-LINK are  built
        into the program and set when the TNC type is read from the  LAN-


        LAN-LINK.DOC (c) G3ZCZ 1988





        LAN-LINK VERSION 1.50  PAGE 67


        LINK.SYS  file  at the program load time.  The non  packet  modes
        will obviously result in error messages if attempted on a  packet
        mode TNC.

        The   following  notes  apply  to  different  TNC's  or   digital
        communications controllers.

        A4.1 TNC2 (MFJ 1270) Version 1.1.2

        A4.1.1     Default Commands.

        Rename  the LAN-LINK.SYS file as PK232.SYS.  Rename the  TNC2.SYS
        file as LAN-LINK.SYS and edit it using your word processor in its
        non document mode to customize it to your station.

        A4.1.2     Program differences.

        The  following  functions DO NOT WORK because the  TNC  does  not
        support them.

        All NON PACKET modes.
        Software controlled HF/VHF switching.
        Software controlled baudrate switching.
        CQ/BEACON Packet terminal mode.
        TNC Transmit Buffer flush.

        A4.2 TNC1 (HD-4040)

        A4.2.1     Default Commands.

        Rename  the LAN-LINK.SYS file as PK232.SYS.  Rename the  TNC1.SYS
        file as LAN-LINK.SYS and edit it using your word processor in its
        non document mode to customize it to your station.

        A4.2.2     Program differences.

        The  following  functions DO NOT WORK because the  TNC  does  not
        support them.

        All NON PACKET modes.
        Day/Time functions.
        'MH' and remote :QMH: functions.
        MAIL Packet terminal mode.
        CQ/BEACON Packet terminal mode.
        TNC Transmit Buffer flush.
        Conference and multi-connect modes.

        A4.3 Kaypro KPC-2

        A4.3.1     Default Commands.

        Rename  the LAN-LINK.SYS file as PK232.SYS.  Rename  the  KPC.SYS
        file as LAN-LINK.SYS and edit it using your word processor in its
        non document mode to customize it to your station.



        LAN-LINK.DOC (c) G3ZCZ 1988





        LAN-LINK VERSION 1.50  PAGE 68


        A4.3.2     Program differences.

        The  following  functions DO NOT WORK because the  TNC  does  not
        support them.

        All NON PACKET modes.
        MAIL Packet terminal mode.
        CQ/BEACON Packet terminal mode.
        TNC Transmit Buffer flush.

        A4.4 KAM  EPROM Version 2.8.2.

        A4.4.1     Default Commands.

        Rename  the LAN-LINK.SYS file as PK232.SYS.  Rename  the  KAM.SYS
        file as LAN-LINK.SYS and edit it using your word processor in its
        non document mode to customize it to your station.

        A4.4.2     Program differences.

        The  following  functions DO NOT WORK because the  TNC  does  not
        support them.

        TNC Transmit Buffer flush.
        The SIGNAL communications mode.
        The NAVTEX communications mode.
        The Alt-D key in the MORSE Communications mode.

        The BAUDOT NAVY MARS Protocol is also not available.

        A4.5 PK-232 EPROM Version 30 AUG 1988

        Turn the 'BBS OFF' if you want the Alert Call and Digipeat Detect
        features to work otherwise turn it on.























        LAN-LINK.DOC (c) G3ZCZ 1988





        LAN-LINK VERSION 1.50  PAGE 69


        APPENDIX 6 LAN-LINK REGISTRATION FORM.

        To: Joe Kasser G3ZCZ
             P O BOX 3419
             SILVER SPRING
             MD 20904.



        CALL ________________   TODAY'S DATE _____________

        NAME ______________________________________________

        ADDRESS ___________________________________________

                ___________________________________________

        CITY    ___________________________________________

        STATE   _________  POSTCODE  ______________________

        TNC TYPE _____________________

        I  enclose  a check for $35.00. Please register me as a  user  of
        LAN-LINK.  I am currently  using Version ________________   which
        I obtained from  _________________________________________.

        Please send me the latest version of LAN-LINK or if a more recent
        one  does not exist at this time, QSL my registration and add  my
        name  to  the  list  to receive a free  update  when  it  becomes
        available.

        Signature

        Comments, likes, dislikes, wish list, etc.




        My favourite operating modes are ______________________________.



        Additional  Features I'd like to see in future releases of  LANK-
        LINK.
        Keep Conference Bridge Up       __________
        YAPP Binary File compatibility  __________
        Export Logs to dBASE 3          __________
        Expanded Contest Operation      __________
        More AMTOR                      __________
        Others
        _________________________________________________________________





        LAN-LINK.DOC (c) G3ZCZ 1988





        LAN-LINK VERSION 1.50  PAGE 70


        APPENDIX 7 LAN-LINK PROBLEM REPORT

        Name ______________________________________  CALL _______________

        Street __________________________________________________________

        City _______________________________  State _____  ZIP __________

        Tel ____________________  LAN-LINK version _____________________

        1.  Describe your computer system.

        Manufacturer ____________________ Model ___________TNC __________

        DOS Version  ________________  Clock Frequency _________ MHz.

        List peripheral equipment and cards installed in your computer.

        _______________________  _______________________

        _______________________  _______________________

        _______________________  _______________________

        What  memory  resident programs were installed when  the  problem
        occurred?

        _______________________  _______________________

        _______________________  _______________________

        2.  Describe the problem in detail.






        3.  Describe the sequence of events or keystrokes that led to the
        problem.



        4.  Any other information that may help in locating the problem.




        Use additional sheets of paper if necessary.  ATTACH copy of your
        LAN-LINK.SYS  file.  Mail to:  Joe Kasser, P O Box  3419,  Silver
        Spring, MD. 20901.






        LAN-LINK.DOC (c) G3ZCZ 1988





@