CQ-VHF

                                     version 2.10
























          Notice

          Better Software Co. reserves the right to make improvements in
          the  product described in this manual at any time and without
          notice.

          This manual is copyrighted. All rights are reserved. No portion
          of this manual may be copied, photocopied, reproduced, translated
          or reduced to any electronic medium or machine form without prior
          consent in writing from Better Software Co.

          Copyright 1992, Better Software Co.







          CQ-VHF Users Guide              1








                                  Table of Contents

          Introduction  . . . . . . . . . . . . . . . . . . . . . . . .   3

          Features  . . . . . . . . . . . . . . . . . . . . . . . . . .   4

          Installation  . . . . . . . . . . . . . . . . . . . . . . . .   5

          Program Startup . . . . . . . . . . . . . . . . . . . . . . .   7

          The Screen  . . . . . . . . . . . . . . . . . . . . . . . . .   9

          Logging Function  . . . . . . . . . . . . . . . . . . . . .    11

          Editing Log Entries . . . . . . . . . . . . . . . . . . . .    14

          Grid Map  . . . . . . . . . . . . . . . . . . . . . . . . .    15

          Direction and Distance Calculator . . . . . . . . . . . . .    16

          Scheduling  . . . . . . . . . . . . . . . . . . . . . . . .    17

          QSOs for a Call . . . . . . . . . . . . . . . . . . . . . .    20

          QSOs from a Grid  . . . . . . . . . . . . . . . . . . . . .    21

          CW Keyboard . . . . . . . . . . . . . . . . . . . . . . . .    22

          Exit to DOS . . . . . . . . . . . . . . . . . . . . . . . .    23

          Change your Grid/State (Rovers Only)  . . . . . . . . . . .    24

          Backup Logs . . . . . . . . . . . . . . . . . . . . . . . .    25

          Load CW Memory Buffers  . . . . . . . . . . . . . . . . . .    27

          DOS Shell . . . . . . . . . . . . . . . . . . . . . . . . .    28

          RECOVER.EXE . . . . . . . . . . . . . . . . . . . . . . . .    29

          SUBMIT.EXE  . . . . . . . . . . . . . . . . . . . . . . . .    30

          Appendix A  . . . . . . . . . . . . . . . . . . . . . . . .    32

          Appendix B  . . . . . . . . . . . . . . . . . . . . . . . .    33

          Appendix C  . . . . . . . . . . . . . . . . . . . . . . . .    34






          CQ-VHF Users Guide              2










                                     Introduction

          CQ-VHF is a software product of Better Software Company of
          Greenville, South Carolina. The initial release of the software 
          is for contest logging during the ARRL VHF contests. Later
          releases  will be for the ARRL UHF and CQWPX contests. This
          software runs  on most IBM or compatible PC's.

          The software was designed by VHF contesters with many years
          experience  and several Top 10 finishes. Until now no contest
          logging software  supported multiuser, multiop stations. CQ-VHF
          is available in single user and multiuser versions.

          Better Software wishes to express our sincere appreciation to 
          Danny Taylor, N4DT for his input as a beta tester.




































          CQ-VHF Users Guide              3










                                       Features

               Fast log entry even with XT class computer

               Will operate from floppy disk based systems 

               Automatic duplicate checking

               Rover duplicates allowed

               Display of bands needed as each grid is worked

               Grid map with worked grids highlighted

               Band score and total score always current

               Built-in CW keyboard
             
               Calculate direction, distance and reciprocal heading
               for any grid

               Contact scheduling feature with alarm

               Display QSOs logged for a given call

               Display calls missed from a grid for Rover operators
           
               Multiuser version available for multiop stations with
               message sending system

               Output of ASCII files for submission to ARRL

               Printouts of contest logs and score sheets

               Automatic backup to floppy drive

               Context sensitive help messages

               Automatic backup to printer












          CQ-VHF Users Guide              4










                                    Installation 

          The CQ-VHF disk is supplied with at least eight files.

          BTRIEVE.EXE         This is the file I/O
                              system.
          CQ-VHF.EXE          This is the main logging
                              program.
          CQ-VHF.HLP          Help file for ROVER.EXE,
                              contents displayed when
                              you press the F1 key.
          CQ-VHF.DOC          This is the user manual
                              file for CQ-VHF. 
          CQ-VHF.BAT          This is the batch file to
                              start CQ-VHF. 
          SUBMIT.EXE          This program creates the
                              submission report and
                              disk file. 
          SUBMIT.HLP          Help file for SUBMIT.EXE,
                              contents displayed when
                              you press the F1 key.
          RECOVER.EXE         Reconstructs data files
                              from the filename.DT6
                              backup file. 
          READ.ME             This file if present
                              contains the latest news
                              about CQ-VHF.
























          CQ-VHF Users Guide              5










          To install CQ-VHF on hard disk systems, follow these easy steps:

          1)   Create a directory on your hard disk drive.

               MD CQ-VHF  <<ENTER>>

          2)   Move to the new directory.

               CD CQ-VHF  <<ENTER>>

          3)   Place the CQ-VHF diskette in the A:
               drive and copy the files to the new directory.

               COPY A:*.*/V  <<ENTER>>

          To install CQ-VHF on floppy disk systems, you should set up the
          following diskettes.

          1)   A bootable diskette with the BTRIEVE.COM file.  This
               diskette is used to boot and load the ISAM file system.

          2)   A diskette with CQ-VHF.EXE, CQ-VHF.HLP and COMMAND.COM. 
               This is the diskette you use during the contest.

          3)   A diskette with the other programs.  This diskette is
               used for file recovery and submission log creation.

           























          CQ-VHF Users Guide              6










                                   Program Startup

          Once you are in the CQ-VHF directory type

          CQ-VHF  <<ENTER>>
          If you are using a color monitor.

          CQ-VHF/M  <<ENTER>>
          If you are using a CGA card with a composite monitor.

          CQ-VHF/P  <<ENTER>>
          If you are using a Laptop with a plasma screen.

          You can also change the COM port the CW keyboard feature will
          use.  The default is COM1.  To change you add a /2 for COM2, /3
          for COM3, /4 for COM4.

          Example:  CQ-VHF/M/2  this means you have a monochrome monitor
          and want to use COM2 for the CW keyboard feature.

          This will bring up the program and display the opening credits
          screen.  Pressing the <<ENTER>> key removes the credits screen
          and begins a series of prompts you must answer.

          ENTER CONTEST NAME:

          Enter the name you wish to call the files for this contest.  A
          suggestion would be to use the date the contest begins, ie.
          061392 for the 1992 June VHF contest.  The name you chose will be
          the name used for all data files.

          ENTER HOURS FROM UTC:

          Here you enter the time offset from your computer's clock to UTC. 
          UTC is used for all logging functions.  If, for example, your
          computer is on EDT the offset would be 4 hours.

          ENTER STATION GRID:

          Here you enter the grid square you are operating from. This
          information  will be used in calculating direction and distance
          to other grids.  If you are a Rover station, enter the grid you
          are starting the contest from.  Later as you move to a new grid
          square you can change this entry.

          ENTER STATE:

          Enter the state you are operating from.  Rover stations should
          enter the state they are starting the contest in.  This entry can
          be changed as Rovers move to a new state.

          CQ-VHF Users Guide              7








           
          ENTER STATION CALL:

          Here you enter the call used by your contest station.

          The grid map will now display using the defaults of your station
          grid and band A (50 mhz). The scoreboard will be updated with
          information from the data base. 

          You are now in logging mode.

          At any prompt within CQ-VHF you may press F1 and get a help
          message about the prompt you are on.  Pressing <<ENTER>> will
          remove the help message.







































          CQ-VHF Users Guide              8










                                      The Screen

          The screen has seven sections.

          Across the top line is the UTC date and time, your grid, state
          and call for your reference.  Rover stations should carefully
          check this line after each move to make sure they have the
          correct grid and state entered.

          Just below the reference line and to the left is the scoreboard.

          Then to the right of the scoreboard is the grid map.

          Below these sections on the left is the logging section. To the
          right of the logging section is the multi-use section. This
          section is used for the multi-user message system, for the
          direction and distance  calculator, and for setting up contact
          schedules.

          Below these two sections are the function key definitions.  The
          definitions will change if you hold down the ALT or CTL keys. 
          The ALT+function keys are used for additional features of CQ-VHF. 
          The CTL+function keys are memory buffers for the CW sending
          feature.

          Below the function key line is a message line used by the program 
          to prompt the operator.
























          CQ-VHF Users Guide              9










          EDITING KEYS

          When entering data the following editing keys are available.

          Ins         -  Toggles between typeover and insert
                         modes.  In type over new text
                         overlays old. In insert mode text
                         to the right of the cursor is push
                         to the right, characters pushed off
                         the screen are lost.

          Del         -  Deletes characters beneath cursor
                         and moves text to right of cursor
                         one character to the left.

          Back Space  -  Deletes character to left of cursor
                         and moves text one character to
                         left.

          Left Arrow  -  Moves cursor one character to left.

          Right Arrow -  Moves cursor one character to
                         right.

          Up Arrow    -  Moves cursor to previous input
                         prompt.

          Home        -  Moves cursor to beginning of input.

          End         -  Moves cursor to end of input.

          ESC         -  Aborts changes to input and
                         restores original data.


















          CQ-VHF Users Guide              10










                                   Logging Function

          To log a contact, you must supply four pieces of data; band,
          mode, call and grid.

          BAND:

          Enter the letter associated with the band you are working. The
          definition  of the letters are on the scoreboard. The default
          band will the  band last worked. To accept the default press
          <<ENTER>>.

          MODE:

          Enter the mode of this contact.  AM, FM, CW, SSB are the allowed
          modes.  The default mode is the mode last used.  To accept the
          default press <<ENTER>>.

          CALL:

          Enter the call of the station you are working.  The program will
          check for a duplicate and give you a warning message is it finds
          a dup.  After entering the call, the current date and time are
          also displayed. If you want to change to a date & time other than
          the current, you press the 'up arrow' key and move back to time
          ant then date.

          GRID:

          Enter the grid of the station you are working.

          A message will now appear on the last line of the screen asking
          you to confirm your entry. Pressing <<ENTER>> will begin the
          second dup check and logging process.  If you typed something
          wrong, enter 'N' and you can correct the contact prior to
          logging.


          DUP CHECKING & WRITING CONTACTS

          Rover dups are  allowed. If the contact is a dup, a message will
          be displayed on  the last line of the screen and the entry will
          not be logged.  The  dup message includes the date and time of
          dup contact. 

          If the entry  passes the dup check, the program will display any
          bands needed in  the grid you just worked. This might allow you 
          to work another multiplier on a different band. The grid map and 
          scoreboard are also updated.


          CQ-VHF Users Guide              11









          If at any point during the logging process you decide not to log
          the contact you may press ALT+F9 to clear all log entries and
          return you to the band entry.

            
          LOGGING FUNCTION KEYS

          At any point in logging mode you may press a function key and
          move  to another operation.

          F1   Brings up a help message about the prompt you are on.

          F2   Brings up the log data editor.

          F3   Allows you to move or change the displayed grid map.

          F4   Takes you to the direction and distance calculator.

          F5   Takes you to the contact scheduling feature.

          F6   Allows you to display the QSOs for a particular call.

          F7   Allows you to display the QSOs missed from another
               grid.  This feature is for Rover operation.

          F8   Allows you to change the CW sending speed and spacing.

          F9   Puts you in CW send mode.

          F10  Exit the program. 






















          CQ-VHF Users Guide              12










          LOGGING ALT+FUNCTION KEYS

          To use these function keys, hold down the ATL key while pressing
          the function key.

          F1   Brings up a help message about the prompt you are on.

          F2   Allows you to change your grid and state.  Used by
               Rover operators after moving to a new grid or state.

          F3   Toggle off and on the printer for log entries.

          F4   Toggle off and on the floppy disk backup of log
               entries.

          F5   Load the CW memory buffers.

          F6   Toggle the scoreboard between current grid only and
               totals for all grids.

          F7   Currently not used in this version of CQ-VHF.

          F8   Currently not used in this version of CQ-VHF.

          F9   Clear the current logging entry.

          F10  Shell to DOS to execute another command.
























          CQ-VHF Users Guide              13










                                 Editing Log Entries

          The log data editor is obtained by pressing the F2 key while in
          the logging function.  Once selected, the grid map section will
          be overwritten by the last twelve logged contacts.

          The display shows the Band, Mode, State, Grid, Call, Date and
          Time of the stations  worked with the first logged contact
          highlighted.

          The highlight bar is moved by using the Up, Dn, Pg Up and Pg Dn
          keys. The Up & Dn keys move the highlight bar one entry up and
          down at a time. If the bar is at the top or bottom of the list of
          contacts, pushing an arrow key will display the previous or next
          page of log entries. The Pg Up & Pg Dn keys display the previous
          or next page of log entries.

          If the highlight bar is at the last contact logged or the end of
          the  log file then pushing the arrow keys will cause a beep and
          will not  move the highlight bar, pushing the Pg Up or Pg Dn keys
          will move the highlight bar to the top or bottom of that page.

          EDITING A LOG ENTRY

          Once the contact is highlighted, you may press, F3 to delete  the
          contact completely or press, F2 to edit the contact. In  both
          cases the contact is removed from the log, and the scoreboard, 
          grid map, and bands needed files will be updated.

          If you chose to edit the contact (F2) the contact will now be 
          displayed in the logging section. You may now accept items that
          are  correct and change incorrect items. You will also be allowed
          to edit  the date and time, however once you have accepted them
          you must press  F9 in order to be allowed to edit them again.

          This editor is for making changes that you find during and after
          the  contest. If you entered the data editor by mistake, press
          <<ESC>> to exit the editor and return to the logging function.

          LOG EDITOR FUNCTION KEYS

          F1  -     Brings up a help message about the prompt you
                    are on.

          F2  -     Deletes the log entry and places a copy of it
                    into the logging section, then returns to the
                    logging section.

          F3  -     Deletes the log entry, then returns to the
                    logging section. 

          CQ-VHF Users Guide              14










                                       Grid Map

          The grid map will show at a glance what squares for a particular
          grid  and band, you need to work. As you work contacts the grid
          maps are  updated. Any map can be displayed. The worked squares
          are marked  in reverse video.

          The grid map display change option is obtained by pressing the F3
          key. You can now use the arrow keys to move around the map.  The
          grid map can be scrolled to the desired position. Scrolling  has
          two advantages over entering the grid and band.  First, it allows
          you set the grid map across grid squares. This is very useful if
          the grid you are operating from is at a grid's border.  Second,
          it allows you to move the map around one square at a time 
          allowing you to get an idea of the area you are working (much
          like  moving a magnifying glass over a map).

          The map can be scrolled one row or column at a time by pushing
          the four arrow keys. The band can also be changed by pressing 
          the PG-UP & PG-DN keys. Once the desired grid area is displayed
          pushing <<ENTER>> sets it and returns you to the logging
          function.

          To change to a particular map, you press F2 and supply two pieces
          of data, grid and band.

          GRID:

          Enter the two letter prefix of the new grid square to display or
          press <<ENTER>> to leave unchanged.

          BAND:

          Enter the letter associated with the new band you want to display 
          or press <<ENTER>> to leave unchanged. The scoreboard has the
          definitions of the letters.

          If you selected the map change by mistake, press <<ESC>> to exit 
          without changing the displayed map.

          The grid map also has a unique toggle feature to compare grid
          squares.  First enter the grid to compare by pressing F3 and
          entering a grid square.  Once entered you can now compare the
          entered grid to your current grid by pressing F4.







          CQ-VHF Users Guide              15










                          Direction and Distance Calculator

          This function helps you zero in on rare grids when you hear the
          grid  square but don't know which way to point the antenna. After
          entering  the target grid the direction to and from the target is
          shown in degrees and minutes and the distance in miles.

          ENTERING TARGET

          The direction and distance calculator is obtained by pressing the 
          F4 key from then logging function.  To calculate you supply one
          piece of data.

          ENTER TARGET GRID:

          Enter the grid square to calculate or press <<ENTER>> to use the
          default value.

          CQ-VHF now displays the heading to the grid, the reciprocal
          heading from the grid and the distance between the grids.

          If you selected the direction and distance calculator by mistake,
          press <<ESC>> to exit.




























          CQ-VHF Users Guide              16










                                      Scheduling

          This feature is used to schedule contacts or events in the future 
          and to be told about them when their scheduled time approaches.

          The scheduling function is selected by pressing F5 from the
          logging function.  An alarm will sound informing the operator of
          the sched at 15 minutes, 10 minutes, 5 minutes, 1 minutes and at
          the scheduled time.

          SCHEDULING A CONTACT

          To schedule a contact or event, you can supply up to five pieces
          of  data; freq, call, date, time and grid.

          FREQ:

          Enter the frequency of the contact you are scheduling. The
          frequency  is not validated or required. You can push <<ENTER>>
          without entering  a frequency if you are scheduling an event
          rather than a contact.

          CALL:

          Enter the call of the station you are scheduling.  The call sign
          is not validated and may be any text message ten characters in
          length such as GAS GEN or SHIFT CHG if you are scheduling an
          event rather than a contact.

          DATE:

          Enter the date of the scheduled event. The current date is the
          default.  Press <<ENTER>> to select the default.

          TIME:

          Enter the time of the scheduled event. The current time is the
          default  and must be edited.

          GRID:

          Enter the grid of the station you are scheduling.  This entry is
          not required and may be left blank. The prompt is validated  if
          anything is entered.

          A message will now appear on the last line of the screen asking
          you  to confirm your entry. Pressing <<ENTER>> will store the
          event.  If  you typed something wrong, enter 'N' and you can
          correct the event  prior to saving.


          CQ-VHF Users Guide              17










          SCHEDULING FUNCTION KEYS

          At any point in scheduling mode you may press a function key and
          move  to another operation.

          F1        Brings up a help message about the prompt you
                    are on.

          F2        Brings up the schedule data editor.

          <<ESC>>   Returns to the logging section.








































          CQ-VHF Users Guide              18










          SCHEDULE DATA EDITOR

          The schedule data editor is obtained by pressing the F2 key while
          in the schedule function.  Once selected, the grid map section 
          will be overwritten by the last twelve schedules.

          The display shows the Date, Time, Call and Frequency of the
          schedules with the first highlighted.

          The highlight bar is moved by using the Up, Dn, Pg Up and Pg  Dn
          keys. The Up & Dn key move the highlight bar one entry 
          up and down at a time. If the bar is at the top or bottom of the
          list  of events, pushing an arrow key will display the previous
          or next  page of schedule entries. The Pg Up & Pg Dn keys display
          the  previous or next page of schedule entries.

          If the highlight bar is at the last schedule or the end of  the
          schedule file then pushing the arrow keys will cause a beep and 
          will not move the highlight bar, pushing the Pg Up or Pg Dn keys
          will move the highlight bar to the top or bottom of that  page.

          EDITING A SCHEDULE ENTRY

          Once the scheduled contact is highlighted, you may press, F3  to
          delete the event completely or press, F2 to edit the event. In 
          both cases the event is removed from the schedule.
          If you chose to edit the event (F2) the event will now be
          displayed  in the scheduling section. You may now accept items
          that are correct  and change incorrect items.

          This editor is for making changes when, schedules change and
          entry  errors are made. If you entered the data editor by
          mistake, press <<ESC>> to exit the editor and return to the
          scheduling function.

          SCHEDULE EDITOR FUNCTION KEYS

          F1        Brings up a help message about the prompt you
                    are on.

          F2        Deletes the schedule event and places a copy
                    of it into the scheduling section, then
                    returns to the schedule function.

          F3        Deletes the schedule event, then returns to
                    the schedule function.

          <<ESC>>   Aborts editor and returns to schedule
                    function.


          CQ-VHF Users Guide              19










                                   QSOs for a Call

          The QSOs for a call display will show at a glance all QSOs for a
          given call. This option is useful in several ways.  First, use it
          to check if you have  made all the contacts with a Rover before
          he moves on.  Second, check if  the contact you are about to make
          is a dup.  Third, check if you have  contacted a station on all
          bands planned.

          DISPLAYING THE QSOs

          The display QSOs for a call function is obtained by pressing the
          F6 key from the logging function.  The grid map section will be
          cleared and you will prompted for one piece of data; the call.

          ENTER CALL:

          Enter the call of the station who's QSOs you want displayed. The
          default  will be the one that is entered in the logging section.

          Once the call is entered the grid map section will be overwritten
          by up to twelve QSOs for the call entered.  If there are no QSOs
          for the call entered you will be informed of this and returned to
          the logging function.

          The display shows the Call, Band, Grid, Date and  Time of the
          QSOs  for the entered station.

          If there are more than twelve QSOs for a call the rest of the
          QSOs can  be displayed by using the Pg Up and Pg Dn keys. The 
          Pg Up & Pg Dn keys display the previous or next page of QSOs.

          When finished looking at the QSOs or if you entered the QSO
          display  by mistake, press <<ESC>> to exit and return to the
          logging function.

          HINT:  For quick dup checking in the logging function; enter the
          band and mode you are working.  Now you can enter calls heard and
          then press F6 to put you in the QSOs for a call function.  The
          call you just entered is the default.  Press <<ENTER>> and CQ-VHF
          will quickly tell you if you have worked.  The call will remain
          in the logging function so you can work and log a "new one".









          CQ-VHF Users Guide              20










                                   QSOs from a Grid

          The QSOs from a grid display will show at a glance all QSOs from
          a given grid that have not been worked form the current grid. 
          This allows Rover operators to make sure they have worked all the
          stations they can before moving on to a new grid.

          DISPLAYING THE QSOs

          The display QSOs from a grid function is obtained be pressing F7
          from the logging function.  The grid map section will be cleared
          and you will be prompted for one piece of data; the grid.

          ENTER GRID:

          Enter the grid you wish to compare to the current grid.  Once the
          grid is entered the grid map section will be overwritten by up to
          twelve QSOs for the grid entered.  These will be stations not
          worked from the current grid.

          If there are more than twelve QSO's to display, the rest can be
          displayed by using the <<Pg Up>> and <<Pg Dn>> keys.

          This function is exited by pressing the <<ESC>> key.



























          CQ-VHF Users Guide              21










                                     CW Keyboard

          CQ-VHF provides a full feature CW keyboard.  The CW keyboard
          requires a simple hardware connection to your radio.  A schematic
          diagram for the hardware is provided in Appendix A.  You can also
          purchase a manufactured version of the hardware from Better
          Software (see the order form).

          The character speed and spacing for the CW is set by pressing F8
          from the logging function.  You enter a four digit number
          followed by <<ENTER>>.  The first two digits indicate the
          character spacing and the second two digits indicate the speed. 
          For example, 0520 would mean 20 WPM characters with 5 WPM
          spacing.

          To manually send CW text, you press F9 from the logging function. 
          Once selected, any characters entered will be sent to the
          selected COM port.  Pressing F1 while in manual CW mode will
          toggle off and on the computer speaker for sidetone.  F2 while in
          manual CW mode will toggle on and off a continuous tone.

          Ten CW memory buffers are also provided and are explained later
          in the users guide.




























          CQ-VHF Users Guide              22










                                     Exit to DOS

          To exit CQ-VHF and return to DOS, press F10 while in the logging
          function.  You will be asked to confirm your entry and then
          dropped out of the program to DOS.  

          CQ-VHF uses ISAM files which are constantly updated.  There will
          be no lost data when your exit the program.











































          CQ-VHF Users Guide              23










                         Change your Grid/State (Rovers Only)

          Rover stations need the ability to change their grid or state
          when they move.  This is done by pressing ALT+F2 from the logging
          function.  You may now enter the new grid square or state.  The
          scoreboard can be set to show only the score from this new grid
          or all totals for all grids.












































          CQ-VHF Users Guide              24










                                     Backup Logs

          There are three types of backup logs kept by CQ-VHF.

          The first is a text file called filename.DT5 and is kept in the
          same directory as the other data files used by CQ-VHF.

          The second is a optional hard copy printout identical to the
          filename.DT5 file.

          The third is a copy of the filename.DT5 file optionally copied
          and maintained after each log entry on the A: floppy drive.  This
          copy is called filename.DT6.

          The filename.DT5 file is a text file kept for backup purposes. If
          the data base used by CQ-VHF becomes corrupt, it can be rebuilt 
          from this text file.

          The records in filename.DT5 must follow this format:

               Position 1 - 4      Grid operated from
               Position 5          space
               Position 6 - 7      State operated from
               Position 8          Band
               Position 9 - 10     spaces
               Position 11         Mode
               Position 13 - 16    Grid Square
               Position 17 - 28    Call Worked
               Position 29 - 36    UTC Date as MM/DD/YY
               Position 38 - 42    UTC Time as HH:MM
               Position 44 - 46    Record Code: ADD for new contacts
                                                EDT for edits
                                                DEL for deletes

          HARD COPY

          The optional hard copy printout is toggled on & off by pushing
          the ATL+F3 key. When this function is on the keyword PRT will
          appear on the top line of the screen and each contact logged will
          be printed on the printer.

          Keeping a hard copy printout of the log is recommended in case of
          computer  problems during the contest. With the printout you
          should be able  to continue with the contest in case your
          computer stops working.  You can also use a text editor to enter
          the log entries from the printout  into a file called
          filename.DT5 and recover the data base used by CQ-VHF in case you
          loose all data on the computer.



          CQ-VHF Users Guide              25










          BACKUP OF filename.DT6 TO FLOPPY DISK

          The filename.DT6 file can be copied and updated on floppy by
          pushing  then ALT+F4 key from the logging function. After pushing
          the ALT+F4 key you will be asked to insert a backup disk in drive
          A:. This disk should be a blank formatted disk.  If you selected
          this option by mistake then push the letter 'A' to abort, else
          push <<ENTER>> and the filename.DT6 file will be copied to the
          floppy and you will be returned the to logging function. The 
          keyword DSK will also appear on the top line of the screen and
          all contacts logged will also be written to the floppy disk.

          If a disk error occurs while copying the log file to the floppy
          you will be informed of the disk error and allowed to retry with
          another disk or abort the process. If an error occurs writing to
          the floppy  while logging contacts the error will be displayed
          and the program will be aborted. The program may the be restarted
          with no loss of data.

          DO NOT REMOVE THE FLOPPY FROM THE DRIVE WHILE THE KEYWORD DSK  IS
          DISPLAYED AT THE TOP OF THE SCREEN.

          Multiple backups of the filename.DT6 file can be kept by pushing
          ALT+F4 when the DSK keyword is displayed to close the log file,
          then  changing the disk, and pushing the ALT+F4 key again to copy
          the log file to another disk.

          Backing up to multiple floppies is recommended in case of
          computer  problems. The backup log can be used to reconstruct the
          data base  after a computer crash or it can be printed to
          continue contesting  after a computer failure.




















          CQ-VHF Users Guide              26










                                Load CW Memory Buffers

          CQ-VHF offers the user ten definable CW memory buffers.  To load
          a buffer, press ALT+F5 from the logging function.  You can now
          enter up to 120 characters of text to send.  Once you have
          entered your text your are asked to supply a description of the
          buffer.  This description can be up to six characters in length. 
          You are then asked to indicated which function key to store this
          buffer under.  The description you supplied will be visible on
          the screen any time you press and hold the CTL key.

          To send a CW memory buffer all you need to do is press and hold
          the CTL key and then press the function key associated with the
          buffer you want to send.  If you want to stop the transmission,
          press <<ESC>>.  F1 will toggle on and off the speaker sidetone.

          You may edit previously entered buffers by pressing F2 while in
          the CW memory buffer function.
            
          There are several keywords that can be used in the CW memory
          buffers.  These keywords are replaced at runtime with their
          equivalents.

               :1   your call

               :2   your current grid

               :3   the call you are currently logging

               :4   the grid you are currently logging





















          CQ-VHF Users Guide              27










                                      DOS Shell

          CQ-VHF allows you to "shell to DOS" to perform DOS commands.  The
          DOS shell function is obtained by pressing ALT+F10.  You are
          instantly taken to DOS.  You return to CQ-VHF by typing "EXIT"
          <<ENTER>>.  You will then instantly pop back into CQ-VHF.













































          CQ-VHF Users Guide              28










                                     RECOVER.EXE

          The RECOVER program allows the user to recreate the contest data
          files from the file filename.DT5 or filename.DT6. This could be
          used after a computer problem that corrupted your other data
          files. You could also restore from a backup copy of the
          filename.DT5 or filename.DT6 file.

          filename.DT5 is a text file (see the section on Backup Logs for
          layout) that you can  edit or create, enabling you to enter data
          from a previous contest,  from a printed backup or a hand written
          log and then use the RECOVER  program to create the other data
          files used by CQ-VHF.

          USING THE RECOVER PROGRAM

          To execute the RECOVER program change into the directory that
          contains the CQ-VHF programs and the filename.DT5 or filename.DT6
          file you want to recover.

          Then type :

              RECOVER  <<ENTER>> at the DOS prompt. 

          The program will request that you <<Press any key to begin>>.
          Once you push a key the program will initialize the data files.

          The program will make two passes on the data to create the other
          data  files. At the end of the second pass you are asked to
          <<Press any key  to end>>. The CQ-VHF data base has been
          restored.

          The RECOVER program also allows an additional feature. If you
          wish  to exchange logs with other users of CQ-VHF, simply send 
          then the filename.DT5 file. They can then use RECOVER to create
          the other data files.















          CQ-VHF Users Guide              29










                                      SUBMIT.EXE

          The SUBMIT program creates both hardcopy and disk file logs for
          submission to the contest committee.

          USING THE SUBMIT PROGRAM

          Change to the directory where the CQ-VHF programs and the  data
          files you want to create the submission log for are located.

          Then type:

              SUBMIT <<ENTER>> at the DOS prompt.

          Once the program is started you must supply several pieces of
          data.

          STATION:

          Enter the call used by your contest station.

          OPERATING FROM GRID:

          Enter the grid you operated from during the contest

          CITY:

          Enter the nearest city or landmark to your contest operation.

          CQ-VHF:

          Enter the name of the contest you operated in for this log. (ex.
          June 1992 ARRL VHF QSO Party)

          START:

          Enter the date the contest started.

          END:

          Enter the date the contest ended.

          CATEGORY:

          Enter the category you are entering (ex. Single Operator)






          CQ-VHF Users Guide              30










          MULTIOP CALLS:

          If you operated a multiop station, enter the calls for the other
          operators.  Leave this area blank otherwise.

          At anytime while you are entering the above information you may
          push  F2 key to save the information to a disk file. Pushing the
          F3  key will retrieve this information.  Use this feature so you
          only  have to enter this information once even though you may run
          the SUBMIT program several times.

          After entering the last piece of information you are asked to
          confirm  that the Data is ok. Push <<ENTER>> to continue
          processing or push 'N' to edit the information.

          You are the asked if you want a printed copy of the log. Answer
          'Y' or 'N' to the question. In either case the disk files
          SUBMIT.LOG & SUMMARY.LOG are created.

          Once the program begins processing it sorts the log entries and
          processes  the grid multipliers. If printer output was selected
          the program asks  if the printer is ready and at top of form.
          Press <<ENTER>> when the  printer is ready.

          The summary sheet should be signed and submitted to the contest
          committee  in all cases. Even if submitting your log on disk you
          need to attest  to the data.
























          CQ-VHF Users Guide              31










                                      Appendix A

          The hardware to attach you computer to your radio for CW
          operation is detailed below.  The parts are all readily available
          at Radio Shack or hamfests.  Should you desire to purchase a
          manufactured version of the hardware please see the order form in
          Appendix C.












































          CQ-VHF Users Guide              32










                                      Appendix B

          CQ-VHF is available in a demo version for those wishing to try
          the software before purchasing.  If you obtained your copy of CQ-
          VHF from a computer bulletin board it is the demo version.  This
          version will give you a feel for how CQ-VHF works.

          The demo version is supplied with a sample contest data base.  To
          use the sample data enter 060891 for the contest name at program
          startup.  Using this data you can see how the various functions
          and displays perform.  This sample data is from a Rover station
          and will have contact made from several different grid squares.

          We may also create your own blank data base by supplying another
          contest name at startup.  We will be allowed to enter only 25
          contacts and the editing function has been removed.  This should
          let you see how easy CQ-VHF is to use.

          The RECOVER and SUBMIT programs described in the users guide are
          not included in the demo version.

          The latest version of CQ-VHF with full features and the RECOVER
          and SUBMIT programs is available by completing the order form in
          Appendix C.



























          CQ-VHF Users Guide              33










                                      Appendix C


          To order the complete and latest version of CQ-VHF please
          complete the order form below.  Each copy of CQ-VHF will be
          shipped with a complete, illustrated Users Guide.


          Order Form

          Send _______ copies of CQ-VHF software at $25.00 each.

          Send _______ CW computer to radio interfaces at $25.00 each.

          Include $3.00 shipping and handling with each order.


          Name:  ___________________________________ Call:  ___________

          Address:  ___________________________________________________

          City/State/Zip:  ____________________________________________

          Mail the completed order form along with payment to:

                    Better Software Company
                    10 Wilburn Avenue
                    Greenville, SC 29611























          CQ-VHF Users Guide              34