WeatherFAX
				       Weather Facsimile for IBM and
				       Compatible Personal Computers



				       USER'S GUIDE




















				       First edition
				       March 1990

				       Copyright 1990 Jerry Dahl

				       6404 Lakerest Court
				       Raleigh, NC 27612
















		 WeatherFAX User's Guide                 Page 1



		   TABLE OF CONTENTS
		   ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ


GENERAL INFORMATION ............................ 2
	 Introduction
	 Purpose and Goals
	 License information
	 The Software
	 The Author

SUPPORTED CONFIGURATIONS ....................... 4
	 Hardware
	 Software

INSTALLATION INSTRUCTIONS ...................... 5
	 Installing the WeatherFAX card
	 CONFIG.SYS Modifications
	 AUTOEXEC.BAT Modifications
	 Copying the diskette
	 Starting the Program

GETTING STARTED ................................ 7
	 Getting help information
	 Testing the card
	 Selecting your printer type and display mode
	 Connecting your computer to your fax receiver

USING WEATHERFAX ............................... 9
	 Adjusting the page alignment
	 Getting the image
	 Viewing the image
	 Printing the image
	 Saving the image to disk

ADDITIONAL INFORMATION ......................... 18
	 Calibrating the card
	 Using Expanded Memory (LIM 4.0)
	 Using extended VGA (800 X 600 Pixel) mode
	 Sources for weather facsimile
	 Decoding RTTY
	 WeatherFAX specifications

IF YOU HAVE DIFFICULTY ......................... 23

ADAPTER/SOFTWARE AVAILABILITY .................. 24

TRADEMARKS USED IN THIS GUIDE .................. 25














		 WeatherFAX User's Guide                 Page 2



GENERAL INFORMATION
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

  INTRODUCTION

		   These instructions explain how to install and use the
		   WeatherFAX weather scan converter and software.  You
		   may print this guide with your printer by typing the
		   following command from the DOS command line:

			COPY FAXGUIDE.DOC LPT1

		   This scan converter and software can be used with your
		   IBM or compatible personal computer.  With the proper
		   receiving equipment and antenna, your computer will be
		   able to capture, enhance, save and print not just black
		   and white, but gray-scale weather-facsimile images received
		   on the HF, VHF and UHF bands.  Users of this Automatic
		   Picture Transmission (APT) imagery include military and
		   commercial meteorologists, ships at sea, scientific
		   observers, educators, and amateurs.

		   The system features include:

		    o Direct weather-satellite imagery, including: geo-
		      stationary earth-orbiting satellites (GOES APT/WEFAX,
		      METEOSAT), polar-orbiting satellites (NOAA 9/10 APT
		      IR/Vis, Soviet Meteor), HF-FM NAFAX, and similar APT
		      formats.

		    o Expanded memory support.	You can capture images
		      with a wide variety of resolutions.  The size of the
		      captured image is limited only by the amount of RAM
		      in your computer.  To view images larger than your
		      monitor can display at one time, you can scroll up,
		      down, left, and right.

		    o Incoming pictures can be saved directly to disk.
		      Either the Tag Image File Format (TIFF) or Graphical
		      Interchange Format (GIF) can be selected to allow the
		      images to be used with other graphics-based software.

		    o Print images with 16-level gray scale on a wide variety
		      of printers including 9- and 24-pin dot-matrix printers
		      and laser printers.

		    o All standard graphics cards are supported including
		      CGA, MCGA, EGA, VGA, and the extended 800 x 600 mode.

		    o Histograms, enhancement, zoom, scroll, gray scale,
		      256,000+ colors, real-time acquisition/display.
		      Complete RGB level intensity control for each
		      displayable color.  Contrast and brightness are
		      fully adjustable.  4 user-settable imagery enhancement








		 WeatherFAX User's Guide                 Page 3



		      curves.  Enhancement is retroactive and instantaneous.

		    o Frequency-shift-keyed (FSK) radioteletype (RTTY)
		      decoding.  In addition to pictures, you can receive
		      land-based weather-station Baudot RTTY transmissions.

		    o Automatic gain-lock circuitry.  The optimum gain value
		      for WEFAX-signal reception is statistically calculated.
		      This provides better and more consistent pictures than
		      either automatic gain control (AGC) or fixed-gain
		      circuits.

		    o No need for external test equipment to test and
		      calibrate the board.  The software and special circuitry
		      on the board allow the computer to automate the testing
		      and calibration.

		    o Unattended operation.  Image capture can be fully or
		      partially automatic, including APT start tone detect,
		      sync, image save to disk, APT stop tone detect, and
		      cycle repeat.


  LICENSE INFORMATION

	      Your right to use WeatherFAX

		   This software is copyrighted in order to control its
		   orderly development.  However, you have the right to
		   use the program for private, non-commercial purposes
		   without further permission.	That is, you can copy it,
		   use it, and share it so long as you do not charge any
		   money for it other than the cost of the disk or other
		   transfer medium, not to exceed $2.  Please note that you
		   MUST return a completed registration form as contained in
		   the file REGISTER.DOC as a condition of using WeatherFAX.

	      Suggested Contributions

		   In order to cover expenses associated with the development
		   and distribution of WeatherFAX, such as equipment,
		   software, postage, supplies, and telephone calls to users,
		   I suggest a voluntary contribution of $10 (or whatever is
		   affordable to you) for each copy of the program.

  THE SOFTWARE

		   WeatherFAX is written in Turbo C* version 2.0.  The
		   development of the program began in early 1986, and has
		   gone through several revisions.  New versions will be
		   released as features are added and corrections are made
		   to previously released versions.










		 WeatherFAX User's Guide                 Page 4



		   The latest version can be obtained by sending a FORMATTED
		   (360-kbyte) 5-1/4" diskette (or 3.5" diskette) and a STAMPED,
		   SELF-ADDRESSED diskette mailer to the author at the address
		   below.  The request should also be sent with sufficient
		   postage that it does not arrive with postage due!  Also a
		   Shareware contribution makes the author whistle while he
		   works making your copy!

  THE AUTHOR

		   The author can be contacted by mail at the following
		   address:

			6404 Lakerest Court
			Raleigh, NC 27612

		   For a mail reply, please enclose a self-addressed,
		   self-stamped envelope.

		   Credit must also be given to the many users who have made
		   suggestions for improving the program.  Many of their
		   suggestions have been incorporated into WeatherFAX.


SUPPORTED CONFIGURATIONS
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

  MACHINE REQUIREMENTS

		   o WeatherFAX Card

		   o IBM PC or compatible computer that uses the standard
		     PC-bus architecture.

		   o RAM (Random Access Memory):
		     - 512 kbytes or more of memory:
		       In most configurations, approximately 190 kbytes
		       of memory is required for DOS, the WeatherFAX
		       program and drivers loaded by CONFIG.SYS.  All of
		       the remaining memory is available for image storage.

		     - Expanded Memory (optional)
		       LIM 4.0 expanded memory allows up to 16 Mbytes
		       for image storage.  Requires both expanded memory
		       and a LIM 4.0 software driver.

		   o A graphics monitor and video adapter card including
		     - Color/Graphics Adapter (CGA)
		     - Enhanced Graphics Adapter (EGA)
		     - Multi-Color Graphics Array (MCGA).
		     - Video Graphics Array (VGA)
		     - Extended VGA (800 x 600 pixel resolution)










		 WeatherFAX User's Guide                 Page 5



		   o One diskette drive (one of the following):
		     - 5.25-inch drive (360 kbytes)
		     - 3.5-inch drive (720 kbytes).

		   o Fixed disk (optional)

		   o Printer: (optional)

		     Printer types and print resolution - dots per inch (dpi)
		     ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
		     - All standard 9-pin dot-matrix printers  (120 dpi)
		     - All standard 24-pin dot-matrix printers (180 dpi)
		     - IBM Pageprinter 3812		       (240 dpi)
		     - PCL command compatible printers	       (300 dpi)

		   o Receiving equipment and antenna for the frequencies you
		     want to cover.

  PROGRAM REQUIREMENTS

		   To run the WeatherFAX software, you need:

		     o IBM Personal Computer Disk Operating System (DOS)
		       Version 3.0 or later


INSTALLATION INSTRUCTIONS
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

  INSTALLING THE WEATHERFAX ADAPTER

		   Refer to the Guide to Operations for your computer
		   for instructions for installing cards.  You will need
		   to turn the computer off and remove the cover from
		   the computer to insert the fax card into an unused
		   card socket.

  CONFIG.SYS MODIFICATIONS

		   No changes to CONFIG.SYS are normally needed.  However,
		   if you ever get the error message "DRIVE NOT READY"
		   when retrieving very large files (1 Mbyte or larger),
		   the reason may be the assignment of an insufficient
		   number of DOS buffers.  Try increasing the number of
		   buffers by adding the statement BUFFERS=64 to the
		   CONFIG.SYS file.

  AUTOEXEC.BAT MODIFICATIONS

		   NOTE FOR USERS HAVING THE ORIGINAL IBM CGA DISPLAY
		   ADAPTER.  (Does not apply if you are using a PS/2*
		   computer or a VGA or EGA Display adapter).  The CGA
		   adapter ROM does not include the entire graphics
		   character set.  You will need to load the DOS graphics-








		 WeatherFAX User's Guide                 Page 6



		   character-set driver GRAPHICS.COM into memory.  The
		   driver is available on the DOS diskette.  Add the
		   statement  GRAPHICS.COM  to your DOS AUTOEXEC.BAT file
		   to load the driver every time you start your computer.
		   If GRAPHICS.COM is in a subdirectory, supply the
		   necessary path information on the driver statement.
		   For example:  C:\DOS\GRAPHICS.COM

		   When using this program, make sure your AUTOEXEC.BAT
		   file is "clean."  Some terminate-stay-resident (TSR)
		   programs--especially those that control screen functions
		   (such as screen blanking) may interfere with the proper
		   operation of the software.  If you experience difficulty
		   when running the fax software, check your AUTOEXEC.BAT
		   file first.

  COPYING THE DISKETTE

		   Copy the WeatherFAX diskette and save the original
		   diskette in a safe place.  You can copy the diskette
		   to either a hard disk or to another diskette.  Refer
		   to your DOS manual for instructions for copying
		   diskettes.  The WeatherFAX program is not copy protected.

  STARTING THE PROGRAM

		   Start the WeatherFAX program by typing FAX.EXE from
		   the DOS command line.

		   Optional Command Line Parameters:
		   ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
		   ³ Syntax: FAX [options]			       ³
		   ³	 Where options are:			       ³
		   ³						       ³
		   ³ /E     = Use Expanded (EMS) memory if installed.  ³
		   ³	      Requires LIM 4.0 driver.		       ³
		   ³ /C     = Use conventional memory.		       ³
		   ³ /A     = Go into acquire mode		       ³
		   ³ /Ffile = Go into acquire mode, save next image to ³
		   ³	      disk with the given file specification,  ³
		   ³	      then exit to DOS. 		       ³
		   ³ /Hxx   = BIOS display mode for 800x600 resolution ³
		   ³	      mode.  See section 'Using Extended VGA   ³
		   ³	      (800x600 Pixel) mode'.                   ³
		   ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

		   NOTE: Program will automatically use EMS memory if
		   the available EMS memory size is greater than the
		   conventional memory size.

		   Examples:
		     C:>FAX /FC:NEWFILE.TIF
		       Allows unattended operation.  Program automatically
		       goes into capture mode, stores next image into








		 WeatherFAX User's Guide                 Page 7



		       disk file C:NEWFILE.TIF, then exits to DOS.
		       This allows you to use an external timer to start
		       the computer at a preselected time.  A batch file
		       would then instruct WeatherFAX to save the next
		       image into a specified file.

		     C:>FAX /H54
		       Enables 800 x 600 pel resolution mode for ATI
		       VGAWonder compatible card.  See the section:
		       Using Extended VGA (800 X 600 Pixel) mode.


GETTING STARTED
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

  GETTING HELP INFORMATION

		   Help information is available anytime you see 'F1=Help'
		   displayed on the screen.  You can access Help by
		   pressing the 'F1' key on your keyboard.  You can
		   quit viewing Help by pressing the 'Esc' key on
		   your keyboard.

  TESTING THE ADAPTER

		   Test the fax adapter by using the Test option on the
		   Main Menu.  The various tests will indicate whether
		   the adapter is operating within its correct operating
		   region.  If any of the tests indicate that the adapter
		   needs calibration, refer to the section: Calibrating
		   the adapter.

		   Static Test
		     This test is used to check for normal operation and
		     calibration.  The nominal parametric values on the
		     adapter are displayed.  All of the marks should be
		     in the 'OK' region.

		   Dynamic Test
		     A test signal is applied to the input of each function
		     and the output is checked for correct operation.
		     The Start and Stop Detectors are tested for both
		     ON and OFF states.  The FM and AM Detectors are
		     tested to verify linear operation.

		   AM Graph Test
		     A test signal is applied to the AM Detector at
		     various amplitudes and the output linearity is
		     displayed.  The graph line should be straight and
		     sloping upward.

		   FM Graph Test
		     A test signal is applied to the FM detector at various
		     frequencies and the output linearity is displayed.








		 WeatherFAX User's Guide                 Page 8



		     The graph line should be straight, sloping upward,
		     and centered between 0 and 256.


  SELECTING YOUR PRINTER TYPE AND DISPLAY MODE

		   Go to the fax menu to specify the Display Mode and
		   Printer type.

		   You can select a compatible printer type from the list
		   of supported printers.  Check your printer documentation
		   to determine which of the supported types that it emulates.

		   Printers supported and print resolution (dots per inch)
		   ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
		   ³ Epson compatible 8-pin printers	(120 dpi) ³
		   ³   - Epson FX, MX, RX, LX series		  ³
		   ³   - IBM Graphics or Proprinter		  ³
		   ³   - Okidata 192I+, 193I+, 292, 293 	  ³
		   ³   - Okidata in IBM-compatible mode 	  ³
		   ³   - Panasonic KX-P1080i, P1091i, P1093	  ³
		   ³   - Cannon PW-1156A			  ³
		   ³   - Citizen MPS-25 			  ³
		   ³   - Star Micronics: Gemeni 10X		  ³
		   ³						  ³
		   ³ Okidata compatible 8-pin printers	(120 dpi) ³
		   ³   - Okidata 192, 193			  ³
		   ³						  ³
		   ³ Apple ImageWriter II		(160 dpi) ³
		   ³						  ³
		   ³ Epson  24-pin compatible printers	(180 dpi) ³
		   ³   - Epson LQ series			  ³
		   ³   - IBM Proprinter X24 and XL24		  ³
		   ³						  ³
		   ³ Toshiba 24-pin compatible printers (180 dpi) ³
		   ³   - Toshiba P321, P341, P351		  ³
		   ³						  ³
		   ³ IBM Pageprinter 3812		(240 dpi) ³
		   ³						  ³
		   ³ PCL command compatible printers	(300 dpi) ³
		   ³   - HP LaserJet series II			  ³
		   ³   - HP DeskJet				  ³
		   ³   - Apple LaserWriter II			  ³
		   ³   - IBM LaserPrinter			  ³
		   ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

		   NOTE:
		   If you are using a printer attached to the serial port
		   (COM1), you need to set up the serial port using the
		   DOS MODE command before starting the WeatherFAX program.
		   These commands could be placed in your AUTOEXEC.BAT file.
		     1) Set the baud rate and other parameters with the
			DOS MODE command.  (e.g., MODE COM1:96,N,8,1,P)









		 WeatherFAX User's Guide                 Page 9



		     2) Redirect LPT1 to COM1 with the DOS MODE command
			(e.g., MODE LPT1=COM1)

		     3) Start WeatherFAX program and set the Printer
			Destination in the SETUP MENU to LPT1

		   Serial port printers are usually configured for either
		   7-bit or 8-bit graphics mode.  Be sure that the printer
		   is configured for 8-bit mode.  Otherwise, the printed
		   sample will have a blank row (space) every 8 lines.


  CONNECTING YOUR COMPUTER TO YOUR FAX RECEIVER

		   Use a two-wire cable to attach the fax adapter to
		   your fax receiver.  The cable should have a standard
		   3.5-mm phone plug on the end that plugs into the
		   adapter.  Plug the cable into either the receiver
		   earphone jack or fax output jack.


USING WEATHERFAX
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ


  ADJUSTING THE PAGE ALIGNMENT

		   You will need to set the page alignment the first
		   time you use the adapter.  The page alignment
		   synchronizes the timing of the computer with the
		   fax image.  The image will appear slanted across
		   the display screen when the page alignment needs
		   to be changed.  Once set, the page alignment will
		   not normally need to be changed again.

		   The alignment is set while an image is being received.
		   The procedure is listed below.

		   1) Begin receiving an image into computer memory.  Set
		      fax parameters and select the Acquire fax action.
		      The program will automatically capture the next image
		      into the computer storage.  After the adapter has
		      started to display an image, go to step 2.

		   2) Use the cursor down (down-arrow) key until the
		      page alignment function is selected.  If the image
		      slants to the right, use the cursor left (left-arrow)
		      key to decrease the alignment value.  Otherwise,
		      use the cursor right (right-arrow) key to increase
		      the alignment value.  Continue adjusting until the
		      image appears perfectly vertical.  The alignment
		      value is automatically stored in the program file
		      on disk so that the image is perfectly aligned
		      each time you use the program.








		 WeatherFAX User's Guide                 Page 10



  GETTING THE IMAGE

	      1) SET THE FAX PARAMETERS.

		   o ADAPTER MODE.  The fax card can capture three types
		     of weather facsimile images:

		     - Marine Weather Facsimile.  These images are received
		       on HF radio on shortwave radio frequencies
		       (e.g., 8080 kHz).  The adapter is set to FM mode.

		       The fax adapter allows the FM Marine fax signal to be
		       within a wide amplitude range.  However, if the signal
		       output from your receiver is very strong or very weak,
		       you can compensate by adjusting attenuation pads on the
		       adapter. The F4 key allows you to change the pads.
		       Usually, you will keep the attenuation set at NORMAL.
		       This setting allows operation for input-signal
		       amplitudes that vary between -20 dBm to +10 dBm.

		     - WEFAX image.  This is the format for geostationary
		       weather satellites.  The receiver is usually tuned
		       to S-Band 1691 MHz.  The adapter is set to AM mode
		       and Automatic Gain Lock (AGL) is used to automatically
		       set the correct level for any type of image.

		       AGL determines the optimum gain setting at the
		       beginning of every image and fixes the gain level
		       for the duration of the image.  This technique
		       provides a distortion free high dynamic range
		       image each time, whether the image capture is
		       started automatically or manually.

		     - Polar image.  These are images transmitted from polar
		       orbiting satellites at VHF 137.x MHz. The adapter
		       is set to AM mode and a fixed gain level is used.

		       The F5 key allows you to set the gain of the fax
		       adapter so that the signal level is just right.
		       Use the cursor keys to increase or decrease the
		       signal level while an image is active so that the
		       level covers a wide dynamic range without exceeding
		       the MAX (clipping) value.

		   o SCANS PER MINUTE
		     Selects the number of image lines sampled every minute.
		     Use the same value as that of the signal that you
		     receive.  Typically GOES satellites are 240, Polar
		     satellites are 120, and HF fax signals are 120.

		   o PELS PER SCAN LINE
		     Selects the number of samples (pixels) stored for each
		     image line.  You would typically set this value to be at
		     least as large as the resolution of your graphics display








		 WeatherFAX User's Guide                 Page 11



		     mode (e.g., 640 for EGA or VGA).

		     This sets the resolution of the image and affects the
		     amount of computer storage needed to hold the image.
		     The equation for image size (bytes) is:

		     IMAGE_SIZE = PELS_PER_LINE * NUM_LINES / PELS_PER_BYTE

		     Where:
			 PELS_PER_LINE = pixels stored for each image line
			 NUM_LINES     = lines in the image
			 PELS_PER_BYTE = pels stored per byte, either 1 or 2

		     NOTE: The greater the number of Pels Per Line the greater
			 the image resolution.	However the maximum value may
			 be limited by the speed of your computer.  For
			 earlier PCs having a 4.77-MHz clock speed use a
			 maximum value of 700 when using 240 Scans Per Minute.

		     The 'squareness' of the displayed image depends upon
		     the Index of Cooperation (IOC) of the received image, the
		     Pels Per Line setting, and the aspect ratio of your display
		     adapter.  The relationship for these parameters is:

			 PELS_PER_LINE = ã * IOC * ASPECT

		     Where:
			 ã	= Pi = 3.14
			 IOC	= Index of Cooperation of received signal
				  GOES (WEFAX)	      = 268
				  polar satellites    = 288
				  HF fax (Marine)     = 576
			 ASPECT = horizontal/vertical pixel density set by
				  adapter display mode, not the physical
				  size of the display.
				  Extended VGA, VGA   = 1.00
				  EGA (640x350)       = 0.73 approximately
				  CGA, MCGA	      = 0.83 approximately

		     Example: If you want to receive WEFAX (IOC = 268) in VGA
			 display mode for a square picture, use 842 pels
			 per line.

		   o PELS PER BYTE
		     The fax program uses all of the available memory
		     in your computer to capture images.  The image size
		     can be calculated by the formula:

		       SIZE = PELS_PER_LINE * NUMBER_OF_LINES / PELS_PER_BYTE



		     PELS_PER_LINE and PELS_PER_BYTE control the image
		     resolution and number of grayshades.  If you








		 WeatherFAX User's Guide                 Page 12



		     have limited memory (less then 512 kbytes), consider
		     selecting 2 pels per byte.  This value saves memory
		     by packing two pixels into each memory storage byte,
		     which allows you to capture images twice as large.
		     The image is stored with 16 gray shades and once
		     captured, you cannot enhance the brightness and contrast.

		     If you have more then 512 kbytes of memory or expanded
		     memory (LIM 4.0), you should select 1 pel per byte.
		     The image is stored with up to 256 shades of gray,
		     and you can enhance the brightness and contrast of
		     the image at any time.

	      2) SELECT ACQUIRE FAX ACTION.

		   You must have a fax card installed in your computer
		   and your fax receiver must be attached to the card
		   with a cable.  The program will automatically capture
		   the next image from the fax receiver into the computer's
		   memory.  If the first image appears slanted, the page
		   alignment needs to be adjusted.

		   The bottom line of the display is the action line.
		   It displays the current receive status and allows you
		   to select various actions while receiving the image.
		   Different actions are displayed using the cursor keys.

		   ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
		   ³ ACTION LINE SELECTIONS				 ³
		   ³							 ³
		   ³ Manual start	    Press <ÄÙ for manual start	 ³
		   ³ Move/scroll image	    <- -> keys scroll left/right ³
		   ³ Darker -		    <- -> to adjust brightness	 ³
		   ³ Adj contrast	    <- -> to adjust contrast	 ³
		   ³ Printer: on/off	    <ÄÙ   to turn printer on/off ³
		   ³ Disk   : on/off	    <ÄÙ   to save to disk on/off ³
		   ³ Page alignment	    <- -> adjust timing.	 ³
		   ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

		   Disk allows you to save the image to disk as it is stored
		   in memory.  You will be prompted for the filename to use.

		     NOTE: The Disk function has been tested on IBM
		     computers.  However, the BIOS of some computer
		     clones disable interrupts when saving to disk;
		     that will cause part of the received image to be
		     lost.  When this happens, part of the image will
		     appear shifted.  Do not use this function if you
		     have this type of clone computer.

		   Page alignment allows you to adjust the adapter timing
		   if the image is slanted.  Once adjusted, the timing
		   should not need to be changed again.  Use cursor keys
		   to increase and decrease the timing value.  Increase








		 WeatherFAX User's Guide                 Page 13



		   if the image slants to the left.  Decrease if the
		   image slants to the right.

		   ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
		   ³ RECEIVE STATUS			     ³
		   ³					     ³
		   ³ Wait	 : Waiting for start signal  ³
		   ³ Start	 : Start signal detected     ³
		   ³ Sampling	 : Putting image into buffer ³
		   ³ End of mem  : Image size exceeds buffer ³
		   ³ Stop	 : Stop signal detected      ³
		   ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

	      3) EXIT ACQUIRE MODE

		   After image is captured, press the Esc key exit to
		   the Fax Acquire Menu.  Press Esc again to exit to
		   the Fax Action Menu.  From the Fax Action Menu you
		   can view or print the image.

  VIEWING THE IMAGE

		   You can view an image once it is stored in memory.
		   The image may be either retrieved from disk, or
		   acquired from the fax card.	You can then view the
		   image with different display modes, scroll, zoom,
		   and enhance the image details in several ways.

		   DISPLAY MODE
		     You can view the image with different display modes to
		     change the resolution and palette range.  Change the
		     display mode using the Setup Menu.

		     Example:
		     VGA mode has high resolution (640 x 480), so most or all
		     of the image may be displayed.  However only 16 colors
		     (or grayshades) are viewable at a time.

		     However, by selecting MCGA mode with a lower resolution
		     (320 x 200), small details of interest in the image may
		     be more easily seen.  Also with MCGA mode, you can
		     highlight details with 64 grayshades.  If you use
		     50 percent zoom you can see almost the same area as VGA
		     mode but with more grayshades.

		   The cursor keys will allow you to scroll the image
		   up, down, right, and left while in Scroll Mode.
		   Also, you can press the Alt key and either the F1,
		   F2, F3, or F4 keys to select one of the four color
		   look-up tables (LUT).












		 WeatherFAX User's Guide                 Page 14



		     ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
		     ³ In Scroll Mode the active keys are:	     ³
		     ³						     ³
		     ³ cursor keys:	scroll up, down, right, left ³
		     ³ Home		go to top of image	     ³
		     ³ End		go to bottom of image	     ³
		     ³ F1		help information	     ³
		     ³ Esc		- return from help	     ³
		     ³			- abort when writing screen  ³
		     ³			- return to last screen      ³
		     ³ Alt/F1..F4	Select color table	     ³
		     ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

		   If you press the space bar while viewing the image, an
		   action line appears and the mode changes to Action Mode.

		   Use the cursor keys to chose an action, then press
		   the Enter key.  The different image enhancement
		   selections are described below.  Press the Esc key
		   to return to Scroll Mode.

		   ENHANCEMENT
		     You can change the contrast and brightness using the
		     Enhancement menu if the image was captured with
		     1 Pel Per Byte.  The menu displays a histogram and an
		     adjustment scale which are used as visual aids to help
		     adjust the image brightness and contrast.
		     This changes the display Look Up Table (LUT).
		     The actual image data is not changed.  The LUT assigns
		     each of the 256 brightness levels in the image to the
		     limited number of levels displayable by the graphics
		     adapter.

		     The histogram displays a chart of the distribution of
		     brightness values in the displayed image.	The horizontal
		     axis displays the brightness level between 0 and 255.
		     The vertical axis displays the number of pixels for
		     each brightness level.

		     The adjustment scale "[   ³   ]" indicates both the
		     contrast range and brightness level.  The center mark
		     "³" indicates the brightness level.  You can make
		     the image darker by moving the "³" to the right using
		     the right arrow key.  The "[ ]" marks indicate the
		     contrast range.  The contrast is increased by moving
		     the "[ ]" marks closer together.

		     You can use the visual aids for two types of image
		     enhancement: optimize overall picture or; detailed
		     analysis of a particular item of interest.

		     OVERALL PICTURE ADJUSTMENT
		     1) Use the histogram to locate the right and left edges
			of the curve where the number of pixels decreases.








		 WeatherFAX User's Guide                 Page 15



		     2) Adjust the brightness so that the "³" mark is
			centered between the edges on the histogram.
		     3) Adjust the contrast range so that the "[  ]" marks
			are directly under the right and left edges of the
			curve respectively.

		     DETAILED ANALYSIS
		     This provides more detailed enhancement of specific
		     areas of the image at the expense of the rest of the
		     image.  For example you may want to detail the
		     temperature gradients of the Atlantic Ocean to locate
		     the Gulf Stream.
		     1) As you adjust the brightness the level corresponding
			to the "³" mark will briefly flicker or select the
			corresponding level in the image.  Adjust the
			brightness until you select the area to analyze.
		     2) Adjust the contrast range so that the "[  ]" marks
			cover the desired image intensity range.  Finding
			the best contrast range will probably require several
			trial-and-error adjustments.

		     When you exit the window with the Esc key the display
		     is redrawn with the new Brightness and Contrast values.
		     The values are also used for printing the image.

		   PALETTE
		     You can change the colors and gray scales of the
		     image by changing the look-up tables (LUT) that
		     define the way the image is displayed.  With VGA,
		     EGA, and MCGA, 4 tables can be defined.  For each
		     table, you can adjust the red, green, and blue
		     colors separately.  The table number is displayed
		     at the top of the panel.  While the image is
		     displayed you can change to a different tables at
		     any time by pressing the Alt key and either F1, F2,
		     F3, or F4.

		   ZOOM
		     You can select a Zoom of 50, 100, 200 or 400 percent.
		     The 50 percent zoom is useful for shrinking the image
		     to half size to display more of it at one time.  The
		     200 and 400 percent zooms can be used to enlarge the
		     image to better display small details of interest.

		   NEGATIVE IMAGE
		     This displays the negative view of the image similar
		     to a photographic negative.  This option is set using
		     the Zoom menu.

		   ROTATE 180 DEGREES.
		     Rotate turns the picture upside down for viewing.
		     This is useful for viewing images from ascending-node
		     (South-to-North track) polar-orbiting satellites that
		     send images upside down.








		 WeatherFAX User's Guide                 Page 16



  PRINTING THE IMAGE

		   Before printing for the first time, use the Setup Menu
		   to select your printer.  You can print the image
		   either to a printer connected to your computer's
		   printer port or to DOS device name.	The device name
		   could be a file name or the name of a printer attached
		   to a Local Area Network.

		   You can print the entire image or just the part
		   displayed on the screen.  The image is printed starting
		   at the top and left side displayed on the screen.
		   This allows you to trim the top and align the left-hand
		   side before printing.

		   You can print the image in black and white, or with
		   a choice of various gray-scale dithering patterns.
		   Dithering is a printing method of using a series of
		   dots in an area to simulate gray information in the
		   same way that a newspaper would via the halftone
		   technique.  The dither patterns allow your image to
		   be printed with up to 16 gray shades.

		   Because of the lower resolution of 9-pin dot-matrix
		   printers, you will get good results using either black
		   and white, or 2- and 4-gray-shade dithering patterns.

		   For 24-pin dot-matrix and laser printers, you will
		   get excellent results with all of the dithering
		   patterns including the 16 gray-shade dithers.  The
		   16 gray-shade dithers available are:

		     ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
		     ³ BAYER	       ³ Brings out detail at the expense   ³
		     ³		       ³   of tonal reproduction (contrast).³
		     ³		       ³   Used for very detailed images.   ³
		     ³ FATTING	       ³ Good compromise between detail     ³
		     ³		       ³   and good tonal reproduction.     ³
		     ³ VERTICAL LINE   ³ Emphasizes horizontal lines.	    ³
		     ³ HORIZONTAL LINE ³ Emphasizes vertical lines.	    ³
		     ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

		   Choosing the best dithering pattern for an image is
		   a matter of both experimentation and experience.  The
		   Fatting dither offers a good compromise between
		   detail and contrast and is commonly used.

		   The printhead on some printers may overheat when printing
		   large images.  If this happens the printer will go into
		   a pause mode to cool down.  If the wait is longer than
		   approximately 20 seconds, the program will time-out and
		   quit waiting for the printer to resume.










		 WeatherFAX User's Guide                 Page 17



		   If the printhead overheats:
		   - wait for a few minutes for the printer to cool before
		     printing another image.
		   - configure the printer for Unidirectional printing instead
		     of Bidirectional printing.  This will slow the printer
		     and allow more time for cooling.
		   - Use the DOS MODE command to prevent the printer time-out
		     condition and to allow the printer to resume printing
		     the image after the printhead has cooled down
		     (e.g.,MODE LPT1:,,P).  This DOS command could be placed
		     in the AUTOEXEC.BAT file so that it is executed every
		     time the computer is started.

		   NOTE:
		     If you're using the graphics driver shipped with
		     DOS 4.0 (or later), the 'Shift/Print Screen' keys
		     on the computer keyboard can be used to print a
		     very crude representation of the image.  The DOS
		     GRAPHICS.COM driver must first be loaded into
		     memory.  The graphics driver shipped with DOS 4.0
		     supports VGA graphics mode.


  SAVING THE IMAGE TO DISK

		   You can save either the entire image or just the part
		   displayed on the screen.  The image is saved starting
		   at the top and left side displayed on the screen.
		   This allows you to trim the top and align the left
		   hand side before saving to disk.

		   You can save the image using either the standard TIFF
		   (Tag Image File Format) or GIF (Graphics Interchange
		   Format).  TIFF has fast file operations and stores an
		   image as an uncompressed raster-scan gray-scale image.
		   GIF is the standard format used for storing images by
		   CompuServe and other computer bulletin boards systems
		   (BBS).  GIF is much slower than TIFF, but uses an efficient
		   compression algorithm that minimizes file size and saves
		   disk space.

		   These standard image file formats allow images to be
		   imported as graphics files into various painting and
		   Desktop Publishing applications that support either
		   of the formats.

		   TIFF files are supported by Aldus PageMaker, IBM Image
		   Edit, Logitech PaintShow, and WordPerfect 5.0.  Image
		   Edit is excellent for modifying large TIFF image files.
		   GIF format files are used by many computer bulletin
		   board systems (BBS) and are supported by Compuserve
		   CSHOW and several painting programs.










		 WeatherFAX User's Guide                 Page 18




ADDITIONAL INFORMATION
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

  CALIBRATING THE ADAPTER

		   WeatherFAX card physical layout

		   ÚÄÄÄÄÝÛÄÄÄÄÄÄÝÛÄÄÄÄÄÄÄÄÄÄÄÝÛÄÄÄÄÄÄÄÄÄÝÛÄÄÄÄÄÄÄ¿
		   ³  ÚÄÛÛÄ¿  ÚÄÛÛÄ¿	   ÚÄÛÛÄ¿     ÚÄÛÛÄ¿	 ³ÚÄÄÄ
		   ³  ³POT2³  ³POT4³	   ³POT3³     ³POT1³	 ³³
		   ³  ÀÄÄÄÄÙ  ÀÄÄÄÄÙ	   ÀÄÄÄÄÙ     ÀÄÄÄÄÙ	 ³³
		   ³   Stop    Start	     AM 	FM	 ³³
		   ³ Detector  Detector   Demodulator  Demod. ÛÛÛÛÛ <Ä¿
		   ³  450 Hz   300 Hz	   2400 Hz    1800 Hz ÛÛÛÛÛ  phono
		   ³						 ³³  jack
		   ³						 ³³
		   ³						 ³³
		   ³						 ³³
		   ³						 ³³
		   ³						 ³³
		   ³						 ³³
		   ÀÄÄÄÄÄÄÄÄÄ¿				     ÚÄÄÄÙ³
			     ÀÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÙ	  ³


		   Calibration is needed if any of the Self-Tests indicate
		   that the card is operating out of the indicated
		   operating range.  The self tests will indicate which
		   parameter is out of range and needs adjustment.

		   Instructions are provided below for making the adjustment.
		   The procedure is simple and can be performed without
		   special tools or knowledge.	Because adjustments are
		   made while the computer is powered on it is recommended
		   the adjustment be done by a qualified service
		   technician.

		   A non-metallic screwdriver should be used for the
		   adjustment.	This will prevent damage to the computer
		   if the screwdriver should accidentally be dropped
		   into the computer.

		   1) Turn power to the computer off.
		   2) Remove the cover of the computer.  Refer to the
		      Guide to Operations for your computer for
		      instructions for removing the cover.
		   3) Locate the fax card.
		   4) Turn computer power on and start the WeatherFAX
		      program.
		   5) Select Test Adapter, and then Static Test.
		      Adjust the potentiometers for the parameter out
		      of range.  When you are finished all parameters
		      should be in the 'OK' region.








		 WeatherFAX User's Guide                 Page 19



		   6) The final adjustment for the FM demodulator should
		      be done while viewing the FM Graph Test.	The line
		      should be linear, sloping upward with time, and
		      centered between 0 and 256.  If not centered adjust
		      the FM potentiometer while viewing the Graph.

  USING EXPANDED MEMORY (LIM 4.0)

		   Expanded memory eliminates the problem of acquiring
		   images that are too large for the computer's 640 kbytes
		   of conventional memory.  LIM (Lotus Intel Microsoft)
		   4.0 allows up to 16 Mbytes for image storage.  It
		   requires both expanded memory and a LIM 4.0 software
		   driver.  The WeatherFAX program will automatically
		   use either conventional or expanded memory based upon
		   the larger available amount of RAM.

		   If you have an 80386 type computer then EXTended
		   memory can emulate LIM 4.0 EXPanded memory by
		   using a device driver shipped with DOS 4.0.

		   The EXTended memory on 80286-type computers cannot
		   emulate EXPanded memory.  You must use an actual
		   LIM 4.0 capable memory card.

		   EMS SIMULATORS using either a hard disk or EXTended
		   memory are not supported because of the 'data aliasing'
		   problem that is inherent with simulators.

  USING EXTENDED VGA (800 X 600 PIXEL) MODE

		   If you have a multifrequency (multisync) monitor and
		   a graphics card that supports the extended 800 X 600 graphics
		   mode, you can display images in this mode.
		   Because different cards use different 800 by 600
		   modes, you must specify the mode as command line
		   parameter when starting FAX.EXE.  To specify the
		   graphics mode:

		     FAX.EXE /Hxx	 where: 'xx' is the hex mode.

		   Examples:
		   For ATI VGAWONDER the hex mode is 54 ->   FAX.EXE /H54
		   For Paradise Plus the hex mode is 58 ->   FAX.EXE /H58

		   Be sure to check that you have the correct monitor
		   and graphics card.  The software does not verify the
		   monitor or graphics card.  Selected cards and their
		   respective 800 X 600 graphics mode (hex) are listed
		   below.  If your graphics card is not listed, you'll
		   have to consult your card's user's guide to determine
		   the correct mode.










		 WeatherFAX User's Guide                 Page 20



		     ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄ¿
		     ³ CARD				 ³ MODE ³
		     ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄ´
		     ³ ATI VGAWONDER			 ³ /H54 ³
		     ³					 ³	³
		     ³ Paradise VGA Plus/Professional	 ³ /H58 ³
		     ³ AST VGA Plus			 ³ /H58 ³
		     ³ Compaq VGA			 ³ /H58 ³
		     ³ Dell VGA 			 ³ /H58 ³
		     ³					 ³	³
		     ³ Video7 VRAM/Fastwrite		 ³ /H62 ³
		     ³					 ³	³
		     ³ Genoa Super VGA/VGA Hi-Res	 ³ /H29 ³
		     ³ Orchard Designer VGA		 ³ /H29 ³
		     ³ Sigma VGA/H			 ³ /H29 ³
		     ³ STB VGA Extra			 ³ /H29 ³
		     ³					 ³	³
		     ³ Everex EVGA			 ³ /H70 ³
		     ³					 ³	³
		     ³ Tecmar VGA-AD			 ³ /H18 ³
		     ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÙ

		   NOTE:
		   You may need to adjust your multisync monitor to
		   display the 800 X 600 graphics mode properly.  Use
		   the vertical and horizontal size and position controls
		   on your monitor to display the entire image without
		   distortion.

  SOURCES OF WEATHER-FACSIMILE SIGNALS

		   There are three direct sources for weather-fax signals:
		   geostationary satellites; polar-orbiting satellites;
		   and Marine weather-radio transmitters.  The fax card
		   along with the WeatherFAX software can capture all
		   the above types of facsimile.  Tone detectors on the
		   card will automatically detect the beginning and
		   ending of each image.

		   Geostationary Satellites.
		     Geostationary satellites include US GOES, European
		     Space Agency METEOSAT, and Japanese GMS.  These
		     spacecraft broadcast on S-Band frequencies; GOES
		     at 1691 MHz and Meteosat at 1694.5 MHz.  These
		     satellites are located approximately 22,000 miles
		     above the Earth and provide WEFAX (Weather Facsimile)
		     transmissions using the standard Automatic Picture
		     Transmission (APT) format.  Reception of WEFAX
		     images require an antenna, downconverter, and receiver
		     The antenna can be either a small parabolic dish or
		     a loop Yagi.  The downconverter converts the S-Band
		     signal to 137.5 MHz.  An inexpensive scanner radio
		     may be used for the receiver.  A phone cable from
		     the receiver plugs into the WeatherFAX card.








		 WeatherFAX User's Guide                 Page 21



		     Configure the software for AM mode and 240 scans
		     per minute.

		   Polar-Orbiting Satellites.
		     These satellites transmit on VHF frequencies between
		     137 and 139  MHz.	The NOAA (TIROS-N) series
		     transmit at 137.50 MHz and 137.62 MHz.  The Russian
		     Meteor series satellites transmit at 137.15, 137.3
		     and 137.850 MHz.  A general-purpose scanner receiver
		     capable of receiving the frequencies between
		     136-138 MHz is required.  Many of the newer Regency,
		     Uniden, and Radio Shack scanners cover this frequency
		     range and give excellent results.	This receiver can
		     also be used in conjunction with the geostationary
		     satellite antenna and downconverter.  Configure the
		     software for AM mode and 120 scans per minute.

		   Marine weather radio facsimile.
		     These broadcasts can be received direct from government
		     radio transmissions.  There are over 65 transmitter
		     sites worldwide which utilize over 200 different
		     radio frequencies.  The information transmitted
		     includes weather-analysis charts, satellite pictures,
		     and radar charts.	These radio signals are received
		     on short wave radio frequencies (e.g., 8080 kHz) on
		     Upper Sideband.  A stable general coverage single
		     sideband (SSB) receiver is required.  The published
		     frequency is normally the center frequency of the
		     upper sideband.  Tune your SSB receiver approximately
		     1600-1700 Hz below the published frequency.  For example,
		     the US Navy Fleet Weather Station at Norfolk (NAM),
		     transmits at 8080 kHz.  Tune your receiver to 8078.3
		     kHz (USB) to receive its transmissions.  Configure
		     the software for FM mode and 120 scans per minute.

  DECODING RTTY

		   Many weather radiofacsimile transmitters broadcast
		   radioteletype messages in addition to charts and
		   images.  These are primarily coded surface and upper
		   air reports from around the world.
		   - Surface Reports contain temperature, dew point,
		     wind speed and direction, altimeter, present weather,
		     past weather, 6-hour precipitation amounts, cloud
		     coverage, snow accumulation, high and low temperature,
		     and occasional text information.
		   - Upper Air Reports contain temperature, dew point,
		     wind speed and direction at standard and variable
		     levels of the atmosphere.
		   These RTTY messages are usually transmitted at 100
		   WPM with normal sense and 850-Hz wide shift.
		   WeatherFAX allows you to receive these RTTY broadcasts
		   with standard Baudot speeds from 60 to 133 words per
		   minute.  A stable, general-coverage, single sideband








		 WeatherFAX User's Guide                 Page 22



		   (SSB) receiver is required.	You can select normal
		   or reverse sense.  Reception is in FM mode.	You can
		   send the RTTY messages to your printer or a disk file.

		   NOTE: This product is not suitable for general-purpose
		   Amateur radio RTTY decoding.  It has limited performance
		   in noisy environments and with narrow shifts.  It is
		   primarily intended to decode RTTY from HF fax stations
		   that broadcast both RTTY and fax.


  WEATHERFAX SPECIFICATIONS

		   o Recording Rate : 60, 90, 120, 240 SPM
		     (Scans Per Minute)

		   o Index of cooperation IOC
		     576 - Marine fax
		     288 - TIROS
		     267 - WEFAX (GOES)

		   o FSK input	: 1500 Hz "black", 2300 Hz "white"

		   o FSK input level  :  Range selectable by pads.
		     -10 dBm to +20 dBm   Strong Signal
		     -20 dBm to +10 dBm   Normal Signal
		     -30 dBm to   0 dBm   Weak Signal

		   o AM input	:  2400 Hz AM modulation
		     lower voltage  = "black"
		     higher voltage = "white"

		   o AM input level : -20 dBm to +10 dBm.

		   o Input impedance:  10 kilohms
		   o Control signals   Automatic start, frame, and stop
		     with manual start and frame.

		     - START : Signal modulated between "black" and
		       "white" at 300 Hz rate for 5 seconds.

		     - STOP : Signal modulated between "black" and
		       "white" at a 450 Hz rate for 5 seconds.

		     - FRAME : "black" signal interrupted by a short
		       burst at a "white" signal each scan line for 5
		       seconds immediately following start signal.

		   o Hardware interrupt    8 (BIOS timer interrupt)

		   o I/O Addresses   386H and 387H











		 WeatherFAX User's Guide                 Page 23



		   o Voltage & current requirements
		     ÚÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄ¿
		     ³ Voltage ³ Current ³
		     ÃÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄ´
		     ³	+ 5V   ³ 120 ma  ³
		     ³	+12V   ³  25 ma  ³
		     ³	-12V   ³  15 ma  ³
		     ÀÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÙ


IF YOU HAVE DIFFICULTY
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

		   SYMPTOM	SOLUTION
		   ÄÄÄÄÄÄÄÄÄÄÄÄÄ ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

		   NO PICTURE	 1) Run fax card tests to assure that
				    the card is operating within the
				    correct range.
				 2) Verify that Adapter Mode is set correctly
				    for the facsimile signal.
				 3) For Marine fax mode verify that the
				    receiver signal level is within the
				    range of the fax card attenuation
				    pads.  If the signal level is very weak
				    then decrease the attenuation pads using
				    the F4 key on the adapter mode menu.
				 4) Is the fax receiver powered on and the
				    cable connected to the fax adapter?

		   DISTORTED	 1) Verify that the Adapter Mode is set
		   PICTURE	    correctly for the received signal.
				    (e.g., if the image is WEFAX then
				    the Adapter Mode must be set to AM.
				 2) Verify that Scans per minute is set
				    correctly for the received signal.
				 3) If the image is slanted then the Page
				    Alignment needs to be adjusted while
				    an image is received.
				 4) For FM Marine fax verify that the
				    receiver is tuned correctly.  Marine
				    fax images are usually transmitted
				    using Upper Side Band (USB).  The
				    receiver must be tuned approximately
				    1700 Hz lower then the center frequency.

				    Example: For a 8080 KHz HF fax signal,
				    the receiver should be tuned to 8078.3
				    KHz.  (8080 kHz - 1.7 kHz = 8078.3 kHz).
				    Vary the receiver frequency slightly to
				    get the best picture.
				 5) Check to see if any TSR (terminate and
				    stay resident) programs are in memory.
				    If they are, remove them.  Some TSR








		 WeatherFAX User's Guide                 Page 24



				    programs may cause problems when
				    running WeatherFAX.

		   EXPANDED	    Be sure that the Expanded memory
		   MEMORY NOT	    device driver (LIM 4.0) is loaded
		   RECOGNIZED:	    into memory.  If you have an 80386
				    type computer, then the EXTended
				    memory can emulate LIM 4.0 EXPanded
				    memory using a device driver shipped
				    with DOS 4.0.  For 80286 computers,
				    EXTended memory cannot emulate EXPanded
				    memory.

		   800 x 600	 1) Verify your graphics card supports this
		   DISPLAY	    mode.
		   DOESN'T       2) Verify that you have a multifrequency
		   WORK 	    monitor that supports 800 x 600 resolution.
				 3) Verify you have set the correct BIOS
				    display mode.
				 4) Verify that the correct mode is listed
				    as a command line parameter.


ADAPTER/SOFTWARE AVAILABILITY
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

		   The WeatherFAX adapter and software are available from:
		     OFS Software
		     6404 Lakerest Ct.
		     Raleigh, N.C. 27612

		   o Assembled and tested scan-converter board,
		     software and instructions ......................$360.

		   o Kit including PC board, all parts,
		     software and assembly instructions .............$230.
		   o Software only
		     See section "General Information" for copyright
		     information and suggested contribution.

		   Terms:
		   - Specify either 5.25" or 3.5" diskette format for the
		     software.
		   - North Carolina residents add 5% sales tax.
		   - Please add $6.50 for shipping and handling.
		     (or add $12.00 for overseas orders.)
		   - Check drawn on a US bank in US funds.
		     International bank or postal money order in US funds.
		     All foreign orders must be prepaid.
		   - Please allow 4-6 weeks for US delivery.












		 WeatherFAX User's Guide                 Page 25



TRADEMARKS USED IN THIS GUIDE
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

		   o GIF and Graphics Interchange Format are trademarks
		     of Compuserve Incorporated
		   o Turbo C is a trademark of Borland International
		   o IBM and PS/2 are trademarks of International
		     Business Machines Corporation
		   o PageMaker and Aldus are registered trademarks of
		     Aldus Corporation.
		   o Apple, ImageWriter are registered trademarks of
		     Apple Computer Inc.
		   o LaserJet is a trademark of Hewlett-Packard Company.
		   o Intel is a trademark of Intel Corporation.
		   o Microsoft, and MS-DOS are registered trademarks of
		     Microsoft Corporation.
		   o WordPerfect is a trademark of WordPerfect Corporation.