RTTY for RS-232 and Your PC



                                      From:

                                JOST TECH ASSOCIATES
                                   P.O. BOX 75
                                BEDFORD, N.H.  03102
                                   603-472-3694




        This program will turn your pc or jr. into an RTTY terminal.
        The program has many features.


             Among the many features are:

		1.   Eight (8) selectable buffers of 1000 bytes each.
		2.   Type ahead into any selected buffer.
		3.   Load disk file into buffer.
		4.   Send a disk file.
		5.   Preview a buffer.
		6.   60/66/75 or 100 WPM Baud speeds.
		7.   110 or 300 Baud ASCII.
		8.   USOS on/off.
		9.   Send "Quick Brown Fox".
		10.  Send "RYs".
		11.  Load a standard message for transmission.
		12.  Send all data from screen to your printer.
		13.  Send any of the buffers as required.




			Function Keys are defined as follows:


    <F1>    Allows the operator to switch between 60 and 100
            WPM Baud speeds.

    <F2>    Allows the operator to switch between 67 and 75
            WPM Baud speeds.

    <F3>    Allows the operator to switch between 110 and 300
            Baud ASCII speeds.

    <F4>    Sends the standard file which is loaded when the program is
            first brought up.  The program loads into a buffer from a
            file named "GIGO" [Garabage-In-Garbage-Out].  As with all
            of the buffers, the maximum size for GIGO is 1000 characters.

    <F5>    Allows you to send any [-ASCII-] disk file.

    <F6>    Permits you to type data from your keyboard into any of
            the selected buffers for later transmissions.

    <F7>    Allows you to display selected buffer on the CRT.

    <F8>    This function will allow the operator to load a ASCII disk
            file into a selected buffer.   If the file length is greater
            than 999 bytes, only the first 998 bytes of the disk file
            will be loaded.

    <F9>    Sends the data from a selected buffer.

    <F10>   Displays the Main Menu for the RTTY program.




        The following function/number keys should be pressed at the same
        time as	the "ALT" key is held down.


    <ALT+F1>	Enables or disables the Un-Shift-On-Space flag.

    <ALT+F2>	Sends "Quick Brown Fox".

    <ALT+F3>	Sends a single line of "RY's".

    <ALT+F4>	Enables or disables the printer.  If there is no printer,
                or the printer is out of paper, a "NO-PTR" message will
                appear on line 25 of the display, causing this function
                to be disabled.

    <ALT+F5>	Forces the incoming data to be LETTERS.

    <ALT+1 to ALT+8>    Select buffer 1 through 8 as desired.


    <ESC>       Allows you to re set the display.

    <CTRL+F10>  By pressing the "CTRL" key and then the "F10" key, you will
                exit the RTTY program and return to the system prompt.




			Special functions:


     When the character - ~ - [tilda] is found, the current time will be
inserted in any of the data sent, whether from a disk file, typed into
a buffer, or a disk file in a buffer,

     Whenever you are not typing data into a buffer, you will be transmitting
data out the RS-232 port of your pc.

     This program will allow you to select either com1 or com2 for your
RTTY I/O.

     Line 25 will display the current status of the program.  It will tell
you the current speed,  USOS [On or Off], printer status [ON/OFF Not On Line].
While you are typing into a selected buffer, number of characters typed into
the buffer, and which buffer has been selected.