NAME rc85prg - program an RC-85 repeater controller. SYNOPSIS rc85prg [options] prgfile DESCRIPTION RC85PRG will program an A.C.C. RC-85 controller, using a telephone modem with a PC running MS-DOS. Both dialup and control receiver access methods are supported. The modem must be capable of sending digits 0 through 9, * and #. The Hayes (TM) modem is supported by default. RC85PRG has been compiled with default sequences for the owner unlock code, the control operator code, the user autodialer programming codes, and the controller phone number. Each of these sequences can be redefined by command-line options.  is an input file containing the programming commands. If not specified on the command line, stdin is used. Hence pipes (|) or redirection (<) may be used to provide programming commands. The MBBIOS interrupt-driven I/O package by AA4RE must be loaded prior to invoking RC85PRG. Contact your local packet BBS sysop if you need help in obtaining AA4RE's excellent package. OPTIONS If RC85PRG is invoked improperly, it will display a usage summary, and indicate the current value of all settable options. Options include: -v enable verbose mode. -t enable test mode (simulate operation, no delays). -u indicate autodialer is kept unlocked. -w N wait N secs after dialing the RC85, to permit the phone answer message to finish. -p N pause N secs after each command, to permit the response message to finish. -m COMn:baud,8N1 select a modem port and parameters. Any COM port supported by MBBIOS is permitted. -d phonenumber override the default phone number of the con- troller. Include any exchange access and pause for dialtone characters in this string. -o owner_code override the default owner unlock code. -c ctrlop_code override the default control op code. -2 code override the default 2-digit slot programming code. -3 code override the default 3-digit slot programming code. -r indicate the modem audio drives a radio transmitter. -i STRING specifies a modem initialization string. -i0 STRING overrides the default modem command-prefix. -i1 STRING overrides the default modem command-suffix. -s enter an interective phrase-to-code translation mode (see SPEECH, below). -sd display all the speech vocabulary words. -s FILE load a file of words and their translations. MODEM REQUIREMENTS RC85PRG will default to the appropriate sequences used by Hayes(TM)- compatible modems. This sequence differs, depending on whether a phone or radio connection is used (see the -r option). For telephone access to the RC85 controller, commands are prefixed by "ATDT", and suffixed by ";". For radio access, commands are prefixed by "ATH1DT" and suffixed by ";H0". This permits the off-hook LED to be wired to PTT, and modem audio output wired into the mike audio input with appropriate padding resistors. These sequences can be changed with the -i options. An initialization string is specified by the -i option, while the prefix and suffix strings are set by the -i0 and -i1 options. PRGFILE FORMAT This file is an ASCII file containing one command per line. Comments may be placed anywhere, and are indicated by a '#' and continue to the end of the line. Although a '#' can be used in control sequences sent via radio, the '#' must be used to terminate a programming sequence sent via the telephone. Hence its use as a comment delimiter is not ambiguous. Commands consist of two characters beginning in column 2. Case is not significant. Commands are: CU unlock the controller lock, to permit message programming (for example). CL lock the controller (after a CU command). CS string send  to the controller, permitting an arbitrary RC85 command to be issued.  is composed of words separated by spaces or tabs. Each word is looked up in the vocabulary tables, and its value, if found, replaces the word in . CO string send the control-operator prefix followed by  to the controller.  is expanded in the same fashion as for the CS command. S n s p program the autodialer slot number , identified by string , to dial the phone number

. string  may be used to record the callsign or any other text; no spaces are permitted, and this information is otherwise ignored. The S command is equivalent to a sequence of CS commands to enter unlocked mode (if slots 0 through 9 are selected), to unlock the autodialer (if needed, see -u), to clear the current slot contents, and to program a new phone number. If the slot number  is negative, the slot is programmed to speak the number being dialed. If phone number

is omitted, then the slot  is cleared, thereby erasing any previous phone number. MP program the previously-sent message. Equivalent to CS *0. MR readback the message being programmed. Equivalent to CS *2. MA abort the message being programmed. Equivalent to CS *4. ID dots/dashes causes a Hayes-compatible modem to send a Morse code identification string. This command is func- tional only when radio access (-r option) is set. The ID command should be used as often as needed in the PRGFILE so as to identify your station every 10 minutes. EXAMPLE PRGFILE # Program phone numbers into three slots S3 Fire 268-5501 S4 LPSO 232-9211 S11 N5KNX 555-1234 # Program emergency msgs cu cs *1113 #slot 3 = Fire cs fire #equivalent to code *634 mp cs *1114 #slot 4 = LPSO cs L P S O #equivalent to codes 53 71 73 63 mp cl co 75 #Select stardust courtesy tone id -./...../-.-/-./-..- # send N5KNX in morse (ignored unless -r option set) THEORY OF OPERATION Rc85prg first validates its command-line arguments. It then dials the RC85 controller, if telephone access was selected, and waits (see -w) a while for the dialing and rc85 greeting message to complete. Rc85prg will then read the input file looking for programming commands. Each line of the input file constitutes one command. If the command is CS, CO or ID, each following word (words are separated by blanks or tabs) is replaced by its translation, if any, from the vocabulary tables. This is most useful for speech-related commands. Each command is then sent to the RC85 (suffixed automatically by the required # tone) and then the program pauses (see -p) for the spoken acknowlegement. Commands should be given in the proper sequence, that is, unlocked-mode commands should not be mixed with control-operator commands. Autodialer slot programming does not require explicit unlocking; the RC85 is unlocked automatically if slots 0 through 9 are selected. After end-of-file is encountered, the appropriate lock and hangup commands are sent to the RC85, and then the modem is told to hang up the phone line. If the program is interrupted by ctrl-C, it will attempt to terminate the session gracefully. SPEECH Since the speech vocabulary is so limited, an option exists (-s) to permit various word combinations to be tried until a sentence is perfected. The -s option enters an interective mode, in which each input line is translated and displayed as a sequence of speech codes, where possible. The byte count is also displayed, to help the user keep messages within their length limits. A list of words beginning with a desired letter(s) is obtained by beginning a line with '?' followed by the letter(s) desired. A '?' by itself will display all words in the vocabulary. The entire vocabulary can also be displayed by using the -sd option. RC85PRG will halt after the display is completed. The vocabulary can be augmented by using the -s option followed by a file name. This file consists of one pair of words per line. The first word of the pair will be translated into the second word when encountered in a CS, CO or ID command. Comments may be inserted in the file by placing a "#" in column one. EXAMPLE rc85prg -o 1989082344 -c 654 -d 121,9,5551212 setimers.r85 dials 555-1212 and programs the controller from the file named setimers.r85. grep ^S11 autodial.r85 | rc85prg -o 1989082344 -c 654 -d 121,9,5551212 uses the grep program to find the line beginning with S11 in the file named autodial.r85, and provides this line to rc85prg for programming. rc85prg -sd > vocab.85 dumps the speech vocabulary into the file named vocab.85. LIMITATIONS RC85PRG makes a one-pass translation of CO, CS and ID commands. Also, the wait and pause timers may be inaccurate if a multitasker is used. The usual times required by the RC85 to execute commands can be lengthened if it needs to ID the repeater. I tried disabling the repeater (CO 01) before I started a programming session, but this seemed to break some programming commands, despite documentation to the contrary. AUTHOR James Dugal, N5KNX @ W5DDL (packet) jpd@usl.edu (Internet) P.O. Box 44844, Lafayette, LA 70504 Latest version available by anonymous FTP from PC.USL.EDU; look in the pub/ham directory.