VHFPROP!  is a versatile and accurate program for  computing  VHF 
and  UHF  line-of-sight  (ground  wave/terrestrial)   propagation 
range.   Inputs  are  extensive,  including  individual   antenna 
heights,  transmitter power output, antenna gains,  line  losses, 
and required receiver input level for the desired signal-to-noise 
ratio or quieting. 

The  output is the calculated range, in miles (all values are  in 
English measure) for a particular reliability level ranging  from 
50% to 99.9%. 

The  program  is based on a well-accepted  propagation  model  by 
Egli.  One  limitation  to  the  program  is  that  it  does  not 
incorporate a terrain roughness factor correction. Therefore, the 
predicted  range  may be overly optimistic if  terrain  has  high 
points in the path between the stations.

Reference:  John  J. Egli, "Radio Propagation above 40  Mc.  over 
Irregular Terrain", Proc. IRE, October 1957, pp 1383-1391.

Further described and validated in: "Review of Propagation in the 
470-890  MHz.  Band  with Emphasis on Land  Mobile  and  Cellular 
Systems."  by F.H. Palmer. Communications Research Centre  Report 
Number 1288, February 1976. Avaliable through N.T.I.S. as  report 
number N76-27450.

This program, VHFPROP! appears as one of several programs in "The 
Meteor Burst Communications Handbook", by Jacob Z. Schanker. This 
should be available through N.T.I.S. late in 1988 or early 1989.