.PL
        WHATS-UP.DOC Release 0.4 Page 1.


                                  _______
                             ____|__     |                  (tm)
                          --|       |    |-------------------
                            |   ____|__  |  Association of
                            |  |       |_|  Shareware
                            |__|   o   |    Professionals
                          -----|   |   |---------------------
                               |___|___|    MEMBER


                         WHATS-UP (c) Joe Kasser, G3ZCZ, 1990

                                 Joe Kasser G3ZCZ/W3
                                       POB 3419
                               Silver Spring, Md. 20918
                                    (301) 593 6136

                                     G3ZCZ @ N4QQ

        This  is  an interim documentation file. A fuller  document  will  be 
        published with release 1.00.

                                  Table of Contents

        1.0 Introduction
        2.0 Capabilities
        3.0 Things You Should Know
             3.1  TNC State
             3.2  Limit Checking
             3.3  Link Quality Measurements
             3.4  Program Requirements
             3.5  Data Format
             3.6  Display Pages
             3.7  Function Keys
             3.8  Typical Screen Color Combinations 

        4.0 Bringing Up WHATS-UP For the First Time
             4.1  Editing the Configuration File.
             4.2  Starting the program.

        5.0 Standby Mode
        6.0 Playback Mode
        7.0 Interactive Mode
        8.0 Real Time Mode
        9.0 (Data) Extraction Mode
        10.0 Configuration File
        11.0 Spacecraft Parameter Files
        12.0 Telemetry Channel Extraction File
        13.0 Extracted Telemetry Data File








        COPYRIGHT Joe Kasser, G3ZCZ 1990.

        WHATS-UP.DOC Release 0.4 Page 2.


        1.0 Introduction

        This  version  of  WHATS-UP is a concept demonstration  version  of  a 
        Telemetry  Decoding  and display Program for the  MicroSat  Spacecraft 
        (OSCARs  16, 17, 18 and 19). It is table driven via the  configuration 
        files to allow maximum flexibility.

        This version contains a few cosmetic display bugs. I expect (but don't 
        promise)  to  put  out  Revision 1.00 with  more  features,  (such  as 
        automatic  spacecraft  parameter file switching to  match  spacecraft, 
        scheduled   events,  TNC  configuration  files,  etc.)   and    proper  
        documentation,  sometime between March and June 1990. This program  is 
        not in the public  domain but may be copied and passed on. 

        If  you would like a copy of  Revision 1.00 which will be released  as 
        shareware, send in a FORMATTED disk and sase.  If  you  have  captured 
        any  telemetry to disk,  especially  daytime  or  southern  hemisphere 
        passes, please put them on the disk. Don't let the data  files  become  
        too  long. I suggest that you  rename  them  every couple of  days  or 
        so, such as DOVE2-16.RUN, DOVE2-18.RUN, etc.

        Better still, why not register your copy, receive Revision 1,  qualify 
        for  further  updates,  and  support  development  of  this  kind   of 
        software. 

        Suggestions for improvements and additions are always welcome.

        2.0 Capabilities

        WHATS-UP contains the following features:

        * Real time and Playback modes.

        * Automatic Capture-to-disk of raw telemetry.

        * Extracts  predetermined  telemetry  channel data to  a  database  or 
          spreadsheet readable file for further analysis.

        * Link quality measurement.

        * Capability to print the raw telemetry as it is received.

        * Up  to  16 user configurable display pages (screens). You  set   the 
          position  on the page (width of engineering unit field,  and  number 
          of decimal places) that a parameter is displayed  at.

        * Wild card page (parameter shows up on all pages).

        * Selectable  display of Engineering units or Hex byte for each   dis-
          play page.

        * Display of raw packets (i.e. STATUS)

        * Color  changes  if  a parameter  value  changed  between  successive   
          frames.


        COPYRIGHT Joe Kasser, G3ZCZ 1990.

        WHATS-UP.DOC Release 0.4 Page 3.



        * Audio  and visual alarms if a telemetry value exceeds, falls   below 
          or falls outside a preset limit value(s).

        * Dumb split screen terminal mode (a la LAN-LINK).

        * Customizable  colors,  PC to TNC baud rate, data  parity  and   stop 
          bits.

        * Default spacecraft configuration files.

        * Time of day clock display (in HH:MM:SS format)

        3.0 Things You Should Know

             3.1  TNC State

             WHATS-UP does not change the TNC state, unless you command a time 
             change. Make sure the TNC is set up so as not to beacon.

             3.2  Limit Checking

             Limits are only checked for parameters being displayed (in  Engi-
             neering  units).  With this approach, you can  set  up  different 
             pages  for  different on-board subsystems, you can  also  set  up 
             different  display  pages of the same  parameters  for  daylight, 
             darkness  and  terminator crossing passes, with  different  limit 
             values to draw your attention to changes.

             3.3  Link Quality Measurements

             The  link quality part allows the following to be done.  You  can 
             define  which  of the packets you want to display/count  (If  you 
             just want to count them and not display them, set the page  value 
             to 99). You can then view an incrementing count counter each time 
             a selected packet is received. You can also display the  contents 
             of the STATUS, WASH or BCRXMT packets in any display page.

             3.4  Program Requirements

             IBM PC or clone with 256k memory.

             TNC of some kind, I've tested it with a TNC2, a KAM and a  PK-232 
             so far.

             3.5  Data Format

             The  program  DOES require that the telemetry  be  received,  and 
             captured-to-disk  with the packet header on a different  line  to 
             the  contents of the packet (HEADERLINE ON). I also suggest  that 
             you  turn  the date/time stamp on so that when you  get  Revision 
             1.00, you will be able to playback your data and extract selected 
             values and their corresponding time codes into a file that can be 
             read into your spreadsheet program for further trend analysis.
             


        COPYRIGHT Joe Kasser, G3ZCZ 1990.

        WHATS-UP.DOC Release 0.4 Page 4.


             3.6 Display Pages

             My  version (the default) is set up to display those  packets  as 
             wild  cards  (i.e will show up on all pages),  and  then  display 
             several temperatures and solar cell array currents.

             By putting the correct parameters in the SPACECRAFT.SYS file, you 
             can  set  up  any of the pages to display any  of  the  telemetry 
             channel data in any row and column in that page.

             3.7  Function Keys

             The following function keys are active:
                  FK 1 capture to disk Toggle
                  FK 2 type of display Engineering Units/Hex Byte Toggle
                  FK 3 select display page

                  Alt-B send a 'Break' to the TNC, interactive mode only.
                  Alt-P Printer on/off
                  Alt-S Sound on/off
                  Alt-X Quit
                  left arrow decreases playback speed
                  right arrow increases playback speed.

             3.8  Typical Screen Color Combinations 

             TBS

        4.0 Bringing Up WHATS-UP For the First Time

        WHATS-UP  has four basic modes of operation;  Interactive,  real-time, 
        data  extraction and playback. You must configure WHATS-UP before  you 
        try any Real Time activity.

             4.1  Editing the Configuration File.

             The  configuration file is called WHATS-UP.SYS. You must edit  it 
             with an ASCII word processor (in the non document mode) to set up 
             the  correct parameters on the RS-232 link between your  TNC  and 
             your PC. See Section 10 for details of what parameter is on which 
             line of the WHATS-UP.SYS file.

             4.2  Starting the program.

             You may start the program in three ways as follows.

                  4.2.1     Default

                  Type 'whats-up' and return (without the 's). This brings the 
                  program  up  in the default mode. It will  read  the  whats-
                  up.sys file to determine the spacecraft being monitored, and 
                  then prompt you for the mode.





        COPYRIGHT Joe Kasser, G3ZCZ 1990.

        WHATS-UP.DOC Release 0.4 Page 5.


                  4.2.2     User Chosen spacecraft
                  
                  Type 'whats-up spacecraft' and return (without the 's).  The 
                  program reads the spacecraft.sys file to load the parameters 
                  for  the  MicroSat of choice, and then prompts you  for  the 
                  mode.

                  Examples of the command are :

                  'WHATS-UP DOVE' or 'WHATS-UP PACSAT'

                  4.2.3     Custom Mode

                  Type 'whats-up spacecraft mode' and return (without the 's). 
                  This brings the program up in the custom mode. It will  read 
                  the  whats-up.sys  file to determine  the  spacecraft  being 
                  monitored,  and  then start up in the mode  you  set.  Valid 
                  modes are 'p', 'i', 'e' and 'r'.

                  Examples of the command are :

                  'WHATS-UP DOVE R' or 'WHATS-UP PACSAT R'

                  If  you place a command line like this in your  autoexec.bat 
                  file,  should  you  be copying telemetry  in  an  unattended 
                  manner and a power failure take place, the system will  boot 
                  up into the correct WHATS-UP mode when power is restored.

        5.0 Standby Mode

        TBS

        6.0 Playback Mode

        The  Playback mode allows you to play back captured telemetry  with  4 
        speeds (speedy, slow, slower and snail's pace).

        7.0 Interactive Mode

        The  Interactive mode is a dumb terminal. You can use it to give  com-
        mands  to the TNC. The usual one is to set the TNC date from the  com-
        puter's  clock. You should also use it to set the 'HEADERLINE ON'.  In 
        this  mode, you will see the raw packets on the channel. You can  also 
        use  this mode as a regular TNC program (If you do, you ought  to  get 
        your head examined, because LAN-LINK will do the job much better). 

        8.0 Real Time Mode

        The  Real-time  mode converts and displays engineering data.  You  can 
        display up to 16 (configured by you) pages of information. Information 
        that changes between successive frames, is shown in a different color. 
        Information  that has exceeded a preset (by you) limit is shown in  an 
        alarm color (default: blinking red). The capture-to-disk will turn  on 
        when  the first packet is copied, and will turn off two minutes  after 
        the last.


        COPYRIGHT Joe Kasser, G3ZCZ 1990.

        WHATS-UP.DOC Release 0.4 Page 6.



        9.0 (Data) Extraction Mode

        TBS
        Note: Start and stop times are text string matches.


        10.0 Configuration File

        The contents of the Configuration file (WHATS-UP.SYS) are as follows:

        Your callsign   (e.g. G3ZCZ)
        Default configuration file) (e.g. Dove)
        station latitude  (e.g. 35.00)
        station longitude  (e.g. 74.00)
        station altitude  (e.g. 100)
        capture-to-disk file (e.g. dove.RUN)
        playback file   (e.g. dove.run)
        extracted data file (e.g. whats-up.txt)
        list of telemetry parameters to extract file (e.g. ARRAYS)
        PC serial port   (e.g. 1)
        PC serial baud rate  (e.g. 1200)
        data bits    (e.g. 8)
        Stop bits    (e.g. 1)
        parity     (e.g. 0)
        status (top) window color (e.g. 79)
        Telemetry Page color (e.g. 14)
        outgoing window color (e.g. 14)
        incoming window color (e.g. 30)
        prompt window color  (e.g. 15)
        alarm window color  (e.g. 15)
        bottom window color  (e.g. 79)
        Emphasis color   (e.g. 14)
        prompt color   (e.g. 14)
        option color   (e.g. 78)
        parameter changed color (e.g. 95)
        parameter limit exceeded color (e.g. 14)

        The callsign and geographic parameters are not used in this version.

        You must configure WHATS-UP before you try any Real Time activity.

        11.0 Spacecraft Parameter Files

        You  will need a Different spacecraft parameter file for  each  space-
        craft.  Spacecraft  parameter files are named by the  spacecraft   and 
        given the extension '.SYS'. Examples are 'DOVE.SYS' and  'PACSAT.SYS'. 

        The contents of the SPACECRAFT.SYS file are as described below.

        Spacecraft ID.
        Selected or default display page number

        Number of display pages (maximum = 16)



        COPYRIGHT Joe Kasser, G3ZCZ 1990.

        WHATS-UP.DOC Release 0.4 Page 7.


        Then follows the page definitions, as in for example;

        4
        SPACECRAFT HOUSEKEEPING, 30,31
        PAYLOAD, 30, 31
        BATTERY STATUS, 30, 30
        MISC,30,2

        the number above the page definitions must be set correctly.

        For each page:

               Page title
               Page color

        The  next  set  of items are the  Telemetry  parameter  configurations 
        (maximum = 64). You must have at least one of these lines in the file. 
        If  you want a value to show up in more than one page (other than  the 
        wild card [0]) you must enter it twice (once per page). Typically each 
        row looks as follows:-

        00,Rx E/F Audio(W):,+0.000,+0.0246,0.000,V(p-p),2,11,1,6,1,0,0,0
        01,Rx E/F Audio(N):,+0.000,+0.0246,0.000,V(p-p),2,11,32,6,1,0,0,0

        For each telemetry parameter:

               hexadecimal channel number (2 bytes, e.g. '0F' )
               Description text string (e.g. '+Z Array Temp.')
               Equation Coefficient C
               Equation Coefficient B
               Equation Coefficient A
               Units text string (e.g. '.C')

        In the telemetry processing part of WHATS-UP, only the  quadratic 
        equation is hard coded, the coefficients are table driven from  a 
        configuration file. 

               Display page number
               Display page row
               Display page column
               Display width for Engineering Units
               Number of digits after the decimal point
               Limit check flag (0 =  do  nothing, 1 =  check  below  low 
                                   limit,2=  check above high limit, 3  = 
                                   check for [below low limit] or  [above 
                                   high limit])
               Low limit value (e.g. -4.00)
               High limit value (e.g. +10.6)

        A  line with an '*' as the first character terminates  that  sec-
        tion.






        COPYRIGHT Joe Kasser, G3ZCZ 1990.

        WHATS-UP.DOC Release 0.4 Page 8.


        Packet types:-

               packet types are set as follows:-

               name of UNP address (e.g. WASH, BCXRT)
               Display page for the contents of the packet
               Display color 
               Display row
               Display column
               Display page for the cumulative count of the packet type
               Display row
               Display column

        Typical entries are as follows:

        WASH, 0, 30,4, 1, 0, 5, 1
        TIME, 0, 31, 1, 1, 0, 5, 12
        STATUS, 0, 29, 2, 1, 0, 5, 24
        BCRXMT, 0, 28, 3, 1, 0, 5, 37
        TLM, 99, 31, 3, 1, 0, 5, 50

        These also terminate with an '*' character.


        12.0 Telemetry Channel Extraction File

        ZCZC (default start time string) {start of file}
        NNNN (default stop time string) {end of file}
        26    (list of telemetry channels to be extracted)
        27 (This one contains the solar array currents)
        28
        29
        2A
        2B

        13.0 Extracted Telemetry Data File

        This an ASCII string, comma delimited file which can be  imported 
        into your spreadsheet.


















        COPYRIGHT Joe Kasser, G3ZCZ 1990.

        WHATS-UP.DOC Release 0.4 Page 9.


        APPENDIX Other Amateur Radio Software by Joe Kasser G3ZCZ

                                   PC-HAM 3.3 

        PC-HAM contains a number of programs some of which are  described 
        below.  

        LOGBOOK
        Full  blown  logging package. With automatic check  of  logs  for 
        awards such as DXCC. Allows you to recall any entry by call  sign 
        within  seconds.  Indexed displays, QSLing, Contest  mode  QSLing 
        (prints the lot) and lots more written in dBASE3, but a  compiled 
        LOGBOOK.EXE file is supplied together with the source code. 

        CONTEST
        Keeps Dupes in memory, logs QSO's to disk in format which can be 
        processed by the LOGBOOK package. 

        CQSS
        Sweepstakes  game.  Work  the ARRL Sweepstakes  contest  on  your 
        computer. You are located just outside Washington DC. A  propaga-
        tion  model is built in to the program. This program is  REQUIRED 
        training  for all sweepstakes operators. Program is based on  the 
        one  described in detail in 'Software for Amateur Radio'  by  Joe 
        Kasser  G3ZCZ,  published by TAB Books, Blue  Ridge  Summit,  PA. 
        17214.

        WHATSON
        Predict HF Propagation. Contest mode with printout to whole world 
        at hourly intervals. Needs BASIC


                                  LAN-LINK 1.55

        Function  key  and  Menu driven. Automatic  logbook  entries  for 
        Packet  and  Mailbox/Beacon Mode  AMTOR  Connects,  semiautomatic 
        logbook entries for other modes. Log file can be processed by the 
        Logbook Package of PC-HAM.

        Contest  operation,  sends  standard  message  and  automatically  
        increments  QSO count. Automatic optimized configuration  of  the 
        TNC  for each communications mode. All mode Function  key  'OVER' 
        feature (End).

        There  are 10 files with fixed names (LAN-LINK.001 through   LAN-
        LINK.010) which may be viewed and transmitted by means of   func-
        tion keys. They may also be edited from the Edit Menu.

        Set up of TNC for AMSAT-OSCAR (non packet) Telemetry reception.

        Time display and event scheduler. ASCII Text Editor. Customizable 
        Colors.  Access to the TNC Command Mode is provided in  case  the 
        user wishes to override any defaults.

        Automatic capture to disk of all packet radio connects.  Automat-


        COPYRIGHT Joe Kasser, G3ZCZ 1990.

        WHATS-UP.DOC Release 0.4 Page 10.


        ic  indication of the number of Packet connects. Local Area  Net-
        work (LAN) message store and Forward capability. 

        Capable  of  automatic connect attempts to download  a  QTC  from  
        another station in the LAN. Capable of automatic connect attempts 
        to  a  packet BBS to download your incoming messages,  when  your 
        callsign  appears on the BBS mail beacon annunciator. Capable  of 
        automatically requesting Bulletins on subjects that interest  you 
        from your local packet BBS.

        Digipeat  monitoring  and capture. Alert signal to let  you  know 
        when a predetermined call shows up in a packet header on frequen-
        cy. 

        Conference Mode in multiconnect situations. Bridge Mode in multi-
        connect  situations. Path determination to DX station via  :QMH:. 
        Indicator that a specific station designated as the 'target' call 
        connected  in  Packet Mode, or linked  to  AMTOR   Beacon/Mailbox 
        while you were away.

        Automatic  NET/ROM  and  KA Node path set  up  from  LAN-LINK.DIR  
        call/path directory file. Selective answering machine and MAILBOX 
        using  NC/L  command  dialogue. Screen indication of  connect  by 
        desired station (target  call).

        Automatic  Beacon Mode CQ caller. Will call CQ  repetitively  and 
        either work the connect and keep going after disconnect or signal 
        you when a reply is  received.

        SAREX special features. :QRA: trigger to determine who else is on 
        channel.

        Automatic  AMTOR SELCAL determination. Function key  change  from 
        monitoring AMTOR FEC CQ's to QSO's in progress (chirpcopy).

        NAVY MARS RTTY file transmitting protocols for the PK-232.





















        COPYRIGHT Joe Kasser, G3ZCZ 1990.

        WHATS-UP.DOC Release 0.4 Page 11.


        WHATS-UP 0.4  Registration Fee $35.00
        LAN-LINK 1.55 Registration Fee $35.00 
        PC-HAM 3.3    Registration Fee $36.50

        Register them all for $95.00.

        Evaluation  Copies free, you pay only for the disk/postage.   For 
        an  evaluation  copy (unregistered full blown  version)  of  each 
        software  send a formatted disk and SASE to Joe Kasser.  Overseas 
        users,  send  $3.00 ($5.00 covers all three)   instead.  Try  the 
        software  first, and only register your copy if you make  use  of 
        it. 

          To: Joe Kasser G3ZCZ
            P O BOX 3419
            SILVER SPRING
            MD 20918.

          CALL ________________ TODAY'S DATE _____________

          NAME ______________________________________________

          ADDRESS ___________________________________________

            ___________________________________________

          CITY ___________________________________________

          STATE _________ POSTCODE ______________________

          TNC TYPE _____________________ Home BBS __________

        I enclose a check for ______. Please send me the latest version 
        of ______________, and register me as a user.

        I enclose a disk/sase or $3.00. Please send me the latest version 
        of
        ______________________  to evaluate. If I like it and use  it,  I 
        plan to become a registered user.

        Disk Size 5.25 _____(360k) 5.25 _____(1.2Mb) 3.5 ______(730k)

        I AM NOT/AM currently using Shareware Version _____

        which I obtained from _________________________________________.

          Signature _______________________

        Club Registrations  10 or more copies, 10% discount.
                            50 or more copies, 25% discount.

        Designate one contact person to receive club registered  updates, 
        and  supply  a list of names and call signs of club  members  who 
        will be using the Registered Club Copy.



        COPYRIGHT Joe Kasser, G3ZCZ 1990.