PAC.DOC

2-5-89, 4-5-89.

Includes changes from firmware of 12-30-88.

Alphabetic list of PK-232 Commands and Parameters by mode, with
short descriptions and defaults.

Jeb Boswell, W1YO, 24 Edgewood Park, Springfield, Illinois 62704,
217) 546-5269.

------------------------------------------------------------------------------

Terminal Commands:

ACRDISP n	Terminal/screen/printer width, n = characters.
  ACRD n

ALFDISP		ON--LF sent to terminal after CR.  Received LF ignored.
  ALFD		OFF--LF not sent.

AMTOR		Immediate command to switch to AMTOR ARQ mode standby.
  AM

ASCII		Immediate command to switch to ASCII RTTY mode.
  AS

AWLEN n		Data bits per word, PK-232 to terminal.
  AW n

BAUDOT		Immediate command to switch to Baudot RTTY mode.
  BA

BKONDEL		ON--<backspace><space><backspace> echoed for delete.
  BK		OFF--<backslash> echoed for delete.

CALIBRATE	Modem calibration routine.
  CAL		  K--toggles PTT line.	Q--quits routine.
		  H--toggles between wide (1200 hertz) and narrow (200).
		  <SPACE>--toggles between mark (low) and space (high) tones.
		  D--Alternates between mark and space
		     at radio baud (HB) rate.

COMMAND n	0 to $7F ASCII character code to enter COMMAND mode from
  COM n		  CONVERSE mode.  Default is $03, CTRL-C.

CONVERSE	Switch from COMMAND mode to CONVERSE mode, immediate
  CONV or K	  command.

CUSTOM nnnn	n = 4 digit hex value.  Each bit controls a different function.
  CU nnnn

Summary: 
bit 0--0 = display all packets regardless of DCD/Threshold.
       1 = discard all packets too weak to light the DCD LED.
           (1 is default.)
bit 1--0 = MONITOR set to level 4. (Default)
       1 = MONITOR set to level 6.
bit 2--0 = Break does not affect PK-232.
       1 = Break puts PK-232 in Command mode. (Default)
bit 3--0 = Packet channels numbered 0-9.  (Default)
       1 = Packet channels laveled A-J or a-j.
bit 4--0 = Baudot only, no figures before numeral after space.
       1 = Figures before numeral after space--USOS match.
           (1 is default)
bit 5--0 = Power up in command mode. (Default)
       1 = Power up in previous mode.
bit 6--0 = Monitoring disabled in transparent mode. (Default)
       1 = Monitoring active in the transparent mode.
 
Bits 7 to 15 are presently unused.

DAYTIME date&time <yymmddhhmm>  See CONSTAMP, DAYSTAMP, MHEARD, and
  DAY		  MSTAMP.  See program DAYLOAD.

DAYSTAMP	ON--the date is included in CONSTAMP and MSTAMP.
  DAYS		OFF--date is not included.  Default is OFF.

DELETE		ON--<DELETE> key to delete while typing.  Default is OFF.
  DEL		OFF--<BACKSPACE> key to delete.  See BKONDEL, REDISPLAY.

DISPLAY (class)	(A)sync	     asynchronous port parameters.
  DISP		(C)haracter  special characters.
		(F)AX        FAX related parameters.
		(I)d	     ID parameters.
		(l)ink	     link parameters.
		(M)onitor    monitor paremeters.
		(R)TTY	     Baudot/ASCII RTTY, ASMTOR and Morse parameters.
		(T)iming     timing parameters.
		(Z)          display the entire command/parameter list.

ECHO		ON--characters from terminal to PK-232 ARE echoed.
  E		OFF--characters are not echoed.  Default is ON.

ESCAPE		ON--<ESCAPE>, $1B, is output as '$', $24.
  ES		OFF--<ESCAPE> is output as <ESCAPE>, $1B.

FAX		Immediate command to put PK-232 in FAX Mode.

FLOW		ON--stops PK-232 output to terminal.  Default is ON.
		OFF--PK-232 output to terminal continues.

FULLDUP		ON--full duplex radio operations.
  FU		OFF--full duplex disabled.  Default is OFF.

HELP		Help list.
  H

HOST		ON--computer friendly mode.  Default is OFF.
  HOST		OFF--normal TNC mode.  <CTRL-A> O H O N <CTRL-W> cancels.

MORSE		Immediate commnad to switch to Morse code mode.
  MO		  See MSPEED.

NEWMODE		ON--automatic Command Mode on disconnect.  Default is ON.
  NE		OFF--no return to Command Mode on disconnect.

NOMODE		ON--PK-232 switches modes explicitly--NEWMODE ignored.
  NO		OFF--PK-232 follows NEWMODE.  Default is OFF.

NUCR		ON--Null characters are sent to temrinal after <CR>.
  NU		OFF--Null characters not sent.  Default is OFF.

NULF		ON--Null characters are sent to terminal after <LF>.
  NUL		OFF--Null characters are not sent.  Default is OFF.

NULLS n		Number of nulls to the terminal send when NUCR or
  NULL n	  NULF are on.  Default is 0.

OPMODE		Shows current mode of operation and status of PK-232.
  O

PACKET		Switches the PK-232 to Packet mode, the default mode
  PA		  at initial turnon.

PARITY n	To terminal.  0 = no parity. 1 = odd parity. 2 = no parity.
  PAR n		  3 = even parity.  Transparent mode. See AWLEN.  

REDISPLA n	0 - $7F ( 0 - 127 decimal).  Re-display current input line.
  RED n		  Default is CTRL-R ($12).

RESET		Everything back to "square one".  All personalized
  RESET		 parameters and monitor lists are lost.  USE RESTART!

RESTART		Same as turning PK-232 off, then on.  Power down reset. 
  RESTART	Not the same as RESET.

START n		0 - $7F ( 0 - 127 decimal ) character to start output to
  STA n 	terminal after STOP character used.  Default is CTRL-Q.

STOP n		0 - $7F ( 0 -127 decimal ) character to stop output to
  STO n		terminal.  START charqcter resumes.  Defualt is CTRL-S.

TBAUD n		PK-232 to terminal baud rate.
  TB n

TCLEAR		Clears the transmit buffer, cancels further transmission
  TC		of data.  May not clear all packets.

TIME N		0 - $7f ( 0 - 127 decimal ) character imbedded to send time.
  TI n		Default is CTRL-T (#14).  DAYSTAMP ON also sends date.

TRFLOW		ON--software flow control activated for terminal in
  TRF		Transparent Mode.  OFF--only hardware flow control.
		Software set by STOP and START.  Default is OFF.

XFLOW		ON--XON/XOFF terminal software flow control is on.
  XF		OFF--XON/XOFF software flow control off.
		Hardware flow control: START, STOP, XON, XOFF = 0.
		Default is ON.

XOFF n		0 - $7F ( 0 - 127 decimal) character to stop input
  XO n		from terminal.  Restart with XON.  Default is CTRL-S.

XON n		0 - $7F ( 0 - 127 decimal) character to start input
  XON n		from terminal.  Stop with XOFF.  Default is CTRL-Q.

------------------------------------------------------------------------------

AMTOR Commands:

AAB		Answer back text to WRU?, maximum of 17 characters.
  AA		  WRU set on.  Also ASCII, Baudot.

ACHG		Receiving station command for immediate changeover,
  AC		  "breadk-in".  Use care.

ACRTTY n	1 to 255 characters before automatic CR.
  ACRR n	  0 disables.  ( 71 for standard 69 column AMTOR.)

ADELAY n	Transmitter keyup delay in 10 msec before data sent.
  AD n

ALIST		Immediate switch to ARQ Listen mode--Mode L.
  AL		  Repeat AL for synchronization.

ARQ aaaa	Starts AMTOR Mode A SELective CALl to a distant station.
  AR aaaa	  (See SELCAL.)

ARQTMO n	0 to 255 seconds to send an ARQ SELCAL befroe shutdown.
  ARQT n

CWID n		Changes the "cwid send" character.  Default is $06, CTRL-F.
  CW		  ON sets feature on.  OFF sets feature off.  Obsolete.

DCDCONN		ON--RS-232 pin 8 follows the state of the CON LED.
  DC		OFF--pin permanently set high (active).  Default.

EAS		ON--display as transmitted.  (Echo As Sent.)
  EAS		OFF--display characters as sent to the PK-232.  Default.

FEC		Immediate command for AMTOR FEC (mode B) transmission.
  FE		For CQ and satellite calls.  See SELCAL, ARQ, RCVE, AMTOR.

LOCK		Immediate command for measuring Morse code speed and
  L		  setting letters in Morse and AMTOR.

MYALTCAL aaaa	Alternate SELective CALling identification, for 'all ships
  MYS aaaa	  and stations' calls.

MYSELCAL aaaa	nnnn = SELective CALling code.
  MYS aaaa

NEWMODE		ON--automatic Command Mode on disconnect.
  NE		OFF--no return to Command Mode on disconnect.

NOMODE		ON--PK-232 switches modes explicitly--NEWMODE ignored.
  NO		OFF--PK-232 follows NEWMODE.

NUMS		Forces FIGURES.
  N

RECEIVE n	0 - $7F (1 - 127 decimal). The control character in a file
  R n		to switch from transmit to receive.  Default is CTRL-D ($04).

RFEC		ON--Mode B (FEC) signals are displayed in AMTOR standby.
  RF		OFF--not displayed.  Default is ON.

RXREV		ON--Received polarity is reversed--mark/space reversal
  RXR		OFF--not reversed.  Default is OFF.

SELFEC aaaa	SELective CALling code for specific distant station.
  SEL aaaa	See MUSELCAL.  End SELFEC xmission with CTRL-C and "R"eceive.

SRXALL		ON--receive ALL selective transmissions (SELFEC).
  SRX		OFF--Receive only SELCAL-assressed SELFEC transmissions.
		  Default is OFF.

TCLEAR		Clears the transmit buffer, cancels further transmission
  TC		of data.  May not clear all packets.

TXREV		ON--Transmit data polarity is reversed.  Mark-space reversal.
  TXR		OFF--normal.  Default is off.

WORDOUT		ON--characters held in transmit buffer until space, or
  WO		punctuation.  OFF--characters sent at once.  Default is OFF.

WRU		Always on in AMTOR.
  WR		

------------------------------------------------------------------------------

ASCII Commands:

AAB <17>	Answer back text to WRU?, maximum of 17 characters.
  AA <17>	  WRU set on.  Also AMTOR, Baudot.

ABAUD n		ASCII Baud rate from PK-232 to radio.
  AB n		  45, 50, 57, 75, 100, 110, 150, 200, 300 bauds available.

ACRTTY n	1 to 255 characters before automatic CR.
  ACRR n	  0 disables.  ( 71 for standard 69 column AMTOR.)

ALFRTTY		ON--LF sent after every CR.  Default.
  ALFR		OFF--LF not sent after every CR.

CWID n		Changes the "cwid send" character.  Default is $06, CTRL-F.
  CW		  ON sets feature on.  OFF sets feature off.  Obsolete.

DIDDLE		ON--sends LTRS in Baudot, NUL (00) ASCII.
  DID		OFF--no character sent.  Default.

EAS		ON--display as transmitted.  (Echo As Sent.)
  EAS		OFF--display characters as sent to the PK-232.  Default.

NEWMODE		ON--automatic Command Mode on disconnect.
  NE		OFF--no return to Command Mode on disconnect.

NOMODE		ON--PK-232 switches modes explicitly--NEWMODE ignored.
  NO		OFF--PK-232 follows NEWMODE.

RCVE		Immediate command to switch from Transmit to Receive in
  R		Baudot and ASCII RTTY.  CTRL-C for command mode.

RECEIVE n	0 - $7F (1 - 127 decimal). The control character in a file
  R n		to switch from transmit to receive.  Default is CTRL-D ($04).

RXREV		ON--Received polarity is reversed--mark/space reversal
  RXR		OFF--not reversed.  Default is OFF.

TCLEAR		Clears the transmit buffer, cancels further transmission
  TC		of data.  May not clear all packets.

TXREV		ON--Transmit data polarity is reversed.  Mark-space reversal.
  TXR		OFF--normal.  Default is off.

WIDESHFT	ON--RTTY tones shift is 1000 hertz.
  WI		OFF--200 hertz.  Default is OFF.

WORDOUT		ON--characters held in transmit buffer until space, or
  WO		punctuation.  OFF--characters sent at once.  Default is OFF.

WRU		ON--respond to a WRU?
  WR		OFF--no response to WRU?  Default is OFF.

XMIT		Immediate command to transmit in Command Mode (CTRL-C for
  X		Command Mode.)

------------------------------------------------------------------------------

Baudot Commands:

AAB <17>	Answer back text to WRU?, maximum of 17 characters.
  AA <17>	  WRU set on.  Also AMTOR, ASCII.

ACRTTY n	1 to 255 characters before automatic CR.
  ACRR n	  0 disables.  ( 71 for standard 69 column AMTOR.)

ALFRTTY		ON--LF sent after every CR.  Default.
  ALFR		OFF--LF not sent after every CR.

BITENV n	0 - $1F ( 0 -31 decimal).  Exclusive OR for bit inversion
  BI n		Baudot transmissions.  Default is 0, no bit inversion.

CCITT		ON--International Alphabet #2.  Default.
  CC		OFF--American Standard Baudot (Western Union).

CODE n		Code 0 with CCITT.  Default.  Code 1: U.S. teleprinter.
  COD n		Code 2: Cyrillic.  Code 3: Transliterated Cyrillic.
		Code 4: Katakana.  Code 5: Transliterated Katakana.

CRADD		ON--line end sequence is <CR CR LF>.  (Old standard.)
  CRA		OFF--sequence is <CR LF>.  Default is OFF.

CWID n		Changes the "cwid send" character.  Default is $06, CTRL-F.
  CW n		Also, CWID ON sets feature on, CWID OFF sets feature off.

DIDDLE		ON--sends LTRS in Baudot, NUL (00) ASCII.
  DID		OFF--no character sent.  Default.

EAS		ON--display as transmitted.  (Echo As Sent.)
  EAS		OFF--display characters as sent to the PK-232.  Default.

LOCK		Immediate command for measuring Morse code speed and
  L		  setting letters in Morse and AMTOR.

NEWMODE		ON--automatic Command Mode on disconnect.
  NE		OFF--no return to Command Mode on disconnect.

NOMODE		ON--PK-232 switches modes explicitly--NEWMODE ignored.
  NO		OFF--PK-232 follows NEWMODE.

NUMS		Forces FIGURES.
  N

RBAUD n		On air Baudot baud rate.  Default is 45 bauds.
  RB		  45, 50, 57,  75, 100, 110, 150, 200, 300 bauds.
		  60, 66, 75, 100, 132, 145, 198, 264, 396 WPM.

RCVE		Immediate command to switch from Transmit to Receive in
  R		Baudot and ASCII RTTY.  CTRL-C for command mode.

RECEIVE n	0 - $7F (1 - 127 decimal). The control character in a file
  R n		to switch from transmit to receive.  Default is CTRL-D ($04).

RXREV		ON--Received polarity is reversed--mark/space reversal
  RXR		OFF--not reversed.  Default is OFF.

TCLEAR		Clears the transmit buffer, cancels further transmission
  TC		of data.  May not clear all packets.

TXREV		ON--Transmit data polarity is reversed.  Mark-space reversal.
  TXR		OFF--normal.  Default is off.

USOS		ON--unshift on space.
  USO		OFF--no unshift on space.  Default is OPP.

WIDESHFT	ON--RTTY tones shift is 1000 hertz.
  WI		OFF--200 hertz.  Default is OFF.

WORDOUT		ON--characters held in transmit buffer until space, or
  WO		punctuation.  OFF--characters sent at once.  Default is OFF.

WRU		ON--respond to a WRU?
  WR		OFF--no response to WRU?  Default is OFF.

XMIT		Immediate command to transmit in Command Mode (CTRL-C for
  X		Command Mode.)

------------------------------------------------------------------------------

FAX commands:

ASPECT n	1 - 6.  Default is 2.  IOC.  Index Of Cooperation.
  ASP n		2: Weather charts.
		3: Wirephoto.
		4: WEFAX Satellite.

FAXNEG		ON--reverses picture, negative to positive.
  FAXN		OFF--positive picture.  Default is OFF.

FSPEED n	0 - 4.  horizontal scan rate, as follows:
  FS n		1: 1 line/second, 60 lines/minute.
		2: 2 lines/second, 120 lines/minute.
		3: 3 lines/second, 180 lines/minute.
		4: 4 lines/second, 240 lines/minute.
		0; 1.5 lines/second, 90 lines per minute.
		Default is 2.

GRAPHICS n	0 - 6.  Horizontal dot density, as follows:
  GR n		0 - 480, 1 - 960 (high quality) (default), 
		2 - 980 (ribbon save), 3 - 1920 (highhest quality),
		4 - 640, 5 - 576, 6 - 720.

JUSTIFY n	0 - 15.  Shift image to left 1/2 inch per unit.
  JU n

LEFTRITE	ON--left to right print of picture.  Normal.
  LE		OFF--right to left print.  Default is ON.

LOCK		Forces synchronization and start of printing.
  L

PRCON		ON--Parallel printer connected.
  PRC		OFF--Parallel printer not connected.  Default is OFF.

PRFAX		ON--FAX to parallel printer port.  Default is ON.
  PRF		OFF--FAX to RS-232 (terminal) port of PK-232.
		AWLEN 8, 8BITCONV ON, PARity 0, ACRDISP 0.

PROUT		ON--All data, text, keyboard sent to parallel printer
  PRO		if PRCON is also on.  OFF--all to RS-232 (terminal).
		Default is OFF.

RCVE		Immediate command for receive.  Use instead:
  R		CTRL-D sends FAX stop signal.  CTRL-F sends FAX
		stop signal plus CW ID.

XMIT		Immediate command to transmit FAX.
  X

------------------------------------------------------------------------------

Morse commands:

EAS		ON--display as transmitted.  (Echo As Sent.)
  EAS		OFF--display characters as sent to the PK-232.  Default.

LOCK		Immediate command for measuring Morse code speed and
  L		  setting letters in Morse and AMTOR.

MSPEED		Sets transmit speed, 5 to 99.
  MSP

MWEIGHT n	n = 5 to 15.  10 is default, 1:1 dot/space ratio.
  MW n		5 = 0.5:1 ratio.  15 = 1.5:1 ratio.

NEWMODE		ON--automatic Command Mode on disconnect.
  NE		OFF--no return to Command Mode on disconnect.

NOMODE		ON--PK-232 switches modes explicitly--NEWMODE ignored.
  NO		OFF--PK-232 follows NEWMODE.

RECEIVE n	0 - $7F (1 - 127 decimal). The control character in a file
  R n		to switch from transmit to receive.  Default is CTRL-D ($04).

TCLEAR		Clears the transmit buffer, cancels further transmission
  TC		of data.  May not clear all packets.

WORDOUT		ON--characters held in transmit buffer until space, or
  WO		punctuation.  OFF--characters sent at once.  Default is OFF.

XMIT		Immediate command to transmit in Command Mode (CTRL-C for
  X		Command Mode.)

------------------------------------------------------------------------------

Packet Commands:

8BITCONV	ON--does NOT strip high order bit in CONVERSE mode.
  8B		OFF--Strips high order bit.  Default is OFF.

ACRPACK		ON--CR, the send packet character, is added to all packets.
  ACRP		OFF--not added.  (Converse mode.)  Default is ON.

ALFPACK		ON--LF added to each packet after CR.
  ALFP		OFF--no LF added.  Default.

AUDELAY n	n = 0 - 120 of 10 msec delay between PTT line clsoed and
  AUD n		start of audio.  Default is 0.

AX25L2V2	ON--Version 2 protocol.  Default is ON.
  A		OFF--Version 1 protocol.

AXDELAY n	key-up delay for voice repeaters, 10 msec.  0 - 190.
  AXD  		  Default is 0.

AXHANG N	'hang time', 100 msecs.  0 - 20.  Default is 0.
  AXH

BEACON EVERY|AFTER n	EVERY--Beacon at regular intervals.
  B			AFTER--After no activity.
			0--off.
			n--10 second intervals, 1 - 250.

BTEXT <120>	BEACON text message. Clear with %, &, N, NO, NONE, or OFF.
  BT <120>	  (See PASS.)

CANLINE n	n = 0 to $7F ASCII code.  CANCEL-LINE input editing
  CAN		  command character.  Default is CTRL-X, $18.

CANPAC n	n = 0 to $7F ASCII code.  CANCEL-PACKET input editing
  CANP n	  command character.  Default is CTRL-Y, $19.

CASEDISP n	Characters to display. 0 = as is (no change).  Default.
  CAS n		  1 = lower, lower case only.  2 = UPPER, upper case only.

CBELL		ON--Three bell characters sent to terminal with "connected
  CB		  to" message.  OFF--no bell sent.

CFROM all, none, yes, no--accept or reject requests for connect.
  CF		Default is ALL.  Clear with %, &, or OFF.

CHCALL		ON--callsign of distant station displayed in multiple
  CHC		  connection operation.  OFF--not displayed.  Default is ON.

CHDOUBLE	ON--received CHSWITCH characters doubled.  See CHSWITCH.
  CHD	          OFF--received CHSWITCH characters not doubled.  Default.

CHECK n		1 to 255 is check time in 10 second intervals.  Default = 30.
  CH		  0 disables.  Connect timeout.  AX25L2V2 dependent.

CHSWITCH n	n is an ASCII character, 0 to $29, $40 to $FF, for new.
  CHS n		  connection channel. Default is $00.  
		  See CHCALL and CHDOUBLE.

CMDTIME n	0 to 255 in 100 msec intervals for timeout in transparent 
  CM n		  mode and return to CONVERSE mode.  Default is 1 sec.

CMSG		ON--CTEXT message sent on connect request.
  CMS		OFF--CTEXT message not sent.  Default is OFF.

CONMODE		CONVERS--automatic CONVERSE mode on connect.  Default.
  CONM		TRANS--automatic TRANSPARENT mode on connect.

CONNECT call1 [VIA call2 <,call3,...call9>]  call1 is distant station.
  C call1...	  call2 to call9, are digipeaters in path.  See RETRY.

CONPERM		ON--Disconnected state not allowed on current connection.
  CONP		OFF--disconnection allowed.  Default.

CONSTAMP	ON--connect staus messages are time stamped.
  CONS		OFF--connect status messages are not timestamped.  Default.

CPACTIME	ON--Packet transmit timer is used in CONVERSE mode.
  CP		OFF--timer not used.  See PACTIME, SENDPAC, ACRPACK.
		  Default is off.

CSTATUS		Immediate command to display the status of all channels.
  CS

CTEXT <120>	If CMSG is ON, then CTEXT message is sent on connection
  CT <120>	  by another station.  120 characters maximum.

DCDCONN		ON--RS-232 pin 8 follows the state of the CON LED.
  DC		OFF--pin permanently set high (active).  Default.

DFROM all, none, yes/no call1 [, call2, ... call9]  Digipeater request
  DF		  control.  Default is ALL.

DISCONNE	Immediate command to disconnect from another station.
  D

DWAIT n		Delay to Packet transmitter keydown sequence in
  DW n		  10 millisecond intervals.  Default is 16 (160 msecs).

FRACK n		1 to 15, FRame ACKnowledgement timeout, 1 second intervals.
  FR		  Default is 3.

HBAUD n		PK-232 to radio baud rate.  45, 50, 57, 75, 100, 110, 150,
  HB n		  200, 300, 600, 1200, 2400, 4800, 9600.  Default is 1200.

HEADERLN	ON--header and monitored packet on same line.  Default is ON.
  HEAD		OFF--header and packet text on the same line.

HID		ON--PK-232 sends HDLC identification as a digipeater.
  HI		OFF--does not send HDLC identification.  Default is OFF.

ID		Sends special identification packet on closing a digipeater
  I		  station down.  HID must be ON.

ILFPACK		ON--PK-232 ignores all LF's from terminal.
  IL		OFF--transmits LF's from terminal.  Default is OFF.

KISS		ON--KISS TNC.
  KI		OFF--AX.25 Level 2 TNC.  Default is OFF.

MAXFRAME n	1 to 7 limit on unacknowledged packets on a link at
  MAX		  one time.  Default is 4.  1 is best for HF.

MBX call1[,call2][-'n']  Monitor station.  Call1 and call2 must be 
  MB		  in contact for MBX to work.

MCON n		Monitor Packet at various levels when connected.  
  MC n		  Default is 0.

MDIGI		ON--I and UI frames displayed if MYCALL or MYALIAS is
  MD		  next digipeater.  OFF--Normal monitoring.  Default is OFF.

MFILTER n1[,n2, ... ,n4]  Characters to be excluded from monitored packets,
  MFI ,,,	  e.g., CTRL-L, CTRL-Z, etc.  Default is $07, $13.

MFROM ALL/NONE or YES/NO call1 ... ,call8.  Display ALL/NONE packets, or 
  MF		  YES/NO with call list.  See MTO.  Default is ALL.

MHEARD		Immediate command to list stations heard, to a maximum
  MH		  of 18.  Disabled by PASSALL ON.  Clear with %, & N, No...

MID n		n = 0 - 250 is Morse ID timing in 10 second intervals.
  MI n		0 disables function.

MONITOR n	Monitor level setter, 0 to 6. Page 6-73.  Default is 4.
  M n

MRPT		ON--Digipeaters in header.  Default is ON.
  MR		OFF--Packets from originating and sestination stations only.

MSTAMP		ON--monitored frames are time stamped. See DAYSTAMP, HEADERLN.
  MS		  DAYTIME.  OFF--frames are not time stamped.  Default is OFF.

MTO ALL/NONE or YES/NO call1[,call2 ...,call8]  Stop display of packets
  MT		  addressed to all stations = ALL.  See MFROM.  Default: NONE.

MYALIAS call[-n]  Alternate idenity of the PK-232.
  MYA ..

MYCALL call[-n]  call = station call sign.  -n = substation ID (SSID).
  MY		Must be used for PK-232 to work packet.  Defautl is PK-232.

NEWMODE		ON--automatic Command Mode on disconnect.
  NE		OFF--no return to Command Mode on disconnect.

NOMODE		ON--PK-232 switches modes explicitly--NEWMODE ignored.
  NO		OFF--PK-232 follows NEWMODE.

PACLEN n	0 to 255 (zero = 255) for length of the data portion 
  PACL	n	  of a packet.  Default is 128.

PACTIME	EVERY|AFTER n	0 - 250 100 millisecond intervals.
  PACT EVERY|AFTER n	Packetizes input from keyboard EVERY n 100 msec
		interval or AFTER n 100 msecs of no keyboard input.
		Default is 10 (1000 msecs).  Always used in transparent mode,
		and with CPACTIME ON in Converse Mode.

PASS n		0 - $07F (0 - 127 decimal)  The character used to "pass" the
  PAS n		  next character in Converse mode.  See BTEXT and CTEXT.
		  Devault is $16, CTRL-V.

PASSALL		ON--PK-232 aceepts packets with bad CRC"s.
  PASSA		OFF--PK-232 accepts packets with valid CRC's only.  Default.

PERSIST n	1 - 254 threshold value for a random number attempt to
  PE n		transmit.  0 is 1/256th chance every SLOTTIME, 255 is
		transmit right away.  Default is 127.

PPERSIST	ON--The pk-232 uses PERSIST and SLOTTIME parameters in
  PP		executing p-persistant CSMA (Carrier Sense Multiple Accesss).
		OFF--PK-232 uses DWAIT for TAPR-type 1-persistent CSMA.
		Default is OFF.

RELINK		ON--automastically tries to relink after time-out on retries.
  REL		OFF--No relink after failed attempt.  Default is OFF.

RESPTIME N	0 - 250 delay of 100 milliseconds before sending
  RES n		acknowledgemenat packets.  Default 10.  Prevents collisions.

RETRY n		0 - 15 = Number of frame transmission retries before
  RE n		disconnect.  Default is 10.

SENDPAC n	0 -$7F ( 0 -127 decimal), the caharacter used to force
  SE n		a packet to be sent in converse mode.  Default is CTRL-M ($0D)
		(<CR>).  See CPACTIME, CR ON.

SLOTTIME n	0 - 250 10 millisecond intervals between random number
  SL n		transmit attempts.  Default is 1.

SQUELCH		ON--positive squelch.  Stops doubling with voice on Packet
  SQ		channel.  OFF--megative sqyelch.

TCLEAR		Clears the transmit buffer, cancels further transmission
  TC		of data.  May not clear all packets.

TRACE		ON--trace function on--headers displayed.
  TRAC		OFF--trace off.  Default is OFF.

TRANS		Immediate command to switch to Transparent Mode.
  T		Transparent mode for binary file transfer.

TRIES n		0 - 15 number of retries on given input channel.
  TRI n		See RETRY.  Also PACLEN and MAXFRAME.  Default is 0.

TXDELAY n	0 - 120 10 milliseconds interval after keying PTT line.
  TXD n		Default is 30 (300 milliseconds).

TXFLOW		ON--terminal software flow control activated in Transparent
  TXF		mode.  OFF--no software terminal control.  Default is OFF.

UNPROTO	call1[ VIA call2[, call3,,, call9]]  Call1 goes to "TO" field.
  U ...		If no call then "CQ".

USERS n		0 - 10 simultaneous incoming connections.
  US n		Default is 1.

VHF		ON--Packet tones are shifted 1000 hz for VHF.
  V		OFF--200 hz shift.  HBAUD at 300. Default is ON.

WHYNOT		ON--reason why packet not displayed.
  WHY		OFF--no reason displayed.

XMITOK		ON--PTT line active.
  XMITO		OFF-transmit (PTT) disabled.  Default is ON.

------------------------------------------------------------------------------

SIAM (Signal Identification and Acquistion Mode) commands.

OK		Sets RXREV, RBAUD or ABAUD, and OPMODE to SIGNAL
  OK		analysis values.

SIGNAL		Starts analysis.
  SI

End of file.