Description of TTY Program
TTY requires advanced basic 1.1, communications adapter,
and 80 character wide screen.
Comm adapter pins used are (2) xmit data, (3) rcv data, and (20) DTR.
DTR is active (plus) when the program is in transmit mode, and may
be used to control t/r switching in the TU or transceiver.
TTY transmits and receives 5 bit teleprinter code (murray/baudot)
at 45.45 baud (60 wpm) in half duplex mode and is intended for use
in the amateur radio service.
This documentation assumes the reader is familiar with amateur radio
teleprinter conventions and practices.
CAUTION: The IBM PC comm adapter uses rs 232 input and output voltage
levels of +12v/-12v. Most commercial TUs use TTL levels 0v/+5v.
Conversion circuitry may be required.

The TTY menu provides for selection of receive or transmit mode.
Switching between transmit and receive modes is done by calling the
menu, using the F10 key.
In receive mode, the normal mode of operation is to ignore incoming
cr and lf characters, and print full lines of 80 characters to the
display and printer. However, the F1 key may be used to select a mode
of operation in which cr/lf characters are recognized, and normal
teleprinter operation is simulated. F1 toggles this function on/off.
F2 toggles the PC line printer on/off.The printer is used in receive
mode only.
In receive mode, the program is arranged for "unshift" on space,
cr and lf, as well as "ltrs".

In transmit mode, ltrs and figs shift characters are inserted
where needed by the program.Ltrs and figs cannot be sent directly
from the keyboard. The ascii cr (enter) key sends a cr/lf/ltrs
sequence.The program assumes that the receiving terminal is
equipped with unshift on space, and inserts figs accordingly.
F3,F4,F6,and F7 are used to send preprogrammed messages. These
messages reside at lines 17000,18000, 20000,and 21000, and may
readily be changed to meet the needs of your station.
F5 sends the required Morse code station identifier. This subroutine
starts at line 19060. Morse code is sent by calling dit, dah, and
intercharacter space subroutines at 19500,19600,and 19700 in sequence.
Change lines 19060 thru 19080 to send your callsign.
The program will accept either upper case or lower case keyboard entry.
Other ascii characters which have no equivalent in murray code are
ignored.

Hints and Kinks:

The `ignore cr/lf' mode is very useful when receiving conditions are
less than perfect, and produces much more reliable copy. However,if the
chap on the other end wants to send you some teleprinter art, use the
cr/lf `on' mode.
If the other station is using a conventional teleprinter, his line
length is probably 70 or 72 characters. TTY lets you send 80 character
lines which will overprint at the other station. Be careful!
In transmit mode, characters appear on the screen when they are sent
to the output buffer. The screen may be up to 128 characters ahead of
the comm adapter output! F5 or F10 (cwid or return to menu) are stored
and do not take effect until the buffer is empty. Hence the program
may appear to `hang' while the buffer is emptying. Be patient! If it
didn't work this way, some of your deathless prose would be lost down
the bit bucket!
73 es GL de Bob Johnson AA4L, 11305 Rums Hill, Raleigh NC 27614
 phone 919 847 5606