TAP-std working group                                       D. Bernstein
RFC NNNN                                                              IR
                                       June 1991, revised 17 August 1992

			          TAP


Status of this Memo

   This memo provides information for the Internet community. It does
   not specify an Internet standard. Distribution of this memo is
   unlimited.


1. Introduction

   It is common for Internet hosts to associate relatively long-lived
   information to each TCP connection, often (but not always) including
   a ``username'' or ``owner name'' or some other information about the
   entity using the connection. TAP announces the information associated
   with a particular TCP connection to the host on the other end of the
   connection. TAP may be used on any host which associates relatively
   long-lived information to each connection.


2. Overview

   This is a connection-based application which runs over TCP. The TAP
   server listens for TCP connections on port 113 (decimal). After a
   connection is established, the server reads one line of data which
   specifies the connection of interest. If that connection exists and
   is associated with system-dependent information, the server sends
   the information. Otherwise it sends an error line. After sending the
   information or error line, the server closes its connection. After
   reading the information or error line, the client closes the
   connection.

   The server will give information about TCP connections between the
   server's host and host H only to host H itself. The two hosts (i.e.,
   IP addresses) involved are not transmitted explicitly by the
   protocol; they are implicit in the connection made to the server.


3. Request format

   The server accepts simple text query requests of the form

      <localport> , <foreignport>



TAP-std working group                                           [Page 1]


RFC NNNN                         TAP                         August 1992


   where <localport> is the TCP port on the server's host and
   <foreignport> is the TCP port on the client's host. All numbers are
   expressed in decimal without a sign, and all text is ASCII. If the
   request is not in this format, the server may immediately drop the
   connection.

   For example, say rose is connected to the standard TELNET port on
   host tulip, through TCP ports 6191 on rose and 23 on tulip. (Note
   that rose and tulip are simply names used in this document to
   identify two IP-connected machines. They are not fully qualified
   domain names.) tulip connects to the TAP server at port 113 on rose.
   It sends this line:

      6191 , 23

   Here 6191 is the TCP port on the TAP server's host (rose) and 23 is
   the TCP port on the TAP client's host (tulip). This uniquely
   specifies the given TELNET connection.

   The precise format of the request line is as follows: <localport>,
   followed by any amount of whitespace, followed by a comma and any
   amount of whitespace, followed by <foreignport>, followed by carriage
   return and line feed. Whitespace means space or tab; "any amount"
   means zero or more, though a client should not print excessively many
   spaces. The server should read until the line feed and respond
   immediately. The client should not send anything after the line feed,
   though future revisions of this specification may permit additional
   data. The client should not add initial zeros to its decimal numbers,
   but the server must accept such numbers. Future revisions of this
   standard may assign additional meaning to decimals with a leading 0.


4. Response format

   The server sends a response line in one of these two formats:

      <localport> , <foreignport> : USERID : <systemtype> : <conn-info>
   or
      <localport> , <foreignport> : ERROR : <errortype>

   Here <localport> and <foreignport> are the same numbers as in the
   query. (If the client uses initial zeros, the server may do so as
   well, but otherwise it should not use initial zeros.) <systemtype> is
   an operating system name for the server's host as described in
   Assigned Numbers, RFC 1060 or its successors. <conn-info> is
   system-dependent information associated to the connection.
   <errortype> is text describing an error as outlined below.




TAP-std working group                                           [Page 2]


RFC NNNN                         TAP                         August 1992


   <systemtype> may also be OTHER to specify any other operating system
   not yet listed in Assigned Numbers. Even if the server's system is
   listed in Assigned Numbers, the server may use OTHER for any reason,
   including operating system type privacy. Future revisions of this
   document may permit further values of <systemtype>.

   <conn-info> is in some format defined by the system. This document
   does not define the format or meaning of <conn-info>. Often
   <conn-info> is in the same format as a system-dependent mailbox name,
   which is typically in the same format as a system-dependent username,
   but these equivalences are not required. <conn-info> could be
   encrypted with a secret key; it could carry something other than
   information about the entity using the connection. For the purposes
   of this protocol, <conn-info> is an uninterpreted octet string. See
   section 5 for further details.

   For example, some possible responses to the 6191 , 23 query might be
   the following:

      6191 , 23 : USERID : UNIX : joe
      6191 , 23 : USERID : MULTICS : StJohns.DODCSC.a
      6191 , 23 : USERID : OTHER : StJohns.DODCSC.a
      6191 , 23 : USERID : TAC : MCSJ-MITMUL
      6191 , 23 : USERID : UNIX : a6X#-Yp,3147,2910
      6191,23     :USERID:OTHER:wewishyouamerrychristmasandahappynewyear
      6191 , 23 : ERROR : NO-USER

   An ERROR line means that the server could not determine the
   information associated to the TCP connection. <errortype> tells why.
   <errortype> may be any of the following:

      INVALID-PORT

	 <localport> or <foreignport> was improperly specified---out of
	 the range 0 to 65535, for example---or the request was
	 otherwise non-standard. In this case the server may drop the
	 connection without replying.

      NO-USER

         The connection specified by the port pair is not currently in
         use.

      HIDDEN-USER

	 The connection is in use, but the information associated to it
	 is explicitly hidden.




TAP-std working group                                           [Page 3]


RFC NNNN                         TAP                         August 1992


      UNKNOWN-ERROR

         Cannot determine the information associated to the connection,
	 for an unknown reason. The server may give this <errortype> in
	 any case and for any reason, including privacy, whether or not
	 another <errortype> applies.

   Future revisions of this document may allow other <errortype> values.
   The server may also report an <errortype> beginning with the letter
   X; all such <errortype>s are reserved for experimental or
   non-standard use.

   The precise format of the response line is as follows: <localport>,
   followed by any amount of whitespace, followed by a comma and any
   amount of whitespace, followed by <foreignport>, followed by any
   amount of whitespace, followed by a colon and any amount of
   whitespace. In the USERID case, it is then followed by USERID and any
   amount of whitespace, a colon and any amount of whitespace,
   <systemtype> and any amount of whitespace, a colon and any amount of
   whitespace, one or more characters giving <conn-info>, and finally
   carriage return and line feed. In the ERROR case, it is followed by
   ERROR and any amount of whitespace, a colon and any amount of
   whitespace, one or more characters giving <errortype>, and finally
   carriage return and line feed.

   Note that this format is ambiguous if <systemtype> contains colons or
   whitespace. Assigned Numbers does not currently list any <systemtype>
   with colons or whitespace, but if it ever does, the TAP server must
   use OTHER for the <systemtype> on such a machine. The server should
   also not use a <systemtype> containing carriage return or line feed.

   Similarly, if <conn-info> or <errortype> begins with whitespace or
   contains carriage return-line feed, the response line format is
   ambiguous. The server must never use <errortype> containing
   whitespace, carriage return, or line feed, and future revisions of
   this RFC will never provide for such an <errortype>. The server
   cannot send <conn-info> beginning with whitespace or containing
   carriage return-line feed; it should not send <conn-info> containing
   whitespace, carriage return, or line feed. ERROR : UNKNOWN-ERROR is
   preferable.

   Finally, <systemtype>, <conn-info>, and <errortype> cannot be empty
   strings, and cannot contain ASCII NUL (character 0).
   







TAP-std working group                                           [Page 4]


RFC NNNN                         TAP                         August 1992


   Later revisions of this protocol specification may further restrict
   the octets which may be transmitted. In light of this, servers
   should, if possible, limit <conn-info> to at most ASCII codes 33
   through 126. Clients should, however, be prepared to handle all
   octets.

   Note that there is no limit on line lengths: in particular, on the
   length of <conn-info>. The client may drop the connection at any
   time to avoid overflow. The server should, if possible, place the
   most useful information within the first 512 characters of
   <conn-info>.


5. Applications and security

   A TAP server may place any information it wants into its responses to
   a TAP query. This protocol does not assign any meaning to <conn-info>
   beyond its intrinsic existence as an octet string. So, in most cases,
   a TAP client will simply record the bytes of <conn-info> in some
   manner for possible interpretation later by the server host. This is
   primarily useful as a form of remote auditing: if the client host
   judges that the TCP connection represents an accidental or malicious
   malfunction on the part of the server host, then <conn-info> may
   permit the server host's owner to track down the exact source of the
   malfunction. So the information returned by TAP in this case is of
   primary benefit to the host generating that information.

   The TAP client can do nothing more than this unless it has an
   external reason to assign meaning to <conn-info> received from that
   particular host. Beware that assigning <conn-info> an unjustified
   meaning will in general lead to security holes. Do not use TAP for
   access control without documenting the external knowledge you have
   which ensures that your use of <conn-info> for access control is
   justified. An attacker could subvert the security of a server host or
   of TCP/IP; and any host could send any information it wants along a
   TAP connection. Two dangers of weak methods of access control are
   that they may permit access which should be denied, and that they may
   deny access which should be permitted.


6. Notes

   This section is not part of the TAP description proper. It provides
   historical information and pointers to further information.







TAP-std working group                                           [Page 5]


RFC NNNN                         TAP                         August 1992


   TAP is derived from the protocol defined in RFC 931 by Mike StJohns.
   It was first implemented by this author in early 1990, then again in
   February 1991, and distributed via the USENET network under the name
   authd. Later in 1991 two more independent interoperable
   implementations were distributed through the Internet. In 1992
   another independent interoperable implementation was distributed.
   TAP, as defined in this document, is the same as the authd protocol,
   which has not changed since its first implementation in early 1990.

   This document is a cooperative effort of the TAP-std working group.
   TAP-std is an ad-hoc group with the following charter: ``This group
   is chartered to document the TAP protocol as used on TCP port 113
   around the Internet. Its first goal is to publish as quickly as
   possible an accurate, well-understood, complete TAP specification
   which reflects the consensus of the community. Afterwards it will
   keep track of TAP usage and produce further documents as necessary.
   This group will not publish as a standard any TAP variation which has
   not been tested on the Internet, though it will make all reasonable
   allowances for future extensions.''

   At the time of publication of this document, you can join the
   tap-std mailing list by sending a subscription request to
   tap-std-request@kramden.acf.nyu.edu, or by connecting to TCP port
   39311 on 128.122.142.2 and typing your username. There is also a
   mailing list for people who want to use TAP to solve problems. To
   join, send mail to rfc931-users-request@kramden.acf.nyu.edu.

   The author would like to thank Chris Davis, Peter Eriksson, and Dave
   Borman for their helpful suggestions used in creating the TAP-std
   base document. Thanks go to all the participants in the TAP-std
   working group for their suggestions, comments, and criticism.


Security Considerations

   Security issues are discussed in section 5.


Author's Address

   Daniel J. Bernstein
   5 Brewster Lane
   Bellport, NY 11713

   Email:  brnstnd@nyu.edu






TAP-std working group                                           [Page 6]