Availability of cards for PCroute or PCbridge.

PCroute and PCbridge were first designed to work with the Western Digital
WD8003E card.   Later Western Digital came out with 16 bit versions
WD8013EBT that PCroute and PCbridge also support.   Unfortuately both
of these cards are no longer available.  The have been replaced with the
WD8003EP and WD8013EP (as well as others).  Unforunately these cards are
not exact replacements and SOME people have experienced problems getting
them to work.   Thus if you are buying new cards you have a problem.  
Some solutions are:

	1) Try it and see.  As I said most people do not have problems.  For
	   all I know it is not the cards at fault but some other aspect
	   of installation.  It is also possible that certain early batches
	   of cards were slightly different and this caused the bug.  Thus
	   you stand a good chance of it working by simply using the
	   WD80xEP cards.  Be aware that you MAY have problems however.

	2) Use 3c507 card.  PCroute also supports this card.  This card IS
	   still available.  Unforunately it is more expensive.  On the other
	   hand, it IS a very good, high performance card, so you are not
	   spending your money for nothing.

	3) Use packet drivers.  PCroute (but NOT PCbridge) can used packet
	   drivers (available from sun.soe.clarkson.edu in packet-drivers 
	   directory).  This allows most ethernet cards to be used.  
	   Unfortuately this solution slows the router down by more than
	   half.

	4) Use the COMPEX card.
		 It has been reported that a WD8013EBT clone exists and works
		 well with PCroute and PCbridge.  It is made by COMPEX.  It
		 is also quite cheap (cheaper than the original!).    The 
		 model number is #ENET-16-COMBO (supports UTP/AUI/BNC).  
		 Revision D has been confirmed to work.  Cost is $115 (3/93).
		 There seems to be a version that is slightly less expensive 
		 ($95) that does not have UTP support.    A possible vendor
		 is given below.  Note that this information is supplied simply
		 as a courtesy, it is not a recomendation for this card or
		 this particular vendor.

					Advance Computer Support
					5515 North 7th Street
					Suite 5-504
					Phoenix, AZ 85014

					PH: 602-305-1345 (Hagan Fox)

If you are buying Western Digital cards (now owned by SMC), or 3Com cards
(andy maybe even COMPEX cards), the best place to get a good price is probably
the back of PC Shopper Magazine.  If you don't have this most other PC
oriented magazines have a shopping section (PC Magazine, Byte etc).  

Good Luck