INSTALLATION of PCROUTE

    Installation of PCroute consists of essentially four parts.

        1) Compiling the software
        2) Setting up the hardware.
        3) Configuring the software.
        4) Testing.

    This section tells you the 'theory' behind the installation 
    process.  Files of the form *.EXA are example installations of 
    precompiled PCrouters provided with this release. 


1) COMPILING THE SOFTWARE

        PCroute can have as many as 6 network interfaces attached
    to it, however, for efficiency reasons, the number and type of
    interface must be COMPILED into the code.  For convenience, PCroute
    is distributed with compiled version of the following

        Ethernet (WD8013E) - Ethernet (WD8013E)   called wd13wd13.exe
        Ethernet (WD8003E) - Ethernet (WD8003E)   called wd03wd03.exe
        Ethernet (PKT DRV) - Ethernet (PKT DRV)   called pktpkt.exe
        Ethernet (PKT DRV) - SLIP     (PKT DRV)   called pktslip.exe
        Ethernet (WD8003E) - SLIP     (WD8003E)   called wd03slip.exe
        
    If any of these are the configuration you want, simply rename the 
    proper one to 'pcroute.exe' and go on to step 2.  Note that starlan
    cards will work in code compiled for the WD8003E card, but works
    better if a version of the code is specifically compiled for the
    WD8003S card.

        If you need to recompile, you will need TURBO assembler 1.0.  
    MASM does NOT work, for reasons I have not looked into.  If you want, 
    you can try porting it but since Turbo assembler cost only $69, it 
    is probably not worth porting.

        Before you compile and link the code, you must first declare
    how many and what types of interfaces the router will have.  You do
    this by modifying the DECLARE.INC file.  No other files need to be
    changed!  For most configurations, it is just a mater of uncommenting
    the right declarations.  The general case, however, requires some
    understanding of DECLARE.INC.  For a full discussion on this, see
    the document COMPILE.DOC.

        After you have modified DECLARE.INC simply compile and link
    the files as shown below.  

            TASM /KS170 *.ASM
            LINK

    LINK invokes the LINK.BAT file, that contains (the rather long)
    turbo link command.

--------------------------------------------------------------------------
2) HARDWARE SETUP

    Hardware setup simply involves getting the proper networking 
    cards, jumpering them properly, and installing them in the PC
    to be used as a router.   Note that PCroute only requires less
    than 128K of RAM itself, so 256K PCs are fine (more memory
    buys you NOTHING!). 

    The type of cards, and the jumper settings for them are all 
    determined by the declaration in DECLARE.INC.  In addition each
    interface is given a number (starting with one) based upon its
    order in DECLARE.INC.  This number will be used below when we
    configure IP addresses.

    WD8003 Cards (Starlan or ethernet)

            There are only two settings that have to be made on each
        of the WD8003 Cards.  The first is configuring it for THICK/THIN
        ethernet, and the other is the I/O address of the card (interrupts
        are not used so the Interrupt number is irrelevant, as long as
        it does not conflict with other hardware).

            Refer to the DECLARE.INC file to determine the I/O addresses
        for the ethernet cards.  In DECLARE.INC there will be a line 
        WDE_DECLARE (for ethernet) or WD_DECLARE (for starlan) for each
        card.  The second parameter on this line is the I/O address of
        the card.  Set jumpers on the respective card to agree with this
        number.   For precompiled routers the first WD8003 card has I/O
        address 280H, and the second (in the case of the ether-ether router)
        has I/O address 2A0H.

            Also make sure to make sure the card is configured for the
        correct type of ethernet.  From the factory these cards are 
        configured for THIN Ethernet (BNC connector), if you are not using 
        THIN Ethernet (That is you are using the 15 Pin DSUB connector), 
        you will need to change a bank of jumpers.  Refer to the manual 
        that came with the card on exactly how to do this.

            If you are using a 6Mhz AT (and only a 6Mhz AT), you should 
        set one more jumper on the wd80003e.  This jumper determines the
        number of wait states used when accessing the shared memory and
        for a 6Mhz AT the default is not optimal.  Consult the Manual that
        came with the Ethercard for more details.

            SLIP AND PACKET DRIVER USERS: Since SLIP and Packet drivers
        both use interrupts, if these are used it is VERY important that
        the WD8003 cards are jumpered so that their IRQ does not
        conflict with the ones used by SLIP or the card used with the
        packet driver.  You may set all the IRQ's of the WD8003 cards to
        the same IRQ, but this must be different from the IRQs used by
        any other hardware.  Since COM2 uses IRQ 3 and many popular cards
        use IRQ 3 by default, some care is required to avoid a conflict.
        On an XT IRQ 2, 3, 4 are not used by standard hardware.  In
        addition, if the PC does not have a hard drive CONTROLLER IRQ 5 is 
        also available.  COM1 uses IRQ 4 and COM2 uses IRQ3.  Keep this in 
        mind when choosing Interrupts for your cards.

    Packet Driver Hardware

        For those who are unfamiliar with Packet drivers, a packet driver
        is a software spec designed by FTP software et al that hides
        the hardware dependencies of networking cards.  The idea is that
        you write your software to work with the packet driver, and then
        it will work with any networking card that is supported.  Information
        on the packet driver spec as well as packet drivers for many common
        network cards is available from sun.soe.clarkson.edu (128.153.12.3).

        PCroute is able to run using the packet driver software interface.
        Note however that there is a heavy performance penalty to pay.
        PCroute will forward packets at only 1/3 the speed of a native
        interface.  Still for may applications this is acceptable (certainly
        if one of the interfaces is SLIP).  

        Packet drivers are accessed through a software interrupt.  This
        interrupt number as well as hardware information is passed on the
        command line of the command that loads the packet driver.  PCroute
        expects a different packet driver for each card using the packet
        driver.  The software interrupt PCroute uses is on the PKT_DECLARE
        line in DECLARE.INC.  Default interrupt numbers are 60H for the first
        packet driver and 61H for the second (if present).  

        Thus the only thing PCroute cares about is the software interrupt 
        number.  All other hardware configuration is arbitrary as long as
        it does not conflict with anything else and that the packet driver
        and the hardware agree on it. 

    Localtalk Card

        PCroute does not directly access the Localtalk card.  Instead it
        goes though the driver that comes with the card (ATALK.EXE).  
        For this reason PCroute can only support one localtalk interface.  
        The card should be configured as specified in the manual that 
        came with the software driver.  The only concern is that there is
        no conflict (in I/O address or IRQ level and DMA channel) with any
        other cards.  The driver (ATALK.EXE) also must be loaded BEFORE 
        PCroute is run.

    Slip Cards

        The SLIP interfaces use a standard COM port for a network interface.
        The maximum number of SLIP interfaces is not limited directly by
        the PCroute software.   Ultimately there are two factors that
        limit the number of interfaces.  First, many cards can only be
        configured to be either COM1 or COM2.  Clearly if you only have
        these cards, only two interfaces can be supported.  Other cards
        allow COM3 and COM4, but do not allow you to choose IRQ lines
        other than 3 and 4.  Since each SLIP line needs its own IRQ, 
        these cards are also a problem.  Finally, standard COM ports place
        a heavy interrupt load on the CPU at high baud rate.  at 19.2K
        50% of the CPU of a 5Mhz XT is used in handling interrupts.  Thus
        a 10Mhz XT or better is recommended for supporting 2 serial lines
        and a 12MHz AT clone is recommended for 4 serial lines.  If you
        are buying serial cards, I recommend buying ones with the 16550AF
        chips in them.  These chips have FIFOs in them that will cut 
        interrupt overhead by 10 times!  With these cards a 5Mhz XT would
        have no problem handling 4 serial lines.

        Like the ethernet cards, the COM cards must be configured so that
        they agree with the declarations in DECLARE.INC.  The precompiled
        version of PCroute is compiled to work with the COM1 PORT (I/O
        address 3F8H, IRQ = 4).  Set the jumpers for each COM port 
        appropriately.  Note that each COM Port needs its own IRQ line.
        Thus make very certain that no other hardware you are installing
        conflicts.  Standard PC hardware (disk, cpu), does not use
        IRQ 2,3 or 4, so these are prime candidates.  IRQ 5 is also 
        available if there is no hard drive controller in the PC.

-------------------------------------------------------------------------
2) SOFTWARE SETUP

    A) Creating a PCROUTE.CFG file

            All the configuration data that PCroute needs is in a file
        called 'pcroute.cfg'.  To ease programming of PCroute, this file 
        is NOT an ascii file.  Instead, it is a binary file, and there 
        is an program called 'config' that edits/creates this file.  

            Thus the procedure to configure PCroute is to run config in
        the directory that PCROUTE.EXE is in.  Config then looks in 
        PCROUTE.EXE and determines how many and what type of interface 
        information is needed. It then prompts for this data.  Among the 
        data config will ask for is

            For every interface it will ask for
                IP address      - self explanatory
                Subnet mask     - MUST begin with 255.255
                Flags           - Meaning below

            Every interface on IP network must have a unique IP address.
        In addition IP has two level hierarchy in its addressing.  Of the
        32 bits in a IP address, a certain number of bits is considered the
        'network' part of the address and the others are the 'host' part.
        IT IS A REQUIREMENT that all hosts on the same network (ethernet)
        have the same network part.  Originally, the network part was 
        encoded into the IP address itself for example if the IP address has
        the form

            <0-127>.X.X.X       Network part first 8 bits (Class A) 
            <128-191>.X.X.X     Network part first 16 bits (Class B) 
            <192-223>.X.X.X     Network part first 24 bits (Class C) 

        It turned out that this encoding schemed was too limited, so a
        'subnetting' mask was added.  Every bit in the subnet mask that
        is a '1' implies that this bit in the IP address is part of the
        network part of the address.  Note, however, that the subnet mask
        have several restrictions

            1) Subnet masks can only cause bits that would have been
               interpreted as the host part to be interpreted as the network
               part.  Thus a class A number MUST have a subnet mask of the
               form 255.X.X.X, a class B number 255.255.X.X and a class C
               number 255.255.255.X.

            2) PCroute network masks must ALWAYS have the form 255.255.X.X

            3) A subneted network MUST have a consistant subnet mask.  For
               example, let us assume IF1 has IP address 129.105.1.2
               and network mask 255.255.255.0, then if IF2 has IP address
               129.105.3.1, then it MUST also have the mask 255.255.255.0.
               This is because 129.105.1.2 and 129.105.3.1 have the same
               network part, 129.105 (as determined by the number's Class)
               thus they must have a consistant view of how that network
               is subnetted, and thus the same network mask.

        Flags - This is a HEX number that determines several configuration
            options for the interface.   In a 'standard' networking 
            environment FLAGS=0 is a good choice.   If you don't know about
            networking, a 'safer' choice is FLAGS = 0BH.

            Bit 0 - Don't send routing (RIP) info out this interface.
                See RIP.DOC for more information about RIP and how to use it.

            Bit 1 - Don't listen to routing (RIP) info from this interface.
                See RIP.DOC for more information about RIP and how to use it.

            Bit 2 - Proxy Arp on this interface.  Normally the router will
                only respond to ARP requests for itself.  With this option
                turned on, it will reply for itself and any IP address such
                that that is in the same network as the interface, but NOT
                in the same subnet (For example if the interface was 
                129.105.3.2 and the network mask was 255.255.255.0 then
                it would respond to any ARP asking for an address that begins
                129.105 but does not begin with 129.105.3).   This is useful
                if you have hosts that do not know how to subnet.  

            Bit 3 - Disable Directed Broadcasts
                Normally it is perfectly legitimate for and IP host to send
                a packet the broadcast address of another network.  The 
                router on the destination network then broadcasts the the packet
                on behalf of the sender.  Unfortunately, if you have hosts
                running old IP code that handle broadcasts improperly, these
                hosts will hear the broadcast and forward it back to the 
                router, who in turns rebroadcasts it.  This is called a 
                broadcast storm, and will quickly saturate the network.  To
                avoid this problem, you can disable directed broadcasts.

            Bit 4 - Disable Sending ICMP redirects
                Normally when a PCrouter receives a packet it has to route
                out the same interface the packet came in, it sends a 
                redirect message to the sender.  Many hosts ignore these 
                packets, so this bit allows you to turn this feature
                off and conserve network bandwidth.

            Bit 5 - Broadcast using old (0's) format
                Normally when PCroute sends out an IP broadcast (sending RIP
                for example), it uses the 1's format.  That is it fills the
                host part of the address with the number which when views
                as a binary number is all 1's.  Old hosts use a simmilar 
                convention, except they fill with 0's instead of 1's.  Turning
                this flag on makes PCroute use the old format.  NOTE THAT
                YOU ARE STRONGLY ADVISED TO USE THE NEW FORMAT IF AT ALL
                POSSIBLE.  The reason for this is a conflict can sometimes 
                lead to broadcast loops which quickly saturate the network.  
                Also if you use this option you should also use option Bit 3 
                (turn off directed broadcast).

        Interface Metric - This is a HEX number that determines the RIP
                metric to be added to routes going through this interface.
                A large number means that this is an undesirable (slow)
                interface.  I recommend the following
                        Ethernet interfaces             metric 1
                        Starlan interfaces              metric 2
                        Localtalk interfaces            metric 3 or 4
                        Slip interfaces                 metric 4
        
        Next the CONFIG program will ask you for interface specific 
        information.  In particular

            FOR LOCALTALK:

                Zone names: CONFIG asks you for a list of zone names
                    that contain all the other PCrouter (or Macs using
                    NCSA telnet).  THIS LIST MUST INCLUDE THE ZONE OF
                    THE ROUTER ITSELF (you can either use its full name
                    or use the abbreviation '*' (the current zone))
                    When PCroute needs to find and IP address, it looks
                    in all of the zones listed here to find it.

            FOR SLIP:

                Baud rate: Slip allows you to configure the baud rate
                    of each of the SLIP lines.  Baud rates up to 19200
                    have been tried.  38400 should work but has not been
                    tried.   Even 57.6K is possible, but that is the limit

                Many people like to 'cheat' and use the same network number
                for the serial line as they do for one of the other networks
                connected to PCroute.  This may work, but it NOT RECOMMENDED.
                It is very likely to confuse PCroute in one way or another.
                Serial lines should be treated EXACTLY as if they where an
                ethernet. In particular the serial line should be given its
                own network number.  If you don't have official network 
                numbers to spare, you can simply use unused class C numbers
                (for example use 223.254.254.1 for IP address of PCroute on
                the serial line).   Then add a Static route of 
                223.254.254.0 -> 223.254.254.1  with metric = 0 and flags = 1.
                This tells PCroute not to propagate this 'hidden' network
                via RIP.
                    
        Next the CONFIG program will ask you for the static routes.  For
        each static route CONFIG will ask you for

            Network number
            Gateway to send it to
            RIP metric (1-16)
            Flags

            1) The network number looks much like a IP address except that
                it has zeros for the host bits.  PCroute does NOT except host
                routes.  The network number 0.0.0.0 has a special meaning,
                it is the default route.  This route will be used as a route
                of last resort.  Note that as far as RIP is concerned the
                default route is just another route.

            2) The gateway it the host to send the packet to.  It must be
                a host directly attached to a network the router is directly
                attached to (that is 1 hop away).

            3) The Metric should be the number of 'hops' the network is away
                from the router.  Note that this number can be inflated for
                less preferred routes (ie though slow SLIP lines for example)
                Note that this number MUST be 1 or more for any normal route.
                (the route mentioned above in the SLIP section is not normal)

            4) The flag bits have the following meaning

                Bit 0 - Silent.  This route will not be propagated via
                        RIP, it will only be used for packet routing.

                Bit 1 - Transient.  Normally any static routes are permanent
                        and cannot be removed by RIP.  By setting this bit
                        you allow the route to be changed by RIP (which
                        means this route will be expired in 90 sec if a RIP
                        update does not come along)

            Static routes should be used SPARINGLY.  Use RIP if you can,
            and you will save yourself a lot of work when your network 
            grows.  I have found it useful to put Transient Default route
            in the table with a metric of 15.  This allows that router
            to operate to between the time that it is booted up and the 
            time it receives its first RIP update.  Because the route is 
            transient, it will be replaced or deleted shortly thereafter.

        Next the CONFIG program will ask you for the address to forward 
        BOOTP packets to.  This can be a directed broadcast (and directed
        broadcasts are not turned off on all routers connected to the 
        destination net).  If you have no diskless machines booting across
        the gateway, just leave this value 0.0.0.0.

        Next the CONFIG program asks you to specify where and what kind
        of error messages it should print.  It asks you for a 

            1) A syslogd host
            2) A facility mask
            3) A priority (0-9)

            1) The syslog host is a BSD UNIX 4.3 system that is running
               the syslog daemon.  This daemon listens for error reports
               and sends them to a person or a file (as directed by
               /etc/syslog.conf).  PCroute logs errors to syslogd as
               facility 'LOCAL0'  Thus by putting the line (on 4.3 systems)

                    local0.debug        /usr/adm/router 

               and restarting syslogd, the daemon will log all messages
               from a PCrouter to the file /usr/adm/router.

            2) The facility mask allows you to filter out messages from
               certain parts of PCroute.  This is really only of use for
               specific debugging, and to this mask should usually be 0.

            3) Error messages from PCroute are given priorities anywhere
               from 0 (Critical) to 7 (debug).  By setting the priority
               low, you can filter out messages.  In addition by specifying
               priorities above 8, you make PCroute log a status message
               every minute.  This is useful in the beginning to make sure
               PCroute is still alive.  For production system, you should
               set this value to 7 (everything but debugging).

    B) Create a Floppy to boot from 

            At this point we are ready to create a floppy that will be
        used by the PC that will actually be the router.  To do so create 
        a bootable floppy using the FORMAT with the /S option.  Do this on 
        a low density drive it the PCrouter has a low density drive.  

            Next copy the PCROUTE.EXE and PCROUTE.CFG files.  If you are
        running any localtalk interfaces, copy the ATALK.EXE driver too.
        If you are using packet drivers, then you should also copy the
        driver to the bootable floppy.

            Finally create a AUTOEXEC.BAT file that will execute PCROUTE
        when the machine boots.  If you are running any localtalk interfaces,
        the AUTOEXEC.BAT file should load the ATALK.EXE driver before 
        running PCroute.  If packet drivers are used, there should be a
        line in the AUTOEXEC file for each card used.  Each line will have
        the hardware parameters for the card used as well as the software
        interrupt that PCroute will use.  See PACKET.EXA for an example.

------------------------------------------------------------------------------
3) RUNNING and TESTING

        We are now ready to go.  The machine has been installed with the
    proper cards and a bootable floppy with the software on it has been
    created.  Insert the floppy into the PCrouter and try booting it up.

    1) Pinging the PCrouter.  Try pinging the PCrouter from a local host
          on a directly connected network.

    2) Check the log file on the syslogd host.  It should say the the
          router is up (unless you filtered out the message).  Note that
          if the logging host is not on the local network and you are
          relying on RIP to provide routing, this message may not make
          it since PCroute will not know how to route it until it gets
          its first RIP update.  By placing a transient default route
          as described above, you can be sure to get all the messages
          from PCroute.

    3) If the router seems dead, remove the floppy and go to a PC.  
          Look at the file PCROUTE.LOG on the floppy.  This file was
          created when PCroute booted up.  In particular check to
          see that the Ethernet address are reasonable and that the file
          ends with the message 'PCroute closing log file'.  

    4) If the PCrouter replies to the Ping, try pinging it from distant
       hosts.

    5) Also try looking at the routing tables of host that are running
       RIP (routed, gated).  See if the routes that PCroute is announcing
       are being picked up.

    Congratulations!! you just installed PCroute.  If you have any NFS
file systems mounted through the router and you are using cards with
small shared memory (WD8003E), you should edit the /etc/fstab 
(or equivalent) and set the rsize and wsize parameters to 4K so that NFS
will not send more than 4K of data in a quick spirt. (see readme.doc)

------------------------------------------------------------------------

REFERENCES

    For those who are unfamiliar with IP ARP, RIP etc here are 
    some good references.

    IP Tutorial - Internetworking with TCP/IP by David Comer
               available at your local bookstore

    RIP     - rip.doc. Available most places RFC's are available.
            In particular it is available by anonymous ftp from
                uxc.cso.uiuc.edu (128.174.5.50) in dir RFC
                nic.ddn.mil (10.0.0.51) in dir RFC


    RFC     - These are the definitive references for internet standards.
            They are referenced by numbers, and there is a master
            index that is updated periodically.  The are available
            from (among other places)
                uxc.cso.uiuc.edu (128.174.5.50) in dir RFC
                nic.ddn.mil (10.0.0.51) in dir RFC
            Of particular interest might be

                TCP/IP tutorial - RFC1180
                Internet Quest/Ans - RFC1177

                IP protocol - RFC791
                IP subnets - RFC950
                ARP protocol - RFC1011
                ICMP protocol - RFC792
                UDP protocol - RFC768
                BOOTP protocol - RFC951, 1048, 1084