IN CASE OF TROUBLE

    Here is a list of common problems and their solutions as well as some
very useful debugging techniques.  Using these techniques should enable you
to find most problems.  Please let me know if this guide is insufficient.

In general there are three sources of good information for debugging PCroute
they are.
        
        PCROUTE.LOG   - This file is created and written to when PCroute
                        first starts up.  PCroute writes out all its 
                        configuration data to insure that is it what you
                        think it is, and to make sure the hardware is
                        working properly.

        Logging host -  Once PCroute boots up, it sends diagnostic information
                        to the logging host.  This is useful for debugging
                        dynamic problems.

        3rd Party    -  Much information can be gained by using PING 
                        (either to or though the router) traceroute (if you
                        have it) and examine the routing tables (for 
                        RIP problems).

----------------------------------------------------------------------------
PROBLEM: Can't PING PCroute from either local net (PCroute seems dead).

    The first thing to check is the PCROUTE.LOG file on the floppy.

        PCROUTE.LOG does not exist
            Make sure the floppy is not write protected.
            Make sure the floppy is bootable and that PCroute
                is run in the autoexec file.  
            If necessary install a monitor and check the boot sequence

        If PCROUTE.LOG says the configuration file is corrupt, you must
            rerun config.exe.  If that does not work make sure you are
            using the config.exe that came with the version of PCroute that
            you are running.  If that does not work, delete PCROUTE.CFG
            and rerun config.exe from scratch.

        Check the ethernet addresses in the PCROUTE.LOG file.  If any 
            are FFFFFFFFF, that means the card does not have the I/O 
            address set properly, and the software cannot find the card.  

        Check that the IP addresses in PCROUTE.LOG are correct.  Remember 
            for the precompiled PCroute.exe interface 1 is the card with
            I/O address 280H, and interface 2 is the card with I/O
            address 2A0H.  Make sure they are not mixed up.

        Check the ethernet card to make sure it is set for the correct
            type of ethernet (THIN or THICK)

        Check the cabling to the ethernet.

----------------------------------------------------------------------------
PROBLEM: The network comes to a halt when PCroute is brought up

    This symptom indicates a broadcast storm.  This is caused not by
    PCroute but by some other (OLD) IP host.  Try turning off directed
    broadcasts on all interfaces of PCroute (Bit 3 of the interface flags)
    This usually stops the problem, but the real solution is to update
    all old networking software.
        
----------------------------------------------------------------------------
PROBLEM: PCroute can be pinged, but no messages are received by the 
         logging host.
        
    Check PCROUTE.LOG to make sure that the logging host IP address is
        correct.

    Try Pinging PCroute from the logging host, if you cannot there is
        a routing problem (see below).  If possible, choose a logging
        host that is on a local network.

    Maybe you simply filtered out all of the messages, so that PCroute
        SHOULD send nothing.  Good production settings for the filter
        parameters are (mask 0, priority 7), for debugging you should
        use (mask 0, priority 8) and if you set it to (mask 0 priority 9)
        PCroute will send 'I'M ALIVE' messages every minute.

    Make sure that the /etc/syslog.conf file is set up properly it should
        be listening for logging messages from facility 'local0' and
        priority 'debug' (everything).  

----------------------------------------------------------------------------
PROBLEM: PCroute can be pinged from a local net, but not a remote net.

    This is either a a routing problem or a subnetting problem, to
        test if it is a subnet problem, ping a host OUTSIDE your subnet
        from a host that must route through PCroute to get there.  In the
        example, pinging any host that does NOT begin with 129.105 from
        a host on net A will do the job.  If this ping succeeds, the subnetting
        mask is wrong and needs to be changed.

    If it is a routing problem, try inserting a static route, it that solves
        the problem, make sure that the other gateways are broadcasting 
        RIP properly.