This program accepts a list of pole and zero locations and
then calculates the amplitude response for a set of
frequencies.  Real and complex poles can be specified.
However, complex poles are always assumed to occur
in conjugate pairs.  Therefor, only one of a complex
conjugate pole or zero entry per pair is made.  The
other will automatically be created.

New and improved pzsim will accept a much broader range
of frequency scaled root locations without resulting
in an internal overflow.  pzsim will also now calculate
phase response and step response.  A major format difference
from the original program is that every line must end with
a space and a semicolon (i.e., " ;").

Input Format

FS <val> [modif] ;		The starting frequency in Hz.
FE <val> [modif] ;		The ending frequency in Hz.
FP <val> [modif] ;		The number of partitions the
				frequency range is to be divided
				into.
TS <val> [modif] ;		The starting time in seconds.
TE <val> [modif] ;		The ending time in seconds.
TP <val> [modif] ;		The number of points the time range
				is to be divided into.
P <val> [modif] ;		The location of a pole on the real axis.
Z <val> [modif] ;		The location of a zero on the real axis.
PC <val_re> <val_im> [modif] ;	The complex location of a pole.
ZC <val_re> <val_im> [modif] ;	The complex location of a zero.
LOG ;				The output will be calculated in dB
				(attenuation).  Only applies to
				magnitude response.
RADS ;				The starting, ending, and output printed
				frequencies are accepted and printed in
				radians instead of Hz.
PHASE ;				Phase response is calculated and printed
				in degrees.
STEP ;				The step response is calculated.  At
				present, this routine will not work with
				multiple poles at the same location.

Modifiers

All input data can be modified by a metric modifier
or an exponential power.  The modifiers are n,u,m,K,M,G,
for ten to the -9,-6,-3,+3,+6,+9 powers respectively.
An exponential modifier can be entered as "E +36",
which is ten to the thirtysixth power.

Output

The output will be two columns of numbers: the first being the
frequency in hertz, the second being the amplitude response
in absolute units or attenuation in dB, phase response
in degrees, or the step response.  In addition to the x-y
coordinates, further information is supplied to the
output for use by the "plot" program.

Multiple Inputs

Multiple sets of simulations can be executed and directed
to the same plot by deliminating between input sets
of information with the "#" character.