NAME

                srec - convert DSP56000 load file records to Motorola

                       S-record format



        SYNOPSIS

                srec [-1 | -3 | -r] <input file ... >



        DESCRIPTION

                Srec takes as input a DSP56000 absolute load file and produces

                byte-wide Motorola S-record files suitable for PROM burning.

                The DSP56000 START and END records are mapped into S0 and

                S9 records respectively.  All other DSP56000 record types

                are mapped into S1-type records (SYMBOL and COMMENT records

                are currently ignored).  Since the DSP56000 uses a 24-bit

                word size, the words must be split into bytes and stored in

                an appropriate format.  In the default mode of operation the

                program writes the low, middle, and high bytes of each word

                consecutively to the current S1 record being written.  For

                example, given the DSP56000 DATA record below:



                                address field

                                |

                        _DATA P 0000

                        0008F8 300000 340000 094E3E

                        |      |      |      |

                        |      |      |      fourth word

                        |      |      third word

                        |      second word

                        first word



                srec would create the following S1 record:



                          byte count field

                          | address  field              checksum field

                          | |                           |

                        S10D0000F808000000300000343E4E09F9

                                |     |     |     |

                                |     |     |     fourth word

                                |     |     third word

                                |     second word

                                first word



                Output records are written to a file named according to

                the following convention:



                        <basename>.M



                where <basename> is the filename of the input load file

                without extension and M is the memory space specifier

                (X, Y, L, or P) for this set of data words.  Note that a

                separate file is created for each memory space encountered

                in the input file; thus the maximum number of output files

                in the default mode is 4.



                When the -3 option is specified, srec splits each 24-bit

                word into bytes and stores the bytes in three parallel S1

                records.  For example, the following DSP56000 DATA record:



                                address field

                                |

                        _DATA P 0000

                        0008F8 300000 340000 094E3E

                        |      |      |      |

                        |      |      |      fourth word

                        |      |      third word

                        |      second word

                        first word



                would be converted by srec into the three S1 records below:



                          byte count field

                          | address  field

                          | |

                        S1070000F800003EC2 -- low  byte

                        S10700000800004EA2 -- mid  byte

                        S1070000003034098B -- high byte

                                | | | | |

                                | | | | checksum field

                                | | | fourth word

                                | | third word

                                | second word

                                first word



                The three records corresponding to the high, middle, and

                low bytes of each data word are written to separate files.

                The files are named according to the following convention:



                        <basename>.<M><#>



                where <basename> is the filename of the input load file

                without extension, <M> is the memory space specifier

                (X, Y, L, or P) for this set of data words, and # is

                one of the digits 0, 1, or 2 corresponding to low, middle,

                and high bytes, respectively.



                Note that a separate set of byte-wide files is created for

                each memory space encountered in the input file.  Thus the

                number of output files generated is (number of memory spaces

                in input * 3).  The maximum number of output files generated

                with the -3 option is 12.



                The -1 option writes all information to a single file,

                storing the memory space information in the address field

                of the S0 header record.  The values stored in the address

                field and their correspondence to the DSP56000 memory

                spaces are as follows:



                        Value           DSP56000 Memory Space

                        -----           ---------------------

                          1                     X

                          2                     Y

                          3                     L

                          4                     P



                When the memory space changes in the DATA or BLOCKDATA

                record, a new S0 header record is generated.  The resulting

                output file is named <basename>.s, where <basename> is

                the filename of the input load file without extension.

                The -1 and -3 options are mutually exclusive.



                The -r option causes srec to produce the same type of output

                as the default mode, except that the bytes are written high

                to low, rather than low to high.



                Address fields in the DSP56000 records are two bytes and

                are copied as is to the appropriate S1 record (except for

                incrementing as necessary in very long DATA records).  Only

                the module id in the START record is passed as header data

                for the S0 record; the version number, revision number, and

                comment are ignored.



        NOTES

                One (and only one) of the operating system DEFINEs below

                must be activated to obtain appropriate conditional

                compilation.  This can be done either directly in the source

                by changing the 0 DEFINE for the desired operating system

                to a 1, or via the compiler command line (ex. -DATT=1).

                Note that the UNIX flag is simply a logical ORing of the

                more specific Unix OS flags (ATT and BSD) and thus should

                not be specified explicitly.



        OPTIONS

                -1      - write data to a single file, putting memory

                          space information into the address field of the

                          S0 header record. Bytes may be reversed with

                          the -r option.  The -1 and -3 options are

                          mutually exclusive.

                -3      - split each 24-bit word into bytes and store

                          the bytes in three parallel S1 records.   The

                          -1 and -3 options are mutually exclusive.

                -r      - produce the same type of output as default mode,

                          but write bytes high to low, rather than low to

                          high.  to low, rather than low to high.



        DIAGNOSTICS

                The program does some checking for invalid input record

                formats, memory spaces, and hex values.  It obviously

                cannot check for bad data values if the load file has

                been tampered with.  Both START and END records must be

                found in the input file.



        HISTORY

                1.0     The beginning.

                1.1     Added code to support new default mode and -r

                        option (-3 was old default mode).

                1.2     Added support for ATT Unix System V.

                1.3     Fix for bug in default mode where S-record address

                        was not being computed correctly (e.g. not a byte

                        multiple of the 56000 word size).

                1.4     Added support for Macintosh II.

                1.5     Added separate include file, getopt () support,

                        -1 (single output file) option.

                1.6     Fix for bug in default mode when handling BLOCKDATA

                        records; repeated call to reverse bytes was reversing

                        bytes in place!