Device Timeout (ERR=57) on Communication Ports
                        by D. Thomas Mack
                         August 12, 1983

For those who write BASIC programs that read the IBM-PC's
communications Ports, you will occasionally experience a DEVICE
TIMEOUT error condition.  Regretably, under the BASIC interperter
the system will simply "lock up" with the cursor blinking in the
upper left hand corner of the screen.  If the program is
compiled,  you will get a program termination (i.e. it will
return to DOS) with the message on the screen DEVICE TIMEOUT. The
problem occurs  when the program logic is as follows:

1416 ON ERROR GOTO 13000 'Trap error conditions
1420 Y$=INPUT$(1,#3)     'Read the COM1 device as file # 3
1425
              o
              o
13000 'Error Trapping ------------------------
13009 IF ERR=57 AND ERL=1420 THEN RESUME 1425

First the DEVICE TIMEOUT condition occurs on reading a
communication port in the PC for one of four types of errors:

1.  Overrun  -- the PC did not read the data in the Receive
                Buffer Register before the next character was
                put into it,
2.  Parity   -- the parity bit is set incorrectly for the number
                of data bits received,
3.  Break    -- when a break single is detected, or
4.  Framming -- no stop bit detected following the parity bit.

The last two error conditions are handled by DOS and the BASIC
interperter with no problem.  All that has to be done is to
continue processing (i.e. line 13009 above is the correct logic).
Error conditions 1 and 2 are the ones that present the problem
because these indicators are not turned off in the Line Status
Register (LSR) of the 8250 microprocessor that controls the
IBM-PC's communications ports until the LSR is read (i.e. during
an OPEN). If you don't want to cut somebody off by closing and
opening the communications port, you can reset the error
indicators in the LSR  by reading the LSR.  If you don't reset
the LSR and continue processing (i.e. reading the communications
port), you will either lock up your system under the BASIC
interperter or return to DOS if your BASIC program has been
compiled.

However, to handle the first two conditions line 13009 should be
changed as follows for the IBM-PC's COM1 port:

13009 IF ERR=57 AND ERL=1420 THEN R1=INP(&H3FD) RESUME 1425


This error condition normally occurs under RBBS-PC when XMODEM
transfers are taking place.