******* WARNING ***** WARNING ***** WARNING ***** WARNING *********
        *                                                                 *
        * THE AUTHOR OF THIS SOFTWARE DOES NOT PROVIDE ANY WARRANTY WHAT- *
        * SOEVER! YOU USE IT OR TRY IT ENTIRELY AND STRICTLY AT YOUR OWN  *
        * RISK. THE AUTHOR EXPRESSLY DISCLAIMS ANY LIABILITY FOR DAMAGE   *
        * TO YOUR COMPUTER, FILES OR ASSOCIATED ELECTRO-MECHANICAL        *
        * DEVICES. NOR IS THERE ANY GUARANTEE AS TO THE ACCURACY OF THE   *
        * RESULTS OR AS TO THE FITNESS OF THE SUNPO PROGRAMS FOR ANY PAR- *
        * TICULAR PURPOSE.                                                *
        *                                                                 *
        *    REMEMBER, YOU USE IT OR TRY IT SOLELY AT YOUR OWN RISK!      *
        *                                                                 *
        ******* WARNING ***** WARNING ***** WARNING ***** WARNING *********

        1.0 GENERAL INFORMATION
        
        SUNPO will calculate the azimuth and elevation of the sun as a
        function of the date and time of day at any place on the earth
        (with the possible exception of the poles and precisely where the
        0 or 180 degree meridians cross the equator). It will also compute
        the approximate times of sunrise and sunset and the azimuth of the
        sun at those times. In addition, SUNPO provides estimates of the
        sea level solar intensities at visible, uv-a and uv-b wavelengths.
        SUNPO does not take careful account of the fact that a year isn't
        composed of exactly 365 twentyfour hour days, so you may expect
        errors of a few degrees over a leap year cycle.

        Why would you want to know such things? Use your imagination!
        Maybe you would like to know where the sun sets on June 21 (the
        approximate date of the summer solstice in the northern hemi-
        sphere) so that you can figure out where to plant a tree to put
        the shade just where you want it on the longest day of the year.
        Maybe you want to decide how big to make some awnings so that they
        will block the sun's direct rays (or pass them) in some particular
        season. SUNPO's ultraviolet intensity values can help you choose the
        times of day for minimizing your exposure to damaging radiation.
        SUNPO will tell you what you need to know about the sun's position
        and approximate sea level intensity values if you can figure out
        reasons to know them!

        SUNPO's results are displayed as a table showing the local and GMT
        time in a 24 hour "military" format (for example, 6:34 PM would
        appear as 1834). Azimuth angles are measured clockwise from north
        (so, due south corresponds to an azimuth angle of 180 degrees).
        Elevations are measured from a level horizon (straight up is a 90
        degree elevation angle). Results may be saved in an ascii formatted
        file for later printing if desired. There is also an internal print
        command but it funtions properly IF and ONLY IF your default Windows
        printer has graphics capabilities.





        In order to actually run SUNPO you need to know your geographical
        longitude and latitude in at least degrees and minutes. You also
        need to know or figure out a "time zone" value for your location.
        Data for a few cities may be found below.

        Please note: The graphing portion of SUNPO version 1.32 requires that
        the computer be equipped with at least an 80286 cpu and an 80x87 math
        coprocessor or equivalent.

        SUNPO is distributed as Shareware. That means you may try it for a
        reasonable period (say three weeks) at no cost, but that you should
        register it and pay the registration fee if you use it after the
        trial period. SUNPO is supplied as a Windows (3.0) application.


        SUNPO was written using Borland International's Turbo Pascal for
        Windows (1.5), and uses the Graphics Server software marketed by
        Pinnacle Publishing, Inc.

        
        Windows and MS-DOS are trademarks of Microsoft Corporation.
        Turbo Pascal is a trademark of Borland International,Inc.
               
        2.0 INSTALLATION INFORMATION

        2.1 STANDARD FILES
        
        The SUNPO files included in the authorized archive are:

             SUNPO132.EXE - Windows 3.x executable application file.
             SUNPO.INI    - Initialization file for SUNPO132.
             SUNPO.DTA    - Radiance data file.
             SUNPO132.DOC - This file
             SUNPO.BMP    - Logo bitmap file.
             GSW.EXE      - Graphics server executable file.
             GSWDLL.DLL   - Dynamic link library for graphics server.
             CHANGES.TXT  - Brief remarks on changes for this verion.
             READTHIS.NOW - Minimal installation information.
             VALIDATE.DAT - Anti-virus data based on McAffee Associates'
                            VALIDATE.COM (0.4).






        2.1 INSTALLATION HINTS
        
        SUNPO is so simple that no installation program is provided,
        but some basic instructions follow. (Actually, the developer
        does not know how to write a carefree installation program!)

        SUNPO may be run from either a fixed disc drive or directly from a
        diskette that contains all the dearchived files. The notes which
        follow apply to setting up SUNPO on a fixed disc, using a DOS
        Window or perhaps the File Manager.

        While assorted components of SUNPO can be placed in any number of
        directories if your PATH statement has the right properties, it is
        recommended that all of the SUNPO files (except SUNPO.INI, see below)
        be placed in a single dir ectory or sub-directory. That simplifies
        both installation and removal. SUNPO.INI MUST be placed in your
        "base" Windows directory if you wish to use it. An installation
        example follows:

        This example assumes the following:

        A) Your base Windows directory is C:\WINDOWS.
        B) You will place all SUNPO files (EXCEPT SUNPO.INI, which MUST
            be in your base Windows directory) in a NEW directory on fixed
            drive D:
        C) The (de-archived) SUNPO files are on a diskette in diskette
           drive B:, and there are no other files on that diskette.
        D) The installation will be done from DOS or a DOS Window, and that
           your DOS "prompt" appears as C:\>

        Note: in the following example the term <CR> means that you press the
              "RETURN" or "ENTER" key.

        1) Create the SUNPO directory:

           C:\> MKDIR D:\SUNPO <CR>

        2) Copy files:

           C:\> Copy B:\SUNPO.INI C:\WINDOWS
           C:\> Copy B:\*.* D:\SUNPO

        3) Running or Preparing to Run SUNPO:

        METHOD 1: a) Click on the Program Manager's "File" option and
                     select "Run".
                  b) Enter D:\SUNPO\SUNPO132.EXE and <CR>.





        METHOD 2: (add SUNPO to an existing group of applications)
                  a) Click on (or TAB to) the title bar of the desired
                     group.
                  b) Select the Program Manager's "File" option, and then
                     "New".
                  c) Select "Program Item".
                  d)   i) For the "Description" enter: SUNPO
                      ii) For the "Command Line" enter:
                          D:\SUNPO\SUNPO132.EXE
                     iii) For "Working directory" enter: D:\SUNPO
                      iv) Select "OK".

        If all is well, then the SUNPO icon will appear in the program
        group box and you can start SUNPO by clicking on that icon.

        Before running SUNPO, you will probably want to customize it for
        your geographical location. There are two ways to do that:

        1) Edit the SUNPO.INI file to reflect your longitude, latitude and
           time zone before starting the SUNPO application.


           DO NOT EDIT SUNPO.INI USING A WORD PROCESSING PROGRAM (SUCH
           AS WORDPERFECT, WORD FOR WINDOWS OR DOS, ETC) UNLESS YOU ARE
           SURE YOU KNOW HOW TO WRITE THE EDITED FILE IN PLAIN OLD ASCII
           FORM CONTAINING NO EXTRANEOUS INFORMATION INSERTED BY THE
           WORDPROCESSING PROGRAM. MS-DOS'S EDITOR OR THE WINDOWS
           NOTEPAD EDITOR ARE SUGGESTED.

        2) Simply go ahead and run SUNPO and enter your location and time
           zone via the "Observer Position" option under the "Control"
           menu item found on the main SUNPO menu bar. Once you select
           "OK" you will be asked if you wish to save the new data in the
           SUNPO.INI file. Choosing "Yes" will save the customized
           SUNPO.INI file, but the file may not contain the instructional
           comments found in the original version.

        Consult "Help" on the main SUNPO menu bar for other brief hints.

        It MAY BE wise to read the SUNPO.DOC file, however. It contains
        additional information.

        If you will NEVER want to examine SUNPO's graphs, you can omit
        copying of the "GSW..." files (or delete them later).

        If you already have a copy of GSW.EXE and GSWDLL.DLL in a directory
        named in  your AUTOEXEC.BAT's PATH= statement, then you can probably
        save some diskspace by deleting GSW.EXE and GSWDLL.DLL from the
        SUNPO directory. The GSW.. files PROBABLY must belong to at least
        version 2.1, however.

        NOTE: IF YOU USE OS/2-2.X SEE THE END OF THIS DOCUMENT!





        3.0 RUNNING SUNPO

        When you run SUNPO you must provide data for your geographical
        location. You need to know your longitude and latitude. See the
        borders of a local road map for data, or perhaps the weather
        section of your local newspaper, or Section 5 of this file.
        
        When you start SUNPO you will be greeted by a more or less blank
        screen. There is no "cursor". There is a standard menu bar at the
        top of the screen. The menu choices are as follows:
        
        File  Control Data  Run  Sunrise  Reset Graph  Help


        3.1 The "File" Menu Item
        
        Clicking on the "File" option brings up a popup menu composed of
        four items: "New", "SaveAs", "Print" and "Exit".

        Selecting "New" simply clears any previous results from the screen
        and memory and resets some in ternal flags.

        The File "SaveAs" option is chosen to initiate saving of the
        current results into an ascii file. It works pretty much as you
        might expect.

        The "Print" option will dump the currently displayed numerical
        results to the DEFAULT Windows printer. THE PRINTER MUST HAVE
        GRAPHICS CAPABILITIES! If it doesn't, you may get a lot of blank
        sheets of paper!. You must handle all printer setup operations
        via the Windows Print Manager.

        The "Exit" option terminates SUNPO.

        3.2 The "Control Data" Menu Item
        
        This item also brings up a popup menu with three sub-choices:
        "Observer Position", "Time of Day" and "Atmospheric model".

        If you have not copied the SUNPO.INI file to your Windows directory
        you should click on the "Observer Position" choice and enter your
        geographical data, and a time zone value in the spots provided.
        (See section 2.1.2 B (above) for a few comments on time zones, and
        Section 5.0 (below) for sample data.)

        If you have made a change in the observer position or time zone
        data, then when you exit from  the dialog via the "Ok" button you
        will be asked if you wish to save the changes in the SUNPO.INI
        file. If you answer "yes" then all the file data will be replaced.

        You will need to execute the "Time of Day" dialog to set the month
        and day of the month for which you want solar position data. Within
        that dialog you also set the hours for the first and last times of
        day and the increment in minutes for the calculations. All the
        input numbers are expected to be integers with no  decimals, etc.
        Some, but not all, parameters are checked before a run, so if you
        enter any oddball values (like ~23, for example), all bets are off.





        You may also select one of five atmospheric models. The five models
        are the US Air Force Geophysics Laboratory's tropical, midlatitude
        summer, midlatitude winter, subarctic summer and subarctic winter
        models.


        3.3 The "Run" Menu Item
        
        Choosing the "Run" menu item is the action which actually causes
        something to happen to produce data to be displayed in the blank
        window. There will probably be something of a delay before you
        see any results because SUNPO does all calculations before it
        displays any results.


        3.4 The "Sunrise" Menu Item
        
        This item initiates iterative calculations which attempt to find
        the APPROXIMATE times at which the sun crosses the horizon (or
        for which the elevation angle is zero). These calculations may
        also take a while if you do not have a fast computer. Those times
        and the approximate solar azimuth at those times are then shown in
        a popup window. The results are nominal "astronomical" values and
        are not corrected for refractive atmospheric effects or topography.
        Refractive effects advance sunrise and delay sunset by about three
        minutes or so (roughly one solar diameter).

        3.5 The "Reset" Menu Item
        
        Choosing the "Reset" menu item erases the "worksheet" and prepares
        some internal flags for "new" calculations. "Reset" does not, 
        however, alter the observer or time of day data. "Reset" performs
        the same actions as the "File New" choice (see above).


        3.6 The "Graph" Menu Item

        Select this item by mouse click or Alt+G to get simple graphs of
        elevation and azimuth angles (in degrees) or visible and UV-A solar
        intensities (watts per square meter per streadian) vs local time
        (hours). Use the popup menu to select the desired type of graph.
        Negative elevation angles will not appear on the graph. Instead of
        using the 0 to 360 degree range, azimuth angles are shifted into
        the - 180 to + 180 range. After shifting, an azimuth angle of 0 is
        still North and + 90 is still East, but West becomes - 90. Both
        -180 and +180 mean due south.

        Use the Alt + Spacebar keys and then select the CLOSE popup menu
        item to close the graph window if you don't havå a mouse.





        3.7 The "Help" Menu Item
        
        This choice brings up another popup menu from which you can select
        the display of a few terse descriptions of various SUNPO related
        items. It does not (as yet) bring up a full-fledged Windows style
        help window.


        3.8 Last But Not Least
        
        You can begin execution of SUNPO132.EXE by clicking the Windows
        Program Manager's "File" menu item and then the "Run" item from
        the popup menu. Then you simply enter the complete path name needed
        to locate SUNPO132.EXE. If you placed SUNPO132.EXE in your base
        Windows directory you can omit the directory portion of the file
        name. SUNPO has no command line parameters.

        If you added SUNPO132 to a program group, then just start it in the
        usual fashion.



       *********************** WARNING No. 2 ******************************
       *                                                                  *
       * SUNPO132 REQUIRES A COMPUTER WITH AN 80286 CPU OR LATER PLUS     *
       * AN 80X87 MATH COPROCESSOR. IT WILL NOT RUN IN THE WINDOWS REAL   *
       * MODE. IT HAS BEEN TESTED ON A 16-MHZ ZENITH 80386 MACHINE, A     *
       * 16 MHZ IBM PS/2 MODEL 70, AND A GATEWAY 80486 33 MHZ machine.    *
       *                                                                  *
       * BUT YOU MUST UNDERSTAND THAT YOU USE SUNPO132 AND SUNPOD12       *
       * ENTIRELY AT YOUR OWN RISK. THE DEVELOPER OFFERS NO WARRANTIES    *
       * AND EXPRESSLY DISCLAIMS LIABILITY FOR DAMAGE TO YOUR HARDWARE    *
       * OR SOFTWARE OR TO ANY CONCURRENTLY EXECUTING PROGRAMS OR DATA,   *
       * WHETHER IN ACTIVE MEMORY OR IN OR ON OTHER STORAGE MEDIA.        *
       *                                                                  *
       *********************** WARNING No. 2 ******************************




        4.0 OTHER IMPORTANT INFORMATION

        SUNPO is distributed as Shareware. If you use it after some
        reasonable trial period, please send the author $ 7.50 for his
        trouble. Its the right thing to do! That will also make you feel
        better and will get you on a mailing list for information about
        any fixup versions or future enhanced versions.  (Please send
        $ 7.50 if you want to receive a diskette containing files for the
        latest version - in which case also tell me the disk size needed).

        You may not incorporate SUNPO into any commercial package without
        express written approval of the author, but you may feel free to
        give away unmodified copies of the original files (all or none,
        however) or post copies on any BBS which will accept them AND which
        makes no charges other than those made on the basis of connect time.

        Send your $ 7.50 as well as any constructive comments or suggestions
        to:

        A. Miller
        P.O.Box 3512
        Las Cruces, NM 88003-3512

        (internet: amiller@nmsu.edu)


        IF YOU ENCOUNTER ANY "ABNORMAL" BEHAVIOR, PLEASE SEND AS MUCH
        INFORMATION ABOUT ITS NATURE AND CIRCUMSTANCES UNDER WHICH IT
        WAS OBSERVED TO AUTHOR.

                                * ADVERTISEMENT *

        There is now a MOONPO which provide low resolutino angular position
        data for both the moon and the sun as well as the phase of the moon.
        Look for MOONPO22.ZIP. The registration fee for MOONPO is $ 12.50
        (U.S.), or $ 15.00 if you want a directly shipped diskette. $ 20.00
        will get you a diskette containing both the latest SUNPO and MOONPO
        files. MOONPO does not provide intensity data.

                                * ADVERTISEMENT *





        5.0 MISCELLANEOUS INFORMATION 

        In case you don't know where you are, here are a few clues:

                            Latitude       Longitude      TimeZone
                            -------------  ------------   --------
        Atlanta, GA         33D 21M North   84D 22M West     - 5
        Boston, MA          41D 21M North   71D  3M West     - 5
        Chicago, IL         41D 52M North   87D 37M West     - 6
        Dallas, TX          32D 47M North   96D 47M West     - 6
        Denver, CO          39D 44M North  104D 59M West     - 7
        El Paso, TX         31D 45M North  106D 29M West     - 7
        Fairbanks, AK       64D 48M North  147D 51M West     - 9
        Las Cruces, NM      32D 19M North  106D 47M West     - 7
        Los Angeles,CA      34D  3M North  118D 14M West     - 8
        New Orleans, LA     29D 56M North   90D  3M West     - 6
        Phoenix, AZ         33D 26M North  112D  3M West     - 7
        San Francisco, CA   37D 47M North  122D 25M West     - 8
        Seattle, WA         47D 37M North  122D 19M West     - 8

        London              51D 32M North    0D  4M West       0
        Hamburg             53D 33m North   10D  2M East     + 1
        Capetown            33D 55M South   18D 22M East     + 2
        Guayaquil            2D 10M South   79D 56M West     - 5
        Irkutsk             52D 30M North  104D 19M East     + 7
        Bangkok             13D 45M North  100D 30M East     + 7
        Manila              14D 34M North  120D 56M East     + 9 (I think)
        Mexico City         19D 26M North   99D  7M West     - 6
        Rio de Janeiro      22D 56M South   43D 11M West     - 3
        Tokyo               35D 45M North  139D 45M East    + 10

        wherein, "D" means degrees and "M" means minutes. Some of time zone
        values are based on longitude alone. They may be off by an hour or
        so either way in a few cases due to the author's ignorance of local
        customs.

       



        6.0 DISPLAY INFORMATION

        For an observer located as in the sample SUNPO.INI file, the screen
        display and the ascii output files look something like:

           Local Global  Solar  Solar  Visible   UV-A    UV-B  Observ.
            time   time  Azim.  Elev.  Intens. Intens. Intens. Params.
                                                                      
             600    600     65     -8        0     0.0   0.000  21 Jun
             700    700     67      5        8     0.0   0.000   8.1 N
             800    800     68     19      133     3.6   0.009  12.6 W
             900    900     67     33      226    12.5   0.109  Trop. 
            1000   1000     64     46      279    20.4   0.313        
            1100   1100     57     59      309    25.8   0.526        
            1200   1200     37     70      324    28.7   0.671        
            1300   1300    353     75      327    29.5   0.711        
            1400   1400    315     68      321    28.1   0.639        
            1500   1500    300     56      302    24.5   0.470        
            1600   1600    294     43      267    18.4   0.251        
            1700   1700    292     29      205     9.9   0.068        
            1800   1800    292     15       96     1.7   0.002        
            1900   1900    293      1        0     0.0   0.000        
            2000   2000    296    -12        0     0.0   0.000        
                                                                      


        REMARKS:
        
        The 353 degree azimuth value means that the sun appeared north of
        the observer at some time close to 1300 hrs. The negative eleva-
        tion values indicate that sunrise occurs between 6 AM and 7 AM
        local standard time and that sunset occurs just after 7 PM local
        standard time.        





        7.0  COMPARISON OF SUNPO ANOTHER PROGRAM:

        Date: 2 Feb 1995
        Observer position: 32.32N, 106.78W

                    Azimuths                   Elevations
                  -------------              --------------
         GMT      Sunpo  ILLUM               SunPo   ILLUM
                  -------------              --------------
           0       245    244.8                 7       6.8
         200       261    260.4               -17     -17.3
         400       277    276.3               -42     -42.6
         600       305    305.6               -66     -66.4
         800        32     33.0               -72     -72.2
        1000        76     76.7               -51     -50.8
        1200        94     95.5               -26     -25.6
        1400       109    109.6                -1      -0.8
        1600       128    128.1                21      21.4
        1800       155    155.8                37      37.2
        2000       192    192.6                40      39.9
        2200       224    224.1                28      27.7
           
           
        Program ILLUM is a high precision program written by Ir. AC
        van Bochove. Its results have been rounded to the nearest
        tenth of a degree. SUNPO results are rounded (internally) to
        the nearest degree.

        Thus, SUNPO's results generally agree with those of ILLUM to
        within one degree or better.











        8.0 WHO DID WHAT ?


        SUNPO calculates "astronomical" position data using approximate
        equations for declination and the equation of time. No corrections
        for refractive effects are included in the SUNPO results.


        The numerical algorithms utilized in SUNPO are based on the low
        precision solar position formulae found in the 1993 edition of the
        Astronomical Almamac (US Naval Observatory).

        The code for this Windows-based program consists of about 4000 lines
        of "interfacing" code. Only about 200 lines are used for the
        actual solar position calculations. The interface code was mostly
        written by SUNPO's developer (me), but many basic techniques were
        based closely on the manuals and sample programs which were supplied
        with the Turbo Pascal for Windows software.


        Solar intensity values for the various atmospheric models were found
        using the AFGL program LOWTRAN 6C. Calculations were made at each
        of 14 solar elevation angles for each of the five atmospheric
        models. The results were tabulated and placed in the data file
        SUNPO.DTA. That file actually contains calculated radiance values
        in units of watts per (square centimeter-steradian). SUNPO converts
        them to watts per (square meter-streradian). The final intensity
        units are then watts per square meter per steradian. Results
        are provided for visible (0.38 to 0.7 micrometer wavelengths), uv-a
        (0.315 to 0.38 um range) and uv-b (0.28 to 0.315 um). A three point
        gaussian interpolation routine is used to estimate intensity values
        at untabulated solar elevation angles. The tabulation angles were
        0, 2, 5, 10, 15, 20, 30, 40, 50, 50, 60, 70, 75, 80, 85, 90 degrees.
        These intensities represent values seen looking directly at the sun,
        but do not contain corrections for any aerosol scattering into that
        direction from other portions of the sky. They were found using the
        IEMSCT = 3 setting in LOWTRAN 6.



        Graphics drawing and printing are done using Version 2.1 of
        the Graphics Server SDK marketed by Pinnacle Publishing, Inc.


        9.0 NOTICES

        Microsoft Windows and MS-DOS are products of Microsoft Corporation.
        Turbo Pascal for WIndows is a product of Borland International.
        GSW.EXE and GSWDLL.DLL are products of Pinnacle Publishing, Inc.
        OS/2 2.x are products of IBM.





        10.0 SPECIAL NOTE TO IBM OS/2-2.X USERS:

        If you operate in under IBM OS/2 Version 2.x, your "base windows
        directory" will likely have a name like C:\OS2\MDOS\WINOS2. There
        is where you should put the files to which the installation hints
        say should be placed in the "base windows directory".

        If you sometimes boot MS or IBM DOS and then run Microsoft Windows
        3.x you may need to put copies of some files in both your Win OS/2
        and Windows 3.1 base directories. SUNPO.INI and SUNPO.DTA are small
        and two copies won't cause much grief, but the GSW.EXE and
        GSWDLL.DLL files are fairly big. So, to save space, see if you can
        put them in a directory that appears on both your normal DOS path
        and on the path used for OS/2.The author actually puts them in
        a separate directory named C:\GSW and adds "C:\GSW" to the end of
        the PATH statement in both his DOS and OS/2 AUTOEXEC.BAT files.


        11.0 MISCELLANEOUS

        Details of the various atmospheric models may be found in the
        document "Optical Properties of the Atmosphere", by R. A.
        McClatchey, et al, AFCRL-72-0497, Air Force Cambridge Research
        Laboratories (currently named Air Force Geophysics Laboratory),
        L. G. Hanscomb Field, Bedford, MA, 24 August 1972.

        For information on computer program LOWTRAN 6C, see:
        "Atmospheric Transmittance/Radiance: Computer Code LOWTRAN 6",
        by F. X. Kneizys, et al, AFGL-TR-83-0187, Air Force Geophysics
        Laboratory, Hanscomb AFB, MA 01731, 1 August 1983.

        Terminology for the strength of radiation from an extended soure
        such as the sun or sky is not consistent in technical literature.
        In this document the term "intensity" has been used where the
        term "irradiance" is used in the LOWTRAN printouts. However, the
        LOWTRAN outputs still carry the "per steradian" (per unit solid
        angle) tag - a usage differing from that of many other papers.
        More meaningful results might be obtained if one could remove the
        per steradian units via an integration over solid angle. That
        is easily done in the case of an isotropic or Lambertian radiator,
        but the beam from the sun isn't handled that easily. For the
        purpose of just getting an idea of how the solar elevation angle
        affects the relative levels of visible and UV radiation, the units
        do not really matter except when comparing them with those of other
        models. So, if you really want to know, the SUNPO intensities are
        "power per unit area per unit solid angle". Assign whatever term
        you like (radiance, irradiance or intensity) to the results. Note,
        however, that the SUNPO results HAVE been integrated over
        wavelength.