Before installing this Model # 23013 / 23063 ES1868 Cost Saver 3D Sound Card, please read this manual carefully and retain it for future reference.

Trademark Acknowledgments:

IBM is a trademark of International Business Machines Corporation.

Sound Blaster PRO and Sound blaster are trademarks of Creative lab Inc.

MS-DOS and WINDOWS are trademarks of Microsoft Corporation.

ESS, AudioDrive and AudioRack are trademarks of ESS Technology Inc.

Yamaha OPL3 is a trademark of Yamaha Corporation.

Mitsumi is a trademark of Mitsumi Corporation.

Sony is a trademark of Sony Corporation.

Panasonic is a trademark of Panasonic Corporation.

1. Introduction

The Model # 23013 / 23063 ESS ES1868 Cost Saver 3D Sound Card is a 16-bit Full Duplex sound card based on the ESS integrated digital sound controller chip which is compatible with Sound Blaster PRO.  This sound card provides an integrated audio solution for business audio, education/entertainment, and multimedia applications.

The ESS ES1868 Sound Card will let you run thousands of Sound Blaster and Sound Blaster PRO compatible games and applications, including a rapidly growing number of Windows business applications that are compatible with the Windows Sound System.

Included with full support for these PC popular sound standards, the ESS ES1868 includes multiple audio cable interface for SONY, Mitsumi and Panasonic CD-ROM drives. Also, it has multiple input and output ports for recording and playback of stereo sound.

1.1 The ESS ES1868 Cost Saver 3D Sound Card Features

The ESS ES1868 is a fully featured sound card which includes the following :

16 bit full duplex stereo sound

Record, compress and playback voice, sound and music simultaneously

Integrated 16-bit A/D and D/A converters

Supports on board 3D Sound Effect (Model # 23063 only)

ADPCM as well as patented ESPCM compression for lower bit rates

Maximum sampling rate up to 44.1KHz for recording and playback

6 channel mixer

Software volume control for both record and playback (64 steps)

Built in 2 watts per channel stereo power amplifier

Connector for mic in, line in, line out, speaker out and wave table connector

Game port for joystick or MIDI device

Plug and Play Features

1.2  What is in your package ?

You should have the following items in your package :

Model # 23013 or 23063 ESS ES1868 Cost Saver Sound Card

MMCD CD-ROM with installation drivers, software utilities and manuals

Hardware Installation, product layout & troubleshooting manual

1.3  System Requirements

The ESS ES1868 Sound Card is manufactured for IBM PC compatible components, software and related computer components :

IBM-compatible computer models and compatibles with PnP BIOS

At least 2MB RAM (4MB RAM for Windows 3.1 Applications)

VGA or SVGA graphics adapter and monitor

2MB free on hard disk for installing all ESS ES1868 software

MS DOS version 3.3 or later

Windows 3.1 for games and applications in Windows

External speakers, microphone and headphones (optional)

1.4   Layout of ESS1868 Cost Saver 3D Sound Card

JP6		J4 WAVETABLE          GSGS	 SGGS	 	          MIC IN	   P1

LINE IN  	   P2

JP1             	         SPK OUT	   P3

JP2

ESS1868						GAME PORT

1.5    Jumpers and Connectors Description

JP1 & JP2 : On Board amplifier and Speaker Out / Line Out settings

1-2 = Enable on board amplifier

This directs the signal through the on board amplifier to turn P3 connector in to a speaker out.  This on board amplifier will also drive non-powered speakers .

Pin #    3     2     1

JP1

JP2

2-3 = Disable on board amplifier

This disables the onboard amplifier and directs the signal to the P3 connector to act as a LINE OUT,  where you can connect a cable to your home HI-FI or external amplifier.

Pin #    3     2     1

JP1

JP2

Note :    i) The factory default setting is 1-2

ii) Uses 1-2 setting - when connect the sound card to normal computer speakers

iii) Uses 2-3 setting - when connect the sound card to self-power devices

(e.g. Hi-Fi system, amplifier)

JP6 : Speaker In settings

The ESS1868 chipset has a unique feature whereby you can connect the cable from your motherboard here (this cable would usually connect to the system case internal speaker), and any system ‘beeps’ or sound messages can be routed through this sound card to the speakers or amplifier connected to P3.

GSGS / SGGS : CDROM to Sound Card Audio Cable connections

This card has audio connectors for Panasonic, Sony & Mitsumi standard Audio Cables...

Panasonic					= 	connect to GSGS

Sony						=	connect to SGGS

Mitsumi (reverse cable on Panasonic)		=	connect (reverse) to GSGS

2.0	Software Driver Installation

2.1  DOS Driver Installation

Go to the MSDOS prompt

Insert the MMCD in to your CD-ROM drive. Log onto that drive, and change directories to go to the directory  app\product\2\ess1868\dos\  Then type   setup

The DOS driver installation program will appear.

Use the arrow keys to move the pointer “[          ]” to the parameter which you want to select and then press the “RETURN” or “SPACE” key to confirm the new setting.

If there is more than one parameter you want to change, please repeat the procedure #3 to make all the changing

After you have finished the changing, press the “ESC” key to leave the installation program. The system will prompt you a “Make changes to CONFIG.SYS and AUTOEXEC.BAT (Y/N)?” at this time, you must press the “Y” key to confirm the system update, otherwise the installation program will not install the Sound Card DOS driver for you.

Reboot your computer system.

Note : If you use both of the DOS and MS Windows 3.1, you should skip the installation of the DOS driver of the Sound Card. Instead, you only need to install the Sound Card Window 3.1 driver which will work for both the DOS and Windows environment simultaneously.

DMA - direct Memory Access (DMA) is the electronic channel for moving data directly between main storage and peripheral equipment without requiring processing of the data by the CPU.

IRQ - Interrupt request (IRQ) is the request for processing on a particular priority level. It is generated by the I/O device (the add-on cards).

Port address - is the address used to specify port connectivity parameters and to assign link addresses for the certain I/O device.

2.2 	Windows 3.1 Driver Installation

After running the MMCD program, go to the ESS1868 Cost Saver 3D page and click on the button named Windows 3.1x driver under the ‘Install’ Section on the screen.  This will automatically load the Windows 3.1 driver installation program.

When the Sound Card Windows 3.1 driver installation program appears, click “Continue”  and then “Driver Installation” button to start the installation.

After that, you can modify the setting to what you want under the “Hardware Setting” dialog box shown below. Click the “OK” button when you finish the modification.

Then, click the “Reboot System” button to proceed.

Make sure that all floppy disk has been removed from the floppy disk drive then click the “OK” button, the Windows system will be updated automatically.

2.23 	WINNT 3.51 Driver Installation

After entering WINNT (Version 3.51 or higher). Double click on the “Main” ( “Control Panel” ( “Drivers” icons.

Click the “Add...” button

Select the “Unlisted or Updated Driver” item, and click the “OK” button.

Insert the MMCD in to your CD-ROM drive and then type the letter of drive and app\product\2\ess1868\winnt35\     Then click the “OK” button. (Note : If you are using Windows NT Version 3.5 then the directory location of the driver will be named as ‘winnt35’.   If you are using Windows NT Version 4.0 the directory will be ‘winnt4’)

Click the “OK” button again.

Under the “ESS Base I/O Address” dialog box, click the “continue” button.

After that, you can modify the setting to what you want under the “ESS1868 Configuration” dialog box. Click the “OK” button when you finish the modification.

For the new driver to take effect, you should click the “Restart Now” button.

2.24 	Windows 95 Driver Installation

Note : Install the Sound Card into the motherboard only after the Windows ‘95 has already  installed into the new HDD of the new system, then restart the system and follow the procedure below..

Install the Sound Card on the motherboard, and power on the system.

During the Windows 95 boot procedure, new hardware will be detected as shown below.

Select the “Driver from disk provided by hardware manufacture” item, and click the “OK” button.

Windows 95 will then prompt a “Install From Disk” dialog box.

With the MMCD already loaded into your CD-ROM drive,  type the letter of your CD-ROM drive followed by app\product\2\ess1868\win95\ , then click “OK” button to install the relevant Windows 95 driver.

After that, the “New Hardware Found” dialog box window will appear for gameport joystick.

Select the “Windows default driver” item, and click the “OK” button to complete the installation of the game port driver.

In the same way, you can achieve the installation of the Standard IDE/ESDI Hard Disk Controller.

Finally, Windows 95 will ask if you want to restart system for the new driver to take effect, you should click the “YES” button.