Trademark Acknowledgments:

OPTI is a trademark of OPTI Incorporation.

IBM is a trademark of International Business Machines Corporation.

Sound Blaster PRO and Sound Blaster are trademarks of Creative Lab Inc.

MS-DOS and WINDOWS are trademarks of Microsoft Corporation.

1. Introduction

This Model # 2321 OPTI 931 &  Model # 2326 OPTI 931+3D Audio Controller is a 16-bit Full Duplex sound card based on the OPTi 82C931 Full Duplex Plug-n-Play Integrated Audio Controller Chip.

The OPTI Sound Card is available in two versions. The standard version Model # 2321 OPTI 931 is a 16-bit Full Duplex sound card whereas the Model # 2326 OPTI 931+3D comes with a built-in ‘3D’ features which is always enable. It adds hardware and software 3D sound effect to any audio signal, whether it is from an audio CD, MIDI or Wave file.

The OPTI 931/OPTI 931+3D Sound Card will let you run thousands of Sound Blaster and Sound Blaster PRO compatible games and applications, including a rapidly growing number of Windows business applications that are compatible with the Windows Sound System.

Included with full support for these PC popular sound standards, the OPTI 931/OPTI 931+3D includes audio cable interface for CD-ROM drives. Also, it has multiple input and output ports for recording and playback of stereo sound.

1.1 The OPTI 931/OPTI 931+3D Sound Card Features

The OPTI 931/OPTI 931+3D is a fully featured sound card which includes the following :

16 bit full duplex plug & play stereo sound

22 voice 52 operators FM Music Synthesizer

Integrated 16-bit A/D and D/A converters

Maximum sampling rate up to 48KHz for stereo recording and playback

7 channel mixer - 5 stereo & 2 mono

Software volume control for both record and playback

Built in 2 watts per channel stereo power amplifier

Connector for Mic in, Line in, Line out/ Speaker out, Wavetable & ATAPI IDE Interface

Game port for joystick or MIDI device

Plug and Play Features 1.0a

Optional built-in ‘3D’ features (Model # 2326 only)

1.2  What is in your package ?

You should have the following items in your package :

Model # 2321  OPTI 931  or   Model # 2326  OPTI 931+3D Sound Card

MMCD CD-ROM containing all drivers, utilities and manuals

Hardware Installation, product layout & troubleshooting manual

2.  Installation

Wavetable

Connector          CD-In      MPEG-In

MIC In

J3           J4        AJ4

J2					             Line In

AJ3

JP2	     1

JP3         1

AJ2			Speaker Out /

OPTI 931						      Line Out

IDE	           1

Connector      J1						   J5

Game Port

Layout of OPTI 931 (OPTI 931+3D) Sound Card

Jumpers and Connectors Description

| J1 | IDE Connector (set default as disable; can enable by software) |
| --- | --- |
| J2 | Wavetable Connector |
| J3 | CD-ROM Drive Audio Cable Connector |
| J4 | MPEG-IN |
| J5 | Game Port Connector |
| AJ2 | Speaker Out/ Line Out Connector |
| AJ3 | Line In Connector |
| AJ4 | MIC In Connector |

JP2 & JP3 :

2-3 = Enable on board amplifier	(AJ2 = SPEAKER OUT Connector)

1-2 = Disable on board amplifier	(AJ2 = LINE OUT Connector)

Note :    i) The factory default setting is 2-3

ii) Uses 2-3 setting - when connect the sound card to normal computer speakers

iii) Uses 1-2 setting - when connect the sound card to self-power devices

(e.g. Hi-Fi system, amplifier)

2.1  Hardware Installation

Note that if your system is not PnP compatible, the default configuration is as follows:

| Operation Mode | Sound Blaster Pro Compatible |
| --- | --- |
| IRQ | 5 |
| DMA Channel | 1 |
| I/O Port Address | 220h |
| CD-ROM Interface | None |

2.2  Software Driver Installation

2.21  DOS & Windows 3.1 Driver Installation

Insert the MMCD in to your CD-ROM drive and run the MMCD program. Go to the Opti931 page and click on the Windows 3.1x Driver button under the ‘Install’ section.  The driver will load automatically.

The driver installation program will appear.

Click on the ‘NEXT’ button to begin installation.

You will be prompted to select a drive and directory. The default is C:\ OPTI931.

Press ‘NEXT’ , the installation program will begin.

When the files are copied, reboot your computer system and Driver Installation is completed.

Note : If your system does not support Plug & Play, you will have to make your configuration settings under the ‘Configuration & Sound-Test’ menu. But if your system supports the Plug & Play 1.0a specification, most of these settings will not be user selectable.

2.22 	Windows 95 Driver Installation

Note : Install the Sound Card into the motherboard only after the Windows ‘95 has already  installed into the new HDD of the new system, then restart the system and follow the procedure below..

Install the Sound Card on the motherboard, and power on the system.

Windows ‘95 will automatically detect the sound card.

Select the “Driver from disk provided by hardware manufacture”  and, with the MMCD already loaded into your CD-ROM drive -  direct Windows to the location of the Windows ’95 driver - D:\app\product\3\win3195\   (‘D’ represents the letter for your CD-ROM drive - change as necessary)

This will complete the Windows ‘95 installation.