ZeppeLAN (tm) User's Guide
        
        Chapter 1. Introduction
        
        ZeppeLAN (ZEP) is a program that allows a NetWare user to manage
        certain parts of the NetWare local area network (LAN) environment
        with less trouble than is usually required with the NetWare
        utility programs.
        
        You can run ZEP in one of two ways: as a memory-resident popup
        program or from the DOS command line. Both modes are functionally the
        same. The memory-resident mode is available from within other
        applications when you press a hot key. To run the command-line
        version, you must exit your application or shell out to the DOS
        prompt from within the application you are running. As an
        alternative, you can install the command-line ZEP program in a
        Windows or DesqView window or as a swapped task under the DOS 5
        DOSSHELL program's task swapper.
        
        The shareware version of ZEP, which this document describes, includes
        several work station desktop applications, including shared printer
        selection, a telephone dialer, logging on and off the network, and
        sending one-line messages to other logged-on users or groups. Each of
        these processes is described fully in the chapters that follow.
        
        The commercial version of ZEP, which you get when you register the
        shareware version, adds support for multiple file servers, allows you
        to capture the output of all your printer ports, and includes
        electronic memos between network users and on-line mapping of network
        drives to network directories.
        
        Following is a description of the differences between the commercial
        and shareware versions.
        
        1. The memory-resident mode of the shareware version is fully memory
        resident and occupies about 50K of conventional DOS memory. The
        commercial version swaps most of the program to expanded or extended
        memory or to a swap disk file. The memory-resident part occupies only
        about 5K of conventional DOS memory.
        
        2. The commercial version of ZEP works with multiple file servers in
        a LAN. The shareware version works only with a work station's primary
        file server.
        
        3. The commercial version allows you to concurrently capture the
        output from LPT1, LPT2, and LPT3 to selected network print queues
        across file servers. The shareware version captures LPT1 only to
        print queues on the work station's primary file server.
        
        4. The commercial version allows you to select a Print Configuration
        that you define with NetWare's PRINTCON program. The shareware
        version does not give you access to Print Configurations.
        
        5. The commercial version includes the ZEP Electronic Memo feature
        that allows you to exchange memos with other users on the network.
        The shareware version does not include this feature.

        ZeppeLAN User's Guide                                      Page 2
        
        
        
        6. The commercial version allows you to log in and out of file
        servers on the network from within the program. The shareware version
        does not.
        
        7. The commercial version allows you to map network drives to network
        directories from within the program. The shareware version does not.
        
        8. The shareware version includes an on-line product registration
        form that you can fill out and print from within the program. The
        commercial version does not include this form since it assumes that
        you are already registered.
        
        9. The commercial version includes a printed copy of the user's
        manual, upgrades to new versions for a reduced cost, and telephone
        technical support.
        

        ZeppeLAN User's Guide                                      Page 3
        
        
        Chapter 2. Installation
        
        This chapter is about the installation of ZEP onto a network.
        Usually, the Network Administrator or SUPERVISOR user will install
        the program files on the network file server. Users may install their
        own configurations by using command line options when they load or
        run the program. As an alternative, a work station user can install a
        private copy of the programs. ZEP does not need to be installed on
        the file server.
        
        2.1 System Requirements
        
        To run ZEP, you must have NetWare version 2.15 or greater, DOS
        version 3.0 or greater, and at least 70K available in your
        workstation's conventional memory if you are going to load ZEP as a
        memory-resident program. Note that the commercial version, which you
        get when you register, requires only 5K.
        
        2.2 Files in the ZEP Distribution
        
        Whether you downloaded ZEP from an on-line service or bulletin board
        service or purchased it from a shareware diskette vendor, you will
        have these files:
        
            ZEP.EXE        The load module for the memory-resident program.
            ZEPLAN.EXE     The command line program and the transient part of
                           the memory-resident program.
            ZEP.HLP        The Help database.
            HOTKEY.EXE     A program to help you determine hot key scan codes
                           and shift masks to customize the hot key with a 
                           command-line option.
            ZEP.DOC        This documentation file.
        
        2.2 Installing the ZEP Software
        
        1. Log onto a file server as the SUPERVISOR user or a user with
        SUPERVISOR privileges.
        
        2. Copy the files ZEP.EXE, ZEPLAN.EXE, ZEP.HLP, and HOTKEY.EXE into a
        publicly available subdirectory on the file server. Add a search path
        to the subdirectory in the NetWare System Login Script so that
        everyone can find and load the software into their work stations. The
        simplest way to install ZEP is to copy the files into the SYS:\PUBLIC
        subdirectory.
        
        3. Set up the NetWare print queues with the NetWare PCONSOLE utility
        program. When you associate print queues with printers, name the
        queues with names that are meaningful to the users. The users will
        see these print queue names when they select a printer to which they
        want to direct the print output from their applications programs.
        
        4. The HOTKEY.EXE program is a utility program that displays the ZEP
        command-line option for selected hot keys. If a user wants to change
        the ZEP hot key, this program will help. The instructions for running
        it are here. Enter its name, HOTKEY, on the command line. The program
        will display this message:
        ZeppeLAN User's Guide                                      Page 4
        
        
        
            Hot Key Code Computation (Enter for hot key codes.)
            Press Hot Key...
        
        Press different hot key combinations. As you do, the program will
        display the name of what you entered as shown in this message:
        
            Press Hot Key...Alt+LeftShift+N
        
        When you have pressed the hot key combination that you want and its
        name is displaying in the message just shown, press the Enter key.
        The program will display this message:
        
            Alt+LeftShift+N = BIOS Shift Mask: 0a, Keyboard Scan Code: 31
            Example command line:
            zep +h310a
        
        The example command line is the way you would run ZEP to change the
        command line to Alt+LeftShift+N. See Chapter 3 for a discussion of
        command line options.
        

        ZeppeLAN User's Guide                                      Page 5
        
        
        Chapter 3. Running ZEP
        
        You run ZEP either as a memory-resident program or as a normal DOS
        program from the command line. Both operating modes have command line
        options that follow the program's name on the command line.
        
        3.1 Command Line Options
        
        Following are the command line options for ZEP when you run it in
        either the memory-resident mode or as a DOS program from the command
        line. A command line option consists of plus (+) or minus (-)
        followed by a letter, which may be upper or lower case. Some options
        have more information after the letter.
        
            +c1 or +c2 - Set the Dialer Communications Port
        
        This option sets the Dialer's communication port to COM1 or COM2. Use
        C1 for COM1 and C2 for COM2. This communications port is the port to
        which your modem is connected. C1 is the default.
        
            +m  - Use monochrome display
        
        This option tells ZEP to use monochrome (black and white) screens
        instead of color screens. You would use this option if you have a
        monochrome display monitor attached to a color card and the resulting
        screens are difficult to read or unattractive. Some laptop screens
        are easier to view with this option. ZEP will use this option
        automatically if you have a Monochrome Display Adaptor in your
        computer.
        
        
        The next option applies to ZEP's memory-resident mode only.
        
            +h  - Set the Hot Key
        
        This option sets the ZEP hot key, the key combination that you press
        to pop up ZEP. You would use this option if the default hot key,
        Alt+LeftShift+P, interferes with keys used by other programs that you
        run. You enter a two-digit keyboard scan code followed by a two-digit
        shift mask after the H on the command line. For example, to set the
        hot key to Alt+LeftShift+N, use this command line option:
        
            +h310a
        
        The scan code and shift mask values are hexadecimal, and the
        HOTKEY.EXE program described in Chapter 2 will tell you what its
        values can be.
        
        3.2 Loading Memory-resident ZEP
        
        You load ZEP into memory as a memory-resident program by entering its
        name on the command line like this:
        
            zep
        
        Follow the program name with any command line options you wish to
        ZeppeLAN User's Guide                                      Page 6
        
        
        make. For example, to load ZEP so that it uses COM2 for the Dialer,
        enter this command:
        
            zep +c2
        
        ZEP displays this screen when you load it.
        
           ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
           º ZeppeLAN Version 1.0 (Shareware)                           º
           º Copyright (c) 1992 Contact Plus Corp. All Rights Reserved  º
           º Hot Key = [Alt+LeftShift+P], Help = [F1]                   º
           º NOTE: UNREGISTERED COPY. SELECT Register ON THE MAIN MENU. º
           ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼
             You have used the unregistered ZeppeLAN 4 times
        
        The message at the bottom of the display tells you how many times you
        have used the shareware version. It is a reminder that you should
        register the program and get the commercial version.
        
        3.3 Popping Up ZEP
        
        After you have loaded ZEP into memory, you may pop it up onto the
        screen at any time as long as whatever you are running is not a
        graphics program. To pop it up, press the hot key. ZEP pops up this
        menu.
        
                                    ÉÍÍÍÍÍÍÍÍÍÍÍ»
                                    º Main Menu º
                                    ÌÍÍÍÍÍÍÍÍÍÍÍ¹
                                    º ³Printing º
                                    º ³Users    º
                                    º ³Dialer   º
                                    º ³Register º
                                    º ³Unload   º
                                    ÈÍÍÍÍÍÍÍÍÍÍÍ¼
        
        You can move the cursor bar up and down the menu with the up and down
        arrow keys. Press Enter to select one of ZEP's commands. You can move
        the cursor to a command by typing the first letter of the command.
        
        3.4 Popping Down
        
        To return to the program that you interrupted to run ZEP, press the
        Esc key while the Main Menu is being displayed.
        
        3.5 Unloading ZEP
        
        To unload ZEP from memory, select the Unload command on the Main
        Menu. Use this command only when you have popped ZEP up from the DOS
        command line and when no other memory-resident programs are resident
        above ZEP. If another program is running or resident above ZEP, ZEP
        cannot unload itself and will display an error message to that
        effect. A memory-resident program is above ZEP if you loaded it after
        you loaded ZEP.
        
        
        ZeppeLAN User's Guide                                      Page 7
        
        
        3.6 Running ZEP from the DOS Command Line
        
        If you do not want to keep ZEP resident in memory, you can run it as
        a DOS command line program. Its operation is the same as when it is
        memory resident except that you will not see the Unload command on
        the Main Menu. To run ZEP from the command line, enter this command:
        
            zeplan
        
        ZEP will take over the entire screen with a background display, and
        will display the Main Menu as shown above without the Unload command.
        When you press the Esc key from the Main Menu, ZEP will exit to the
        DOS command line. All of the changes that you made by using ZEP will
        still be in effect, however.
        

        ZeppeLAN User's Guide                                      Page 8
        
        
        Chapter 4. On-Line Help
        
        ZEP provides context-sensitive on-line help. Press F1 at any time
        during the operation of ZEP to see a window that displays what is
        going on. After you have read the help window, press any key to
        return to ZEP.
        

        ZeppeLAN User's Guide                                      Page 9
        
        
        Chapter 5. Printing
        
        ZEP's primary function is to allow you to select network printers. In
        the usual NetWare environment, you must select and de-select a
        network printer from the DOS command line by using the NetWare
        CAPTURE and ENDCAP commands. To use those commands, you must exit
        from your application. With ZEP, you can select a network printer by
        popping up ZEP and selecting the Printing command on the Main Menu.

        5.1 Selecting a Network Printer
        
        When you select the Printing command on the Main menu, ZEP displays
        the Printer menu, which looks like this.
        
                             ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
                             º      Printer Menu      º
                             ÌÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¹
                             º ³LPT Capture (off)     º
                             º ³End Capture           º
                             º ³View Print Job Queues º
                             ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼
        
        The shareware version of ZEP captures one printer port only, LPT1.
        The LPT Capture command indicates whether capturing to LPT1 is on or
        off. To start capturing or to change the capture to a different
        network printer, select the LPT Capture command on the Printer menu.
        You will see a list of network printers as shown here.
        
                    ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
                    º              Capture to LPT1              º
                    ÌÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¹
                    º ³LASERJET III                             º
                    º ³OKIDATA M92                              º
                    ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼
        
        The list shows all the network printers that are available for you to
        print to. Move the menu cursor to the printer you want to select and
        press Enter. ZEP will display the LPT Printer menu again with the
        (on) token shown next to the LPT Capture command.
        
        5.6 End Capture
        
        To end the capture of a printer port, select the End Capture command
        on the printer menu. The capture will stop.
        

        ZeppeLAN User's Guide                                      Page 10
        
        
         5.7 View Print Job Queues
        
        Use the View Print Job Queues command on the Printer menu to view the
        print jobs that are queued to each network printer. The command will
        display a list of the network printers like this:
        
                    ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
                    º             Print Job Queues              º
                    ÌÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¹
                    º ³LASERJET III                             º
                    º ³OKIDATA M92                              º
                    ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼       
        Move the menu cursor to a network printer entry and press Enter. ZEP
        will display the print jobs in the queue like this:
        
                ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
                º  Seq   Job User         Banner       Copies Size  º
                ÌÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¹
                º ³  1   336 ED           Daily Memos      1   287  º
                º ³  2   608 ED           Daily Memos      1 12166  º
                ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼
        
        The Seq field is the sequence assigned by NetWare to the print job
        and indicates the order in which the jobs are to be printed. The Job
        field is a job number assigned by NetWare.
        
        5.8 Deleting a Print Job
        
        To delete a print job from the network printer's print job queue,
        move the menu cursor to the print job and press the Del key. The job
        will be removed from the queue if you are the user who originated the
        job or if you are the Network Administrator or the assigned queue
        operator.
        

        ZeppeLAN User's Guide                                      Page 11
        
        
        Chapter 6. Dialer
        
        ZEP includes a telephone dialer program. Each user has a personal
        phone book with names and telephone numbers. You can add, change, and
        delete entries in the phone book. ZEP will dial the numbers through
        your modem.
        
        To run the dialer, select the Dialer command on the Main menu.
        
        6.1 Phone Book
        
        The Dialer command displays your personal phone book as shown here.
        
                              ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
                              º      Phone Book      º
                              ÌÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¹
                              º ³Bert Francis        º
                              º ³Charlie Bertini     º
                              º ³Donn Powless        º
                              º ³Ed Trujillo         º
                              º ³Fred Grundeman      º
                              º ³Howard Johnson      º
                              ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼
        
        If there are no entries in the phone book, the Dialer command will
        proceed to the procedure discussed in Adding an Entry below.
        
        To select a phone book entry for dialing or changing, move the menu
        cursor to the entry and press the Enter key. To add an entry to the
        phone book, press the Ins key.
        
        6.2 Adding an Entry
        
        When you add an entry to your phone book, ZEP displays a blank phone
        book entry form as shown here.
        
                          ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
                          º       Phone Book Entry        º
                          ÌÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¹
                          º   Name:                       º
                          º  Phone:                       º
                          º         (F2 to dial)          º
                          ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼
        
        Type a name into the Name field and a phone number into the Phone
        field. You can move between the fields by pressing Enter, Tab, or the
        arrow keys. When you are done, press Esc. ZEP will ask this question:
        
                                  ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
                                  º Add the entry º
                                  ÌÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¹
                                  º ³Yes          º
                                  º ³No           º
                                  ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼
        
        Select Yes to add the entry to the phone book. The Dialer will
        ZeppeLAN User's Guide                                      Page 12
        
        
        display another blank entry window so that you can add more entries
        to the phone book.
        
        6.3 Changing an Entry
        
        To change an entry in your phone book, select the entry in the Phone
        Book list window and press Enter. The Dialer will display the entry
        with its current values as shown here.
        
                          ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
                          º       Phone Book Entry        º
                          ÌÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¹
                          º   Name:  Bert Francis         º
                          º  Phone:  873-4123             º
                          º         (F2 to dial)          º
                          ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼
        
        Change the entry by moving between the fields and typing new values.
        When you are done, press Esc. ZEP will ask this question:
        
                                ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
                                º Change the entry º
                                ÌÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¹
                                º ³Yes             º
                                º ³No              º
                                ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼
        
        Select Yes to change the entry in the phone book.
        
        6.4 Deleting an Entry
        
        To delete an entry from your phone book, display the Phone Book list,
        move the menu cursor to the entry you want to delete, and press the
        Del key. The Dialer will ask you to confirm the delete by answering
        this question.
        
                               ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
                               º Delete Bert Francis º
                               ÌÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¹
                               º ³Yes                º
                               º ³No                 º
                               ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼
        
        Select Yes to delete the entry from the phone book.
        

        ZeppeLAN User's Guide                                      Page 13
        
        
        6.5 Dialing
        
        To dial a number from your phone book, select the entry in the Phone
        Book list window and press Enter. The Dialer will display the entry
        as shown here.
        
                          ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
                          º       Phone Book Entry        º
                          ÌÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¹
                          º   Name:  Bert Francis         º
                          º  Phone:  873-4123             º
                          º         (F2 to dial)          º
                          ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼
        
        Press the F2 key. The Dialer will begin dialing the phone number
        through your modem. While it is dialing, it will display this
        message:
        
                                  ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
                                  º Dialing...   º
                                  ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼
        
        When it is done dialing, the Dialer will display this message.
        
                           ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
                           º           Notice           º
                           ÌÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¹
                           º Pick up the phone and then º
                           º       Press any key        º
                           ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼
        
        Be sure to pick up the phone before you press a key. Pressing a key
        is your way of telling the dialer that you have the phone off the
        hook and it is OK for the dialer to hang up the modem. With the phone
        off the hook, the connection is not broken, and your call may
        proceed.
        

        ZeppeLAN User's Guide                                      Page 14
        
        
        Chapter 7. Users Command
        
        The Users command on the Main menu allows you to send one-line
        messages to other users and set your login password. When you select
        the Users command, you see a list of the users who are currently
        logged onto the network as shown here.
        
                    ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
                    º                   Users                   º
                    ÌÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¹
                    º ³Ed Watson (+)                            º
                    º ³John Martinez                            º
                    º ³SUPERVISOR                               º
                    ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼
        
        The entry with the (+) token is you. The (+) token indicates that
        you currently have messages enabled, which means that NetWare and
        other users can interrupt your processing with a one-line message at
        the bottom of the screen. If you did not have messages enabled, the
        token would be (-). See Enabling and Disabling Messages in this
        chapter.
        
        NetWare users have two names: their login userid and a so-called
        "full name." Your userid is a nickname that you use to log into the
        network. The Network Administrator assigns full names to login userid
        accounts with the NetWare SYSCON utility program. If you have a full
        name, ZEP uses it to display lists of users. If you do not have a
        full name, ZEP uses your login userid.
        
        7.2 Sending a Message to a User
        
        You can send a one-line message to a user from the Users list shown
        above. Move the menu cursor to one of the users other than yourself
        and press Enter. You will see this message entry window.
        
                     ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
                     º      Send Message to John Martinez      º
                     ÌÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¹
                     º                                         º
                     ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼
        
        Type a message into the window and press Enter to send the message or
        Esc to reject it. If the user has messages enabled or if the user's
        message buffer is full, you will get an error message to tell you
        that the message is not delivered.
        
        7.3 Enabling and Disabling Messages
        
        You can enable and disable one-line messages to yourself by using
        ZEP. You would do this when you do not want to be interrupted. Some
        programs, such as communications programs, should not be interrupted
        in the manner that the NetWare messages do it.
        
        Select one of your own entries from the Users list shown above. You
        will see the User menu shown here.
        
        ZeppeLAN User's Guide                                      Page 15
        
        
                               ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
                               º     User Menu      º
                               ÌÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¹
                               º ³Messages Enabled  º
                               º ³Change Password   º
                               ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼
        
        With the menu cursor on the first selection, press the Enter key to
        toggle between Messages Disabled and Messages Enabled. Press Esc when
        the command reflects the condition you want.
        
        7.4 Setting Your Login Password
        
        To set your login password, select the Change Password command from
        the User menu. You will see this entry window.
        
                  ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
                  º                 Old Password                  º
                  ÌÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¹
                  º                                               º
                  ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼
        
        Type your old password if you had one before this. Observe that all
        password entries echo to the screen as asterisks regardless of what
        you type. This is to prevent an onlooker from discovering your
        password when you enter it. ZEP will display this entry window.
        
                  ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
                  º                 New Password                  º
                  ÌÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¹
                  º                                               º
                  ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼
        
        Type the new password you want to use. If you want to remove the
        password completely, press the Enter key without entering a password.
        If you are entering a new password, ZEP will display this entry
        window. Its purpose is to assure that you made no keying errors and
        that the password is the one you want to establish.
        
                  ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
                  º             Enter Password Again              º
                  ÌÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¹
                  º                                               º
                  ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼
        
        Enter the password a second time. If the password is accepted, ZEP
        will return to the User menu. If it is not, you will get an error
        message.
        

        ZeppeLAN User's Guide                                      Page 16
        
        
        Chapter 8. Registration
        
        When you register your shareware copy of ZEP, you receive many
        benefits, including the commercial version of ZEP, printed user
        documentation, customer support on our support hot line, free
        upgrades for one year, and low-cost upgrades after that.
        
        Registration costs $95. Select the Register command on the Main menu.
        If you have used your shareware ZEP more than 30 times, ZEP
        automatically executes the Register command each time you load the
        program. This procedure does not mean that you cannot use the program
        without registering at that time or that you must complete the
        registration before using the program any more. Simply press Esc to
        go to the Main menu if you do not want to register right away.
        
        Eventually, however, you should register the program. That is what
        makes the shareware concept work. You can try out the program for a
        while. If it turns out to be useful to you, then and only then do you
        pay for it.
        
        The Register command displays the Registration form as shown here.
        
                ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
                º               ZEP Registration Form               º
                ÌÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¹
                º         Name:                                     º
                º      Company:                                     º
                º       Addr 1:                                     º
                º       Addr 2:                                     º
                º         City:                                     º
                º        State:                                     º
                º          Zip:                                     º
                º        Phone:                                     º
                º   MC/Visa No:                                     º
                º     Exp Date:                                     º
                º Diskette 3.5: [ ] (y/n)                           º
                º         5.25: [ ] (y/n)                           º
                ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼
        
        Move up and down the fields with the up and down arrow keys or the
        Enter key. Type your name, address, and phone number. If you wish to
        pay by credit card, enter your MasterCard or Visa number and its
        expiration date. Put a 'Y' next to the diskette size you want. When
        the form is complete, press Esc. You will see this question.
        
                         ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
                         º Print the ZEP Registration Form º
                         ÌÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¹
                         º ³Yes                            º
                         º ³No                             º
                         ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼
        
        If you have already selected a printer to capture LPT1, or if a
        printer is connected locally to your LPT1 port, select Yes to print
        the form. If not, select No, and set up your printer. Use the
        Register command on the Main menu again to return here. The form will
        ZeppeLAN User's Guide                                      Page 17
        
        
        still have the data you typed and you can print it.
        
        Fold the printed registration form on the dotted lines, insert a
        check if you are not paying by credit card, staple the form, put a
        stamp on it and mail it.