/*=*=*=*=*=*=*=*=*=*=*=*=*=*=*=*=*=*=*=*=*=*=*=*=*=*=*=*=*=*=*=*/
/*=*=*=*=*=*=*=*=*=*=*=*=*=*=*=*=*=*=*=*=*=*=*=*=*=*=*=*=*=*=*=*/
/* HIGH-LEVEL APPLICATION PROGRAMMING IPX INTERFACE FUNCTIONS */
/*=*=*=*=*=*=*=*=*=*=*=*=*=*=*=*=*=*=*=*=*=*=*=*=*=*=*=*=*=*=*=*/
/*=*=*=*=*=*=*=*=*=*=*=*=*=*=*=*=*=*=*=*=*=*=*=*=*=*=*=*=*=*=*=*/


/*******************************************************************/
/*******************************************************************/
/*
  ------------------------
  ------------------------
  FUNCTION: IPXReceiveRT()
  ------------------------
  ------------------------

  Receive data into a buffer or file from a non-specified sender.

  NOTE:
  The sender must know the internetwork address and socket of the
  machine that is to receive its transmission(s), but the receiver
  merely has to issue a LISTEN & can then receive from any sender.

  ----------
  ----------
  PROTOTYPE:
  ----------
  ----------

  unsigned IPXReceiveRT( long   *BfrLen,
                         BYTE   *FileOrBfr,
                         char   *SocketStr,
                         void   (*RTfunc)(void) );

  ---------
  ---------
  INPUT(S):
  ---------
  ---------

  BfrLen = 0 if receiving a file
             OR
           the maximum # of bytes that can be stored in a given buffer

  FileOrBfr = (string) name of file (path optional) into which to write
              the data that is received
                OR
              pointer to given byte buffer into which to store the data
              that is received

  SocketStr = 4 character hex-ASCII string of IPX Socket to
              use for receiving. Note that certain NOVELL sockets
              are reserved, and the caller is cautioned to use
              socket numbers "40xx", e.g., "4010", "40A1", etc.

  RTfunc    = pointer to a function which is to be called during
              time out loops when IPX command is pending.  Set
              to NULL if you don't need this "real time" capability.

  ----------
  ----------
  RETURN(S):
  ----------
  ----------

  0x00 - GOOD_IPX_RETURN - all went well.


  0x10 - BAD_LOCAL_TARGET - the internal IPX call to find the sender's
  local target failed.  Check the global variable IPXerrno for the
  specific reason, e.g.:

         0xFA - DEST_NODE_PATH_NOT_FND - the 6-byte node address
                specified in the received IPX packet parameter SrceAddr
                could not be found.  Either the packet was corrupted,
                or the sending machine with that node has died.


  0x11 - BAD_SOCKET_PARAM - the SocketStr parameter did not consist of
  a string of four hex-ascii digits.


  0x12 - BAD_SOCKET_OPEN - the attempt to open the socket specified in
  SocketStr parameter failed.  The global variable IPXerrno will contain
  return code received from IPX.  It can be one of the following:

         0xFE - SOCKET_TABLE_FULL - each machine gets 20 sockets, so
                this error should never occur unless other non-"well
                behaved" IPX applications are running on the machine.

         0xFF - SOCKET_ALREADY_OPEN - it will be closed upon return,
                so try again.  It is not ignored because at the point
                of call the socket shouldn't have been open, and all
                discrepancies will be caught and reported!


  0x20 - BAD_TX_TRY - an attempt to send a packet failed, due to
  failure of either the network or the configuration of the receiving
  machine.  Check the global IPXerrno to discern the problem.
  It should be one of the following:

         0xFC - EVENT_CANCELED - send request was canceled by
                application due to timeout.

         0xFD - FRAGMENT_SIZE_ERROR - malformed packet size, either
                less than 30 bytes or greater than 576 bytes, or
                the event control block's Fragment Count field was 0.

         0xFE - DESTINATION_NOT_FOUND - the destination machine,
                specified in the NETADDR parameter, is not on the
                network or not powered up.

         0xFF - NETWORK_FAILURE - network or hardware failure.


  0x21 - BAD_RETRIES - the receiver, while awaiting data from the
  sending machine, has exhausted its retry number & count series.
  Check IPXerrno for:

         0xFC - EVENT_CANCELED - listen request was canceled by
                application due to timeout.

         0xFD - FRAGMENT_SIZE_ERROR - either the event control block's
                Fragment Count field was 0, or the receiver's buffer
                space was too small to hold the incoming data.

         0xFF - ECB_SOCKET_NOT_OPEN - Socket for listening has not
                been opened by the application.


  0x22 - BAD_RX_SEQ_NUM - the receiving machine has received a block
  of data whose sequence number is unexpected. If this has occured,
  a network failure has caused the transmission to become garbled,
  or the sending machine had aborted the current send/received sequence
  and restarted anew within the retry number & timeout series of the
  receiving machine.  Both scenarios are highly unlikely.


  0x30 - BAD_FILE_OPEN - the file to be received, specified by
  the FileOrBfr parameter, could not be opened.  Check syntax of
  ASCIIZ string to make sure path and filename are correct, and
  don't forget to use double slashes in the string when specifying
  a path! For example, "D:\MYPATH\MYFILE.DAT" is not a valid C
  string. You must pass it as "D:\\MYPATH\\MYFILE.DAT".


  0x31 - BAD_FILE_WRITE - problem writing to the file specified in the
  parameter FileOrBfr, even though the file was successfully opened.
  This should never occur, barring disk failure or some strange
  interaction between the caller's program and other programs running
  as background processes or TSR's.


  0xBB - USER_TERMINATED - the user has chosen to abort the application
  by hitting the two SHIFT keys & an ALT key during a send/receive sequence.


  0xDD - IPX_NOT_PRESENT - IPX API interface was not detected. Make
  sure NOVELL's IPX.COM or equivalent has been run before attempting to
  access IPX functions.


  -------------------------
  -------------------------
  APPLICATION CODE EXAMPLE:
  -------------------------
  -------------------------

  #include "rkipx.h"

  #define RXSOCKET  "4050"
  #define RXBFRSIZE  8192

  int main( void )
  {
  unsigned rc;
  long     len;
  BYTE     *RxBfr;

  // receiving a file
  len = 0;
  rc = IPXReceiveRT( &len, "RXDATA.DAT", RXSOCKET, NULL );
  if ( rc != GOOD_IPX_RETURN )
     {
     printf( "FUNCTION ERROR: %02X  IPX ERROR: %02X", rc, IPXerrno );
     // take appropriate error action here
     return( -1 );
     }

  // receiving a buffer
  RxBfr = calloc( 1, RXBFRSIZE );
  if ( !RxBfr )
     {
     printf( "MEMORY ALLOCATION FAILURE!" );
     return( -1 );
     }

  len = RXBFRSIZE;
  rc = IPXReceiveRT( &len, RxBfr, RXSOCKET, NULL );
  if ( rc != GOOD_IPX_RETURN )
     {
     printf( "FUNCTION ERROR: %02X  IPX ERROR: %02X", rc, IPXerrno );
     // take appropriate error action here
     return( -1 );
     }

  return( 0 );
  }

*/
/*******************************************************************/
/*******************************************************************/
/*
  ---------------------
  ---------------------
  FUNCTION: IPXSendRT()
  ---------------------
  ---------------------

  Send a file or buffer to specified destination machine

  ----------
  ----------
  PROTOTYPE:
  ----------
  ----------

  unsigned IPXSendRT( long     *BfrLen,
                      BYTE     *FileOrBfr,
                      char     *SocketStr,
                      NETADDR  *Destination,
                      void     (*RTfunc)(void) );

  ---------
  ---------
  INPUT(S):
  ---------
  ---------

  BfrLen = 0 if sending a file
             OR
           the # of bytes to send from a given byte buffer

  FileOrBfr = (string) name of file (path optional) to send
                OR
              pointer to given byte buffer from which to send data

  SocketStr = 4 character hex-ASCII string of IPX Socket to
              use for sending. Note that certain NOVELL sockets
              are reserved, and the caller is cautioned to use
              socket numbers "40xx", e.g., "4010", "40A1", etc.

  Destination = structure containing Network Address, Node
                Address, and receiving socket number of the
                machine that is to receive the file/buffer data.
                See IPX.H for structure layout; if needed, use
                function xatoxb() for converting hex-ascii
                strings to hex-binary bytes.

  RTfunc    = pointer to a function which is to be called during
              time out loops when IPX command is pending.  Set
              to NULL if you don't need this "real time" capability.

  ----------
  ----------
  RETURN(S):
  ----------
  ----------

  0x00 - GOOD_IPX_RETURN - all went well.


  0x10 - BAD_LOCAL_TARGET - the internal IPX call to find the receiver's
  local target failed.  Check the global variable IPXerrno for the
  specific reason, e.g.:

         0xFA - DEST_NODE_PATH_NOT_FND - the 6-byte node address
                specified in the passed parameter Destination.INA.Node
                could not be found.  Either the node is non-extant, or
                the machine with that node is not powered on.


  0x11 - BAD_SOCKET_PARAM - the SocketStr parameter did not consist of
  a string of four hex-ascii digits.


  0x12 - BAD_SOCKET_OPEN - the attempt to open the socket specified in
  SocketStr parameter failed.  The global variable IPXerrno will contain
  return code received from IPX.  It can be one of the following:

         0xFE - SOCKET_TABLE_FULL - each machine gets 20 sockets, so
                this error should never occur unless other non-"well
                behaved" IPX applications are running on the machine.

         0xFF - SOCKET_ALREADY_OPEN - it will be closed upon return,
                so try again.  It is not ignored because at the point
                of call the socket shouldn't have been open, and all
                discrepancies will be caught and reported!


  0x20 - BAD_TX_TRY -  the attempt to send an IPX packet failed due to
  a problem of either the network or the configuration of the sending
  machine. Check the global IPXerrno to discern the problem.  It should
  be one of the following:

         0xFC - EVENT_CANCELED - send request was canceled by
                application due to timeout.

         0xFD - FRAGMENT_SIZE_ERROR - malformed packet size, either
                less than 30 bytes or greater than 576 bytes, or
                the event control block's Fragment Count field was 0.

         0xFE - DESTINATION_NOT_FOUND - the destination machine,
                specified in the NETADDR parameter, is not on the
                network or not powered up.

         0xFF - NETWORK_FAILURE - network or hardware failure.


  0x21 - BAD_RETRIES - the sender has been awaiting an acknowledgement
  from the receiver for most recently sent data, and has exhausted its
  retry number & count series.  Check IPXerrno for:

         0xFC - EVENT_CANCELED - listen request was canceled by
                application due to timeout.

         0xFD - FRAGMENT_SIZE_ERROR - either the event control block's
                Fragment Count field was 0, or the receiver's buffer
                space was too small to hold the incoming data.

         0xFF - ECB_SOCKET_NOT_OPEN - Socket for listening has not
                been opened by the application.


  0x22 - BAD_RX_SEQ_NUM - the destination machine has transmitted an
  acknowledgement to received data, but the sequence number does not
  match the sequence number of the data that the sender transmitted.
  If this problem occurs, either a network failure has caused the
  transmission to become garbled, or the destination machine had
  aborted the current send/received sequence and restarted anew
  within the retry number & timeout series of the sender.
  Both scenarios are highly unlikely.

  0x23 - BAD_RX_SRCE_ADDR - the sending machine received a transmission
  from a machine other than the expected receiver of the original trans-
  mission.  This should never occur, due to the fact that the sender
  socket should be known at this point only to the receiver of the
  message that the sender transmitted.  If other machines transmitting
  on the network are getting through to another sender unexpectedly, then
  some application software debugging is in order, or special TSR programs
  are running, the behavior of which should be monitored more stringently.


  0x30 - BAD_FILE_OPEN - the file to be transmitted, specified by
  the FileOrBfr parameter, could not be opened.  Check syntax of
  ASCIIZ string to make sure path and filename are correct, and
  don't forget to use double slashes in the string when specifying
  a path! For example, "D:\MYPATH\MYFILE.DAT" is not a valid C
  string. You must pass it as "D:\\MYPATH\\MYFILE.DAT".


  0x32 - BAD_FILE_READ - problem reading the file specified in the
  parameter FileOrBfr, even though the file was successfully opened.
  This should never occur, barring disk failure or some strange
  interaction between the caller's program and other programs running
  as background processes or TSR's.


  0xBB - USER_TERMINATED - the user has chosen to abort the application
  by hitting the two SHIFT keys & an ALT key during a send/receive sequence.


  0xDD - IPX_NOT_PRESENT - IPX API interface was not detected. Make
  sure NOVELL's IPX.COM or equivalent has been run before attempting to
  access IPX functions.


  -------------------------
  -------------------------
  APPLICATION CODE EXAMPLE:
  -------------------------
  -------------------------

  #include "rkipx.h"

  #define TXSOCKET  "4050"
  #define TXBFRSIZE  8192

  int main( void )
  {
  NETADDR  na;
  unsigned rc;
  long     len;
  BYTE     *TxBfr;

  // hard-coded example of internetwork address of destination machine
  xatoxb( na.INA.Network, "01234567" );
  xatoxb( na.INA.Node, "0123456789AB" );
  xatoxb( na.Socket, "4010" );

  // sending a file
  len = 0;
  rc = IPXSendRT( &len, "TXDATA.DAT", TXSOCKET, &na, NULL );
  if ( rc != GOOD_IPX_RETURN )
     {
     // take appropriate error action here
     return( -1 );
     }

  // sending a buffer
  TxBfr = calloc( 1, TXBFRSIZE );
  if ( !TxBfr )
     {
     printf( "MEMORY ALLOCATION FAILURE!" );
     return( -1 );
     }

  len = TXBFRSIZE;
  rc = IPXSendRT( &len, TxBfr, TXSOCKET, &na, NULL );
  if ( rc != GOOD_IPX_RETURN )
     {
     printf( "FUNCTION ERROR: %02X  IPX ERROR: %02X", rc, IPXerrno );
     // take appropriate error action here
     return( -1 );
     }

  return( 0 );
  }

*/
/*******************************************************************/
/*******************************************************************/