ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
     ³                                                           ³
     ³             The Administrator's Apprentice                ³
     ³                                                           ³
     ³                                                           ³
     ³                                                           ³
     ³      System Management by E-Mail -  An MHS-based NLM      ³
     ³                                                           ³
     ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ



       Contents


       Introduction
       Requirements
       Installation
       Creating Accounts
       Loading the NLM
       Configuration File
       Commands accepted by E-Mail
       The CRC32 Utility Program
       Planned enhancements
       Revision History
       Ordering Information
















      Copyright (C) 1994                                   PH Consulting
                                                  A-3704 Grosswetzdorf 1
                                                                 AUSTRIA



     ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
     ³ Introduction ³
     ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

     Administrator's Apprentice is an NLM for use on NetWare 3.x and 4.x.
     It interfaces with MHS (SMF-70 or SMF-71, i.e. MHS 1.5, Global MHS
     or Infinite Technologies' Connectý) to receive commands from and send
     alerts to the administrator (supervisor).

     Functions include:

       - NetWare broadcast message to Mail conversion

         NetWare broadcast messages to a specified user (the type of
         message normally displayed in the bottom line of a user's 
         screen by the NetWare shell) are not buffered, so they are 
         easy to miss. This NLM traps such messages and sends the 
         administrator an E-mail message instead.

         Benign messages may be filtered.

       - Remote File Server Console Status

         Upon receiving a command to do so, the NLM will take a "snapshot"
         of the server console's virtual screens and return them to the
         administrator.

       - Execute console commands

         Batches of console commands can be executed. Execution can be
         delayed for a specific time, or until an NLM is loaded/unloaded.

       - Print attached files to a specified queue

         Automatically print orders, invoices or anything else to a
         printer queue residing on the local file server.

       - List directory or calculate file CRC remotely

         Want to check which versions of a program a remote site is
         running? Send a one-line E-mail message.

       The (multithreaded) NLM runs completely in the background and 
       causes no noticeable server load when idle. It only polls the 
       server in regular intervals.

       When executing a command, utmost care is taken to minimize load
       on the server's CPU. The commands execute fast enough to prevent 
       any noticeable server performance degradation.

       This NLM is particularly useful for monitoring remote sites that  
       do not have an on-line (WAN) connection to the main LAN, but can
       be reached through E-mail.


     ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
     ³ Requirements ³
     ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

       ADMINAPP runs on NetWare 3.11, 3.12, 4.00, 4.01 and 4.02.

       Note that ADMINAPP requires CLIB 3.12f or later on NetWare 3.x.  
       If you are running Netware 3.11, don't be alarmed - you can also
       upgrade to CLIB 3.12x. As of this writing, the most current version
       is 3.12g, which is found in the file LIBUP3 or LIBUP4 (available in
       the NOVLIB forum on CompuServe or from ftp.novell.com on Internet).
       Novell does acknowledge a problem with CLIB 3.12g and GMHS 2.0, and
       recommends using CLIB 3.12f in this configuration.

       If you are for some reason unable to upgrade to CLIB 3.12f+, please 
       contact PH Consulting (addresses at the end of this document) for
       a separate Backward Compatibility Module.

     ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
     ³ Installation ³
     ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

     To install Administrator's Apprentice, copy ADMINAPP.NLM, 
     ADMINAPP.CFG and either ADAPP30D.NLM (for a 30-day trial)
     or ADAPPINS.NLM (for the retail version) to SYS:SYSTEM.

     At the file server console, enter

       LOAD ADAPP30D

     to start the 30 day trial period or

       LOAD ADAPPINS

     to install the retail product. Note that Administrator's Apprentice
     is licensed by NetWare File Server, independent of NetWare user count
     or MHS licensing.

     Next, edit the configuration file. You may use the command 

       LOAD EDIT SYS:SYSTEM/ADMINAPP.CFG

     at the file server console or any text editor from an attached
     station. Follow the comments in the sample ADMINAPP.CFG to fill in
     the proper parameters for your configuration. You should enter an MHS
     mail address and a local NetWare user name (see description below).


     ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
     ³ Creating Accounts ³
     ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

     If you have not already done so (or used an existing account), 
     use SYSCON or NETADMIN to create the user account the the NLM 
     will use to log in to the file server. This account need not have 
     any special rights to the file system; it is only used to receive 
     broadcast messages. 

     Make sure that this user account is specified in the appropriate
     places in other programs (such as backup utilities) and/or is a
     member of the proper user groups to receive all the broadcast 
     messages that you want. 

     Note that you may restrict this account's login address to 

       (file server internal net: node 1) 

     if you want to make sure it is not used by someone trying to 
     obtain undue access to the server over the network.

     Also, if the MHS mail account specified above does not exist yet,
     create it now. IMPORTANT: Make sure that MHS is the preferred 
     application defined for this account.

     Verify that you can log in to the server from a workstation
     using the username and password specified in the ADMINAPP.CFG
     file as 

        [BROADCASTS]
        NetWareUserName = AdminApp
        NetWarePassword = AdminAppPassword



     ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
     ³ Loading the NLM ³
     ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

       At the file server console, enter

         LOAD ADMINAPP

     ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
     ³ Configuration File ³
     ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

       The configuration is read from the file SYS:SYSTEM/ADMINAPP.CFG.

       This file follows the Windows conventions of INI files, i.e. it
       is divided into sections (indicated by section names in []),
       which hold a number of assignments of the form

         Parameter = Value

       Blanks around the equals sign are ignored if present.
       Comments can be entered on blank lines by prefixing them with a
       semicolon. Upper/lowercase is ignored for the parameter names.

       Path values must be entered in NetWare format:

             Volume:Dir1\Dir2\Dir3
 
       The volume name must be specified. A forward slash may be used 
       instead of a back slash. Volumes must be on the local server;
       this NLM does not support logging in to other servers.


     ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
     ³ Commands accepted by E-Mail ³
     ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

     Administrator's Apprentice reads E-mail messages addressed to it
     and processes the command specified on the "Subject:" line of the
     message. The following commands are defined:

       PRINT Queuename

         Enters attached file(s) as job(s) in the specified print queue.

       STATUS [G][V][C][N][S][T][*]

         Returns a status report to the sender of the message.

         Contents: G = General, V = Volumes, C = Connections, N = NLMs,
                   S = Screens, B = Bindery, P = Bindery + Properties

         Any or all of the optional report types may be specified. An 
         Asterisk may be specified in place of the options to get all of
         the reports. If no options are specified, a "Vols/Conns/Screens" 
         report is returned.

       IGNORE

         Ignores this message completely.

       CONSOLE ConsolePassword

         Interprets the lines of the message body. The console password
         must match the one specified in ADMINAPP.CFG for the message to
         be processed.
         The following keywords are recognized:

           COMMAND ConsoleCommandLine

             The console command line is passed to NetWare.

           STATUS MHS-Address;[G][V][C][S][T]

             Sends a status report to the address specified (in this case
             it can be different from the sender's address).
             The address must be present and is separated from the options
             by a semicolon.

           DELAY NumberOfSeconds
 
             Delays for the specified number of seconds.
             Note that polling for broadcast messages is not affected
             because this continues to run in another thread.

         (CONSOLE sub-commands continued on next page)


         (continued: CONSOLE sub-commands)

           WAITFOR NLMLOAD NLMName [Timeout]
           WAITFOR NLMUNLOAD NLMName [Timeout]

             Waits for the specified NLM to be loaded/unloaded.

             Note that the name is the internal name of the NLM, which
             is not necessarily identical to the file name. If in doubt,
             consult the information obtained with STATUS N.

             Note that only the base name is used for this command -
             the file extension (.NLM, .LAN etc.) is ignored.

             If the NLM is not loaded/unloaded within the specified
             timeout (in seconds), the command continues nonetheless.
             The default timeout is 30 seconds.

             Example: WAITFOR NLMUNLOAD NGM 600

           CLOSE ScreenName

             Switches to the specified virtual screen and "presses the 
             ENTER key" there. Used to close screens displaying the
             message "Press any key to close screen".

           MESSAGE MHS-Address;Subject 

             Sends an MHS Message with the specified subject to the
             specified address. Address and Subject are separated by a
             semicolon.

           CRC FilePath
 
             Calculates the CRC32 (CCITT) of the specified file. This CRC
             is the same as it is used by popular archiving programs such
             as PKZIP or ARJ. Used to compare file versions with known
             references. See also the description of the enclosed CRC32 
             utility program for DOS.

           DIR FilePath [/S]

             Lists the directory. Note that you have to specify a file
             wildcard, such as in

               DIR SYS:SYSTEM/*.*

             Option /S will cause subdirectories to be listed as well.
             Note that the result is sent as the body of a message.
             Therefore, if its length exceeds 64K and Global MHS has to
             "downgrade" the message, i.e. convert from SMF-71 to SMF-70,
             the message will be rejected by GMHS because GMHS insists
             that an SMF-64 message cannot be longer than 64K.

             Such a limit does not exist if the format stays at SMF-71
             or if the message is handled by MHS 1.5 or Connectý.

           FETCH FilePath

             Attaches the specified file to a reply message.


         Example usage of the CONSOLE command to control the backup of a 
         NetWare SQL database:

             To start backup, send the following message to AdminApp:

               Subject:  CONSOLE !You#will#never#guess!
       
               COMMAND Load NSUTIL -StartBU DatabaseName
               DELAY   20
               STATUS  Operator@Company;S
               CLOSE   NSUTIL
               MESSAGE Backup@Company;BACKUP MyServer

             This places the database in continuous-operation (backup)
             mode, sends a status message to the administrator and closes
             NSUTIL's screen. Then it sends a message to a backup gateway.

             This gateway (example shown next page) (ab)uses the MHS 
             server to perform a backup procedure. Upon completion of 
             that procedure, it sends the following message to AdminApp:

               Subject:  CONSOLE !You#will#never#guess!
       
               COMMAND Load NSUTIL -EndBU DatabaseName
               DELAY   20
               STATUS  Operator@Company;S
               CLOSE   NSUTIL
               MESSAGE Operator@Company;Database backup completed




             Example RUNIT.BAT for Infinite Technologies' Connectý MHS
             compatible message router which can directly run batch files
             as gateways:
             (Note: Specify parameters for SENDIT on a single line!)

               @echo off
               cls
               echo.
               echo.  RUNIT Gateway to control Backup
               echo. 
               echo.  Processing message from %gwfrom% ...
               echo. 
               rem   delete old log file, if present
               if exist backup.log del result
               rem   Parameter n is n-th Word on Subject line
               rem   we're using Parameter 1 as a keyword
               rem
               rem   Command 1: BACKUP
               rem
               if not [%1]==[BACKUP] goto nobackup
               BackupProgram Script=%2 Logfile=BACKUP.LOG
               if errorlevel 1 goto backuperr
               sendit /t%gwfrom% /f%GWNAME%@%GWNAME%(Backup)
                     /sBackup completed. /b /q
               goto cont1
               :backuperr
               sendit /t%Operator@Company /f%GWNAME%@%GWNAME%(Backup)
                     /sBackup FAILED! /bBACKUP.LOG /q
               :cont
               sendit /tAdminapp@Company /f%GWNAME%@%GWNAME%(Backup)
                     /sCONSOLE !You#will#never#guess! /bENDBU.MSG
               sendit /t%Operator@Company /f%GWNAME%@%GWNAME%(Backup)
                     /sBackup completed. /bBACKUP.LOG /q
               goto cont2
               rem
               rem   Example command 2:
               rem
               if not [%1]==[LIST] goto cont2
               BackupProgram List=%2 Logfile=BACKUP.LOG
               sendit /t%Operator@Company /f%GWNAME%@%GWNAME%(Backup)
                     /sRequested List /bBACKUP.LOG /q
               :cont2
               rem   More commands can be implemented the same way
               rem
               rem   Delete already-processed message (Cý doesn't)
               del %GWDIR%OUT\%GWMSG%
               echo - Done!

             (STARTBU.MSG/ENDBU.MSG contain the text of the previously
             shown mail messages).

             Please refer to the documentation of Connectý as well.

             For sites running Global MHS or MHS 1.5, Infinite
             Technologies offers a gateway called RunIt! that offers
             this functionality for these environments.


     ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
     ³ The CRC32 Utility Program ³
     ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

     The CRC32 program is a DOS-based utility to calculate the 32bit CRC 
     (cyclic redundancy check) checksum as defined by ANSI X3.66, 
     FIPS PUB 71, FED-STD-1003 or CCITT/ITU-T X.25.

     This is the same CRC method as implemented in popular compression or 
     archiving programs such as PKZIP(tm), ARJ(tm) and others.

     Note to those who want to know it all: The polynomial being used is
     X^32+X^26+X^23+X^22+X^16+X^12+X^11+X^10+X^8+X^7+X^5+X^4+X^2+X^1+X^0.

     Using the program
     ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

       crc32 filespec { filespec }

     Filespecs may use the wildcard characters * and ? as common in DOS.

     The option /X<ext>{,<ext>} excludes files with extension <ext> for
     the rest of the command line or up to the next /X option.

     Progress of the CRC calculation is indicated by a spinning line.
     The program's output may still be redirected by DOS.


     Example
     ÄÄÄÄÄÄÄ

       crc32 /XSYS SYS:SYSTEM/*.* /X SYS:PUBLIC/*.*

     Hints
     ÄÄÄÄÄ

     The same file may be specified multiple times on the command 
     line to test disk/LAN integrity, e.g. 

       crc32 test.dat test.dat test.dat test.dat test.dat test.dat 

     The program should of course calculate the same CRC value 
     every time.

     To quickly tell if two files are equal, use (for example)

       crc32 SYS:SYSTEM/CLIB.NLM SYS:SYSTEM/CLIB.OLD

     The advantage to comparing files with a program like DIFF or FC 
     is that using ADMINAPP, the CRC32 value can be computed and sent 
     quickly for a remote file, even if it is several megabytes in 
     size. FC would require the whole file to be transferred for the 
     comparison.

     Alternatively, the CRC can bee transferred by even lower-tech
     methods, such as reading over the phone.


     ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
     ³ Planned enhancements to AdminApp for upcoming releases ³
     ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

     - Monitoring NetWare internal events such as Volume mount/dismount,
       user login/logout, bindery security change etc., configurable 
       through the INI file and/or E-mail commands

     - Monitoring log files for error messages

     - Conditional execution & labels in CONSOLE subcommand-blocks,
       e.g. depending on the result of WAITFOR NLMLOAD

     - Exploit the diagnostics capabilities built into NetWare 4 to return
       information about memory utilization etc.


     Any other suggestions are cordially welcomed!


     ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
     ³ Revision History ³
     ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

       V1.00   94/10/23  Initial Beta Release.
       V1.00A  94/10/30  Added NLM Info, WAITFOR NLMLOAD, 
                         WAITFOR NLMLOAD commands.
       V1.10   94/11/07  Added NetWare 3.x support for NLM Info/WAIT 
                         commands. Cleaned up UNLOAD code. Beta Rel. 2.
       V1.20   94/12/27  Release candidate
       V1.20A  94/12/30  Fixed NW 3.11 NLM list garbage. 
                         First production release.
       V1.20B  95/01/11  Moved ConsolePassword= setting to [Settings]
                         section. Added MailPollDelay= setting.
                         Clarified documentation.


     ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
     ³ Ordering Information ³
     ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

     Administrator's Apprentice is supplied as a 30-day evaluation
     version. You are welcome to try out the program during that period.
     After this period, the evaluation version will cease to run.
     You may install a purchased license at any time without any change
     in configuration. 

     You are also welcome to give copies of this evaluation package to
     whomever you wish, provided that you pass the original archive in
     its entirety.

     The price of the licensed version is US $280 per server in the U.S.,
     or ATS 3000 in Europe and elsewhere, including E-mail delivery, but 
     excluding mail or courier S/H.

     E-mail if you want to negotiate site or corporate licenses.
     Resellers please inquire about terms.

     To order the licensed version, contact

         Peter Holzleitner Consulting
         A-3704 Grosswetzdorf 1
         Austria, Europe

     by E-mail as

       MHS: 
             Peter@PHConslt  (via LEND-ING, CSERVE, NHUB)

       Internet:

             pholzl@ping.at

       From CompuServe, you may enter 

             MHS:Peter@PHCONSLT       (preferred as it is faster for me)
         or
             100427,234