Everex NetBIOS v2.x Upgrade

Everex NetBIOS v2.x differs from previous versions in several ways.
This file contains information on the features of the new NetBIOS.
Version 2.x is not compatible with older versions of NetBIOS.  All 
stations on the network must run NetBIOS v2.x to communicate with
each other.  If you have any stations running a previous version, 
you must upgrade to Version 2.x.

The command format for NetBIOS v2.x is:

   NET21E [/Ixx] [/Mxxxx] [/Ax] [/Nxx] [/Sxx] [/Exxxx] [/K]

where

   /Ixx   - This option specifies the interrupt signal used by the 
            adapter.

            The default is 4.  Valid options are 2, 3, 4, 5, 6, 7,
            9, 10, and 15.

   /Mxxxx - This parameter specifies the base memory address used 
            by the adapter.
 
            The default is C800.  Valid options are C000, C800, 
            D000, and D800.

   /Ax    - This option specifies the adapter number to which this 
            NetBIOS is configured.  This specification allows 
            installation of multiple Everex cards in one system, 
            when supported by the Network Operating System (NOS). 
            Some NOS allow multiple adapters in one computer (e.g.,
            Artisoft's LANtastic NOS).  Consult your NOS manual for 
            more information on multiple network cards.

            The default is 0 (the first card installed).  Valid 
            options are 0, 1, 2, and 3.

   /Nxx   - This parameter specifies the maximum number of NCBs 
            supported by this NetBIOS.  NCBs are command blocks used 
            by applications or NOS software to pass commands to NetBIOS.
            Setting the maximum number of NCBs limits the number of 
            commands that an application or NOS can issue to NetBIOS. 
            The program occupies less memory when configured for fewer
            NCBs.

            The default is 32.  Valid options are 1 - 32.

   /Sxx   - This option specifies the maximum number of sessions 
            supported by this NetBIOS.  Sessions are connections over
            which data can be sent.  Most NOS require that at least 
            one session per user be supported (i.e., the more users 
            supported by the NOS, the more sessions required).  NetBIOS 
            occupies less memory when configured for fewer sessions.

            The default is 32.  Valid options are 1 - 32.

   /Exxxx - This parameter specifies the Ethernet protocol type to use 
            when transmitting and receiving frames.  It is used by 
            NetBIOS to differentiate its own frames from other protocol 
            frames when several protocols are running on the same network.
            All stations must use the same Ethernet type in order to 
            communicate.  No Ethernet types are needed if the entire 
            network uses only NetBIOS. 

            The default is No Ethernet Type.  Valid options are
            0 - FFFF.

   /K     - This is a special option used for IBM PC LAN NOS.  If you 
            are running IBM PC LAN with this NetBIOS this switch is
            required.


Where options are not specified, the default values are used.

Examples :

   NET21E                ; Loads NetBIOS with default interrupt signal 4,
                         ; base memory address C800, adapter 0 (the first
                         ; adapter installed), 32 sessions, 32 NCBs, and 
                         ; no Ethernet type.


   NET21E /I3 /MD000     ; Loads NetBIOS for one adapter with interrupt
                         ; signal 4 and base memory address D000.

   NET21E /I2 /MC000 /A0 ; Loads NetBIOS for two adapters with the first
   NET21E /I3 /MC800 /A1 ; adapter using interrupt signal 2 and base memory 
                         ; address C000, and the second adapter using 
                         ; interrupt signal 3 and base memory address C800.


   NET21E /N12 /S12      ; Loads NetBIOS with fewer sessions and NCBs.  
                         ; This lowers the amount of memory required by
                         ; NetBIOS.  This configuration is good for
                         ; workstations since NOS require fewer sessions for 
                         ; workstations.

   NET21E /E3875 /K      ; Loads NetBIOS with Ethernet protocol type 3875 and
                         ; running under IBM PC LAN NOS.