TCPrint - Host TCP/IP Printer Server for NetWare

   TCPrint is a printer server resides on NetWare file server
 which complaint with RFC1179 protocol - LPD (Line Printer Daemon).

   All hosts that supports TCP/IP LPD protocol can assign their print
 job into NetWare server's print queue directly via TCPrint. There is
 no additional software required for those hosts.

   User can assign their job transparently just as they are printing
 on host. All processes will be done by host and TCPrint.

   Also, TCPrint do Unix->DOS text ascii translation automatically.

   This version of TCPrint is designed as REGISTWARE ( i.e. no extra
 registration fee !). Please refer NOTE in this file for registration.


INSTALLATION

    TCPrint must be installed at NetWare file server. Installation
  step is listed below :

    (1) Check if NetWare file server has TCPIP.NLM loaded previously.

    (2) Load TCPIP.NLM as below if not loaded

        :LOAD TCPIP FORWARD=YES
        :LOAD NE2000 INT=3 PORT=300 FRAME=ETHERNET_II NAME=E_II
        :BIND IP TO E_II ADDRESS=132.147.160.251 MASK=255.255.255.0

        the NIC driver name/parameters can be replaced with your configuration
        IP address, subnet mask is depands on your network's assignment

    (3) Load TCPrint from server console, the syntax is :

        :LOAD TCPRINT [IP Address] [Authentication Key]

        all parameters in bracket are optional

        for example :

        :LOAD TCPRINT 132.147.160.251 3AjPsLDwHj2DFw03



         You need to provide your company information (mail address, fax no.
        contact person .., etc.) and NetWare serial number for registration.

    (4) All remote printer which resides on host must be created as print
        queue on NetWare in same name. Please create queue in bindery mode
        if in NetWare v4.x environment.

 NOTE

      Host installation please refers administration guide for each system.

      TCPrint will accept 10 printing jobs then unload itself if
    authentication key is absent. The authentication key must obtained from
    Transcend Information, Inc. CIS 101400,271 WILLIAM WANG