* * * * * * * * * * * * * * * * * * * * * * *
                   * * * * * * * * * * * * * * * * * * * * * * *
                   * *                                       * *
                   * *         T I M E   S E R V E R         * *
                   * *                                       * *
                   * *      Keeps Your Network On Time       * *
                   * *                                       * *
                   * * * * * * * * * * * * * * * * * * * * * * *
                   * * * * * * * * * * * * * * * * * * * * * * *



                                   version 2.2





                         (c) Copyright Jiri Severa, 1994




      TSERVE USER GUIDE                                               1
      -----------------------------------------------------------------


      COPYRIGHT NOTICE

      The software found in the archive file along with this document
      is the property of Jiri Severa of Ottawa, Ontario, Canada. Any
      use, reproduction and/or distribution of this software on terms
      other than those expressly stated in the SHAREWAR.E document
      enclosed is prohibited.


      ABOUT TSERVE

      The single purpose of this software collection is to provide the
      means of setting and maintaining a reliable time standard on a single
      Intel processor-based PC or on a Novell network. Simply put, the progr-
      ams connect a user's machine to a very accurate clock via modem and
      synchronize the PC's internal clock with an international standard. The
      process is repeated at intervals of the user's choosing. On a network,
      the machine selected to import the exact time becomes a time server:
      primary source from which the whole network synchronizes the clocks
      of its local servers.

            What is the benefit of a time server ? The answer to that is
      that there are a number of benefits:

           * authoritative time reference - human inquiry : someone mentioned
             to me the other day that since we installed a time server on our
             network 'my Windows clock actually tells time'. An accurate time
             source and a means to broadcast it is something that adds to any
             organization's productive assets.

           * event tracking - a number of network processes are logged and the
             logs are later analyzed to evaluate specific functions. More often
             then not the entries' date stamps are of crucial importance, rel-
             ating to other, external, events in real time. When an unattended
             server goes down you would want to know when exactly it happened.

           * software alarms - a popular feature with a number of Office-type
             software schedulers are warning bells that ring an x-number of
             minutes before meetings, departures, etc. These programs, not to
             say their users, assume that the workstation keeps accurate time.

           * e-mail handling - the performance of e-mail facilities is often
             subject of queries, and there the needs of a modern, distributed
             data-handling come into a relief. Today, hundreds of thousands of
             messages will be exchanged among the world's e-mail users on which
             the date stamp of the reply will precede that of the original mess
             age. No great harm done, but under these conditions it becomes
             difficult to follow the traffic on an e-mail net and gauge the
             throughput at different transfer points by simply comparing time
             stamps.

      These are but a few examples but the trend to distributed, client-server
      data processing will soon force time synchronization as a matter of
      course.



      TSERVE USER GUIDE                                               2
      -----------------------------------------------------------------

            The solution to getting oneself on a standard time would have
      been in the most recent past to buy some pretty fancy and
      expensive gear to get in sync with the nearest cesium atomic
      clock. That is the expensive solution and a massive overkill because
      the precision of a few nanoseconds is mostly lost on systems whose
      internal oscillator registers ticks once every 55 milliseconds. So,
      apparently a connection to a 300 baud transmitter which provides
      the public with the precision time reading will do under such circum-
      stances. This is what TSERVE does.



      ABOUT THE NATIONAL RESEARCH COUNCIL'S (CANADA) TIME SERVICE

      The provider for TSERVE time standard is the Institute for National
      Measurement Standards, a branch of Canada's National Research
      Council. The time services run by the Institute are available
      to the general public and include voice service, telephone digital
      code time signals, short wave transmission and remote calibration.
      You may write for more information on those services to :

                   National Resarch Council
                   Institute for National
                   Measurement Standards
                   (Time Services)

                   Ottawa, Canada
                   K1A OR6

      Needless to say, this software would not be possible without a
      public service which makes time standard available at low-cost,
      actually, at this time , at no cost other than the telephone
      call. Naturally then, this shareware becomes also a sort of a
      crusade to assure that this service does not go on the chopping
      block, and that the facilities are upgraded to answer the demand.
      Please, take time to fill in the Request for Continuous Time
      Service in the CRUSADE.NRC file and send it together with your
      registration fee. This request is of course valid only in case
      you are a Canadian resident. For U.S. citizens, we would be grate-
      ful if you send the requested $20 (US) NRC contribution as a goodwill
      gesture.




      TSERVE USER GUIDE                                               3
      -----------------------------------------------------------------


      THE ARCHIVE FILES

      The shareware package contains the following files :

      SHAREWAR.E  - spells out the terms and conditions under which
                    you may use this software.

      CRUSADE.NRC - form letter to the National Research Council
                    requesting the continuance of service.

      TSERVE.DOC  - user manual
      TSERVE.EXE  - time server communication program
                    synchronization

      NSSFX.EXE   - Netware Sync Single File Server module
      NSMFX.EXE   - Netware Sync Multiple File Server module - up to eight.

      DAYLIGHT.EXE - Standard-Daylight, Daylight-Standard switch module
      STIME.EXE    - Server time update utility for Netware workstations

      GENIE.EXE    - Batch Scheduler / Processor
      SETGENIE.EXE - Setup Utility for GENIE
      BTRACK.EXE   - Batch tracking utility

      GENIE.DOC    - GENIE user guide



      HARDWARE AND SOFTWARE REQUIREMENTS

      Intel 8088 based PC or better.
      Hayes-compatible 1200 baud modem.
      MS DOS ver. 3.3 +




      TSERVE USER GUIDE                                               4
      -----------------------------------------------------------------



      INSTALLATION AND OPERATION OF TSERVE

            To install the time server software simply copy the files
      to a directory on your hard disk or even to a diskette. You may
      run TSERVE from a diskette and on a plain old XT with no loss of
      time-keeping precision.
            To run a timesync session enter the following command at a
      DOS prompt in the directory where you installed the software, e.g.:

                   C:\TSRV>TSERVE  <Enter>

      After TSERVE has been started you don't need to do anything to aid
      the program to communicate with the time provider. The program has
      been designed as a fully automated process requiring no manual
      intervention. After a short pause at the beginning of the program,
      about which more shortly the following two display windows appear
      on the screen:

     ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
     º                                                              º
     º             NRC Atomic Clock Time Synchronization            º
     º                                                              º
     º Time Zone :                                                  º
     º Start Time  :                          Date :                º
     º Equip. Bias :                   Clock Ticks :                º
     º Loop Delay  :                   Sync at :                    º
     º                                                              º
     ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

     ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
     º                                                              º
     º                                                              º
     º                                                   ...wait  ! º
     ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

      The upper window reports on the time-keeping parameters during
      the ongoing dialog. Their meaning is explained below in 'SETTING
      SESSION PARAMETERS'. The lower box reports session status,
      dutifully reporting on what the program is up to at all times.
      See below TROUBLESHOOTING AND TSERVE MESSAGES for clues.
      The upper display stays on for several seconds after the end
      of the session.
          Starting with version 2.0 it is possible to cancel the call
      to NRC at any time during modem initialization or dialup.





      TSERVE USER GUIDE                                               5
      -----------------------------------------------------------------

      SETTING SESSION PARAMETERS

          At the start the program loops for 5 seconds displaying
      the maple leaf logo. During this time the user has the option
      to reset session parameters. Hit any key.

      The following panel will appear :

                                                                   ³
                         ÚÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄ¿                         ³³
        Communication :  > COM1: < COM2: ³         Time Zones :    ³³
                         ÀÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÙ                         ³³
          ÚÄÄÄÄÄÄspeedÄ¿ Údata¿ Ústop¿ Úparity¿  ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿  ³³
          >   300 baud < >  8 < >  1 < > none <  ³ Newfoundland ³  ³³
          ³  1200 baud ³ ³  7 ³ ³  2 ³ ³  odd ³  ³   Atlantic   ³  ³³
          ³  2400 baud ³ ³  9 ³ ³  0 ³ ³ even ³  >   Eastern    <  ³³
          ³  9600 baud ³ ÀÄÄÄÄÙ ÀÄÄÄÄÙ ÀÄÄÄÄÄÄÙ  ³   Central    ³  ³³
          ³ 14400 baud ³  speaker Netware Sync   ³   Mountain   ³  ³³
          ÀÄÄÄÄÄÄÄÄÄÄÄÄÙ  > on  < ³  enable  ³   ³   Pacific    ³  ³³
         bias   0/100 sec ³ off ³ > disable  <   ³  GMT offset  ³  ³³
         clck  .05495 sec ÀÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ   ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´  ³³
         loop delay[Y/N]>Y  retry line error>1   >   Standard   <  ³³
         telephone number              busy>99   ³   Daylight   ³  ³³
             [1-613-745-3900                  ]  ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ  ³³
                                                                   ³³
       ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ³
        ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

      The arrows (which on the screen are represented by a scroll bar) are
      the defualt values. Besides communication parameters, the panel
      registers time-keeping parameters, which are of two kinds : time
      zones and precision control.

      COM1 and COM2 ports are supported. The NRC modem presently operates
      at 300 baud, eight data bits, one stop, no parity. Together with the
      phone number these are  g i v e n s  and they should not be reset
      unless more lines are open and these operate differently. The
      'speaker' switch refers to the modem speaker. If you want a silent
      operation set the switch to the off position. If 'Netware Sync'
      is enabled, the program does not terminate at the end of the
      NRC session but passes to the Time Server - File Server dialog.

      Three variables allow the user to 'calibrate' the received time:
      (equipment) bias, clock tick intervals, and deciding whether to
      factor in the measured loop delay. Starting with version 2.2 you
      may select line- and busy- retries. Previously, receiving a line
      error during dialling caused the session to terminate. Now you may
      may retry the dialup up to 9 times. If line was busy, the previous
      versions of TSERVE continued indefinitely until a key was struck.
      Now, you may hang up after specified number of 'busy' responses.
      You may enter any number from 0 to 99. Entering '99' retries for
      busy means continue indefinitely, any other number triggers a
      counter.


      TSERVE USER GUIDE                                               6
      -----------------------------------------------------------------

            T i m e   Z o n e s -  TSERVE started by supporting North
      American users only. In the last two months, however, we have receiv-
      ed a number of inquiries via Compuserve, asking for the support of
      European time zones. This demand has been answered by TSERVE starting
      with version 2.0.  All world time zones are supported ! The user is
      allowed to enter any time offset from the GMT as parameter.
            The time zones panel lists North American time zones and a
      'GMT offset' selection which allows the user to set up any hour/minute
      offset from the GMT. When you press Enter or Tab in the Zones with
      the GMT offset selected you will be prompted to enter the hour and
      minute values. If you are in Alaska you will enter -9 in hours and 0
      in minutes, if in Bombay enter 5 in hours and 30 minutes. Do not
      adjust for daylight time ! That is done by the daylight switch !

      I M P O R T A N T : If you are updating from version 1.x of TSERVE
                          you must first delete file TSPARMS.DAT and
                          reset the parameters table before running
                          TSERVE again. Program may not run properly if
                          you omit this step.

            The manipulation of the table is very simple. Move forward
      by pressing Enter (or TAB for the tables) and select values by
      pressing space bar. In entry fields, clear fields forward by Enter.
      You may quit the setup by pressing Esc at any time. If you make a
      mistake you may return to a prefious field by Alt-Tab combination
      for tables or F5 in entry fields.

            When you clear the last field (telephone number) you are asked
      to accept the parameter settings. Once accepted, the values replace
      whatever default or previous settings. After the parameters are
      filed, the program asks if you want to open up a session with the
      NRC host immediately. If you answer 'N'o the program terminates.

      I M P O R T A N T :  If you happen to live in the local area (of
      code 613, that is the region of Ottawa,) the phone number must be
      altered for local connection. The same applies for users from out-
      side of North America. Also, do not forget to include dial-out
      digits !!!

      TIME PRECISION FACTORS

            The time broadcast via telephone lines gives a very accurate
      time but realistically it will not come close to transferring the
      kind of accuracy it receives from a cesium atomic clock. A number
      factors reduce the expectations of precisions from a the order of
      nanoseconds to tens of milliseconds, and tenths of a second. First
      of all, there is the transmission delay.
            The transmitter, the NRC documentation says, sends the stop
      bit of the carriage return (which terminates the time broadcast)
      precisely at the full second. From the labs of INMS it travels via
      trunk lines and microwave bands, through multiplexors, repeaters
      and the occasional Strowger to arrive with some sort of a delay.
      This delay the NRC proposes to measure by means of a transmit-
      retransmit session with a client, in which the client sends a



      TSERVE USER GUIDE                                               7
      -----------------------------------------------------------------

      single character and the host returns it. The measured time is
      then halved to represent the propagation delay of the transmitt-
      ed time. The Council warns that for certain values received (25-
      29 milliseconds of full loop delay) this technique of 'halving' does
      not reliably represent the lag since such delay indicates the
      signal has travelled one way overland and the other via satelite.
          A second set of factors concerns the PC's timer. The method of
      keeping time on the PC has not changed since the unveiling of the
      machine in 1981 even though the processors have become vastly more
      sophisticated. The venerable 8253 timer-chip's way of pushing the
      clock while synchronizing the procesor and the bus is still the
      canon. The result is that today's Intel processors can switch
      between tasks six to eight times faster than register a 55 millisecond
      tick. You may write a simple program to contemplate mysteries of PC
      time. Set the time on a full second (using INT 21H function 2DH)
      and then get the ticker value from the lower memory (by INT 21H
      function 2CH) and when you display it, low and behold, it's still
      b e f o r e  the time you set it. The other issue is the precision
      of the oscillator. The standard - 1.19318 MHz - is a rarity most
      of the time the quartz is a few Hertz off, sometimes quite a few
      Hertz. Even if the chip is dead on, it falls behind 88 milliseconds
      every day. On top of this notoriously crude time keeping, the timer
      channel 0 can be manipulated by programs which can vary the time
      divisor to suit their purposes, and some of them do without worrying
      about such details as the system clock going haywire.
            Further down the line come concerns regards the transfer of
      the clock value between the system memory and CMOS, and the state
      of lithium battery. The single greatest loss of the clock precision
      originates in those transfers although in fairness it should be said
      that this deviation has to do more with local time-keeping than
      the accuracy of the transfer of NRC atime.

            The transfer speed between DCE and DTE, ie. the modem and the
      PC represents another possible source of delays, the type of queuing
      and buffering protocol, the buffer overrun protection and the delay
      for the RTS-CTS negotiations set by the Hayes S9 register being the
      chief players.
            Finally, of course, there is the program code. Even though the
      delay associated with the translation of the ASCII codes to binary
      digits and executing a system interrupt may seem trivial in compar-
      ison with the above, it is a factor when we compare the precision
      standard which we are asked to duplicate. I am happy to report that
      TSERVE was coded with this in mind. The program goes into a character
      mode (as opposed to string input) for the NRC time reading and processes
      the incoming time digits individually, using the time between their
      arrival to do the binary conversion tricks and time zone calculations.



      TSERVE USER GUIDE                                               8
      -----------------------------------------------------------------

      PRECISION CONTROL

            So what can be done to come as close as possible to the NRC
      standard ? The simplest way is to use the loop delay measurement
      recommended by NRC. TSERVE performs the loop delay calculation
      when the 'loop delay' parameter (on the panel above) reads 'Y'. When
      the session runs the obtained value (the half-time) is displayed, and
      recorded into a log. The measurement is done in such a way that it
      includes also a half of the modem delay.
            If you have access to some local source of precise time which
      you can connect to your PC then I would suggest a calibrating
      session. Take a sample of the actual delay from several NRC sessions
      to determine if the lag is more or less constant. You may then enter
      the average ms delay directly in TSERVE in the 'bias' parameter. In
      that case you would also want to set the loop delay to 'N'.
            A little bit of PC neurosurgery can turn the a PC - if you
      can spare one - to a much more precise clock reading instrument.
      It involves reprogramming the timer chip, as I have mentioned earlier.
      That presumes a sophisticated programmer and a high degree of custom-
      ization. The 'clck' variable in the parameter table prepares the
      program for a new time keeping interval on the chip. By default, clck
      displays is set to the 55 millisecond standard.


      TIME VERIFICATION

      You may verify the time you have received by TSERVE by calling
      NRC's voice time service at 613-745-1576. The second tick occurs
      at the beginning of the tone after the announcement.


      TSERVE SESSION LOG

      The results of each time sync session are recorded in an ASCII file
      called TSLOG.DAT. An entry of a succesfully negotiated transfer
      may look like this :

          Session 7-May-94  23:29:04 - synchronized time with NRC.
          Time corrected by      -0.05 secs  Date not reset.
          Propagation delay in loop : 0.10990 seconds.

      If an error occurs which forces the program to cancel a session
      the log records the reason why. Please see TSERVE ERROR MESSAGES
      below.



      TSERVE USER GUIDE                                               9
      -----------------------------------------------------------------

      NETWARE SERVER TIMESYNC DEMO

      The shareware package includes a demonstration of synchronizing
      the time server station with a single file server and multiple
      file servers. Like with the time download the transfer to servers
      is automatic. In order to sync with  a file server the station must
      be logged into that server as a valid user with minimum of console
      operator access. For multiple server sync the user must be attached
      from the time server station to all servers with those rights. The
      session parameter 'Netware Sync' (see SETTING SESSION PARAMETERS
      above) must be set to 'enable' for  TSERVE to load the Netware module
      and pass control to it.
           There are two Netware Sync modules in the package: NSSFX, for
      single server, and NSMFX, for multiple (up to 8 sessions). Select the
      one you want to use and rename it to 'TS.REX'. Make sure that TS.REX
      is in the same directory as TSERVE.

         Briefly this is what happens when TS.REX executes: A check of
      connection to the primary server is made when it is found a
      display of the program appears on the screen with the name of
      the workstation user and the file server. If no connection exists
      the program terminates with a note in the log file. If the user
      has console clearance the program then waits for the beginning
      of the next full second (Netware does not allow setting for 1/100s
      of a second) and then resets the file server timer. A test is then
      performed to see if the time has sync-ed and the result is displayed.
      The display stays on for a minute after which the program ends.
      You may terminate the program after sync at any time by a keyboard
      stroke.
          With a multiple module, the same process takes place for all
      the servers to which the user has a valid connection. The pause after
      each file server session is 10 seconds.
         The program has been tested with Netware 2.2, 3.11 and 3.12 and
      in all instances it works fine. Netware 4.x has not been tested yet.
      I make no representation of the fitness of this program to set the
      Reference or Single Reference Server in the Netware 4 environment
      although I encourage people to try it. It will most probably work.
      The modules may be used with either the NETX style shells or VLMs.

      I M P O R T A N T  ! : Both modules, NSSFX and NSMFX can be run
      from the command line. This allows you to resynchronize the servers
      without having to make a call to NCR each time.

      I M P O R T A N T  !  The Netware synchronization modules are a demo.
      Functionally they are equivalent to the licensed modules but they
      will expire at some time in the future. Please, register as a user
      if you plan to add this time server to your network facilities. The
      terms are very reasonable. Please, read SHAREWAR.E.



      TSERVE USER GUIDE                                               10
      -----------------------------------------------------------------

      TROUBLESHOOTING AND TSERVE MESSAGES

            TSERVE has no special requirements other than a modem which
      recognizes Hayes Smartmodem commands. Hopefully, it would be in
      a working order. MS DOS version 3.3 is listed as the minimum. In
      fact, version 3.3 is the earliest version that the program was
      tested with. It may even work with an earlier release. There is
      however one important restriction which has not yet been mentioned:
      When running TSERVE make sure that you either

                 run the program with its own directory as
                 the default path

                 or

                 you set an environmental variable TSERVE
                 pointing to TSERVE directory.

      This is important because the program looks for the session
      parameter file (TSPARMS.DAT) in the default path and if it does not
      find one it reverts to the initial set it was shipped with.

            If you run into problems they will most likely be due to the
      one of the following : a wrong session parameter, faulty modem,
      a serial port problem. When a program catches a condition serious
      enough to keep it from continuing, it displays a message (writes
      to a log) and calls it quits.

      There are two kinds of screen messages : bottom line orientation
      cues, which direct the program operator, and communication messages
      in the lower of the two display windows.

      Bottom Line Orientation Cues
      ----------------------------

      > To edit Session Parameters press any key .... <

        This message appears during the initial display and directs the
        user to press a key if he wants to edit the parameter table.
        See section SETTING SESSION PARAMETERS above.

      > Select by Space Bar, Move by Tab ...                 Esc=abort edit <
      > Edit Fields ...   Enter to clear, F5= step back      Esc=abort edit <

        These two messages guide the user through the parameter panel
        selections - the first one through the multiple choice tables,
        the second through the entry fields below.



      TSERVE USER GUIDE                                              11
      -----------------------------------------------------------------

      > Accept [Y/N] ÍÍ>[_] <

        This is a prompt asking user to approve the entries in the
        panel above. If the answer is 'Y' the parameters are written
        to a file overwriting the previous set.


      > Do you want to start a Time Synch session now ? [Y/N] ÍÍ>[_] <

        This is a prompt which appears after parameter editing has ended,
        or has been aborted. It ask user if he/she wants to open up a
        time-synchronizing session with the National Research Council
        labs in Ottawa, Canada.

      > Follow Communication Messages above <

        Directs attention of the user to the displays in the windows
        above. No user input required.

      > DOS Error [   ] loading Netware Sync program  ...wait !  <

        Reports on a DOS error received when a program tried to load
        the Netware Sync module (TS.REX). The possible values in the
        brackets are '002' - File not found, and '008' - Not enough
        memory. If you get the latter you should try to optimize the
        first MB of your PC's memory by using upper memory blocks or
        by removing unused resident software. Consult MS DOS manuals
        or guides for details on memory management.

      > Cannot open COMport       aborting program  ...wait ! <

        This usually happens when a serial port selected for communication
        is not physically present. Check the comport, or try the other one
        if you have two.

      Communication Messages
      ----------------------

        ( These appear in the lower of the the display windows )

      >> ....Initializing Modem  <<

        This message appears briefly when the program prepares the
        attached modem for a communication session.



      TSERVE USER GUIDE                                              12
      -----------------------------------------------------------------



      >> Error Initializing Modem... cannot continue <<

        Terminating condition !  Modem could not be prepared most prob-
        ably because:   a) the power is off or the DC-adapter is
                           defective
                        b) the serial cable connection is loose or
                           broken
                        c) modem is not connected to the serial port
                           specified in the SESSION PARAMETER TABLE
                        d) program has been started from a directory
                           other then TSERVE's resulting in loss of
                           correct serial port selection.

      >> ...Dialling National Research Council  <<

        The modem is in the process of dialling the NRC time service.


      >> ...Transmission Error <<

        This one you should never see. It signifies an internal problem.
        If you keep a second copy of TSERVE, try that one. Some corrupt-
        ion may have occured. Terminating error.

      >> ...Line busy ... retry <<

        Line is busy, the program redials until it connects or an error
        occurs.

      >> ...No answer <<

        The NRC lab modem has not answered within 30 seconds. Equipm-
        ent might be offline for maintenance. Try later. This terminat-
        ates the program.

      >> ...No carrier <<

        No carrier was detected (or was lost) after a pickup. Terminating
        condition. Again the only remedy is to try later.

      >> ...No dial tone <<

        No dial tone detected ...phone off the hook ?  Terminating cond-
        ition.



      TSERVE USER GUIDE                                              13
      -----------------------------------------------------------------

      >> ....Starting a session <<

        NRC lab is now on the line. The session has started. Session is
        in good shape.


      >> ....Measuring Loop Delay <<

        Program is in the process of calculating loop delay. Indicates
        normal session progress.

      >> ....Getting Date Info  <<

        Date Information is being transferred. Indicates normal session
        progress.

      >> ....Synchronizing Time  <<

        Time digits are being read in. Indicates normal session
        progress.


      >> ....Transfer complete...Hanging Up <<

        The time synchronizing session has terminated : AOK.


      GENIE BATCH SCHEDULER AND PROCESSOR

         To run TSERVE unattended, use GENIE, a program designed to
       run executables and batch files from a secure network station.
       GENIE, its setup program and user documentation are enclosed in
       this package.

       T I P :  On most systems, you will need to run TSERVE only once
       a day to keep the precision within a second. However it is a good
       idea, if you run an installation with multiple servers to resync
       the servers via NSMFX in GENIE every couple of hours or so.

      'DAYLIGHT' PROGRAM

         DAYLIGHT is a simple toggle switch which changes a pointer in the
      TSERVE parameter file form daylight to standard time and vice-versa.
      If you are presently on daylight zone time then DAYLIGHT will set
      it to standard, if on standard then to daylight. On next running of
      TSERVE the time will set to the new variant. Again, the program is
      designed to be run on autoschedule (by GENIE, e.g.) to enable the
      server time to be reset unattended.



      TSERVE USER GUIDE                                              14
      -----------------------------------------------------------------


      NRC SESSION MARKERS

      The following are approximate time limits on the phases of the
      automated time synchronization session :

      Modem Initialization :   2 - 12 seconds
      Dialling to Connect  :  32 - 50 seconds
      Loop Delay Test
      (if selected)        :  0.05 - 0.9 seconds
      Date Reading         :  0.05 - 15 seconds
      Time Reading         :  0.05 - 15 seconds
      Netware Sync
      (if selected)        :  0.05 - 1 second ( + 60 seconds display)

      TSERVE ENVIRONMENTAL VARIABLE

      Starting with version 1.1a an environmental variable (TSERVE) may be
      used to point to the directory which contains the session parameters
      file (TSPARMS.DAT) for TSERVE. You may include a similar statement
      to the one below in your AUTOEXEC.BAT file :

      SET TSERVE=C:\

      When TSERVE variable is present and it contains the file above you may
      execute the program from any current directory. The log file for TSERVE
      however will always be created in the current directory.



      TSERVE USER GUIDE                                              15
      -----------------------------------------------------------------

      RELEASE NOTES

      Version 1.1 features
      (27/4/94)
      þ loop delay test may be switched off
      þ equipment bias may be entered as a constant
      þ a bug which has caused modem to fail initialization
        after switch from COM1 to COM2 has been fixed
      (7/5/94)
      þ created a safety check for received date after problems were rep-
        orted with installation on 66 MHz 80486s'. The date reader will now
        retry 15 times to read the full length of the date string. Failing
        that the display and the log will complain that the date has been
        lost. (However, inserting the retry loop seems to have corrected
        the problem)

      (20/5/94)
      þ improved loop delay measurements - removed local queue-time-wait,
        clocking loops to estimate time.
      þ user may break out of busy line by pressing a key

      version 1.1a
      (10/6/94)

      þ TSERVE environmental variable: defines directory in which parameter
        file (TSPARMS.DAT) can be found

      (23/8/94)
      þ Date will not be reset unless the new value is received twice in
        succession. This eliminates transmission errors sometimes causing
        the date to reset to strange values.

      (31/8/94)
      þ The changes of 23/8 have eliminated errors but also caused under
        certain circumstances the loss of date. Date capture was completely
        reworked (like time it now passes by single characters).

      Version 2.0 features
      (19/9/94)
      þ Support for all World Time Zones.
      þ Cancel call by any key during modem initialization of dialup.

      (20/10/94)
      þ Protection against 'unrecognized baud rate divisor' error (CErr=46)
      þ Break on unrecognized error on dialup.

      version 2.0a
      (27/10/94)
      þ Protection against interrupted transmission or sudden loss of
        carrier. Logging this condition as 'aborted - no characters
        transmitted' or 'transmission error : ??'.

      (30/10/94)
      þ Protection against directory pointer mixup which results in
        'line busy' error or switching to standard time.



      TSERVE USER GUIDE                                              16
      -----------------------------------------------------------------

      (15/11/94)
      þ time corrections now shown in seconds instead of 'ticks',
        reported when run under Windows

      version 2.1
      (27/11/94)
      þ -----------------not released -----------------

      version 2.2
      (19/01/95)

      þ reporting unidentified modem error by number
      þ larger buffer for dialing string
      þ retries counts for line problems and line busy condition
      þ corrects internal error in calculating the time adjustment

      version 2.2b
      (24/2/95)

      þ new compile parameters

      version 2.2c
      (6/4/95)

      þ break out from TS.REX session by Esc key
      þ corrects problem with DAYLIGHT.EXE corrupting TSPARMS.DAT
        file





    FAQ about TSERVE

    Q. Can I run TSERVE under Windows 3.1 ?
    A. Yes, but no guarantees. TSERVE.EXE is a DOS program with a
       powerful engine which 'talks' directly to UART, the port
       and modem. It does not abide by the serial com conventions
       set for Windows. In addition the program uses other DOS
       interrupts which may potentially be a source of trouble.
       If you use TSERVE under Windows make sure you set up a
       PIF file.

    Q. Can a workstation running TSERVE synchronize more than eight
       Netware servers ?
    A. Yes, it can. The maximum of 8 servers applies to one synchr-
       onizing session. There may be as many consecutive sessions
       as the user wishes. If there are more than 8 servers the
       station must be able to log in (attach) to all of them with
       a minimum of console operator privileges. To automate the
       login/logout processes use the accompanying batch scheduler/
       processor program GENIE.

    Q. When I make a second call to NRC quickly after the first one
       TSERVE often reports an adjustment of several hundreths of
       a second. Is there a problem ?
    A. No, there is not. This is normal and expected and it does not
       mean a time gap is opening in a linear fashion. Some of this
       fluctuation is due to differing loop delays, some is a precis-
       ion error in frequency division.




      TSERVE USER GUIDE                                              17
      -----------------------------------------------------------------

    Q. Is there a difference between STIME.EXE and Netware utility
       SYSTIME ?
    A. Yes. STIME waits for next second rollover in the server's clock
       before it synchronizes the station.

                            ---@@@---

     For further information on the offered product contact me at the
     following addresses:

                             JIRI SEVERA
                             101 Renfrew #3
                             Ottawa, ON
                             Canada  K1S 1Z6


     Compuserve 70534,3475
     Internet : jiri@ott.mmcl.ca,  ah158@freenet.carleton.ca

                                   - @@@@ -