CORELOOK.EXE

                     PC Memory Scan and Search


    This program is a simple tool for viewing the contents of the
PC's memory.  It will display any memory address within the 1024 K
bytes that are addressable in the Intel segmented addressing scheme.
Thus includes the 640 K bytes of user memory and the 360 K bytes
defined for system and hardware support functions.

    This program also has a string search function that will find
the memory locations that contain a string of up to five characters
that you define.

    When CORELOOK is loaded, a screen frame appears that includes
the viewing "window" into the memory contents as well as the
address/string input fields and all required help information.


MEMORY CONTENTS DISPLAY

    CORELOOK displays the Hex values of 256 bytes of memory in the
viewing "window", arranged in 16 rows of 16 bytes, similar to DOS's
DEBUG utility.  Each row is preceded by the 16-bit segment and
offset components of the 20-bit segmented address of the first byte
in the row.  At the end of each row, the ASCII representations of
the 16 bytes are displayed.  Unprintable low-ASCII and extended
characters are shown as blank spaces, much as DEBUG displays
periods.

    When CORELOOK first starts, the viewing window displays the
memory beginning at address 0000:0000.  You can then change to other
addresses by using the several scanning options, as follows.

    >0000:0000<  ENTER BEGINNING DISPLAY ADDRESS

         This option provides an input field to specify the segment
and offset of the beginning of the desired block of memory.
The cursor starts under the leftmost position: enter valid
hex values (0-9 and A-F) across the field, skipping over
unchanged positions with the <Right> cursor.  The Backspace
and <Left> cursor do not work, but entry will wrap around
to the beginning if you need to correct a value.  At any
place in the field, pressing Enter will put the indicated
memory block in the viewing window.

    F7 - BACK PAGE

         Changes the contents of the viewing window to begin at an
address 256 bytes lower than the current beginning address.

    F8 - FORWARD PAGE

         Changes the contents of the viewing window to begin at an
address 256 bytes greater than the current beginning
address.

    F9 - BACK LINE

         Changes the contents of the viewing window to begin at an
address 16 bytes lower than the current beginning address.

    F10 - FORWARD LINE

         Changes the contents of the viewing window to begin at an
address 16 bytes greater than the current beginning
address.

    When these function key commands are used to scroll the viewing
window, the address in the BEGINNING DISPLAY ADDRESS input field is
updated automatically, and will always be consistent with the first
memory location displayed in the viewing window.

    The viewing window scroll functions also have a wrap capability
at the ends of the addressable memory.  If the viewing window
beginning address is 0000:0000 and you use F7 to move back one page,
the new viewing window will begin at the address of FFF0:0000.


STRING SEARCHING

    CORELOOK provides a string search feature that will find memory
locations that hold byte values matching a five character ASCII
string.  The match must be exact, including leading and trailing
spaces that you have in the input field.

    Alt F - ENTER FIND STRING

         Press ALT F to access the string search function.  The
cursor will move to the input field where you type the five
characters to be matched.  If the search string is less
than five characters, you need to enter leading and
trailing spaces exactly as you expect them to be located.
This may take a little experimentation if you are not sure
how the search string is delimited in its memory storage.
When the input field is to your liking, press <Enter> to
begin the search.

    F5 - REPEAT FIND

         This will search for the next occurrence of the string
currently displayed in the input field.  Memory addresses
are searched in ascending order.


PROGRAM TERMINATION

    Pressing <ESC> at any time will terminate CORELOOK and take you
back to DOS.



Rev 0 (docs only)
TAM 9/3/88